## Slide 1: What we know (and don’t know) about air quality impacts of oil and gas development
Anna Karion
NOAA/ESRL
University of Colorado/CIRES
Photo: Uinta Basin, UT credit: David Oonk, CIRES
Notes: Thank Gaby for slides

## Slide 2: NOAA Cooperative Global Air Sampling Network - Greenhouse Gases
http://www.esrl.noaa.gov/gmd/ccgg/flask.html
GHGs (including methane) are measured in weekly air samples collected around the globe.
Data is free and available online at:
http://www.esrl.noaa.gov/gmd/dv/data/
Notes: Mention Scot Miller PNAS 2013, continental methane emissions estimates using model inversion with NOAA data.

## Slide 3: Potential Air Impacts of Unconventional Oil and Gas Development
Volatile Organic Compounds (VOC) & Nitrogen Oxides: Ozone Precursors
Air Toxics
(Benzene, Toluene, H2S…)
Particles (dust)
Methane (CH4),
Carbon dioxide (CO2)
Global Scale
Regional Scale
Local-Regional Scale
Health
Air Quality
Climate Forcing
Slide credit: G. Pétron
Notes: Not talking about hydraulic fracturing – just development and booming production so we need to account for larger impact on air quality. Conventional development may or may not be cleaner or dirtier – still an unknown.

## Slide 4
Raw gas is composed of 70-90% methane
Distribution gas is >90% methane
Slide credit: G. Pétron
eia.gov
Notes: WE turn to methane as an example of how inventories vs. top-down methods work and quantify “leak rates”

## Slide 5: So what are the CH4 emissions from natural gas?
Chart: Year
| 2005 | 2006 | 2007 | 2008
2010 Report | 6.2238 | 4.9333 | 4.9095 | 4.7381 | 4.5905
2011 Report | 9.968 | 9.069 | 10.364 | 9.771 | 10.087 | 10.535
2013 Report | 7.572 | 8.018 | 7.782 | 7.178 | 6.838 | 6.893
Chart: Report
Production | 0.67143 | 5.854 | 3.64
Processing | 0.61905 | 0.748 | 0.756
Transmission | 1.8857 | 2.025 | 1.942
Distribution | 1.4 | 1.423 | 1.422
EPA Inventory of GHG Sources and Sinks

## Slide 6: So what are the CH4 emissions from natural gas?
Chart: Report
Production | 0.16294 | 1.4206 | 0.88335
Processing | 0.15023 | 0.18152 | 0.18346
Transmission | 0.45531 | 0.5004 | 0.48987
Distribution | 0.34553 | 0.34533 | 0.34509
Chart: Year
| 2005 | 2006 | 2007 | 2008
2010 Report | 6.2238 | 4.9333 | 4.9095 | 4.7381 | 4.5905
2011 Report | 9.968 | 9.069 | 10.364 | 9.771 | 10.087 | 10.535
2013 Report | 7.572 | 8.018 | 7.782 | 7.178 | 6.838 | 6.893
Chart: Report
Production | 0.67143 | 5.854 | 3.64
Processing | 0.61905 | 0.748 | 0.756
Transmission | 1.8857 | 2.025 | 1.942
Distribution | 1.4 | 1.423 | 1.422
EPA Inventory of GHG Sources and Sinks

## Slide 7: How can one assess atmospheric impacts of an industry?
Well completion
Well workover
Well normal fugitives
Liquid unloading
Separators
Dehydrators
Tank vents
Pneumatic Devices
Meters
Compressors
…
Inventory approach
estimates emissions for various types of operations or equipment using activity data and emission factors
Atmospheric evidence-based approach
estimates emissions at various scales using atmospheric measurements
Slide: Gabrielle Pétron

## Slide 8: Can we detect emissions in the atmosphere?
wind
Concentrations of pollutants measured by tower, instrumented van, or aircraft downwind of the area source reflect emissions from oil and gas production operations
surface emissions
Slide: Gabrielle Pétron
Notes: What are these pictures of? Potential emissions of different mixes depending on processing stage. Has impact on regional air.
Drilling rig, condensate tanks + produced water in small tank, xmas tree is wellhead, compressor station – push gas through pipeline to processing plant is central,
Separator on wellpad, truck brings produced water to a pond in Utah.
Use the atmosphere as a check on bottom-up inventory estimates

## Slide 9: Uinta Basin, Utah
Horse Pool
~60 km
Colorado
Utah
oil wells
gas wells
Uinta Basin

## Slide 10: Utah, 2012
Distance perpendicular to wind (km)
CH4 (ppb)
downwind
upwind
Karion, A., C. Sweeney, et al. (2013). Methane emissions estimate from airborne measurements over a western United States natural gas field. Geophysical Research Letters.
High emissions (6-12% leak rate of NG), but this field only represents ~1% of US production. Best inventory: ~5%.
Notes: Far enough downwind to know that we are fully mixed

## Slide 11: What we know
Katzenstein et al., PNAS 2003
Miller et al., PNAS 2013

## Slide 12: What we know
Green River Basin, WY: high winter time surface ozone in natural gas field (Schnell et al., 2009)
Uinta Basin, UT:
Jan/Feb 2012 winter-time ozone study (Feb. 2012: Karion et al., 2013.)
- Feb. 2013 (Oltmans et al., in prep.)
Denver-Julesburg Basin, CO: Hydrocarbon emissions from oil and gas operations in Weld County
(Pétron et al., 2012; Gilman et al., 2013; Pétron et al., 2014)

## Slide 13: What we know
Barnett Shale, TX: Third largest shale gas field in the US.
Marcellus Shale, PA
Haynesville Shale (LA/TX) & Fayetteville Shale (AR)
[NOAA: Peischl, in prep.]
[Zavala-Araiza et al, 2014; Karion et al, in prep.]
[NOAA: Peischl, in prep.]

## Slide 14: Upcoming work
Marcellus Shale, PA
San Juan Basin, CO/NM
[DOE Penn State]
Bakken, ND
[NOAA]
[NOAA]

## Slide 15
Brandt et al., 2014: Emissions estimates from atmospheric measurements generally exceed inventories by ~50%.
Allen et al., 2013: On-site measurements show leakage similar to EPA estimates.

## Slide 16
But… many production regions have not yet been sampled.
(i.e. what we don’t know!)

## Slide 17
What are inventories missing? (what we don’t know)
Processes that emit that are not accounted for (e.g. Caulton et al., 2014)
Long-tailed emissions distribution (a few sources causing the majority of leaks).

## Slide 18: Air Toxics and Methane in Colorado
Top-down oil and gas emission estimates based on flight data in May 2012 are ~2 times larger than state inventory estimates for NMHCs and 7 times larger for the carcinogen benzene (C6H6).
CH4 emissions are close to 3 times larger than an estimate based on EPA GHGRP data.
C6H6
CH4
NMHC
cars
Pétron et al., 2014
Benzene
*Measured NMHC: propane, n-butane, i-pentane, n-pentane, benzene
Notes: The U.S. Occupational Safety and Health Administration (OSHA) has set a permissible exposure limit of 1 part of benzene per million parts of air (1 ppm) in the workplace during an 8-hour workday, 40-hour workweek. The short term exposure limit for airborne benzene is 5 ppm for 15 minutes.

## Slide 19: Denver-Julesburg Basin
Pétron et al., 2014
Methane Enhancement (ppb)
Propane Enhancement (ppb)

## Slide 20: Photochemical Ozone (O3) production
Volatile Organic Compounds (VOC):
venting, flashing, flaring, fugitive emissions
OH
HO2
NO
NO2
O3
O2
VOCs,
CO, CH4
OVOCs,
CO2, H2O
(O2)
Sunlight
Slide: Jessica Gilman

## Slide 21: Photochemical Ozone (O3) production
Nitrogen Oxides (NOx=NO + NO2):
engine exhaust, drill rigs, compressor engines
OH
HO2
NO
NO2
O3
O2
VOCs,
CO, CH4
OVOCs,
CO2, H2O
(O2)
Sunlight
Slide: Jessica Gilman

## Slide 22: Photochemical Ozone (O3) production
Sunlight: UV from sunlight to trigger photochemistry
OH
HO2
NO
NO2
O3
O2
VOCs,
CO, CH4
OVOCs,
CO2, H2O
(O2)
Sunlight
Slide: Jessica Gilman

## Slide 23: Photochemical Ozone (O3) production
Ingredients: VOC + NOx + Sunlight Ozone
OH
HO2
NO
NO2
O3 = ozone
O2
VOCs,
CO, CH4
OVOCs,
CO2, H2O
(O2)
Slide: Jessica Gilman
Sunlight
Summertime Ozone: Typical in urban areas. Weld County, Colorado is non-attainment in summer.
Wintertime Ozone: Rural western oil and gas basins, such as in Utah and Wyoming.

## Slide 24
Gilman et al., “Source Signature of Volatile Organic Compounds from Oil and Natural Gas Operations in Northeastern Colorado”, ES&T, 2013
A NOAA study in 2011 estimated that 55% of OH reactivity in the DJ region was attributable to VOCs emitted by oil and gas operations.

## Slide 25
Schnell et al., 2009
Upper Green River Basin, Wyoming
Notes: Wintertime ozone phenomenon – meteorology driven – VOCs + Nox + sun

## Slide 26: Uinta Basin’s record surface ozone - 2013
High emissions of ozone precursors
Snow covered ground (reflected UV)
Shallow inversion layer
75 ppb 8hr average standard
11am
4-6pm
Notes: Under very strong temperature inversion, the Uinta Basin experienced very high ozone levels at the surface (up to 150 ppb). Snow cover amplifies effect both b/c of albedo but also snow chemistry (HONO formation)
Emissions from oil and gas operations are the main source of ozone precursors.
The U.S. Occupational Safety and Health Administration (OSHA) has set a permissible exposure limit of 1 part of benzene per million parts of air (1 ppm) in the workplace during an 8-hour workday, 40-hour workweek. The short term exposure limit for airborne benzene is 5 ppm for 15 minutes.

## Slide 27: Summary
What we know:
  Oil and gas production emissions affect air quality globally (greenhouse gases) and regionally (air toxics and ozone).
  Atmospheric measurements show that emissions are greater than inventory accounts.
What we don’t know:
  How inventories can be improved / what they are missing
  What the emissions from US oil and gas production are and how they will change.

## Slide 28
Gabrielle Pétron, Colm Sweeney, Jessica Gilman, Sam Oltmans, Russ Schnell, Eric Kort, Ben Miller, Stephen Montzka… and more
Photo: sunset over the Denton, TX airport, courtesy S. Wolter
Contact: Anna.Karion@noaa.gov
Thanks to contributions from:

## Slide 29: Thank you!

## Slide 30: Some references
Daniel Zavala-Araiza, David W. Sullivan & David T. Allen, Atmospheric Hydrocarbon Emissions and Concentrations in the Barnett Shale Natural Gas Production Region, 48 ENVTL. SCI. TECH. 5, 314, 5,315-5,319 (2014).
Studies of Uintah:
Edwards, P. et al., (2013). Ozone photochemistry in an oil and natural gas extraction region during winter: simulations of a snow-free season in the Uintah
Basin, Utah. Atmospheric Chemistry and Physics.
D. Helmig et al., (2014) Highly Elevated Atmospheric Levels of Volatile Organic Compounds in the Uintah Basin, Utah, 48 ES & T.
Ahmadov R., et al. (in prep). Understanding high wintertime ozone in an oil and natural gas producing region of the western U.S.
Carter & Seinfeld, Winter Ozone Formation and VOC Incremental Reactivities in the Upper Green River Basin of Wyoming, 50 Atmospheric Envt. 255, 255 (2012).

## Slide 31: Barnett Shale, TX
Upwind (Duchess)
Downwind (Mooney)
~200 km

## Slide 32: 19 Oct 2013
CH4
C2H6
5 downwind transects
Karion et al., in prep.
Notes: Methane (left) and ethane (right) in five separate downwind transects show consistency of plume. They also indicate that a portion of the methane enhancement does not correspond with an ethane enhancement.

## Slide 33: Ethane to Methane Ratio: Barnett Shale
Notes: Differentiating between individual plumes and their ratios with ethane or co can show influence of other non-natural gas sources (i.e. urban sources like landfills).
WRF meteorology has been run for these time periods by T. Lauvaux at Penn State and will help distinguish the geographical footprint of each plume and its source. He has already shown that in March the meteorology can pick out the plume from Dallas vs. from the gas field.

## Slide 34: Ethane to Methane Ratio: Barnett Shale
~10%
~2-3%
Kort et al., in prep.
Notes: Differentiating between individual plumes and their ratios with ethane or co can show influence of other non-natural gas sources (i.e. urban sources like landfills).
WRF meteorology has been run for these time periods by T. Lauvaux at Penn State and will help distinguish the geographical footprint of each plume and its source. He has already shown that in March the meteorology can pick out the plume from Dallas vs. from the gas field.

## Slide 35
Downwind (Mooney)
CH4
C2H6
CO
CH4
CO
Upwind (Duchess)
Karion et al., in prep.

## Slide 36: Utah 2013
Oltmans, in prep.
Uinta Basin

## Slide 37
Hydrocarbons co-emitted with methane (CH4) in Uintah Basin (Feb 2012)

## Slide 38: Denver-Julesburg Basin
wind
Pétron et al., 2014.

## Slide 39: 19 Oct 2013
Downwind Transects
Transect 1
Transect 2
CH4
C2H6
CO
CH4
C2H6
CO
Longitude
Longitude
Notes: Differentiating between individual plumes and their ratios with ethane or co can show influence of other non-natural gas sources (i.e. urban sources like landfills).
WRF meteorology has been run for these time periods by T. Lauvaux at Penn State and will help distinguish the geographical footprint of each plume and its source. He has already shown that in March the meteorology can pick out the plume from Dallas vs. from the gas field.