## Slide 1
Critical Design Review
December 4, 2014
Cameron Comeau, Daniel Flora, Smith Johnston, Alexander Potter, Maria Rocco, Evan Schomer, Dylan Stewart, Sarah Wilson, Ashley Zerr

## Slide 2: Presentation Structure
Overview
Sensor Selection
Mechanical
Thermal
Electrical & Software
Integration & Test
Management
Purpose, Overview of Design Solution,
CPE’s
Major Driving Requirements
Design Solution
V&V
Risks, Plans, Overview of Design Solution
Maria
Sarah
Sarah
Dylan
Evan
Ashley
Ashley
Notes: Maria

## Slide 3: PDR Comments Addressed
Requirement for multiple sensors
Sensor Interface
Thermistor Attachment
Wire Management
Thermal Gradient
Sensor Selection
Mechanical
Mechanical
Mechanical
Thermal
20
25
29
30
44
Notes: Maria

## Slide 4: Overview & Design Solution
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software

## Slide 5: Project Purpose
Characterize
5 Different COTS Non-Contact IR Sensors over:
STATIS =TEST BED
5 Target Surfaces
11 Temperatures between 250-350 K
Vacuum Environment
3 Distances between ¼ - 3”
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: Maria

## Slide 6: Motivation
Fast Steering Mirrors (Ball Aerospace)
Inability to sense temperatures with
current temperature sensors due to:
  Complex wiring systems across moving parts
  Marring of the surface - reducing the effectiveness of the surface
Overview
Mechanical
Management
Sensor Selection
Thermal
Testing & Integration
Electrical & Software
Notes: Complex wiring … currently used for recording temperature data aboard spacecraft
Maria
Visual – pic of mirror, draw line to represent wire – another visual with rotation and abrasion

## Slide 7: Design Solution Assembly
Overview
Mechanical
Management
Sensor Selection
Thermal
Testing & Integration
Electrical & Software

## Slide 8: Concept of Operations
Overview
Mechanical
Management
Sensor Selection
Thermal
Testing & Integration
Electrical & Software

## Slide 9: Functional Block Diagram CDR
Notes: Dylan

## Slide 10: Functional Block Diagram CDR Updates
Notes: Dylan

## Slide 11
Functional Block Diagram - Mechanical
Notes: Dylan

## Slide 12: Functional Block Diagram - Thermal
Notes: Dylan

## Slide 13: Functional Block Diagram – Electrical & Software
Notes: Dylan

## Slide 14: Functional Requirements Overview
FR 1 = Vary parameters
(distance, temp, target)
FR 2 = Collect measurement data
(distance, temp, target, IR sensor output)
FR 3 = Integrate with thermal vacuum chamber
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: Say TARGET temps

## Slide 15: Functional Requirements
FR 1: STATIS shall vary parameters relevant to characterizing the performance of COTS non-contact infrared temperature sensors.
DR 1.1 Vary Distance (Min =1/4 inch; Max =3 inches; 3 incremental steps)
DR 1.2 Vary Temperature (Min=250K; Max=350K; 10K steps)
DR 1.3 Vary Target Surfaces (5 surfaces; unique ID; FOV consideration)
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: Maria

## Slide 16: Functional Requirements
FR 2: STATIS shall collect measurement data required to characterize the performance of the COTS IR sensors.
DR 2.1 Target temperatures collected via contact temp sensors (accuracy of ≤1K; STD ≤ 0.1K)
DR 2.2 Sensor under test and Target under test shall be known (unique ID’s)
DR 2.3 Creation of test file at any time (UTF-8 csv file)
DR 2.4 Time stamped (resolution of 100ms ±50ms)
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: MR

## Slide 17: Functional Requirements
FR 3: STATIS shall be designed for use within Ball Aerospace’s thermal vacuum chamber.
DR 3.1 Electrical interface (3x37 pin connector and 1x @ ≤7.5 MHz; analog and digital signals; resistance known to within 3Ω)
DR 3.2 IR sensors temperature (between 275-325K)
DR 3.4 Meet outgassing and pressure standards
DR 3.5 Fit in 5 day test period
DR 3.6 Size constraints (4x4x4 feet)
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: MR

## Slide 18: Critical Project Elements
CPE.1: Sensor Selection
→ Budget, Mechanical Integration and Electrical Interface
CPE.2: Mechanical System
→ Rotation, Translation, Interface with Provided Hardware
CPE.3: Thermal Modeling and Control
→ Heat Dissipation and Feasibility of Control Algorithms
CPE.4: Electrical & Software Systems
→ Contact Temperature Sensor Precision and Accuracy
CPE.5: TVAC Integration
→ Materials Acquisition and Compatibility
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: 5% of grade
Maria
Cp 3 Model and control

## Slide 19: Sensor Selection
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Goals:
Find viable COTS non-contact IR sensors.
Major Modifications from PDR:
5 different IR sensors
IR Sensor Plate
Notes: 5% of grade
Maria
Cp 3 Model and control

## Slide 20: Sensor Selection Driving Requirement
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
DR 1.3.2 Four or more non-contact IR sensors shall be integrated into STATIS
  Motivation:
  The intent is to use multiple sensors in order to get a sample of the available technology and characterize the IR sensors.
  Allow testing of alternative sensors through a modular IR sensor plate design.
Notes: Smith - ____ Driving Requirement

## Slide 21: IR Sensor Selection
Sensor 1
Sensor 2
Sensor 4
Sensor 3
Sensor 5
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
All sensors shall undergo the bake out process at Ball Aerospace.
Notes: Smith

## Slide 22: FOV Driving Requirement
DR 1.1.2 The maximum distance between the target surfaces and non-contact IR sensors shall be 3 inches.
  Motivation: The intent is to replicate the expected maximum distance between the non-contact IR sensors and target surfaces in the intended application on spacecraft.
Overview
Mechanical
Management
Sensor Selection
Thermal
Testing & Integration
Electrical & Software
Notes: Smith
___ Driving Requirement
CHANGE THE REQUIREMENT 1.1.3?

## Slide 23: FOV Calculation
Sensor
d
x
L = 3”
 | Sensor | FOV
1 | OS36 | 17°
2 | MLXA | 35°
3 | TPT | 5.5°
4 | MLXBAD | 40°
5 | MLXB | 10°
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
At distance, L, of 3 inches
FOV = 41°
All sensors have FOV <41°
Notes: Smith

## Slide 24: Mechanical System
Goals
House Sensors
Change Distance
Change Target Surface
Major Modifications from PDR:
Step Motor provided by Ball
TVAC Compatibility
5 different IR sensors
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: Sasha

## Slide 25: IR Sensor Plate Design Solution
2 Housed Sensors
3 sensors mounted to
printed circuit boards
¼” HDPE IR Sensor Plate
Modular Design
¼” Thick Al 6061 L Bracket
  Mounted to stager and IR sensor plate.
6”
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
DR 1.3.2 Satisfied
Integrated 4+ IR Sensors  5 Sensors

## Slide 26: Distance Driving Requirements
DR 1.1 The distance between the target surface and non-contact infrared temperature sensor shall be adjustable.
  DR 1.1.1 Min Distance of ¼”.
  DR 1.1.2 Max Distance of 3”.
  DR 1.1.3 Distance variable in 3 incremental steps.
  DR 1.1.4 Accuracy of ±0.001”.
  Motivation: The intent is to determine whether distance is a contributing factor to temperature accuracy of the non-contact IR sensors.
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software

## Slide 27: Linear Stage Mount Design Solution
 | Stage Provides | Required
Max Distance | 17.7” | 3”
Min Distance | 0” | 0.25”
Step Size | User defined | 3 steps
Accuracy | ±0.00023” | ±0.001”
Linear Stage (Provided By Ball)
¼” Thick Al 6061 L bracket
¼” Thick HDPE IR Sensor Plate
17.7”
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
All Distance Requirements Satisfied
Notes: Sasha: note, this trimetric view should be updated and include the HDPE baseplate

## Slide 28: Target Rotation Driving Requirement
DR 1.3 Every IR sensor will be able to view every target surface.
  DR 1.3.1 Five target surfaces.
  DR 1.3.2 Four or more IR temperature sensors.
  Motivation: The intent is to determine how the IR sensors measure temperatures on different materials commonly found on spacecraft.
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: Sasha
More edits

## Slide 29: Target Wheel Design Solution
Five Target Surfaces
  - Anodized Aluminum
  - Chromated Aluminum
  - Graphite Composite
  - Glass
  - Z306 Emissive Paint
Thermistors
Al Target Wheel Diameter: 12”
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Al 6061 “Picture Frame”
Plastic washer to secure
Thermistor to target surface
Target Surface
Diameter: 2.25”

## Slide 30: Target Wheel Design: Wire Management
Thermistor wires come around the two target plates
Thermistor wires go to a strain relief bracket
10 thermistor wires +2 heater wires
enter the hollow axel via two slots
Bundled Wires leave
out the back
of the hollow
axle
IR Temperature Sensor + Digital
Thermometer Wires
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
All rotations will never exceed max 144° from neutral strain wire position

## Slide 31: Target Wheel Design: Axle and Bearings
12” Al Target Wheel
9.5” Kapton Heater
12” Al Radiator
Dry Contact Bearings
12” Al Backplate
Hollow 1” OD Delrin Plastic Axle
4:1 Gear Ratio
Arun C14.4 Step Motor (Provided by Ball)
Expanded View
Full Assembly

## Slide 32: Target Wheel Design Solution: Motor and Gears
Torque Supplied Arun C14.4 motor τS= 75 Nmm
Torque Required (IST, μB, design) τR= 97.8 Nmm
τRequired> τsupplied
GEARS REQUIRED
Gear Ratio 4:1; FOS =2.8; τ required=24.2 Nmm
τrequired< τsupplied
System can be rotated, DR 1.3 satisfied
72 degree rotation in 10 seconds

## Slide 33: Thermal System
Goals:
Target Temperature Control
IR Sensor Survivability
Major Modifications from PDR:
Passive temperature control of IR sensors
Updated thermal rejection system
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: DAN

## Slide 34: Temperature Control Driving Requirements
DR 3.2: The sensor plate shall be maintained within
275 – 325 K.
  Motivation: The intent is to maintain temperatures in a window within the operating range of each sensor.
DR 1.2.2: The target surfaces shall be controllable from
250 – 350K.
  Motivation: The intent is to sample temperatures within a range that components on a thermally controlled spacecraft will experience.
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: DAN

## Slide 35: Thermal System Layout
Patch Heater
Al Radiator Plate ~108K
1 Thermistor per Target
Digital Thermometer
Key:
Heater
Primary Conduction
Primary Radiation
Temperature Sensor
Copper Conducting Bar
GM Cooler 100K
(Provided by Ball)
Al Target Wheel
250 – 350 K
Al Sensor Plate
275K < Tsensors<325K
Covered in Al Tape
Covered in Al Tape
Notes: DAN

## Slide 36
Heat Transfer Overview
Ts>Tt
qrad
qcond
qrad
qrad
Covered in Al Tape
Covered in Al Tape
Key:
Heater
Primary Conduction
Primary Radiation
Notes: DAN

## Slide 37
If Ts<Tt
qrad
Heat Transfer Overview
qin
qcond
qcond
qrad
qcond
qcond
qrad
If Ts>Tt
qrad
q=heat rate (W)
qrad
Key:
Heater
Primary Conduction
Primary Radiation
Heater
Target Wheel
Backplate
Radiator Plate
Copper Conducting Bar
GM Cooler
Notes: DAN

## Slide 38: Thermal Circuit Overview
Paste
Cond.
Temps
Radiation
Sensorwheel
Radiation exchange, sensors and targets
Gcond,strap
Radiation exchange
to radiator disk
Cold Finger
Shroud
Assumptions:
1D heat transfer
Steady state
Boundary Conditions:
  Sensor Wheel: 275-325 K
  Cold Finger: 100 K
  Chamber Surroundings: 298 K
22 equations, 22 unknowns
MATLAB -> fsolve()
Key:
G = Conductance=1/R
Radiation G (W/K4)
Conduction G (W/K)
Conduction to/thru each target and remaining area
Notes: DAN

## Slide 39: Heater Power Requirement Satisfaction
Conclusion:
62 W < 200 W budget
SS control of the targets can be achieved in range 250-350 K.
UltiBots 24V Kapton Heater:
Max Power: 300W; 1.07W/in2
Heater capable
* FOS of 4 on heater power required
Method:
Set Ttarget  Calculate qheater
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
62W
Notes: DAN

## Slide 40: Heat/Cool Rates Driving Requirements
DR 1.2.2.1 /2: The target surfaces shall increase in temperature at a minimum rate of 20K/hr and shall decrease in temperature at a minimum rate of 5K/hr.
  Motivation: The intent is to test the apparatus in the allotted time based on limited access to the thermal vacuum chamber.
DR 1.2.2.3 : The temperature of the target surfaces shall be modified in incremental steps of 10K.
  Motivation: The intent is to test the full range between 250K and 350K, determine if/when sensors begin to lose accuracy.
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: DAN

## Slide 41
Cool down= 2.9 hrs
Finish Pump Down
Test (x11)+ Heat up(x10)
Requirement Satisfaction:
Cool Down:
-16.5 K/hr < -5 K/hr
Satisfies DR 1.2.2.2
Max Heat up:
+100 K/hr > +20 K/hr
For steps of 10 K
Satisfies DR 1.2.2.1/3
Heat/Cool Rate Requirement Satisfaction
Max heat up
6 min
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: DAN

## Slide 42: Sensor Operating Range Driving Requirements
DR 3.2 : The sensor plate shall be maintained within the temperature range of 275 - 325K.
  Motivation: The intent is to maintain temperatures in a window within the operating range of each sensor.
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: DAN

## Slide 43: Predicted Sensor and Target Temperatures vs. Time
Cool down
Finish Pump Down
Tests (x11)+Heat up(x10)
Requirement Satisfaction:
Sensor Temperature:
Tsensor ≤ 298K < 325K
275K < 286K ≤ Tsensor
Meets DR 3.2
(275K<Tsensor<325K)
10 K steps
Sensor Operating Range
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: DAN

## Slide 44: Temperature Accuracy Driving Requirements
DR 2.1.2 : The absolute temperature of the targets shall be collected with an accuracy of 1K or better.
  Motivation: The intent is to have a reliable measurement within 10% of the temperature change described in DR 1.2.2.3 from which to compare temperature data.
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: Dylan

## Slide 45: Radial Gradient Concerns
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
ΔT must be <1K in order to satisfy DR 2.1.2 such that the thermistors and IR sensor are reading a consistent temp of the target.
ΔT
Thermistor

## Slide 46: 3D Model Methodology
r
z
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software

## Slide 47: 3D Model Methodology cont.
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software

## Slide 48: Radial Gradient Requirement Satisfaction
ΔT=0.2<0.5K*
DR 2.1.2 Satisfied
*Due to electrical considerations discussed later this must be 0.5K as opposed to 1K
ΔT (K)
W

## Slide 49: Electrical & Software
Goals:
Data Acquisition
Control Implementation
Data Storage
Major Modifications from PDR:
All electronics outside TVAC

## Slide 50: Hardware Overview
NI MyRIO Embedded Platform
Custom board to stack on top of MyRIO
  ADCs
  Heater control
  IR Sensor Input
Cable Harnessing
  Interface with TVAC 37-pin
  Internal boards handle sensor and
  heater interface
Custom PCB
NI myRIO

## Slide 51: Electrical/Software Overview
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
Electrical & Software FBD
51
Notes: Microcontroller external to TVAC
ADC internal to TVAC to reduce signal noise
Stage control handled by separate controller

## Slide 52: Electrical/Software Overview
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
52
Notes: Microcontroller external to TVAC
ADC internal to TVAC to reduce signal noise
Stage control handled by separate controller

## Slide 53: Electrical/Software Overview
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
53
Notes: Microcontroller external to TVAC
ADC internal to TVAC to reduce signal noise
Stage control handled by separate controller

## Slide 54
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
DR 2.1 – Temp collected by conventional contact sensors for reference
DR 2.1.2 – Reference temp accuracy of 1K or better
Design Solution:
Thermistor measurement error less than 0.5K (calibrated).
Includes resistor tolerances, source precision, and parasitics.
DR 1.2.1 – Reference temp STD < 0.1K over 30 sec
Design Solution:
Electrical noise less than 0.02K (including LPF).
Includes capacitive, inductive, and radiative coupling from noise sources.
Reference Temperature
54
Notes: Microcontroller external to TVAC
ADC internal to TVAC to reduce signal noise
Stage control handled by separate controller

## Slide 55: Electrical/Software Overview
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
DR 1.2.1 – Reference temp STD < 0.1K over 30 sec
DR 2.1.1 – Target temps collected at 1Hz
Temperature Conversion
55
Notes: Microcontroller external to TVAC
ADC internal to TVAC to reduce signal noise
Stage control handled by separate controller

## Slide 56: Electrical/Software Overview
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
DR 1.2 – Temperature control through user commands.
Heater Control
56
Notes: Microcontroller external to TVAC
ADC internal to TVAC to reduce signal noise
Stage control handled by separate controller

## Slide 57: Electrical/Software Overview
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
DR 1.2.1 – Reference temp STD < 0.1K over 30 sec
Analysis: System allows for 40mW step size in heater power.
MOSFET Circuit
57
Notes: Microcontroller external to TVAC
ADC internal to TVAC to reduce signal noise
Stage control handled by separate controller

## Slide 58: Electrical/Software Overview
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
DR 1.1 – Distance control via user input commands.
DR 2.3 – Correlate sensor–target pairing to data sets.
DR 1.3 – Measure all target surfaces with all IR sensors.
Mechanical Control
58
Notes: Microcontroller external to TVAC
ADC internal to TVAC to reduce signal noise
Stage control handled by separate controller

## Slide 59: Electrical/Software Overview
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
Mechanical Actuators
59
Notes: Microcontroller external to TVAC
ADC internal to TVAC to reduce signal noise
Stage control handled by separate controller

## Slide 60: Electrical/Software Overview
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
DR 1.3.2 – 5 different IR sensors
Design flexibility for IR sensor compatibility:
0.8V to 12V supply voltage
SPI/I2C Digital interface
Analog Voltage or Current interface
Thermopile interface w/ internal converter
IR Sensor Interface
60
Notes: Microcontroller external to TVAC
ADC internal to TVAC to reduce signal noise
Stage control handled by separate controller

## Slide 61: Electrical/Software Overview
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
Down Sampling
Notes: Microcontroller external to TVAC
ADC internal to TVAC to reduce signal noise
Stage control handled by separate controller

## Slide 62: Electrical/Software Overview
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
DR 2.4 – Save data to output file
DR 2.5 – Data time stamping and measurement correlation to 1sec
Data Output
Data Processing and File Write
ADC Read
IR Sensor Read
5ms
1ms
2ms
<10x FOS for timing
Offramp - FPGA for data acquisition and timestamping
62
Notes: Microcontroller external to TVAC
ADC internal to TVAC to reduce signal noise
Stage control handled by separate controller

## Slide 63: Integration & Test
Goals: Mitigate and expose risks by assembling and testing systems
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: Talk about how component tests will be done and how all purchased or provided equipment will be checked for functionality prior to systems level testing.

## Slide 64: Overview of Subsystem Checkouts
Purchased/Provided Part Functionality
  Heater
  Linear Stage
  Motor
  Sensors
Subsystem Checks
  Electrical Checkouts
  Software Testing
  Mechanical Tolerance Checks
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software

## Slide 65: T1: Ambient Thermal Test
Main Objective: Show functionality and commandability of thermal system.
Requirements Verified:
  1.2.1 STD of target temp <0.1K over 30s
  1.2.2 Target temps commandable to 250-350K in 10K intervals
Location: CU Campus
General Procedure: Command temp to greater than ambient temperature and verify stability of 0.1K STD
Software
Heater Control
Target Wheel
Heater
Radiator Plate
5x Installed Thermistors
Required Systems:
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
12”

## Slide 66: T2: Alignment Test
Main Objective: Ensure FOV of IR sensors are on targets
Requirements Verified:
  2.3 Known combination of sensor and surface
  1.3 Every target will see every IR sensor
  1.3.1.1 Target area shall be big enough for FOV
Location: Ball facilities – Ambient
General Procedure: At the furthest difference with heaters on, test to make sure that FOV is on the target by introducing a surface cooled with liquid nitrogen in front of target and around target.
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Software
Stage
IR Sensor Plate
Target Wheel & Heater
Motor
Stage Control
48”
Required Systems:

## Slide 67: T3: STATIS Full System Test AMBIENT
Main Objective: Run entire testing cycle at ambient to show functionality and chamber compatibility.
Location: Ball TVAC – No change in pressure (5 day test window)
Action Items for Failed Test:
  Dependent on failed systems
  Cannot depressurize in TVAC without passing ambient test
Required Systems: All
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
STATIS
Ambient Pressure TVAC
Thermally Strapped

## Slide 68: T4: STATIS Full System Test TVAC
Main Objective: Run entire testing cycle in TVAC to show complete functionality before handing test bed over to Ball.
Location: Ball TVAC 10e-7 Torr
(Additional 5 day test window)
Action Items for Failed Test:
  Dependent on failed systems
  Cannot reach top level success without passing TVAC test
Required Systems: All
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
STATIS
Depressurized TVAC
Thermal Strapped

## Slide 69: Management
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Major Takeaway:
On Schedule
On Budget
Notes: Maria

## Slide 70: Organizational Chart
STATIS
Customer
(Ball Aerospace – Joe Lopez)
Project Manager
(Maria Rocco)
Systems Engineer
(Ashley Zerr)
Integration and Test
(Sarah Wilson)
Financial
(Smith Johnston)
Safety
(Sarah Wilson)
Mechanical
(Alexander Potter)
Manufacturing
(Daniel Flora)
Thermal
(Cameron Comeau)
Electrical
(Evan Schomer)
Software
(Dylan Stewart)
Sensor Selection
(Smith Johnston)
ADVISOR
Jeliffe Jackson
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration &Test
Electrical & Software
Notes: Point out technical leads

## Slide 71: Work Breakdown Structure
Course Deliverables
CDR
Management
Integration & Test
Mechanical
Thermal
Electrical &
Software
FFR
MSR
TRR
AIAA paper
SFR
PFR
Schedule
Risk Matrix
WBS
Budget
V&V Test Plans
Data
Ambient Test
Time
Distance
ID’s
Temperature
TVAC Test
CAD model
Component Selection
3 Plates/Disks
Sensor Housing
Attachment Mechanism
STATIS
1D Model
Quasi 3D Model
Insulation Design
Component Selection
Trade Study - DAQ
Board Schematic
Component Selection
I/O Software FBD
Complete
Hardware Sys.
Software Executable
Test Reports
Complete at CDR
Incomplete at CDR
LEGEND
Procured Parts
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: What are key products that will be most critical to produce

## Slide 72: Schedule Overview
Ambient Test (at Ball)
Bakeout Session (at Ball)
Thermal
Mechanical
Electrical
Software
Finance
Holidays/Breaks
Testing
Milestone
Margin
Finalize All Models
Winter Break
Spring Break
Ambient Test
Manufacturing, Part Population, Software Development
Final Vacuum Test
Component and Integration Testing
Final Test (at Ball)
FFR
MSR
TRR
SFRx2
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Week 1
Week 10
Week 17
Notes: Maria

## Slide 73
Test Schedule
Bakeout
Subsystems
Component
Multi-System
Milestone
Margin
Component and Distance Tests
FFR
CDR
MSR
TRR
SFR
SFR
Ambient Test (at Ball)
Bakeout Session (at Ball)
Final Test (at Ball)
Alignment Test (at Ball)
Ambient Thermal Test
Full Ambient Test (at Ball)
Full TVAC Test (at Ball)
Week 1
Week 10
Week 17

## Slide 74: Budget
Thermal
5%
$312
Testing
6%
$420
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: Maria
Smith

## Slide 75: CDR Risk Matrix
 | 3 |  | 
 | 2 | 1 | 
 | 4 |  | 
Probability of Failure
Importance
High
Low
Low
High
Thermal modeling fidelity
  Additions to model to improve fidelity
Access to Ball’s facilities and hardware
  More hardware guaranteed
  Direct correspondence with TVAC manager
Prove temp control system is capable of meeting requirements
  Built in margins of error in other systems
Purchasing schedule risk (order/delivery time frames)
  Obtained A-Card
2
3
1
4
Indicates Risks at PDR

## Slide 76: Pre-Test Risk Matrix
 | 3 |  | 
2 |  | 1 | 
4 |  |  | 
Probability of Failure
Importance
High
Low
Low
High
Thermal modeling accuracy
  No change
Access to Ball’s facilities and hardware
  Should already have facility access
Prove temp control system is capable of meeting requirements
  No change
Purchasing schedule risk (order/delivery time frames)
  All parts should be ordered and installed
2
4
1
3
Indicates Risks at CDR

## Slide 77: Summary
Al
4:1 Gears
5 Targets: Anodized Al, Chromated Al, Glass, Graphite composite, Emissive Paint (Provided by Ball)
Aerotek Pro 115 Linear Stage (provided by Ball)
GM Cooler (provided by Ball)
5 IR Sensors: OS36, TPT, MLX-BAD, MLX-B, MLX-A
24V Kapton Heater
HDPE Plastic
Arun C14.4 Motor (provided by Ball)
TVAC Floor
HDPE Plastic
HDPE Plastic
Copper Conducting Bar
Notes: How does this satisfy major requirements

## Slide 78: Questions?

## Slide 79: Backup Slides

## Slide 80: Functional Block Diagram Original PDR
Overview
Mechanical
Management
Sensor Selection
Thermal
Testing & Integration
Electrical & Software
Notes: Dylan

## Slide 81: Functional Block Diagram PDR Redesigns
Overview
Mechanical
Management
Sensor Selection
Thermal
Integration & Test
Electrical & Software
Notes: Dylan

## Slide 82: Sensor Selection Backup

## Slide 83: Sensor Selection Trade Study
Overview
Mechanical
Management
Sensor Selection
Thermal
Testing & Integration
Electrical & Software
# | Sensor | FOV | Cost | Mechanical Considerations | Electrical Considerations
1 | OS36-3-T-50F | 17deg | $389 | Housing already built and Compatible | 
2 | MLX90614KSF-ACC | 35deg | $26.32 | Manufacture Cylindrical Housing | 
5 | MLX90614ESF-BCF | 10deg | $27.22 | Manufacture Cylindrical Housing | 
4 | MLX90620ESF-BAD | 40deg | $75.62 | Manufacture Cylindrical Housing | 
3 | TPT300V | 5.5deg | $375.51 | Manufacture Cylindrical Housing | 
 | PSC-SSS | 3deg | $815 | Housing already built and Compatible | Cannot use without Electronics Box (not vacuum compatible)
 | OS36-3-K-1200F | 17deg | $1,035 | Bulky Housing | 
 | CT-SF02-C1 | 27deg | $505 | Housing already built and Compatible | Cannot use without Electronics Box (not vacuum compatible)
 | ZTP-115M | 5.5deg | $13 | Geometrically awkward - Not simple design solution | 
 | ZTP-115 | 50deg | $5 | Manufacture Cylindrical Housing | 
Notes: Smith

## Slide 84: Mechanical Backup

## Slide 85: Shaft Bending Stress and Deflection
Bending stress of cantilevered beam:
The load F = 36.8 N (weight of target disks)
For Delrin: Tensile Strength = 36 MPa
Bending Stress Safety Factor: 41
Deflection of cantilevered beam:
For Delrin: E = 2.4 GPa
0.000006 m = 0.00024”
Allowable 0.06” > 0.00024”
856 kPa
0.000006 m
Notes: Sasha

## Slide 86: Shaft Shear Stress
F = 36.8 N (weight of target disk assembly)
A = 0.000222 m2
For Delrin: shear strength = 35.8 MPa, which gives
a safety factor of 215.
Shear stress on hollow shaft cross section

## Slide 87: Thermal Contraction: Shaft, Bearings, Supports
Using Linear expansion, where the starting lengths are the thicknesses in the radial direction, and further assuming
that all the components reach the
radiator temperature of 100K:
Total Contraction = 0.0017”
0.06”> 0.0017”
Delrin Shaft, Thermal Expansion = 16*10-6 m/(mK)
Initial Length = 0.125”
Bearing, Thermal Expansion = 9.9*10-6 m/(mK)
Initial Length = 0.0625”
Support, Thermal Expansion = 12*10-6 m/(mK)
Initial Length = 0.5”
-193 K

## Slide 88: Inertia, Motor and Gears
r1
F
-F
r2
Contact Force Pair
Contact Force Pair
Pinion Gear Radius
Gear Radius
Gear Ratio
Torque Supplied by Motor (70 mNm)
Pinion/Gear Schematic

## Slide 89: Inertia, Motor and Gears Continued
Radius of Shaft:
0.5”
Coefficient of Static Friction:
0.15
Normal Reaction Forces on
Supports (45N and 5.6 N)
Determined with moment
and force balance.
72 degree rotation
in 10 seconds
To deliver this requires a gear ratio of 1.4,
a gear ratio of 4 gives a factor of safety of 2.8.

## Slide 90: Bearing Stresses
F (reaction force)
b (hole diameter)
b=1”
t (hole depth)
t=1/2”
A=0.000323 m2
The contact areas between the
shaft and support structure carry
bearing stresses. The larger of the
two (45 N compared to 5.6 N) is
highlighted here.
For the Delrin Shaft, Compressive strength = 35.8 MPa, this gives a safety factor of 256.
For the iGlideJ, permissible surface pressure = 35 MPa, which gives a factor of safety of 250.

## Slide 91: Support Compressive Stress
The HDPE supports experience compressive (front) and
tensile (rear) stresses due to the weight of the Delrin shaft and
the target disk assembly.
45 N
Width = 2”
Thickness = ½’
Height = 10”
A = width*thickness = 0.00065 m2
= 69 kPa
For HDPE, compressive strength = 20.6 MPa,
this gives a safety factor of 298.

## Slide 92: Compressive Buckling
The HDPE supports are only ½” thick, thus, buckling was a possible concern.
P = 45 N
Width b = 2”
Thickness t = ½”
Height L = 10”
From Euler Pre-Buckling Theory
the critical load is given by:
For a rectangular cross section:
For HDPE, E = 0.883 GPa
This gives a critical load Pcr = 1171 N.
The supports experience a maximum of 45 N.
This gives a safety factor of 26.

## Slide 93: Wire Clearances
Orignially, the design was ¼” diameter shaft, this could not fit all the wires.
Then ½” diameter shaft was investigated, and the fit was too tight.
1” provides plenty of clearance.
½” diameter shaft
1” diameter shaft
To get into the hollow shaft, the 10 thermistor
wires pass through slots cut in the shaft and
the rear target attachment plate.
Target Plate/Shaft Attachment and Wire Slots
Hollow Shaft
Slots for Wires (4)
1/5”x1/5”
Holes for set pin (4)
(expanding “C” clamp)
1/8” diameter
Thermistor wire
Heater wire
Front Target
Disk

## Slide 94: Wire Strain Relief Brackets
The two heater wires come out of the center of the hollow shaft, so they may pass straight
down the length of the shaft (directly off of the back of the front target disk).
The thermistor wires, however, must go around both the front and rear target disks to then
pass into their slots and go down the shaft, so they must have strain relief, so that any tension
in the wires from twisting is not concentrated at the thermistors attachment point.
¼” thick Aluminum Strain Relief
Brackets (tension from rotation
taken here)
1/5”x1/5” Slots for wires
entrance into hollow shaft.
Back of rear target disk
Thermistor wire pairs
Hollow Shaft

## Slide 95: Thermal Backup

## Slide 96: Target Temp Residuals
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
Difference in temp of each target due to material properties very small, glass only outlier

## Slide 97: Steady State Heat Loads
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
Dominant heat path:
Heater power radiates to radiator disk, conducts to cooler. Radiation with shroud and between sensors/targets is very small

## Slide 98: Distance Comparison
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
Difference between heater power for each distance is very small.
The radiation path between targets and sensors has very small contribution

## Slide 99: Distance Comparison
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
Running cooler at 100 K will give 350 W of lift capacity.
350 W >> 65 W max
(65 W needed for 350K steady state)
Chart: Al330 Performance (3/19/2008)
| 11.089 | 12.23 | 14.393000000000001 | 16.048999999999999 | 18.795999999999999 | 24.286999999999999 | 29.995000000000001 | 40 | 50.01 | 75 | 100 | 150 | 200 | 250 | 300
Cold Power (W) | 0 | 10.09 | 20.06 | 30.03 | 39.97 | 74.9 | 107.52 | 160.59 | 206.18 | 288.36 | 349.09 | 431.39 | 475.56 | 476.94 | 501.33

## Slide 100: Quasi-Equilibrium Analysis
Flow diagram of what we did? How is analysis different? “Same” model is being used but the APPLICATION of the model is different. So show this not the circuit diagram
Circuit diagram looks the same so do something to show this variation
Sequence:
Cool Down at 250 K @ max distance
Maintain steady state 250 K for rest of pump down
Perform steady state 190 sec test for distances 1, 2, 3
Heat up target 10 K to next SS temp @ distance 3
Notes: DAN

## Slide 101: Sensor Temp Limits
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
After 4 hr pump down, 9.8 hrs of 250 K before Tsens<275 K
Equilibrium: Tsens=268 K
End of pump
End of tests
9.8 hrs
6.8 hrs
After 1 full test cycle,6.8 hrs of 350 K before Tsens> 325 K
Notes: This is a backup

## Slide 102: Steady Target Temperature
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal

## Slide 103: Steady State Temperature Deviation
Overview
Sensor Selection
Summary
Requirements
Mechanical
Electrical
Thermal
Target Temp: std=0.0243 < 0.1
Target Temp: std=0.0056 < 0.1
Heater Resolution: .04 W
Steady Drift
Correction w/ Reference
DR 1.2.1 Satisfied.
Notes: This is a backup

## Slide 104: Electrical & Software

## Slide 105: Function Definitions
30 sec STD
  Input: Target Temps (1Hz)
  Output: 30 sec rolling STD
Temperature plotting
  Input: Target Temps, Setpoint Temp (1Hz)
  Output: Continuous plot of temperatures
Temporal Average
  Input: Voltage reading from ADC (10Hz) (Thermistors and IR Sensors)
  Output: 10 point unweighted average (1Hz)
Convert from Voltage to Resistance
  Input: Temporally averaged voltage from thermistors (1Hz)
  Output: Resistance (1Hz)
Convert from Resistance to Temperature
  Input: Thermistor Resistance readings (1Hz)
  Output: Temperature (1Hz)
Heater Duty Cycle Controller
  Input: Serial average of target temps (1Hz), Heater Setpoint
  Output: PWM signal generation
Motor Controller Commander
  Input: Position Setpoint, Current position (derived from SensorID & TargetID)
  Output: Serial commands
Automator
  Input: CSV file defining experiments
  Output: heater setpoint, target wheel position setpoint, stage position setpoint
Data file generator
  Input: Target Temps & Voltages, Sensor Voltages, SensorID, TargetID, distance setpoint, Timestamp
  Output: CSV file containing the above

## Slide 106: Thermistor Calibration
Precision Voltage (10V) Source Error
  Measured by lab multimeter with 0.1mV accuracy
Precision Voltage (5V) Reference Error
  Measured by lab multimeter with 0.1mV accuracy
ADC Error
  Offset Error
  Gain Error
  Precision resistor reference

## Slide 107: Thermistor Calibration
ADC Offset Error
*taken from Atmel: Characterization and Calibration of the
ADC on an AVR (http://www.atmel.com/images/doc2559.pdf)

## Slide 108: Thermistor Calibration
ADC Gain Error
*taken from Atmel: Characterization and Calibration of the
ADC on an AVR (http://www.atmel.com/images/doc2559.pdf)

## Slide 109: Bring Up Plan
Electrical Tests | 
Board Bring Up Tests | Verifies/Tests for
Continuity and Short Testing | Board layout errors, fabrication errors
Soldering Quality Assurance | Cold solder joint risk mitigation, solder shorts
Power Draw Test | Finalized short testing to prevent damage to power supplies
Board Voltage Supply Test | Correct voltage outputs and within accuracy needed
Level 1 | Basic electrical functionality
PWM Frequency Control | Frequency can be set to 1kHz or above
PWM Duty Cycle Control | Duty cycle step size meets heat injection precision requirements
SPI Communication with ICs | IC basic functionality, SPI protocol working
I2C Communication | IC basic functionality, I2C protocol working
Communication with Motor Control | Verifies component functionality
Heater Circuit Functionality | Circuit/design functionality
Level 2 | Independent electrical functionality
PWM control of heaters | Full heater control functionality
Read ADC values with known voltages | ADC accuracy requirement, calibration, noise levels
Read Digital IR Sensors | IR sensor functionality
Stepper Motor Control | Full stepper motor control
Level 3 | 
Full concurrent electrical control (heaters, temperature measurements, motor control, control looping) | Full electrical functionality with no concurrency issues

## Slide 110
TVAC Feedthrough Pins |  |  |  |  | 
Connector A |  | Connector B |  | Connector C | 
Pin | Assigned | Pin | Assigned | Pin | Assigned
1 | Thermistor 1 | 1 | Motor A | 1 | Reserved for Motor
2 | Thermistor 1 | 2 | Motor A | 2 | Reserved for Motor
3 | Thermistor 2 | 3 | Motor B | 3 | Reserved for Motor
4 | Thermistor 2 | 4 | Motor B | 4 | Reserved for Motor
5 | Thermistor 3 | 5 | Heater 1 | 5 | Reserved for Motor
6 | Thermistor 3 | 6 | Heater 1 | 6 | Reserved for Motor
7 | Thermistor 4 | 7 | Heater 1 RTN | 7 | Reserved for Motor
8 | Thermistor 4 | 8 | Heater 1 RTN | 8 | Reserved for Motor
9 | Thermistor 5 | 9 | Heater 2 | 9 | Reserved for Motor
10 | Thermistor 5 | 10 | Heater 2 | 10 | Reserved for Motor
11 | Thermistor 6 | 11 | Heater 2 RTN | 11 | Reserved for Motor
12 | Thermistor 6 | 12 | Heater 2 RTN | 12 | Reserved for Motor
13 | GND | 13 | Heater 3 | 13 | Reserved for Motor
14 | GND | 14 | Heater 3 | 14 | Reserved for Motor
15 | GND | 15 | Heater 3 RTN | 15 | Reserved for Motor
16 | GND | 16 | Heater 3 RTN | 16 | Reserved for Motor
17 | IR Current | 17 | GND | 17 | Reserved for Motor
18 | IR Current | 18 | GND | 18 | Reserved for Motor
19 | IR Current | 19 | One Wire | 19 | Reserved for Motor
20 | IR Current | 20 | One Wire | 20 | Reserved for Motor
21 | GND | 21 | SPI | 21 | Reserved for Motor
22 | GND | 22 | SPI | 22 | Reserved for Motor
23 | GND | 23 | SPI | 23 | Reserved for Motor
24 | GND | 24 | CS | 24 | Reserved for Motor
25 | Motor Set Point | 25 | CS | 25 | Reserved for Motor
26 | GND | 26 | CS | 26 | Reserved for Motor
27 | GND | 27 | CS | 27 | Reserved for Motor
28 | IR Power 5V | 28 | GND | 28 | Reserved for Motor
29 | IR Power 3.3V | 29 | GND | 29 | Reserved for Motor
30 | IR Power 3V | 30 | I2C | 30 | Reserved for Motor
31 | IR Power | 31 | I2C | 31 | Reserved for Motor
32 | GND | 32 | Reserved | 32 | Reserved for Motor
33 | GND | 33 | Reserved | 33 | Reserved for Motor
34 | Reserved | 34 | GND | 34 | Reserved for Motor
35 | Reserved | 35 | GND | 35 | Reserved for Motor
36 | GND | 36 | GND | 36 | Reserved for Motor
37 | GND | 37 | GND | 37 | Reserved for Motor

## Slide 111
MyRIO (1950) (board only) |  |  |  |  |  |  | 
Connector A |  |  |  | Connector B |  |  | 
Pin |  | Function | Assigned | Pin |  | Function | Assigned
1 |  | 5V |  | 1 |  | 5V | 
2 |  | AO1 |  | 2 |  | AO1 | 
3 |  | AI0 |  | 3 |  | AI0 | 
4 |  | AO1 |  | 4 |  | AO1 | 
5 |  | AI1 |  | 5 |  | AI1 | 
6 |  | AGND |  | 6 |  | AGND | 
7 |  | AI2 |  | 7 |  | AI2 | 
8 |  | DGND |  | 8 |  | DGND | 
9 |  | AI3 |  | 9 |  | AI3 | 
10 |  | UART RX |  | 10 |  | UART RX | 
11 |  | DIO0 | SS | 11 |  | DIO0 | TEMP
12 |  | DGND |  | 12 |  | DGND | 
13 |  | DIO1 | SS | 13 |  | DIO1 | TEMP
14 |  | UART TX |  | 14 |  | UART TX | 
15 |  | DIO2 | SS | 15 |  | DIO2 | SS
16 |  | DGND |  | 16 |  | DGND | 
17 |  | DIO3 | SS | 17 |  | DIO3 | SS
18 |  | DIO11 | SS | 18 |  | DIO11 | SS
19 |  | DIO4 | SS | 19 |  | DIO4 | SS
20 |  | DGND |  | 20 |  | DGND | 
21 |  | SPI CLK | SPI | 21 |  | SPI CLK | SPI
22 |  | DIO12 | SS | 22 |  | DIO12 | SS
23 |  | SPI MISO | SPI | 23 |  | SPI MISO | SPI
24 |  | DGND |  | 24 |  | DGND | 
25 |  | SPI MOSI | SPI | 25 |  | SPI MOSI | SPI
26 |  | DIO13 | SS | 26 |  | DIO13 | SS
27 |  | PWM0 | Heater1 | 27 |  | PWM0 | Heater1
28 |  | DGND |  | 28 |  | DGND | 
29 |  | PWM1 | Heater2 | 29 |  | PWM1 | Heater2
30 |  | DGND |  | 30 |  | DGND | 
31 |  | PWM2 | Heater 3 | 31 |  | PWM2 | Heater 3
32 |  | I2C SCL | I2C | 32 |  | I2C SCL | I2C
33 |  | 3.3V |  | 33 |  | 3.3V | 
34 |  | I2C SDA | I2C | 34 |  | I2C SDA | I2C

## Slide 112: Sensors

## Slide 113: Thermistor Wheatstone Bridge
Measure differential voltage with reference resistance
Requires 16-bit ADC for 0.05K resolution
  24-bit ADC allows 1mK resolution (2uV) with negligible increased cost (21-bit effective from internal noise)
Error (needs to be less than 1K)
  Modelled to be less than 0.8K (calibrated,can be reduced to 0.4K with more expensive voltage reference)
  Includes resistor tolerances, voltage source precision, ADC precision parasitic resistance in wiring

## Slide 114: Wheatstone Bridge Error Analysis
Absolute Temperature Knowledge 1.0K
  Error analysis indicates 0.8 K maximum absolute temperature error for factory settings
  0.4 K temperature error with calibration
  Error values taken from reference components
Electrical noise (0.1K STD)
  ADC (65nV RMS)
  Thermal Noise Floor 80nV (10Hz BW)
  Over 80dB 60Hz suppression (Worst case 12uV)
    13uV < 137uV (0.05K step size)
Voltage Supply
Error
Thermistor Error

## Slide 115: Thermistor - Current Source
Current Source

## Slide 116: Voltage Divider Analysis
Compare accuracy to wheatstone bridge
  Error above 1.6K

## Slide 117: Heater Control
PWM Control of MOSFET
12-bit PWM control -> 74mW steps
200W maximum target heater power (cost)
Heater power supply isolated from low voltage components
Able to handle up to two 20W heaters if necessary
One 200W heater for targets
Meets requirements
Switching P-channel MOSFET controlled with low voltage MCU pin
Highest power heater is 5.1 ohm or 153W with 28V supply
  Max power needed is 70W
  Limit supply to 300W for cost
Power MOSFET with Rds = 20mOhm
  Predicted power dissipated by transistor is 5W (fully on)
NPN transistor for voltage isolation

## Slide 118: Power Supplies
Low Voltage Power
  Variable linear regulators (0.8V to 10V)
  12V AC/DC converter 12W
    Total power needed 500mW
    myRIO powered from USB
28V Supply
  Supplies target heater
  320W PSU
  Maximum heater draw is 200W with 50% margin
  Room for 2 additional heaters if necessary

## Slide 119: Thermistor Noise Coupling
Predict possible noise sources and model capacitive and inductive coupling
Assume worst case scenario of two floating parallel wires 2 radii apart for 1m (inside shaft)
  Capacitance = 100pF -> -75dB
  Inductance = -184dB
Voltage coupled is -75dB (of 28V) or 170mV – does not meet noise requirement -> add filtering
Worst noise source is 1KHz Heater control (LPF removes higher frequencies)
  Add differential RC Filter (insertion loss can be measured to reduce error)
  2uVpeak noise seen at ADC (2mK)
  Radiative coupling negligible
Shield thermistor cabling/pcb for improved suppression of unaccounted sources (motor control, stage)

## Slide 120
Data Budget
Data Generation |  | 
Contact Sensors |  | 
Bytes per Sample | (bytes) | 4.00
Rate | (Hz) | 10.00
Data Rate per sensor | (Bytes/sec) | 80
Number of Contact Sensors | (--) | 5
Total Data Generation | (Bytes/sec) | 400.00
IR Sensors |  | 
Bytes per Sample | (bytes) | 4.00
Rate | (Hz) | 10.00
Data Rate per sensor | (Bytes/sec) | 80
Number of Sensors | (--) | 5
Total Data Generation | (Bytes/sec) | 400.00
Distance Sensor |  | 
Bytes per Sample | (bytes) | 3.00
Rate | (Hz) | 10.00
Data Rate per sensor | (Bytes/sec) | 70
Number of Sensors | (--) | 1
Total Data Generation | (Bytes/sec) | 70.00
Total Raw System Data Generation | (kBytes/sec) | 0.87
Overview |  | 
Timestamp Size | (bytes) | 4.00
Margin Added | (percent) | 15.00%
Total System Data Generation (with margin) | (kBytes/sec) | 1.00

## Slide 121: Power Budget
Main Board Components |  | 
Microcontroller | (V) | 3.30
 | (mA) | 200.00
 | # | 0
 | (mW) | 0
ADC | (V) | 5.00
 | (mA) | 0.40
 | # | 3
 | (mW) | 6
LED | (V) | 5.00
 | (mA) | 3.00
 | # | 5
 | (mW) | 75
Motor Contoller | (V) | 5.00
 | (mA) | 15.00
 | # | 0.00
 | (mW) | 0
Digital Temperature Sensor | (V) | 5.00
 | (mA) | 0.50
 | # | 1.00
 | (mW) | 2.5
Digital Thermocouple Converter | (V) | 5.00
 | (mA) | 1.00
 | # | 1.00
 | (mW) | 5
SPI Isolator | (V) | 5.00
 | (mA) | 10.00
 | (mW) | 50
I2C Isolator | (V) | 3.30
 | (mA) | 6.00
 | (mW) | 19.8
Current Monitor | (V) | 5.00
 | (mA) | 13.00
 | (mW) | 65
MISC | (mW) | 100.00
Voltage Regulation |  | 
10V Precision Regulator | (V) | 2.00
 | (mA) | 5.00
 | (mW) | 10
5V Precision Regulator | (V) | 7.00
 | (mA) | 5.00
 | (mW) | 35
HP Linear Regulator | (V) | 6.00
worst case | (mA) | 25.00
 | (mW) | 150
LP Linear Regulator | (V) | 2.30
 | (mA) | 7.00
 | (mW) | 16.1
3.3V Linear Regulator | (V) | 1.70
 | (mA) | 7.00
 | (mW) | 11.9
3V Linear Regulator | (V) | 2.00
 | (mA) | 7.00
 | (mW) | 14
Switching Regulator | (mW) | 42.00
 | (Eff %) | 80%
 | (mW) | 8.4
Margin | (%) | 15%
Total Main Board Power | (W) | 0.44
Sensors |  | 
Contact Sensors |  | 
Supply Voltage | (V) | 5.00
Supply Current | (mA) | 1.00
Supply Power (each) | (mW) | 5
Number of Sensors | (--) | 5.00
Total Power Draw | (mW) | 25.00
IR Sensors |  | 
Supply Voltage | (V) | 3.00
Supply Current | (mA) | 2.00
Supply Power | (mW) | 6
Supply Voltage | (V) | 3.00
Supply Current | (mA) | 2.00
Supply Power | (mW) | 6
Supply Voltage | (V) | 3.00
Supply Current | (mA) | 2.00
Supply Power | (mW) | 6
OS36 |  | 
Supply Voltage | (V) | 3.30
Supply Current | (mA) | 1.50
Supply Power (each) | (mW) | 4.95
TPT300V |  | 
Supply Voltage | (V) | 9.00
Supply Current | (mA) | 22.00
Supply Power (each) | (mW) | 198
Number of Sensors | (--) | 5.00
Total Power Draw | (mW) | 30.00
Distance Sensors |  | 
Margin | (%) | 15%
Total Sensor Power | (W) | 0.06
Heaters |  | 
Patch Heater Targets |  | 
Supply Voltage | (V) | 28.00
Equivalent Resistance | (ohm) | 2.40
Supply Current | (A) | 11.67
Duty Cycle | (%) | 60.00%
Supply Power (each) | (W) | 196.00
Number of Patch Heaters | (--) | 1.00
Total Patch Heater Draw | (W) | 196.00
Transistor Heat Dissipation | (W) | 3.40

## Slide 122: Heat Dissipation
52mW
28C
50 mW
31C
200mW
41C
150 mW
31C
28 mW
27C
10 mW
28C
200mW
47C
20 mW
29C
20 mW
29C
65 mW
36C
Power MOSFET
Predicted 3.41W at full power
For 5W dissipation temperature raise by 44C
Final temp 69C (rated 150C)
All components within operating temperature range

## Slide 123: Integration & Test Backup

## Slide 124: COTS Infrared Temperature Sensor: V&V
DR 1.3.2 Five non-contact IR sensors shall be integrated into STATIS
DR 1.3.1.1 Area of target surfaces shall be larger enough such that the FOV of each non-contact IR sensor is spanned completely by the target surface at the maximum separation distance of 76mm.
Design Requirement | Type of Test | Pass Criteria
DR 1.3.2 | Test/Inspection | -Mechanical: - Fit in IR Stand holes. -Wires don’t get pinched during state movements. -Electrical: - Verify that sensors provide data when integrated into DAC system. - All wires shall fit in TVAC cable pass throughs.
DR 1.3.1.1 | Test/Inspection | -Target Material shall be 2.25” in diameter -Measured by calibrated calipers.

## Slide 125: Distance Requirements: V&V
DR 1.1 The distance between the target surface and non-contact infrared temperature sensor shall be adjustable through user input commands.
  DR 1.1.1 Minimum Distance of 7mm ±0.01mm.
  DR 1.1.2 Maximum Distance of 76mm ±0.01mm.
  DR 1.1.3 Distance Variable in 3 incremental steps.
Design Requirement | Type of Test | Pass Criteria
DR 1.1 | --- | DR 1.1.1 – 1.1.3 are met.
DR 1.1.1 DR 1.1.2 DR 1.1.3 | Test/Inspection | -Distance commanding works through use of Ball’s LabVIEW A3200 machine controller system. -Distances measured by calibrated calipers

## Slide 126: Rotation Design Requirements: V&V
DR 1.3 Every target surface temperature will be measured by every non-contact IR temperature sensor during the allotted test time.
  DR 1.3.1 Five target surfaces
  DR 1.3.2 Five IR temperature sensors.
Design Requirement | Type of Test | Pass Criteria
DR 1.1 | --- | DR 1.1.1 – 1.1.3 are met.
DR 1.1.1 DR 1.1.2 DR 1.1.3 | Test/Inspection | -Distance commanding works through use of Ball’s LabVIEW A3200 machine controller system. -Distances measured by calibrated calipers

## Slide 127: Subsystem Checkouts: Stage
Requirements Verified:
  1.1.1 Min distance 7mm
  1.1.2 Max distance 76mm
  1.1.3 Achieve 3 steps
Location: Ball facilities ambient
Systems: Mechanical Stager, Software
Command Distance
Receive Position
Software
Stager Control Com
Manually Measure
Verify Equivalence
Repeat
Risks Mitigated > Action for Failed Test
  Ball’s existing stager control > Rework software
  Verify functioning stager > Switch to a functioning stager

## Slide 128: Management Backup

## Slide 129: PDR Risk Matrix
 |  | 3 | 
 |  |  | 1
 |  | 2 | 
 | 4 |  | 
Probability of Failure
Importance
High
Low
Low
High
Thermal modeling accuracy
  Needed additional research and implementation in model
Access to Ball’s facilities and hardware
  No clear point of contact
Prove temp control system is capable of meeting requirements
  Temp control essential to project
Purchasing schedule risk (order/delivery time frames)
  No parts chosen yet

## Slide 130: PDR Risk Matrix
 |  | CPE.2 CPE.4 | CPE.1 CPE.3 CPE.5
Probability of Failure
Importance
High
Low
Low
High
CPE.1: Sensor Selection
→ Structural Design Dimensions, Budgetary Constraints
CPE.2: Mechanical System
→ Manufacturability, Sufficient Torque
CPE.3: Thermal Modeling and Control
→ Thermal Rejection and Heater Design
CPE.4: Electrical & Software Systems
→ Thermistor Accuracy, Thermal Precision, Development
Time
CPE.5: TVAC Integration
→ Outgassing Specifications, 12 Hour Testing Window

## Slide 131: CDR Risk Matrix
 | CPE.4 | CPE.3 | CPE.5
 |  | CPE.2 | 
 |  |  | CPE.1
Probability of Failure
Importance
High
Low
Low
High
CPE.1: Sensor Selection
→ Survive Bake Out
CPE.2: Mechanical System
→ Parts Acquisition, Manufacturing Schedule, Rotational
Alignment
CPE.3: Thermal Modeling and Control
→ Heat Dissipation and Control Feasibility
CPE.4: Electrical & Software Systems
→ Parts Acquisition, Manufacturing Schedule
CPE.5: TVAC Integration
→ Materials Acquisition and XXXXXX

## Slide 132: Pre-Testing Risk Matrix
 | CPE.4 | CPE.3 | CPE.5
 | CPE.2 |  | CPE.1
Probability of Failure
Importance
High
Low
Low
High
CPE.1: Sensor Selection
→ Mechanical Integration and Electrical Interface
CPE.2: Mechanical System
→ Rotation, Translation, Interface with Provided
Hardware
CPE.3: Thermal Modeling and Control
→ Heat Dissipation and Control Feasibility Algorithms
CPE.4: Electrical & Software Systems
→ Development
CPE.5: TVAC Integration
→ Materials Acquisition and XXXXXX

## Slide 133: Post Testing Risk Matrix
CPE.4 | CPE.4 | CPE.3 | CPE.5
CPE.3 |  | CPE.2 | 
CPE.5 | CPE.2 |  | CPE.1
 | CPE.1 |  | 
Probability of Failure
Importance
High
Low
Low
High
CPE.1: Sensor Selection
→ Mechanical Integration and Electrical Interface
CPE.2: Mechanical System
→ Wire Harnessing
CPE.3: Thermal Modeling and Control
CPE.4: Electrical & Software Systems
CPE.5: TVAC Integration