## Slide 1: BUBO BUBO Test Readiness Review March 3rd, 2020
Presenters: Charlotte Bellerjeau, Andrew Fendel, Karim Krarti, Kaitlyn Olson, Jesse Williams
Customers: Dr. Brian Argrow and Christopher Choate Advisor: Dr. Donna Gerren
Team: Charlotte Bellerjeau, Andrew Fendel, Keaton Fitton, Ethan Gabrielle, Karim Krarti, Nickolas Mororo, Kaitlyn Olson, Seif Said, Jesse Williams, Jeremy Yanowitz

## Slide 2: Overview

## Slide 3: Project Purpose
The goal of BUBO BUBO is to design, build, and test an unmanned, radio-controlled (RC), box-wing aircraft. The aircraft will be a scalable data collection platform for a Flush Air Data Sensing (FADS) system, which will collect pressure data to aid in the study of turbulence by Dr. Brian Argrow of the University of Colorado Boulder.

## Slide 4: Specific Objectives – Levels of Success
Notes: Because FADS is not critical for first flight, manufacturing has been pushed to allow test flight preperation

## Slide 6: Functional Block Diagram Of BUBO BUBO for Manufacturing Status Review

## Slide 7: Critical Project Elements
Aerodynamics
Structures
FADS
Propulsion
Power
Configuration
Stability
Flight Performance
Power Distribution
Component Placement
Propulsive Setup
Endurance
Efficiency
Placement
Integration
Relative Wind Recovery
System Integration
Structural Integrity
Survivability
Pressure Distribution
Controls
Gains
Stability
Flight Performance
Control Surfaces
Materials

## Slide 8: Design Overview

## Slide 9: Baseline Design
Box-wing Configuration
  Top wing swept back 30°
  Bottom wing straight
1 m span
0.3 m chord
0.3 m stagger
0.3 m gap
Total Mass: 3.65 kg
NACA 6412
NACA 23112

## Slide 10: Boom Design
In order to address negative static margin and improve longitudinal stability, a ballasted boom was added to the front of the aircraft
Extensive vibrational analysis has been done for the boom
Concluded that vibrations will not resonate with any natural frequencies, and are small enough to not have any significant effect during regular flight
Unballasted C.G. Location
Unballasted Mass
Desired C.G. Location
Ballast Mass
Boom Quadratic Solver
Boom Length
Notes: Boom reduces risk of damage to top wing and eliminates the unstable tumble mode

## Slide 11: Schedule

## Slide 12
Notes: Note any major changes since CDR
Whiffletree testing pushed back by one week  this is due to the need for the CAD to be modified/updated to account for our airfoil change
Note that we previously planned to start manufacturing the first full airframe before the whiffletree test was completed, we have decided to wait until the results of the whiffletree testing are conclusive to begin construction of the full airframe, otherwise we could be wasting materials if the whiffletree test shows previously undiscovered failures
Flight test pushed back by one week  this is due to the dependency on the whiffletree test which also got pushed, NOTE: flight test is a parred down version of the full plane (no sensors, minimal battery, going for very minimal flight time just a take off a circle and a landing to prove feasibility of flight)
Discuss need for margin on appropriate tasks
- Plenty of margin for power and endurance testing to chan
Note major milestones

## Slide 13: Overall Schedule
Critical Path
Deliverables
Manufacturing/Assembly
Testing

## Slide 14: Testing

## Slide 15: Test Overview
Whiffletree
Static Thrust
Controls
Power and endurance
Flight Test
  Flight test readiness (Glide test)
FADS
Whiffletree
Static Thrust
Controls
Power and endurance
Flight Test
  Flight test readiness (Glide test)
FADS

## Slide 16: Whiffletree Test
Verifying: stress models and finite element analysis
Validating: ability to withstand expected aerodynamic loads, survivability requirement

## Slide 17: Whiffletree Test Setup and Procedure
Whiffletree used in ASEN 2001
  Straps placed on ribs
  Whiffletree assembled so weight is distributed close to expected aerodynamic loading conditions
Added weight in 5/2.5 lb increments
  For top wing, to failure
  For bottom wing, until bucket was full
Safety Considerations
  Safety goggles
  Floor protection
  Kept all team members away from testing setup

## Slide 18: Whiffletree Results
Top (Swept) wing:
  Max Load: 70lb
  Failure Mode: trailing edge bent downwards
Bottom (Straight) wing
  Max Load: 65lbs
  Failure Mode: 3 middle ribs
Conclusion: Airframe will withstand expected flight loads
Notes: This is important to us because it means construction of the full airframe could begin and so testing can continue on schedule.
These results are currently being analyzed to validated our finite element analysis and to identify areas where structure could be reduced or eliminated to aid in weight reduction

## Slide 19: Whiffletree Results
Top (Swept) wing:
  Max Load: 70lb
  Failure Mode: trailing edge bent downwards
Bottom (Straight) wing
  Max Load: 65lbs
  Failure Mode: 3 middle ribs
Conclusion: Airframe will withstand expected flight loads
Notes: This is important to us because it means construction of the full airframe could begin and so testing can continue on schedule.
These results are currently being analyzed to validated our finite element analysis and to identify areas where structure could be reduced or eliminated to aid in weight reduction

## Slide 20: Whiffletree Results
Top (Swept) wing:
  Max Load: 70lb
  Failure Mode: trailing edge bent downwards
Bottom (Straight) wing
  Max Load: 65lbs
  Failure Mode: 3 middle ribs
Conclusion: Airframe will withstand expected flight loads
Notes: This is important to us because it means construction of the full airframe could begin and so testing can continue on schedule.
These results are currently being analyzed to validated our finite element analysis and to identify areas where structure could be reduced or eliminated to aid in weight reduction
Eliminates the risk of plane breaking apart under flight loads

## Slide 21: Static Thrust Test
Verifying: Propulsion performance models
Validating: Thrust and Endurance requirements

## Slide 22: Static Thrust Test: Setup and Procedure
Informs motor choice and confirms thrust is appropriate for flight
Safety Considerations
  Balanced propeller prior to test
  Slowly throttled motor up to full to make sure vibrations would not cause issue.
  Shielding of motor and propeller to protect all individuals involved
DBF Static Thrust Stand
  Uncertain results due to uncalibrated equipment
Notes: Thrust testing Measures thrust of motor/propeller combination
This information, along with our models, is intended to aid in motor/propeller selection

## Slide 23: Static Thrust Testing Results
Propulsion: ELM4025-B and APC 10x7E
  Chosen for small size and existing testing data
  Obtained data is compared to model predictions
  59.5% discrepancy discovered
  Causes:
    Load cell proportional calibration error.
    Motor unable to accelerate to expected maximum RPM.
Conclusion: Test stand results can be scaled based on comparison to models and manufacturer performance estimates until test stand can be fixed.
Notes:   Magnitude is uncertain, thrust profiles appear accurate.
  A linear calibration error is possible.
  Rectify by comparison to models and manufacturer performance estimates.

## Slide 24: Controls Test
Verifying: modeled gains are appropriate, desired deflections are attainable
Validating: navigation and control requirements

## Slide 25: Controls Test Setup and Procedure
Autopilot Test
Connected elevons to PixHawk controller
Rotated PixHawk and checked for appropriate elevon response
Manual Test
Elevons remotely connected to controller
Test roll and pitch maneuvers in each direction, verifying that elevon response is appropriate
  Modify gains to allow for maximum elevon deflection

## Slide 26: Controls Results
Verified correct elevon responses
Lengthened servo arms to reach desired maximum deflection of at least 30 degrees
Elevon response is adequate to move forward to glide testing and flight testing

## Slide 27: Flight Test
Verifying: aerodynamic stability, structural models on takeoff and in-flight
Validating: flight stability and takeoff/landing survivability requirements
Notes: This is the only test we have left on our critical path and it is scheduled for __(insert date here)____

## Slide 28: Safety Considerations for Flight Testing
Obtaining permission from Dan Hesselius, Director of CU Flight Operations, before any flight testing
  Will be piloting maiden flight test
Checking battery status before connecting to electronics
Extensive testing done on every subsystem before full flight test
  Separately and integrated
Clearing flight space before launch

## Slide 29: Flight Test Readiness
Glide test verified airframe stability, control responses.
Notes: Glide test verified airframe stability, control responses

## Slide 30: Flight Test Setup and Procedure
Location: CU Boulder South
Pilots: Dan Hesselius and Jeremy Yanowitz
Pre-flight checklist
Launch aircraft from table bungie
Ascend to cruising altitude
Perform several maneuvers and obtain Cooper-Harper rating for each
Descend and land safely
Identify any damage and determine re-flight time

## Slide 31: Flight Test Results
Obtain Cooper-Harper ratings for each maneuver
Identify where improvements must be made
Maneuver | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Takeoff |  |  |  |  |  |  |  |  |  | 
Ascent |  |  |  |  |  |  |  |  |  | 
Steady flight |  |  |  |  |  |  |  |  |  | 
30° banked turn |  |  |  |  |  |  |  |  |  | 
Descent |  |  |  |  |  |  |  |  |  | 
Landing |  |  |  |  |  |  |  |  |  | 
Flight Performance
Desired performance
Adequate performance
Control
No control

## Slide 32: Testing Status Recap
Notes: This is the only test we have left on our critical path and it is scheduled for __(insert date here)____

## Slide 33: Whiffletree Status
Monokote wing section
Produce wing section pieces
Assemble complete wing section
Perform whiffletree test
= Completed
= In Progress
= Planned
Assemble whiffletree

## Slide 34: Static Thrust Testing
Motor 1 (GH SMJ) Preliminary Test
Motor 2 (EFLM4025B) Thrust Test
Motor 2 Endurance Test
= Completed
= In Progress
= Planned

## Slide 35: Controls
Test the PixHawk
Test the GPS Module
Test the Telemetry Kit
Integrate Components
Integrate the Components with Control Surfaces
Integrate the System into the Airframe
Manual Control Setup
= Completed
= In Progress
= Planned
Verify Elevons Deflection Behavior
Ground Test
Flight Test
Expected: March 8

## Slide 36: Power
Initial Functional Model Circuit
Autopilot Integration Circuit
Dynamometer Data Collection Circuit
Airframe Wiring & Component Layout Test Circuit
Endurance Test Circuit
Aircraft Final Circuit
= Completed
= In Progress
= Planned

## Slide 37: Flight test readiness (Glide test)
Construct full airframe
Ensure control system is functional
Verify no aeroelasticity issues
Complete preliminary glide test
Practice synchronized longboarding
= Completed
= In Progress
= Planned

## Slide 38: Flight Test
Produce full airframe
Verify systems integration
Integrate electronics, power, propulsion
Certification, FAA Registration
Perform flight test
= Completed
= In Progress
= Planned
Conduct glide test
Expected: March 8

## Slide 39: FADS
FADS Functional Circuit Built
Preliminary Data Collection Test
FADS Pressure Isolation Test
Full Airframe Integration
= Completed
= In Progress
= Planned
FADS Circuit Designed
Parts Ordered
Expected: March 16
Expected: March 15
Expected: March 14

## Slide 40: Budget

## Slide 41
Chart: 
| Structural | Electronics | Propulsion | FADS | Security Deposit | MK II | Remaining
Current Budget | 792.43 | 530.32 | 582.2 | 446.7 | 200 | 1547 | 1551.35
Notes: MK II is about $800 less than we spent on the first iteration because we had several fixed costs from buying tools (like a heat gun) and a few bulk items (like our carbon fiber tubes) that will not need to repurchase. In addition, we are not implementing the FADS system into the first airframe to prevent damage to the system in the case of a crash on the first flight.

## Slide 42
Chart: MK II
| Structural | Electronics | Propulsion
MK II | 501.28 | 458.71 | 587.01
MK II Electronics | 
Flight Controller (Pixhawk) | $330.00
Telemetry Radio | $22.99
Receiver | $39.55
Wires | $19.98
Arduino (Teensy 3.5) | $24.95
Buck DC to DC Converter | $11.25
XT60H Bullet Connector | $9.99
MK II Structure | 
Glue, Accelerator, Wood Filler | $108.78
Balsa Wood | $167.20
Bass Wood | $19.35
Birch Plywood | $130.95
Aluminum Rods | $3.04
Boom Dowels | $3.68
Ultracoat | $45.97
Tooling (screws, sandpaper, etc.) | $22.31
MK II Propulsion | 
ESC | $26.99
Batteries | $456.81
Propeller | $3.21
Motor | $100.00
Notes: This budget for MK II represents a total loss on MK I (like if the plane caught fire and we lost everything in it). We are not expecting to actually spend $1547 on the second iteration of our aircraft, but we budgeted for it just in case.
These charts show the items that would need to be repurchased that have been accounted for in this budget.
The yellow items here are more expensive items that we don’t want to have to replace if possible. To mitigate this budget risk, we are doing our maiden flight of MK I with only 4 batteries instead of 16 and we have reinforced the structure surrounding the pixhawk to attempt to protect it as much as possible in the case of a rough landing.

## Slide 43
Chart: Spending Thus Far
| MK I Spending ($2351.65) | Security Deposit ($200.00) | MK II Spending ($176.92) | MK II ($1370.08) | Remaining ($1551.35)
Current Budget | 2351.65 | 200 | 176.92 | 1370.08 | 1551.35
Total Spent: $2728.57, 48%
Total Remaining: $2921.43, 52%
Notes: MK II Spending Thus Far
$45.97 on monokote
$130.95 on plywood

## Slide 44: Electronics & Controls

## Slide 45: Propulsion

## Slide 46: Airframe

## Slide 47: FADS

## Slide 48
Thank You
Questions?

## Slide 49: Directory
Title
Overview Title
Project Purpose
Levels of Success
CONOPS
FBD
Critical Project Elements
Design Overview
Baseline Design
Boom Design
Schedule Title
Testing Schedule
Overall Schedule
Testing Title
Test Overview
Whiffletree Test Title
Whiffletree Setup and Procedure
Whiffletree Results
Whiffletree Results zoomed
Whiffletree Results
Static Thrust Test Title
Thrust Test Setup and Procedure
Thrust Testing Results
Future Thrust Testing
Controls Test Title
Controls Test Setup and Procedure
Control Test Video
Controls Results
Flight Test Title
Flight Test Readiness (Glide video)
Flight Test Setup and Procedure
Flight Test Results
Testing Status Recap Title
Whiffletree Status
Static Thrust Test Status
Controls Status
Power Status
Flight Readiness (Glide Test) Status
Flight Test Status
FADS Status
Budget Title
Current Budget
MK II Budget
Spent vs Remaining Budget
Electronics and Controls Procurement
Propulsion Procurement
Airframe Procurement
FADS Procurement
Questions
Directory
Backup Slides Title
Boom Design Backup Title
Boom Trade Studies (1 vs 2)
Boom Trade Study (Eigenvalues)
Boom Design Solver
Boom Vibrational Analysis Formulation
Boom Equivalent Torsional Spring Constant
Boom Vibrational Analysis Initial Conditions
Boom Analysis Results (Short Time Scale)
Boom Analysis Result (Long Time Scale)
Boom Analysis Results (Frequencies)
Thrust Testing Backup Title
Propulsion Models
Propulsion Models (Assumptions, Margins, and Limitations)
Propulsion Model Verification
Using Models to Aid Motor Selecion
E-flite 25 Power 1250 Kv Motor
Static Thrust Test Video
Flight Testing Backup Title
Cooper Harper Descriptions
Flight Checkout
Flight Test Preparation
Electrical Backup Title
Main Circuit
FADS Circuit

## Slide 50: Backup Slides

## Slide 51: Boom Design and Vibrational Analysis

## Slide 52: Boom Design Trade Studies
Investigated weight of boom mass vs necessary weight in order to select an adequate combination

## Slide 53: Boom Design Trade Study
Stability modes are minimally impacted by the choice.

## Slide 54: Boom Design Solver
Using center of gravity equation, the following quadratic equation was developed, with the only unknown parameter being the boom length, L
where
m = boom mass
mac = unballasted aircraft mass
q = mass/length of dowel
x = location of dowel's start relative to unballasted C.G.
xcg = location of desired C.G.
xac = location of unballasted C.G.
This equation was then solved to find the required boom length

## Slide 55: Boom Vibrational Analysis Formulation
Equations of motion were found using Lagrange's equation, an energy method:
Energies and Rayleigh's dissipation function are given by:
And qs represents each degree of freedom:

## Slide 56: Boom Equivalent Torsional Spring Constant
Apply a known force at a known length, measure resulting vertical displacement and calculate k according to:

## Slide 57: Boom Vibrational Analysis Initial Conditions
In order to determine the initial displacements of the boom, the aircraft's pitch and yaw responses to both 10° perturbations and natural modes were examined
  Represents maximum expected in-flight perturbations
The maximum pitch and yaw rates were found and converted into linear boom velocity assuming rigid body motion
Displacements resulting from drag induced moments during these rotations then found and used as initial conditions, with an additional factor of safety of 2:
θ1,0 = 7.6919e-4o
θ2,0 = 2.0435e-4o

## Slide 58: Boom Vibrational Analysis Results
Lagrange's equation yields the following equations of motion:
Numeric simulation produced time response plots

## Slide 59: Boom Vibrational Analysis Results
Extended time series to show (slight) effect of drag dissipation

## Slide 60: Boom Vibrational Analysis Results
Vibration oscillation frequencies:
f1 = 2.578 Hz f2 = 2.518 Hz
Natural frequencies of oscillatory modes:
flong mode = 0.0787 Hz
flat mode = 0.653 Hz
Motor frequency range:
7,000 – 15,000 rpm ≈ 116 – 250 Hz
Therefore concluded resonance with the boom won't be an issue

## Slide 61: Thrust Testing

## Slide 62: Propulsion Models

## Slide 63: Propulsion Models
Assumptions
Cruise Airspeed: 14.5 m/s
Stall Airspeed: 7.5 m/s
Target Thrust: 10 N
Maximum Thrust: 20 - 30 N
Margins and Limitations
•AVL Drag:
•Estimated at 4 N, FoS of 2.5 is applied due to uncertainty
•Accounts for air density via:
• Does not consider changes in Reynold’s number due to altitude.

## Slide 64: Propulsion Model Verification

## Slide 65: Using Models to Aid Motor Selection
General Rationale:
Full throttle flight condition defines the desired max RPM.
Max RPM defines Kv (In conjunction with battery voltages)
Power estimates defines desired maximum motor power load.
The Ideal Motor (33% throttle @ cruise)
1372.5 RPM/V (Kv)
1390.4 W @max
285.14 W @cruise
125.2 A @max
The Ideal Motor (50% throttle @ cruise)
1156.1 RPM/V (Kv)
662.64 W @max
236.65 W @cruise
59.7 A @max

## Slide 66: E-flite 25 Power 1250 Kv Motor (EFLM4025B)
Specifications/Features
1250 kV
50 A (continuous)
58 A (burst)
850 W (continuous)
183 g
Can produce easily enough thrust to overcome drag even with 2.5 FoS. Capable of running 8-12 inch propellers, allowing for a range of flight requirements.

## Slide 67: Flight Testing

## Slide 68: Cooper-Harper Rating Descriptions
1 - Excellent, highly desirable
  Pilot compensation not a factor
2 - Good, negligible deficiencies
  Pilot compensation not a factor
3 - Fair, some mildly unpleasant deficiencies
  Minimal pilot compensation required
4 - Minor but annoying deficiencies
  Moderate pilot compensation
5 - Moderately objectionable deficiencies
  Considerable pilot compensation
6 - Very objectionable, yet tolerable deficiencies
  Extensive pilot compensation
7 - Major deficiencies
  Adequate performance not attainable with maximum tolerable pilot compensation
8 - Major deficiencies
  Considerable pilot compensation for any control
9 - Major deficiencies
  Intense pilot concentration required for control
10 - Major deficiencies, unpilotable
  Control will be lost during operation

## Slide 69: Flight Checkout
Steps to BUBO flight testing:
  Flight Director Dan Hesselius requires proof of piloting ability
  Wants to see piloting of a fast, difficult to control aircraft
    Built ducted fan, elevon-only jet to fulfill requirements
    Shares control setup with BUBO
Flight checkout scheduled
Another step:
  MSR Goal: Will acquire one FAA sUAS Registration Number to use on test airframes.
    Must wait for Temp License before applying --> still pending

## Slide 70: Flight Testing Preparation
Flight testing will be conducted under FAA 14 CFR Part 107
  Requires test pilot to hold FAA Remote Pilot Certificate
Airmen Knowledge Test Taken (2/1/2020) (Passed)
  Remote Pilot Certificate applied for
  Expecting Temp License later this week
Will acquire one FAA sUAS Registration Number to use on test airframes.
  Must wait for Temp License before applying
  Costs $5 per registration number
    Can be swapped between airframes as long as only one is airborne at a time

## Slide 71: Electrical

## Slide 72: Main Circuit
Aircraft Circuit Design / Analysis complete, ready for manufacturing
Switch from passive resistor voltage control to DC-DC buck converter for powering FADS system – more robust solution

## Slide 73: FADS Cicuit
FADS Circuit Design complete
  Using Teensy for motor testing as well as FADS data collection
Teensy acquired but awaiting orders of I2C Mux and Transducers
Code developed for data collection, awaiting motor testing
Taking low priority as not essential to achieve flight <-- top priority
* quarter for scale