## Slide 1
High Endurance Rapidly Deployable Collaborative UAS (HERD-CU)
Preliminary Design Review
11 October 2021
Jason Peloquin (Project Manager)
Vyacheslav Rychenko
Patrick Tippens
Zachary Vanlangendonck
Dante Vigil
Christian Williams
Selmo Almeida
Nicholas Boender
Anthony Danna
Ethan Fleer
Collin Kasunic
John Oliver
Customer: Professor John K. Mah
Notes: Flip the slide template. Title on the left and make more space in general. Move the page numbers to the right side. Mka the timeline on the bottom of each slide to half the slide. Include transition slides to give a pause moment.

## Slide 2
Presentation Outline
Project Overview
Baseline Designs
Feasibility Studies
Summary
Logistics
Appendix Slide
Notes: Take our the abcd… from the project overview. Keep the baseline design details

## Slide 3
UAS: Unmanned Aerial System- includes ground systems, launch systems, and any UAV(s) required to provide required overwatch duration.
UAV: Unmanned Aerial Vehicle - a single aircraft
CONOPS: Concept of Operations
FMC: Fully Mission Capable
GTOW: Gross Takeoff Weight
MTOW: Maximum Takeoff Weight
MSL: Mean Sea Level
RFP: Request for Proposal
Definitions
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Appendix Slide
Notes: Move this to the appendix. Announce what each acronym means. Can have acronyms but just say the full name.

## Slide 4
BIG PINE KEY
Mission Statement
The purpose of Phase 1 of the High Endurance Rapidly Deployable Collaborative UAS (HERD-CU) is to develop a high endurance, human-portable, rapidly deployable unmanned aerial vehicle capable of supporting mission overwatch profiles that demand agility, low cost, high persistence, and broad coverage capability.
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Appendix Slide
Notes: Too many words. Split into two slides? Change the bolding or color (highlight or underline) important takeaways from slide.

## Slide 5
BIG PINE KEY
Design Objectives
Key Design Objectives:
Single UAV Endurance of up to 4 hours, UAS endurance up to 12 hours
  3UAVs ⨉ 4hr = 12hr endurance
Low weight and single-operator portable
  Total system less than 50 lbs and less than 5ft disassembled
Single operator launched without a runway
Under $5,000 build cost (omitting R&D)
Operational Envelope up to 10k ft MSL
Mission-capable payload bay
Operational in inclement conditions, rain, cold, and heat
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Appendix Slide
Notes: Too many words. Split into two slides? Change the bolding or color (highlight or underline) important takeaways from slide.

## Slide 6
Why Build a New UAV?
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Current UAS solutions:
Lack high endurance
Expensive
Lack portability
Require extensive training
CU HERD solution:
Cumulative UAS endurance of greater than 12 hours
UAV prototype cost < $5,000
Single operator transport, launch and service
Appendix Slide
Notes: Refit this onto the screen. Make the CONOPS take the whole page! Too much encroaching on the concops with the format!
Make so the numbers and stages are more reasonable. Shift grass up and add black box at the bottom similar to box 3!

## Slide 7
Concept of Operations (CONOPS)
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics

## Slide 8
Appendix Slide

## Slide 9
Functional Block Diagram (FBD)
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics

## Slide 10
FBD
KEY:
Physical connections
Connections via wireless method
Power supply connections
(illustrate subsystem
complexity and importance)
Appendix Slide

## Slide 11
Functional Requirements
FR1: The UAS shall provide a continuous overwatch window of 12 hours through the use of one or more UAVs (i.e. three UAVs each with 4 hours of endurance is acceptable).
FR2: UAS (including all UAVs and their supporting equipment) shall be transported, launched, recovered, and operated by a single person to satisfy Requirement 1 under a 10 minute launch window per UAV.
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Appendix Slide
Notes: Slides 9 and 10 are repetitive with slide 6. Might think about combining and removing less important info. Use colors to distinguish between which ones we will talk about in the presentation and the general list from contractor!
Better explain the FR1 to essentially show that 3 UAVs times 4 hours is 12 hour mission for example/

## Slide 12
Functional Requirements
FR3: UAS shall have short takeoff and landing capabilities to deploy in areas with unprepared launch surfaces and obstructed climb windows as specified by the customer.
FR4: UAV shall provide a payload bay to house a sensor suite.
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Appendix Slide

## Slide 13
Baseline Design
Conventional Fixed Wing Aircraft
High CL/CD
Mid/High range Aspect Ratio
Slight Wing Taper
Electric Propulsion System
Modular Payload Bay
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Elbit Skylark
Appendix Slide
Notes: Add visuals to this to complement the words! Maybe a CAD model if time?

## Slide 14
Critical Project Elements
Earth
Airframe Structure
Aerodynamics and Wing Design
Propulsion
Mechanics
Avionics
Safety Considerations
Simulations and Systems
Focus of Preliminary Design Review
Airframe Structure
Propulsion
Aerodynamics and Wing Design
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Critical Project Elements
Project Elements
Appendix Slide

## Slide 15
Feasibility Analysis
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics

## Slide 16
Aerodynamics and Wing Design
Design Considerations:
Aspect Ratio (AR) - Slide 17-18
Taper Ratio (λ) - Slide 19
Bending Moment - Slide 20
Airfoil - Slide 21 - 22
Lift Coefficient (CL) - Slide 23 - 25
Drag Polar (CD) - Slide 26-27
AoA - Slide 28
Span Efficiency - Slide 29
Performance - Slide 30
Span | 10ft
AR | ?
Chord | ?
Taper | ?
Airfoil | ?
Cl | ?
Cd | ?
AoA | ?
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
10ft Span partially satisfies FR2
Appendix Slide

## Slide 17
Aspect Ratio (AR):
Defined as wingspan, b,
squared over the planform wing area, S.
  b2/S
Affect aircraft
Performance parameters:
  Endurance
  Maneuverability
  Stability
Span | 10ft
AR | 15.59
Chord | ?
Taper | ?
Airfoil | ?
Cl | ?
Cd | ?
AoA | ?
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Aerodynamics and Wing Design
Appendix Slide

## Slide 18
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Aerodynamics and Wing Design
Span | 10ft
AR | 15.59
Chord | ?
Taper | ?
Airfoil | ?
Cl | ?
Cd | ?
AoA | ?
Span | 10ft
AR | 15.59
Chord | ?
Taper | ?
Airfoil | ?
Cl | ?
Cd | ?
AoA | ?
Appendix Slide

## Slide 19
Taper Ratio (λ): A ratio of root and tip chords
Affects CL/CD
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | ?
Cl | ?
Cd | ?
AoA | ?
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Aerodynamics and Wing Design
Appendix Slide

## Slide 20
Bending Moment:
Metric for how much load is held by each wing’s area.
Vortex Panel Method
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | ?
Cl | ?
Cd | ?
AoA | ?
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Aerodynamics and Wing Design
Appendix Slide

## Slide 21
Camber: NACA profiles determine thickness and camber
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | NACA 4412
Cl | ?
Cd | ?
AoA | ?
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Aerodynamics and Wing Design
Appendix Slide

## Slide 22
NACA 4412
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | NACA 4412
Cl | ?
Cd | ?
AoA | ?
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Aerodynamics and Wing Design
Appendix Slide

## Slide 23
Generated Lift (CL):
The ratio of lifting force to the force produced by dynamic pressure multiplied by area
  SLUF L = W
  Lift is quantified by the area created by a pressure distribution across an airfoil
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | NACA 4412
Cl | 1.118
Cd | ?
AoA | ?
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Aerodynamics and Wing Design
Appendix Slide

## Slide 24
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | NACA 4412
Cl | 1.118
Cd | ?
AoA | ?
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Aerodynamics and Wing Design
Appendix Slide

## Slide 25
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | NACA 4412
Cl | 1.118
Cd | ?
AoA | ?
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Aerodynamics and Wing Design
Appendix Slide

## Slide 26
Drag Polar (CD):
CD= CD0+CDi
  CD0 - Zero-lift drag coef.
    Drag from size, speed and altitude
    XFOIL Data interpolated
  CDi - Induced drag coef. at min. Power
    Drag from lift and vortices
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | NACA 4412
Cl | 1.118
Cd | ?
AoA | ?
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Aerodynamics and Wing Design
Appendix Slide
Notes: Explain the terms better because PAB don’t know aircraft stuff.

## Slide 27
Drag Polar (CD):
CD= CD0+ CDi = 0.063338
  CD0 = 0.030567
  CDi = 0.032771
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | NACA 4412
Cl | 1.118
Cd | 0.063
AoA | ?
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Aerodynamics and Wing Design
Appendix Slide
Notes: Explain the terms better because PAB don’t know aircraft stuff.

## Slide 28
AoA: Angle the wing is flying through the air
AoI: Angle between chord line and fuselage
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Aerodynamics and Wing Design
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | NACA 4412
Cl | 1.118
Cd | 0.063
AoA | 7.989°
Appendix Slide

## Slide 29
Span Efficiency Factor
change in drag with lift of a three-dimensional wing
- 0.7795447459 - 0.7795436358
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Aerodynamics and Wing Design
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | NACA 4412
Cl | 1.118
Cd | 0.063
AoA | 7.989°
Appendix Slide
Notes: DO NOT CHANGE IMAGE ASPECT RATIO

## Slide 30
Performance:
Max Lift - 118N
Weight - 71N
Drag - 19.5N
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Aerodynamics and Wing Design
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | NACA 4412
Cl | 1.118
Cd | 0.063
AoA | 7.989°
Appendix Slide

## Slide 31
Propulsion: Feasibility Goals
Propulsion - What do we need to know?
Levels of Success and FR’s
  Max Endurance Flight (FR1)
  Climbout (LS & FR3)
  30 mph headwind (LS)
Does the Market support it?
  Motor and Propellor combinations
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Appendix Slide

## Slide 32
Propulsion: Variables
Variable | Estimate by Aero Model | Estimate used in Prop Model | Typical Market Values
Weight (W) | 7.25 kg (16 lbs) | 7.25 kg (16 lbs) | 4 kg to 7 kg (9 lbs to 15 lbs)
Span Efficiency Factor (e) | .779 | .75 | .6 to .9
Chord Length (c) | .3048 m (12”) | .3048 m (12”) | .1778 m to 0.381 m (7” to 15”)
Taper Ratio (Ctip / Croot ) | .2828 | .2828 | .3 to 1
Aspect Ratio (AR) | 15.6 | 15.6 | 10 to 18
Wing Area (S) | .596 m2 (6.41 ft2) | .596 m2 (6.41 ft2) | .25 m2 to 1 m2 (2.69 ft2 to 10.76 ft2)
Span (s) | 3.048 m (10 ft) | 3.048 m (10 ft) | 2 m to 3 m (6.56 ft to 9.84 ft)
Zero Lift Drag (CD0 ) | .015 | .02 | .01 to .05
Propellor Efficiency (η) | ~ | 60% [1] | 75% to 90%
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Appendix Slide

## Slide 33
Propulsion: Max Endurance
Endurance Maximizing Velocity (Minimum Preq ) [1]
Coefficient of Lift (Lift = Weight) [2]
Thrust (Thrust = Drag) [1]
Power [2]
Results | IMP | SI
Treq END |  | 
Preq END |  | 
Vreq END |  | 
CLreq END |  | 
Treq Climbout |  | 
Preq Climbout |  | 
CLreq Climbout |  | 
Vreq Climbout |  | 
Treq Headwind |  | 
Preq Headwind |  | 
CLreq Headwind |  | 
Vreq Headwind |  | 
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Results | IMP | SI
Treq END | .861 lbf | 3.83 N
Preq END | .107 hp | 79.8 W
Vreq END | 28 mph | 12.5 m/s
CLreq END | 1.48 | 1.48
Endurance Flight satisfies FR1
Appendix Slide

## Slide 34
Propulsion: Climbout
Results | IMP | SI
Treq END | .861 lbf | 3.83 N
Preq END | .107 hp | 79.8 W
Vreq END | 28 mph | 12.5 m/s
CLreq END | 1.48 | 1.48
Treq Climbout |  | 
Preq Climbout |  | 
CLreq Climbout |  | 
Vreq Climbout |  | 
Treq Headwind |  | 
Preq Headwind |  | 
CLreq Headwind |  | 
Vreq Headwind |  | 
Levels of Success for Climbout: (measured from ground)
ɣ1 = 5.71°
ɣ2 = 11.3°
ɣ3 = 21.8°**
**outside Small Angle Approx
Rate of Climb (RoC) [2]:
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
γ
θ
𝛼
θ
θ
L
W
T
D
Treq Climbout | 8.16 lbf | 36.3 N
Preq Climbout | 1.33 hp | 993 W
CLreq Climbout | .975 | .975
Vreq Climbout | 36.7 mph | 16.4 m/s
Climbout satisfies FR3
Appendix Slide

## Slide 35
Propulsion: Headwind
Results | IMP | SI
Treq END | .861 lbf | 3.83 N
Preq END | .107 hp | 79.8 W
Vreq END | 28 mph | 12.5 m/s
CLreq END | 1.48 | 1.48
Treq Climbout | 8.16 lbf | 36.3 N
Preq Climbout | 1.33 hp | 993 W
CLreq Climbout | .975 | .975
Vreq Climbout | 36.7 mph | 16.4 m/s
Treq Headwind |  | 
Preq Headwind |  | 
CLreq Headwind |  | 
Vreq Headwind |  | 
Requirement for Headwind: 30 mph Headwind
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Treq Headwind | 0.75 lbf | 3.34 N
Preq Headwind | 0.116 hp | 86.84 W
CLreq Headwind | .950 | .950
Vreq Headwind | 35 mph | 15.6 m/s
Vwind
T
L
W
D
Appendix Slide

## Slide 36
Proof of Feasibility 1: PROPDRIVE v2 5050 580KV Brushless Outrunner Motor and APC
14x10 Folding Propeller Blade Set
Battery: 4-6S (22.2 V LiPo)
Power: 2000W Continuous
Max Thrust: ~ 52.5 N
Specific Flight Condition (PROPDRIVE Data Sheet)
18.5V - 1077W - 60.7A - 4.03kg thrust ~ 39.5 N
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Results | IMP | SI
Treq END | .861 lbf | 3.83 N
Preq END | .107 hp | 79.8 W
Vreq END | 28 mph | 12.5 m/s
CLreq END | 1.48 | 1.48
Treq Climbout | 8.16 lbf | 36.3 N
Preq Climbout | 1.33 hp | 993 W
CLreq Climbout | .975 | .975
Vreq Climbout | 36.7 mph | 16.4 m/s
Treq Headwind | 0.75 lbf | 3.34 N
Preq Headwind | 0.116 hp | 86.84 W
CLreq Headwind | .950 | .950
Vreq Headwind | 35 mph | 15.6 m/s
𝛼 = 12.5°
𝛼 = 6.8°
𝛼 = 6.8°
Propulsion: Market Analysis
[3] [4]
Appendix Slide
Notes: https://www.banggood.com/Racerstar-Racing-Edition-4108-BR4108-600KV-4-6S-Brushless-Motor-For-500-550-600-for-RC-Drone-FPV-Racing-p-1122900.html?cur_warehouse=CN
https://www.hobbypartz.com/02p-motor-607-mt4008-kv600.html

## Slide 37
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Endurance Estimations
Equation used by RC aircraft pilots to determine endurance
  Does not factor in unpowered glide
  Factors Climbout and Cruise
  Assumes mid-full throttle during climbout phase
Parameter | Value
Bcapacity | 6,000mAh
Bdischarge | 90%
Battery Packs | 5
Itakeoff | 60A
Icruise | 3.0A
R.O.C | 6.1 m/s
Time to M.A. | .5 - 4 min
This methodology for endurance passes FR1
Equation used in Tempest Estimates [1]
  Does not factor in unpowered glide
  Does not factor in climbout
  Factors more battery parameters
Parameter | Value
Bcapacity | 6,000mAh
Bdischarge | 90%
Battery Packs | 5
V | 22.2 V
Rt | 1
n | 1.3
ηprop | 60%
This methodology for endurance
passes FR1
Appendix Slide
Notes: https://www.banggood.com/Racerstar-Racing-Edition-4108-BR4108-600KV-4-6S-Brushless-Motor-For-500-550-600-for-RC-Drone-FPV-Racing-p-1122900.html?cur_warehouse=CN
https://www.hobbypartz.com/02p-motor-607-mt4008-kv600.html

## Slide 38
Airframe Structure: Aircraft Loading Conditions
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Maximum expected loading values determined from structural analysis:
  Maximum Tensile Stress: 765.1 kPa
  Maximum Compressive Stress: 765.1 kPa
  Maximum Shear Stress: 10.8 kPa
Appendix Slide

## Slide 39
Airframe Structure: Open Thin Wall Approximation
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Torsional analysis of wing root and tip:
  Assumed constant open thin walled rectangular cross-section for Expanded Polystyrene (EPS) foam - open thin walled analysis gives worst case torque
    Lowest shear strength candidate material
Results:
  Maximum allowable torque at root: 57.354 N-m
  Maximum allowable torque at tip: 12.491 N-m
Expected values experienced by vehicle:
  Expected torque at root: 4.995 N-m
  Expected torque at tip: 1.088 N-m
Appendix Slide

## Slide 40
Airframe Structure: Open Thin Wall Approximation
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Determining twist angle after applied torque for EPS
  Open thin walled approximation gives limiting case for maximum twist angle
  Maximum allowable twist angle for root: 11.3°
  Maximum allowable twist angle for tip: 21.1°
Expected values experienced by vehicle:
  Expected twist angle for root: 1.36°
  Expected twist angle for tip: 3.48°
Maximum Expected Tip Deflection
  Assumes load is applied entirely at wingtip
  Maximum EPS foam tip deflection: 3.28 cm
Appendix Slide

## Slide 41
Aircraft Preliminary Mass Budget
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
UAV Specifications:
Total Mass: 7.47 kg
Weight: 16.46 lbs (73.25 N)
Approximate UAS weight for 12hr. overwatch
2 FMC UAVs, 2 auxiliary batteries, 1 receiver
Total UAS Weight: 46.60 lbs (207.29 N)
  Payload weight of 2.1 lbs (9.34 N)
Cumulative Endurance Satisfies FR1
Demonstration Payload Capacity Satisfies FR3
Total UAS Weight Satisfies FR4
Appendix Slide

## Slide 42
Cost Estimates
Cost based on market estimates
  Amazon
  SparkFun
  Home Depot
  Hobby Sites
  Independent Retailers
Overestimates
  Include shipping estimates
  Assume expensive options
Cost Estimates |  | 
Sub System | Quantity | Cost ($)
Airframe |  | 
Carbon Fiber Rods | 4 | 7.57
3D Printing Resin | Mass Approximation | 373.5
Balsa Wood | Surface Area Approx. | 15.06
Propulsion |  | 
Brushless Motor | 1 | 68.72
Propellor | 1 | 12
4S LiPo Batteries | 5 | 300
Avionics |  | 
Flight Controller | 1 | 300
Servos | 5 | 750
Wiring | 1 | 50
Speed Controller | 1 | 50
Payload |  | 
Particle 3G | 1 | 100
Total UAV Cost |  | 2026.84
Cost of 2 UAVs |  | 4053.70
Appendix Slide
Notes: https://docs.google.com/spreadsheets/d/1Z1zK1ah4jcD0RY_jm0Z3KQHR5nCHbvbiWtiiujIvGak/edit?usp=sharing

## Slide 43
Summary
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics

## Slide 44
Status Summary
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Key Takeaways Going Forward:
Feasibility analysis shows the aircraft will fly
Significant structures & materials analysis must occur to determine airframe integrity upon skid landing
Endurance is a primary concern
  Additional Motor & Propeller Analysis & Endurance testing is needed
  Custom Lithium Ion Battery pack options need to be explored
Design Feature | Requirement | Feasibility
Span 10ft | FR2 | 
Short Takeoff | FR3 | 
Payload | FR4 | 
Endurance | FR1 | 
UAS < 50lbs | FR2 | 
Appendix Slide

## Slide 45
Logistics/Gantt Chart
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics

## Slide 46
Final Report
CDR
Critical Path

## Slide 47
Questions?
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics

## Slide 48
26_JAN_2017_Florida_Keys_5R_4G_3Bxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx
Appendix
Aerodynamics and Wing Design - Slide 16
Aspect Ratio - Slide 17
Taper Ratio - Slide 19
Bending Moment - Slide 20
Airfoil - Slide 21
Lift Coefficient - Slide 23
Drag Polar - Slide 26
AoA - Slide 28
Span Efficiency - Slide 29
Performance - Slide 30
Aircraft Dynamics - Slide 75
Avionics and Electronics - Slide 52
Baseline Design - Slide 13
Backup Slides - Slide 49
CONOPS - Slide 8
Cost Estimates - Slide 40
Critical Project Elements - Slide 14
Design Objectives - Slide 5
Endurance Estimations - Slide 37
FBD - Slide 10
Functional Requirements
Primary - Slide 11
Secondary - Slide 50
Gantt Chart - Slide 46
Mass Budget - Slide 41
Materials - Slide 54
Mission Statement - Slide 4
NACA 4412 Data - Slide 70
Other Marketed Solutions - Slide 63
Overview - Slide 2
Propulsion - Slide 31
Feasibility Goals - Slide 31
Derivations - Slide 32Market Analysis- Slide 36
Sources - Slide 77
Status Summary - Slide 44
Structures - Slide 38, Slide 58
Wing Specifications - Slide 74

## Slide 49
Backup Slides

## Slide 50
FR4: UAS shall provide a payload bay to house a sensor suite.
FR5: UAS shall operate up to a maximum altitude of 10,000 ft. MSL.
FR6: UAS shall adhere to FAA 14 CFR Part 107, SMALL UNMANNED AIRCRAFT SYSTEMS, contingent on waivers.
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Functional Requirements
Appendix Slide

## Slide 51
Functional Requirements
FR7: UAS shall maintain a minimum of 80% operational capabilities in customer specified environmental conditions.
FR8: UAS will maintain a FMC standby posture.
FR9: UAS total flyaway cost shall not exceed 5,000 USD for a single air vehicle along with the required launch and recovery system.
Appendix Slide

## Slide 52
Avionics & Electronics
Avionics system - (Pending Further Research)
Flight Controller
Control Surface Servos
Telemetry Receiver (for flight)
Gyroscope
Speed Controller
Altimeter
Appendix Slide

## Slide 53
Potential Payloads
Avionics system - Payload Bay
Video Camera
3G/LTE Communications relay
IR Sensors
Other to-be-determined components
Appendix Slide

## Slide 54
Airframe Structure: Foam Candidate Material Selection
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Expanded Polystyrene Foam
  Heavily used in RC market for wings and fuselages
Matweb Material Data:
  http://www.matweb.com/search/datasheettext.aspx?matguid=5f099f2b5eeb41cba804ca0bc64fa62f
Tensile Strength, Yield | 47.1 - 51.0 MPa
Compressive Strength, Yield | 0.0400 - 10.9 MPa
Shear Strength | 0.124 - 0.300 MPa
Appendix Slide

## Slide 55
Airframe Structure: Wood Candidate Material Selection
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Balsa Wood
  Potential use for wing/fuselage spars and ribs
Matweb Material Data:
  http://www.matweb.com/search/datasheet.aspx?matguid=81c269f50f424573a4f9978cfcb41bc8
Tensile Strength | 73.0 MPa (Axial) / 1.00 MPa (Perpendicular)
Compressive Strength | 6.90 MPa (Axial) / 1.00 MPa (Perpendicular)
Shear Strength | 1.10 MPa
Appendix Slide

## Slide 56
Airframe Structure: Composite Candidate Material Selection
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
Carbon Fiber
  Potential use for wing and fuselage structural support
Matweb Material Data:
  http://matweb.com/search/datasheet.aspx?matguid=5df1e45601214077b674daa817cba3d3&ckck=1
Tensile Strength | 110.0 MPa
Compressive Strength | 110.0 MPa
Shear Strength | 260.0 MPa
Appendix Slide
Notes: https://www.cstsales.com/hm_carbon_shapes.html

## Slide 57
Airframe Structure: Composite Candidate Material Selection
Overview
Baseline Designs
Feasibility Analysis
Summary
Logistics
3D Printed Resin
  Potential use for wing skin & structural support
Material Data:
Tensile Strength | 55.7 MPa
Compressive Strength | 34.0 MPa
Shear Strength | TBD
Appendix Slide

## Slide 58
Structures
Developing a Structural Model:
Load Factor Equations: T.H.G. Megson, in Aircraft Structures for Engineering Students (Sixth Edition), 2017
Bank (θ = 2.47°):
Sharp-Edge Gust (30 ft/s or 9.144 ms/s):
Total (n = 1.0542):
Appendix Slide

## Slide 59
Airframe Structure: Closed Thin Wall Approximation
OTW ɑ & 𝛃 approximation: (ref: W. C. Young, Roark’s Formulas for Stress & Strain, McGraw-Hill, 6th ed., 1989, p. 34.)
Appendix Slide

## Slide 60
Airframe Structure: Closed Thin Wall Approximation
CTW Equations (ref: S. P. Timoshenko and J. N. Goodier, Theory of Elasticity, 3rd ed., McGraw-Hill, New York, 1969, Sec 109.). Assumed rectangular cross-section.
Shear flow: Shear:
Ae = Enclosed area
GJ: Torsional Rigidity
(Shear modulus * polar MOI)
Twist angle:
Appendix Slide

## Slide 61
Airframe Structure: Open Thin Wall Approximation
OTW Equations (ref: S. P. Timoshenko and J. N. Goodier, Theory of Elasticity, 3rd ed., McGraw-Hill, New York, 1969, Sec 109.)
Assumed constant wall thickness for max shear
Shear:
GJ: Torsional Rigidity
(Shear modulus * polar MOI)
Twist angle:
Appendix Slide

## Slide 62
Airframe Structure: Distributed Load & Tip Deflection
Tip deflection assumes maximum load applied at wing tip only
Distributed load function via Anderson, John D. Introduction to Flight. New York: McGraw-Hill, 1985.
Bending moment and max shear, compression, and tension assume beam model for wing
Distributed Load Function:
Bending Stress:
(t/2) is distance from neutral axis, M is bending moment, I is MOI about neutral axis
Tip Deflection: F is maximum force over wing, E is Young’s Modulus
Appendix Slide

## Slide 63
Other Marketed Solutions
Appendix Slide

## Slide 64
Other Marketed Solutions
Appendix Slide

## Slide 65
Other Marketed Solutions
Appendix Slide

## Slide 66
Other Marketed Solutions: Weight Comparisons
Appendix Slide

## Slide 67
Other Marketed Solutions: Wingspan vs MTOW
Appendix Slide

## Slide 68
Other Marketed Solutions: Endurance Comparisons
Appendix Slide

## Slide 69
26_JAN_2017_Florida_Keys_5R_4G_3Bxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx
Other Marketed Solutions: Weight vs Payload
Appendix Slide

## Slide 70
Confirmation:
Matlab Wing
Designer
ver 1.6
written by
Phillip J. Root and
John R. Rogers
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | NACA 4412
Cl | 1.118
Cd | 0.063
AoA | 7.989°
NACA 4412 Data
Appendix Slide

## Slide 71
Confirmation:
Baylor-
NACA 4412
Wind Tunnel
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | NACA 4412
Cl | 1.118
Cd | 0.063
AoA | 7.989°
NACA 4412 Data
Appendix Slide

## Slide 72
Validation:
Matlab Wing Design code (Phillip J. Root and John R. Rogers)
Baylor NACA 4412 Wind Tunnel Studies
Ansys Fluent CFD
NACA 4412 Data
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | NACA 4412
Cl | 1.118
Cd | 0.063
AoA | 7.989°
Appendix Slide

## Slide 73
Confirmation: CFD - Computational Fluid Dynamics
Ansys Fluent
Cl = 1.1553
Cd = 0.0227
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | NACA 4412
Cl | 1.118
Cd | 0.063
AoA | 7.989°
NACA 4412 Data
Appendix Slide

## Slide 74
Aerodynamics and Wing Design: Wing Specifications
Parameter: | Specification:
Span | 10ft
AR | 15.59
Chord | 12in
Taper | 0.283
Airfoil | NACA 4412
Cl | 1.118
Cd | 0.063
AoA | 7.989°
Appendix Slide
Notes: Explain what Wing Designer 1.6 means and what where we found it!

## Slide 75
Aircraft Dynamics
Pitch Stiffness
Range of Values
    Static Margin: 0.25 - 0.32 %
    Horizontal Tail Volume: 0.33 - 0.42 ft3
    Horizontal Weight: 0.58 - 0.75 lbs
    Horizontal Surface Area: 0.71 - 0.91 ft2
    Horizontal Span: 1.41 - 1.81 ft
Appendix Slide
Notes: Assumptions:
Alpha aw is small
z/c is negligible compared to vehicle scope
Alpha wb-epsilon is small
Zt is negligible
Mac,t is negligible
Mp is negligible
Lt = 3 ft
W tail = 1lb
Partial Epsion wrt alpha = 0.35
Rho = 9.919
Horz tail cord = .5
Thickness = 1 inch

## Slide 76
Aircraft Dynamics
Yaw Stiffness
Range of Values
    Static Margin: 0.25 - 0.32 %
    Vertical Tail Volume: 0.02 - 0.01 ft3
    Vertical Weight: 0.42 - 0.25 lbs
    Vertical Surface Area: 0.5 - 0.3 ft2
    Vertical Span: 1.01 - 0.60 ft
Appendix Slide

## Slide 77
26_JAN_2017_Florida_Keys_5R_4G_3Bxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx
Sources
[1] Traub, Lance W., et al. “Range and Endurance Estimates for Battery-Powered Aircraft.” Journal of Aircraft, 22 May 2012, https://arc.aiaa.org/doi/10.2514/1.C031027.
[2] Anderson, J. D., & Bowden, M. L. (2022). Introduction to flight. McGraw-Hill.
[3] PROPDRIVE v2 5050 580KV Brushless Outrunner Motor. (n.d.). Retrieved October 8, 2021, from https://hobbyking.com/en_us/propdrive-v2-5050-580kv-brushless-outrunner-motor.html#qa[bW9kZT03JnBhZ2U9MSZxdWVzdGlvbl9zZWFyY2hfY29udGVudD0=].
[4] Performance data. APC Propellers. (2021, March 9). Retrieved October 8, 2021, from https://www.apcprop.com/technical-information/performance-data/
[5] T.H.G. Megson, in Aircraft Structures for Engineering Students (Sixth Edition), 2017
[6] W. C. Young, Roark’s Formulas for Stress & Strain, McGraw-Hill, 6th ed., 1989, p. 34.
[7] S. P. Timoshenko and J. N. Goodier, Theory of Elasticity, 3rd ed., McGraw-Hill, New York, 1969, Sec 109.
Appendix Slide