## Slide 1
TALON: Tactical Autopilot Long-Term Overwatch Network (HERD-CU)
Critical Design Review
02 December 2021
Jason Peloquin (Project Manager)
Vyacheslav Rychenko
Patrick Tippens
Zachary Vanlangendonck
Dante Vigil
Christian Williams
Selmo Almeida
Nicholas Boender
Anthony Danna
Ethan Fleer
Collin Kasunic
John Oliver
Customer: Professor John K. Mah
Notes: Flip the slide template. Title on the left and make more space in general. Move the page numbers to the right side. Mka the timeline on the bottom of each slide to half the slide. Include transition slides to give a pause moment.

## Slide 2
Presentation Outline
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Overview
Design Solution
Critical Project Elements (CPEs)
Design Requirements
Project Risks
Verification and Validation
Project Planning
Verification & Validation
Project Planning
Notes: Take our the abcd… from the project overview. Keep the baseline design details

## Slide 3
Project Overview - Mission Statement
Project TALON’s purpose is to develop a high endurance, human-portable, rapidly deployable unmanned aerial vehicle. The aircraft will be capable of supporting multiple mission overwatch profiles that demand agility, low cost, high persistence, and broad coverage capability.
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: Take our the abcd… from the project overview. Keep the baseline design details

## Slide 5
Design Solution
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 6
Design Solution - Functional Block Diagram
KEY:
Physical connections
Data Connections
Data Connections via wireless method
Power supply connections
(illustrate subsystem
complexity and importance)
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: FBD is comprised of 4 sections: Ground, UAV, Payload, Supported Additions
Ground Team operates a transmitter
Received by 8 channel receiver Onbard UAV
Communicates to inline current sensor and electric speed controller which drive the motor and propellor, and servos which control the flaperons elevator and rudder.
All these systems run off our power supply solution
Payload is comprised of customer dictated system and power supply
In addition, we accommodate Phase 1bs integrate with a pitiot tube and pixhawk
Transmitter/Receiver in Ground Control System (Tx/Rx)

## Slide 7
Design Solution - Final Design Overview
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: - Streamlined/Aerodynamic
- Easily serviceable
- Small package footprint
High Wing mount
- Conventional Tail
1.46 m (5 ft) long
10 ft wing span

## Slide 8
Design Solution - Fuselage
Focus: Provide seamless access to electrical components and a volume for a mission specific payload.
Features: Rapidly removable canopy for ease of access into electronics bay and interchangeability payload bay for various user defined payloads.
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: Primary focus: Structurally supportive - Rapidly serviable
Features: - Removable canopy for electronics access - Removable payload bay for mission specific uses

## Slide 9
Design Solution - Wing Harness
Focus: Integrating the wing with fuselage while providing enhanced structural support.
Features: Three piece system based on dovetail connections for rapid interchangeability and servicing. Structural reinforcement for wings at critical shear point along the fuselage interface.
Other Concepts Considered: Integrated wing and FishBAC control surfaces.
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: Focus: -Integration of high mounted wing design - Structural support
Features: -Three piece dovetail system - Structural support at critical shear point on fuseagle interface

## Slide 10
Design Solution - Tail
Focus: Providing pitch and yaw stability while minimizing flow disturbance.
Features: Aerodynamic sleeving leading up to the empennage decreases turbulent flow to tail. The three identical control surfaces provide rapid manufacturing and replacement, all acting on the same dovetail mounting platform.
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: Focus: Inherent pitch/yaw stability - Min flow disturbance
Features Aerodynamic Sleeving - Three piece identical mount and control surfaces - Easy manufacturing and replacement

## Slide 11
Design Solution - Wing
NACA4412
NACA4412
NACA4406
Span | 1524 mm
Taper Ratio | 0.40
AR | 14.25
Root Chord | 304.8 mm
Root Airfoil | NACA4412
Tip Chord | 121.9 mm
Tip Airfoil | NACA4406
Leading Edge
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: Most critical component
Span of 1.52 m
Starting at root
At ⅗ span, beghin transition to NACA 4406
Tip
4:43

## Slide 12
Design Solution - Propulsion
Motor:
470Kv (Kv=RPM per Volt)
Low Amp Draw
4S-6S compatible
Propeller:
17x7E
Maximum RPM = 8,529
Lightweight Plastic
Economical
Motor/Propeller Combination:
Capable of generating 16+ lbs of thrust
Motor - 470Kv Brushless
Input Voltage: | 14.8-22.2V
Idle Current: | 2.1A @ 20V
Current: | Up to 100A
Propeller - 17X7E
Propeller - 17x7E
Diameter: | 17 in
Pitch | 7E
Max RPM: | 8,529
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: “The team selected a 470Kv brushless motor with a 17x7E propeller which is capable of efficiently generating over 16 lbs of thrust and is fully compatible with our battery”

## Slide 13
Design Solution - Electronics
Spektrum 8020T Receiver - 8 Channel
Spektrum SPMXAE1100 - ESC
HS-125MG Slim Wing Servo
Input Voltage: | 11.1-22.2V
BEC Voltage: | 6V, 7.4V, or 8.4V
Cont. Max Current: | 100A (120A Max Burst)
Input Voltage: | 3.5-9.0V
Band (Freq.): | 2.4GHz
Current: | 80mA
Input Voltage: | 6.0V
No Load Current: | 230mA
Stall Current | 1.2A
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: Aircraft components that would achieve flight included Spektrum ESC and 8-Channel Receiver as well as a 4 servos that have been chosen primarily for 3 reasons:
These parts are readily available in the market
Spektrum offers data acquisition of in-flight telemetry
And these components can be interfaced with Phase 1b’s Pixhawk 4 flight controller.
Esc controls the motor, its wide range of use from 11.1 to 22.2 volts, which correlates to a 3s to 6s power source, means that we can use a variety of battery packs without requiring a change in ESC.This specific ESC can accommodate a continuous current of up to 100 amps.
Receiver allows for control up to 8 different channels corresponding to 8 control surfaces operating at the FAA approved frequency of 2.4 GHz.
In our case, the servos correspond to four control surfaces including a flaperon on each wing, which is effectively a hybrid flap and aileron, as well as the horizontal and vertical stabs also known as the elevator and rudder.

## Slide 14
Design Solution - Battery
 | Single Cell |  | 9P-5S | 
Battery Characteristics | Value |  | Value | 
Nominal Voltage | 3.65 | V | 18.25 | V
Nominal Capacity | 5000 | mAh | 45000 | mAh
Usable Capacity | 4500 | mAh | 40500 | mAh
Continuous Discharge Rate | 9.60 | A | 86.40 | A
Continuous Power Capability | 35.04 | W | 1576.80 | W
Nominal Total Energy | 18.25 | Wh | 821.25 | Wh
Usable Total Energy | 16.43 | Wh | 739.13 | Wh
Mass | 68 | g | 3060 | g
Cell Type: Lishen 21700 5000mAh 9.6A Battery (LR2170SD)
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: After conducting some trade studies, the Lishen 21700 battery was chosen to power the Talon due to its high capacity to mass ratio. To suit the voltage and current demands of the Talon, the cells were put into a 5 series and 9 parallel configuration boosting the voltage to 18.25 V, continuous discharge rate of 86.40 A, and a nominal capacity of 45000 mAh. However, since lithium based batteries cannot be safely discharged to their full capacity, we assumed that we could drain the battery to 10% of the nominal capacity bringing the total usable capacity to 40500 mAh. The model on the left is a crude mockup of the battery pack which has an estimated weight of 3.06 kg or 6.75 lbs.

## Slide 15
Mass Budget
3D Printed Resin
Used for most structural components
High strength and rigid
3D Printed PLA Foam
Used for non-structural components to save weight
Proposed Payload
LilyGo LORA Radio
  Allows long range communication without cell towers
  Lightweight
  Fits possible mission case for TALON
  Allows meshing with other LORA radios
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 16
Critical Project Elements Driven By Functional Requirements
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 17
Project Overview - Critical Project Elements
CPE | Description | Importance to Success | Functional Requirement
Maximizing endurance through aerodynamics | Achieve high endurance through comprehensive aerodynamic design and modelling | Poor aerodynamics directly translates to decreased endurance | FR1
Maximizing endurance through electronics and battery configuration | Achieve high endurance through efficient battery design and power use | Poor electronics design greatly decreases endurance | FR1
Propulsion system optimization | Achieve high endurance through propulsion system optimization | Propulsion is key for climbout and endurance | FR1 & FR3
Structures | Ensure structural integrity of vehicle through various flight conditions while maintaining light weight and portability | Structural design is critical for landing survivability and portability but must be lightweight for endurance | FR2, FR3 & FR4

## Slide 18
Primary Functional Requirements
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 19
Project Overview - Functional Requirements
FR1: The UAS shall provide a continuous overwatch window of 12 hours through the use of one or more UAVs (i.e. three UAVs each with 4 hours of endurance is acceptable).
FR2: UAS (including all UAVs and their supporting equipment) shall be transported, launched, recovered, and operated by a single person to satisfy Requirement 1 under a 10 minute launch window per UAV.
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: FR1: overwatch of 12 hours
FR2: outlines aircraft portability through a single user

## Slide 20
Project Overview - Functional Requirements
FR3: UAS shall have short takeoff and landing capabilities to deploy in areas with unprepared launch surfaces and obstructed climb windows as specified by the customer.
FR4: UAV shall provide a payload bay to house a sensor suite.
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: FR3: Outlines short takeoff and landing
FR4: Read it off.

## Slide 21
Design Requirement Satisfaction
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 22
Design Requirements - Key Drivers of TALON Success
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Optimized Propulsion
2
Optimized propeller & motor combination for low amperage draw
Efficient Electronics
3
Smart ESC
Appropriately sized servos
Capable of Phase B integration
High Capacity Battery
4
Maximized energy density per overall battery weight
Custom 5S configuration
Strong & Lightweight Materials
5
Utilize a composite/hybrid wing design to maximize strength and minimize weight
Highly Efficient Wings
1
High AR
Taper
Aerodynamic twist

## Slide 23
FR1 Endurance through Aerodynamics
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 24
Design Requirement - Endurance through Aerodynamics
Endurance of Propeller Driven Aircraft
Goals:
Design Highly Efficient Aerodynamic Bodies
Assumptions:
Steady Unaccelerated Flight
Limitations:
Ignores Propulsion System & Propeller Efficiency
Maximize CL3/2/CD to Meet FR1 (Cruise) and L/D FR3 (Climbout)
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
TALON Design Elements:
Airfoil: NACA 4412 & NACA 4406
Taper Ratio: 0.40
Aspect Ratio: 14.25
Notes: This is the Breguet Endurance Formula for a reciprocating propeller driven aircraft. While our a/c is electric, we understand that to maximize endurance we want to minimize the power required which is not influenced by the propulsion system. Thus we see that endurance, from an aerodynamic perspective is a function of CL over CD.
We used this heuristic in comparing airfoils and making design choices such as Airfoil, taper and AR.
For discussion tomorrow: It may be a problem that we don’t have a prediction for Endurance? Needed for validation stage.

## Slide 25
Design Requirement - Endurance through Aerodynamics
Optimal L/D @ 4.8° AOA & 16.4 m/s | 
CL | 0.7991
CD | 0.0319
CL/CD | 25.06
Lift | 72.1 (N)
Drag | 5.9 (N)
Predicted Aerodynamic Characteristics - Potential Flow Theory
Albatross (Bird)
20:1
U-2 (Spy Plane):
25.6:1 (12 Hrs)
Rutan Voyager
27:1 (216 Hrs)
Assumptions:
Steady-State
Incompressible Flow
No Side-Slip
Limitations:
No Compressibility
No Viscous Drag
Simple Geometry
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: What is MAX? MAx AOA before Stall? Maximum achievable speed? Not sure why its worth talking about.
Albatross is highly efficient bird able to fly 100km /day without flapping wings, with 22:1 glide ratio
U-2 spyplane - prolific recon plane with 12 hr unrefueled endurance
Rutan Voyager: first plane to circumnavigate the globe unrefueled, non stop. 216 hours
Birds: Government Surveillance Drones?
Sources: https://en.wikipedia.org/wiki/Rutan_Voyager, https://en.wikipedia.org/wiki/Lift-to-drag_ratio

## Slide 26
FR1 & FR3 Propulsion System Optimization
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 27
Design Requirement - Propulsion System Optimization
Goals
Solve propulsion requirements for 3 mission profiles
  Max Endurance, Climbout, Headwind
Assumptions
All Flight Cases:
  15 lb. total mass, Finite wing (Induced drag), 5,700 ft alt. conditions
Max Endurance
  L=W, T=D, CD0 = (⅓)kCL2, No wind
Climbout
  Adheres to Level 3 Req, CD0 = kCL2 , No wind
Headwind
  No crosswind, constant headwind
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 28
Design Requirement - Propulsion System Optimization
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Flight Phase | Thrust Required [lbf] | Amps Desired [A]
Endurance | 0.9 | As low as possible
Climbout | 8.2 | As low as possible
Headwind | 0.78 | As low as possible
Propulsion Model Calculates Thrust needed each flight phase [1]
Propulsion Optimization Findings:
Lower Amperage = More Endurance
Amp draw depends on:
  Propeller
  Motor
  Thrust requirements
Model Slides
Notes: FR3 is met if the thrust generated from propulsion system is greater than the model’s estimated required thrust for level 3 climbout.
FR1 is met if the thrust generated from the propulsion system is greater than the model’s estimated required thrust while simultaneously reducing current draw as much as possible.
P_req = Power required for steady level unaccelerated flight
Endurance Amp Draw driving motor and propellor combo

## Slide 29
FR1 & FR3 Endurance through Electronics and Battery
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 30
Design Requirement - Endurance through Electronics
Goal
Efficient power usage through select component choices and custom battery
Power Budget Assumptions
High loading takeoff conditions
No adverse wind effects
No losses in wiring
Ideal battery
Ideal motor
Constant current draw
Servos
ESC = motor current draw
Solution
Account for all losses with the margin
  20% contingency power
Battery
FET/Switch
Processor
BEC
ESC
Motor
Receiver
Left Flaperon
Elevator
Rudder
Right Flaperon
Servos
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: CONDENSED:
Restate goal
Streamline the Functional Block Diagram (FBD)
Understanding that the power budget assumptions outline ideal conditions we have accounted for this with the use of 20 percent margin.
-------------------------------------------------------------------------------------------------------------------------------
Power Budget Assumptions:
Define high loading takeoff conditions: maximum flight angle of 21.8 degrees to meet level 3 success, sea level conditions (i.e. density of air at sea level), minimum takeoff distance of 50ft or 15.24 meters which will require high amperage demand from the battery.
Ideal flight: no adverse wind effects
Overall efficiency of the system is model to have no losses in the wiring, battery, and motor.
Although current draw to the servos and motor will vary on the flight conditions as well as aircraft configuration, but constant representative values have been chosen to model our aircraft power budget.
The ESC is modeled to be ideal, therefore the ESC will draw the same amount current that is required by the motor without any losses due to lack of manufacture provided efficiency data.
SOLUTION:
Since many of these assumptions and component efficiencies can not be easily verified without a full system test, a 20% contingency power cost was implemented to cover the differences that will result from the ideal cases

## Slide 31
Design Requirement - Endurance through Electronics
 |  | Takeoff |  | Cruise | 
Component | Quantity | Max. Current Draw | Margin (20%) | Max. Current Draw | Margin (20%)
ESC | 1 | 50.00 | 60.00 | 6.00 | 7.20
Motor | 1 |  |  |  | 
Servo | 4 | 0.71 | 0.85 | 0.43 | 0.51
Receiver | 1 | 0.08 | 0.10 | 0.08 | 0.10
Current Required: |  | 52.91A | 63.49A | 7.78A | 9.34A
Power Budget
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: As previously mentioned, the ESC effectively behaves as a power valve, meeting the amperage demands of the motor. Given the lack of efficiency data, the 20% margin was implemented to cover the possibility of power losses and power consumption of the ESC.
Worst case scenario the receiver is expected to draw 80 milliamps, which appeared to be the upper threshold/worst case across RC industry standard receivers.
The servo is assumed to have 2 different power requirements for takeoff and cruise due to loading inherited from the level 3 success and conditions experienced for each stage of flight
HIghlight AMPERAGE requirements for TO at 52.91-63.49A and Cruise at 7.78-9.34A

## Slide 32
Design Requirement - Endurance through Electronics
Custom Battery Pack
Parallel: 9 cells
Series: 5 cells
Total: 45 cells
 | Single Cell |  | 9P-5S | 
Battery Characteristics | Value |  | Value | 
Nominal Voltage | 3.65 | V | 18.25 | V
Nominal Capacity | 5000 | mAh | 45000 | mAh
Usable Capacity | 4500 | mAh | 40500 | mAh
Continuous Discharge Rate | 9.60 | A | 86.40 | A
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: To quickly reiterate, the custom battery pack we are going with will have 45 cells with 5 cells in series and 9 cells in parallel. This in turn will supply us with 18.25 nominal voltage and a capacity of around 40500mAh with a maximum continuous discharge rate of 86.40 A which can not be exceed for prolonged periods of time. We can draw up to this threshold but can not exceed it otherwise the battery would be insufficient.

## Slide 33
Design Requirement - Endurance through Electronics
Final values:
 | Without Margin |  | With Margin | 
Time to Altitude | 0.10 | hr | 0.10 | hr
Capacity Used For Takeoff | 5291.08 | mAh | 6349.30 | mAh
Capacity Left for Cruise | 35208.92 | mAh | 34150.70 | mAh
Time of Cruise | 4.53 | hr | 3.66 | hr
* Note: Time parameters based on motor run time not full aircraft estimates
Satisfies Cruise FR1 and Climbout FR3
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: Given that the time required to climb to altitude is around 6 minutes or 0.1 of an hour, we multiplied the current used at takeoff by the time to altitude to find how much of the battery capacity was used for takeoff. Then we subtracted that from the usable capacity of 40500 mAh to find the capacity left for cruise. The next step was to divided the left over capacity by the current required to maintain cruise finally yielding the time of cruise you see in gray boxes. With that said, we are estimating a cruise time between 3.6 to 4.5 hours from the electronics alone which satisfies FR1 endurance of around 4 hours while also meeting the climbout requirements of FR3.

## Slide 34
FR2 & FR3 Capability through Structures
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 35
Design Requirement - Structures
Goals:
Develop a lightweight composite wing capable of surviving takeoff and landing
Takeoff Stress Assumptions:
Constant acceleration for climbout
Lift force split evenly between wings
  Level ascent
Solution:
Yield Strength of XPS Foam: 234.4 kPa
Max Bending Stress During Takeoff: 298 kPa
XPS Foam Wings will be reinforced with carbon fiber rods and strips
Bending stiffness increases by around 15 times with introduction of carbon fiber
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: How we cave man eliminated it without being able to quantify

## Slide 36
Design Requirement - Structures
ANSYS Wing Setup - Launch
Fixed support at wing harness
Acceleration determined to be:
  1.31 m/s² (+y)
  10.0 m/s² (+z)
Lift force of 37 N distributed over wing surface
Large deflections ON - account for nonlinear behavior
  Stiffness changes as material deforms
Simulation run until 1% solution convergence
Limitations
Assumed entirely solid wing
Unable to test inclusion of carbon fiber supports
  Meshing limitations with complex geometry
Used typical XPS foam values
  ⍴ = 48 kg/m³
  E = 80.12 MPa
Wing harness set as ABS plastic
  Exact 3D printed properties difficult to predict
Project Risks
Overview
Design Solution
CPEs
Project Planning
Design Requirements
Verification & Validation
Notes: How we cave man eliminated it without being able to quantify

## Slide 37
Design Requirement - Structures
Wing Launch Simulation | XPS Wing Results | XPS Wing Allowed | ABS Harness Results | ABS Harness Allowed
Max. Tensile Bending Stress | 192.2 kPa | 234 kPa | 1.058 MPa | 14.85 MPa
Max. Compressive Bending Stress | 205.7 kPa | 234 kPa | 0.984 MPa | 14.85 MPa
Total Tip Deflection | 0.111 m 4.37 in | 0.08 - 0.2 m 3.0 - 7.8 in | N/A | N/A
Wing Launch - Wing Bending Stress [Top] / Total Deformation [Bottom] / Harness Bending Stress [Bottom-Right]
Project Risks
Overview
Design Solution
CPEs
Project Planning
Verification & Validation
Design Requirements
Notes: How we cave man eliminated it without being able to quantify

## Slide 38
Risk & Mitigation
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 39
TALON - Risk Matrix Unmitigated
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Talon Specific Risk Matrix
Dominant Risks:
Crash During Full Scale Test
Damage due to hard landing
Harness/Structures Failure
Total Loss of aircraft
Wing Structural Integrity
Wing durability
Excessive deflection
Battery
Total Loss of aircraft due to electronics fire
Inaccurate charging
CL/CD
Lift loss due to tip stall
Basic models do not quantify total drag rise

## Slide 40
TALON - Risk Matrix Revised
Crash During Full Scale Test
Individual component test/verification
Margin implemented across all subsystems
Ground based workup/pre-flight checklist
Margin to build multiple aircraft
Harness/Structures Failure
Load simulations performed in ANSYS
Conduct fatigue and failure testing
Incorporation of safety factor
Wing Structural Integrity
Load simulations performed in ANSYS
Integrated composite reinforcements
Fatigue and failure testing
Battery
Collaborate with IRISS on building and servicing custom batteries
Use of battery management system (BMS)
CL/CD
Excess thrust & design reduces tip stall
Reducing Risk:
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Talon Specific Risk Matrix

## Slide 41
Verification and Validation
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 42
Verification and Validation - Propulsion
Objective | Obtain real data on propellor/motor combination to incorporate into full vehicle model
Description | Test propellor/motor combination with multiple battery packs to analyze thrust and current draw. Battery Packs: 6S 22.5V & 4S 14.5V
Model Comparison | Static thrust measured compared to manufacture data sheets and primary propulsion model
Expectation | Measured thrust to exceed 8.16 lbf. as required for climbout
Validation Against FRs | Perform full scale test at previously calculated climbout and cruise throttling for determination of inflight propulsion requirements, satisfying FR1 and FR3.
Propulsion - Thrust Validation
Load cell (½)
Arduino
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 43
Verification - Propulsion
Propulsion Test 6S 22.5 V | Results | Required | Margin
Thrust (lbs) | 16.0 | 8.2 | 1.95X
Takeoff Amps | 66 | <100 | 1.5X
Cruise Amps | 8.6 | N/A | N/A
Propulsion Test Results
Future Validation - Full scale flight test
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: Desire maximum Thrust per Amps during cruise conditions while simultaneously able to exceed climbout thrust performance requirements as this is most demanding part of mission.

## Slide 44
Verification and Validation - Battery
Objective | Determine 5S viability for full UAV by testing using a 4S (14.5V) and 6S (22.5V) battery
Description | Test propellor/motor combination with 4S & 6S battery packs to analyze thrust and current draw
Model Comparison | Compare the 4S and 6S thrust and current draw test data to validate 5S
Expectation | 5S battery will supply enough amperage and voltage to achieve climbout requirements
Validation Against FRs | Perform static test at previously calculated climbout and cruise requirements with custom battery for validation of battery performance, satisfying FR1 and FR3.
Battery - 5S Validation
Battery
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: For the battery validation, we are going to determine the viability of a 5S battery by testing previously available 4S and 6S batteries with predetermined propellor and motor combination. This set up on a static test stand will allow us to analyze the thrust and current draw to ensure that we achieve the climbout requirements of our FR3 and maximize the cruise requirement of FR1.

## Slide 45
Battery Sizing Results
18x8E propeller was chosen to maximize motor strain and amp draw
  Thrust for 4S 14.8V = 10.7 lbs
  Thrust for 6S 22.2V = 17.6 lbs
Validation - Electronics / 5S Battery Choice
5S 18.5V
4S 14.8V
6S 22.2V
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: We found that the 4s battery configuration provided a maximum of 10.7 lbs of thrust at 35 Amps while the 6s battery configuration provided 17.6 lbs of thrust but required upward of 100 amps of continuous current. Both of these cases, exceeded the thrust requirement for maximum climbout of 8.2 lbs. Using this data, we are confident that the 5s battery would supply us a solid middle ground to power the TALON system. However, we will continue to further examine motor and propellor combinations to potentially allow us to scale down to a 4s battery. This in turn would allow us to further scale the capacity of the battery and increase the cruise time of the aircraft.

## Slide 46
Initial Model - Electronics Heat Limitations
Governing Equations:
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Goals:
A thermodynamic heat transfer model was developed to predict internal temperature building during climbout
Assumptions:
1D flow
Perfectly closed system
Instant electronics temperature
Ideal battery
Model Predictions:
Time to Electronics Maximum of 150° F: 2.4 min
Maximum Cruise Temp: 64.8° C (148.7° F)
Notes: How we cave man eliminated it without being able to quantify. I NEED TO UPDATE THIS EQUATION for Delta T

## Slide 47
Verification and Validation - Electronics Heat Limitations
Objective | Determine flight duration required to generate heat buildup in excess of electronic threshold of 65.5° C (150°F)
Description | Simulate heat buildup generated through initial takeoff and cruise to determine if sensors and resin can withstand internal heat buildup via DAQ and Simulink
Model Comparison | Thermodynamics energy balance equation
Expectation | Expected maximum temperature: 150°F
Validation Against FRs | High duration static flight simulations with custom battery and full scale flight test will be conducted to verify FR1 and FR3
Thermodynamic Testing:
Electronics were sealed within a mock fuselage and a simulated flight test was performed
Test Conditions:
Simulated 4 minute climbout at 50A
Simulated 6 minute cruise at 6A
Sealed fuselage
Outside temperature: 3.9°C (39°F)
4 thermocouple internal configuration
Thermocouples
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: How we cave man eliminated it without being able to quantify

## Slide 48
Validation - Electronics Heat Limitations
Thermodynamic Test | Results
Time to reach 150° F | Temp Not Achieved
Climbout Max Ambient Temperature | 48.9° C (120.0° F)
Cruise Max Ambient Temperature | 47.7° C (117.9° F)
Thermodynamic Model Vs. Test Results:
Model predictions:
  2.4 minutes to exceed electronics limit of 150° F
  Maximum Cruise Temp: 64.8° C (148.7° F)
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: How we cave man eliminated it without being able to quantify
Lith poly is hotter than lithium ion.
Gen 1 fuselage is 3mm thicker
Full fuselage will have larger internal volume

## Slide 49
Verification and Validation - Structures
Objective | Accurately reflect wing loading conditions during climbout, flight, and descent
Description | Test bending, tension, and compression limits of full wing with added structural support of carbon fiber
Model Comparison | ANSYS Wing launch simulation, expected flight loads from lift, sharp-edged vertical gusts and banked turn
Key Results | Structural failure, wing deflection, permanent deformation, material separation, surface delamination
Validation Against FRs | Validates wing can support loading conditions for climbout, flight, and descent - satisfying FR3
Structures - Wing Whiffletree Test
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: How we cave man eliminated it without being able to quantify

## Slide 50
Verification and Validation - Structures
Objective | Characterize forces experienced during landing
Description | Pull vehicle off of elevated surface at required landing velocity and impact ground using varying initial heights - record testing data using load cells
Model Comparison | 3D printed material limitations from ITLL testing of fuselage, ANSYS landing simulations
Key Results | Forces experienced by fuselage due to impact on landing, wing deflection on landing
Validation Against FRs | Aircraft can withstand impact upon landing, securely transporting payload with no structural failures - verifying FR3 & FR4
Structures - Aircraft Landing Test
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: How we cave man eliminated it without being able to quantify

## Slide 51
Verification and Validation - Aerodynamics
Objective | Verify/Improve aerodynamic estimates with CFD
Description | Computational Fluid Dynamics allow modeling of viscous effects and turbulence absent from previous modeling techniques.
Model Comparison | Potential Flow Estimates of Lift and Drag
Expectation | Increase in predicted drag. Decrease in lift due to flow separation.
Validation Against FRs | Aerodynamic surfaces optimize lift and minimize drag to meet FR1 & FR3
Aero - Computational Fluid Dynamics
Setup
2D Wing
SST k-ω
Standard Sea Level
AOA: 0, 3, 6, 9
Velocity: 143.7 m/s
Boundary Conditions
Inlet: Freestream Velocity Vector
Outlet: 0 Gauge Pressure
Wall: No Slip
CFD Validation Method
Refine until CL and CD converge w/ experimental
Quantify Error
Apply same method to further studies
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: FORMATTING
Notes for slide that is now in appendix:
2% error for CL vs. AOA between CFD and Experimental.
40% error for CL vs. CD between CFD and Experimental.

## Slide 52
Verification and Validation - Aerodynamics
Aero - 2D Airfoil
Parameter | Potential Flow | CFD (Composite)
CL | 0.7991 | 0.7917
CD | 0.0319 | 0.0289
Lift | 63.2 N | 62.4 N
Drag | 1.28 N | 2.9 N
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Velocity Streamlines - NACA 4412
Velocity Streamlines - NACA 4406
Notes: Seen above are the streamlines of the flow directly around the NACA 4412 airfoil color coded according to velocity. This sim was run with an AOA of 4.8° and and inlet velocity of 16.4 m/s at standard atmospheric conditions of 10,000ft in altitude.

## Slide 53
Verification and Validation - Full Scale Flight Testing
Objective | Validate Flight Performance Against Functional Requirement
Description | A series of increasingly complex test flight leading up to maximum duration flight at mission altitude with payload.
Model Comparison | Actual measured endurance will be contrasted against the predicted power budget endurance values
Expectation | Individual aircraft endurance exceeds 3.5 h
Validation Against FRs | Multiple high duration test flights will be conducted to prove fulfillment of FR1 & FR3
Flight Test Highlights
Test | Goals | Duration | Pass Criteria
Airworthiness | Demonstrate Launch and controlled landing | 30 s | 1. Powered flight 2. Statically Stable
Climb & Turn | Demonstrate A/C can climb to 100’ AGL | 5 min | 1. Climb to 100’ AGL 2. Returns to launch point.
Loiter | Demonstrate 30 minutes of powered flight at 500’ AGL | 30 min | 1. 30 minute flight 2. Orbit about a static ground location.
Max Climb / Max Endurance | Demonstrate climb to 10,000 ft MSL and sustained flight | +3.5 Hours | 1. Aircraft reaches 10,000 ft MSL 2. Aircraft maintains orbit for >3.5 hours
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning
Notes: Anthony to flesh out

## Slide 54
Project Planning
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 55
Gantt Chart
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 56
Critical Path
Keys to Success
Notes: How we cave man eliminated it without being able to quantify

## Slide 57
Cost Plan - Budget
Vehicle Cost
(with Margin)
$2,685.21
Electronics salvage means potential for 2-3 vehicle builds within $5,000 budget
Project Risks
Overview
Design Solution
CPEs
Design Requirements
Verification & Validation
Project Planning

## Slide 58
Future Testing - Phase 1
Phase 1 - Pre Construction Further Testing/ Simulation |  |  |  |  |  | 
Subsystem | Test | Goals | Dates | Testing Location | Equipment | Safety
Propulsion | Thrust Testing on Static Test Stand | · Choose motor and Prop combo · Determine 4S Battery Viability · Determine motor thrust across flight envelope | 11/29/21 - 12/10/21 | Aerospace Building - Garage | Static Test Stand Motors (E-Flite, Scorpion) Propellers (15x8 → 18x8) Spektrum Avionics Equipment | Eye Protection Ear Protection Protective Barriers
Aerodynamics | 3D CFD/Wind Tunnel | · Analyze 3D wing Lift and Drag · Determine overall A/C drag coefficient | 11/29/21 - 12/10/21 | Aerospace Building - | Pilot Wind Tunnel | Eye Protection Ear Protection
Structures | Load Testing | · Determine Wing Material · Optimize Structural Reinforcements | 11/29/21 - 12/10/21 | ITLL / Aerospace Building | Printed Airframe Samples Wing Material Samples | Eye Protection Ear Protection
Notes: How we cave man eliminated it without being able to quantify

## Slide 59
Future Testing - Phase 2
Phase 2 - Large Scale Testing After Assembly |  |  |  |  |  | 
Subsystem | Test | Goals | Dates | Location | Equipment | Safety
Propulsion | Thrust Testing on Static Test Stand | · Choose motor and Prop combo · Determine 4S Battery Viability · Determine flight envelope | 11/29/21 - 12/10/21 | Aerospace Building - Test Cell | Static Test Stand Motors & Props Spektrum Avionics Equipment | Eye Protection Ear Protection Protective Barriers
Structures | Load Testing - Wiffle Test | · Analyze final wing structural/material properties | 3/4/22 - 3/9/22 | ITLL / Aerospace Building | ITLL material testing machines Full Scale Composite wing | Eye Protection Ear Protection
Structures | Landing Simulation | · Determine if the airframe can successfully belly land under normal conditions | 3/10/22- 3/13/22 | Aerospace Building/Parking Lot | Elevated Platform, support system, ropes and full A/C | Eye Protection Ear Protection
Thermal | Heat Analysis | · Determine internal fuselage & electronics temperature during simulated flight | 3/14/22- 3/18/22 | Aerospace Building or outside area | DAQ, Simulink, thermocouples & Fully configured A/C | Eye Protection Ear Protection
Notes: How we cave man eliminated it without being able to quantify

## Slide 60
Future Testing - Phase 3
Phase 3 - Full Scale Flight Testing |  |  |  |  |  | 
Subsystem | Test | Goals | Dates | Location | Equipment | Safety
Whole UAV | Initial Flight Test | · Confirm UAV airworthiness and analyze flight characteristics | 4/1/22 - 5/6/22 | Arvada Airpark Sod Farm Local Ranch | Entire UAS | Certified Pilot Ground Safety Officer Eye Protection + Protective Gear
Whole UAV | Environmental Testing | · Determine if Aircraft can fly in adverse conditions as specified by customer | 4/1/22 - 5/6/22 | Arvada Airpark Sod Farm Local Ranch | Entire UAS Spare Battery Packs | Certified Pilot Ground Safety Officer Eye Protection + Protective Gear
Whole UAV | Portability testing | · Determine if the aircraft can successfully be transported and operated by one person | 4/1/22 - 5/6/22 | Outside/Hiking Trails | Full UAS Hiking Boots and Pack | Outdoor Gear Comms/phones Water/Supplies
Whole UAV | Time to Assemble Testing | · Determine the time it takes to assemble a UAV in the field | 4/1/22 - 5/6/22 | Outside/Hiking Trails | Full UAS Hiking Boots and Pack | Outdoor Gear
Notes: How we cave man eliminated it without being able to quantify

## Slide 61
Questions?

## Slide 62
Appendix

## Slide 63
Aerodynamics - Backup

## Slide 64
Design Requirement - Endurance through Aerodynamics
Endurance of Propeller Driven Aircraft
Goals:
Design Highly Efficient Aerodynamic Bodies
Assumptions:
Steady Unaccelerated Flight
Limitations:
Ignores Propulsion System & Propeller Efficiency
Design Elements:
Airfoil: NACA 4412 & NACA 4406
Taper Ratio: 0.40
Aspect Ratio: 14.25
Maximize L3/2/LD to Meet FR1 (Cruise) and L/D FR3 (Climbout)
Notes: This is the Breguet Endurance Formula for a reciprocating propeller driven aircraft. While our a/c is electric, we understand that to maximize endurance we want to minimize the power required which is not influenced by the propulsion system. Thus we see that endurance, from an aerodynamic perspective is a function of CL over CD.
We used this heuristic in comparing airfoils and making design choices such as Airfoil, taper and AR.
For discussion tomorrow: It may be a problem that we don’t have a prediction for Endurance? Needed for validation stage.

## Slide 65
Design Requirement - Endurance through Aerodynamics
Wing Tip Stall:
Notes: At low reynolds numbers (below 100,000) flow separation can cause decrease in lift and increase in drag reducing efficiency. Near the wing tips and at lower flight speeds this is a concern for the last ⅓ of the wing. To mitigate this
increasing chord, and add aerodynamic twist at the wing tips. The thinner airfoils should emulate rough airfoils or flat plate increasing efficiency vs the conventional NACA 4412. Additionally we will use advanced computational methods to better understand these flows.

## Slide 66
Verification and Validation - Aerodynamics
Objective | Qualitatively Understand Wing Tip Stall
Description | Extend 2D techniques to 3D, and create high fidelity simulation of wing tips including fine boundary layer resolution.
Model Comparison | Compare to literature on low Re airfoils.
Expectation | Understand whether aerodynamic twist effectively mitigates separation and increases efficiency.
Validation Against FRs | Successfully mitigate wing tip stall increasing efficiency FR1 & increasing maximum lift FR3
Aero: Computational Fluid Dynamics
Setup
3D Wing
SST k-ω
Atmosphere at 10,000ft cruise
AOA: 0, 3, 6, 9
Velocity: 12.2 m/s
Boundary Conditions
Inlet: Freestream Velocity Vector
Outlet: 0 Gauge Pressure
Wall: No Slip
Notes: Slide 8 from aero junkyard

## Slide 67
Verification and Validation - Aerodynamics
Aero - Computational Fluid Dynamics
Notes: Talk about plots. State error in CL and CD vs wind tunnel

## Slide 68
Aerodynamics - Backup Prior Reynolds Number Analysis
Appendix Slide

## Slide 69
Aerodynamics - Estimation of Body CL and CD
Stanford Model:
Wetted Area and Flat Plate Skin Friction
Appendix Slide

## Slide 70
Aerodynamics - Backup
CFD: Sensitivity analysis
Appendix Slide
Notes: Started with a basic 2d CFD simulation and decreased cell count to see error induced. Allows us to understand a bare minimum cell count for “accurate” results with quantifiable error.

## Slide 71
Aerodynamics Values- Backup
Appendix Slide
Cruise: 4.8° AOA / 16.4 m/s |  | Max: 11.5° / 22 m/s | 
CL (Cruise) | 0.7991 | CL (Max) | 1.402
CD (Cruise) | 0.0319 | CD (Max) | 0.0716
CL/CD (Cruise) | 25.06 | CL/CD (Max) | 19.59
Lift (Cruise) | 72.1 (N) | Lift (Max) | 199.7 (N)
Drag (Cruise) | 5.9 (N) | Drag (Max) | 22.9(N)

## Slide 72
Aerodynamics - Backup
Objectives: CFD model verification
Total Elements = 45,000
Appendix Slide

## Slide 73
Aerodynamics - Backup
Objectives: CFD model verification
Standard sea level atmospheric conditions applied
Appendix Slide

## Slide 74
Aerodynamics - Backup
Objectives: CFD model verification
Appendix Slide

## Slide 75
Aerodynamics - Backup
Objectives: CFD model verification
Appendix Slide

## Slide 76
Aerodynamics - Backup
Objectives: CFD model verification
Mesh refinement can be seen
Total number of cells now 45,735
Appendix Slide

## Slide 77
Aerodynamics - Backup
Objectives: CFD model verification
Resulting Y+ and Coefficient of Pressure distribution
Appendix Slide

## Slide 78
Verification and Validation - Aerodynamics - Backup
Objective | Verify Aerodynamic Characteristics of Wing and Body
Description | Quantify Lift and Drag
Model Comparison | Potential Flow Estimates of Lift and Drag
Expectation | Increase in Predicted Drag
Validation Against FRs | Aerodynamic surfaces optimize lift and minimize drag to meet FR1 & FR3
Aero - Wind Tunnel
Setup
3D printed model of wing scaled according to Reynold’s number
Use Smead Wind tunnel or TBD

## Slide 79
Propulsion - Backup

## Slide 80
Propulsion - Backup
Motor Selection
Criteria:
  Power
  Thrust
  Current Draw
  Weight
  Battery Needed
  Size
  Cost
Appendix Slide
Target Climbout Power | 950-1050 W
Target Climbout Thrust | 8.2-8.8 lbf

## Slide 81
Propulsion: Max Endurance - Backup
Endurance Maximizing Velocity (Minimum Preq ) [1]
Coefficient of Lift (Lift = Weight) [2]
Thrust (Thrust = Drag) [1]
Power [2]
Endurance Flight satisfies FR1
Results | IMP | SI
Treq Endurance | .901 lbf | 4.00 N
Preq Endurance | .109 hp | 81.6 W
Vreq Endurance | 27.3 mph | 12.2 m/s
CLreq Endurance | 1.42 | 1.42
Treq Climbout | 8.20 lbf | 36.5 N
Preq Climbout | 1.28 hp | 957 W
CLreq Climbout | .975 | .975
Vreq Climbout | 35.1 mph | 15.7 m/s
Treq Headwind | 0.78 lbf | 3.47 N
Preq Headwind | 0.121 hp | 90.4 W
CLreq Headwind | .871 | .871
Vreq Headwind | 35 mph | 15.6 m/s

## Slide 82
Design Requirement - Propulsion System Optimization
Levels of Success for Climbout: (measured from ground)
ɣ1 = 5.71°
ɣ2 = 11.3°
ɣ3 = 21.8°**
**outside Small Angle Approx
Rate of Climb (RoC) :
γ
θ
𝛼
θ
θ
L
W
T
Results | IMP | SI
Treq Endurance | .901 lbf | 4.00 N
Preq Endurance | .109 hp | 81.6 W
Vreq Endurance | 27.3 mph | 12.2 m/s
CLreq Endurance | 1.42 | 1.42
Treq Climbout | 8.20 lbf | 36.5 N
Preq Climbout | 1.28 hp | 957 W
CLreq Climbout | .975 | .975
Vreq Climbout | 35.1 mph | 15.7 m/s
Treq Headwind | 0.78 lbf | 3.47 N
Preq Headwind | 0.121 hp | 90.4 W
CLreq Headwind | .871 | .871
Vreq Headwind | 35 mph | 15.6 m/s
Satisfies Climbout FR3
Notes: FR3 is met if the thrust generated from propulsion system is greater than the model’s estimated required thrust for level 3 climbout.
FR1 is met if the thrust generated from the propulsion system is greater than the model’s estimated required thrust while simultaneously reducing current draw as much as possible.
P_req = Power required for steady level unaccelerated flight

## Slide 83
Propulsion: Headwind
Requirement for Headwind: 30 mph Headwind
Vwind
T
L
W
D
Results | IMP | SI
Treq Endurance | .901 lbf | 4.00 N
Preq Endurance | .109 hp | 81.6 W
Vreq Endurance | 27.3 mph | 12.2 m/s
CLreq Endurance | 1.42 | 1.42
Treq Climbout | 8.20 lbf | 36.5 N
Preq Climbout | 1.28 hp | 957 W
CLreq Climbout | .975 | .975
Vreq Climbout | 35.1 mph | 15.7 m/s
Treq Headwind | 0.78 lbf | 3.47 N
Preq Headwind | 0.121 hp | 90.4 W
CLreq Headwind | .871 | .871
Vreq Headwind | 35 mph | 15.6 m/s

## Slide 84
Propulsion
Motor Selection
T-Motor winner of down-selection process
  Real-world problems
Scorpion a strong 2nd place
E-Flite is a valuable resource for testing
Appendix Slide
Scorpion SII-4025-520KV
T-Motor AM480 650KV
E-Flite 470KV
Notes: A low Kv motor has more winds of thinner wire—it will carry more volts at fewer amps, produce higher torque, and swing a bigger prop. A high Kv motor has fewer winds of thicker wire that carry more amps at fewer volts and spin a smaller prop at high revolutions.

## Slide 85
Propulsion - Backup
Scorpion Sll 520KV with 15x8E APC Propeller
Appendix Slide
Performance Criteria | Motor Specification | Target Specification(climbout)
Power [W] | 925.9 | 950
Thrust [grams] | 3970 | 3950
Current [amps] | 50 | Lower is Better
Weight [grams] | 353 | Lower is Better
Cost [$] | 150 | Lower is Better
Compatible Battery | 6s 3500-5000mah | Smaller is Better

## Slide 86
Propulsion - Backup
Static Testing
Goal: Obtain quantitative data for thrust dependent of current draw and percent throttle as a means to validate motor specs and pick ideal propeller size
Appendix Slide
Motor
ESC
Load cell (½)
Arduino
3D Printed Motor Mount

## Slide 87
Propulsion - Backup
Static Testing
Appendix Slide

## Slide 88
Propulsion - Backup
Static Testing
Appendix Slide

## Slide 89
Propulsion - Backup
Thrust Vs. Amps Metrics
Appendix Slide
Notes: This is data that is handed to team 1b

## Slide 90
Electronics - Backup

## Slide 91
Electronics - Servo Selection (Assumptions) - Backup
Appendix Slide
Key Assumptions:
The induced forces on the control surface will be applied to the trailing edge
When servo is torquing, no jitters from the control surfaces will be experienced (i.e. equilibrium condition is satisfied)
Air density is set at sea level (𝝆SL = 1.225 kg/m3)
Control surface with largest area will drive calculations
  AWing = 2 in. x 48 in. (modeled after Tempest Aircraft)

## Slide 92
Electronics - Servo Selection (Assumptions) - Backup
Appendix Slide
Appended Assumptions:
Aircraft will experience Incompressible Flow
Reynolds Number = 1✕ 105
Wing geometry of NACA 4412 airfoil
Airfoil experiences total velocity of Vtotal = 25.144 m/s
Average chord length, c̅ = 8 in = 0.2032 m
  Control surface is hinged at 75% of wing chord

## Slide 93
Electronics - Payload
Appendix Slide
LILY GO T-BEAM:
Portable Long Range Radios
18650 Battery: 72 hours of power
Multiple frequencies available
  433/868/915 Mhz
GPS Capable
Weight: 82.2g (2.82 oz)
Working Temp: -40℃ + 85℃
Cost Effective: $40 per radio

## Slide 94
Electronics - Servo Selection (Torque Calculations) - Backup
Appendix Slide
Hinge Moment/Span:
-0.1672 Nm/span
-0.1698 Nm = -24.05 oz-in.
Selected Servo Properties:
Factor of Safety (FoS) = 2
Thin design
Lightweight

## Slide 95
Verification and Validation - Electronics / Servos - Backup
Objective | Model servo performance based on manufacture mechanical and electrical details.
Description | Analyze input and output power of servo to calculate servo efficiency and determine operational range.
Model Comparison | N/A. This model is uniquely affected by the aircraft’s flight path and weather conditions.
Expectation | High servo loading correlates to high amperage draw and low loading reflects low current draw.
Validation Requirements | Place inline current sensor within circuit during test flight to analyze true amperage demand of servos.
Servo Parameters
Vcruise = 16.4 m/s
Max Gust Speed = 9.144 m/s
Notes: How we cave man eliminated it without being able to quantify

## Slide 96
Li-Po vs Li-Ion Batteries - Backup
Appendix Slide
Li-Po Batteries
Li-Ion Batteries
Pros:
Pros:
Cons:
Cons:
Lower profile
Pre assembled units
Longer lifespan
Higher cost
Known overheating issues
Low power density
Higher power density
Customizable
  Voltage
  Current
  Capacity
Less likely to overheat
No built in protection
Requires additional manufacturing
Shorter lifespan
Notes: Appendix

## Slide 97
Li-Ion Trades - Backup
Appendix Slide
Best capacity per mass battery:
  LG F1L1865 (18650)
    3350 mAh
    4.87 A (Too small)
    $6.99
    45 g
  Lishen LR2170SD (21700)
    5000 mAh
    9.6 A
    $4.99*
    68 g
Final selection: Lishen LR2170SD
* Bulk order discount (~ 15 %)
Notes: Appendix

## Slide 98
Battery Pack - Backup
Appendix Slide
Notes: Appendix

## Slide 99
Electronics - Thermal Testing - Backup
Appendix Slide

## Slide 100
CAD Model - Backup

## Slide 101
TALON - Electronics Housing Design - Backup
Appendix Slide
Focus: Provide seamless access to electrical components such as battery, motor, and flight controller without complete disassembly or hassle
Features: Rapidly removable canopy for ease of access into electronics bay

## Slide 102
TALON - Payload Bay Design - Backup
Appendix Slide
Focus: Provide a mass and volume for user to fill with mission specific payload while not disturbing aircraft dynamics and flight characteristics
Features : Provides rapid interchangeability and spacious room for various user defined payloads
Notes: Important because modularity

## Slide 103
TALON - Mounting - Backup
Appendix Slide
Concepts Considered: 3D printing clips
Focus: Provide access to crucial components without jeopardizing mission performance
Features: Rapid removal and securing for minimal down time between service and operation

## Slide 104
TALON - Wing Integration Design - Backup
Appendix Slide
Concepts Considered: Integrated Wing and FishBAC Control Surfaces
Focus: Integrating the wing with fuselage while providing structural support
Features: Three piece system based on dovetail connections for rapid interchangeability and servicing. Structural reinforcement for wings at critical shear point along the fuselage interface
Notes: Highlight wing harness b/c it needs to be portable so important and modularity

## Slide 105
Aircraft Dynamics - Backup
Objective: Maintain controllability and establish inherent stability to reduce flightpath deviation and energy draw for correction
Appendix Slide

## Slide 106
Aircraft Dynamics - Backup
Objective: Maintain controllability and establish inherent stability to reduce flightpath deviation and energy draw for correction
Appendix Slide
 | Volume coefficient | Surface Area [ft^2] | Span [ft] | Weight [lbs]
Horizontal Tail Estimates | 0.40 | 0.85 | 1.69 | 0.35
Vertical Tail Estimates | 0.02 | 0.36 | 0.73 | 0.15

## Slide 107
Aircraft Dynamics - Backup
Objective: Maintain controllability and establish inherent stability to reduce flightpath deviation and energy draw for correction
Cm_alpha = -1.9849
Neutral Point = 51.1% Chord
SM = 0.3377 % chord = 4.05 inches
Cn_beta =
Appendix Slide

## Slide 108
Modular Design - Backup
Carbon Fiber Bar
Carbon Fiber Rod
Clevis Pin
Appendix Slide

## Slide 109
Design Requirement - Endurance through Aerodynamics
Cruise: 4.8° AOA / 16.4 m/s |  | Max: 11.5° / 22 m/s | 
CL (Cruise) | 0.7991 | CL (Max) | 1.402
CD (Cruise) | 0.0319 | CD (Max) | 0.0716
CL/CD (Cruise) | 25.06 | CL/CD (Max) | 19.59
Lift (Cruise) | 72.1 (N) | Lift (Max) | 199.7 (N)
Drag (Cruise) | 5.9 (N) | Drag (Max) | 22.9(N)
Predicted Aerodynamic Characteristics - Potential Flow Theory
Albatross (Bird)
20:1
U-2 (Spy Plane):
25.6:1 (12 Hrs)
Rutan Voyager
27:1 (216 Hrs)
Notes: What is MAX? MAx AOA before Stall? Maximum achievable speed? Not sure why its worth talking about.
Albatross is highly efficient bird able to fly 100km /day without flapping wings, with 22:1 glide ratio
U-2 spyplane - prolific recon plane with 12 hr unrefueled endurance
Rutan Voyageer: first plane to circumnavigate the globe unrefueled, non stop. 216 hoursa
Sources: https://en.wikipedia.org/wiki/Rutan_Voyager, https://en.wikipedia.org/wiki/Lift-to-drag_ratio

## Slide 110
Structures - Backup

## Slide 111
Verification and Validation - Structures - Landing
ANSYS Wing Setup - Landing
Fixed support at wing harness
Acceleration determined to be:
  5.00 m/s² (+y)
  4.90 m/s² (-z)
Standard Earth gravity
Large deflections ON - account for nonlinear behavior
  Stiffness changes as material deforms
Simulation run until 1% solution convergence
Limitations
Assumed entirely solid wing
Unable to test inclusion of carbon fiber supports
  Meshing limitations with complex geometry
Used typical XPS foam values
  ⍴ = 48 kg/m³
  E = 80.12 MPa
3D Print properties difficult to estimate - Wing harness set as ABS plastic
Notes: How we cave man eliminated it without being able to quantify

## Slide 112
Verification and Validation - Structures - Landing
Wing Landing Simulation | Wing Results | XPS Wing Allowed | ABS Harness Results | Harness Allowed
Max. Tensile Bending Stress | 340 kPa | 234 kPa | 1.058 MPa | 14.85 MPa
Max. Compressive Bending Stress | 347 kPa | 234 kPa | 0.984 MPa | 14.85 MPa
Total Tip Deflection | 0.165 m 6.5 in | 0.08 - 0.2 m 3.0 - 7.8 in | N/A | N/A
Wing Launch - Total Deformation [Top] / Wing Bending Stress [Bottom] / Harness Bending Stress [Bottom-Right]
Notes: How we cave man eliminated it without being able to quantify

## Slide 113
Verification and Validation - Structures - Landing
ANSYS Fuselage Setup - Landing
Fixed support on furthest side of simulated soil from fuselage
Velocity of fuselage set to:
  0.5 m/s² (-y in ANSYS coordinates)
  10.0 m/s² (+z in ANSYS coordinates)
Standard Earth gravity over entire system
Large deflections on to account for potential nonlinear behavior
Used typical values of soft clay for soil composition
  ⍴ = 1.3 g/cm³
  E = 3 MPa
  Coefficient of static/dynamic friction: 0.3/0.2
Limitations
Assumed primary fuselage thickness of 0.5 in.
Assumed solid ABS plastic for tail connection
  Meshing limitations with complex geometry
Main fuselage was assumed to be high density polyethylene plastic with similar properties to 3D printing materials
External forces applied for weight of wings and tail
Notes: How we cave man eliminated it without being able to quantify

## Slide 114
Verification and Validation - Structures - Landing
Fuselage Landing - Fuselage deformation on impact
Fuselage Landing Simulation | Results
Max. Tail Connector Deflection | 0.6 in
Notes: How we cave man eliminated it without being able to quantify

## Slide 115
Verification and Validation - Structures - Landing
Fuselage Landing - Normal Stress [Top] / Shear Stress [Bottom]
Wing Launch Simulation | Results
Max. Shear Stress [MPa] | 0.447
Max. Normal Stress [MPa] | 1.916
Max. Shear Strain [m/m] | 0.000749
Max. Normal Strain [m/m] | 0.000343
Notes: How we cave man eliminated it without being able to quantify

## Slide 116
Verification and Validation - Structures
Objective | Confirm that XPS foam reinforced with carbon fiber rods satisfies our aircraft structural requirements
Description | Perform tensile testing on a sample of XPS with carbon fiber rods and strips inserted
Model Comparison | Confirm that tensile testing results are consistent with previously found flexure testing results.
Expectation | Yield Strength greater than 298 kPa with an acceptable factor of safety of 1.5
Validation Against FRs | Wing able to support the takeoff loads imparted by level 3 success of FR3
Structures - Wing Tensile Testing
Notes: How we cave man eliminated it without being able to quantify

## Slide 117
Structures Backup Slide
Rectangular Wing Lift Distribution:
Bending Stress:
Bending Stress Along Wing:
Moment of Inertia of Wing:
Bending Stiffness:
Notes: How we cave man eliminated it without being able to quantify

## Slide 118
Structures Backup Slide
V_climbout = 16.4m/s
Time to 50 feet = 3.05s
Upwards acceleration to 20ft: 1.31m/s^2
L = m(g + a_z) = 6.4kg(9.81m/s^2 + 1.31m/s) = 75.6N = 37.8N/wing
Notes: How we cave man eliminated it without being able to quantify

## Slide 119
Verification and Validation - Operator Launch - Backup
Goals:
Simulate an operator overhead TALON launch
Test Parameters:
Controlled Repeatable Launch
  1 Step overhead throw
  Minimal launch angle
20lb Med ball
  1.33X TALON weight
Testing:
Non fatigued Launch
  Launch under normal heart rate
Launch under operational stress
  Upper body workout + 1 mile run
  No rest
Results:
Controlled launch velocity of 6.1 m/s (20 ft/s)
  39% of the required 15.7 m/s TALON launch velocity
Notes: How we cave man eliminated it without being able to quantify

## Slide 120
Risk Matrix Criteria - Scoring - Backup
Appendix Slide

## Slide 121
Manufacturing - Timetable
Source | Items | Shipping Lead-times | Shipping Location
Mohr Composites | Foam Wings | 1 week | USA
Plastic Anvil Workshop | 3D printed materials | 6 days | N/A
Mcmaster Carr | Carbon fiber, Misc. hardware | 2 days | USA
Hobbytown | Electronics | N/A | N/A
Amazon | Resin for 3D printing | 1 day | USA
Fleer Auto Reconditioning | Painting and Monokote | 2 days | N/A
Horizon Hobby | Electronics | 3 days | USA
Notes: How we cave man eliminated it without being able to quantify

## Slide 122
Manufacturing - Task List
Task | Time Required | Reliance on prior task completion
Materials Testing | 1 day | No
Wind Tunnel Testing | 1 day | No
Wing assembly | 11 days | Yes
Wing Testing | 5 days | Yes
Electronics Harness assembly | 3 days | No
Electronics Stress Test | 2 days | Yes
Full Vehicle Assembly | 14 days | Yes
Full Vehicle Test | 3 days | Yes
Notes: How we cave man eliminated it without being able to quantify

## Slide 123
26_JAN_2017_Florida_Keys_5R_4G_3Bxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxxx
Sources
[1] Traub, Lance W., et al. “Range and Endurance Estimates for Battery-Powered Aircraft.” Journal of Aircraft, 22 May 2012, https://arc.aiaa.org/doi/10.2514/1.C031027.
[2] Anderson, J. D., & Bowden, M. L. (2022). Introduction to flight. McGraw-Hill.
[3] PROPDRIVE v2 5050 580KV Brushless Outrunner Motor. (n.d.). Retrieved October 8, 2021, from https://hobbyking.com/en_us/propdrive-v2-5050-580kv-brushless-outrunner-motor.html#qa[bW9kZT03JnBhZ2U9MSZxdWVzdGlvbl9zZWFyY2hfY29udGVudD0=].
[4] Performance data. APC Propellers. (2021, March 9). Retrieved October 8, 2021, from https://www.apcprop.com/technical-information/performance-data/
[5] T.H.G. Megson, in Aircraft Structures for Engineering Students (Sixth Edition), 2017
[6] W. C. Young, Roark’s Formulas for Stress & Strain, McGraw-Hill, 6th ed., 1989, p. 34.
[7] S. P. Timoshenko and J. N. Goodier, Theory of Elasticity, 3rd ed., McGraw-Hill, New York, 1969, Sec 109.