## Slide 1
CUBE3
Test Readiness
Review
CU Boulder Engineers Creating Universal Boom Extensions for CUBEsats
Customer:
Professor Robert Marshall
Advisor:
Professor Sanghamitra Neogi

## Slide 2: Overview
Budget Update
Testing Update
Schedule Update
Overview
Notes: RH

## Slide 3: Project Overview
Overview
Project Schedule
Manufacturing Status
Budget
CUBE3
CubeSat
Bus
1.5 U
1.5 U
9.5cm
9.5cm
6.6cm
8cm
Instrument
(Notional)
The purpose of this project is to create an extendable CubeSat boom to separate a sensitive instrument from the cubesat bus
Notes: Boom alignment

## Slide 4: Project Objectives
Overview
Project Schedule
Manufacturing Status
Budget
Support a 500 g payload at the end of the boom
Extend a minimum distance of 60 cm
Fit within 1.5 U when undeployed (including payload)
Have a mass of less than 1.5 kg (not including payload)
Have a first resonant frequency over 2.5 Hz
Deploy on command in under 2 minutes
Provide routing for power and signal cabling to/from payload

## Slide 5
Overview
Project Schedule
Manufacturing Status
Budget
CONOPS

## Slide 6
Overview
Project Schedule
Manufacturing Status
Budget
FBD

## Slide 7
Overview
Project Schedule
Manufacturing Status
Budget
FBD

## Slide 8
Overview
Project Schedule
Manufacturing Status
Budget
FBD

## Slide 9
Overview
Project Schedule
Manufacturing Status
Budget
FBD

## Slide 10
Overview
Project Schedule
Manufacturing Status
Budget
FBD

## Slide 11
Overview
Project Schedule
Manufacturing Status
Budget
FBD

## Slide 12: Baseline Design
Project Schedule
Manufacturing Status
Budget
11.2cm
1.
3.
PEEK Connectors
Prior Design
Manufactured
1
3
1
2
3
2
10mm
10mm
5.5mm
Overview
Notes: Overview (10%) - BASELINE DESIGN & MAJOR CHANGES
Brief review of the baseline design with respect to CDR. Describe major changes to the design. (Clear what all major elements of the project are, and how the baseline design works (5 pts) )
This is a key design element that we put a lot of time and hours into ensuring the accuracy of manufacture

## Slide 13: Baseline Design Change - IR sensor
Project Schedule
Manufacturing Status
Budget
Trade study performed based on MSR question
IR sensor better solution
  No moving parts
  Simplified spool manufacture
  Smaller spool assembly
Full trade study in backup slides
Baseline Telemetry Switch
IR LED emitter
Updated Telemetry Switch
IR phototransistor
IR reflective half
IR absorptive half
Overview
Notes: Overview (10%) - BASELINE DESIGN & MAJOR CHANGES
Brief review of the baseline design with respect to CDR. Describe major changes to the design. (Clear what all major elements of the project are, and how the baseline design works (5 pts) )
This is a key design element that we put a lot of time and hours into ensuring the accuracy of manufacture

## Slide 14: Software Baseline
Project Schedule
Manufacturing Status
Budget
Not for delivery
MATLAB GUI
  Built in App Designer
  Uses Arduino Hardware Support Package
v1.1 is released for use
  Temperature display
  Burn wire relay arm/control
  IR spool revolution sensor telemetry
Overview
Notes: Overview (10%) - BASELINE DESIGN & MAJOR CHANGES
Brief review of the baseline design with respect to CDR. Describe major changes to the design. (Clear what all major elements of the project are, and how the baseline design works (5 pts) )
This is a key design element that we put a lot of time and hours into ensuring the accuracy of manufacture

## Slide 15: Critical Project Elements
Project Schedule
Manufacturing Status
Budget
Deployable Boom Structure
  Stow in 1.5U with an 8x8x8 cm, 500 g payload
  First resonant frequency ≥ 2.5 Hz
Payload Connectivity
  Power/data cable provisions
</>
Software Interface
  Command and telemetry
Deployment System
  Deploy on command
  Confirm deployment via telemetry
Environmental Resilience
  LEO radiation/thermal environment
  Vibrational launch environment
Overview

## Slide 16: Schedule Update
Budget Update
Testing Update
Schedule Update
Overview
Notes: RH

## Slide 17
Elements and Updates
Schedule Update
Manufacturing Status
Budget
Rest of Year Critical Path Timeline
College Expo
April 24
April 20
SFR Presentation (est)
AES Industry Symposium
April 17
March 6
LASP Thermal Chamber Testing on 3rd Boom Assembly
March 16 (TBR)
Mass/Dimension Test
March 9
Full Deployment Test
Cable Routing Test
March 4
Launch Environment Test
Analysis & Validation

## Slide 18: Schedule
Elements and Updates
Schedule Update
Manufacturing Status
Budget
Baselined at CDR
Planned
Complete

## Slide 19: Testing Update
Budget Update
Testing Update
Schedule Update
Overview
Notes: MB/VG

## Slide 20
Elements and Updates
Project Schedule
Testing Update
Budget
LASP Thermal
Chamber
Full
Deployment
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Mass /
Dimension
Cable
Routing
Launch
Environment
Resonant
Frequency

## Slide 21
Elements and Updates
Project Schedule
Testing Update
Budget
LASP Thermal
Chamber
Full
Deployment
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Mass /
Dimension
Cable
Routing
Launch
Environment
Resonant
Frequency

## Slide 22
Elements and Updates
Project Schedule
Testing Update
Budget
Cable Routing Test
Motivation - Verify that the cable routing design allows for full deployment of the boom and cables are
still functioning after deployment
Requirements Under Test
Boom shall have capability of routing three-wire power setup
DR_2.1
DR_2.2
FR_2
Boom shall have capability of routing 3 separate differential cables
Boom shall provide routing for power and signal cabling
Equipment:
Sorensen XPH 35-4D Power Supply set as Voltage Supply
Arduino Due microcontroller (as mock flight computer)
Keysight 34461A Digital Multimeter
Keysight 33220A Function/Arbitrary Waveform Generator
Oscilloscope
General Procedure:
Attach the various equipment to the undeployed boom assembly
Send deployment command from mock flight computer.
Check for physical damage to boom and/or cables
Check for cable functionality with desired equipment
Restow boom
Facilities:
Electronics Lab, Pilot Room
Notes: Need to reword motivation

## Slide 23
Elements and Updates
Project Schedule
Testing Update
Budget
Cable Routing Test
IMAGES
Expected Key Outcomes:
There is no physical damage to either the 3 differential signal cables or 3-wire power setup
The differential signal cables and 3-wire power setup remains connected to boom structure during and after deployment
Differential signal cables can properly transfer data
3-wire power setup is capable of distributing power to instrument
All design requirements tied to FR 2 pass, therefore this FR passes.

## Slide 24
Elements and Updates
Project Schedule
Testing Update
Budget
LASP Thermal
Chamber
Full
Deployment
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Mass /
Dimension
Cable
Routing
Launch
Environment
Resonant
Frequency

## Slide 25
Elements and Updates
Project Schedule
Testing Update
Budget
Launch Environment Test
Motivation - Verify that the boom assembly components can survive the vibrational loads experienced during
launch.
Requirements Under Test
FR_7
Survive 10 G vibrations in the undeployed state.
DR_7.1
Survive under the conditions of the launch environment in the undeployed state.
Equipment:
UD shaker table
8-Bay Structure
General Procedure:
Setup undeployed boom on shaker table
Qualification test
  General Environmental Verification Standard
Remove boom from shaker table
Deploy boom structure
Facilities:
Vibe room

## Slide 26
Elements and Updates
Project Schedule
Testing Update
Budget
Launch Environment Test
IMAGES
Expected Key Outcomes:
There is no physical damage to the boom structure
Deployment mechanism functions as expected
All design requirements tied to FR 7 pass, therefore this FR passes.
Risk Reduction:
Ensure that the boom will survive the launch environment and function as expected afterwards

## Slide 27
Elements and Updates
Project Schedule
Testing Update
Budget
LASP Thermal
Chamber
Full
Deployment
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Mass /
Dimension
Cable
Routing
Launch
Environment
Resonant
Frequency

## Slide 28
Elements and Updates
Project Schedule
Testing Update
Budget
Resonant Frequency Tests
Motivation - Verify that the boom assembly resonant frequency falls within acceptable
ranges
Requirements Under Test
FR_6
Demonstrate a resonant frequency greater than 2.5 Hz when fully deployed.
Equipment:
Mallet
2 Teardrop accelerometers
Horizontal Shaker Table
8-Bay Structure
General Procedure:
Setup deployed boom on shaker table with accelerometers
Sweep through low frequencies and measure the driven response
  Data has been processed
Hit the boom with a mallet and measure the impulse response
  Data not yet processed
Facilities:
Electronics shop

## Slide 29
Elements and Updates
Project Schedule
Testing Update
Budget
Impulse Resonant Frequency Test

## Slide 30
Elements and Updates
Project Schedule
Testing Update
Budget
Driven Resonant Frequency Test

## Slide 31
Elements and Updates
Project Schedule
Testing Update
Budget
Preliminary Resonant Frequency Test
 | Analytical | Experimental
Resonance | 2.04-7.24 Hz | 2.6 Hz

## Slide 32
Elements and Updates
Project Schedule
Testing Update
Budget
LASP Thermal
Chamber
Full
Deployment
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Mass /
Dimension
Cable
Routing
Launch
Environment
Resonant
Frequency

## Slide 33
Elements and Updates
Project Schedule
Budget
Full Deployment Test
Motivation - Verify the deployment capabilities of the fully assembled boom through a commanded
deployment and verify restow capability.
Requirements Under Test
FR_1
Deploy an instrument of up to 500 g, with 8 x 8 x 8 cm dimensions
FR_4
The boom assembly can communicate with the flight computer
FR_5
Provide ability to re-stow for redeployment
Additionally: DR_1.1, DR_1.2, DR_1.4, SR_1.4.1, DR_1.5, DR_4.1, DR_4.2, SR_4.2.1, DR_4.3, DR_5.1
Equipment:
Sorensen XPH 35-4D Power Supply set as Current Supply
Arduino Due microcontroller (as mock flight computer)
Westward Tape Measure, +/- 1 cm
Teardrop Accelerometer
Timer
Roller
General Procedure:
Attach the various equipment to the undeployed boom assembly such that gravity does not affect deployment
Send deployment command from mock flight computer
Confirm deployment telemetry is being received
Restow boom assembly
Facilities:
Electronics Lab, Pilot Room
Testing Update

## Slide 34: Deployment Test
Elements and Updates
Project Schedule
Budget
Testing Update
STOWED
DEPLOYMENT COMMANDED
DEPLOYMENT IN PROGRESS
DEPLOYMENT COMPLETE
CUBE3 Shell
CUBE3 Shell
CUBE3 Shell
CUBE3 Shell

## Slide 35
Elements and Updates
Project Schedule
Budget
Full Deployment Test
Expected Key Outcomes:
Deployment occurs on command
Deployment status can be identified and sent to the flight computer
After deployment power to the boom is halted
Fully extended the boom is 68.5 cm long with 8 bays
Maximum Instrument Acceleration: To be tested
Deployment Time: To be tested
All design requirements tied to FR 1, 4, and 5 pass, therefore these FR pass
Risk Reduction: Proves that the boom assembly fully deploys as intended and demonstrates designed capabilities
Testing Update
Notes: An instrument can be connected to the attachment plate.
Oscillations are damped out within 65 sec

## Slide 36
Elements and Updates
Project Schedule
Budget
Full Deployment Modeling
Testing Update
M
m
k1
k2
R
M - satellite bus
m - instrument
k1 - boom structure equivalent spring
k2 - power/data cable coils equivalent spring
R - restraining cable
Assume - M >> m, k1 and k2 modeled as linear springs, gravity is orthogonal to direction of motion, rolling resistance is negligible, mass of boom is negligible
m
F1
TR
F2
F1 - force due to Nitinol hinges in compression
TR - tension in restraining cable (tunable)
F2 - force due to cable coil in tension
f - friction
f
Kinematics and energy conservation analysis for unrestrained case yield a deployment time of
t = 0.38 s and final speed of v = 4 m/s*
⇒ Real system will be much slower
*see Nitinol Test backup slides

## Slide 37
Elements and Updates
Project Schedule
Testing Update
Budget
LASP Thermal
Chamber
Full
Deployment
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Mass /
Dimension
Cable
Routing
Launch
Environment
Resonant
Frequency

## Slide 38
Elements and Updates
Project Schedule
Budget
Mass/Dimension Test
Motivation - Verify that the physical characteristics of the undeployed boom assembly fit within the
given requirements.
Requirements Under Test
DR_3.1
Stow with a length less than or equal to
15 cm, including instrument
DR_3.2
Stow with a height less than or equal to
10 cm, including instrument
DR_3.3
Stow with a width less than or equal to
10 cm, including instrument
DR_3.4
Provide 6 mm by 6 mm accommodation space at each corner for NanoRacks guide rails
FR_9
The whole system, including instrument, will have a maximum total mass of 2kg
Equipment:
Shars Aventor Calipers, +/- 0.01 mm
Acculab SV-50 Scale, +/- 10 g
General Procedure:
Measure the dimensions of the x-y-z axes
Measure the accommodation space for the guide rails
Weigh the full boom assembly
Facilities:
Electronics Lab
Testing Update
Notes: Success Criteria:
Length, width, and height dimensions fall at or below required value.
Accommodation space for guide rails meets NanoRack specification.
Mass of the full boom assembly lies within the required range.

## Slide 39
Elements and Updates
Project Schedule
Budget
Mass/Dimension Test
Test Results
Req. ID
Expected Result
DR_3.1
Length = 15 cm
DR_3.2
Height = 10 cm
DR_3.3
Width = 10 cm
DR_3.4
Guide Rail Space =
6 mm x 6 mm
FR_9
Mass ≤ 2 kg
Risk Reduction: Confirms that the manufactured boom assembly fits within the sizing and weight restraints set at the start of the project
Testing Update
Preliminary Result
Length = 14.99 cm
Height = 9.95 cm
Width = 9.95 cm
Guide Rail Space =
6 mm x 6 mm
Mass = 0.89 kg

## Slide 40
Elements and Updates
Project Schedule
Testing Update
Budget
LASP Thermal
Chamber
Full
Deployment
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Planned
Scheduled
Completed
Processed
Mass /
Dimension
Cable
Routing
Launch
Environment
Resonant
Frequency

## Slide 41
Elements and Updates
Project Schedule
Testing Update
Budget
LASP Thermal Chamber Test
Motivation - Verify that the boom assembly components can survive the thermal fluctuations
experienced in space and establish good deployment temperatures.
Requirements Under Test
DR_8.1
The boom assembly shall survive the thermal fluctuations of the space environment in both the deployed and undeployed configuration.
Equipment:
Big White Thermal Chamber
Thermocouples
2-Bay Structure
General Procedure:
Setup undeployed boom in thermal chamber
Ramp down to -60 °C
Ramp up to 10 °C
Deploy Boom
Ramp down to -60 °C
Return to ambient and repeat with different deployment temperatures
Facilities:
LASP Thermal Chamber Room
Notes: Success Criteria:
Length, width, and height dimensions fall at or below required value.
Accommodation space for guide rails meets NanoRack specification.
Mass of the full boom assembly lies within the required range.

## Slide 42
Elements and Updates
Project Schedule
Testing Update
Budget
LASP Thermal Chamber Test
Risk Reduction:
Establish feasibility of components not breaking due to extremely low temperatures
Establish adequate deployment temperatures for the Nitinol hinges
Thermocouple Locations
Big White
Thermal Chamber
Expected Key Outcomes:
Components remain unbroken and functional at the extreme minimum temperature
Associate deployment times with deployment temperatures
Determine lowest possible deployment temperature of the Nitinol
1
2
Notes: Success Criteria:
Length, width, and height dimensions fall at or below required value.
Accommodation space for guide rails meets NanoRack specification.
Mass of the full boom assembly lies within the required range.

## Slide 43
Elements and Updates
Project Schedule
Testing Update
Budget
LASP Thermal Chamber Profile
Notes: Success Criteria:
Length, width, and height dimensions fall at or below required value.
Accommodation space for guide rails meets NanoRack specification.
Mass of the full boom assembly lies within the required range.

## Slide 44
Elements and Updates
Project Schedule
Testing Update
Budget
Thermal Model
Notes: Success Criteria:
Length, width, and height dimensions fall at or below required value.
Accommodation space for guide rails meets NanoRack specification.
Mass of the full boom assembly lies within the required range.

## Slide 45: Budget Update
Budget Update
Testing Update
Schedule Update
Overview
Notes: MB

## Slide 46
Elements and Updates
Project Schedule
Manufacturing Status
Budget Update
Budget - Parts/Materials Procurement Status
Area of Interest | Supplier | Cost | Status
Tooling | McMaster Carr | $322.44 | Delivered
Hardware | McMaster Carr | $260.71 | Delivered
Epoxy | Ellsworth | $90.58 | Delivered
PEEK | McMaster Carr | $770.66 | Delivered
Carbon Fiber | Goodwinds | $627.94 | Delivered
Nitinol | Confluent Medical | $295.80 | Delivered
Wiring/Electronics | DigiKey, Amazon | $255.55 | Delivered
Total | All | $2,623.68 | 

## Slide 47
Elements and Updates
Project Schedule
Manufacturing Status
Budget Update
Budget - Financial Budget Status
10% Margin
15% Contingency
Notes: Change TVAC to LASP
-Only costing $200 now

## Slide 48: Questions?
Project Schedule
Manufacturing Status
Budget
CUBE3
</>
</>

## Slide 49: Backup Slides
Project Schedule
Manufacturing Status
Budget
Backup Slides
</>
</>

## Slide 50
Project Schedule
Manufacturing Status
Budget
Backup Slides
Power Test
Motivation - Determine the power consumption of the Polyethylene-Burn Wire system. Used to verify
requirement DR_1.3
Facilities:
Electronics Lab
Equipment:
Sorensen XPH 35-4D Power Supply set as Current Supply
Keysight 34461A Digit Multimeter set as Ohmmeter
Mock Polyethylene-Burn Wire System
General Procedure:
Measure systems resistance
Set current to 0.8 Amps and start test
Record time taken to burn
Calculate Power consumption (P=I^2*R)
Risk Reduction: Confirms that the deployment mechanism uses less than the maximum allocated amount of power of 30 W.
Test Results
Test No.
Resistance
Time of Burn
Power
Current
1
3.59Ω
3 sec
2.30 W
0.8 A
2
3.59Ω
4 sec
2.30 W
0.8 A
3
3.59 Ω
3 sec
2.30 W
0.8 A
4
3.59 Ω
3 sec
2.30 W
0.8 A
5
3.59 Ω
2 sec
2.30 W
0.8 A
Avg.
3.59 Ω
3 sec
2.30 W
0.8 A

## Slide 51
Project Schedule
Manufacturing Status
Budget
Backup Slides
Epoxy Test
Axial stress test to failure
Three tests of each plug design,
Plug A held 12.1 +/- 1.96 kg
Plug B held 11.2 +/- 1.70 kg
Plug C held 7.9 +/- 3.73 kg

## Slide 52
Project Schedule
Manufacturing Status
Budget
Backup Slides
Nitinol Test

## Slide 53
Project Schedule
Manufacturing Status
Budget
Backup Slides
Nitinol Test

## Slide 54
Project Schedule
Manufacturing Status
Budget
Backup Slides
Nitinol Test Results
Mean force: 5.3 N
Total displacement: 18.7 cm
Total work: 4.05 J
Work-Energy Theorem implies that 2.0 J stored as potential energy in each truss bay
Conservation of energy for a massless boom yields a final velocity of the instrument
8-bay truss gives 4.0 m/s

## Slide 55: Telemetry Switch Trade Study
Project Schedule
Manufacturing Status
Budget
Backup Slides
 | Weight | Snap Switch | IR Sensor | Optical Encoder
Mechanical Complexity (0-5) | 30% | 2 | 5 | 3
Redundancy Opportunity (0-1) | 10% | 0 | 1 | 1
Software Complexity (0-5) | 10% | 5 | 5 | 3
Power Draw (0-5) | 10% | 5 | 3 | 4
Size (0-5) | 40% | 1 | 5 | 4
Total | 100% | 40% | 96% | 74%
During MSR a valid point was brought up as to why an encoder was not considered to count rotations.
  A viable option given manufacturing timeline and space available
A trade study was performed against the current baseline design option and optical encoder based options

## Slide 56
Project Schedule
Manufacturing Status
Budget
Backup Slides

## Slide 57
Project Schedule
Manufacturing Status
Budget
Backup Slides

## Slide 58
Project Schedule
Manufacturing Status
Budget
Backup Slides
GEVS Standard

## Slide 59: Software FBD
Project Schedule
Manufacturing Status
Budget
Backup Slides
MATLAB App
Arduino Code
Sense Temp
Arm Relay
Deploy Boom
Confirm Temp
Confirm Relay Arming
Power IR LED
Close Relay
Detect Spool Revolutions
Open Relay
Report Deployment State

## Slide 60: Circuit Board V1.0
Project Schedule
Manufacturing Status
Budget
Backup Slides
Key
GND Layer
Top Layer

## Slide 61
Project Schedule
Manufacturing Status
Budget
Backup Slides
Thermal Model MATLAB Equations

## Slide 62
Project Schedule
Manufacturing Status
Budget
Backup Slides
Resonant Frequency Analytical Model
“The Solidworks vibration simulations have been run with accurate physical models, meaning that the physical assembly being meshed is fully compliant with what the team intends to produce in the end. Sixteen cases were run, made up of cases for one bay through eight bays, all with both an instrument case and a no instrument case. A max of only eight bays was run because any more than that is pushing the limit of what a laptop can do, and it’s the number of bays needed for 60cm extension. All sixteen simulations were run with the highest quality blended-curvature mesh, using the adaptive solver.”