## Slide 1: Deployed RF Antennas for GPS-denied Optimization and Environmental Navigation
Dawson Beatty, Christian Carmack, Jeremy Fie,
Chris Greer, Ross Kloetzel, Jack Maydan,
Kyle Nieukirk, Virginia Nystrom, Amanda Siirola,
Ryan Stewart, Luke Tafur, Ivan Yurkin
Test Readiness Review

## Slide 2: Project Overview
Project Overview
Schedule
Budget
Testing

## Slide 3: Project Purpose
Imagine a rover with an objective to explore a remote location, such as Martian deserts or urban canyons
Methods of Navigation:
  GPS
  Landmarks
  Odometry
The DRAGON team pursues a solution using deployed RF beacons as an in-situ GPS network to correct inertial error
High Error

## Slide 4: Specific Objectives
The DRAGON team will provide a fully autonomous method to navigate an unmanned rover in GPS-denied environments with 1m accuracy
This will be done by developing:
  Pods which contain RF-Localization beacons.
  Deployment mechanism to deploy pods to software-determined locations
  Software to determine absolute position and navigate to waypoints
The pods will also have the demonstrational ability to collect and transmit environmental data.

## Slide 5: CONOPS
1 | Upload Mission Information Package |  | 
2 | Collect GPS Truth Position |  | 
3 | Generate Path |  | 
4 | Generate Pod Locations |  | 
5 | Deploy 3 Anchor Pods |  | 
6 | Deploy & Map Pods | or | Move & Localize Rover
7 | Repeat 6 Until Final Waypoint |  | 
MIP
Terrain Map
Waypoints
Obstacles
Mission Planning
Mission Execution
A
B
C

## Slide 6: Levels of Success
 | Level 1 | Level 2 | Level 3
Rover Navigation | Localize rover to 1m with pod array for a 15m user-controlled path. | Correct rover position to 1m with closed-loop error correction. | Autonomously navigate SW-L1 path to within 1m of all 5-10 waypoints.
Pod Deployment | Pods are hand placed, in analytically predetermined locations. | Deploys pod to range > 10m. Internal electronics function after impact. | Rover software calculates trajectories and commands to deploy.
Scientific Data |  | Pods record pressure, temperature, and acceleration data. | Pods collect environmental data at 5 minute frequency.
Pod | Pods provide RF ranging measurements to the rover. | Pods communicate amongst themselves using a mesh network. | Pods toggle between high and low power modes.
Software | Find path for rover to reach 5-10 waypoints avoiding obstacles. | Software determines pod placement for best RF-ranging | Pod placement software balances best science and best RF-ranging.
Verified on Rover
Verified on Laptop
 | Level 1 | Level 2 | Level 3
Rover Navigation | Localize rover to 1m with pod array for a 15m user-controlled path. | Correct rover position to 1m with closed-loop error correction. | Autonomously navigate SW-L1 path to within 1m of all 5-10 waypoints.
Pod Deployment | Pods are hand placed, in analytically predetermined locations. | Deploys pod to range > 10m. Internal electronics function after impact. | Rover software calculates trajectories and commands to deploy.
Scientific Data |  | Pods record pressure, temperature, and acceleration data. | Pods collect environmental data at 5 minute frequency.
Pod | Pods provide RF ranging measurements to the rover. | Pods communicate amongst themselves using a mesh network. | Pods toggle between high and low power modes.
Software | Find path for rover to reach 5-10 waypoints avoiding obstacles. | Software determines pod placement for best RF-ranging. | Pod placement software balances best science and best RF-ranging.

## Slide 7: FBD

## Slide 8: Deployment Module Design
Front View
Side View
20”
17”
10”
30”

## Slide 9: Pod Structure Design
Pod structure contains the ranging electronics: deployed from cannon
Contains batteries in tail for power, electronics are potted for resilience.

## Slide 10: Pod Electronics Design
Capabilities:
  Pod to Pod Ranging
  Environmental data (pressure, temperature, and altitude)
  Accelerometer data (+/- 100g’s)
  SD card writing (Environmental and Accel. data)
Dragon Egg Shield [6cm x 6cm]

## Slide 11: Navigation Software Design
Capabilities:
  Generate path and pod deployment points to reach all 10 waypoints
  Localize rover using RF ranging data to correct rover odometry
  Generate closed-loop control routine to use localization data to keep rover within 1 m of path

## Slide 12: Critical Project Elements
CPE | Testing Status
State Estimation | 15m localization test successful
Path Following | Tested forward and yaw control
RF Ranging | 14/14 PCBs pass checkout test
Spring Cannon | Motor and gear safety demo complete
Pod Storage & Reload | Testing interface with pod structure
Pod Structure | 4 pod structures complete

## Slide 13: Schedule
Project Overview
Schedule
Budget
Testing

## Slide 14: Gantt Chart
Complete
In Progress
May Use Margin
Expected on Time
Removed Task
Critical Task

## Slide 15: Testing
Project Overview
Schedule
Budget
Testing

## Slide 16: Testing Plan
Subsystem
System
Nav. + Electronics | 
Rover/Pod Cmd Test | 3/17
Mission-Length Ctrl | 3/24
Struct. + Electronics | 
Pod Protection Test | 3/24
Cannon + Rover | 
Cannon Interface Test | 3/31
Integration
Full System | 
Safety Demo | 4/7
Mission Sim | 4/14
Cannon | 
Reloading Demo | 3/8
Range Demo | 3/8
Pod Electronics | 
Checkout Test | 2/25
Accuracy Test | 3/1
Mesh Network Test | 3/7
Pod Structure | 
Stability Test | 2/25
Drop Test | 3/1
Navigation | 
MIP Ingest Demo | 2/25
Rover Odometry Ctrl | 3/1
Rover GSLAM Demo | 3/7
Complete
In Progress

## Slide 17: Navigation Testing
 | Test | Purpose | Status
Localization | Localize Stationary Rover | Software determines position relative to any pod in range via RF-Localization | Results Verified 2/21
 | 15m Localization Test | Verify that localization results match model for 15m | Results Verified 2/28
 | Mission-Length Localization Test | Verify localization results match model & keep error under 1m in mission conditions | Test Scheduled 3/15
Control | Odometry Control Test | Characterize rover control error with odometry only | Test in Progress
 | RF + Odometry Control Test | Demonstrate that pods correct odometry error and match model for 15m | Test Scheduled 3/8
 | Mission-Length Control Test | Verify pod correction to under 1m in mission conditions | Test Scheduled 3/24
Risk Reduction: These tests generate internal heritage and allow for easy build up upon previous success

## Slide 18: 15m Localization Test
Facility: Business/Kitt Field
Equipment:
  Rover + beacon
  3x Pods
  Tape/measuring equipment
Procedure:
  Distribute pods at known locations
  Tele-op rover along path with estimation algorithm running
Objective: Localize rover during 15m tele-op’ed traversal with pods
Requirements Verified | 
S2.1 | The software shall combine RF-Localization and inertial/odometry position estimates in order to enhance position estimation accuracy
S2.1.2 | The rover shall estimate position using onboard odometer and IMU
Additional: S2.1.1 | 
Expected Result: Rover position estimate falls within model from CDR
Test Scheduled
Test Completed
Data Analyzed
Results Verified
Complete
In Progress
Notes: Need to include status

## Slide 19: 15m Localization Test Setup
Pod locations and rover path marked with tape
Tele-operate rover along path
Level One success criteria: within 1m of path at all times

## Slide 20: 15m Localization Test Model
Model: 10,000 Monte Carlo simulations with 60cm sample error

## Slide 21: 15m Localization Test Results
Odometry max error = 1.15 m
GSLAM max error = .35 m

## Slide 22: Testing Plan
Subsystem
System
Nav. + Electronics | 
Rover/Pod Cmd Test | 3/17
Mission-Length Ctrl | 3/24
Struct. + Electronics | 
Pod Protection Test | 3/24
Cannon + Rover | 
Cannon Interface Test | 3/31
Integration
Full System | 
Safety Demo | 4/7
Mission Sim | 4/14
Cannon | 
Reloading Demo | 3/8
Range Demo | 3/8
Pod Electronics | 
Checkout Test | 2/25
Accuracy Test | 3/1
Mesh Network Test | 3/7
Pod Structure | 
Stability Test | 2/25
Drop Test | 3/1
Navigation | 
MIP Ingest Demo | 2/25
Rover Odometry Ctrl | 3/1
Rover GSLAM Demo | 3/7
Complete
In Progress

## Slide 23: Pod Electronics Checkout Test
Facility: ITLL
Equipment:
  14 Fully Populated Pods (Electronics Only)
  1 Rover Beacon
  Power to boards (micro USB and Batteries)
Procedure:
  Verify electrical connections
  Test ranging and environmental data transfer
  Verify current in high power mode
  Verify current in low power mode
Requirements Verified | 
P6.1 | Pod shall have an environmental sensor package
P6.2 | Pod shall operate above 3.3V and under 20mA current in ‘low power mode’, refer to DR 5.3
P6.3 | Pod shall operate above 3.3V and under 300mA current in ‘high power mode’, refer to DR 5.3
P6.4 | Pod shall have ability to toggle between low power and high power modes
Additional: P6.1.1, P6.1.3, P6.1.4, P6.3.1.1, P6.3.1.2, P6.4.1, P6.4.2 | 
Objective: Verify the Hardware Capabilities of the Pod Electronics
Expected Result: Pod is able to transmit ranging and environmental data, verify power constraints
Test Scheduled
Test Completed
Data Analyzed
Results Verified
Complete
In Progress
Notes: Need to include status

## Slide 24: Pod Electronics Results
 | Requirement High/Low Power | Expected High/Low Power | Actual High/Low Power
Average | 300/20 [mA] | 290/17.5 [mA] | 211.7/12.44 [mA]
Risk Reduction: Every single board proven to meet requirements
P6.2 | Pod shall operate above 3.3V and under 20mA current in ‘low power mode’, refer to DR 5.3
P6.3 | Pod shall operate above 3.3V and under 300mA current in ‘high power mode’, refer to DR 5.3
Each board was tested using a multimeter recording min/max for a full cycle (30 seconds)

## Slide 25: Pod Ranging Accuracy Test
Facility: Business Field
Equipment:
  14 Fully Populated Pod (Electronics Only)
  1 Rover Beacon
  Power to boards (micro USB and Batteries)
  Tape Measure
Procedure:
  Place the beacon and pods 60 m apart and take measurements to ensure precision between pods
  Power 1 pod at a time verify that each pod can measure to at least 60 m
  Using 1 pod and the beacon take measurements starting at 10 m up to max distance in 5 m increments
Requirements Verified | 
P6.5 | Pod shall have operational 'ranging' capability at distances no less than 60m.
P6.5.1 | Pods shall have range measurement errors no greater than 0.5m averaged over 30 samples.
Objective: Range and Accuracy of Pod Measurements
Expected Result: Max range of pod ranging is >60 m and the measurements can be corrected to less than 0.5 m uncertainty
Test Scheduled
Test Completed
Data Analyzed
Results Verified
Complete
In Progress
Notes: Need to include status

## Slide 26: Pod Ranging Validation Test Results
Calibrated Distance = 0.9986*(Measured Distance) - 0.5511
Fi
Max Distance: 80 [m]
3σ Bound
CDR Test: 0.665 [m] Error
TRR Test:
0.319 [m] Error
Risk Reduction: Every single board is characterized for accuracy. Provides clear understanding of error and validates each board.

## Slide 27: Testing Plan
Subsystem
System
Nav. + Electronics | 
Rover/Pod Cmd Test | 3/17
Mission-Length Ctrl | 3/24
Struct. + Electronics | 
Pod Protection Test | 3/24
Cannon + Rover | 
Cannon Interface Test | 3/31
Integration
Full System | 
Safety Demo | 4/7
Mission Sim | 4/14
Cannon | 
Reloading Demo | 3/8
Range Demo | 3/8
Pod Electronics | 
Checkout Test | 2/25
Accuracy Test | 3/1
Mesh Network Test | 3/7
Pod Structure | 
Stability Test | 2/25
Drop Test | 3/1
Navigation | 
MIP Ingest Demo | 2/25
Rover Odometry Ctrl | 3/1
Rover GSLAM Demo | 3/7
Complete
In Progress

## Slide 28: Deployment Range Pretests
Pretests |  | Status
DT2.1 | Gear rotation with no load | Done
DT2.2 | Gear rotation with rack and applied load (no spring) | Done
 | Safety Demonstrations and Pre-tests | Done
DT2.3 | Partial spring compression | 3/5
DT2.4 | Full spring compression | 3/8
Objective: Ensure safety of cannon sub-system before full range testing
Risk Reduction: Electronics validated with no load first, then combined with load and additional mechanical components.
Complete
In Progress
Notes: Need to include status

## Slide 29: Updated Pod Trajectory Model
Gear Rack and Launch Plate Mass: 470 [g] (Up from 320 [g])
Pod Mass: 400 [g] (Down from 500 [g])
Predicted Distance: 11.52 [m]
Intend to verify model using measuring tape and video recording in RECUV Lab
Objective: Verify cannon deploys to at least 10m
Notes: 10.3 m/s is approx 23 mph

## Slide 30: Deployment Range Test
Facility: Business Field or RECUV Lab
Equipment:
  Fully built deployment module (gears, spring, support, launch tube, baseplate)
  DC motor
  At least one fully built pod
Procedure:
  With safety procedures in place, load pod into launch tube
  Send command to begin spring compression
  Measure distance after pod is deployed
  Repeat
Requirements Verified | 
D3.8.1 | DM shall have the following range: No less than 10m
Objective: Verify cannon deploys to at least 10m
Expected Result: Overall launch system works as designed and will allow for repeatable deployments to at least 10 m
Test Completed
Data Analyzed
Results Verified
Complete
In Progress
Test Scheduled (3/8)
Notes: Need to include status

## Slide 31: Testing Plan
Subsystem
System
Navigation + Electronics | 
Rover/Pod Cmd Test | 3/17
Mission-Length Ctrl | 3/24
Pod Structure + Electronics | 
Pod Protection Test | 3/24
Cannon + Rover | 
Cannon Interface Test | 3/31
Integration
Full System | 
Safety Demo | 4/7
Mission Sim | 4/14
Cannon | 
Reloading Demo | 3/8
Range Demo | 3/8
Pod Electronics | 
Checkout Test | 2/25
Accuracy Test | 3/1
Mesh Network Test | 3/7
Pod Structure | 
Stability Test | 2/25
Drop Test | 3/1
Navigation | 
MIP Ingest Demo | 2/25
Rover Odometry Ctrl | 3/1
Rover GSLAM Demo | 3/7
Complete
In Progress

## Slide 32: Integration Plan
Ready for Full System Testing
Challenge: Fit checks and tolerance stack up
Estimated Work:
2 hours for fit checks
1 hour for final install
2 hour Cannon Interface Test 3/31
Cannon + Rover
Challenge: Consistency and fatigue testing
Estimated Work:
1 hour potting per board (x14)
2 hour Pod Protection Test 3/24
Challenge: Combining different software pieces software into main function
Estimated Work:
35 hours testing rover software
2 hour Rover/Pod Command Test
4 Hour Mission Length Control Test
Pod Structure + Electronics
Navigation + Electronics
62 Hours
System Integration
by April 1

## Slide 33: Testing Plan
Subsystem
System
Nav. + Electronics | 
Rover/Pod Cmd Test | 3/17
Mission-Length Ctrl | 3/24
Struct. + Electronics | 
Pod Protection Test | 3/24
Cannon + Rover | 
Cannon Interface Test | 3/31
Integration
Full System | 
Safety Demo | 4/7
Mission Sim | 4/14
Cannon | 
Reloading Demo | 3/8
Range Demo | 3/8
Pod Electronics | 
Checkout Test | 2/25
Accuracy Test | 3/1
Mesh Network Test | 3/7
Pod Structure | 
Stability Test | 2/25
Drop Test | 3/1
Navigation | 
MIP Ingest Demo | 2/25
Rover Odometry Ctrl | 3/1
Rover GSLAM Demo | 3/7
Complete
In Progress

## Slide 34: Full System Safety
Cannon Safety |  | 
Motor Reverse | User sends reverse motor direction mid-spring compression | To Be Tested: 3/31
Electrical Inhibit | Electrical inhibit prevents deployment electronics from working | To Be Tested: 3/22
LED Indicator | LED mounted on rover indicating safety state | To Be Tested: 3/31
Rover Safety |  | 
Deadman’s Switch | Button on PS4 controller required to be depressed or rover stops | Tested on: 2/22
User Takeover | Built-in multiplexer gives controller priority over any other commands | Tested on: 2/22
Remote Shutdown | User sends full shutdown command via Ground Station | To Be Tested: 3/15
Complete
In Progress
Notes: Need to include status
Could be combined or replaced as Full System Safety Demo —-Needs to be done before ranging test!

## Slide 35: Full Mission Demo
Facility: Open flat grass field
Equipment:
  Jackal rover, deployment system, pods, electronics
  GPS
  Final MIP
Requirements Verified | 
M1 | Project’s primary objective
- | Many subsequent requirements
Objective: Full mission completion and demonstration
Expected Result: GPS readings & rover internal estimates match within 1m at EOM
Test Completed
Data Analyzed
Results Verified
Complete
In Progress
Test Scheduled (4/14)
Notes: Need to include status

## Slide 36: Full Mission Demo
Testing Procedure:
Mark waypoints and rover obstacles
Place team members surrounding area for range safety
Begin GPS recording on rover, pre-verified
Perform all safety checks, check: remote kill, takeover
Load pods and zero cannon azimuth
Upload mission sequence
Perform initial deployment, collect pod readings
Rover builds pose estimate, proceeds with mission
Collect post data mission and verify mission success
Special Requirements:
Obtain permission for field operations
Mark out hazard zone for range safety
Weather cooperation
1e-2 m accuracy, 10Hz sample rate, record to ground station computer
5e-1 m accuracy, 30Hz sample rate per pod, closed loop control on rover
Success: GPS readings and rover internal estimates match within 1m at EOM

## Slide 37: Full Mission Expected Results

## Slide 38: Budget
Project Overview
Schedule
Budget
Testing

## Slide 39: Budget
*Notes:
Budget based on estimated 12 pods + 4 pods for prototyping
Total Cost: | $3,454.29
Total Spent: | $3,356.77
Margin (for replacements): | $830.77
Shipping: | $300.00
Reserve: | $414.94
 | $5000.00
Purchased
Margin
Notes: * Status of all procurements (color code: parts received, pending, and planned)
* Highlight parts with long-lead and most important parts to project success.
* Highlighting uncertainties and corresponding budget margins

## Slide 40: Budget
All long lead time parts have arrived
All critical parts have arrived except pod structure
Pod Structure parts in transit or can be purchased locally
Left to Purchase:
Pod Booms
Wall Housing
Tail Cap
To be purchased after pod/cannon interface testing (3/12)
Purchased
Margin
Received
To Purchase
Long Lead Time
Critical Part
Notes: * Status of all procurements (color code: parts received, pending, and planned)
* Highlight parts with long-lead and most important parts to project success.
* Highlighting uncertainties and corresponding budget margins
How have we saved money:( I originally planned for a worst case scenario) Money saved by not doing third PCB revision, cheaper to buy blue pill than STM32 processors, deployment finding different company to purchase base plate to say money, reusing components during PCB testing (and buying the support components in bulk at once), minimizing shipping as much as possible, custom PCB through Osh Park rather than Advanced circuits which was originally planned.

## Slide 41: Appendix

## Slide 42: A. Navigation Tests

## Slide 43: Testing Plan
Subsystem
System
Nav. + Electronics | 
Rover/Pod Cmd Test | 3/17
Mission-Length Ctrl | 3/24
Struct. + Electronics | 
Pod Protection Test | 3/24
Cannon + Rover | 
Cannon Interface Test | 3/31
Integration
Full System | 
Safety Demo | 4/7
Mission Sim | 4/14
Cannon | 
Reloading Demo | 3/8
Range Demo | 3/8
Pod Electronics | 
Checkout Test | 2/25
Accuracy Test | 3/1
Mesh Network Test | 3/7
Pod Structure | 
Stability Test | 2/25
Drop Test | 3/1
Navigation | 
MIP Ingest Demo | 2/25
Rover Odometry Ctrl | 3/1
Rover GSLAM Demo | 3/7
Complete
In Progress

## Slide 44: Localize Stationary Rover
Facility: N/A
Equipment:
  Rover + beacon
  3x Pods
Procedure:
  Place pods a known distance from rover
  Input the “deployment angle” of each pod to the rover
  Range between pods and rover
Objective: Show rover is able to localize using pods alone
Requirements Verified | 
S2.1.1 | Software shall be able to determine position relative to any pod in range via RF-Localization
Result: Algorithm estimate of rover/pod locations accurate to ~10cm
Test Scheduled
Test Completed
Data Analyzed
Results Verified
Complete
In Progress
Notes: Need to include status

## Slide 45: GNSS Accuracy Test
Facility: Baseline
Equipment:
  Rover
  GNSS module
Procedure:
  Walk GNSS unit along Baseline
  Mount GNSS on rover, drive rover along the same path
  Record data at 1m increments
  Compare recorded data to truth
Objective: Demonstrate GNSS accuracy
Requirements Verified | 
G1.1.1 | GNSS accuracy shall be 1m or less
S1.3.1 | Software shall record initial GNSS position of rover
S7.1 | Software shall be capable of recording GNSS data on the rover for the duration of the mission
Expected Result: GNSS accurate to <1m
Test Completed
Data Analyzed
Results Verified
Test Scheduled
Complete
In Progress
Notes: Need to include status

## Slide 46: MIP Upload Test
Facility: N/A
Equipment:
  Rover
  GNSS Unit
  Sample valid and invalid MIP
Procedure:
  Upload MIP
  Rover collects GNSS truth
  Generate path with A*
  Determine pod locations
Requirements Verified | 
G9.4.1 | User shall upload MIP to Software
S1.3 | Software shall generate a path through the terrain to reach up to 10 waypoints
S3.1.1 | Software can determine pod location for placement for most effective ranging
Additional: S1.3.1, S1.3.2, S1.3.2.1, S1.3.3 S1.3.3.1 | 
Objective: Verify MIP upload and start of mission capabilities
Expected Result: Able to complete mission-start procedure
Data Analyzed
Results Verified
Test Completed
Test Scheduled
Complete
In Progress
Notes: Need to include status - if Christian fixes GPS we can test this but currently works w initial GPS guess -- RYAN

## Slide 47: Pod Location Validity Test
Facility: N/A
Equipment:
  Localization MC simulation
  Pod ranging estimates
Procedure:
  Simulate path traversal
  Simulate pod deployment and ranging
  Propagate pessimistic assumption of error
Objective: Demonstrate ability to determine effective pod locations
Requirements Verified | 
S3.1.1 | Software can determine pod location for placement for most effective ranging
S3.1.2 | Software can determine pod location for placement for for most valuable environmental data.
S3.1.3 | Software shall incorporate terrain obstacles into deployment location selection to avoid pre-defined obstacles
Additional: .S3.1, S3.1.4 | 
Expected Result: Show localization error sufficiently low in theory
Data Analyzed
Results Verified
Test Completed
Test Scheduled
Complete
In Progress
Notes: Need to include status

## Slide 48: Time-on-Target
Facility: Business/Kitt Field
Equipment:
  Rover + beacon
  11x Pods
  Tape/measuring equipment
Procedure:
  Distribute pods at known locations
  Rover drives autonomously along path, correcting deviations and adjusting velocity to meet time-on-target requirements
Objective: Rover follows path and meets time requirements
Requirements Verified | 
S1.3.3 | Rover shall meet MIP time requirements, ‘on-time, on-target’ for each waypoint
Expected Result: Rover arrives at waypoints within CHANGE_ME seconds of specified time
Test Completed
Data Analyzed
Results Verified
Test Scheduled
Complete
In Progress
Notes: Need to include status

## Slide 49: Full-Mission-Length Traversal
Facility: Business/Kitt Field
Equipment:
  Rover + beacon
  11x Pods
  Tape/measuring equipment
Procedure:
  Distribute pods at known locations
  Tele-op rover along path with estimation algorithm running
Objective: Localize rover during full-mission-length tele-op’ed traversal with pods
Requirements Verified | 
M2 | The rover shall estimate its absolute position
S2.1.2 | The rover shall estimate position using onboard odometer and IMU
Additional: S2.1.1 | 
Expected Result: Rover position estimate accurate to 1m along path
Test Completed
Data Analyzed
Results Verified
Test Scheduled
Complete
In Progress
Notes: Need to include status

## Slide 50: Rover Control Test
Facility: COHRINT Space
Equipment:
  Rover + beacon
  3x pods
  Procedure:
  Upload set of points to rover
  Rover follows path using odometry alone
Objective: Rover follows a path with odometry alone
Requirements Verified | 
S1.2.1 | Software shall be capable of controlling rover’s physical motion through wheel actuators/ROS nodes
Expected Result: Able to direct rover to move autonomously
Test Scheduled
Test Completed
Data Analyzed
Results Verified
Complete
In Progress
Notes: Need to include status

## Slide 51: Closed-Loop Correction
Facility: Business/Kitt Field
Equipment:
  Rover
  3x Pods
  Tape/measuring equipment
Procedure:
  Distribute pods at known locations
  Rover drives autonomously along 15m path, correcting deviations
Objective: Rover follows A* path with RF-corrected odometry
Requirements Verified | 
S1.2 | Rover shall have feedback control to correct for path deviance
S1.2.2 | Software shall have closed loop correction of inertial/odometry location measurement error by using pod RF-Localization
Expected Result: Rover navigates path deviating no more than CHANGE_ME cm
Data Analyzed
Results Verified
Test Completed
Test Scheduled
Complete
In Progress
Notes: Need to include status

## Slide 52: Deployment-Rover Interface
Facility: N/A
Equipment:
  Rover
  Deployment mechanism with arduino control system
Procedure:
  Command firing while rover moving
  Verify rover stops
  Verify deployment mechanism turns and fires at correct angle
Objective: Rover commands deployment mechanism azimuth angle
Requirements Verified | 
S9.2.1 | Rover shall always stop before commanding a deployment
S9.2.2 | Software shall provide heading with respect to rover state to deployment
D3.4 | DM shall have interface with rover SW for commanding deployment mechanism to deploy pods
D8.3.1 | Deployment module shall be compatible with provided onboard power
Expected Result: Deployment mechanism interfaces with rover
Test Completed
Data Analyzed
Results Verified
Test Scheduled
Complete
In Progress
Notes: Need to include status

## Slide 53: RF State Estimation Test
Facility: Open flat grass field
Equipment:
  Jackal rover and ranging boards
  GPS
  Weather cooperation
Procedure:
  Begin GPS recording on rover (1e-2m accuracy)
  ‘Hand Place’ pods at desired locations
  Upload mission sequence
  Collect first pod readings, Build pose estimate
  Tele-op rover to second known position
  ‘Hand Place’ additional pods, Build second pose estimate with rover
Requirements Verified | 
M2 | 
M5 | 
S2.1 S2.1.3 S2.1.1 S9.2.3 | 
Additional: | 
Objective: Demonstrate pod network functionality to rover
Expected Result: Rover can range to pods, Calculate pose, Add new pods to network
Data Analyzed
Results Verified
Test Completed
Test Scheduled
Complete
In Progress
Notes: Need to include status

## Slide 54: B. Electronics Tests

## Slide 55: Testing Plan
Subsystem
System
Nav. + Electronics | 
Rover/Pod Cmd Test | 3/17
Mission-Length Ctrl | 3/24
Struct. + Electronics | 
Pod Protection Test | 3/24
Cannon + Rover | 
Cannon Interface Test | 3/31
Integration
Full System | 
Safety Demo | 4/7
Mission Sim | 4/14
Cannon | 
Reloading Demo | 3/8
Range Demo | 3/8
Pod Electronics | 
Checkout Test | 2/25
Accuracy Test | 3/1
Mesh Network Test | 3/7
Pod Structure | 
Stability Test | 2/25
Drop Test | 3/1
Navigation | 
MIP Ingest Demo | 2/25
Rover Odometry Ctrl | 3/1
Rover GSLAM Demo | 3/7
Complete
In Progress

## Slide 56: Pod Electronics Results
P6.2- Pod shall operate above 3.3V and under 20mA current in ‘low power mode’, refer to DR 5.3
P6.3- Pod shall operate above 3.3V and under 300mA current in ‘high power mode’, refer to DR 5.3
Each board was tested using a multimeter recording min/max for a full cycle (30 seconds)
Risk Reduction: Every single board proven to meet requirements
Pod | Requirement High/Low Power | Expected High/Low Power | Actual High/Low Power
Average | 300/20 [mA] | 290/17.5 [mA] | 211.7/12.44 [mA]
0 |  |  | 215/12.7 [mA]
1 |  |  | 206/12.5 [mA]
2 |  |  | 224/12.1 [mA]
3 |  |  | 204/12.8 [mA]
4 |  |  | 209/12.3 [mA]
5 |  |  | 220/12.6 [mA]
6 |  |  | 201/12.6 [mA]
7 |  |  | 221/12.3 [mA]
8 |  |  | 219/12.8 [mA]
9 |  |  | 206/12.3 [mA]
10 |  |  | 197/12.4 [mA]
11 |  |  | 221/12.1 [mA]
12 |  |  | 207/12.3 [mA]
13 |  |  | 214/12.4 [mA]

## Slide 57: Pod Electronics Results
Requirements Verified |  | Verified By | Details
P6.1 | Pod shall have an environmental sensor package | Inspection | Each pod has an accelerometer and pressure/temperature sensor
P6.3.1.1 | Pod shall transmit ranging data | Software | Each pod was pinged for ranging and responded with 10 measurements when 10 were requested
P6.3.1.2 | Pod shall transmit environmental data | Software | Each pod was pinged for environmental data and responded with all the environmental data present on the SD card
P6.4 | Pod shall have ability to toggle between low power and high power modes | Measurement | Each pod transitioned from high power mode to low power mode
Additional: P6.1.1, P6.1.3, P6.1.4, P6.4.1, P6.4.2 |  | Software | 

## Slide 58: Pod Initial Network Test
Facility: Business Field
Equipment:
  5-6 fully populated pods (some with structure)
  1 rover beacon
  Power (micro USB and batteries)
Procedure:
  Place pods at various locations on the field
  Verify ranging data transmit between rover beacon and pods
  Verify ranging data transmit between pods
  Verify environmental data transmit between rover beacon and pods
Requirements Verified | 
P5.2 | The pods shall communicate data to the rover and amongst themselves
P5.2.1 | Pods shall have localization data transmit capability using DW1000
Additional: | 
Objective: Intermediate test to verify that 5 pods do not interfere with each other
Expected Result: Multiple pods are able to communicate to the rover beacon with no interference issues
Test Scheduled
Test Completed
Data Analyzed
Results Verified
Complete
In Progress
Notes: Need to include status

## Slide 59: Pod Initial Network Test Results
Currently this test has been performed with a laptop and a stationary rover
There were no issues in terms of pods interfering with each other in the stationary tests
There have been teleop issues with the rover so the test still has to be performed with a moving rover
The test can be performed as soon as teleop is working on the rover
Next Step -- Final Network Test
This test requires 11 pod structures
The test is currently scheduled for XX/XX/XXXX pending status of the pod structures
Since there are intermediate tests for this final test we are confident that on the success of the previous tests this one will also be successful

## Slide 60: C. Pod Structure Tests

## Slide 61: Testing Plan
Subsystem
System
Nav. + Electronics | 
Rover/Pod Cmd Test | 3/17
Mission-Length Ctrl | 3/24
Struct. + Electronics | 
Pod Protection Test | 3/24
Cannon + Rover | 
Cannon Interface Test | 3/31
Integration
Full System | 
Safety Demo | 4/7
Mission Sim | 4/14
Cannon | 
Reloading Demo | 3/8
Range Demo | 3/8
Pod Electronics | 
Checkout Test | 2/25
Accuracy Test | 3/1
Mesh Network Test | 3/7
Pod Structure | 
Stability Test | 2/25
Drop Test | 3/1
Navigation | 
MIP Ingest Demo | 2/25
Rover Odometry Ctrl | 3/1
Rover GSLAM Demo | 3/7
Complete
In Progress

## Slide 62: Pod Structure Aero Test

## Slide 63: D. Deployment Tests

## Slide 64: Testing Plan
Subsystem
System
Nav. + Electronics | 
Rover/Pod Cmd Test | 3/17
Mission-Length Ctrl | 3/24
Struct. + Electronics | 
Pod Protection Test | 3/24
Cannon + Rover | 
Cannon Interface Test | 3/31
Integration
Full System | 
Safety Demo | 4/7
Mission Sim | 4/14
Cannon | 
Reloading Demo | 3/8
Range Demo | 3/8
Pod Electronics | 
Checkout Test | 2/25
Accuracy Test | 3/1
Mesh Network Test | 3/7
Pod Structure | 
Stability Test | 2/25
Drop Test | 3/1
Navigation | 
MIP Ingest Demo | 2/25
Rover Odometry Ctrl | 3/1
Rover GSLAM Demo | 3/7
Complete
In Progress

## Slide 65: Reloading Test
Facility: ITLL or Project Depot
Equipment:
  Power supply
  Full assembled reloading system with stepper motor
  At least 5 pods
Procedure:
  Load 5 pods onto timing belt
  Send reload command to turn the stepper motors
  Repeat for all pods
Requirements Verified | 
D3.5 | DM shall be capable of deploying 10 pods within a 20 minute duration
D3.5.1 | DM shall be capable of reloading and deploying a new pod every 2 minutes
P5.1 | Pods are deployable and compatible with DM
Additional: None | 
Objective: Verify reloading capability and funnel design
Test Scheduled
Test Completed
Data Analyzed
Results Verified
Complete
In Progress
Expected Result: Timing belt shown to support all loads, commanding is functional, no jamming in funnel, ideal reloading step count verified
Notes: Need to include status

## Slide 66: Reloading Pretests
Pretests |  | Status
DT3.1 | Turn timing belt | 
DT3.2 | Reload one pod | 2/23
Objective: Verify reloading capability and funnel design
Complete
In Progress
Notes: Need to include status

## Slide 67: Cannon Safety Pretests
Pretests |  | Status
 | Serial command from computer → Arduino to reverse motor direction | 
 | Serial command from computer → Arduino to shut off motor | 
 | Command from kill switch → rover to cut power (no deployment module) | 
 | Command from kill switch → rover to shut off motor (no spring compression) | 
 | Command from kill switch → rover to reverse motor direction (no rack or spring compression) | 
Objective: Verify safety procedure and remote kill switch
Complete
In Progress
Notes: Need to include status

## Slide 68: Cannon Safety Demo

## Slide 69: Manual Spring Safety
If the spring is slightly compressed and not in a fire sequence, the spring can be reversed and stopped using manual commands.

## Slide 70: E. Integration Tests

## Slide 71: Testing Plan
Subsystem
System
Nav. + Electronics | 
Rover/Pod Cmd Test | 3/17
Mission-Length Ctrl | 3/24
Struct. + Electronics | 
Pod Protection Test | 3/24
Cannon + Rover | 
Cannon Interface Test | 3/31
Integration
Full System | 
Safety Demo | 4/7
Mission Sim | 4/14
Cannon | 
Reloading Demo | 3/8
Range Demo | 3/8
Pod Electronics | 
Checkout Test | 2/25
Accuracy Test | 3/1
Mesh Network Test | 3/7
Pod Structure | 
Stability Test | 2/25
Drop Test | 3/1
Navigation | 
MIP Ingest Demo | 2/25
Rover Odometry Ctrl | 3/1
Rover GSLAM Demo | 3/7
Complete
In Progress

## Slide 72: Cannon Integration Test
Facility: Cohirnt/Field
Equipment:
  Rover
  Cannon installed
  Pod
Procedure:
  Send various heading commands
  Check zero-out and heading is accurate
  Send fire command
  Check deployment does not effect vehicle
  Send reload command
  Verify reload is successful, went to corresponding side and turn radius
Requirements Verified | 
Additional: | 
Objective: Verify that the cannon can accept heading/fire commands from the rover
Expected Result: Rover is able to command the deployment mechanism as expected via serial r/w to deployment microcontroller.
Test Scheduled
Test Completed
Data Analyzed
Results Verified
Complete
In Progress
Notes: Need to include status

## Slide 73: Pod Final Network Test
Facility: Business Field
Equipment:
  11 fully populated pods with structure
  1 rover beacon
  Power (micro USB and batteries)
Procedure:
  Place pods at various locations on the field
  Verify ranging data transmit between rover beacon and pods
  Verify ranging data transmit between pods
  Verify environmental data transmit between rover beacon and pods
Requirements Verified | 
P5.2 | The pods shall communicate data to the rover and amongst themselves
P5.2.1 | Pods shall have localization data transmit capability using DW1000
Additional: | 
Objective: Verify that all 11 pods do not interfere with each other and are ready for integration with the navigation team
Expected Result: All pods are able to communicate to the rover beacon with no issues with a full scale test and are ready to be integrated with the navigation team
Test Scheduled
Test Completed
Data Analyzed
Results Verified
Complete
In Progress
Notes: Need to include status

## Slide 74: Overall System Safety Test
Facility: Open flat grass field
Equipment:
  Integrated deployment module w/ electronics
  Completed reloading module w/ electronics
  Completed azimuth module w/ electronics
  Remote kill switch
  10 pod structures w/ appropriate mass
Procedure:
  Perform a vehicle traversal
    using a known and basic path
  Install deployment module and fully load 10 pods
  Perform same path
Objective: Demonstrate safety mechanisms, validate safe operation
Test Scheduled
Test Completed
Data Analyzed
Results Verified
Complete
In Progress
Requirements Verified | 
M4 | 
D4.4 D3.7 D4.1 D4.1.1 D3.6 | 
Additional: | 
Expected Result: Rover can range to pods, Calculate pose, Add new pods to network
Notes: Need to include status

## Slide 75: F: Full Gantt Chart

## Slide 76: Gantt: Software & Electronics

## Slide 77: Gantt: Manufacturing

## Slide 78: Gannt: Assembly & Integration

## Slide 79: Gantt: Deliverables

## Slide 80: G: Team Organization

## Slide 81: Organizational Chart: 09/18 – 02/19
4 Team Members
Progress: On Track
5 Team Members
Progress: Back on Schedule
3 Team Members
Progress: Ahead of Schedule

## Slide 82: Organizational Chart: 03/19 – 05/19
* Pod Electronics Team moves to Deployment Team when their integration tasks are complete
4 Team Members
Progress: On Track
8 Team Members
New team members assist with motors & pod assembly
0 Team Members
PCB Complete
Pod SW Complete