## Slide 1: EMU
Test Readiness Review
Client:
Steve Borenstein
Advisor:
Jean Koster
Project Manager:
Dakota Labine
Endurance Multirotor UAS
Team:
Alejandro Castillo, Becca Rivera, Dakota Labine,
Henry Moore, Libby Hasse, Matthew Lehmann,
Max Alger-Meyer, Michael Flores, Mitchell Spencer
Nathan Castille, Nathan Hetzel, Shawna McGuire
Notes: Dakota 10.45 s

## Slide 2
Overview
Notes: Dakota
1:33 Total

## Slide 3: Project Motivation and Statement
Mission:
The EMU team will design a fully autonomous, 25 lb, multirotor UAS capable of completing long duration flight while supporting a 5 lb payload and streaming video
Motivation:
The IRISS team would benefit from a heavy lift, long duration UAS to expand their mission profiles
Create a chassis capable of being scaled to allow the IRISS team develop mission specific vehicles
Notes: Dakota

## Slide 4: CONOPS
Notes: Michael

## Slide 5: Functional Block Diagram
Notes: Michael

## Slide 6: Critical Project Elements (CPEs)
CPE | Rationale
Chassis | UAS chassis must withstand operational forces, support components, and allow component integration
Drivetrain | Drivetrain must safely transfer power to rotors in a stable configuration
Rotor Assembly | Rotor assembly must provide aerodynamic lift and control over the UAS
Power Plant | Power plant must provide enough power for all flight phases across a two hour hover operation
Flight Software | Flight software must enable UAS communication and manual or autonomous flight control

## Slide 7: Design Recap: Mechanical Systems
Rotors
8 Rotor Blades & Assemblies
Chassis
Carbon Fiber Prop Arms & Hex Tube Supports
Drivetrain
Drive Shaft Supporting Quarter-Turn Belt Drive
Landing Assembly
4 Carbon Fiber Legs & Shock Absorbers
Power Plant
Gas Engine & Centrifugal Clutch

## Slide 8: Project Progress: Requirements
Verified
Verification in Progress
To Be Verified
64 Total Requirements

## Slide 9: Project Progress: Levels of Success
11% Completed
Controls |  |  |  | 
Flight Endurance |  |  |  | 
Power Plant |  |  |  | 
Chassis |  |  |  | 
Autonomy |  |  |  | 
Safety |  |  |  | 
Ground Station |  |  |  | 
Payload |  |  |  | 
27 Total Levels

## Slide 10
Schedule
Notes: Dakota

## Slide 11: Schedule - Full
Notes: Dakota

## Slide 12: Schedule - Manufacturing and Testing
Notes: Dakota

## Slide 13: Schedule - Integration and Testing
Notes: Dakota

## Slide 14
Test Readiness

## Slide 15: Rotor Thrust Testing
Rationale:
  Validate the rotor thrust model to confirm correct blade selection
Equipment:
  Engine Cell
  Strain Sensors
  Photo Tachometer
  Electric Motor
  Servos
Status:
  The testing and data processing has been completed

## Slide 16: Rotor Thrust Testing
Procedure:
  Measure blade pitch and rotor RPM as model inputs
  Compare recorded thrust to model predictions at given inputs
Mitigation:
  Verify our lift predictions to ensure chosen propellers meet flight requirements
Theory:
  Cantilever beam has a linear force/strain relation

## Slide 17: Rotor Thrust Testing
Rotor testing compared to analytical model
One removed outlier
Mean error 4.8%
Max error 17%
Further analysis in progress
Validates analytical model to necessary accuracy
Main error sources: energy lost to vibrations, sticky rotor head pitching.
Notes: Low reynolds number likely cause of outlier
Possible harmonic effects of either test stand or aerodynamics causing periodicity of error
model errs on the low side of data, meaning that thrust is slightly *above* predicted value

## Slide 18: Engine Dyno Testing
Engine Dyno Test Rationale
  Engine Break-in:
    Engine speeds reach up to 20,000 RPM so the dyno is the most practical safe manner to break in the engine
    Other methods (propeller) would be unsafe at these speeds
  Thermal Testing:
    Exact engine operating temperatures are not clear prior to testing
    Thermal testing using a FLIR camera and a laser thermometer will help quantify motor thermals and temperature ranges near the carbon fiber during operation.
  Systems functionality:
    Other systems such as the engine speed regulation, and the emergency ignition-kill system need to be tested prior to installation
  Power Verification:
    Allows for verification of advertised HP and torque at advertised RPM
Notes: Rationale only on this slide

## Slide 19: Engine Dyno Testing
Engine Test Design
  Setup:
    Eddy current dynamometer with custom motor mount and belt tensioner
  Equipment:
    Engine cell, dyno, tachometer, load cell, engine, kill switch, wireless receiver
  Safety:
    Throttle servo is powered by power supply in safe room
    Throttle servo and kill switch are connected to wireless receiver
    Data harness cables routed into safe room for live Dyno control on a PC
Notes: Testing Design only on this slide

## Slide 20: Engine Dyno Testing
  Test Procedure:
  Motor is installed on the dyno test stand within the engine cell, belt is tensioned
  5 minutes of fuel in external tank
  Motor is started and idles. Clutch doesn't engage until 6000 RPM
  Cell is cleared
  Motor throttle controlled from safe room ramps up RPM
  Load on motor increased after clutch engages: torque, RPM, HP recorded live
  Kill switch triggered to end test
DYNO-MAX software window
Theory:
Notes: Equipment needed and Procedures on this slide

## Slide 21: Engine Dyno Testing
  Risk Mitigation:
    Engine break-in will allow the piston ring to sit properly in the cylinder wall and prevent failure during flight
    Thermal verification will ensure engine doesn’t output too much heat for the safe operation of the surrounding equipment or the engine itself
    Endurance testing will allow us to more accurately predict fuel consumption and help with determining the ideal amount of fuel
  Task Status:
    Manufacturing: 70% done
    Assembly: 50% done
Project Risk Mitigation and Task Status
Notes: Project risk mitigation and Task status

## Slide 22: Flight Electronics
Pixhawk Setup
  Radios in sync sending telem/commands
  Here 2 GNSS (GPS system)
  Servos connected and live
  BEC to power servo rail
  Battery to power Pixhawk
  Throttle servo connected and live
  Gimbal connected
Ground Station
  HITL mode in Mission Planner
  GPS location live
  Test commands to servos
  Set waypoints
Notes: I’ll be getting a full image of everything we have electronics wise tomorrow (2/26) including a picture of the GS while the GPS is reading live

## Slide 24: Quadcopter Hardware & Electronics Integration
HITL Demonstration 1 - No engine, no rotor blades spinning
  Rationale: Verify the effectiveness of flight software to appropriately control copter components in response to transmitted commands
  Test Equipment:
    GCS
    Flight electronics (PixHawk) on-board with appropriate firmware
    Servos connected to rotor blades with PWM cables to PixHawk
  Procedure:
    Power all electronics and verify they respond to:
      GCS commands
      Changes in orientation/position
    Check gimbal control and verify live video feed from payload
    Check loss of connection and other safety commands from pixhawk

## Slide 25: Quadcopter Hardware & Electronics Integration
HITL Demonstration 2 - Engine running, no engagement with drivetrain
  Rationale: Verify ability of flight software to function and control appropriately with the added vibrations/disturbances of the running engine
  Test Equipment:
    HITL 1 equipment assembled on the chassis
    Engine on chassis
  Procedure:
    Same fundamental checks and procedures as HITL 1
    Check GS ability to send kill command to engine shutdown
    Monitor telemetry from PixHawk with motor vibrations
    Monitor for any communication interferences between GCS and PixHawk
  Safety Risks: The UAS chassis disjointing or coming loose from vibrations
  Mitigation: Loctite and appropriate fasteners in place

## Slide 26: Quadcopter Hardware & Electronics Integration
HITL Demonstration 3 - Engine running, drivetrain delivering power, anchored
  Rationale: Verify ability of flight software to function and control appropriately with the added vibrations/disturbances of engine, drivetrain, and rotors
    Ensure rotors are spinning up securely
  Test Equipment:
    HITL 2 chassis assembly with functioning drivetrain
    Anchors to lock the entire aircraft down to ensure no lift is generated
  Procedure:
    Same fundamental checks and procedures as HITL 2
    Monitor belt integrity/performance
    Confirm functional operation of kill switch by cutting engine power from GS
    Confirm servo functionality by pointing servos to zero AoA

## Slide 27: Quadcopter Hardware & Electronics Integration
HITL Demonstration 3 (cont.) - Engine running, drivetrain delivering power, anchored
  Safety Risks: Flight of UAS, shearing of rotor blades, loss of communications
  Mitigation:
    Secure UAS to anchor with no slack
    Motor will be limited 7200 rpm
    Zero AoA of rotor blades ±5° AoA to keep lift minimal
    Keep the total power supply in the safe room for easy emergency kill
    Test crew will be a safe distance away from UAS in safe room

## Slide 28
Budget
Notes: Dakota

## Slide 29: Cost Plan
Expense | Cost
Copter Parts | $3,838.73
Spare Parts | $709.10
Operational Expenses | $95.00
Left to Buy | $50.00
Total | $4,692.83
Remainder | $307.17
Notes: Dakota

## Slide 30: Major Procurements
System | Acquired | Need | Need Cost
Powerplant | All Parts | None | $0
Drivetrain | Driveshaft, Pulleys, Bearings. | Belts | $50
Rotorhead | All Parts | None | $0
Electronics | All Parts | None | $0
Payload | All Parts | None | $0
Chassis | All Parts | None | $0
Operational | 2-Stroke Oil, Servo Programmer | Fuel | $50
Notes: Dakota

## Slide 31: Closing Slide
Thank You