## Slide 1: FlOWeR FlOWeR
Presenters: Adriana Lysak, Weston Luke, Preston Tee, Eric Tate, Max Buchholz
Additional Team Members: Anand Kappagantu, Angelo Hristopoulos, Anthony Gregg,
Nathan Portman
Advisor: Alexandra Le Moine
Customer: U.S. Air Force Research Laboratory
Flow Optimization & Weight Reduction Project
Critical Design Review

## Slide 2: Project Overview
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 3: Purpose Objectives
Successfully compete in AFRL’s annual Aerospace Propulsion Outreach Program (APOP) competition
Improve performance of JetCat P100-RX hobbyist jet engine
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Increase T/W ratio
Maintain or increase thermal, propulsive efficiencies
Maintain or decrease thrust specific fuel consumption (TSFC)
Create a thermodynamic model of the engine

## Slide 4: Concept of Operations (CONOPs): Competition
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Notes: Colin: Add stage numbers at each part of the conops
Animate to have one engine pop up at a time

## Slide 5: Design Solution
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Notes: Dont justify or explain changes just say what were doing

## Slide 6: Our Solution: Ejector Nozzle
Objective: Maximize exit flow velocity by optimizing area ratio while avoiding shocks and flow separation
Purpose: Increase thrust through increase of exhaust momentum
Considerations:
  Mass flow rate increase vs exit velocity decrease
  Weight penalty for larger ejector
  Optimizing converging nozzle
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Notes: Discuss in detail the picture shown, add labels
Add another slide with general ejector nozzle details
Change title. “Actual” solution doesn’t look good

## Slide 7: Ejector Nozzle: Overview
Exhaust gasses from engine turbine exit through converging nozzle
Mass flow out of converging nozzle entrains mass flow from surrounding air and is forced out the back of the ejector nozzle
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Primary mass flow (from engine)
Secondary mass flow (from surrounding air)
Combined mass flow
Notes: Discuss in detail the picture shown, add labels
Add another slide with general ejector nozzle details
Change title. “Actual” solution doesn’t look good
Animations:
Red arrows to blue and yellow
Change arrow sizes

## Slide 8: Ejector Nozzle: Performance
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Models show thrust to increase 82 newtons over the stock nozzle (182 newtons total)
Weight of ejector nozzle will increase by 91 grams over stock nozzle (1171 grams total)
Overall this leads to a predicted thrust to weight increase of 67.8%
Primary mass flow (from engine)
Secondary mass flow (from surrounding air)
Combined mass flow
Notes: Discuss in detail the picture shown, add labels
Add another slide with general ejector nozzle details
Change title. “Actual” solution doesn’t look good
Animations:
Red arrows to blue and yellow
Change arrow sizes

## Slide 9: Orthographic Drawing: Integration
Units in mm
Notes: Discuss in detail the picture shown, add labels
Add another slide with general ejector nozzle details
Change title. “Actual” solution doesn’t look good

## Slide 10: Orthographic Drawing: Ejector Nozzle
Units in mm
Notes: Discuss in detail the picture shown, add labels
Add another slide with general ejector nozzle details
Change title. “Actual” solution doesn’t look good

## Slide 11: Model Design for Stock Engine
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Derived from Brayton Cycle with isentropic stage efficiencies and variable specific heats included
Variable Cp and specific heat ratios through combustion chamber

## Slide 12: Operational Functional Block Diagram
Previous Project
Previous Project
Notes: Colin: Increase font size
Add box with what is the scope of our project

## Slide 13: Critical Project Elements (CPEs)
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 14: CPEs
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Label | Critical Feasibility Element | FR
T/W | The T/W ratio of the engine shall increase and the TSFC shall decrease or remain constant. | 1,2
MODEL | Model accurately simulates thermodynamic properties of the engine, predicting increases in thrust and/or decreases in TSFC. | 3
INT-TEMP | All components can withstand temperatures throughout their section and can integrate with each other seamlessly. | 4
TEST | External sensors are integrated to augment engine’s internal sensors and gather necessary temperature and pressure data, and an off-engine testing setup is developed to validate nozzle design. | 4

## Slide 15: Design Requirements & Satisfaction
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Notes: Colin: reference design requirements

## Slide 16: Key Design Requirements
Overview
Design Solution
Requirement Satisfaction
Risks
Verification & Validation
Planning
CPE | Related Design Requirement | Satisfied?
T/W | DR 1.1: Design a T/W-improving modification that increases thrust and/or decreases weight which does not trigger the fail-safes that shut the engine down. | 
MODEL | DR 3.1: A thermodynamic model is developed which predicts baseline and modified engine performance. | 
INT-TEMP | DR 2.4: The engine's weight increases by less than 25% or decreases. | 
TEST | DR 4.2: A method of testing modifications external to the engine is developed. | 
CPEs
Requirement Satisfaction

## Slide 17: Chosen Ejector Nozzle Model
Using J.W. Heiser’s two-density, incompressible, inviscid thrust augmentation formulation
Accounts for different densities of the two streams of air entering the ejector and their mixing
Note: φ is multiplication factor for nozzle’s thrust
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Notes: Colin: increase plot label size
Change plot to T/W increase in comparison to STOCK nozzle, not improved conv nozzle
Explain why we didn’t pick bigger alpha E
Alpha e = 3.5, alpha D = 1.5, Phi = 1.45

## Slide 18: Design Point Selection
Accounting for:
Improved converging nozzle
Ejector thrust augmentation
Estimate of weight
The mixing chamber length = 4 times its diameter
Minimizes friction losses, but is expected to result in incomplete mixing
Diffuser size is a trade off between length and area ratio
Minimize weight without flow separation
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Notes: Slide 128 for model comparison

## Slide 19: Ejector Nozzle Predicted Performance
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
 | Thrust [N] | Total Weight [g] | Thrust-to-Weight [N/g] | Thrust-to-Weight Increase [%]
Stock Nozzle | 100 | 1080 | 0.0926 | N/A
Improved Converging Nozzle | 126 | 1094 | 0.1152 | 24.4
Improved Nozzle with Ejector | 182 | 1171 | 0.1554 | 67.8
Notes: These are exact weights now

## Slide 20: Key Design Requirements
Overview
Design Solution
Requirement Satisfaction
Risks
Verification & Validation
Planning
CPE | Related Design Requirement | Satisfied?
T/W | DR 1.1: Design a T/W-improving modification that increases thrust and/or decreases weight which does not trigger the fail-safes that shut the engine down. | ✔
MODEL | DR 3.1: A thermodynamic model is developed which predicts baseline and modified engine performance | 
INT-TEMP | DR 2.4: The engine's weight increases by less than 25% or decreases. | 
TEST | DR 4.2: A method of testing modifications external to the engine, is developed. | 
CPEs
Requirement Satisfaction

## Slide 21
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Thermodynamic Model
Derived from Brayton Cycle with isentropic stage efficiencies and variable specific heats included
The model is not isentropic through any part of the engine
  Current isentropic efficiencies are estimated from literature
  Efficiencies specific to the P100-RX are pending engine repairs
Cp and γ vary only through the combustion chamber
The mass flow rate of fuel and the change in composition of the gasses in the engine due to combustion products are accounted for
Notes: Assumptions currently using:
Subsonic Engine -- exit pressure is equal to atmospheric pressure
Inlet mach is 0

## Slide 22: Thermodynamic Properties Through Stock Engine
Overview
Design Solution
CPEs
Risks
Verification & Validation
Planning
Requirement Satisfaction
Notes: Colin: bigger font size again
Mention trends, why the plots make sense

## Slide 23
Thermodynamic Model and On-Engine Testing
Temperature values inside combustor are difficult to measure safely
  AFRL will send temperature at stations 3 and 4, can be used to calculate combustor efficiency
Remaining efficiencies: on-engine testing
  Compressor, turbine, and nozzle efficiencies will be calculated from temperature measurements between each of the stations
  To be completed upon return of engine from service
  Temporary solution: SPECS (2018-2019) team efficiencies
Overview
Design Solution
CPEs
Risks
Verification & Validation
Planning
Requirement Satisfaction
Notes: Dont forget that the engine is broke!

## Slide 24: Key Design Requirements
CPE | Related Design Requirement | Satisfied?
T/W | DR 1.1: Design a T/W-improving modification that increases thrust and/or decreases weight which does not trigger the fail-safes that shut the engine down. | ✔
MODEL | DR 3.1: A thermodynamic model is developed which predicts baseline and modified engine performance | ✔
INT-TEMP | DR 2.4: The engine's weight increases by less than 25% or decreases. | 
TEST | DR 4.2: A method of testing modifications external to the engine, is developed. | 
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 25: Converging Nozzle Material Selection
Material Choice: Stainless Steel 304
Expected Max Operating Temperature: 873 K
Yield Strength at 873 K: 4.4×10⁸ Pa
Maximum Equivalent Stress: 1.85×10⁸ Pa
Minimum Factor of Safety: 1.58
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Notes: This model contains thermal stresses and also stresses from joints

## Slide 26: Mixing Chamber Material Selection
Material Choice: Aluminum 6061
Expected Max Operating Temperature: 473 K
Yield Strength at 473 K: 1.59×10⁸ Pa
Maximum Equivalent Stress: 5×10⁷ Pa
Minimum Factor of Safety: 3.18
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 27: Manufacturing & Integration Plan
Converging nozzle (green) - metal 3D printed stainless steel 304 via Direct Metal Laser Sintering (DMLS)
Mixing chamber and diffuser (blue) - thin aluminum 6061 sheets on a roller and spot or tig welded together
Connecting struts (red) - DMLS printed with nozzle, stainless steel 304
Holes will be drilled in outer struts so bolts can attach the mixing chamber/diffuser to converging nozzle
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 28: Estimated Component Weights
Component | Volume [cm3] | Material | Density [g/cm³] | Weight [g] | Total Engine Weight Increase [%]
Improved Converging Nozzle | 9.21 | Stainless Steel 304 | 7.92 | 72.9 | 1.31
Mixing Chamber and Diffuser | 20.5 | Aluminum 6061 | 2.71 | 55.6 | 5.15
Interface struts | 2.68 | Stainless Steel 304 | 7.92 | 21.2 | 2.00
Total | - | - | - | 149.7 | 13.9
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Notes: Based directly on solidworks model. Can look into using just 3 interface struts if necessary to reduce weight

## Slide 29: Key Design Requirements
CPE | Related Design Requirement | Satisfied?
T/W | DR 1.1: Design a T/W-improving modification that increases thrust and/or decreases weight which does not trigger the fail-safes that shut the engine down. | ✔
MODEL | DR 3.1: A thermodynamic model is developed which predicts baseline and modified engine performance | ✔
INT-TEMP | DR 2.4: The engine's weight increases by less than 25% or decreases. | ✔
TEST | DR 4.2: A method of testing modifications external to the engine, is developed. | 
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 30: Cold Test Purpose
Test is designed to replicate turbine exit Mach, pressure
Exhaust temperature conditions will not be reproduced
Test nozzle material: 3D-printed ABS (Acrylonitrile Butadiene Styrene)
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 31: Cold Test Setup
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Notes: Go through this quickly, Eric will be adding more detail later in the presentation

## Slide 32: Key Design Requirements
CPE | Related Design Requirement | Satisfied?
T/W | DR 1.1: Design a T/W-improving modification that increases thrust and/or decreases weight which does not trigger the fail-safes that shut the engine down. | ✔
MODEL | DR 3.1: A thermodynamic model is developed which predicts baseline and modified engine performance | ✔
INT-TEMP | DR 2.4: The engine's weight increases by less than 25% or decreases. | ✔
TEST | DR 4.2: A method of testing modifications external to the engine, is developed. | ✔
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 33: Risks
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 34: Identified Hazards
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
 | 1 - Minimal | 2 - Minor | 3 - Noticeable | 4 - Major | 5 - Catastrophic
5 - Almost certain |  |  |  |  | 
4 - Likely |  | 1 |  |  | 1
3 - Possible |  |  | 3 | 3 | 
2 - Unlikely |  |  | 1 | 2 | 1
1 - Rare |  | 1 | 1 |  | 3
Acceptable
Acceptable with mitigation
Unacceptable

## Slide 35: Risk Mitigation: Safety
Engine damage
  No modifications to the internal parts of the engine
  No test equipment in direct contact with the engine during tests
  Essential personnel will be present for all engine tests
Test equipment damage
  Phased approach slowly work up to max conditions
  Ensurer test equipment has a large factor of safety
Human safety
  All on and off engine test will be performed in the test cell (AERO 169A)
  Non-essential personnel will be located outside of the test cell (AERO 169)
  Essential personnel will operate equipment from a distance behind a protective shield
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 36: Risk Mitigation: Project Success
Predicted/real-world value discrepancies
  Consulting with faculty to ensure fidelity of models
  Design will be an iterative approach allowing for error removal
Manufacturing difficulties
  Consulting with faculty to ensure manufacturability of proposed design
  Performing structural analysis (FEA) to ensure functionality
Work distribution/scheduling conflict
  Keeping in close contact to ensure that everyone is updated
  Making sure multiple people can complete each task
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 37: Updated Risk Matrix
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
 | 1 - Minimal | 2 - Minor | 3 - Noticeable | 4 - Major | 5 - Catastrophic
5 - Almost certain |  |  |  |  | 
4 - Likely |  | 1 |  |  | 
3 - Possible |  |  | 3 |  | 
2 - Unlikely |  |  | 3 | 4 | 
1 - Rare |  | 1 | 1 | 2 | 2
Acceptable
Acceptable with mitigation
Unacceptable

## Slide 38: Verification & Validation
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Notes: Colin: Tie everything back into design requirements
Colin: Emphasize which tests are most important to reach design requirements
Colin: Final validation inclusion, i.e. full system tests - this is likely in planning section, mention it

## Slide 39: Project Flow Chart
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Notes: Maybe edit some of these bubbles -- come back and check. Focus on iteration and why tests being done

## Slide 40: On-Engine Test: Data Acquisition
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Measurement Device | Quantity of Interest
Static test stand | Thrust
Jet-tronics software, onboard sensors | RPM, exhaust gas temperature, fuel consumption
Additional sensors on test stand | Nozzle exit static and total pressures; nozzle inlet, exit, and surface temperature; cowling surface temperature
Given by AFRL | Combustion chamber temperature
Notes: Emphasize thrust stand test setup was used previously, but we have our own analysis that we’ve performed at this point

## Slide 41: On-Engine Test Design
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Pitot probes with pressure transducers at nozzle exit and engine inlet
USC pitot-static probe at nozzle exit with attached type K thermocouple
Type E/K thermocouples used to determine cowling temperature
Data Capture Sensors:
  USC Reverse Pitot-Static Probe with Type K Thermocouple
  Honeywell MLH100P Pressure Transducers
  McMaster-Carr Bendable Type K Thermocouples
  Arduino Mega
    Micro SD Card for data storage
Notes: Central picture of test stand, smaller pictures of each sensor around outside, lines/arrows pointing to where it goes

## Slide 42: On-Engine Test: Electronics FBD

## Slide 43: Thermodynamic Model Verification
Using data from on-engine testing to improve model
  Compare theoretical values to actual engine temperature and pressure data
Calculate the efficiencies of each engine station
  Use first law of thermodynamics and temperature losses through each engine station
Incorporate the calculated efficiencies into the model
  Currently using AFRL 2018-19 SPECS Project efficiencies - P90-RXi Engine
Helps satisfy DR1.1 (T/W Improvement Modification)
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Notes: Like preston touched on, take data, feed to model, calc efficiency

## Slide 44: Nozzle Cold Test Design
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Designed to replicate flow Mach number entering nozzle
Will manufacture intermediate iterations of nozzle out of ABS plastic
Two tanks and pressure regulators necessary to ensure adequate mass flow into settling chamber
  11.69 second nominal test time
Notes: State where we got it (2016-2017 SABRE Team)
State WHY we’re iterating nozzle design

## Slide 45: Nozzle Cold Test Design
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Feed tanks opened by electronic ball valves
Flow out of settling chamber controlled by manual ball valve pulley system
Supply tanks rated for 200 psi
  Maximum supply from building is 110 psi
Settling chamber minimum FOS = 138

## Slide 46: Cold Test Design - Test Setup
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 48: Nozzle Cold Test Design
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Honeywell MLH100P Pressure Transducer
Kulite HKL-M Pressure Transducer
Parker 53R Pressure Regulator
Electronic Ball Valve
Notes: smaller pictures/text boxes labeling what goes where

## Slide 49: Cold Test Verification
Honeywell MLH100P pressure transducer will measure pressure inside settling chamber
Kulite HKL-M pressure transducer with integrated thermocouple will be placed at test nozzle exit to record temperature and pressure
Use recorded pressures and isentropic relations to determine exit flow velocity
  Compare with stock nozzle to characterize any thrust improvements
Helps satisfy DR 1.1 (T/W Improvement Modification) and DR 4.2 (Off-Engine Testing Methods)
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 50: Project Planning
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 51: Work Breakdown
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Test
Deliverables
Materials
Manufacturing & Integration
Model
PDD
CDD
PDR
CDR
FFR
TRR
SFR
PFR
SDS
AIAA
Cold test material
Final material
Stress, Strain, & Fatigue Analyses
Stock engine data
On-engine test setup
Cold test setup
Nozzle: on-engine
Nozzle: cold test
Cold test nozzle
Design ejector attachment
Test final nozzle on engine
Complete
Ongoing
Upcoming
Legend
Brayton Cycle
Eliminate assumptions
Calculate efficiencies
Finalize robust model

## Slide 52: Work Plan
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Notes: Colin: red line of today.
Zoomed in view of immediate future - first couple weeks of next semester potentially

## Slide 53: Manufacturing & Off-Engine Test Plan
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 54: Spring Semester Tests
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Test | Purpose | Facility | Equipment | Week
Test engine | Determine stock properties | AERO 169A | Thrust test stand | 10-Jan
Scaled stock nozzle | Baseline for FlOWeR converging nozzle | AERO 169A | SABRE-Nozzle cold test setup | 17-Jan
Scaled FlOWeR converging nozzle | Compare to stock nozzle, get thrust increase without ejector | AERO 169A | SABRE-Nozzle cold test setup | 24-Jan
Scaled FlOWeR ejector nozzle | Compare to stock nozzle, calculate T/W increase for FlOWeR nozzle | AERO 169A | SABRE-Nozzle cold test setup | 7-Feb
On-engine FlOWeR nozzle test | Measure actual T/W increase from FlOWeR nozzle | AERO 169A | Thrust test stand | 28-Mar

## Slide 55
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 56
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 57: Cost Plan
Engine is out for service with an expected cost between $250 and $750
Al6061 Sheet Stock:
  Necessary dimensions: 395.8mm x 338.6mm x 1mm (15.583” x 13.331” x .039”)
  Grainger: $16.94 for 18” x 18” x .04”
  Midwest Steel Supply: $36.10 for 18” x 18” x .04”
In-house DMLS is expected to cost ~$650 for necessary gases
  SS304: $100/kg
Outsourced Nozzle costs here
  Minimum order costs for forging/casting and machining range from $300 to $500
  DMLS nozzle quotes have been requested and are under review
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning

## Slide 58: Acknowledgements
AFRL: Lt Kavi Muraleetharan, Lt Collin Parsons, and Mr. Tim Erdmann
Advisor: Alexandra Le Moine
TAs: Emma Markovich and Colin Claytor
Technical Advisors: John Mah, James Nabity, Matt Rhode, Bobby Hodgkinson, Trudy Schwartz, Kathryn Wingate

## Slide 59: References
Mattingly, J.D. and Boyer, K.M. Elements of Propulsion: Gas Turbines and Rockets. American Institute of Aeronautics and Astronautics, 2 edition, 2016
Huang, K.P, Kisielowski, E. “An investigation of the thrust augmentation characteristics of jet ejectors,” April 1967.
Frank, G., Piper, S., Chen, Y., FitzRandolph, P., Camacho, C., Knickerbocker, M., Junker, M., Oropeza, D.C., Cutler, J., Fuernkranz, M., and Harthan, D. Specialized propulsion engine control system critical design review, 2018.
Coulon, T., Johnson, R., Jones, L., Mines, M., Schumacher, G., and Swart, C. Thrust to weight improvement of jetcat p100-rx turbojet engine, 2019
Soars, C. Gas Turbines: A Handbook of Air, Land and Sea Applications. Butterworth-Heinemann, 1 edition, 2014.
Violett, B. A few reminders for safe turbine operations.
White, F.M. Viscous Fluid Flow. McGraw-Hill, 3 edition, 2011
Heiser, H. W. Ejector thrust augmentation. Journal of Propulsion and Power, 26(6), November-December 2010.
Huang, K. P and Kisielowski, E. An investigation of the thrust augmentation characteristics of jet ejectors
JetCat. Jetcat turbine datasheet, 2015
Razak, A.M.Y. Gas turbine combustion.
Aeronautics Guide. Aircraft turbine engine fuel system components
Erickson, D.M., Day, S.A., and Doyle, R. Design considerations for heated gas fuel.
Larson, G.C. The hotter the better.
Autonomous Manufacturing. A guide to 3d printing with titanium
Online Metals, URL: https://www.onlinemetals.com/en/buy/aluminum-round-bar-7075-t6-t651-cold-finish?q=%3Aprice-asc&page=1&pagesize=25&sort=price-asc
FATHOM Advanced Manufacturing
Protolabs Manufacturing
Forecast 3D Manufacturing
SpecMaster, Inc.
Dynamic Design & Manufacturing, Inc.
SS Grade 316 / 316 L Technical Data. Action Stainless Steel KwaZulu Natal, URL: Grade 316 Stainless Steel Technical Data (askzn.co.za)
Dr. D. Lewis Abata, The Thermodynamics of Emptying a Pressure Vessel, South Dakota School of Mines and Technology.
Gibson, P. W., “Blast Overpressure and Survivability Calculations For Various Sizes of Explosive Charges”, Army Natick Research Development and Engineering Center MA, June 1994.

## Slide 60: Supplemental Material

## Slide 61: Table of Contents
PDR Material
On-Engine Testing
Real Turbojet Thermodynamic Model
Material Selection
Risk Mitigation
Ejector Design
Notes: Variable geometry ruled out due to static conditions during testing
Nozzle weight is a small % of engine weight

## Slide 62: Design Requirements
DR | Design Requirement | FR
1.1 | Design a T/W-improving modification that increases thrust and/or decreases weight which does not trigger the fail-safes that shut the engine down. | 1
2.1 | The engine’s TSFC increases by less than 5% of its nominal value or decreases by any amount | 2
2.2 | The engine’s propulsive efficiency decreases by less than 5% of its nominal value or increases by any amount | 2
2.3 | The engine’s thermal efficiency decreases by less than 5% of its nominal value or increases by any amount | 2
2.4 | The engine’s weight increases by less than 10% or decreases, unless an after-burner is implemented on the engine, in which case engine weight increases will be less than 30% | 2
2.5 | The cost of modifications is within the budget. Up to $5,000 may be spent on modifications to the engine and will be automatically provided to the group, while up to$14,000 may be used to fund project expenses not directly used for modification design and manufacturing | 2
TOC
Notes: Variable geometry ruled out due to static conditions during testing
Nozzle weight is a small % of engine weight

## Slide 63: Design Requirements, cont.
DR | Design Requirement | FR
2.6 | The fuel flow rate does not increase significantly; ideally, it decreases while maintaining engine performance | 2
2.7 | The engine’s max thrust decreases by less than 5%, or increases | 2
3.1 | A thermodynamic model based on the ideal Brayton cycle is developed and predicts baseline engine performance | 3
4.1 | The team’s engine test lead and an instructor or graduate student experienced with operating the P100-RX engine are present at all hands-on test events. | 4
4.2 | A method of testing modifications external to the engine, dependent on the type(s) of modification(s) designed, is developed | 4
TOC
Notes: Variable geometry ruled out due to static conditions during testing
Nozzle weight is a small % of engine weight

## Slide 64: Trade Study Matrices
TOC

## Slide 65: First Round of Trade Study
TOC

## Slide 66: Second Round of Trade Study
TOC

## Slide 67: Nozzle Trade Study
Criteria | 1 | 2 | 3 | 4 | 5
Thrust (45%) | Decrease in thrust | Little to no thrust improvement | Moderate increase in thrust | Significant increase in thrust within bounds of previous accomplishments | Significant increase in thrust that exceeds previous accomplishments
Weight of Nozzle (5%) | Significant Increase in weight | Small Increase in weight | No effect on weight | Small decrease in weight | Significant Decrease in weight
Modeling Complexity (20%) | Unable to model with desired accuracy | Able to model with desired accuracy with significant time and resources | Able to model with desired accuracy with moderate time and resources | Able to model with desired accuracy with little time and resources | Model requires little overall work to achieve desired accuracy
Likelihood of Success (30%) | Performance is highly sensitive to external parameters and meeting expected performance is highly unlikely | Performance is moderately sensitive to external parameters and meeting expected performance is unlikely | Performance is slightly sensitive to external parameters and meeting expected performance is likely | Performance is not sensitive to external parameters and meeting expected performance is likely | Performance is not sensitive to external parameters and meeting expected performance is likely. Design also includes contingencies
TOC
Notes: All will have similar levels of manufacturing difficulty, depending on material chosen
CD nozzle depends highly on external factors

## Slide 68: Nozzle Trade Study
 | Converging | Fixed Converging-Diverging | Ejector
Thrust (45%) | 4 | 4 | 5
Weight of Nozzle (5%) | 4 | 2 | 2
Modeling Complexity (20%) | 4 | 3 | 2
Likelihood of Success (30%) | 4 | 2 | 5
Total | 4 | 3.1 | 4.25
TOC
Notes: Variable geometry ruled out due to static conditions during testing
Nozzle weight is a small % of engine weight

## Slide 69: CAD model of stock nozzle
Inlet area = 15.6687cm^2
Exit area = 17.2021cm^2
TOC

## Slide 70: CAD model of stock nozzle 2
Inlet area = 15.6687cm^2
Exit area = 17.2021cm^2
TOC

## Slide 71: Stock Render 1
TOC

## Slide 72: Stock Render 2
TOC

## Slide 73: Material Replacement
Thermal Stresses
  Maximum temperature reached is approximately 1100 K in combustor
  Tf = 1100K and Ti = 293K
𝜎 = E𝛼(Tf - Ti )
Alloy | Elastic Modulus (GPa) | Yield Strength (MPa) | Tensile Strength (Mpa) | Density (g/cm3) | Thermal Expansion Coefficient (K-1) | Thermal Stress (GPa)
Stainless Steel | 180 | 860 | 502 | 8.0 | 1.73e-5a | 2.51
Al 6061 | 69 | 35 | 42 | 2.7 | 2.34e-5 | 1.30
Al 2024 | 72.4 | 42 | 64 | 2.78 | 2.32e-5 | 1.36
Al 7075 | 71 | 70 | 78 | 2.81 | 2.36e-5 | 1.35
TOC
Notes: Explicitly state which part has listed initial, final temps
material sourcing:
Stainless steel, aluminum:
grainger has aluminum rod stock, hollow rod stock, bar stock, plate stock, 3-14 days shipping upon order placement (better sourcing and reliability)
industrial metal supply also has current stock, can do custom cuts, 4-12 days for standard orders
Titanium:
tmstitaniun focuses on titanium bar, solid rod, hollow rod, etc., 4-12 days
titanium supply co is also an option

## Slide 74: Material Properties
Material | Density (g/cm3) | Melting Point (K) | Cost (/kg)
Stainless Steel 304 | 8.00 | 1678-1728 | $18
Stainless Steel 316 | 7.99 | 1643-1672 | $23
Stainless Steel 410 | 7.80 | 1753-1803 | $25
Aluminum 7075-T6 | 2.81 | 750 - 908 | $58
Aluminum 6061-T6 | 2.70 | 850 - 925 | $28
Aluminum 2024-T4 | 2.78 | 775 - 911 | $45
Titanium Ti-6Al-4V | 4.43 | 1877 - 1933 | $50
Titanium Ti 3Al 2.5 | 4.48 | 1973 | $103
TOC
Notes: Need to put nozzle weight considerations somewhere
More generic than specific alloys
Measure cowling again (more accurately, graduated cylinders)
Not sure water displacement volume is necessary on this slide

## Slide 75: T-S Diagram of Jet Engines
TOC

## Slide 76: OET: Pressure Regulator and Tank Feasibility
Dimensions
  Feed Tanks (2x)
    1-¼” outlet
  Feed Ball Valves (2x)
    1-¼” inlet, outlet
  53R Feed Regulators (2x)
    1-¼” inlet, outlet
  Settling Chamber:
    1-¼” inlet (2x)
    Outlet: Apollo 94A-109-01 full port brass ball valves
      2.520” ID
  Taper Cone:
    1.8” inlet
    1.075” outlet
TOC

## Slide 77: OET: Desired Settling Chamber Pressure
Content
TOC

## Slide 78: OET: Settling Chamber Structural Analysis
TOC

## Slide 79: OET: Pressure Regulator and Tank Feasibility
Isentropic relations were used to calculate the mass flow rate out of the settling chamber
Mass flow rate out of the feed tanks was calculated using non-ideal relations with both choked and unchoked flow, following conservation laws
The pressure, temperature, mass, and mass flow within each tank was calculated and plotted in an to determine nominal test time
  While feed tank pressures remain high, nominal test time is 11.69 seconds due to the combined feed tank mass flow rate dropping below the mass flow rate out of the settling chamber
  This will reduce pressures in the settling chamber, decreasing nozzle test efficacy
  Note this test time and the mass flow plotted on slide 72 is for two regulators---one regulator system can not keep up with the mass flow out of the settling chamber due to the choked flow in the feed pipe
TOC

## Slide 80: Mass Flow (Settling Chamber)
R = 8.3145 Pa-m3/K-mol = 286.5 J/kg-K
P2 = 131.84 kPa
P10 = 145.34 kPa
𝜌2 = 1.5931 kg/m3
MWair = 28.97 g/mol
a2 = 331.78 m/s
u2 = 93.88 m/s
V̇ = .0743 m2/s
ṁ = .1184 kg/s
TOC

## Slide 81: Mass Flow (Feed Tanks)
Known values:
  P0 = 758.42 kPa = 110 psi
  Pthroat = Psettle = 148.34 kPa
  Vtank = 80 gal. = .3636 m3
  T0 = T = 293.15 K
  R = 287 J/kg-K = 8.3145 Pa-m3/K-mol
  Athroat = 1.227 in2 = 7.9173x10-4 m2
  mmax = 3.2780 kg
TOC

## Slide 82: Mass Flow (Feed Tanks)
Choked Flow:
Non-Choked Flow:
Flow out of the feed tanks is initially choked due to small pipe diameter---this restricts mass flow rate from a single tank to relatively low values
TOC

## Slide 83: Mass Flow (Feed Tanks)
Calculations are derived from the first law of thermodynamics
  The second equation is the driving temperature calculations, as seen in the bottom right
  Iterative models were used to determine the next mass value, allowing for pressure and temperature calculations
TOC

## Slide 84: Mass Flow (Feed Tanks)
Maximum test time: 11.69 seconds
  Pressure remains high, but mass flow rate out of feed tank drops below mass flow rate out of settling chamber
TOC

## Slide 85: Cold Test Risk Mitigation
Vsettling = .032175925 cubic meters
Vfeed = .3636 cubic meters
Psettling= 148.34 kPa
Pfeed = 758.42 kPa
Pa = 86 kPa
W=P0V0(ln(P0/Pa)-1)+PaV0
1kg TNT = 4.184*10^6 J
Wsettle = 596 J
  TNT EQ: 1.42 g
Wfeed = 355,800 J
  TNT EQ: 85.04 g
The blast and resulting pressures would not cause any physical damage given our test setup [17]
TOC

## Slide 86: Assumptions for Ideal Model
Cp and 𝛾 are Constant
  Due to the amount of fuel being used compared to air is really small, the specific heat and 𝛾 values change very little
  EQL software has 𝛾 changing from 1.4 to 1.379
Isentropic through the compressor, turbine, and nozzle
  Assumes that there is not heat loss, which due to high efficiencies of stations generally, means that there are very little losses 𝛾𝛾
Constant Pressure in combustor
  Pressure losses in actual combustor are really small, so assuming constant pressure
Adiabatic
  If all components(minus combustor) are assumed to be adiabatic
100% Efficiency
  Ignores loses that would occur due to friction, heat transfer, etc. Most station efficiency are around 80-90% so little impact will be made on model.
Subsonic Jet Engine
  Due to the absence of shocks and expansion waves, the exhaust gas will be perfectly expanded and the pressure equal to the atmospheric pressure
TOC

## Slide 87: Baseline Model Calculations - Compressor
Use free stream, sea level, and room conditions to find temperature and pressure changes in compressor
  Constant Total Pressure and Temperature
  Pressure Ratio of Compressor
  Isentropic Assumption
TOC

## Slide 88: Baseline Model Calculations - Combustor
Use compressor exit temperature and pressure values to find change in temperature and pressure in the combustor
  Constant Pressure
  Constant Specific Heat
  EQL to find enthalpy change
    Find temperature change based off of first law of thermodynamics
TOC

## Slide 89: Baseline Model Calculations - Turbine
Use nozzle inlet and combustor exit conditions to find pressure and temperature changes and
  Isentropic
  Constant Total Pressure and Temperature
  Temperature entrance from combustor
TOC

## Slide 90: Baseline Model Calculations -Nozzle
Use given engine data from JetCat to find mach, temp, and pressure changes through the nozzle
  Isentropic Assumptions
    No change in Entropy
      No friction losses
      Adiabatic
  Constant Total Pressure and Temperature
  Area-Mach Relation
TOC

## Slide 91: EQL Software
EQL is a NASA developed software that gives you thermodynamic properties of a combustion process based on the fuel to air ratios and the type of process being performed
  Temperature, Entropy, Enthalpy, Pressure, Internal Energy,
  Knows the energy required to create and break the bonds needed for the reaction
  Knows enthalpy of reactants and products at certain temperatures
  Uses change of energy from bond breaking/formering to calculate the change in enthalpy
  Uses enthalpy to find temperature, entropy, and pressure changes at different stages in process
TOC

## Slide 92: Model Improvement Plan
Steps to Improve current Model
  Start to eliminate assumption
  Acquire necessary sensors
    Pitot tubes, thermocouples, IR Sensor/Camera
  Attach sensors where measurements are needed
    Pitot tube at the entrance and exit of engine,
    Thermocouples before and after each station
    IR sensor/Camera pointing at engine (Maybe)
  Run engine and collect data
  Verify that data makes sense compared to ideal model and follows similar trend
  Rank assumptions based on biggest sources of errors
    Remove assumptions that create significant errors
  Use data obtained from engine, calculate total loses
    Heat Transfer, Rayleigh flow losses, Efficiencies
  Create new model
  Design modifications based off of new model
TOC

## Slide 93: Calculating Efficiencies of Engine Stations
Compressor
  Usually between 0.85 and 0.90
Combustor
  Usually between on .97 and 0.99
Turbine
  Usually between on .90 and on.955
Nozzle
  Usually between 0.95 and 0.98
Key:
hxso = total enthalpy required to achieve Pxo if isentropic
ṁ = total mass flow rate
ṁf = mass flow rate of fuel
hPR = Low heating value of fuel - 43 MJ/kg
ho = total enthalpy
TOC

## Slide 94
TOC

## Slide 95: On-Engine Testing
TOC

## Slide 96
Combustor Testing- Thermocouple Stress from Aerodynamic Forces
Forces modeled perpendicular, with fastest airspeed in engine
  Assumptions are:
    Thermocouple is a solid stainless steel 316 rod fixed at one end
    Worst conditions (velocity and temperature) are taken from current model
    Will not be in contact with any part of combustor
Aero Forces:
Do not know exact velocity and temp in combustor
Velocity and temp are chosen from highest in engine, which take place at nozzle exit
Coefficient of drag is at worst 1.3, cylinder in flow is 1.2
Area is diameter time depth inserted
Density of air is average at Denver
Drag = 0.5 * rho * Cd * A * (V2)
Drag = 0.5 * 1.2[kg/m3] * 1.3 * 7.9e-6[m] * (564[m/s]2)
Drag = 15.76[N]
0.3175 cm
2.0 cm
vair = 564[m/s]2
Beam Equations: https://www.linsgroup.com
Drag Coefficient: https://sv.20file.org/up1/916_0.pdf
Shell
Thermocouple
TOC
Notes: Could be used in back up slides

## Slide 97: Combustor Testing- Thermocouple Stress from Aerodynamic Forces
Modeled as beam with distributed load
I is area moment of inertia, Mmax is max bending moment, σ is bending stress, Vmax is max shear moment, A is cross sectional area, and 𝛕 is shear stress
I = pi * (d4) / 64
I = pi * (0.003175[m])4 / 64 = 4.99e-12 [m4]
Mmax = F * (L2) / 2
Mmax = 15.76[N] * (0.02[m])2 / 2 = 0.0032[Nm2]
σ = -Mmax / I
σ = - 0.0032[Nm2] / 4.99e-12 [m4] = -6.3e8[Pa]
Vmax = F * L = 15.76[N] * 0.02[m] = 0.3135[Nm]
A = π * (d2) / 4 = π * (0.003175[m])2 / 4 = 7.92e-6 [m2]
𝛕 = Vmax/A = 0.3135[Nm] / 7.92e-6 [m2] = 3.98e4[Pa]
TOC

## Slide 98: Combustor Testing- Thermocouple Stress from Aerodynamic Forces
Maximum bending stress is -6.3e8[Pa] or 63 MPa
Maximum shear stress is 3.98e4[Pa] or 40 Mpa
Operating temperature is a maximum of roughly 1100K or about 850C
The maximum stress from aerodynamic forces will not exceed the strength of the material at temperature (120 MPa minimum)
FOS = Allowed Stress / Max Stress
FOS = 120[MPa] / 63[MPa]
FOS = 2
Link to Data Charts: https://askzn.co.za/stainless-steel/tech-grade-316.htm
TOC

## Slide 99
Combustor Testing-Part 2: Sealing Engine Shell and Thermocouple
Mechanical sealant is most removable, least invasive, and unlikely to break
Compression fittings designed for thermocouple sensors
Readily available and easy to use, found at McGuckins ect.
Much thicker and sturdy than thermocouple
Majority of fitting will be outside of engine
TOC

## Slide 100
Inlet Thermocouple
Outlet Thermocouple
SD Module
Breadboard
Arduino Mega
Cold Junction
Compensators
Load Cell
Arduino Pin Connect for Engine Testing
TOC

## Slide 101: Real Turbojet Thermodynamic Model
TOC

## Slide 102: Equations for Total Pressure and Temperature - Inlet
Temperature for Inlet:
Pressure for Inlet:
Ratio of specific heats for before the combustor: γ = 1.4
Specific heat capacity for before the combustor: Cpc = 1004 J/(kg-k)
Total pressure of room:P0= 101.325KPA
Total temperature of room: T0= 288 k
Initial Mach value: M0 = 0
TOC

## Slide 103: Equations for Total Pressure and Temperature - Compressor
Temperature for Compressor:
Pressure for Compressor:
Ratio of specific heats for before the combustor: γ = 1.4
Specific heat capacity for before the combustor: Cpc = 1004 J/(kg-k)
Compression Pressure ratio: rc = 2.9
Total pressure of compressor:P02= Inlet total pressure
Total temperature of compressor:T02= Inlet total temperature
Compressor Efficiency: ηc = 0.8
TOC

## Slide 104: Equations for Total Pressure and Temperature - Combustor
Temperature for Compressor:
Fuel Heat value: QR= 44*106 J/(kg*K)
Specific heat capacity for before the combustor: Cpc = 1004 J/(kg-k)
Specific heat capacity for after the combustor: CpT = 1445 J/(kg-k)
Total temperature of compressor:T03= compressor total temperature
Compressor Efficiency: ηb = 0.9
Fuel to air ratio: f = 0.0214
TOC

## Slide 105: Equations for Total Pressure and Temperature - Turbine
Temperature for Compressor:
Pressure for Compressor:
Ratio of specific heats for after the combustor: γ = 1.23
Specific heat capacity for before the combustor: Cpc = 1004 J/(kg-k)
Specific heat capacity for before the combustor: Cpc = 1445 J/(kg-k)
Fuel to air ratio: f = 0.0214
Total pressure of compressor:P04= Compressor total pressure
Total temperature of compressor:T02= Inlet total temperature
Total temperature of compressor:T03= Compressor total temperature
Total temperature of compressor:T04= Combustor total temperature
Compressor Efficiency: ηc = 0.85
TOC

## Slide 106: Equations for Total Pressure and Temperature - Nozzle
Exit Velocity of Nozzle:
Ratio of specific heats for after the combustor: γ = 1.23
Total pressure of compressor:P06= Turbine total pressure
Total pressure of compressor:P7= Exit Pressure (Equal to atmospheric pressure)
Total temperature of compressor:T05= Combustor total temperature
Gas Constant: R = 274
Nozzle Efficiency: ηc = 0.92
Total temperature and pressure are same as the turbines total temperature and pressure
TOC

## Slide 107: Update Engine Properties
C12H26 + 18.5(O2 + 3.78 N2) -> 12 CO2 + 13H2O + 69.93 N2
Chemical | Mass (g) | Mass % | Mass Fraction
12 CO2 | 528.108 | 19.4% | .194
13 H2O | 234.145 | 8.6% | .086
69.93 N2 | 1959.016 | 71.9% | .719
Gas | Translation Mode | Rotational Mode | Vibrational Mode | ͠Cp Value (Universal Gas Constant Ru)
CO2 | 3 | 2 | 8 | 7.5Ru
H2O | 3 | 3 | 6 | 7Ru
N2 | 3 | 2 | 2 | 4.5Ru
TOC

## Slide 108: Calculation of Engine Properties
Using table values from previous slides we can calculate Cp and Gamma values
Find what the ͠cpmix value is based on chemistry
  ͠cpmix is the heat capacity of the mixture
Find the Molecular Weight of the mixture (MWmix)
TOC

## Slide 109: Calculation of Engine Properties
Find Cpmix from ͠cpmixand MWmix
  Cpmix is the specific heat capacity of the gas after the combustor
  MWmix is the molecular weight of the gas mixture
Use Cpmix and Universal Gas constant to find R
Use Cpmixand R to find gamma
TOC

## Slide 110
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Engine Properties
 | Specific Heat: Cp [J/kg-K] | Specific Heat Ratio: γ
Before Combustor | Cpc= 1005 | γc = 1.4
After Combustor | Cpt =1445 | γt = 1.233
Mass flow rate of air: ṁa [kg/s] | Mass flow rate of fuel: ṁf [kg/s] | Fuel air ratio: f = ṁf/ṁa
0.2252 | 0.00481 | 0.0214
Notes: Put information into table if possible

## Slide 111: Material Selection
TOC

## Slide 112: Material Selection Trade Criteriation

## Slide 113: Material Trade Study

## Slide 114: Estimated Component Weights
Component | Volume [cm3] | Material | Density [g/cm³] | Weight [g] | Total Engine Weight Increase [%]
Improved Converging Nozzle | 9.21 | Stainless Steel 304 | 7.92 | 72.9 | 1.31
Mixing Chamber and Diffuser | 20.5 | Aluminum 6061 | 2.71 | 55.6 | 5.15
Interface struts | 2.68 | Stainless Steel 304 | 7.92 | 21.2 | 2.00
Total | - | - | - | 149.7 | 13.9
TOC
Notes: Based directly on solidworks model. Can look into using just 3 interface struts if necessary to reduce weight

## Slide 115: Heat Conduction through the interface bars
Since the rods are in contact with the converging nozzle, they will conduct heat.
Treating them as an adiabatic fin
Temperature at the ejector end of the bar = 490.4ºK
TOC

## Slide 116: Extrapolated Yield Strength Data for Ti-6Al-4V
TOC

## Slide 117: Extrapolated Yield Strength Data for Ti-5Al-2.5Sn
TOC

## Slide 118: Extrapolated Yield Strength Data for Ti-6Al-2Sn-4Zr-2Mo
TOC

## Slide 119: Extrapolated Yield Strength Data for Commercially Pure Titanium
TOC

## Slide 120: Risk Mitigation
TOC

## Slide 121: Identified Risks with mitigation
TOC
Notes: Way too many risks

## Slide 122: Cold Test Risk Mitigation
Supply tanks rated for 200 psi, building supplies maximum 110 psi
Pipe elbow fittings rated for 300 psi
Settling chamber safety factor of 138.62
Blast shield between team members and test apparatus at all times
No team member will be in the room when the settling chamber is above atmospheric pressure
Maximum feed tank energy is 355,800 J
  No potential for injury to test personnel if a feed tank ruptures given our test setup
Blast shield picture/diagram here
TOC

## Slide 123: Ejector Design
TOC

## Slide 124: Ejector Thrust-to-Weight Modeling Considerations
Incompressible
  Simplifies model
Inviscid flow
  Neglects boundary layer effects and turbulent dissipation
Zero freestream velocity
  Forward velocity of the engine adds complexity to the modeling of the secondary flow through the ejector
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Notes: Colin: increase plot label size
Change plot to T/W increase in comparison to STOCK nozzle, not improved conv nozzle
Explain why we didn’t pick bigger alpha E
While an Ejector has very complicated flow physics, a few common modeling assumptions are the most impactful

## Slide 125: Updated Model - Compressible Failure
Unable to recreate the plots or follow the derivation for the equations for a compressible ejector from from “An Investigation of the Thrust Augmentation Characteristics of Jet Ejectors”
TOC

## Slide 126: Ejector Model - Incompressible with Different Densities
Note notational differences from this presentation:
ɑ = ɑe
β = ɑD
m = ṁ
ms/ mp Needs to be solved for first before finding φ
TOC

## Slide 127: Ejector Model - Incompressible with Different Densities
“Ejector Thrust Augmentation" By W. H. Heiser
Constant but different densities that uniformly mix
Isentropic
Constant Profiles
Pe = Patm
Shows asymptotic behavior
TOC

## Slide 128: External Ejector Models - Compressible
Plot is from “An Investigation of the Thrust Augmentation Characteristics of Jet Ejectors”
Shows only a minor offset in a compressible vs incompressible analysis (~5% error at worst)
TOC

## Slide 129: Ejector Models - Incompressible vs Mixed Densities
Shows the compressible vs incompressible plot vs the output from the chosen mixed densities model
Shows about a 2% error between mixed densities and compressible formulations
TOC

## Slide 130: External Ejector Models - Losses
Plot is from “An Investigation of the Thrust Augmentation Characteristics of Jet Ejectors”
Shows losses in the thrust augmentation for too large of diffuser ratios
Does not account for varying mixing chamber lengths
TOC

## Slide 131: External Ejector Models - Mixing Chamber Length
Plot is from “An Investigation of the Thrust Augmentation Characteristics of Jet Ejectors”
Shows the results from a computation for theoretical mixing chamber length for a given area ratio under incompressible and compressible conditions
This indicates our mixing chamber may be too long, but this is balanced with other sources advocating for more complete mixing than used in this analysis
TOC

## Slide 132: Improved Nozzle Calculation Setup
Using the listed exit temperature from JetCat of a nozzle temperature of 993 K, mass flow rate of 0.23 kg/s, R = 273 J/kg-K, and γ = 1.233
Along with the assumption that Pexit = Patm
TOC

## Slide 133: Improved Nozzle Calculations
Stock nozzle exit: Mach 0.75
Improve the converging nozzle by instead accelerating the flow to Mach 0.95
The area ratio required to achieve this can be separately calculated based off of measured engine properties
Current Nozzle Thrust:
100 N
Improved Nozzle Thrust:
126 N
Overview
Design Solution
CPEs
Requirement Satisfaction
Risks
Verification & Validation
Planning
Notes: Colin: increase plot label size
Change plot to T/W increase in comparison to STOCK nozzle, not improved conv nozzle
Explain why we didn’t pick bigger alpha E

## Slide 134: Preliminary CFD Work
TOC

## Slide 135: Grid Refinement Study - Overview
Fine mesh has a y+ < 1 and max spacing of 0.2 mm (δ/10 or 1/330 lC)
Pseudo-structured meshes are being used
Refining in two separate areas:
y+ = 25 (~33x further from the wall)
max spacing of 0.4 mm (δ/5 or 1/165 lC)
All simulations have identical domains, initial conditions, and were run to 1e-6 residual
Pressure inlet and outlet boundary conditions used
23.4 mm
22.3 mm
66 mm
Inlet
Outlet
TOC

## Slide 136: Grid Convergence - Near-Outflow Results
Purpose is to investigate the solutions sensitivity to max grid spacing
Max velocity is unchanged
Agreement generally throughout the profile
6 mm upstream of outflow (9% of the domain - 6 or 12 nodes)
TOC

## Slide 137: Grid Convergence - Mid Domain Results
Purpose is to investigate the solutions sensitivity to max grid spacing
Max velocity is unchanged
Agreement generally throughout the profile
At the domain midpoint
TOC

## Slide 138: Grid Convergence - Wall Results
Purpose is to investigate the solutions sensitivity to the first wall point distance
Fine mesh and coarser max grid spacing unsurprisingly agree well
y+ = 25 case shows a max error of around 5%
Interestingly, the coarser wall spacing handles the inflow much differently
TOC

## Slide 139: Grid Convergence - Conclusions
There are large differences in the overall mesh sizes:
Fine - 43,677 nodes
Coarse wall - 38,361 nodes
Coarse max spacing - 13,210 nodes
Indicating that max spacing is of the greatest current concern to optimize
Other Notes:
The simulations converged much faster for the coarse wall spacing
TOC