## Slide 1: FlOWeR FlOWeR
Presenters: Max Buchholz, Angelo Hristopoulos, Adriana Lysak, Nathan Portman, Eric Tate, Preston Tee
Additional Team Members: Anthony Gregg, Anand Kappagantu, Weston Luke
Advisor: Alexandra Le Moine
Customer: U.S. Air Force Research Laboratory
Flow Optimization & Weight Reduction Project
Test Readiness Review

## Slide 2: Project Overview
Overview
Schedule
Test Readiness
Budget

## Slide 3: Purpose
Overview
Schedule
Test Readiness
Budget
Successfully compete in the Air Force Research Laboratory’s (AFRL) annual Aerospace Propulsion Outreach Program (APOP) competition
Improve performance of JetCat P100-RX hobbyist jet engine
Notes: IN THIS SECTION: -iterative process
-ejector nozzle flow physics overview

## Slide 4: Objectives
Overview
Schedule
Test Readiness
Budget
Increase the thrust-to-weight ratio of JetCat P100-RX hobbyist jet engine by 35% (Level 5)
Maintain or increase thermal efficiency
Maintain or decrease thrust specific fuel consumption (TSFC)
Create a thermodynamic model of the engine’s performance within 5% accuracy of data gathered (Level 3+)
Notes: Add numerical levels of success to the objectives here rather than spend a lot of time on the success level table
3+ is highest level

## Slide 5: Concept of Operations (CONOPs): Static Test
Overview
Schedule
Test Readiness
Budget
Thrust data
Thrust data
Thrust data
Notes: Idk who has the flipped around version but they should add it in
Indicate thrust data collection, include

## Slide 6: Operational Functional Block Diagram
Notes: Replace with one anthony makes
Summarize prev year project, expand ours - put expanded old one into backup slide
Make it more clear what exactly we’re doing - not just box around name

## Slide 7: Ejector Nozzle: Overview
Primary mass flow (from engine)
Secondary mass flow (from surrounding air)
Combined mass flow
Exhaust gasses from engine turbine exit through converging nozzle
Mass flow out of converging nozzle entrains mass flow from surrounding air and is forced out the back of the ejector nozzle
Overview
Schedule
Test Readiness
Budget
Notes: Discuss in detail the picture shown, add labels
Add another slide with general ejector nozzle details
Change title. “Actual” solution doesn’t look good
Animations:
Red arrows to blue and yellow
Change arrow sizes

## Slide 8: Baseline Design: CDR
Overview
Schedule
Test Readiness
Budget
Stock P100-RX Engine
FLOWeR Converging Nozzle
FLOWeR Mixing Chamber
195.25
202.17
Dimensions in mm
Notes: Combine w/ 10 w/ animations
Start w stock - add piece by piece, text boxes for each specific thing
Keep everything prev on screen and add to it
UNITS

## Slide 9: Baseline Design: Updated
Final ejector geometry will depend on cold testing results
Overview
Schedule
Test Readiness
Budget
Dimensions in mm
195.25
418
Stock P100-RX Engine
FLOWeR Converging Nozzle
FLOWeR Mixing Chamber
Notes: Mixing chamber elongated due to new information found on mixing length requirements
Curvature - Inlet and diffuser flared to reduce risk of flow separation
Converging Nozzle material change

## Slide 10: Critical Project Elements (CPEs)
Overview
Schedule
Test Readiness
Budget
Label | Critical Feasibility Element | FR
T/W | The T/W ratio of the engine shall increase and the TSFC shall decrease or remain constant. | 1,2
MODEL | Model accurately simulates thermodynamic properties of the engine, predicting increases in thrust and/or decreases in TSFC. | 3
INT-TEMP | All components can withstand temperatures throughout their section and can integrate with each other seamlessly. | 4
TEST | External sensors are integrated to augment engine’s internal sensors and gather necessary temperature and pressure data, and an off-engine testing setup is developed to validate nozzle design. | 4
Notes: Describe major changes - mostly verbal with key visual aids (ie arrows or circles) as necessary
Verbally/text relate to testing

## Slide 11: Engine Status Update
Engine returned from maintenance
Nominal thrust performance
Overview
Schedule
Test Readiness
Budget
Notes: Potentially mention that the graph shows thrust vs time as rpm is increased (10k rpm steps, ~40k to 154k), hence the increases/leveling
Describe major changes - mostly verbal with key visual aids (ie arrows or circles) as necessary
Dotted line w max RPM edxpdect

## Slide 12: Schedule
Overview
Schedule
Test Readiness
Budget
Notes: Dont justify or explain changes just say what were doing

## Slide 13: Spring Semester Schedule
Overview
Schedule
Test Readiness
Budget
Notes: Critical path?
Milestones
Completion status - what is done, in progress, upcoming etc
Hard stop date if level 5 not reached

## Slide 14: Testing and Manufacturing Plan
Today
✅
✅
Notes: Add in check/show completed tests; line for today
Include some green in the iteration boxes to show there is manufacturing happening there (change “iteration” to “cold test manufacturing” or something?)
Change the color on equipment delay
Add ECD to address margin, talk about it
Boot off as to why we are doing parametric to later, just state that we are doing it for now

## Slide 15: Test Readiness
Overview
Schedule
Test Readiness
Budget

## Slide 16: Testing Overview
Static testing
Engine running
Thermodynamic model verification
Overview
Schedule
Test Readiness
Budget
Off-engine (“cold testing”)
Engine not required
Ejector model verification
  Informs final design decisions before final manufacturing
Notes: Include sketch up of test set up
Labelled sensors at the start
Specs in back up slides

## Slide 17: Common Testing Needs
Facilities
All on- and off-engine test are performed in the test cell (room 169A) with personnel located in the control room (room 169)
Safety
Nate or Matt must always be notified prior to testing
Personnel must be located in the control room or outside bay doors during testing
All personnel must be familiar with emergency procedures checklist
Overview
Schedule
Test Readiness
Budget

## Slide 18: Testing Overview
Static testing
Engine running
Thermodynamic model verification
Cold testing
Engine not required
Ejector model verification
  Informs final design decisions before final manufacturing
Overview
Schedule
Test Readiness
Budget
Notes: Include sketch up of test set up
Labelled sensors at the start
Specs in back up slides

## Slide 19: Static Test Purpose
Pressure and temperature values measured for FlOWeR’s specific engine
Allows for highly accurate inputs to thermodynamic and ejector models
Verify thermodynamic model
Thrust measurements before and after modifications
Can quantify the improvements to engine thrust before going to competition
Overview
Schedule
Test Readiness
Budget
Notes: Include sketch up of test set up
Labelled sensors at the start
Specs in back up slides

## Slide 20: On-Engine Test: Data Acquisition
Measurement Device | Quantity of Interest
Static test stand | Thrust
Jet-tronics software, onboard sensors | RPM, exhaust gas temperature, fuel consumption
Additional sensors on test stand | Nozzle exit static and total pressures; nozzle inlet, exit, and surface temperature; cowling surface temperature
Given by AFRL | Combustion chamber temperature
Overview
Schedule
Test Readiness
Budget
Notes: Emphasize thrust stand test setup was used previously, but we have our own analysis that we’ve performed at this point
More in depth into what data is collected

## Slide 21: Static Test Stand Setup
Overview
Schedule
Test Readiness
Budget
Arduino Mega
Exhaust Instrumentation
Load Cell
Fuel Tank
Pump
ECU
Engine Wiring
Fuel Lines
Sensor Wiring
JetCat P100-RX
Notes: Central picture of test stand, smaller pictures of each sensor around outside, lines/arrows pointing to where it goes
Add a legend w line colors

## Slide 22: Facilities
Overview
Schedule
Test Readiness
Budget
Exhaust Instrumentation
Load Cell
JetCat P100-RX
Arduino Mega
ECU
Notes: This is a really cluttered slide, maybe drop the picture on the left and just do the right
Actual pictures of room and sensors

## Slide 23: Safety Procedures
Emergency contacts listed
Necessary emergency equipment on standby
  Fire extinguishers
  Fire blankets
All personnel are wearing PPE during testing
Engine operators are located in control room
Personnel located outside bay doors
Overview
Schedule
Test Readiness
Budget
Notes: Not sure we have a fire blanket in the room at the moment
Mini conops
Put in back up slide and state priority

## Slide 24: Testing Procedures
Preliminary Checklist
  Ensures proper engine set-up
  Includes safety prep, fuel set-up, electronics set-up, test cell arrangement, ventilation instructions, sensor set-up, and personnel instructions
Overview
Schedule
Test Readiness
Budget
Notes: Mini conops with lots of info spending lots of time on it

## Slide 25: Testing Procedures
Testing Procedures
  Detail the engine run sequence
  Procedures are derived from AFRL engine test and JetCat
Overview
Schedule
Test Readiness
Budget
Notes: Mini conops with lots of info spending lots of time on it

## Slide 26: Testing Procedures
Shut-Down Procedures
  Ensures safe ventilation of room and dismantling of test set-up
  Outlines storage of data
Overview
Schedule
Test Readiness
Budget
Notes: Mini conops with lots of info spending lots of time on it

## Slide 27: Outline of Engine Testing
Overview
Schedule
Test Readiness
Budget
Test | Purpose | Status
Stock Engine (Refurbished) | Ensure proper functioning engine, ensure expected thrust value, and gather model data | Complete
Improved Converging Nozzle | Verify improvement from converging nozzle, and gather model data | Incomplete
Ejector Nozzle | Test final modification, quantify thrust increase, and ensure competition readiness | Incomplete
Notes: Maybe possible
See WASP presentation for 1-2 slide summary of all this info
“Verify” in second row-- is verify or validate?

## Slide 28: Testing Overview
Static testing
Engine running
Thermodynamic model verification
Cold testing
Engine not required
Ejector model verification
  Informs final design decisions before final manufacturing
Overview
Schedule
Test Readiness
Budget
Notes: Include sketch up of test set up
Labelled sensors at the start
Specs in back up slides

## Slide 29: Cold Test - Purpose
Low risk method for validating aerodynamic models of various scaled nozzle configurations:
Stock nozzle (baseline)
Improved converging nozzle
Parametric study of ejector configurations
  Real world data will help inform final design decisions
Overview
Schedule
Test Readiness
Budget
Notes: Add converging nozzle and baseline nozzle as the “why”
Emphasize parametric study is reasoning to cold test
Talk about baseline test has .9 Mach from testing converging cone

## Slide 30: Data Acquisition
Measurement Device | Quantity of Interest
Static pressure probe at settling chamber | Setting baseline pressure for desired Mach Test time
Total pressure probe at nozzle exit | Nozzle exit Mach
K-type thermocouple | Nozzle exit Temperature
Derived from mass flow rate and Mach | Thrust
Overview
Schedule
Test Readiness
Budget
Notes: If we’re saying interest quantity for pressure at exit is mach, we should probably say the same for the k type thermocouple—they both feed into that
Emphasize thrust stand test setup was used previously, but we have our own analysis that we’ve performed at this point
More in depth into what data is collected

## Slide 31: Cold Test Design
Overview
Schedule
Test Readiness
Budget
Pressure Tanks
Electronic
Ball Valves
Settling Chamber
Manual Ball Valve
Regulators
Converging Cone
Adapter

## Slide 32: Cold Test Design - Pressure Tanks
Overview
Schedule
Test Readiness
Budget
Filled with building air supply
Filled to ~100 psi
Rated for 200 psi
Fill time: ~5 minutes per tank
Tanks have analog dial pressure gauge

## Slide 33: Cold Test Design - Flow Control
Overview
Schedule
Test Readiness
Budget
Electronically controlled ball valves
Switched from control room
Opened to prime settling chamber
Pressure Regulators
Controls pressure in settling chamber during test
Regulator
Electronic
Ball Valve

## Slide 34: Cold Test Design - Settling Chamber
Overview
Schedule
Test Readiness
Budget
Settling chamber reduces turbulence to the test section
Pressure transducer to capture pressure input to test section and test time
Settling chamber FOS = 138
Manual ball valve operated to begin test
Actuated from a distance behind blast shield
Pulley and rope
Manual Ball
Valve
Settling Chamber

## Slide 35: Cold Test Design - Test Section
Overview
Schedule
Test Readiness
Budget
Adaptor with correct area ratio for the desired Mach
Nozzles screw into Converging Test Nozzle
Nozzle instrumentation goes behind the nozzle
K-Type Thermocouple
USC Pressure Probe
Notes: Add labels: converging flow cone, USC probe

## Slide 36: Cold Test Procedure and Safety
All valves and nozzle checked before filling Supply Tanks
PPE must be worn once Supply Tanks begin to fill
  Safety glasses and ear protection
No team members in Test Cell once test is ready
Communication done over 2-way radio
Team members opening the ball valve remain behind blast shield
  Outside test team members let control room test members when to open and close valve
After test, team members can go into Test Cell to retrieve SD with data
Overview
Schedule
Test Readiness
Budget

## Slide 37: Outline of Cold Testing
Overview
Schedule
Test Readiness
Budget
Test | Purpose | Status
Stock Nozzle | Obtain baseline of cold test setup performance | Complete
Improved Converging Nozzle | Verify improvement from stock nozzle and further verify testing and data analysis procedures | Complete
Ejector Nozzle Parametric Studies | Explore the design space in real world conditions in order to compare with expected results from model | Incomplete
Notes: Maybe possible
See WASP presentation for 1-2 slide summary of all this info

## Slide 38: Parametric Study - Purpose
Ejector nozzles contain aspects that are hard to model
Compressibility
Flow separation/diffuser stall
Incomplete mixing
Parametric study informs future design decisions
Overview
Schedule
Budget
Test Readiness
Notes: Parametric study allows the current model to be validated and understood in the context of the current design, informing future design decisions

## Slide 39: Key Design Variables
αE = - Bypass Ratio
αD = - Diffuser Area Ratio
L - Mixing Chamber Length
Overview
Schedule
Budget
Test Readiness
As
Ap
Ad
Amc
As
Amc
Ad
Ap
L
D

## Slide 40: Parametric Study - Method
Each key design input variable will be varied in order to attempt to understand the models accuracy
αE ± 1.0
αD ± 0.5
L ± 1.0 D
Overview
Schedule
Budget
Test | αE | αD | L
Current Design Point | 3.5 | 1.5 | 3 D
Test Readiness
αE+ | 4.5 | 1.5 | 3 D
αE- | 3.5 | 1.5 | 3 D
αD+ | 3.5 | 2.0 | 3 D
αD- | 3.5 | 1.0 | 3 D
L+ | 3.5 | 1.5 | 4 D
L- | 3.5 | 1.5 | 2 D
Notes: Need to introduce alphaE, alphaD, L (names on slides) before you talk about them
Include graphic showing what each one is

## Slide 41: Validating Heiser’s Model
Overview
Schedule
Test Readiness
Budget
From J.W. Heiser[1] modified with skin friction loss estimates[2]

## Slide 42: Validating Heiser’s Model
Overview
Schedule
Test Readiness
Budget
From J.W. Heiser[1] modified with skin friction loss estimates[3]
Variation of αE:
Determine the offset of experimental φ values from theory
Quantify the spacing between the lines plotted
Variation of αD:
Estimate the actual slope of the lines plotted
Notes: In out machine from parametric study - This detailed stuff is probably going to be backups

## Slide 43: Parametric Study - Data Collection
Overview
Schedule
Test Readiness
Budget
Radial total pressure distribution at nozzle exit:
3 data points
Used to calculate average velocity
Bypass inlet static pressure
Used to calculate secondary mass flow rate
Known primary mass flow rate plus this data can be used to calculate thrust

## Slide 44: Parametric Study - Further Testing
Overview
Schedule
Test Readiness
Budget
Time permitting:
Combining best variations of design parameters
  Validate that results are still as expected
Extend variations of certain parameters
  If results from first experiments deem it necessary

## Slide 45: Budget
Schedule
Test Readiness
Overview
Budget

## Slide 46
Schedule
Test Readiness
Overview
Budget
Notes: Can we make the numbers bigger

## Slide 47: Cost Plan, Current exp, budget, rem, etc
Of the planed $5,000 budget, $1,669.63 has been spent so far, leaving $3,330.37 remaining
Remaining planned costs cover modification manufacturing
  $3,450 planned budget with $336.71 spent thus far for manufacturing proof of concept
  Totals for manufacturing should be well below planned budget, as detailed in the following slides
  Approximately $215 in reserve for unplanned hardware or electronics costs, with more likely available due to expected manufacturing costs
Schedule
Test Readiness
Overview
Budget

## Slide 48: Converging Nozzle
In-house manufacturing of converging nozzle using MarkForged metal 3D printer
  17-4 PH Stainless Steel is the current material selection
Expected costs between $650 and $950
Total manufacturing time 1-2 weeks for printing, curing, and finishing
Schedule
Test Readiness
Overview
Budget

## Slide 49: Mixing Chamber and Diffuser
In-house manufacturing of mixing chamber and diffuser sections of ejector nozzle using mills/lathes
Manufactured out of Al6061-T6511 with UHMW polyethylene support during manufacturing
  Expected costs of $190 per mixing chamber/diffuser for materials sourced through McMaster-Carr
Total manufacturing time 1-1.5 weeks for manufacturing and finishing
Schedule
Test Readiness
Overview
Budget

## Slide 50: Acknowledgements
AFRL: Lt Kavi Muraleetharan, Lt Collin Parsons, and Mr. Tim Erdmann
Advisor: Alexandra Le Moine
TAs: Emma Markovich and Colin Claytor
Technical Advisors: John Mah, James Nabity, Matt Rhode, Bobby Hodgkinson, Trudy Schwartz, Kathryn Wingate

## Slide 51: Supplemental Material

## Slide 52: Table of Contents
On-Engine Testing
Cold Test
Material Selection
Ejector Model
Notes: Variable geometry ruled out due to static conditions during testing
Nozzle weight is a small % of engine weight

## Slide 53: References
Mattingly, J.D. and Boyer, K.M. Elements of Propulsion: Gas Turbines and Rockets. American Institute of Aeronautics and Astronautics, 2 edition, 2016
Huang, K.P, Kisielowski, E. “An investigation of the thrust augmentation characteristics of jet ejectors,” April 1967.
Frank, G., Piper, S., Chen, Y., FitzRandolph, P., Camacho, C., Knickerbocker, M., Junker, M., Oropeza, D.C., Cutler, J., Fuernkranz, M., and Harthan, D. Specialized propulsion engine control system critical design review, 2018.
Coulon, T., Johnson, R., Jones, L., Mines, M., Schumacher, G., and Swart, C. Thrust to weight improvement of jetcat p100-rx turbojet engine, 2019
Soars, C. Gas Turbines: A Handbook of Air, Land and Sea Applications. Butterworth-Heinemann, 1 edition, 2014.
Violett, B. A few reminders for safe turbine operations.
White, F.M. Viscous Fluid Flow. McGraw-Hill, 3 edition, 2011
Heiser, H. W. Ejector thrust augmentation. Journal of Propulsion and Power, 26(6), November-December 2010.
Huang, K. P and Kisielowski, E. An investigation of the thrust augmentation characteristics of jet ejectors
JetCat. Jetcat turbine datasheet, 2015
Razak, A.M.Y. Gas turbine combustion.
Aeronautics Guide. Aircraft turbine engine fuel system components
Erickson, D.M., Day, S.A., and Doyle, R. Design considerations for heated gas fuel.
Larson, G.C. The hotter the better.
Autonomous Manufacturing. A guide to 3d printing with titanium
Online Metals, URL: https://www.onlinemetals.com/en/buy/aluminum-round-bar-7075-t6-t651-cold-finish?q=%3Aprice-asc&page=1&pagesize=25&sort=price-asc
Dr. D. Lewis Abata, The Thermodynamics of Emptying a Pressure Vessel, South Dakota School of Mines and Technology.
Gibson, P. W., “Blast Overpressure and Survivability Calculations For Various Sizes of Explosive Charges”, Army Natick Research Development and Engineering Center MA, June 1994.

## Slide 54: References
Heiser, H. W. Ejector thrust augmentation. Journal of Propulsion and Power, 26(6), November-December 2010.
Huang, K.P, Kisielowski, E. “An investigation of the thrust augmentation characteristics of jet ejectors,” April 1967.
White, F.M. Viscous Fluid Flow. McGraw-Hill, 3 edition, 2011

## Slide 55: Levels of Success
Notes: Split w prev slide - list concrete objectives w numerical values

## Slide 56: Functional Requirements
Notes: Split w prev slide - list concrete objectives w numerical values

## Slide 57
TOC

## Slide 58: Operational Functional Block Diagram
Current Project
Previous Year’s Project
TOC

## Slide 59: CDR Design Current Design
Overview
Schedule
Test Readiness
Budget
All units in mm
Notes: Describe major changes - mostly verbal with key visual aids (ie arrows or circles) as necessary

## Slide 60: Understanding Mixing Chamber Length
Overview
Schedule
Test Readiness
Budget
Variation of L
Test skin friction losses modeling
Understand effects of incomplete mixing

## Slide 61: On-Engine Testing
TOC

## Slide 62: On-Engine Safety Procedures
Engine Testing Procedure and Safety - Google Docs
TOC

## Slide 63: Temperature Data
Notes: 1% error

## Slide 64: Pressure Data
Notes: 30% error

## Slide 65: On-Engine Test: Electronics FBD
Notes: If time needs to be cut, put this in backup
9V battery instead of AC/DC converter

## Slide 66: Facilities
Overview
Schedule
Test Readiness
Budget
Exhaust Instrumentation
Load Cell
JetCat P100-RX
JetCat P100-RX
Arduino Mega
ECU
Notes: This is a really cluttered slide, maybe drop the picture on the left and just do the right
Actual pictures of room and sensors

## Slide 67: Cold Test
TOC

## Slide 68: OET: Pressure Regulator and Tank Feasibility
Dimensions
  Feed Tanks (2x)
    1-¼” outlet
  Feed Ball Valves (2x)
    1-¼” inlet, outlet
  53R Feed Regulators (2x)
    1-¼” inlet, outlet
  Settling Chamber:
    1-¼” inlet (2x)
    Outlet: Apollo 94A-109-01 full port brass ball valves
      2.520” ID
  Taper Cone:
    1.8” inlet
    1.075” outlet
TOC

## Slide 69: OET: Desired Settling Chamber Pressure
Content
TOC

## Slide 70: OET: Settling Chamber Structural Analysis
TOC

## Slide 71: OET: Pressure Regulator and Tank Feasibility
Isentropic relations were used to calculate the mass flow rate out of the settling chamber
Mass flow rate out of the feed tanks was calculated using non-ideal relations with both choked and unchoked flow, following conservation laws
The pressure, temperature, mass, and mass flow within each tank was calculated and plotted in an to determine nominal test time
  While feed tank pressures remain high, nominal test time is 11.69 seconds due to the combined feed tank mass flow rate dropping below the mass flow rate out of the settling chamber
  This will reduce pressures in the settling chamber, decreasing nozzle test efficacy
  Note this test time and the mass flow plotted on slide 72 is for two regulators---one regulator system can not keep up with the mass flow out of the settling chamber due to the choked flow in the feed pipe
TOC

## Slide 72: Mass Flow (Settling Chamber)
R = 8.3145 Pa-m3/K-mol = 286.5 J/kg-K
P2 = 131.84 kPa
P10 = 145.34 kPa
𝜌2 = 1.5931 kg/m3
MWair = 28.97 g/mol
a2 = 331.78 m/s
u2 = 93.88 m/s
V̇ = .0743 m2/s
ṁ = .1184 kg/s
TOC

## Slide 73: Mass Flow (Feed Tanks)
Known values:
  P0 = 758.42 kPa = 110 psi
  Pthroat = Psettle = 148.34 kPa
  Vtank = 80 gal. = .3636 m3
  T0 = T = 293.15 K
  R = 287 J/kg-K = 8.3145 Pa-m3/K-mol
  Athroat = 1.227 in2 = 7.9173x10-4 m2
  mmax = 3.2780 kg
TOC

## Slide 74: Mass Flow (Feed Tanks)
Choked Flow:
Non-Choked Flow:
Flow out of the feed tanks is initially choked due to small pipe diameter---this restricts mass flow rate from a single tank to relatively low values
TOC

## Slide 75: Mass Flow (Feed Tanks)
Calculations are derived from the first law of thermodynamics
  The second equation is the driving temperature calculations, as seen in the bottom right
  Iterative models were used to determine the next mass value, allowing for pressure and temperature calculations
TOC

## Slide 76: Mass Flow (Feed Tanks)
Maximum test time: 11.69 seconds
  Pressure remains high, but mass flow rate out of feed tank drops below mass flow rate out of settling chamber
TOC

## Slide 77: Cold Test Risk Mitigation
Vsettling = .032175925 cubic meters
Vfeed = .3636 cubic meters
Psettling= 148.34 kPa
Pfeed = 758.42 kPa
Pa = 86 kPa
W=P0V0(ln(P0/Pa)-1)+PaV0
1kg TNT = 4.184*10^6 J
Wsettle = 596 J
  TNT EQ: 1.42 g
Wfeed = 355,800 J
  TNT EQ: 85.04 g
The blast and resulting pressures would not cause any physical damage given our test setup [17]
TOC

## Slide 78
TOC
Notes: Appendix potentially, here for now

## Slide 79
TOC

## Slide 80
Overview
Schedule
Test Readiness
Budget
Cold Test Electronic Block Diagram
TOC
Notes: Potentially put in backups

## Slide 81
Overview
Schedule
Test Readiness
Budget
Cold Test Mounted Nozzle
TOC
Notes: Potentially put in backups

## Slide 82: Cold Test Safety Procedures
Cold Test Procedures - Google Docs
TOC

## Slide 83: Material Selection
TOC

## Slide 84: 3D Printer Metal Ansys Results -0.66 mm Base
Material | Bolt Hole Stress (Pa) | Strut Stress (Pa) | Location of Max Stress
D2 tool steel | 2.4428E+09 | - | Bolt hole
17-PH4 | 3.6374E+08 | 8.3155E+08 | Strut
H13 tool steel | 1.7847E+09 | - | Bolt hole
A2 tool steel | 2.3591E+09 | - | Bolt hole
SS 304, annealed | 1.6279E+08 | 8.4944E+08 | Strut
SS 304, 1/2 hard | 7.4279E+08 | 1.6538E+09 | Strut
Inconel 625 | 4.7945E+08 | don't have | Strut
TOC

## Slide 85: 3D Printer Metal Ansys Results -0.8 mm Base
Material | Bolt Hole Stress (Pa) | Strut Stress (Pa) | Location of Max Stress
D2 tool steel | 2.3736E+09 | - | Bolt hole
17-PH4 | 3.6174E+08 | 6.9227E+08 | Strut
H13 tool steel | 1.7963E+09 | - | Bolt hole
A2 tool steel | 2.1126E+09 | - | Bolt hole
SS 304, annealed | 1.6126E+08 | 8.0251E+08 | Strut
SS 304, 1/2 hard | 8.1856E+08 | 1.4228E+09 | Strut
Inconel 625 | 4.8347E+08 | 8.1429E+08 | Strut
TOC

## Slide 86: 3D Printer Metal Ansys Results -1 mm Base
Material | Bolt Hole Stress (Pa) | Strut Stress (Pa) | Location of Max Stress
D2 tool steel | 2.4263E+09 | - | Bolt hole
17-PH4 | 3.6371E+08 | 7.0596E+08 | Strut
H13 tool steel | 1.8328E+09 | - | Bolt hole
A2 tool steel | 2.1495E+09 | - | Bolt hole
SS 304, annealed | 1.6384E+08 | 7.9846E+08 | Strut
SS 304, 1/2 hard | 8.3099E+08 | 1.4372E+09 | Strut
Inconel 625 | 4.7078E+08 | 8.2686E+08 | Strut
TOC

## Slide 87: 3D Printer Metal Ansys Results -1.2 mm Base
Material | Bolt Hole Stress (Pa) | Strut Stress (Pa) | Location of Max Stress
D2 tool steel | 2.2251E+09 | - | Bolt hole
17-PH4 | 3.8714E+08 | - | Bolt hole
H13 tool steel | 1.8583E+09 | - | Bolt Hole
A2 tool steel | 2.1512E+09 | - | Bolt Hole
SS 304, annealed | 1.9248E+08 | - | Bolt hole
SS 304, 1/2 hard | 7.9869E+08 | - | Bolt Hole
Inconel 625 | 4.6503E+08 | - | Bolt hole
TOC

## Slide 88: Markforged Inconel 625 Properties
TOC

## Slide 89: Markforged Inconel 625 Properties
TOC

## Slide 90: Markforged 17-4PH Stainless Steel Properties
TOC

## Slide 91: Markforged 17-4PH Stainless Steel Properties
TOC

## Slide 92: Markforged 17-4PH Stainless Steel Properties
TOC

## Slide 93: Ansys Simulations: Gap Width
TOC

## Slide 94: Ansys Simulations: Pressure at Bolt Holes
TOC

## Slide 95: Ansys Simulations: Penetration at Bolt Holes
TOC

## Slide 96: Ansys Simulations: Nozzle Deformation
TOC

## Slide 97: Ansys Simulations: Screw Deformation
TOC

## Slide 98: Ansys Simulations: Deformation of Nozzle With Screws
TOC

## Slide 99: Ansys Simulations: Nozzle Stress
TOC

## Slide 100: Ansys Simulations: Stress With Screws
TOC

## Slide 101: Ansys Simulations: Stress With Screws
TOC

## Slide 102: Ejector Model
TOC

## Slide 103: Ejector Model - Incompressible with Different Densities
Note notational differences from this presentation:
ɑ = ɑe
β = ɑD
m = ṁ
ms/ mp Needs to be solved for first before finding φ
TOC

## Slide 104: Ejector Model - Thrust-to-Weight Predictions
Shows weight predictions for fixed L
TOC

## Slide 105: Ejector Model - Thrust-to-Weight Predictions
Shows weight predictions for fixed αE and αD (baseline)

## Slide 106: External Ejector Models - Compressible
Shows only a minor offset in a compressible vs incompressible analysis (~5% error at worst)[2]
TOC

## Slide 107: Ejector Models - Incompressible vs Mixed Densities
Shows the compressible vs incompressible plot[2] vs the output from the chosen mixed densities model
Shows about a 2% error between mixed densities and compressible formulations
TOC

## Slide 108: External Ejector Models - Losses
Shows losses in the thrust augmentation for too large of diffuser ratios[2]
Does not account for varying mixing chamber lengths
TOC

## Slide 109: External Ejector Models - Mixing Chamber Length
Shows the results from a computation for theoretical mixing chamber length for a given area ratio under incompressible and compressible conditions[2]
TOC

## Slide 110: Model Adjustments
Drag force on a surface[2]
Relating wall shear stress to skin friction coefficient[2]
Putting the two together

## Slide 111: Model Adjustments
Estimate of the free stream velocity of the secondary
Skin friction relation for a ZPG turbulent flat plate
Reynolds number based on location along the plate