## Slide 1: Gravity Offloading and Tethering Somatosensory Enhancement System (GOATSES) Preliminary Design Review
Grace Antonucci, Ben Foehr, Jack Harrison, August Hauter, Quentin Morton, Elena Salgado, Nick Taylor, Isaac Timko, & Cody Wheeler

## Slide 2: MEET THE TEAM
Grace Antonucci
Project Manager
Ben Foehr
Human Factors Lead
Cody Wheeler
Design Lead
August Hauter
Analysis Lead
CFO
Ike Timko Electronics Lead
Nick Taylor Manufacturing Lead
Elena Salgado
Safety Lead
Jack Harrison
Testing Lead
Quentin Morton
Lead Systems Engineer

## Slide 3: Agenda
Project Description
Baseline Design
Feasibility Studies
  Loading Margin
  Angle Margin
  Friction Margin
  Cost
Status & Strategy

## Slide 4: Project Need
Astronauts require, on average, 15 days to recover pre-flight levels of locomotive function required for egress (exiting the capsule). [2]
Astronauts experience loss of proprioceptive function in a microgravity environment.
Proprioceptive function relates to one’s understanding of how their body is positioned and how it is moving.
Retention of postural control is vital for long duration spaceflight missions.
Canadian astronaut, David Saint-Jacques, being carried to the medical tent after returning from 204 days in space. [1]
Notes: Astronauts require, on average, 15 days to recover pre-flight levels of locomotive function required for egress. [2]
Astronauts sufficiently maintain muscular and cardiovascular strength, but typically experience loss of proprioceptive function.
Proprioceptive function relates to one’s understanding of how their body is positioned and how it is moving.
Loss of proprioceptive functions result in difficulty with tasks such as standing, walking, and balancing.
Retention of postural control is vital for long duration spaceflight missions.

## Slide 5: Project Objectives
Current axial loading is problematic
Hypothesis: More realistic gravitational loading = better proprioceptive functions
Device will provide a load that stays perpendicular to support service
Main user base will be bed rest patients
Notes: Bed rest studies offer scientists ways to see how the body adapts to weightlessness. Volunteers spend up to 70 days in bed with a six-degree head-down tilt. They must eat, exercise, and even shower in the head-down position.
Our project aims to create a device in which maintains a force on the user that is perpendicular to their support surface regardless of postural sway.
This device will be used in laboratory studies to prove whether this improvement in loading direction yields better retention of proprioceptive functions.
Study requires a spaceflight analog such as bedrest.
  Bedrest: volunteers spend up to 70 days in bed with a six-degree head-down tilt. They must eat, exercise, and shower in this position. [3]
Astronauts are currently loaded to a single fixed point and therefore they do not need to balance themselves.
It is hypothesized that if astronauts were loaded as if in a realistic gravitational field, it would help maintain proprioceptive function by requiring them to balance themselves.
Our project aims to create a device in which maintains a force on the user that is perpendicular to their support surface regardless of postural sway.
This device will be used in laboratory studies to prove whether this improvement in loading direction yields better retention of proprioceptive functions.
Study requires spaceflight analog such as bedrest.
  Bedrest: volunteers spend up to 70 days in bed with a six-degree head-down tilt. They must eat, exercise, and shower in this position. [3]

## Slide 6: Project Description

## Slide 7: Functional Requirements
Number | Functional (Driving) Requirement | Verified By:
F1 | The device shall provide a force on the user not to exceed 1.3 kN | Force Measurement
F2 | The device shall generate a gravity vector that does not deviate greater than an angle of 2 degrees from the true perpendicular to the support surface | Angle Measurement
F3 | The device shall allow for user postural sway by limiting the coefficient of friction present opposite to the direction of sway to 0.3 | Material Properties
F4 | The device shall be able to load the user as they move within a 2 m2 area | Design Dimensions
F5 | The artificial force should act between the hips and shoulders of the user | Biological Analysis
F6 | The device shall prevent the user from falling if the user enters an unrecoverable state | Simulated Fall
F7 | The device shall be compatible with a person with a height of 1.5-2 m, a weight not to exceed 113.4 kg, and a hip breadth of 31-46 cm [7] | Design Dimensions
F8 | The device shall accommodate Earth-based testing such that Earth gravity will not be a confounding variable | Testing Equipment

## Slide 8: Functional Requirements
Number | Functional (Driving) Requirement | Verified By:
F1 | The device shall provide a force on the user not to exceed 1.3 kN | Force Measurement
F2 | The device shall generate a gravity vector that does not deviate greater than an angle of 2 degrees from the true perpendicular to the support surface | Angle Measurement
F3 | The device shall allow for user postural sway by limiting the coefficient of friction present opposite to the direction of sway to 0.3 | Material Properties
F4 | The device shall be able to load the user as they move within a 2 m2 area | Design Dimensions
F5 | The artificial force should act between the hips and shoulders of the user | Biological Analysis
F6 | The device shall prevent the user from falling if the user enters an unrecoverable state | Simulated Fall
F7 | The device shall be compatible with a person with a height of 1.5-2 m, a weight not to exceed 113.4 kg, and a hip breadth of 31-46 cm [7] | Design Dimensions
F8 | The device shall accommodate Earth-based testing such that Earth gravity will not be a confounding variable | Testing Equipment

## Slide 9: CONOPS
Stage 1: Prep
Take anthropometric measurements
  Mass
  Distance between attachment point & feet
Test Environment
Support Surface
Bed rest Patient
L
Loading Mechanism

## Slide 10: CONOPS
Stage 2: Ingress
User is helped into loading mechanism
  Patient cannot stand
Harness is adjusted to fit comfortably

## Slide 11: CONOPS
Stage 3a: Use
User can be on their side
  Leans front to back
OR User can be on their back
  Leans side to side
Trains proprioceptive function
User leans
Degree of Freedom
FNet
FNet

## Slide 12: CONOPS
Stage 3b: Data Collection
Angle measurement
  Body Angle
  Tether Angles
Load measurement
  Tether Tension
Body Angle ∠
Tether Angle ∠
Tether Angle ∠
Tension
Tension

## Slide 13: CONOPS
Stage 4: Egress
User is helped out of loading mechanism
  Patient cannot stand

## Slide 14: Baseline Design

## Slide 15: Baseline Design Overview
Project contains three components:
  Test Environment to remove influence of Earth Gravity
  Tensioning system to produce force in tether
  Translating device (linear actuator) to adjust location of tether
Support Surface
Direction of Simulated Gravity
Direction of Earth Gravity
Fg
Harness
Platform
Tensioning and Translating Systems:
Screw Drive Linear Actuator
Torque Motor
Angle Sensor
Notes: Subject lays on their back or side on a rolling platform
Two tethers will produce a simulated gravity force perpendicular to Earth’s gravity
The tethers will be loaded via torque motors or sandbags on a pulley system
When the subject leans, the tether attachment points will be moved using a linear actuator to keep the net force perpendicular to the support surface as the subject moves

## Slide 16: Test Environment Baseline Design
A 90-degree test bed removes effect of Earth gravity in the direction of gravity simulation.
This setup will have some friction, which would not be present in a real zero-gravity environment
Coefficient of friction must be low (𝝻 < 0.3) to create most realistic environment
Direction of Earth Gravity
Direction of Simulated Gravity
Low coefficient of friction between rollers and table
Platform
Table
Support Surface
N
Friction = 𝝻*N
Notes: Mention that a feasibility study will be done later in the presentation to cover mu
Mention adjustable height?

## Slide 17: Tensioning System Baseline Design
Active tensioning system
  Torque motor winds end of tether to produce tension
Passive tensioning system
  Load supplied by sandbag on a pulley system connected to each tether
Direction of Simulated Gravity
Direction of Earth Gravity
F1
F2
Fg= F1+F2
𝛂
𝜷
Sandbag
Tether
Earth Gravity
Earth Gravity
Motor
Tether
Direction of Earth Gravity
Direction of Simulated Gravity
F1
msandg = F1
Sandbag
F1
Notes: Two tethers connected to subject
F1 = F2 = constant
Not enough time. Both feasible. Team discretion. (Just taking notes)

## Slide 18: Translation System Baseline Design
The tensioning system is connected to a screw drive linear actuator.
When the angle sensors and accelerometer detect change in 𝛂 , 𝜷, and 𝛉, the actuators will adjust the location of connection points to keep 𝛂=𝜷.
Response time for the actuators determines whether force vector stays within 2° of normal
Support Surface
Harness
F1
F2
Direction of Simulated Gravity
Direction of Earth Gravity
Fg = F1+F2
dx
𝛂
𝜷
dx
±2°
dx
Screw drive
linear actuator
𝛉
Accelerometer

## Slide 19: Safety System Baseline Design
Safety:
  An additional tether will be attached to a fixed point as a passive safety system
  If the user falls and does not catch themself, this tether will be pulled tight and prevent them from falling
Direction of Simulated Gravity
Direction of Earth Gravity
F1
F2
F1
F2
F3

## Slide 20: Functional Block Diagram

## Slide 21: Feasibility Studies

## Slide 22: Critical Project Elements - Feasibility Studies
Critical projects elements were selected for feasibility studies based on the foreseen “dealbreakers” of the project:
F1: Loading Margin: “The Device shall provide a force that does not exceed 1.3 kN” - Force vector strength must remain within needed range
F2: Angle Margin: “Gravity vector remains within 2° normal of support surface” - Force vector direction must act in specified direction
F3: Friction Margin: “Coefficient of friction in direction of postural sway minimized to 0.3” - Test Subject’s ability to displace and respond during testing
Cost Feasibility: How does the budget account for the components needed?
Notes: SAFETY IS A CONCERN, BUT IS IN APPENDIX AND IS FEASIBLE: tHESE ARE OUR PROBLEMS

## Slide 23: Universal Test Subject
50th Percentile American Male, NASA Handbook
(APPENDIX B) [7]
Height: 171.6 cm
Weight: 73 kg
CoM: 103.1 cm
Depth: 24.65 cm
Foot Size: 26.05 cm
Lean Max: 7.6º
Postural Sway of the Human Subject is modeled by 0.5 hz sine wave, as per Dr. Temple’s research.
Back/forth displacement of the Universal Test Subject is assumed to be modeled as a pendulum swing, modeled in MATLAB.
Notes: dr clark used a pendulum w/ .5 hz sine wave with 10 degree amplitude. It’s an assumption: we want to do humans: we MODEL sway as pendulum sway. Mention that these are not worst case (except for the angle)

## Slide 24: Feasibility Study 1 - Force Superposition
Will our baseline setup be analytically solvable so our active components can respond appropriately?
Our loading scheme is a fully determined system with us holding F1 = F2 & 𝛼 = 𝛽
  F1 = F2 = const
  𝛼 = 𝛽 = f(θ), tether-force triangle moves as one entity
F1
F2
Direction of Simulated Gravity
Direction of Earth Gravity
Fg = F1+F2
𝛂
𝜷
θ

## Slide 25: Feasibility Study 1 - Force Superposition
In this study, we mainly focused on the derived loading requirements under our first functional requirement
Even as actuators move to account for load direction, the load magnitude will still vary
The quantity dy drives the magnitude of the load on the user
As the subject leans back-and-forth/side-to-side in a 1/2 Hz sinusoid motion, how much will dy change?
Support Surface
Harness
Linear Actuators
F1
F2
Direction of Simulated Gravity
Direction of Earth Gravity
Fg= F1+F2
θ
dx
dx = Lsinθ
dy = L - Lcosθ
L
𝛂
𝜷
dx
dx
±2°
dy

## Slide 26: Feasibility Study 1 - Attachment Height Variation
As the subject leans back-and-forth/side-to-side in a 1/2 Hz motion, the change in attachment height was tracked
Between maximal angle variations of ±7.6 the change in attachment height was small
Note: The dy is tracked over three various user heights: the Universal Test Subject (UTS) height and ±15cm~6in (15o and 15u, respectively) the UTS height
**15cm~2.5 standard deviations of US adult male height [10]

## Slide 27: Feasibility Study 1 - Force Magnitude Variation
With each individual tether’s tension magnitude being held at a fixed value, the net load acting on the test subject will vary as the tether attachment angles vary.
It was found that the load variations under expected angle changes stayed within our design requirement bounds of ±10N of the applied load on the test subject.
Notes: Notes: +/- 10 N bounds are because of 1 kilogram sensitivity. Client stressed correct angle is more important than correct force magnitude

## Slide 28: Feasibility Study 1 - Load Magnitude
The load will be transferred through human-rated cabling that can be bought off the shelf (OTS):
  Rock climbing ropes
  Low stretch, low wear lifting ropes [4]
  Ratcheting seat belt straps
The actual load can come from multiple possible sources:
  Electric motors (OTS)
  Sandbags connected through a pulley system
    Lowest density: 1522 kg/m^3 [5]
    So for a universal test subject 2x ~36cm per side sandbags
F1
msandg = F1
Sandbag
F1
F1
F2
Direction of Simulated Gravity
Direction of Earth Gravity
Fg = F1+F2
dx
𝛂
𝜷
dx
dx
OR
Torque Motor

## Slide 29: Feasibility Study 2 - (F2) Gravity Vector Deviation
Support Surface
Harness
F1
F2
Direction of Simulated Gravity
Direction of Earth Gravity
Fg = F1+F2
dx
𝛂
𝜷
dx
±2°
dx
±2°
Fg = F1+F2
Sliding Load System:
Screw Drive Linear Actuator
Angle Sensor

## Slide 30: Feasibility Study 2 - (F2) Gravity Vector Deviation
Support Surface
Harness
F1
F2
dx
𝛂
𝜷
dx
±2°
dx

## Slide 31: Feasibility Study 2 - (F2) Gravity Vector Deviation
Factors that Affect Angle deviation
Sensor Accuracy
Time Delay
Tension Measurement Accuracy
Angle Sensor Accuracy
Computational Time
Sensor Response Time
Actuator Movement Time
Inertial Delay
Movement Accuracy
Tension Motor Accuracy
Actuator Accuracy
“The device shall generate a gravity vector that does not deviate greater than an angle of 2 degrees from the true perpendicular to the support surface & Angle Measurement.”

## Slide 32: Feasibility Study 2 - (F2) Gravity Vector Deviation
Factors that Affect Angle deviation
Sensor Accuracy
Time Delay
Angle Sensor Accuracy
Computational Time
Sensor Response Time
Actuator Movement Time
“The device shall generate a gravity vector that does not deviate greater than an angle of 2 degrees from the true perpendicular to the support surface & Angle Measurement.”
Notes: Movement accuracy is neglected because motor and actuator precision is significantly higher than all of our positioning requirements
Current sensor accuracy and inertial forces are also neglected as they are insignificant compared to the other delays and accuracy

## Slide 33: Feasibility Study 2 - (F2) Gravity Vector Deviation
Sensors
Tether Angle Sensor 0
Tether Angle Sensor 1
Current Sensor 0
Current Sensor 1
Power Supply
Controller
Control Algorithm
Tensioning Motors
Motor 0
Motor 1
Linear Actuators
Actuator 0
Actuator 1
Data Output
Visual Display
Master Computer
Key
Power
Data
Motor controller
ΔtController
ΔtSensors
ΔtMotor Response
ΔtActuator Response
+
+
+
𝜀Controller
𝜀Sensors
𝜀Motor Response
𝜀Actuator Response
+
+
+

## Slide 34: Feasibility Study 2 - (F2) Gravity Vector Deviation
Trade Space Overview 1: Electronics Worst Case
Component Type | Component Name | Precision | Frequency Response | QTY | Unit Cost
Angle Sensor | SEN0386 6-Axis Accelerometer | 0.05° | 200 Hz (5 ms) | 2 | $25
Controller | Arduino Uno/Nano | N/A | 30 Hz (33 ms) | 2 | $25
Linear Actuator | Ball Screw Drive | 0.0203mm | 300 mm/s (speed) | 2 | $933
Notes: These are the WORST case component selections that can meet our requirements

## Slide 35: Feasibility Study 2 - (F2) Gravity Vector Deviation
±2°
Notes: Thoroughly explain all lines on both plots

## Slide 36: Feasibility Study 3 - (F3) Friction Margin
“The device shall allow for user postural sway by limiting the coefficient of friction opposite to the direction of sway to 0.3.”
Mobile Contact Surface Material | Static Co. of Friction | Reference Surface Material
Polyurethane - [C3H8N2O] | 0.2 | Steel
Teflon - [C2F4] | 0.05 | Teflon (PTFE)
Direction of Earth Gravity
Direction of Simulated Gravity
Friction interactions between mobile user and test bed surface
Platform
Table
Support Surface
Friction = 𝝻*N = 𝝻*mg
N
Direction of Postural Sway

## Slide 37: Cost Feasibility
The customer has expressed a willingness to provide extra funding (of a non-agreed upon amount at the moment) in order to achieve project success if extra funds would be required.
Raw material & Structure
Actuators/Motors
Data
Notes: More initial budget given to mechanical and non-data driven electronic subsystems as the project is primarily mechanical:
  The combined costs of tethers, structural materials, motors, etc. place an initial cost estimate of a few thousand dollars.
  The Mechanical, Electronic, and Sensor categories were given $500, $250, and $250, respectively, of budget margins to account for needed part replacements and/or increasing design complexity.
  Unaffiliated overall margin of $200 set aside for the whole of the project to be distributed as necessary.

## Slide 38: Status Summary & Strategy

## Slide 39: Status Summary
Primary Feasibility Studies:
Loading Feasibility
Angle Margin Feasibility
Friction within Test Environment Feasibility
Cost Feasibility
Secondary Feasibility Studies:
Safety Feasibility
Ingress/Egress Feasibility
Angle Detection Feasibility
Load Measurement Feasibility
Linear Actuator Feasibility
Tertiary Feasibility Studies (Future Work):
Load Application Selection
Harness Design Feasibility
Power Feasibility
Structural Feasibility
Monte Carlo Simulations

## Slide 40: Next Steps (Future Work)
Phase 1: Feasibility & Trade Studies
Phase 2: CAD & Design Finalization
Phase 3: System Analysis & Performance
Phase 4: CDR Slide Creation
Phase 5: Internal & External Review
Key:
Loading Mechanism
Test Environment
Sliding Load Attachment
Safety & Human Factors
Sensors & Verification
Overview & Budget
Review
Margin
Milestone
External Deadline
Large Margin

## Slide 41: Questions?

## Slide 42: Appendix (Additional Studies)

## Slide 43: Universal Test Subject
50th Percentile American Male, NASA Handbook
(APPENDIX B) [7]
Height: 171.6 cm
CoM: 103.1 cm (Up From Foot)
Shoulder Width: 46.95 cm
Torso Width: 38.4 cm
Depth: 24.65 cm
Foot Size: 26.05 cm
Lean Max: 7.6º
Sway Max: 5.4º
Weight: 73 kg
Notes: Add in dr clark about the pendulum .5 hz sway assumption: we want to do humans: we MODEL sway as pendulum sway

## Slide 44: Max Lean Angle
c = CoM Height = 103.1 cm
Depth: 24.65 cm
Foot Size: 26.05 cm
a = Foot-Depth/2 = 13.725 cm
Arcsin(a/c) = 7.6º
Assumptions:
a = Section of body in front of CoM
MAX LEAN

## Slide 45: Feasibility Study 1 - (F1) Continued Proof

## Slide 46: Attachment Movement Data (Lateral):

## Slide 47: Attachment Movement Data (Vertical and Angle):

## Slide 48: Feasibility Study - (F6) Safety
F6: The device shall prevent the user from falling if the user enters an unrecoverable state.
The device shall not continue the load if the user enters an unrecoverable state.
Unrecoverable: User is at an angle of > 20 degrees, COM position is < 75 cm above the ground, or the COM has a velocity > 1 m/s
20º
Max lean angle of 10-20 degrees before people fall
Min COM position from ground at 10 deg lean is 85 cm
Max vel of COM at 10 deg sway at 0.5 Hertz is 65 cm/s
  When one has reached 1 m/s, they have only moved 5 cm in 0.1 sec
75 cm
1 m/s
.

## Slide 49: Feasibility Study - (F6) Safety
HOW
Mechanical:
Using 1 or 2 slacklines to catch a user in case of a fall with a static length
Grigri auto belay stopping device/ seatbelt mechanism if tether velocity > 85 cm/s
Pin in tethers so it cannot have less than 75 cm of length out
The supporting surface is big enough for the user to step and catch their fall
Electrical:
Coding in when sensors measure an angle > 20 degrees to stop motor force
Coding in when accelerometer measures velocity > 85 cm/s to stop motor force

## Slide 50: Feasibility Study - (F8) Ingress & Egress
F8: The device shall accommodate Earth-based testing such that Earth gravity will not be a confounding variable.
The 90-degree testing environment ensures that the user’s axis of postural sway is normal to Earth’s gravity. Thus, lean is neither hindered nor aided by gravitational force
Testing platform and table will be carefully constructed and assembled to remain parallel to Earth’s surface
Lab team will further negate any effects of gravity by assisting user ingress/egress
In practice, bed rest study patients can be loaded into device by staff in accordance with bed rest study guidelines

## Slide 51: Feasibility Study - Tensioning Device
F1
msandg = F1
Sandbag
F1
OR
Tensioning Motor
Maximum Lean Rate ~ 6 cm/s
Maximum Motor Force = 0 .91 kN
Motor Shaft Diameter = 4 cm
Motor Specs Required = 28.6 RPM with a torque of 36 N-m

## Slide 52: Angle Sensors
For Person Angle:
https://www.mouser.com/ProductDetail/DFRobot/SEN0386?qs=DRkmTr78QAS3VaTwMlAopw%3D%3D

## Slide 53: Angle Sensors
For Tether Angle:
https://www.bendlabs.com/two_axis_datasheet.pdf
Sliding Load System:
Screw Drive Linear Actuator
Angle Sensor

## Slide 54: Actuation
Support Surface
Harness
Linear Actuators
F1
F2
Direction of Simulated Gravity
Direction of Earth Gravity
Fnet= F1+F2
θ
dx
dx = Lcosθ
L
𝛂
𝜷
dx
dx
±2°
Tether Tensioning Device Attachment Point
Actuator Motor And Control Attachment
Screw Drive Powered by Motor
Attachment Point Guides/Track

## Slide 55: Actuation Specifications
The actuation system requires a number of specifications in order to fulfill requirements:
Speed/Responsiveness: 0.10 m/s
Minimum Stroke (Using max COM height and lean): 13.7 mm
Maximum vertical load support required: 0.65 kN
  Minimum vertical load required will be determined through further analysis for actuator sizing/cost optimization (force applied can be distributed through structural support)
Brake Required: No

## Slide 56: Actuation Mechanics Trade
Method | Speed/Responsiveness (mm/s) | Stroke (mm) | Cost | Max Load (N)
Belt Drive Option 1 | N/A (Accuracy .001mm/25mm travel) | 50 | $344 | 1117.2
Screw Drive Option 1 | 300 | 100 | $933 | 294
Belt Drive Option 2 | 1270 | 184 | $888 | 1111.32
Screw Drive Option 2 Model: COLTW0000795760 | 52 | 100 | $662 | 1960

## Slide 57: Feasibility Study 1 - (F1) Load Magnitude
Sensor Type | Sensor Name | Accuracy | Frequency Response | Cost
In-line Load Cell | Mini In-Line Load Cell | ± 0.68 kg | 16.2 kHz (0.06 ms) | $675
In-line Tension Gauge | Multi-Configuration Tension Sensor | ± 1.36 kg | 200 Hz (5 ms) | (need quote)
Precise Scale | Paddie Shipping Scale | ± 0.045 kg | N/A | $58
Trade space Overview 1: Cable Force Sensors
Precision is dependent on analog-to-digital conversion. Can be very high precision
Torque motor: force sensor(s) data will be fed back into motor controller to keep tension constant
Sandbag: precise scale to measure weight and thus tension applied

## Slide 58: Feasibility Study 1 - (F1) Force Application
Device | Name | Current Draw/Output | Voltage Draw/Output | Force Applied | Cost
Hybrid Stepper Motor | ML34HD2L4350 | 3-3.5 A | 48-160 VDC | Up to 1120 N at 50 rpm | $177 (x2)
Stepper Motor Driver | SR8-Plus | 2.4-7.8 A | 24-75 VDC | N/A | $119 (x2)
Trade space Overview 2: Force Application Devices
If mechanical route chosen, components will be weights, pulleys, containers
If electrical route chosen, components will be electric motors and motor driver
  PID control to negate cable slack and keep tension constant
  At 50 rpm, shaft tangential velocity = 3.325 cm/s >> 0.08 cm/s (slide 46)
Notes: Response time
Current does not need to be changing. Very small steps can be taken until the rope is taught enough for desired tension. Stepper motor can turn cw or ccw to respond to cable slack. Tension sensor data will be very important and fed back through the controller to keep tension constant at desired value

## Slide 59: Feasibility Study 2 - (F2) Gravity Vector Deviation
Trade space Overview 3: Computation
Microprocessor Type | Device Name | PID Computation Frequency | Cost
ATmega328P | Arduino Uno/Nano | 30 Hz (33 ms) | $25
Cortex-A72 (ARM v8) | Raspberry Pi 4 | 55 Hz (18 ms) | $35
ARM Cortex-M4 72Mhz | LHI Pro Racing F3 Flight Controller | 115 Hz (8.7 ms) | $40

## Slide 60: Feasibility Study 2 - (F2) Gravity Vector Deviation
Initialize the sway equations: θ(t) = A*sin(T*f*t) dθ_dt(t) = T*f*A*cos(T*f*t)
While (t > simulation_time)
t += sensor_query_time;
new_position = PID_control(current_position,t);
t += PID_computation_time;
translation_speed = shoulder_height*sin(dθ_dt(t));
if ( max(translation_speed) > max_actuator_speed )
t += excess_move_time;
position_array_PID.append(new_position);
PID_difference = position_array_actual - position_array_PID;
Plot results of both of the simulations and their deviations from the true position (error)
While (t > simulation_time)
t += sensor_query_time;
Commanded_rate = K1* (movement_rate - actuator rate)
K2*dθ_dt(t);
t += rate_computation_time;
translation_speed = shoulder_height*sin(dθ/dt);
if ( max(translation_speed) > max_actuator_speed )
t += excess_move_time;
position_array_STEPPER.append(new_position);
STEPPER_difference = position_array_actual
- position_array_PID;
PID Control Simulation
Stepper Rate Command Simulation
Notes: Thoroughly explain all lines on both plots

## Slide 61: Why Not One Tether?
dy
Work = m*g*dy
When the test subject leans forward, slack will be taken out of the system.
  Sandbag goes down
  Work is being done on the person
When test subject leans back to original position, slack will have to be given
  Sandbag goes up
  User has to do work on the system
If there are two tethers:
  One sandbag goes down, one sandbag goes up
  Net work = 0

## Slide 62: Post-CONOPS
Stage 5: Balance Tests
Out of scope of this project
After bed rest is complete (~70 days)
Test for retention of proprioceptive functions
Direction of Earth Gravity

## Slide 63: References

## Slide 64: Presentation References
[1] Garcia, Mark. “Astronaut David Saint-Jacques Is Carried to a Medical Tent.” NASA, NASA, 25 June 2019, https://www.nasa.gov/image-feature/expedition-59-canadian-space-agency-astronaut-david-saint-jacques-is-carried-to-a.
[2] Mulavara, Ajitkumar P., et al. “Locomotor function after long-duration space flight: effects and motor learning during recovery.” \emph{Experimental Brain Research} vol. 202, no. 3, 2010, pp. 649-659 doi: 10.1007/s00221-010-2171-0.
[3] Mars, Kelli. “Analog Missions: Bed Rest Faqs.” NASA, NASA, 26 Mar. 2019, https://www.nasa.gov/analogs/envihab/bed-rest-faqs.
[4] McMaster-Carr,“Fibrous Rope”,McMaster-Carr,https://www.mcmaster.com/fibrous-rope/
[5] Densities of materials. Engineering ToolBox. (n.d.). Retrieved October 5, 2021, from https://www.engineeringtoolbox.com/density-materials-d_1652.html.
[6] Tleto. “Polyurethane Coefficient of Friction.” Gallagher Custom Polyurethane Molding, 29 Oct. 2020, https://gallaghercorp.com/polyurethane-coefficient-of-friction/.
[7] NASA, “Human Integration Design Handbook (HIDH)”, \emph{NASA Special Publication SP-2010-3407-REV1}, 2014.

## Slide 65: Presentation References
[8] “Friction and Friction Coefficients.” Engineering ToolBox, https://www.engineeringtoolbox.com/friction-coefficients-d_778.html.
[9] “Measuring Stepper Motor holding torque” https://www.applied-motion.com/news/2015/10/dynamic-torque-step-motor-sizing
[10] Fryar CD, Carroll MD, Gu Q, Afful J, Ogden CL. “Anthropometric reference data for children and adults: United States, 2015–2018.” National Center for Health Statistics. Vital Health Stat 3(46). 2021.