## Slide 1: Gravity Offloading and Tethering Somatosensory Enhancement System (GOATSES) Test Readiness Review
Grace Antonucci, Ben Foehr, Jack Harrison, August Hauter, Quentin Morton, Elena Salgado, Nick Taylor, Isaac Timko, & Cody Wheel

## Slide 2: MEET THE TEAM
Grace Antonucci
Project Manager
Ben Foehr
Human Factors Lead
Cody Wheeler
Design Lead
August Hauter
Analysis Lead
CFO
Ike Timko Electronics Lead
Nick Taylor Manufacturing Lead
Elena Salgado
Safety Lead
Jack Harrison
Testing Lead
Quentin Morton
Lead Systems Engineer

## Slide 3: Agenda
Project Overview
Schedule
Test Readiness
  Load Magnitude
  Load Direction
  Friction
Budget

## Slide 4: Project Overview
Notes: WHY are we doing this project, HOW are we going to do this project, WHO is using this project, WHAT are we doing in this project

## Slide 5: Project Objectives
Current axial loading is problematic
Hypothesis: More realistic gravitational loading = better proprioceptive functions
Device will provide a load that stays perpendicular to support service
Main user base will be bed rest patients which offer scientists a way to see how the body adapts to weightlessness
Notes: Bed rest studies offer scientists ways to see how the body adapts to weightlessness. Volunteers spend up to 70 days in bed with a six-degree head-down tilt. They must eat, exercise, and even shower in the head-down position.
Our project aims to create a device in which maintains a force on the user that is perpendicular to their support surface regardless of postural sway.
This device will be used in laboratory studies to prove whether this improvement in loading direction yields better retention of proprioceptive functions.
Study requires a spaceflight analog such as bedrest.
  Bedrest: volunteers spend up to 70 days in bed with a six-degree head-down tilt. They must eat, exercise, and shower in this position. [3]
Astronauts are currently loaded to a single fixed point and therefore they do not need to balance themselves.
It is hypothesized that if astronauts were loaded as if in a realistic gravitational field, it would help maintain proprioceptive function by requiring them to balance themselves.
Our project aims to create a device in which maintains a force on the user that is perpendicular to their support surface regardless of postural sway.
This device will be used in laboratory studies to prove whether this improvement in loading direction yields better retention of proprioceptive functions.
Study requires spaceflight analog such as bedrest.
  Bedrest: volunteers spend up to 70 days in bed with a six-degree head-down tilt. They must eat, exercise, and shower in this position. [3]

## Slide 6: Project Objectives
Number | Functional (Driving) Requirement | Verified By:
F1 | The device shall provide a force on the user not to exceed 1.3 kN | Force Measurement
F2 | The device shall generate a gravity vector that does not deviate greater than an angle of 2 degrees from the true perpendicular to the support surface | Angle Measurement
F3 | The device shall allow for user postural sway by limiting the coefficient of friction present opposite to the direction of sway to 0.3 | Friction Measurement
F4 | The device shall be able to load the user as they move within a 1.75 m2 area | Design Dimensions
F5 | The artificial force should act between the hips and shoulders of the user | Biological Analysis
F6 | The device shall prevent the user from falling if the user enters an unrecoverable state | Simulated Fall
F7 | The device shall be compatible with a person with a height of 1.5-2 m, a weight not to exceed 113.4 kg, and a hip breadth of 31-46 cm [7] | Design Dimensions
F8 | The device shall accommodate Earth-based testing such that Earth gravity will not be a confounding variable | Testing Equipment
Notes: F2 being the thing that separates us from existing technology, and F1 and F2 are the ones that can make it as effective as existing technology.

## Slide 7: Levels of Success

## Slide 8: Levels of Success

## Slide 9: CONOPS
Prep
Use
Loading mechanism is assembled and modified to take into account user’s mass and anthropomorphic data
Tether base pulls in a direction normal to the stationary base and moves with the user’s general center of gravity as the user leans.
Fail-safe mechanisms engage if user falls.
Body angle, tether angle, and tether tension data is stored and displayed.
Repeat
Egress
Ingress
User can get into loading system without standing, laying on their back OR their side.
Harness is adjustable to user size.
Harness is easily removed without need for the user to stand.
= harness
= tether
= sliding attachment
= sliding direction
= net force direction
= user lean direction
Top-Down View
User leans
Notes: User can be on their side (Leans front to back) OR User can be on their back (Leans side to side) → Trains proprioceptive function
Mention the details of things (yellow = actuator, tethers are connected to sand bags) and mention that the detail will be covered later.

## Slide 10: Top-Level Overview
Top View
Iso View
Front View
Test Environment
Loading Mechanism
Safety/Human Factors
Sliding Load Attachment
Notes: SAND BAGS ARE TENSIONING THE SYSTEM, actuators

## Slide 11: Sensors and Controls
BendLabs Angle Sensor
6-axis IMU
Actuator Limit Switches
Actuators
Arduino Portenta H7 and Stepper Motor Controllers (Placed behind Support Surface)
Wireless Network Connection
Server
Tension Sensor

## Slide 12: Functional Block Diagram

## Slide 13: Design Changes
Data Communications
Wheel Placement
Linear
Actuators
Server
Stepper Controller
Bendlabs Sensor
IMU
Sensor Data
Movement Command
Motor Command
Sensor Data
Webpage
120 VAC
Notes: Data is collected by the bendlabs sensors and IMU, then the Arduino uses a PID control loop to compute a required response form the linear actuators. The commanded response is passed to the stepper controller, and the linear actuators are moved. Meanwhile, the collected data is transmitted to the server via a wireless network connection and stored. The client can access the webpage via a computer or mobile device, to view and download the data

## Slide 14: Critical Project Elements
α
γ
2) Sliding Load Attachment Speed
Thrust Bearing
Ball Bearings
Friction Mitigation
Pulleys
F2 | The device shall generate a gravity vector that does not deviate greater than an angle of 2 degrees from the true perpendicular to the support surface | Angle Measurement
F3 | The device shall allow for user postural sway by limiting the coefficient of friction present opposite to the direction of sway to 0.3 | Friction Measurement
Notes: Talk about why these are critical:
The person will feel too much force in their lean and thus the test will not be accurate to seeing if a perpendicular gravity vector is a necessary change in ISS technology
If the sliding load does not keep up with the user, there will be slack in the cables, thus pulling the user in the opposite direction to the lean, and this will ruin the test to see if a perpendicular gravity vector is a necessary change in ISS technology (just like before)

## Slide 15: Schedule

## Slide 16: Phase 1: Manufacturing & Component Tests
Brackets
Assembly
Aluminum Tubing
Plywood & Sheet Metal
TRR
AIAA
Structural Testing
Linear Actuator Assembly & Testing
Sensors, Data Storage, Software, & User Interface

## Slide 17: Phase 1: Manufacturing & Component Tests
Manufacturing Team:
Brackets
Assembly
Aluminum Tubing
Plywood & Sheet Metal
TRR
AIAA
Structural Testing
Linear Actuator Assembly & Testing
Sensors, Data Storage, Software, & User Interface
Task | Status
Brackets | Complete
Aluminum Tubing | Complete
Plywood/Sheet Metal | Complete
Assembly | 3/2
Structural Testing | 3/7

## Slide 18: Phase 1: Manufacturing & Component Tests
Brackets
Assembly
Aluminum Tubing
Plywood & Sheet Metal
TRR
AIAA
Structural Testing
Linear Actuator Assembly & Testing
Electronics & Software Team:
Sensors, Data Storage, Software, & User Interface
Task | Status
Machine Shop Submission | Complete
Arduino to Cloud Connection | Complete
Display GUI | Complete
Angle Sensor Reading | Complete
Load Sensor Testing | 3/7
Linear Actuator Control | 3/7

## Slide 19: Phase 2: System Integration & Test
System Assembly
Inspection
System Verification: Loads, Angle Margin, & Friction
SFR
Final Report
Symposium
System Assembly:
Join Structure & Electronics (3/6-3/14)
  Install Linear Actuator Assembly
  Install Tether through system

## Slide 20: Phase 2: System Integration & Test
System Assembly
Inspection
System Verification & Validation: Loads, Angle Margin, & Friction
SFR
Final Report
Symposium
System Test (3/15-4/8)
  Human Testing (Load & Angle)
  Friction Test
  To be completed 1-2 weeks before SFR
System Verification & Validation:
Verification by Inspection (3/15-3/20)
  Functional Requirements 4-8

## Slide 21: System Verification & Validation Schedule
 | Inspection (FR 4-8) | Load Direction & Magnitude (FR 1-2) | Friction (FR 3)
Week 1 (3/15-3/21) | Complete | Attempt test, expect roadblocks | Attempt test, expect roadblocks
Week 2 (3/22-3/28) |  | Resolve issues, attempt test | Resolve issues, attempt test
Week 3 (3/29-4/4) |  | Repeat test 5x with 3 different individuals and edge case | Repeat test 5x or more
Week 4 (4/5-4/8) |  | Margin | Margin

## Slide 22: Critical Path
Test Environment Fabrication
Test Environment Verification
System Verification
Assembly
Mitigation:
Ordering components early
Front loading work week
Alternate procurement
  Additional Brackets

## Slide 23: Test Readiness

## Slide 24: Testing Overview
Major System Verification Tests
  Force Magnitude
  Force Direction
  Friction
Component Verification Tests (in Appendix)
  BendLabs Angle Sensors
  IMU Sensor
  Hanging Scale
  Software Motion Control
Minor System Verification Tests (in Appendix)
  Structural Integrity
  User Safety
Notes: This is a simple overview of the tests we plan to conduct with the GOATSES device. The first three shown in bold are most important and will be covered shortly. The rest of the tests are covered in the appendix, but in the interest of time will not be covered in the main presentation.

## Slide 25: Force Magnitude
= Fg = muserg ± 10 N
BendLabs Angle Sensor
6-axis IMU
Actuator Limit Switches
Direction of Earth gravity
⍺
ꞵ
F1
F2
Purpose: Validate customer need for simulated gravity force and verify requirement F1.4
F1.4: The net load on the user shall not deviate from its original value by more than ± 10 N
Crane Scale
Notes: (WHY) Purpose: Our first requirement simply dictates that the device provides a simulated gravity force on the user not to exceed 1.3 kN. However, in order for the user to feel a consistent and true-to-reality gravity force, the simulated gravity force magnitude must stay within our required bounds as demanded by functional requirement F1.4. These bounds are as shown here, plus or minus 10 N from the user’s weight force.
Equipment: This test will be conducted upon complete assembly of the GOATSES device, and after the device’s safety has been verified. Additionally, it will take place in room N200 of the aerospace building and will require multiple team members to record data or stand in as the user.

## Slide 26: Force Magnitude - Test Procedure
Record known constants
Enter data into Arduino software
User performs multiple trials of postural sway
User position data is recorded throughout
Calculate and compare results to predicted model
= Fg = muserg ± 10 N
BendLabs Angle Sensor
6-axis IMU
Actuator Limit Switches
Direction of Earth gravity
⍺
ꞵ
F1
F2
Crane Scale
Notes: (HOW)
First, known constants will be recorded. These include the user’s weight, the height at which the tethers attach to the harness, and the weight of both sand drums which are measured by in-line crane scales and contribute forces F1 and F2.
Next, these constants will be entered into the Arduino software to be used for calculations during test. Then, the device’s user will perform multiple trials of postural sway in both the forward-backward and side-to-side directions. The two angle sensors as well as the 6-axis IMU will capture data throughout the test duration which will be used in real-time to control the linear actuators which work to keep the force magnitude and direction both constant. Finally, upon completion of the test, the sensor data and calculated data will be compared to a model prediction of the device to measure how the device performs with regard to the plus or minus 10 Newton bounds.

## Slide 27: Force Magnitude - Results
Fg = F1cos(⍺) + F2cos(ꞵ)
= Fg = muserg ± 10 N
BendLabs Angle Sensor
6-axis IMU
Actuator Limit Switches
Direction of Earth gravity
⍺
ꞵ
F1
F2
Crane Scale
Notes: (WHAT WE GET, HOW WE GET IT, WHAT WE WANT)
The aforementioned angle sensors and IMU will provide the Arduino with angle data. First, we assume that the applied force is perfectly perpendicular to the support surface. Then, with this angle data, the Arduino performs a bit of trigonometry to determine these angles, alpha and beta, throughout the duration of the entire test. Then, since we know the constants F1 and F2 by measuring the weights of our sand drums that connect to the tethers, the Arduino simply uses this equation here for Fg to calculate our applied force magnitude throughout the entire test. Thus, our results for force magnitude shall look like this example graph on the left.

## Slide 28: Force Magnitude - Error Quantification
Monte Carlo simulation (2000 runs) using derived uncertainties and the Universal Test Subject (73 kg, 108 cm) for user measurements
Force magnitude must remain within required +/- 2.25lbf (10 N) tolerance
Further accuracy pending component test values
Notes: To quantify the errors associated with our Force Magnitude test, we designed and executed a MC sim for 2000 runs using derived uncertainties and Universal Test Subject measurements for the user. All uncertainties included in this Monte Carlo simulation were derived from physical measurement uncertainties, sensor sensitivities, and linear actuator worst case response times. Furthermore, compounding uncertainties were summed in quadrature. As I mentioned earlier, our F1.4 requirement dictates that the force magnitude remains within 10 Newtons of our desired load, and as you can see in the results shown here on the right, the load almost never strays from our bounds and even 1 standard deviation is still quite close to our desired load. Still, the accuracy of this error quantification can and will be improved upon completion of our scheduled component tests

## Slide 29: Force Direction
±2°
Direction of Earth gravity
Actuator Limit Switches
BendLabs Angle
Sensor
6-axis IMU
Purpose: Validate customer need for simulated gravity force direction and verify Functional Requirement 2
F2: The device shall generate a gravity vector that does not deviate greater than an angle of 2 degrees from the true perpendicular to the support surface
Notes: Purpose:
Ensure the system meets requirement F2
  The applied force is within 2 degrees of normal to the support surface
Ensure proper integration of system electronics, software, and structure
Test Equipment:
Complete assembly of GOATSES
Humanoid dummy mass (anthropomorphic shape)

## Slide 30: Force Direction - Result
Dummy motion will be compared to the modeled Universal Test Subject
  0.5 hz sine wave motion (with a maximum lean angle of 7.6°)
F2: “The simulated gravity force must stay within 2 degrees of normal to the support surface at all times”

## Slide 31: Force Direction - Test Procedure
BendLabs Angle
Sensor
6-axis IMU
Actuator Limit Switches
±2°
Direction of Earth gravity
Record known constants
Enter data into Arduino software
Load dummy into harness, attach tethers
Begin streaming IMU and BendLabs data
Collect 30s of baseline data
Swivel diving board in side-to-side lean motion for 30s
Repeat
Verify direction of force requirement

## Slide 32: Force Direction - Error Sources
Device | Time Budget |  | Error Budget
Arduino Portenta H7 | 5 ms |  | 0°
Drylin ZLN-40 linear actuator | 30 ms |  | 0.1004°
Bendlabs 1-Axis Evaluation Kit | 5 ms |  | 0.18°
Total | 40 ms |  | 0.2804°
Required | 84.03 ms |  | 

## Slide 33: Force Direction - Test Success
±2°
θ
*Not actual collected data
Notes: Actual user lean (theta) found with harness mounted 6-Axis IMU, this will be compared with the angle output by the Bendlabs angle sensors to determine the direction of the force vector applied to the user. The error, which is required to be within 2 degrees, will be found by analyzing and comparing the sensor values, and is a result of the previously discussed time delays and sensor inaccuracies.

## Slide 34: Friction
Thrust Bearing
Ball Bearings
Pulleys
Purpose: Validate analytical model and verify Functional Requirement 3
F3: The device shall allow for user postural sway by limiting the coefficient of friction present opposite to the direction of sway to 0.3

## Slide 35
Friction - Pulley Location
35
User Leans
User leans
SLA translates and Tether adjusts via pulley system
Note location of pulleys
Notes: Note the 4 total pulleys for each respective tether

## Slide 36: Pulley Friction
Build Test Stand
Install tether
Center tether so that buckets are at identical heights
Incrementally add weight to one side until system displaces
x+dx
x
Notes: Introduce pulley testing and narrate the shiz out of it

## Slide 37: Friction - Test Setup
Testing fixture with 90 degree pulley
Tether connects to left side of diving board shown in RED
  Other end of pulley connected to counter weight, labelled “X”
Dummy load placed on rotating diving board to simulate user’s weight
X
Pulley
Tether
Testing Load
Dummy Load

## Slide 38: Friction - Testing
As we load the counterweight
  Diving board rotates at some minimum testing load “X”
Then we have
Where WLOAD is just the Dummy Load
Functional Requirement 3 requires this coefficient is always less than 0.3
X
Pulley
Tether
Note: X represents the minimum input force from user required to overcome friction and “fall”
Dummy Load
Testing Load
Notes: This Functional requirement 3 is want we want to “verify”

## Slide 39: Friction - Test Review
Potential Errors & Assumptions
  Location / height of perpendicular tether connection is assumed to be the CG of user
  Dummy load is a point load, whereas real users represent a distributed load
  Testing Load error
  Friction in the testing fixture pulley
X
Pulley
Tether
Dummy Load
Testing Load

## Slide 40: Friction - Model Review
We expect this test to validate the trend shown in this figure, derived from the model also shown
A successful test verifies Functional Requirement 3, where all data points taken have friction coefficients less than 0.3 for all tested user weights
Notes:   Analytical model predicts a higher friction coefficient for lighter users
  From the model, describe which variables / knobs can be adjusted to help our FR (critical elements of design)

## Slide 41: Budget

## Slide 42: Current Budget Overview
Team is still under budget of with almost all structural material
Shipping costs have significantly increased from the estimates calculated in the Fall
Estimated $1,000 of items (w/ shipping) yet to be purchased with a current $1,600 of budget left
Remaining Margins:
  Structural: -$275
  Electrical: $247
  Loading System: $1200
  Actuator System: $217
  Safety Systems: $227
Notes: Key items yet to be purchased: All harness and safety equipment, Actuator carriage off the shelf items, Sandbags, Pulleys and rope, “Diving Board” material
Say when we’ll buy the stuff that we’ll need left.
State the current level of risk
Add in what’s still outstanding to purchased and lead times (key items

## Slide 43: Appendix

## Slide 44: Force Direction Test
Purpose:
Ensure the system meets FR 2
  The applied force is within 2 degrees of normal to the support surface
Ensure proper integration of system electronics, software, and structure
Test Equipment:
Complete assembly of GOATSES
Humanoid dummy mass (anthropomorphic shape)
GOATSES Project space
BendLabs Angle
Sensor
6-axis IMU
Actuator Limit Switches
±2°
Direction of Earth gravity

## Slide 45: Sensor Verification
Confirming advertised sensor accuracy
Understanding sensor usage and implementation
6-Axis IMU:
Collect range of Gyroscope angle measurements at known angles, analyze error
BendLabs Angle Sensor:
Measure and collect data for incremental known angles using a high-tolerance granite flat surface and machinist angle blocks
30°

## Slide 46: Motion Control Verification
*Not actual data
Confirm software and circuitry is able to communicate with and control the motor driver such that the actuator translates accordingly
Ensure the actuator translates with expected delay, speed, and accuracy
Will feed pre-built lean profile angles into the PID control law and send output commands to the Actuator
Will measure the delay between data receival to command completion, actuator speed, and actuator translational accuracy (to PID output command)

## Slide 47: Crane Scale Verification
Purpose:
Ensure crane scale is accurate to within 0.1 pound so that force magnitude can be accurately calculated
Test Equipment:
Both crane scales, bucket, water, measuring cup
Test Procedure:
Hang up crane scale
Weigh bucket several times. Ensure weight is equal each time
Fill bucket with water in 1000 mL increments
Ensure weight value rises 2.2 pounds each time
Results:
Crane scale passes test if value rises a uniform 2.2 pounds with each addition of 1000 mL water
X.X

## Slide 48: Structural Testing
Purpose:
Ensure weakest aspects of GOATSES assembly can withstand operating stresses
Test Equipment:
GOATSES test environment pre-final assembly
Sand drum (filled with sand)
Test Procedure:
Fill sand drum to max capacity (225 pounds)
Place sand drum on support surface
Check for any visible deformation
Repeat 3 & 4 for diving board and translation table
Results:
Weakest parts of assembly are plywood components. If these components show no sign of deformation under high stresses, structure passes test
1
2
3

## Slide 49: Safety Verification
Purpose:
Ensure system meets requirement F6 and components providing user safety are robust
Test Equipment:
GOATSES harness, D-rings, and snap shackles
Crane scale
Sand drum (filled with sand)
Pulley
Cable
Test Procedure:
Fill sand drum to max capacity (225 pounds) and support it underneath
Connect cable to harness material
Release sand drum support
Check for visible deformation
Repeat for D-rings and snap shackles
Results:
If these components show no sign of deformation under high stresses, safety components pass test
Device tested
Static support
Sand drum (225 lbs)

## Slide 50: Friction Model Derivation - Bearings

## Slide 51: Friction Model Derivation - Bearings

## Slide 52: Friction Model Derivation - Pulleys

## Slide 53: Universal Test Subject
50th Percentile American Male, NASA Handbook
(APPENDIX B) [7]
Height: 171.6 cm
Weight: 73 kg
CoM: 103.1 cm
Depth: 24.65 cm
Foot Size: 26.05 cm
Lean Max: 7.6º
Postural Sway of the Human Subject is modeled by 0.5 hz sine wave, as per Dr. Temple’s research.
Back/forth displacement of the Universal Test Subject is assumed to be modeled as a pendulum swing, modeled in MATLAB.
Notes: dr clark used a pendulum w/ .5 hz sine wave with 10 degree amplitude. It’s an assumption: we want to do humans: we MODEL sway as pendulum sway. Mention that these are not worst case (except for the angle)

## Slide 54: Universal Test Subject
50th Percentile American Male, NASA Handbook (APPENDIX B) [7]
Height: 171.6 cm
CoM: 103.1 cm (Up From Foot)
Shoulder Width: 46.95 cm
Torso Width: 38.4 cm
Depth: 24.65 cm
Foot Size: 26.05 cm
Lean Max: 7.6º
Sway Max: 5.4º
Weight: 73 kg
Notes: Add in dr clark about the pendulum .5 hz sway assumption: we want to do humans: we MODEL sway as pendulum sway

## Slide 55: Safety - Harness and Padding
Harness:
Webbing: Polypropylene, 2”width, supporting 1080 lbs AND Nylon, 1”width, supporting 1415 lbs.
Sliders: Supporting 500 lbs, D-rings: Supporting 1000 lbs.
Padding:
Polyurethane foam, 2” thick
Secondary visual (Eli ideas)
Slackline:
D-Ring: ¼” mounted D-rings, supports 1,200 lbs.
Tether: ¼” Vectran rope, supports 1,600 lbs.
Notes: Grip tape for foot support
Harness design/manufacturing methods
Harness load distribution + adjustability
Slackline system design
Padding for comfort overview

## Slide 56: Loading Mechanism - CAD
Sand-filled Barrel
Force Application Tether
Swiveling Pulley
Stationary Pulley
50.875”
23.875”
30.5”
15.75”
Motion

## Slide 57: Software Team Breakdown
Actuator Control Team
Develop encapsulated function(s) to control the linear actuator position given a desired position
Sensor Data Collection Team
Develop encapsulated function(s) to query and collect data from angle sensors and body mounted IMU
GUI & Matlab Interface Team
Develop a Graphical User Interface in Matlab designed to display test data and develop a simple method for Matlab to Arduino Connection
Control Algorithm Team
Develop encapsulated function(s) to compute the required actuator movement given current measured angle
Software Systems Team
Coordinate the integration of all subsystems
Notes: We can clean up this diagram, but this is the idea

## Slide 58: Sensors and Controls - Component Choices
Microcontroller
Arduino Portentia H7
Angle Sensors
Bendlabs 1-Axis Soft Flex Sensor
Actuator Motor Controller
drylin D7 stepper motor output stage
Body IMU sensor
DFRobot SEN0386
Notes: We can clean up this diagram, but this is the idea

## Slide 59: Chosen Sensor Specs
BendLabs 1-Axis Evaluation Kit
  High precision
  Low power
  Wireless option
  Interfaces with Arduino or LabView DAC
  High Refresh rate
  Relatively expensive

## Slide 60: Chosen Sensor Specs
Arduino
  Arduino Portentia H7 for computations and actuator command
  Dual Cores for simultaneous Processing and command

## Slide 61: Chosen Actuator Specs
Actuator Specs:
  350mm stroke length
  NEMA-17 Motor with torque of 0.5 Nm
  Acceleration controlled by controllers
  48 VDC power input at 1.8A
  Capable of speeds greater than required

## Slide 62: Software Control Block Diagram

## Slide 63: Server GUI
*Not actual data

## Slide 64: Engineering Budgets
Component | Power (W)
6-Axis IMU | 0.132
BendLabs Angle Sensor | 0.00132
Stepper Controllers | 172.8
Total: | 172.93332
Subsystem | Mass (lb)
Loading Mechanism | ~100 (Unloaded), ~550 (Fully Loaded)
Test Environment | ~178
Sliding Load Attachment | ~18
Total System Mass: | 293 - 716

## Slide 65: Cost Plan Major Items BOM (Structural and Mechanical)
Major Item: | Description | Quantity | Total Cost | Vendor
Structural Beams (10’ Long) | Aluminum 1.5"x1.5" square tubing. .125" Thick. 10’ Long | x20 | $1,290.00 | McMaster-Carr
Structural Beams (8’ Long) | Aluminum 1.5"x1.5" square tubing. .125" Thick. 8’ Long | x6 | $312.36 | McMaster-Carr
Angle Bar | Multipurpose 6061 Aluminum, .125” Thick, 90deg Angle with Round Edge, 1.5” Outside Height, 8’ Long | x2 | $76.98 | McMaster-Carr
Aluminum Bar #1 | .125”x4”x36” 6061 Aluminum | x1 | $18.00 | McMaster-Carr
Aluminum Bar #2 (6’ Long) | .125”x1.5” 6061 Aluminum | x1 | $13.28 | McMaster-Carr
Aluminum Bar #2 (3’ Long) | .125”x1.5” 6061 Aluminum | x1 | $7.57 | McMaster-Carr

## Slide 66: Cost Plan Major Items BOM (Structural and Mechanical CONT.)
Major Item: | Description | Quantity | Total Cost | Vendor
Force Tethers | Low-Stretch Easy-Splice Rope—For Lifting | 1 x 25’ spool | $70.00 | McMaster-Carr
Weights | 50 lb Sandbags | x9 | $35.82 | Lowe’s
Platform Metal | 4’x8’, .032" thick, Aluminum | x1 | $137.23 | Armor Steel
Platform Wood | 4’x8’ Southern Yellow Pine | x2 | $74.36 | HomeDepot
Slewing Bearing | Ring Bearing: Aluminum,30mm Inside Dia,100mm Outside Dia, 29mm Wd | x1 | $238.00 | Grainger
Ball Bearing Castors | 286 lbs Heavy Duty Stainless Steel Ball Transfer Unit | x3 | $65.25 | VXB Ball Bearings

## Slide 67: Cost Plan Major Items BOM (Electrical and Human Factors)
Major Item: | Description | Quantity | Total Cost | Vendor
Linear Actuators | ZLN-40 Linear Actuator | x2 | $354.22 | Drylin Drive Technology
Angle Sensors | 1-Axis Evaluation Kit, Flexible bidirectional sensor | x2 | $199.98 | Bendlabs
Arduino | Arduino Portenta H7 Dual Core Microcontroller | x1 | $103.40 | Arduino
Stepper Motors | TB67S249FTG Stepper Motor Driver Carrier - Full Breakout 47V at 1.7 A, NEMA 17 | x2 | $23.90 | Pololu
Mattress Topper | Polyurethane foam, 2”x 22” x 22” | x2 | $17.96 | HomeDepot
Support Surface Mat | Plywood Board | x1 | $37.00 | HomeDepot

## Slide 68: Cost Plan Current Budget Outlook Spreadsheet
Category | Fall Budget | Fall Cost Estimate | Current Cost (as of 2/14/22) | Remaining Margin (as of 2/14/22)
Structural Material | $2,250 | $1,847 | $2,482 | -$232
Electronic Components | $1,300 | $1,253 | $1,053 | $247
Loading Application Systems | $1,500 | $1,372 | $700 | $800
Actuator System | $750 | $602 | $533 | $217
Safety Material | $200 | $140 | $23 | $117
Total | $6,000 | $5,214 | $4,791 | $1,209

## Slide 69: References

## Slide 70: Presentation References
[1] Garcia, Mark. “Astronaut David Saint-Jacques Is Carried to a Medical Tent.” NASA, NASA, 25 June 2019, https://www.nasa.gov/image-feature/expedition-59-canadian-space-agency-astronaut-david-saint-jacques-is-carried-to-a.
[2] Mulavara, Ajitkumar P., et al. “Locomotor function after long-duration space flight: effects and motor learning during recovery.” \emph{Experimental Brain Research} vol. 202, no. 3, 2010, pp. 649-659 doi: 10.1007/s00221-010-2171-0.
[3] Mars, Kelli. “Analog Missions: Bed Rest Faqs.” NASA, NASA, 26 Mar. 2019, https://www.nasa.gov/analogs/envihab/bed-rest-faqs.
[4] McMaster-Carr,“Fibrous Rope”,McMaster-Carr,https://www.mcmaster.com/fibrous-rope/
[5] Densities of materials. Engineering ToolBox. (n.d.). Retrieved October 5, 2021, from https://www.engineeringtoolbox.com/density-materials-d_1652.html.
[6] Tleto. “Polyurethane Coefficient of Friction.” Gallagher Custom Polyurethane Molding, 29 Oct. 2020, https://gallaghercorp.com/polyurethane-coefficient-of-friction/.
[7] NASA, “Human Integration Design Handbook (HIDH)”, NASA Special Publication SP-2010-3407-REV1, 2014.

## Slide 71: Presentation References
[8] “Friction and Friction Coefficients.” Engineering ToolBox, https://www.engineeringtoolbox.com/friction-coefficients-d_778.html.
[9] “Measuring Stepper Motor holding torque” https://www.applied-motion.com/news/2015/10/dynamic-torque-step-motor-sizing
[10] Fryar CD, Carroll MD, Gu Q, Afful J, Ogden CL. “Anthropometric reference data for children and adults: United States, 2015–2018.” National Center for Health Statistics. Vital Health Stat 3(46). 2021.