## Slide 1: GRASS Test Readiness Review (TRR)
February 21st, 2022 (12:50 - 1:40 PM)
ASEN 4018 - 012 Team 7
Presenters
Carter Mak, Madisen Purifoy-Frie, Trey Taylor, Addison Conzet, Eric Roeck, Wil Edwards, and Ruben Briones
Additional Team Members
Gavin O'Connell, Sam Packard, Cole Sechrist, Marissa Palamara, and Daniel Mathews
Customer
Raytheon Technologies
Faculty Advisor
Prof. Jade Morton
Notes: Carter
Hello and welcome
We’re team GRASS presenting our test design review of our project for Raytheon Intelligence and Space

## Slide 2: Presentation Outline - Example
Schedule
Mission Statement
Budget
Project Overview
Test Readiness
Conops
Software
Electronics and RF
Overview
Cost Plan
Purchase Plan
RF Characterization
Power System Characterization
System-Level Testing
Q&A
Backup Slides
Levels of Success
FBD
Design Solutions
Notes: Carter
An outline with links for your convenience, but you already know what we’re going to talk about today

## Slide 3: Project Overview
Project Overview
Schedule
Test Readiness
Budget
Notes: Carter
Project Purpose and Objective (5%)

## Slide 4: Mission Statement and Motivation
Ground station Ranged Assessment Satellite Simulator (GRASS) will provide Raytheon engineers with a high fidelity and configurable satellite simulator to act as a cooperative target for testing and demonstrating ground stations and ground data systems.
Motivation:
Realistic hardware interactions without testing on sensitive flight hardware
Configurable behavior to exercise ground stations and ground data systems
Notes: Carter

## Slide 5: Concept of Operations - Overview
Notes: Madisen

## Slide 6: Concept of Operations - RF
Notes: Madisen

## Slide 7: Concept of Operations - Mounting
Notes: Madisen

## Slide 8: Concept of Operations - Enclosure
Notes: Madisen

## Slide 9: Primary Project Objectives (Levels of Success)
Link margin of 10 dB, range of 75 km, rate of 2 Mbps over main RF link (within FCC regulations)
GRASS shall be modeled and simulated to operate continuously in Front Range conditions for 6 months and tested to operate for 5 days.
A battery power system will be capable of powering GRASS for 2 days
Subsystem simulators for: Attitude, Orbit, Electrical/Power, Command and Data Handling, and Payload.

## Slide 10: Functional Block Diagram - Full System
2 Mbps
Notes: Madisen

## Slide 11: Structural Hardware Design Solution
Notes: Madisen

## Slide 12: Structural Hardware Design Solution
0.46 m
0.23 m
0.38 m
Heated/insulated enclosure to hold all electronics except antenna
Notes: Madisen

## Slide 13: Electronics Design Solution
Parabolic Dish
Quectel EM06-A LTE Cat 6 M.2 Module - Cellular Modem and GPS receiver
Software Defined Radios (SDR)
LimeSDR and HackRF One
Notes: Madisen

## Slide 14: Electronics Design Solution
Sparkfun Electronics ROB - 14391
Renogy 12V 100Ah Battery
Small USB Webcam
Sparkfun Electronics ROB - 14391
Notes: Madisen

## Slide 15: Electronics Design Solution
ODYSSEY X86J4105800
Storage
Spacecraft Simulator
Notes: Madisen

## Slide 16: Software Flowchart
Software must include Flight Software (FSW)
  Typically several major subsystems:
    Guidance, Navigation, and Control
    Attitude Determination and Control
    etc.
Also must include simulation
  Several behaviors to simulate:
    Orbit
    Attitude
    etc.

## Slide 17: Docker and Software Design Solutions
Custom Code
(Python)
Systems
Tool Kit
KubOS
42
Docker
Software Solutions
each has their own container
Notes: Madisen

## Slide 18: Container Communication
Python
KubOS
Payload Subsystem, ADCS, GNC, EPS, and C&DH
Docker
STK
Communication Service
Output
Input
Legend
Attitude Model, Orbital Model, and Link Model
EPS, ADCS, GNC, and Link Model
42
Docker
Docker
Payload Model, EPS Model, Link Model, and C&DH
Docker
(additional explanation in backup slides)
Notes: Madisen

## Slide 19: Orchestration - Docker Compose
Docker
42
KubOS
Docker
STK
Docker
Python
Docker
Docker Compose
Notes: Madisen

## Slide 20: Critical Project Elements (CPE)
ID | Summary | Motivation
E1 | Housing Unit and Mounting | A robust housing and mounting solution are necessary to protect the hardware when deployed.
E2 | Power and Electronics | Self-sufficiency requires robust and self-powered components.
E3 | RF Link | The link over which a ground station can connect to GRASS is the primary mode of use.
E4 | Software & Satellite Simulation | GRASS must emulate real satellite behavior, so robust and accurate software models are necessary.
E5 | Demo Ground Station | While GRASS will be communicating with Raytheon ground station in operations, a test ground station is necessary for project V&V.

## Slide 21: Project Update
Project Overview
Schedule
Test Readiness
Budget

## Slide 22: Major Hardware In Hand
2m Radio Dish
Project Enclosure
100Ah Battery
radios, test antenna, main computer, heater, miscellany, and more

## Slide 23: Update to Hardware Design
Minor design updates to component mounting solutions for ease of manufacturing

## Slide 24: Schedule
Project Overview
Schedule
Test Readiness
Budget
Notes: Carter
Project Purpose and Objective (5%)

## Slide 25: Schedule - All Tasks
Waited on hardware (unexpected delays, hardware we thought we’d have, etc.)
Shifted plans to prototype software before integrating hardware

## Slide 26: Schedule - Software
Currently testing/delivering Minimum Viable Product for software
Constantly developing unit tests
Integration/Functional tests in progress (gate for software delivery)
Primary uncertainty is in how much we can complete past MVP
⭐

## Slide 27: Schedule - Electronics and RF System
Already prototyped software for radios, camera/platform, commands/telemetry, etc.
Working through RF and power system characterization
Power system is low risk (no major dependencies)
RF testing is critical to getting to systems testing
⭐

## Slide 28: Test Readiness
Project Overview
Schedule
Test Readiness
Budget

## Slide 29: Major Tests - Subsystems
Test | Expected End Date | Status
Battery Characterization | Feb. 13 | Complete
Power Draw Characterization | Feb. 25 | Not Yet Started
Wired RF Test | Feb. 7 | Complete
Wireless RF Test - Short Range | Feb. 20 | In Progress
Wireless RF Test - Long Range | Feb. 28 | Net Yet Started
Heater Control Test | Feb. 21 | In Progress

## Slide 30: Major Tests - Full System
Test | Expected End Date | Status
Bench Systems Test | Mar. 8 | Not Yet Started
Local Systems Test | Mar. 14 | Not Yet Started
Field Systems Test | Mar. 18 | Not Yet Started
Systems test schedule is aggressive and optimistic
Current plans have all major tests complete before Spring Break
Margin to push systems-level testing after Spring Break

## Slide 31: RF Characterization
Project Overview
Schedule
Test Readiness
Budget
RF
Power
Systems

## Slide 32: RF Testing - General Test Setup
Hardware
Two SDRs (HackRF One and LimeSDR) connected to computers via USB
GNURadio - an interface on computers which allows for configuration of SDRs
Recording incoming received data as in-phase and quadrature data
Variables are:
The medium between the radios
  For wired testing this medium is an attenuator
  For wireless testing this medium is the air between the two antennas
Transmitted power which is adjusted using sliders in GNURadio
Wired Test
Short Range Test
Long Range Test
Notes: Reitrerate what an SDR is, mention GNUradio and what it is as well
Knowns
  Losses through cables, connectors, and attenuators based on manufacturers/materials
  Gains from antenna are known based on manufacturer or simple geometric equations

## Slide 33: RF Wired Testing
DR3.1 GRASS shall have a dedicated half-duplex radio link able to send and received simulated spacecraft communications to/from Raytheon’s satellite ground station in Aurora, CO.
CPE 3: The link over which a ground station can connect to GRASS is the primary mode of use.
Deadline
Feb. 7th
Complete
Six tests with constant power source flowing in either direction sampling 100K samples per second
  Originally set all receiver gains to 0 but the in order for the HackRF to receive any discernible power the RF amplifier had to be turned on and the LimeSDR needed some value for receiver gain
Incremented transmit gain by 5 dB recording each step for 1 second
Recorded power measurements in in-phase and quadrature binary data (processed in MATLAB)

## Slide 34: RF Wired Test Results
These plots show how the received power was related to the transmit power
Each point is the averaged received power based on 100000 samples vs the transmit power recorded at

## Slide 35: Comparison to Expected Power
Compare the relative power relationship in testing to expected power from model
GNURadio values are measured with respect to an arbitrary value as a result of the hardware that can be experimentally determined
Pr = Ptr- Gattenuator - Lcable/connectors

## Slide 36: RF Wireless Testing
100 m
Long Range Milestone
6700 meter line of sight transmission
6700 m
Connect antennas and computers to SDRs
  2 meter parabolic dish to LimeSDR
  15 dB testing Yagi antenna to HackRF One
Short Range Milestone
100 meter line of sight transmission
DR3.1: GRASS shall have a dedicated half-duplex radio link able to send and received simulated spacecraft communications to/from Raytheon’s satellite ground station in Aurora, CO.
DR3.2: A second telecommunications link shall support downlink of simulator diagnostics and uplink of simulator configuration.
CPE 3: The link over which a ground station can connect to GRASS is the primary mode of use.
Deadline
Feb. 28th
Not Started

## Slide 37: Short Range Test - Characterization
Expected received power (Pr) in dBW based on link budget vs transmit power (Ptr)

## Slide 38: Long Range Test - Characterization
Expected received power (Pr) in dBW based on link budget vs transmit power (Ptr)

## Slide 39: Power System Characterization
Project Overview
Schedule
Test Readiness
Budget
RF
Power
Systems

## Slide 40: Battery Test - General Test Setup
Test Setup
Battery connected to Keithley sourcemeter
  Battery is charged to 14.2V and then discharges into the sourcemeter at 4A
  Source meter records terminal voltage and current until the voltage drops to 10.5V
Variables are:
  The voltage of the battery over time
  Battery capacity and voltage curve vs. manufacturer specifications
Measurements
  Battery terminal voltage vs. time
  Discharge current
4A
Dissipated heat
10.5 - 14.2 V

## Slide 41: Electronics Characterization - Battery
Offset is believed to be linked to the difference between the open-circuit voltage and voltage under load
Likely correlates to 50 mΩ internal resistance in the battery
Data is still being processed

## Slide 42: Power Draw Test - General Test Setup
Test Setup
Odyssey connected to benchtop power
  All electronics are connected to the Odyssey and put under expected load
  Current and voltage are measured over an hour and average power drawn is determined
Variables are:
  The average power drawn dependent on the load

## Slide 43: Systems-Level Testing
Project Overview
Schedule
Test Readiness
Budget
RF
Power
Systems

## Slide 44: Overall Systems Test Plan
Purpose: Verify interactions between modules of containerized software in integrated hardware environments using a bottom-up approach
Phases:
Integrated Systems Bench Test
Integrated Systems Local Test
Integrated Systems Field Test
Notes: O what is being tested for (your rationale for performing the test),
O the design of the test fixtures,
O what test equipment and facilities are needed, and
O an overview of the test procedures.
Describe how the test(s) will reduce risk to your project, what results do you expect, and what models will be validated.

## Slide 45: Integrated Systems Bench Test
DR1.1 GRASS shall support operation of all electrical equipment (in Front Range conditions)
DR1.2 GRASS shall accept external power and distribute it to all internal systems as needed
CPE 1: A robust housing and mounting solution is necessary to protect the hardware when deployed
CPE 2: Self-sufficiency requires robust and self-powered components
Purpose:
Demonstrate the capability of all systems to work together coherently in a wired configuration
Plan / Procedures:
Send sample commands, check status of telemetry data throughput and for proper operation of environmental and payload components
Expectation:
Verify power distribution system and subsystem interactions
Deadline
Mar. 8
Not Started
Notes: Eric

## Slide 46: Integrated Systems Local and Field Tests
DR5.1 GRASS shall have a GPS receiver capable of determining its position with sufficient precision for antenna pointing
DR5.2 GRASS shall be deployable by 1-2 people
CPE 3: The link over which a ground station can connect to GRASS is the primary mode of use
Purpose:
Demo ability to connect and interact with GRASS from a ground station
Plan / Procedures:
Initiate connection from ground station
Send sample commands across a short-range, then a long-range radio link
Check status of telemetry data throughput and for proper operation of environmental and payload components
Expectation:
Verify and validate integrated system behavior, performance, and usability in an operational setting
Deadline Mar. 18
Not Started
Notes: Eric

## Slide 47: Budget
Project Overview
Schedule
Test Readiness
Budget
Notes: Carter
Project Purpose and Objective (5%)

## Slide 48: Cost Plan
36% dedicated to margin across expense categories and whole team
Borrowed hardware
  LimeSDR, Antenna Dish, Antenna Stand
$2837.63 that can be used
  $2162.37 spent so far in subteams
  No margins needed yet
Notes: Right where we expected to be

## Slide 49: Purchase Plan/Status
Products Received
HackRF
Odyssey
Enclosure
Battery
Pending Products
Camera
Solid State Relay
Dish Feed
Cellular Modem
Planned Purchases
Wires
Screws
Connections
Rails
Worries: Antenna feed - logistical issues in ordering but fits in budget
Contingency: Use lower quality antenna feed and compensate in models
Notes: What is DRIVING our cost? - Enclosure, HackRF, Battery/Odyssey respectively.

## Slide 50: Acknowledgements
Raytheon Team:
Sheldon Clark and Martin Wilson
Ann & H.J. Smead Department of Aerospace Engineering Sciences:
Prof. Jade Morton, Steve Taylor, and Harrison Bourne
PAB Members
Trudy Schwartz, Katie Rae, Bobby Hodgkinson, Nicholas Rainville,
Chris Roseman, Prof. Xinlin Li
TRR Reviewers:
Prof. Jade Morton, SP4CE, and Emma Markovich
Notes: Carter
We’d like to acknowledge:
our customers at Raytheon for their advice and support
Several folks in the department including our advisor, Prof. Morton, and the full advisory board
Other instructors and professors for their particular support and expertise
And the lovely folks who helped us prepare this presentation, namely Prof. Morton and Colin

## Slide 51: Questions?
Notes: Carter

## Slide 52: Backup Slides

## Slide 53: Table of Contents
RF Characterization Testing
Software Testing
Thermal Characterization Testing
Budget
Electronics Schematics
Test Plan
Levels of Success
Software Diagrams: Design Requirements
Software Diagrams: Flowcharts
Manufacturing
C&DH

## Slide 54: Project Information

## Slide 55: Levels of Success - More Detail
 | Housing Unit and Mounting | Power and Electronics | Radio Link | Software Architecture and Spacecraft Simulation
Level 1 | Support/protect payload and sensitive electrical components for 24 hours while mounted outdoors | Connected to bench power in order to power all subsystems, with an off the shelf pan tilt camera and a GPS receiver | Link margin of 10 dB, range of 75 km, rate of 9600 bps to send commands from virtual ground station and receive telemetry from GRASS (within FCC regulations) | Subsystem simulators for the following: Attitude, Orbital, EPS (battery charge and temperature), Link (CMD&TLM), and payload models
Level 2 | Support/protect payload and sensitive electrical components for 24 hours while mounted on the Front Range | Connected directly to grid power to power all components. | Second telecommunications interface over which supporting datta can be sent | Three-body orbit propagator capable of returning classical orbital elements
Level 3 | Capable of surviving Front Range winter conditions for 5 days | External solar panel battery power system to power GRASS indefinitely on Mount Evans | All data shall be passed by the RF system fully intact at an increased rate of 2 Mbps | Tunable parameters of satellite models shall be configurable via the secondary control link
Notes: Madisen

## Slide 56: Schedule - Full Project

## Slide 57: Schedule - Manufacturing

## Slide 58: Schedule - Testing

## Slide 59: Software Diagrams

## Slide 60: Software Block Diagram: Design Requirements
Python
42
STK
KubOS
Payload Model
Attitude Model
Orbit Model
EPS Model
Link Model
Payload
Subsystem
ADCS
GNC
EPS
C&DH
Docker
Hardware Payload
Radio
Simulation Apps
FSW Apps
Notes: Thanks Marissa ;)
Madisen still

## Slide 61: Software Block Diagram: Design Requirements
42
STK Components
KubOS
Custom Code
Docker

## Slide 62: Software Flowchart

## Slide 63: Software Flowchart

## Slide 64: Software Flowchart

## Slide 65: Software Flowchart

## Slide 66: Testing

## Slide 67: Test Plan - Reminder of Tests
Unit Testing and Component Characterization
Subsystem Verification
System Verification
System Validation
Individual Container Tests
Hardware Fit Checks
RF Characterization
Integrated Systems Test - Lab
Mestaa’ėhehe Mountain Field Test
ConOps, Objectives
High-Level FRs
Low-Level DRs
Thermal Characterization
Electronics Characterization
Software Integration Tests
Electronics Integration Tests
Analysis
Demonstration
Inspection
Test
Verification Methods
Ground Station Integration Tests
Assembly Fit Checks

## Slide 68: Master Test List

## Slide 69: RF Characterization

## Slide 70: Graphs for each Wired RF Run - HackRF One

## Slide 71: Graphs for each Wired RF Run - LimeSDR

## Slide 72: RF Model - Lime Sweep and Received Power vs Distance

## Slide 73: LimeSDR Researched Results

## Slide 74: Software Testing

## Slide 75: Unit Testing
All small “units” of code (class models as an example) are tested using small unit testing scripts based on Python’s unittest module
Tests expected behavior given inputs for small pieces of code
Verifies that the “building blocks” are correct

## Slide 76: Integration Testing
Two levels of integration testing:
Software Only
  Beginning with only one test case, verify software architecture as focus
  Goal is to verify the individual units perform correctly when integrated in the larger system
  No hardware in the loop
Second, for overall system
  Many test cases, verify architecture and hardware interfacing, particularly C&DH software
  On full test bench

## Slide 77: Thermal Characterization

## Slide 78: Thermal Model: MATLAB 3D Steady State
Driving Requirements: The box must be able to operate within expected environmental temperatures (per FR1.1 and DR1.1.2)
MATLAB Model (3D Steady-State)
Outputs: the Watts of heat produced given the surface temperature of the box
Accounts for: conduction, convection, ambient and solar radiation, altitude, etc.
Extreme Conditions: [-20,30]°C, 30mph (48.3 km/h) winds
Expected Conditions: [-10,15]°C, 15mph (24.1km/h) winds
Required Internal Conditions: must be within [0,45]°C
Conclusion:
  Extreme Conditions: ~35 W of heating and ~35 W of cooling required
  Testing Conditions: ~20 W of heating and no cooling required
MATLAB model closely matched previous SolidWorks thermal fluid simulations
Link to model details
Notes: Eric

## Slide 79: Thermal Model Plots
Expected Enclosure Temperature vs. Heat Flux
Notes: Eric

## Slide 80: MATLAB Thermal Model
The model provides a good estimate of what heating and cooling will be required, and it allows for quick changes to parameters of the box and the effects on thermal loads
The assumption of isothermal is not a good assumption as the temperatures of the inside and outside surfaces may vary and be used to simplify calculations
The amount of solar radiation included was a value typically used for determining power produced by solar panels and is a poor indication of infrared heat produced
The model is verified with SolidWorks simulations
3D thermal model using resistances
Assumes isothermal box, steady-state, no snow or rain, constant conductivity emissivity/absorptivity, perfect cube box, box is entirely enclosed by environment (Earth)
Includes forced and natural convection, and heat produced by electronics
Conservative model
  Extreme Temperatures
  Low end night with no electronics producing power, high winds
  High end day with max power by electronics, maximum solar incident radiation

## Slide 81: MATLAB Thermal Model - Cont.
Q̇cond
Q̇cond
Q̇cond
Q̇cond
Q̇conv
Q̇rad
Q̇gen + Q̇thermal
Q̇solar

## Slide 82: MATLAB Thermal Model - Cont.
Nusselt number of a cube: Simplified Analytical Models for Forced Convection Heat Transfer From Cuboids of Arbitrary Shape, Culham et. al.
Natural Convection
Forced Convection

## Slide 83: SolidWorks Thermal Simulation
30 W Electrical Heating
Internal Temperature 77°C
40 W Active Heating
Internal Temperature -3°C
Cold Extremes Sim
Hot Extremes Sim
SolidWorks Simulation
SolidWorks Fluid Simulation
Used as supplement to thermal model
Same conditions as extreme model
More accurate with CAD model and solar radiation specific to Denver, CO
Result
Simulations show that need we both active heating and cooling to in extreme conditions
Cooling introduces complications, boxes with fans have lower ingress protection

## Slide 84: Thermal Characterization Tests
Heater and thermal system characterization testing
  Heater Lab Characterization Test
    Compare models with heat produced in a controlled environment
  Heater Outdoor Characterization Test
    Compare models with varying external temperatures
Objective: Verify MATLAB thermal models
  Heater PID control will use MATLAB models as a baseline for tuning
  Improving thermal models based on test data allows for more efficient heater control
  Gives confidence that the enclosure can protect components from thermal extremes
Notes: Eric

## Slide 85: Thermal Characterization Test - Controlled Environment
Characterization of thermal system in a controlled environment
  Measurements: Temperature sensors measure internal and external (room) temperature
  Test Setup:
    Arduino used to control heater
    Bench power source
Procedure: Steadily provide power to heater until operational limits exceeded.
  Heat produced to internal temperature recorded as primary point of interest
Verification: Compare with expected temperatures corresponding with heat produced from MATLAB model
Deadline 02/18
Not Started
Notes: Eric

## Slide 86: Thermal Characterization Test - Outdoors
Characterization of thermal system in an outdoors environment
  Measurements: Temperature sensors measure internal and external temperatures
  Test Setup:
    Arduino computer used to control heater
    Battery or bench power source
    PID control to keep enclosure at a steady temperature
Procedure: Run PID-controlled heater through varied external conditions
  Control law should maintain internal temperature
  Heat required and external temperatures recorded as primary points of interest
Verification: Compare with expected heat required to maintain a steady internal temperature from MATLAB model
Deadline 02/21
Not Started
Notes: Eric

## Slide 87: Budget

## Slide 88: Purchase Plan
Products Received: HackRF, Odyssey Computer, Enclosure, Battery, Heater, SSD. Vital components with long lead times prioritized in ordering.
Pending Products: Camera, Solid State Relay, Dish Feed. Important for testing but expected to be in hand soon.
Planned Purchases: Wires, Screws, Connections, Rails. Mostly small components with short lead times and low priority.
Worries: Dish Feed - Ordering issues but fits in budget
Notes: What is DRIVING our cost? - Enclosure, HackRF, Battery/Odyssey respectively.

## Slide 89: Cost Plan
Highest estimate under $5000
Added increased margin per subteam
Reduced risks by borrowing components/ project descoping
$5000

## Slide 90: Structures Cost Plan
Current budget plan breakdown for structures

## Slide 91: RF Cost Plan
Current budget plan breakdown for RF

## Slide 92: Electronics Cost Plan
Current budget plan breakdown for electronics

## Slide 93: Electronics Schematics

## Slide 94: Electronics Functional Block Diagram

## Slide 95: Overview Schematic

## Slide 96
10.5 - 12V DC
12V .15 Vpp
Battery
Voltage converter
5V PWM
Arduino Core
Camera
Pan Tilt Servos
Parabolic antenna
Lime SDR
Cellular antennas
GPS antenna
M.2
Cellular modem
Odyssey Computer
Temp Sensor
I2C
USB 2.0
USB 3.0
Power
Data
Both

## Slide 97: Heater Control Circuit

## Slide 98: Temperature Sensor Circuits

## Slide 99: Hardware Software Interfaces
USB 2.0
8 MSPS
USB 3.1 61.44 MSPS
Software
Arduino
Camera
SDR