## Slide 1: Final Oral Review: iMagpie
A Mobile, Person-Portable, SSA Platform
Sponsors: Dr. Marcus Holzinger and Samuel Wishnek
Team Members: Ashkan Bafti, Michael Dynakowski, Frasier Feight, Nathan Herr, Idam Isnaeni, Alison Jarvis, Matthew Melby, Justin Miller, Alexander Pulliam, Charles Puskar, Jordan Reynolds, and Lucas Teigen
Advisor: Dr. Aaron Johnson
ASEN 4028: Senior Projects April 29, 2020

## Slide 2: Presentation Overview
Project Purpose and Objectives
Design Description
Test Overview, Results, and Analysis
Systems Engineering
Project Management

## Slide 3: Presentation Overview
Project Purpose and Objectives
Design Description
Test Overview, Results, and Analysis
Systems Engineering
Project Management

## Slide 4: Project Purpose
iMagpie: A Mobile SSA Platform
  Deployable to remote locations
  Receives observation tasks from CCAR
  Captures image, extracts uncorrelated tracks (UCTs)
  Reports UCTs in real-time back to CCAR
  UCTs used by CCAR for orbital estimation
UCTs = RA and Dec w/ time stamp
Notes: Explain what uncorrelated tracks are
Clarify processed data
CCAR will also process the data

## Slide 5: Customer Objectives and Constraints
Observations
  GEO, MEO, LEO objects
  Magnitude 13 or brighter
Reporting
  System GPS location
  Object RA, Dec, time stamp
    10 arc-second (3σ) accuracy
Operation
  10 hours/night at 3 tasks/min
Mobility
  Weight: less than 20 kg
  Volume: Airline carry-on
[2]
[1]
Notes: http://hyperphysics.phy-astr.gsu.edu/hbase/eclip.html
https://twitter.com/boeingairplanes/status/1086672652150939649
Call this slide customer requirements

## Slide 6
1. Observation denied to traditional observatory
2. iMagpie deploys to off-grid site by hiking, flying, driving, etc.
3. iMagpie assembled and calibrated on-site
4. Autonomous pointing enabled as human rests
5. iMagpie actuates to task-specified attitude
6. iMagpie images object in transit, saves image locally
7. iMagpie processes image to obtain:
Attitude of 10 nearest stars
Attitude of streak start
Attitude of streak stop
8. UCTs, exposure times, & GPS location sent to CCAR via SMS
10. iMagpie solar panels recharge batteries during the day
9. Pointing, imaging, and processing repeats for the rest of the night, up to three observations per minute
11. Night tasking and day recharging continue for mission duration
12. iMagpie disassembled at end of mission and returned to CCAR
Concept of Operations
Notes: Add cadance
Plane/hiking/both

## Slide 7: Levels of Success

## Slide 8: Presentation Overview
Project Purpose and Objectives
Design Description
Test Overview, Results, and Analysis
Systems Engineering
Project Management

## Slide 9: Functional Block Diagram
Notes: Fix animation
Specify task – what is in the data being sent
What is being sent data transmission to processing
Exposure command, pointing command – degrees of freedom
Think through interfaces
FBD can reflect electronics schematic – ok to repeat

## Slide 10: Design Overview
Mount Head
Image Sensor
Tripod
Lens
Solar Panels
Processor Box

## Slide 11: Processor Box Design
Dimensions: 16.5x11.4x14.6 cm
Ambient Sensor
Raspberry Pi 4B
GSM
(GPS/SMS Board)
Notes: Specify that we're calling this out because it has particular requirements – thermal design

## Slide 12: Design Mass and Volume
Metric | Design | Budget | Margin
Mass | 16.4 kg | 20.0 kg | 18%
Volume | 40.2 L | 44.3 L | 9.3%
Notes: Add the 60 liter pack or state that it can fit within – include requirements, check that they are fulfilled
Numbers on figure are difficult to read
Get rid of margins – set dimensions
Mass is too precise (margin in mass)
Add electrical and data schematics
Label key components

## Slide 13: Critical Project Elements
CPE | Motivation
1. Electronics | Tight, self-reliant power budget
2. Structures | Thermal regulation System stability during observations
3. Comms/Controls | Remote commands via SMS Precise observation requirements
4. Image Processing | 3 task/min cadence 10 arc-second (3σ) accuracy
Notes: This is different from CDR
Most important aspect of manufacturing,

## Slide 14: Presentation Overview
Project Purpose and Objectives
Design Description
Test Overview, Results, and Analysis
Systems Engineering
Project Management

## Slide 15: Test Overview
Completed
In Progress
Planned
Propogator Software
Astromety Image Processing
Streak Detection with Sample Images
Mount Head Control
Camera Sensor Control
GSM Communication and Control
Limiting Magnitude Test
Streak Detection with images captured by system
Timing Testing
Thermal Testing
Power System Testing
Full System Testing

## Slide 16: Control System Test
What's being tested?
  Mount Actuation Rate/Accuracy
  Image Sensor Exposure Time
  Image capturing cadence
How is it tested?
  Input processed task to Pi
  Observe/measure actuation
  Time exposure, observe resulting image
Relevant Requirements | 
DR 4.1.2 | Mount command requirement
DR 4.1.3 | Image Sensor command requirement
DR 3.3 | 3 tasks per minute requirement
Test Status
In Progress
Test Location
Aero 140
Notes: Actuation
  rate tested by timing, compared against given value (10 deg/s) (assumed 5 deg/s^2 acceleration)
  Accuracy tested by input of sample image to astrometry, which will provide high accuracy pointing info to test against
Image sensor
  Exposure time included in metadata provided by camera
Cadence
  Tested by timing the total task time

## Slide 17: Control System Test
  "Task Time" (Actuation time + Exposure time)
Requirement Verification | 
DR 4.1.2 | Time actuation and compare final position against Astrometry data
  Actuation accuracy and rate
  Exposure time accuracy
Most Important Results:
DR 4.1.3 | Retrieve exposure length from camera metadata
Notes: Say that actuation accuracy and rate are important, then how they will be tested and how that satisfies 4.1.2
Say that exposure time accuracy is important, then say how this is tested and how that satisfies 4.1.3
Say that “task time” is important for cadence, that it will be shown on the next slide

## Slide 18: Control System – Cadence Model
LEO
GEO
time (s)
Within budget
DR 3.3 | Time tasks of differing slew angles/exposure times, compare to model
Notes: Talk about how actuation rate was going to be tested to verify the data sheet and refine the model
“Worst case” viable tests would be run to verify the model

## Slide 19: Thermal System Test
What's being tested?
  Heater capability to keep lens above dew point
  Capability to keep electronics within operational range
How is it tested?
  Set up observatory inside and IR camera for observation
  Set heaters to 20% power and record thermometer data from all locations as a function of time till steady state
  Repeat in increments of 20% power, then outdoors
Relevant Requirements | 
DR 2.1 | Power independence requirement
DR 7.1 | Thermal requirements of optical components
DR 7.2 | Thermal requirements of electrical hardware
Test Status
Planned
Test Location
Inside/Outdoors
Notes: Thermal System (FOR) - Frasier/Alex
Data Collected:
Temperature of the front lens element, temperature of the image sensor, temperature of the electronics box
Protocol For Testing:
Assemble full iMagpie system
Point thermal camera at the front lens element
Set heaters to 20% capacity at room temperature
Wait for temperatures to reach steady state
Record temperature measured by iMagpie’s internal sensors and thermal camera
Increase power by 20% and repeat previous two steps until 100% power is reached
Repeat experiment outside on cold night
Verification/Validation (what models/metrics we used to verify correctness)
This test allows us to verify the SolidWorks thermal model, and the MATLAB thermal model of the camera/lens system and the electronics box. Additionally, using the thermal imaging camera allows us to qualify the temperature sensors surrounding the front lens element so that its central temperature is known based on the readings from the surrounding temperature sensors. Taking multiple data measurements at different power levels allows us to better calibrate our heating algorithm, and doing the test at two different external temperatures allows us for more data points to compare with our models. A successful thermal system test ultimately verifies iMagpie’s ability to deal with cold temperatures and potential dew buildup.

## Slide 20: Thermal System Test
Most Important Results:
  Lens center temperature versus heater power
  Lens center temperature versus sensor temperature
  Electronics temperature versus heater power
Results help to confirm/refine thermal modeling
Notes: Thermal System (FOR) - Frasier/Alex
Data Collected:
Temperature of the front lens element, temperature of the image sensor, temperature of the electronics box
Protocol For Testing:
Assemble full iMagpie system
Point thermal camera at the front lens element
Set heaters to 20% capacity at room temperature
Wait for temperatures to reach steady state
Record temperature measured by iMagpie’s internal sensors and thermal camera
Increase power by 20% and repeat previous two steps until 100% power is reached
Repeat experiment outside on cold night
Verification/Validation (what models/metrics we used to verify correctness)
This test allows us to verify the SolidWorks thermal model, and the MATLAB thermal model of the camera/lens system and the electronics box. Additionally, using the thermal imaging camera allows us to qualify the temperature sensors surrounding the front lens element so that its central temperature is known based on the readings from the surrounding temperature sensors. Taking multiple data measurements at different power levels allows us to better calibrate our heating algorithm, and doing the test at two different external temperatures allows us for more data points to compare with our models. A successful thermal system test ultimately verifies iMagpie’s ability to deal with cold temperatures and potential dew buildup.

## Slide 21: Thermal System Test
Notes: Thermal System (FOR) - Frasier/Alex
Data Collected:
Temperature of the front lens element, temperature of the image sensor, temperature of the electronics box
Protocol For Testing:
Assemble full iMagpie system
Point thermal camera at the front lens element
Set heaters to 20% capacity at room temperature
Wait for temperatures to reach steady state
Record temperature measured by iMagpie’s internal sensors and thermal camera
Increase power by 20% and repeat previous two steps until 100% power is reached
Repeat experiment outside on cold night
Verification/Validation (what models/metrics we used to verify correctness)
This test allows us to verify the SolidWorks thermal model, and the MATLAB thermal model of the camera/lens system and the electronics box. Additionally, using the thermal imaging camera allows us to qualify the temperature sensors surrounding the front lens element so that its central temperature is known based on the readings from the surrounding temperature sensors. Taking multiple data measurements at different power levels allows us to better calibrate our heating algorithm, and doing the test at two different external temperatures allows us for more data points to compare with our models. A successful thermal system test ultimately verifies iMagpie’s ability to deal with cold temperatures and potential dew buildup.

## Slide 22: Limiting Magnitude Test
What's being tested?
  System's ability to detect dim satellites
How is it tested?
  System is setup to observe stars/satellites
  System observes stellar object of known magnitude
  Process image to extract signal to noise ratio (SNR)
  Compare modelled SNR to actual SNR
Relevant Requirements | 
DR 4.1.2 | Mount command requirement
DR 4.1.3 | Image Sensor command requirement
Test Status
In Progress
Test Location
Aero 140

## Slide 23: Limiting Magnitude Test
Most Important Results:
  SNR of known star versus modelled SNR
Target Object: Betelgeuse
Exposure time: 0.25 s
Magnitude: 5.3
Notes: Thermal System (FOR) - Frasier/Alex
Data Collected:
Temperature of the front lens element, temperature of the image sensor, temperature of the electronics box
Protocol For Testing:
Assemble full iMagpie system
Point thermal camera at the front lens element
Set heaters to 20% capacity at room temperature
Wait for temperatures to reach steady state
Record temperature measured by iMagpie’s internal sensors and thermal camera
Increase power by 20% and repeat previous two steps until 100% power is reached
Repeat experiment outside on cold night
Verification/Validation (what models/metrics we used to verify correctness)
This test allows us to verify the SolidWorks thermal model, and the MATLAB thermal model of the camera/lens system and the electronics box. Additionally, using the thermal imaging camera allows us to qualify the temperature sensors surrounding the front lens element so that its central temperature is known based on the readings from the surrounding temperature sensors. Taking multiple data measurements at different power levels allows us to better calibrate our heating algorithm, and doing the test at two different external temperatures allows us for more data points to compare with our models. A successful thermal system test ultimately verifies iMagpie’s ability to deal with cold temperatures and potential dew buildup.

## Slide 24: Limiting Magnitude Test (Cont.)
Sample of noise near SO (Red Circle)
  Sample size = 20,000 pixels
  Std. Dev. = 29.08 e/pixel
Sample of pixels from star defines signal (Yellow Circle)
  Size of star = ~227 pixels
  Total Signal = 2.67 * 105 e
  SNR = 517
Model Predictions
  Total Signal = 5.52 *105 e
  SNR = 743

## Slide 25: Limiting Magnitude (Cont.)
Conclusions:
  Test not ideal
    Full moon on night of test
    Thin high-altitude clouds
    Higher than average humidity
    Result may not extrapolate well to dim objects
  Modeling predicts noise very well
  Modeling may over-predict object flux

## Slide 26: Image Processing Test
Image Elements
  Acquiring right ascension and declination of near stars
  Acquiring the field's orientation angle
  Acquiring start and stop pixel of streak
Test with sample images & Known celestial coordinates
  Run Astrometry locally, compare results with NASA's database to 10 arc-second accuracy
  Simulate pixel locations and calculate error for 3σ accuracy
  Measure processing time for 3 images/min cadence
Test Location Test Status
Lab In Progress
Relevant Requirements | 
DR 5.1.3 | Identify start and stop RA and Dec of streak
DR 5.1.4 | Determine RA/Dec w/ 10 arc-sec (3σ) accuracy
DR 5.1.5 | Process images at a rate of 3 images per minute

## Slide 27: Image Processing Test

## Slide 28: Image Processing Test
Testing For:
10 arcsec 3σ accuracy (99.7%)
20 second run time
LEO, MEO, GEO
Magnitude -6 - 13
Testing Methodology:
Generated Data
Real Background + Generated Streak
Real Data
  Individual Images
  System Test
Fig. 1: Generated Data
Fig. 2: Real Background + Generated Streak

## Slide 29: Image Processing Test
Start and End Point Error:

## Slide 30: Image Processing Test: Start Point Error
GEO
MEO
LEO

## Slide 31: Image Processing Test: Stop Point Error
GEO
MEO
LEO

## Slide 32: Image Processing Test: 3σ Accuracy

## Slide 33: Image Processing Test: 3σ Accuracy

## Slide 34: Image Processing Test: 3σ Accuracy

## Slide 35: Image Processing Test: 3σ Accuracy

## Slide 36: Image Processing Test: 3σ Accuracy

## Slide 37: Image Processing Test: Timing

## Slide 38: Image Processing Test: Conclusions
Average Error
Average Error:
6.4 arcsec
Average Error:
𝛉: 0.002 radians
Center: 0.001 arcsec
Total Average Error:
6.7 arcsec

## Slide 39: Image Processing Test: Conclusions
Average Timing
Average Time:
0.7 sec
Average Time:
18.0 sec
Total Time:
18.4 sec
Average Time:
0.4 sec

## Slide 40: Power System Test
What's being tested?
  Provide power to all components
  Full recharge abilities
How is it tested?
  Discharge batteries with simulated load
  Expose solar panels to typical amount of sunlight (w/ tracking), see if batteries fully recharge w/ 4 hour margin
Test Location | Test Status
Electronics Lab | Planned
Relevant Requirements​ | 
DR 2.1 DR 2.2 | iMagpie shall be capable of operating under its own power for up to 10 hours. iMagpie shall be capable of recharging its batteries to full capacity during a single day while off the grid.

## Slide 41: Power System Test
Most Important Results
  Voltage levels [V]
    Component voltages are within specified limits
    Battery charge/discharges without risking damage
  Battery capacity [mAh]
    Ensure that plot of capacity available mirrors that of simulated cycle

## Slide 42: Full System Test
Test Location | Test Status
Boulder/ Arestua Hut | Planned
What's being tested?
  Simultaneous V&V of all subsystems in true operational environment
How is it tested?
  Assemble system and calibrate
  Implement tasking software with provided task queue
  Begin autonomous tasking
  Monitor performance periodically
Relevant Requirements​ | 
FR 1​ | System shall be person-portable.​
FR 2 | Independently Powered​
FR 3 | Capture Images of Objects in LEO, MEO, GEO​
FR 4 | Capable of Processing Tasks​
FR 5 | Capable of Processing Images​
FR 6 | Capable of communication with CCAR​
FR 7 | Capable of Operation in Boulder​

## Slide 43: Full System Test
Most Important Results
  Primary mission deliverables:
    Image (with streak) of every tasked object
    RA and dec of start and stop of streak
    Positions of cataloged stars nearest streak
    Start and stop time of each exposure
    GPS location for each exposure
  System performance data:
    Environmental data – temperature and humidity
    Temp sensor data
    Average actuation rate
    Processing rate per task
    Battery levels for entire mission duration
    List of all captured and missed tasks
Solved Astrometry Field
Solved Streak w/ Endpoints

## Slide 44: Full System Test
.
Verifiable metrics by Requirement | 
DR 2.1 | Capable of operating for a full 10 hours
DR 2.2 | Capable of recharging within a single day
DR 3.1.1 | Capable of detecting objects with apparent magnitude of 13
DR 3.3 | Capable of capturing up to 3 tasks per minute
DR 5.1.2 | Identify the 10 catalog stars nearest streak within FOV
DR 5.1.4 | RA and Dec of object determined with 3-sigma accuracy
DR 7.1 | System shall remain above dew point

## Slide 45: Presentation Overview
Project Purpose and Objectives
Design Description
Test Overview, Results, and Analysis
Systems Engineering
Project Management

## Slide 46: Systems Engineering Approach
[xx]
Notes: https://en.wikipedia.org/wiki/V-Model

## Slide 47: Expected Risks: Software
Primary Software Risks
  Processing timing/capabilities
  Inaccuracy of provided data and corresponding results

## Slide 48: Expected Risks: Hardware
Primary Hardware Risks
  Components performing worse than provided specifications
  Overheating/condensation of components

## Slide 49: Encountered Risks
Software
  No encountered risks, software met requirements
Hardware
  Fragile solar cells prevented execution of first solar panel design
  iOptron mount head used proprietary interface
  Defective ZWO imaging sensor
  Mount head reassembled incorrectly by team member

## Slide 50: Systems Engineering: Lessons Learned
Plan and verify interface control early
  Prevent usage of extra time/budget
Document disassembly/reassembly of components
  Expedite fault correction process
  Maintain warranty for faulty components
Plan for large budget margins
  Allows project to continue w/ initial design faults
Use Legacy/COTS where available
  Reduces cost, typically increases reliability

## Slide 51: Presentation Overview
Project Purpose and Objectives
Design Description
Test Overview, Results, and Analysis
Systems Engineering
Project Management

## Slide 52: Project Management: Organization Chart

## Slide 53: Project Management
Weekly full team meetings
  Subteam progress on delegated tasks
  Individual contributions over past week
  Questions/concerns to bring up w/ customers or advisors
  Upcoming deadlines and delegation of new tasks
Weekly advisor meetings
  Discuss full team progress
  Verify expectations and execution of deliverables
  Discuss questions/concerns
Customer meetings
  Need-by-need basis to discuss questions/concerns

## Slide 54: Project Management: Lessons Learned
Planning
  Planning deadlines w/ margin for unexpected obstacles
  Thinking ahead to prevent work discontinuities
Communication
  Clarification of expectations with customers and advisors
  Clear and concise communication of expectations/deadlines to team members
  Clear delegation and chain of responsibility

## Slide 55: Financial Budget
Subsystem | Expected Cost | Budget | Cost | Budget
Processing | $610 ​ | $725 ​ | $580 | $625
Power | $241 ​ | $275 ​ | $520 | $575
Mount | $1,266 ​ | $1,400 ​ | $1,383 | $1,385
Optics | $1,883 ​ | $2,000 ​ | $1,934 | $1,940
Thermal | $192 ​ | $300 ​ | $210 | $225
Manufacturing/ Testing | $102 ​ | $250 ​ | $156 | $200
Transportation | $43 ​ | $50 ​ | $50 | $50
Total | $4,337 ​ | $5,000 ​ | $4,834.23 | $5,000
CDR Budget
Final Budget

## Slide 56: Significant Budget Differences
EPS Subsystem
Underestimate of needed materials and costs
Manufacturing solar panels proved too difficult, replacement COTS solar panels were needed
Processing Subsystem
Small auxiliary items were not included in budget due to oversight
Satellite communication capabilities had to be abandoned due to high repeating cost
Notes: Power
  Underestimate of overall items and costs
    Things like PCB, electrical components, etc.
  Solar panels cost $215 instead of $40 and assembly
Processing
  Items such as sensors, LED screen, and testing cable
  Satellite gear would have cost around $350 + Usage plan
    This money was needed in other areas
    Abandoning this only cost us level 3 success

## Slide 57: Estimated Industry Cost
Total Team Hours
  3501 Hours*
Overhead of 200%
  $218,812.50
Assume average starting salary of $65,000 for 2,080 hours or $31.25/hour
Cost of Work
  $109,406.25
Material cost
  $4,834.23
Total Cost of iMagpie: $333,052.98
*Including 4 weeks of projected additional work
Notes: True Hours of completed work: 3001 hours
  Average of 125.04 hours per week
4 weeks of work were added
  500 hours

## Slide 58: Acknowledgements
Dr. Marcus Holzinger and Samuel Wishnek
Dr. Aaron Johnson
Project Advisory Board

## Slide 59: Questions?

## Slide 60: References
[1] “Ecliptic Plane”, Hyperphysics, http://hyperphysics.phy-astr.gsu.edu/hbase/eclip.html
[2] Boeing Airlines https://twitter.com/boeingairplanes/status/1086672652150939649
[3] PCBWAY IOTBITS LOGO http://iot-bits.com/iotbits/pcbway-iotbits-logo/
[4] "Lithium Ion Battery – 6Ah", Sparkfun https://www.sparkfun.com/products/13856
[XXI] AVM Standard https://www.virtualastronomy.org/AVM_DRAFTVersion12_rlh02.pdf

## Slide 61: RA/Dec Coordinate Transform
Where CROT angles, Center Right Ascension, and Center Declination are provided from astrometry algorithm
XXI

## Slide 62: Design Requirements

## Slide 63: Design Requirements (cont.)

## Slide 64: Design Requirements (cont.)

## Slide 65: Design Requirements (cont.)

## Slide 66: Test Backups

## Slide 67: Image Processing Error Calculation
Assume cos(𝛉)=sin(𝛉) = 1
𝛅𝛉 = 0.00174533
𝛅x = 𝛅y = 4.53
x= 3250, y = 4656

## Slide 68: Streak Detection Testing

## Slide 69: Streak Detection Testing

## Slide 70: Streak Detection Testing

## Slide 71: Streak Detection Testing

## Slide 72: Streak Detection Testing

## Slide 73: Streak Detection Testing

## Slide 74: Streak Detection Testing

## Slide 75: Streak Detection Testing

## Slide 76: Streak Detection Testing

## Slide 77: Camera Manufacturer Specifications
Resolution: 16Mega Pixels 4656×3520
Pixel Size: 3.8µm
Exposure Range: 32µs-2000s
Interface: USB3.0/USB2.0
Read Noise: 1.2e @30db gain
Full well: 20ke
Dimensions: φ62mm X 41mm
Weight: 140g
Working Temperature: -5°C—45°C
Working Relative Humidity: 20%—80%

## Slide 78: Battery Charging Testing
What's being tested?
  Ability for batteries to recharge at required rate
Risk Reduction:
  Ensures iMagpie will have the required margin to recharge batteries during a sunny day
Relevant Requirements | 
DR 2.2 | iMagpie shall be capable of recharging its batteries to full capacity during a single day while off the grid.
Test Status
Being Planned

## Slide 79: Battery Charging Testing
Test Fixtures:
  Battery connected to charger IC, and then DC power supply
Test Procedure Overview:
  Drain batteries to safe low voltage
  Recharge at required rate to satisfy worst case charge times
Results:
  Batteries should be able to recharge in approximately 7h, allowing margin for sub-ideal weather
Required Equipment
Multimeter, DC power supply
Testing Facility
Electronics Lab

## Slide 80: Thermal Testing
What's being tested?
  Ability of iMagpie's heating system/insulation
  Characterization of heating to compare to model
Risk Reduction:
  Ensures that iMagpie can prevent dew buildup and keep hardware above minimum temperatures
Relevant Requirements | 
DR 7.1 DR 7.2 | iMagpie's optics shall stay above dew point IMagpie's hardware shall be kept within operational ranges
Test Status
In Planning

## Slide 81: Thermal Testing
Test Fixtures:
  Lens/Sensor
  Thermal camera or temperature probe
Test Procedure Overview:
  Heat iMagpie at room temperature until steady state
  Measure optics temperatures
  Compare to modeling
  Repeat outdoors in colder temps
Results:
  Thermal profiling of system
  Heating system verification
Required Equipment
Sensor/Lens Thermal Camera Laptop
Testing Facility
Aero Building

## Slide 82: Timing Testing
What's being tested?
  Characterization of exposure timing
Risk Reduction:
  Ensures that iMagpie can report exposure start and stop times to 0.1 microseconds
  Increases accuracy of streak data
Relevant Requirements | 
DR 4.1.4 DR 4.1.5 | iMagpie shall take exposures at the commanded time iMagpie shall record the start and stop times of exposures
Test Status
Planned

## Slide 83: Timing Testing (Cont.)
Test Fixtures:
  FPGA With 10bit LED counting ability
  Raspberry Pi with GSM
Test Procedure Overview:
  Rasp. Pi records GPS time
  Rasp. Pi sends exposure command to camera
  Rasp. Pi records GPS time
  Rasp. Pi sends start command to FPGA
  FPGA begins to count on LEDs
  Camera takes exposure of LEDs
  LEDs along with GPS timestamps reveal exposure delay
Results:
  Start and stop times of exposure precisely known (exposure duration assumed accurate)
Required Equipment
Sensor/Lens Timing Circuit Raspberry Pi GSM Waveform Generator
Testing Facility
Electronics Lab

## Slide 84: Timing Testing (Cont.)

## Slide 85: Communications System Test
What's being tested?
  SMS Send/Receive
  Status Report
How is it tested?
  Send/Receive sample SMS to/from outside device
  Check Status Report info against known info
Relevant Requirements | 
DR 6.1 | Receive Task requirement
DR 6.2 | Send data requirement
Test Status
In Progress
Test Location
Aero 140

## Slide 86: Electronics Schematics Backup

## Slide 87: Electronic Schematic

## Slide 88: Electronic Schematic (cont.)

## Slide 89: Electronic Schematic (cont.)

## Slide 90: Electronic Schematic (cont.)

## Slide 91: Electronic Schematic (cont.)

## Slide 92: Electronic Schematic (cont.)

## Slide 93: Electronic Schematic (cont.)

## Slide 94: Electronic Schematic (cont.)

## Slide 95: Battery Charger IC Schematic

## Slide 96: Apparent Magnitude
Measure of objects brightness as seen from Earth
  Reverse logarithmic scale
  Magnitude of 5 greater = brightness 100 times dimmer
  Magnitude 13 is ~400 times dimmer than naked eye limit
iMagpie Design Goal
[xx]
Notes: https://www.cambridge.org/core/books/question-and-answer-guide-to-astronomy/stars-and-stellar-systems/CFD8F55B5EF1FD7608CA2EDD8E1FCD3E

## Slide 97: Team Photo