## Slide 1: Test Readiness Review: iMagpie
A Mobile, Person-Portable, SSA Platform
Sponsors: Dr. Marcus Holzinger and Samuel Wishnek
Team Members: Ashkan Bafti, Michael Dynakowski, Frasier Feight, Nathan Herr, Idam Isnaeni, Alison Jarvis, Matthew Melby, Justin Miller, Alexander Pulliam, Charles Puskar, Jordan Reynolds, and Lucas Teigen
Advisor: Dr. Aaron Johnson
ASEN 4028: Senior Projects March 2, 2019

## Slide 2: Presentation Overview
Overview
Schedule
Test Readiness
Budget

## Slide 3: Presentation Overview
Overview
Schedule
Test Readiness
Budget

## Slide 4: Project Purpose
iMagpie: A Mobile SSA Platform
  Deployable to remote locations
  Receives observation tasks from CCAR
  Captures image, extracts uncorrelated tracks (UCTs)
  Reports UCTs in real-time back to CCAR
  UCTs used by CCAR for orbital estimation
UCTs = RA and Dec w/ time stamp
Notes: Explain what uncorrelated tracks are
Clarify processed data
CCAR will also process the data

## Slide 5: Customer Objectives and Constraints
Observations
  GEO, MEO, LEO objects
  Magnitude 13 or brighter
Reporting
  System GPS location
  Object RA, Dec, time stamp
    10 arc-second (3σ) accuracy
Operation
  10 hours/night at 3 tasks/min
Mobility
  Weight: less than 20 kg
  Volume: Airline carry-on
[2]
[1]
Notes: http://hyperphysics.phy-astr.gsu.edu/hbase/eclip.html
https://twitter.com/boeingairplanes/status/1086672652150939649
Call this slide customer requirements

## Slide 6
1. Observation denied to traditional observatory
2. iMagpie deploys to off-grid site by hiking, flying, driving, etc.
3. iMagpie assembled and calibrated on-site
4. Autonomous pointing enabled as human rests
5. iMagpie actuates to task-specified attitude
6. iMagpie images object in transit, saves image locally
7. iMagpie processes image to obtain:
Attitude of 10 nearest stars
Attitude of streak start
Attitude of streak stop
8. UCTs, exposure times, & GPS location sent to CCAR via SMS
10. iMagpie solar panels recharge batteries during the day
9. Pointing, imaging, and processing repeats for the rest of the night, up to three observations per minute
11. Night tasking and day recharging continue for mission duration
12. iMagpie disassembled at end of mission and returned to CCAR
Concept of Operations
Notes: Add cadance
Plane/hiking/both

## Slide 7: Functional Block Diagram
Notes: Fix animation
Specify task – what is in the data being sent
What is being sent data transmission to processing
Exposure command, pointing command – degrees of freedom
Think through interfaces
FBD can reflect electronics schematic – ok to repeat

## Slide 8: Design Overview
Mount Head
Image Sensor
Tripod
Lens
Solar Panels
Processor Box

## Slide 9: Processor Box Design
Dimensions: 16.5x11.4x14.6 cm
Ambient Sensor
Raspberry Pi 4B
GSM
(GPS/SMS Board)
Notes: Specify that we're calling this out because it has particular requirements – thermal design

## Slide 10: Solar Panel Design Changes
Voltaic solar panel - COTS
  10 Watt
  6 Volts
  UV- and scratch-resistant ETFE coating
  Waterproof
  Quantity: 3
Notes: https://voltaicsystems.com/10-watt-panel/

## Slide 11: Solar Panel Design Changes
Materials:
  Acrylic
  PLA
Method
  Epoxy
  Laser cut
  3D print

## Slide 12: Battery Safety and Compliance
The BQ25703A IC being used in conjunction with our battery provides the following benefits:
Over-voltage protection
Under-voltage protection
Over-current protection
Thermal Shutdown Procedures

## Slide 13: Design Mass and Volume
Metric | Design | Budget | Margin
Mass | 16.4 kg | 20.0 kg | 18%
Volume | 40.2 L | 44.3 L | 9.3%
Notes: Add the 60 liter pack or state that it can fit within – include requirements, check that they are fulfilled
Numbers on figure are difficult to read
Get rid of margins – set dimensions
Mass is too precise (margin in mass)
Add electrical and data schematics
Label key components

## Slide 14: Critical Project Elements
CPE | Motivation
1. Electronics | Tight, self-reliant power budget
2. Structures | Thermal regulation System stability during observations
3. Comms/Controls | Remote commands via SMS Precise observation requirements
4. Image Processing | 3 task/min cadence 10 arc-second (3σ) accuracy
Notes: This is different from CDR
Most important aspect of manufacturing,

## Slide 15: Presentation Overview
Overview
Schedule
Testing
Budget

## Slide 16: Scheduling Gantt Chart
Administrative
Testing
Hardware
Software
Critical Path

## Slide 17: Test Schedule
Initial Hardware
Software/Hardware Communication
Integrated Subsystem
Full System

## Slide 18: Presentation Overview
Overview
Schedule
Test Readiness
Budget

## Slide 19: Test Status Overview
Already Complete
In Progress
Being Planned
Propagator Software
Astrometry Algorithm with Samples
Communication with Mount head
Communication with Camera Sensor
Communication with GSM module
Streak Detection with Samples
Sample Tasking for Real Captures
Streak Analysis on Real Captures
Initial Integrated System Testing
Battery Charging Test
Power System Testing
Thermal System Testing
Control System Testing
Full System Operational Testing

## Slide 20: Propagator
What's being tested?
  Conversion from a task to mount commands
  Propagation accuracy (Alt/Az)
  Computation run time
Risk Reduction:
  Lowers risk of streak not being contained in FOV
  Lowers risk of overshooting time budget
Relevant Requirements | 
DR 3.3 | iMagpie shall be capable of performing observations at a cadence of up to 3 tasks per minute.
DR 4.1 | iMagpie shall incorporate a tasker to command the mount and image sensor to carry out observations.
Test Status
Complete

## Slide 21: Propagator
Test Fixtures:
  Python code and Sattrack
Test Procedure Overview:
  Run code on known satellite
  Check sat position on Sattrack
  Verify results
Results:
  Propagator predicts positions of LEO, MEO, and GEO satellites to within one degree of accuracy
Required Equipment
Laptop
Testing Facility
Anywhere

## Slide 22: Sample Streak Detection
What's being tested?
  Capability, accuracy, and timing of algorithm
Risk Reduction:
  Quantify confidence in endpoint accuracy
Relevant Requirements | 
DR 5.1.3​ | Identify start and stop RA and Dec of streak​
DR 5.1.4​ | Determine RA/Dec w/ 10 arc-sec (3σ) accuracy​
DR 5.1.5​ | Process images at a rate of 3 images per minute​
Test Status
In Progress

## Slide 23: Sample Streak Detection

## Slide 24: Sample Streak Detection

## Slide 25: Sample Streak Detection

## Slide 26: Sample Streak Detection
Algorithm to generate streak:
  Magnitude
  Altitude (LEO, MEO, GEO)
  Background noise
  Streak length
ISS
Magnitude 13
Generated ISS
Real ISS
Notes: https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.tutorialspoint.com%2Fsatellite_communication%2Fsatellite_communication_earth_orbit_satellites.htm&psig=AOvVaw0v2GtNHgj_uzKelxZvzHX_&ust=1582913557602000&source=images&cd=vfe&ved=0CAIQjRxqFwoTCND0vOCq8ucCFQAAAAAdAAAAABAD

## Slide 27: Sample Streak Detection
Quantify Error
  10 arcsec 3 sigma accuracy
Notes: https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.tutorialspoint.com%2Fsatellite_communication%2Fsatellite_communication_earth_orbit_satellites.htm&psig=AOvVaw0v2GtNHgj_uzKelxZvzHX_&ust=1582913557602000&source=images&cd=vfe&ved=0CAIQjRxqFwoTCND0vOCq8ucCFQAAAAAdAAAAABAD

## Slide 28: Sample Streak Detection
Accuracy: 20 +/- 5 arcsec
Notes: https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.tutorialspoint.com%2Fsatellite_communication%2Fsatellite_communication_earth_orbit_satellites.htm&psig=AOvVaw0v2GtNHgj_uzKelxZvzHX_&ust=1582913557602000&source=images&cd=vfe&ved=0CAIQjRxqFwoTCND0vOCq8ucCFQAAAAAdAAAAABAD

## Slide 29: Sample Streak Detection
Timing: 67s total
Notes: https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.tutorialspoint.com%2Fsatellite_communication%2Fsatellite_communication_earth_orbit_satellites.htm&psig=AOvVaw0v2GtNHgj_uzKelxZvzHX_&ust=1582913557602000&source=images&cd=vfe&ved=0CAIQjRxqFwoTCND0vOCq8ucCFQAAAAAdAAAAABAD

## Slide 30: Sample Astrometry Software
What's being tested?
  Right Ascension and Declination coordinates of stars
Risk Reduction:
  Testing the accuracy of coordinate transforms provides insurance of usable data
Relevant Requirements | 
DR 5.1.2 | Identify RA/Dec of 10 nearest stars
DR 5.1.5 | Process images at a rate of 3 images per minute
Test Status
Complete

## Slide 31: Sample Astrometry Software
Test Fixtures:
  Offline Astrometry source & Python code
Test Procedure Overview:
  Run sample images through Astrometry platform/transform matrix for comparison
Results:
  Timing within cadence requirement (15s) & 10 arcsecond expected accuracy
Required Equipment
Raspberry Pi 4
Testing Facility
Anywhere

## Slide 32: Astrometry Software Results
Vela Supernova Remnant Solved
Inputs:
  Raw image w/ pointing information
Outputs:
  Right ascension + declination of field center
  Field rotation
Notes: In work - Python function for providing images to astrometry's command line
-Python function for transforming field center RA/DEC to streak's RA/DEC

## Slide 33: Real Capture Processing
What's being tested?
  Ability to capture streaks (manual user control)
  Ability to process real images
  Accuracy of processing
  Ability to capture magnitude 13 objects
Risk Reduction:
  Ensures that iMagpie can accurately acquire/process the needed data
Relevant Requirements | 
DR 3.1.1 DR 5.1.3 DR 5.1.4 | Detect magnitude 13 objects Identify streak RA/Dec Report with 10 arcsec 3 sigma accuracy
Test Status
In Progress

## Slide 34: Real Capture Processing
Test Fixtures:
  Mount/Lens and Sensor
Test Procedure Overview:
  Use propagator to find observation time
  Point mount using controller
  Manually take exposure
  Attempt to process streak
Results:
  Images of streaks
  Processed streak information
Required Equipment
Sensor/Lens Laptop Mount/Tripod
Testing Facility
Outdoors in Boulder/Nederland

## Slide 35: Control System Testing
What's being tested?
  Basic Functionality of Remote System
  Tasking and Control Software
Risk Reduction:
  Minimizes likelihood of having unresponsive hardware in field
Relevant Requirements | 
FR 3 FR 4 FR 6 | Capture Images in LEO, MEO, GEO Process Tasks Remote Communication
Test Status
In Progress

## Slide 36: Control System Testing
Test Fixtures:
  Fully assembled system
Test Procedure Overview:
  Implement system with tasking algorithm
  Activate toggle switches
  Send slew and capture commands via SMS
Results:
  Confirmation that our assembled system is fully controllable
Required Equipment
None
Testing Facility
Outside AERO building

## Slide 37: Power System Testing
What's being tested?
  Ability for batteries to supply the required power for mission duration
  Ability for the project to be powered by non-ideal power source such as batteries
Risk Reduction:
  Minimizes likelihood of failure due to power loss
Relevant Requirements | 
DR 2.1 | iMagpie shall be capable of operating under its own power for up to 10 hours.
Test Status
Being Planned

## Slide 38: Power System Testing
Test Fixtures:
  Fully assembled system
Test Procedure Overview:
  Run system for 24h with appropriate monitoring tools
Results:
  System should be able to discharge and recharge successfully over a 24h period
Required Equipment
Multimeters
Testing Facility
Electronics Lab

## Slide 39: Full System Testing
What's being tested?
  Fully Assembled System Operability
Risk Reduction:
  Minimize risk of any failure modes during remote operation
Relevant Requirements | 
FR 1 FR 2 FR 3 FR 4 FR 5 FR 6 FR 7 | System shall be person-portable. Independently Powered Capture Images in LEO, MEO, GEO Capable of Processing Tasks Capable of Processing Images Capable of communication with CCAR Capable of Operation in Boulder
Test Status
Planning

## Slide 40: Full System Testing
Test Fixtures:
  Fully Assembled System at location
  with SMS reception
Test Procedure Overview:
  Deploy at remote location
  Start system calibration
  Implement CCAR tasking
  Monitor system performance during and after operation
Results:
  Confirmation that system meets all functional requirements
  Insight to failure modes
Required Equipment
None
Testing Facility
Outside Aero Building
Arestua Hut

## Slide 41: Presentation Overview
Overview
Schedule
Test Readiness
Budget

## Slide 42: Predicted Financial Budget

## Slide 43: Predicted Financial Budget
Subsystem | Expected Cost | Budget | Expected Margin | 
Processing | $580 | $625 | $45 | 7.2%
Power | $520 | $575 | $55 | 9.6%
Mount | $1,383 | $1,385 | $2 | 0.14%
Optics | $1,934 | $1,940 | $6 | 0.3%
Thermal | $210 | $225 | $15 | 6.7%
Manufacturing/ Testing | $156 | $200 | $44 | 22%
Transportation | $50 | $50 | $0 | 0%
Total | $4,834 | $5,000 | $167 | 3.34%

## Slide 44: Part Procurement
Item(s) | Ordered | Delivered
Solar Panels |  | 
GSM Module |  | 
PCB Devices |  | 
Recently Ordered Items
Notes: The Thermal and Transportation Subsystems are together because both have ordered all Needed items

## Slide 45: Acknowledgements
Dr. Marcus Holzinger and Samuel Wishnek
Dr. Aaron Johnson
Project Advisory Board

## Slide 46: Questions?

## Slide 47: References
[1] “Ecliptic Plane”, Hyperphysics, http://hyperphysics.phy-astr.gsu.edu/hbase/eclip.html
[2] Boeing Airlines https://twitter.com/boeingairplanes/status/1086672652150939649
[3] PCBWAY IOTBITS LOGO http://iot-bits.com/iotbits/pcbway-iotbits-logo/
[4] "Lithium Ion Battery – 6Ah", Sparkfun https://www.sparkfun.com/products/13856
[XXI] AVM Standard https://www.virtualastronomy.org/AVM_DRAFTVersion12_rlh02.pdf

## Slide 48: Apparent Magnitude
Measure of objects brightness as seen from Earth
  Reverse logarithmic scale
  Magnitude of 5 greater = brightness 100 times dimmer
  Magnitude 13 is ~400 times dimmer than naked eye limit
iMagpie Design Goal
[xx]
Notes: https://www.cambridge.org/core/books/question-and-answer-guide-to-astronomy/stars-and-stellar-systems/CFD8F55B5EF1FD7608CA2EDD8E1FCD3E

## Slide 49: RA/Dec Coordinate Transform
Where CROT angles, Center Right Ascension, and Center Declination are provided from astrometry algorithm
XXI

## Slide 50: Levels of Success

## Slide 51: Design Requirements

## Slide 52: Design Requirements (cont.)

## Slide 53: Design Requirements (cont.)

## Slide 54: Design Requirements (cont.)

## Slide 55: Test Backups

## Slide 56: Camera Manufacturer Specifications
Resolution: 16Mega Pixels 4656×3520
Pixel Size: 3.8µm
Exposure Range: 32µs-2000s
Interface: USB3.0/USB2.0
Read Noise: 1.2e @30db gain
Full well: 20ke
Dimensions: φ62mm X 41mm
Weight: 140g
Working Temperature: -5°C—45°C
Working Relative Humidity: 20%—80%

## Slide 57: Battery Charging Testing
What's being tested?
  Ability for batteries to recharge at required rate
Risk Reduction:
  Ensures iMagpie will have the required margin to recharge batteries during a sunny day
Relevant Requirements | 
DR 2.2 | iMagpie shall be capable of recharging its batteries to full capacity during a single day while off the grid.
Test Status
Being Planned

## Slide 58: Battery Charging Testing
Test Fixtures:
  Battery connected to charger IC, and then DC power supply
Test Procedure Overview:
  Drain batteries to safe low voltage
  Recharge at required rate to satisfy worst case charge times
Results:
  Batteries should be able to recharge in approximately 7h, allowing margin for sub-ideal weather
Required Equipment
Multimeter, DC power supply
Testing Facility
Electronics Lab

## Slide 59: Thermal Testing
What's being tested?
  Ability of iMagpie's heating system/insulation
  Characterization of heating to compare to model
Risk Reduction:
  Ensures that iMagpie can prevent dew buildup and keep hardware above minimum temperatures
Relevant Requirements | 
DR 7.1 DR 7.2 | iMagpie's optics shall stay above dew point IMagpie's hardware shall be kept within operational ranges
Test Status
In Planning

## Slide 60: Thermal Testing
Test Fixtures:
  Lens/Sensor
  Thermal camera or temperature probe
Test Procedure Overview:
  Heat iMagpie at room temperature until steady state
  Measure optics temperatures
  Compare to modeling
  Repeat outdoors in colder temps
Results:
  Thermal profiling of system
  Heating system verification
Required Equipment
Sensor/Lens Thermal Camera Laptop
Testing Facility
Aero Building

## Slide 61: Timing Testing
What's being tested?
  Characterization of exposure timing
Risk Reduction:
  Ensures that iMagpie can report exposure start and stop times to 0.1 microseconds
  Increases accuracy of streak data
Relevant Requirements | 
DR 4.1.4 DR 4.1.5 | iMagpie shall take exposures at the commanded time iMagpie shall record the start and stop times of exposures
Test Status
Re-Planning

## Slide 62: Timing Testing
Test Fixtures:
  12 Bit counting circuit connect to LEDs
  Raspberry Pi with GSM
  Waveform generator
Test Procedure Overview:
  Raspberry Pi sends command to camera and timing circuit to begin
  Timing circuit counts in binary with output displayed on LEDs
  Camera takes exposure of LEDs
  LEDs reveal exposure delay
Results:
  Start and stop times of exposure precisely known
Required Equipment
Sensor/Lens Timing Circuit Raspberry Pi GSM Waveform Generator
Testing Facility
Electronics Lab

## Slide 63: Electronics Schematics Backup

## Slide 64: Electronic Schematic

## Slide 65: Electronic Schematic (cont.)

## Slide 66: Electronic Schematic (cont.)

## Slide 67: Electronic Schematic (cont.)

## Slide 68: Electronic Schematic (cont.)

## Slide 69: Electronic Schematic (cont.)

## Slide 70: Electronic Schematic (cont.)

## Slide 71: Electronic Schematic (cont.)

## Slide 72: Battery Charger IC Schematic

## Slide 73: Team Photo