## Slide 1: HERMES Hazard Examination and Reconnaissance Messenger for Extended Surveillance
Manufacturing Status review
February 4, 2019
Presenters: Brindan Adhikari, Brandon Santori, Michely Tenardi, Marcos Mejia
Customer: Barbara Streiffert and Jet Propulsion Laboratory (JPL)
Advisor: Dr. Kathryn Anne Wingate
Team: Alexander Sandoval, Alexis Sotomayor, Ashley Montalvo, Brandon Santori, Brindan Adhikari, Chase Pellazar, Colin Chen, Junzhe He, Katelyn Griego, Marcos Mejia, Michely Tenardi, Quinter Nyland
Notes: Intro: conops: design

## Slide 2: Project Purpose and Objectives
Project Purpose and Objectives
Design Requirements and their Satisfaction
Project Risks
Design Solutions
Critical Project Elements
Verification and Validation
Backup Slides
Project Planning
Notes: 2 minutes, 28 mins left

## Slide 3: Project Motivation and Statement
The mother rover created by DRIFT is large and difficult to navigate through forest like areas.
The HERMES team will design, build and test a child scout rover (CSR) that will deploy, take images/videos of the surrounding terrain, determine a viable path to a location of interest (LOI), and upon arrival to the LOI, the CSR will send the viable path to the mother rover.
CHIMERA
DRIFT
Note: Blue used for emphasis

## Slide 4: CONOPS: Arriving to Location of Interest
4
4
October 2018
Ground
Station
Requirements
Functions
Mother Rover
LOI
Up to 250 m radius (820 ft)
1
2
Deploy from Ground Station and drop a pathpoint
1
Receive Location of Interest (LOI) from GS
2
Upon arrival it will stop, and notify the GS and drop a pathpoint
5
User commands CSR to point towards LOI
3
Comm between GS and MR
Comm between GS and CSR
Comm between CSR and MR
Autonomously controlled path
Legend
Stop and request user intervention
Pathpoint
Mission Terrain
Manually controlled path
User commands CSR to travel towards the LOI in semi autonomous mode. The CSR will travel until it reaches the LOI.
4
3
5
En route to the LOI, the CSR may encounter one or more of the following:
Obstacles
Discontinuities
Slopes
Loss of communications
Child Scout Rover
4
Notes: Fix picture,

## Slide 5: CONOPS: Other Terrain
5
= Point where sensor detects
obstacle or discontinuity
= Pathpoint
= Stop and request
user intervention
= Manual Control
= Autonomous Control
If the CSR detects an obstacle, the CSR will stop
The user will take control, and manually control the CSR around the obstacle
  Every time the CSR turns, a pathpoint is recorded
After traveling around the obstacle, the user commands the CSR to point towards the LOI, and command it into semi- autonomous mode
1
2
3
Obstacle
Operator manually controls CSR around obstacle
1
2
3
Non-Traversable Obstacles
1
3
4
Up to 9 inches wide
Greater than 2.4 in deep
CSR crosses autonomously
If the CSR detects a discontinuity, the CSR will stop
The user will then send a command to the CSR to enter the discontinuity traversal mode
Then the CSR autonomously crosses the discontinuity
  A pathpoint is recorded since a mobility command was received and executed
After crossing the discontinuity, the CSR stops and requests user intervention
1
2
3
4
2
User sends command to change mode
Discontinuities
Slopes
If the CSR detects a slope, the CSR will stop
The user will control the CSR to get onto the slope and command the CSR into semi autonomous mode
The CSR will travel on the slope in semi autonomous mode
Once the CSR detects flat ground, it will stop
The user will control the CSR to return to flat ground
1
2
3
4
5
Up to a 20° slope
2
3
4
5
Operator manually controls the CSR onto or off-of slope
1
Notes: Fix picture

## Slide 6: Functional Block Diagram
Notes: Needs linear mass stage, fix eps for each. Talk to chase how to present best

## Slide 7: Functional Requirements
Requirement ID | Description
CSR.1 | The CSR shall receive commands from the GS
CSR.2 | The CSR shall send video, GPS coordinates, and sensor data to the GS through mission defined terrain
CSR.3 | The CSR shall drive to a location of interest through mission defined terrain
CSR.4 | The CSR shall travel back to the last reported pathpoint upon loss of communications with the GS
CSR.5 | The CSR shall take video in position hold
Notes: CSR.2 – specify sensor data

## Slide 8: Critical Project Elements
Critical Project Element (CPE) | Rationale | Relation to Manufacturing
Mobility | The CSR must be able to travel forward and backwards and perform 360° turns. | The main needs are : Drivetrain Chassis Linear mass stage assembly.
Software | The CSR software must read in, process, and execute commands from the GS. The CSR must also process data on-board to react to obstacles and discontinuities. | The main needs are: Arduino – ASUS Integration Development of Driving functions Sensing software
Guidance, Navigation, and Control (GNC) | The CSR must be controlled remotely by one operator, and must read its own attitude accurately. | The main needs are: Manual control of the rover
Environment Sensing | The CSR must accurately sense the terrain and obstacles around it to navigate around them. | The main needs are: Data processing of sensors
Communications | The CSR must communicate with the GS to send the viable path, images and videos to the GS. | The main needs are: Integration between the GS and the CSR communication
= Emphasis for this presentation

## Slide 9: Primary Success Levels
Criteria | Level 1 | Level 2 | Level 3
Environment | The CSR shall traverse the following: Open areas Up to 20 degree incline slopes | The CSR shall traverse the following: Type A underbrush Roots up to a 2.4 inch(6 cm) diameter | The CSR shall traverse the following: Type D underbrush Up to a 9 inch wide discontinuities with depths greater than 2.4 inches (6 cm)
Control | The CSR shall navigate by receiving control commands from the GS The CSR shall perform a 360° turn The CSR shall drive forward and reverse | The CSR shall navigate to a LOI and shall detect obstacles en route to the LOI, but manual control is needed to circumvent the obstacles. | The CSR shall autonomously return to the last known GPS location if connection to the GS is lost.
Other Success Levels: Communication, Range, Video/Image

## Slide 10: Design Recap: System Interface
MR Comm System
1 6.5W 900MHz Ubiquiti Radio
MR Comm System
1 6.5W 900MHz Ubiquiti Radio
MR Comm System
1 6.5W 900MHz Ubiquiti Radio
MR
CSR
MR Software System
Function: ROS Slave Machine
CSR Software System
Function: ROS Host Machine
GS Software System
Function: ROS Slave Machine
Displays a GUI for operation
GS
= Wireless Comms.
= Outlines components
Mission Log
CSR Status
Command Options
Video Feed
Notes: I’d say emphasize less on comms and expand more on software. Fix, and talk better. Animate

## Slide 11: Design Recap: CSR Hardware
Drivetrain:
  Design
    One drivetrain per side
    Composed of 6 wheels, 2 chains, chain tensioners, sprockets, 1 motor + gearbox
Chassis:
  Design
    Top housing is 0.25” laser cut acrylic
    Bottom Chassis is 0.25” CNC’ed 6061 Aluminum
Linear Mass Stage:
  Why?
    The COM is shifted as necessary using the linear mass stage to cross discontinuities. The mass is shifted when the ultrasonic sensors detect ground under a certain set of wheels.
  Design
    A COTS linear mass stage is utilized which is controlled by a stepper motor controller. The mass being used is 5 kg.
CSR Physical Properties Summary:
Overall Dimensions: 28 in x 15 in* 11 in
Total Mass: 17 kg
28 in
15.5 in
20.2 in
Notes: Don't assume anyone knows what everything is for. Why is the linear mass stage there? Why are we using ROS in the first place? Why do we need to operate in different modes? We need to make sure to build our presentation in such a way that everything has a purpose when it is presented.

## Slide 12: Design Recap: CSR Hardware
Single Beam LiDAR Sensors:
  Why?
    To detect discontinuities
360 Degree Lidar Sensor:
  Why?
    To detect obstacles
Ultrasonic Sensor:
  Why?
    Used for crossing discontinuities to determine what position the mass
    from the linear mass stage should be in
    Placed on the bottom on the CSR (not shown in diagram)
GPS – RTK Sensor:
  Why?
    To determine the CSR’s position up to a 0.025 m accuracy
Magnetometer/ 3 Axis Accelerometer:
  Why?
    Magnetometer used for determining the CSR’s heading
    Accelerometer used to determine if the CSR is on level ground or a slope
Notes: Don't assume anyone knows what everything is for. Why is the linear mass stage there? Why are we using ROS in the first place? Why do we need to operate in different modes? We need to make sure to build our presentation in such a way that everything has a purpose when it is presented.

## Slide 13: Design Recap: Software Architecture
CSR can run in 6 different modes:
- Initialization
- Manual
- Semi-Autonomous
- Discontinuity Cross
- Loss of Comms
- LOI Reached
Benefits of the Mode Architecture:
- Allows for a reduction in the amount of code running at any point in time
- Allows for data to only be processed from sensors when needed
Notes: She expects us to explain why ROS is being used in a previous slide somewhere so that when we see the software diagram, it is not shocking to people looking at it.

## Slide 14: Scheduling

## Slide 15: Mechanical Schedule
Module Training
Chassis Housing
Wheel Shaft
3D Printed Mounts
Tensioner
Spacers
Shaft Mounts
Chassis Integration
Feb 24. Finish manufacturing
Current Day. Feb, 4 2019
= Completed
= Future Work
= In Progress
= Margin
= Milestone
= Critical Path
Hours
2/2
2/2
0/5
2/2
0/1
2/2
0/1
2/2
0/1
0/4
2/5
0/1
0/4
0/2
0/1
0/1
0/1
0/2
0/2
0/2
0/2
2/2
0/2
0/4
0/1
1/3
0/2
1/4
0/2
0/2

## Slide 16: Software Schedule
360 Degree Lidar
March 4. Finish Unit Software
Feb. 17 Take 360 offramp
Navigation Sensors
Ground Station and GUI
Basic Setup
Fundamental software
Obstacle and Discontinuity Software
Current Day. Feb, 4 2019
Integrated Functions
= Completed
= Future Work
= In Progress
= Margin
= Milestone
= Critical Path
Hours
5/5
5/5
5/5
5/5
3/8
6/10
1/10
3/5
12/18
10/15
1/5
1/5
0/5
2/6
2/6
2/6
0/5
0/5
0/7
0/5
0/7

## Slide 17: Integration & Test Schedule
UT: Unit Tests
MI: Mechanical Integration
SIT: Subsystem Integrated Tests
Current Day. Feb, 4 2019
= Completed
= Future Work
= In Progress
= Margin
= Milestone
= Critical Path

## Slide 18: Integration & Test Schedule
FSIT: Full System Integrated Tests
SIT: Subsystem Integrated Tests
= Completed
= Future Work
= In Progress
= Margin
= Milestone
= Critical Path
Spring Break
Finish System
Friday April 19, 2019

## Slide 19: Manufacturing

## Slide 20: Mobility

## Slide 21: Overview and Scope
28”
15.5”
20.2”
22.25”
= Emphasis for this presentation
Chassis
Status:
Top housing has been laser cut out of acrylic
Remaining Work:
Base must be CNC’ed
Linear Mass Stage
Status:
Parts have been procured
Electronics developed
Remaining Work:
Mass must be machined
Everything must be integrated
Drivetrain
Status:
Will be discussed next
Remaining Work:
Will be discussed next
* Detailed information for Chassis and Linear Mass Stage in backup Slides
Notes: Precision manufacturing
It’s the most complex system of the chassis
Required to have it for the minimum success level for our mission
Color code subsystems, blow up design, add labels, then emphasize why drivetrain only. Integration of drivetrain is critical because schedule will change if not completed
Drivetrain integration is critical for the schedule

## Slide 22: Manufacturing Status: Drivetrain
8” Diameter Rubber Treaded Wheel with press fit 1/2 ID Radial Ball Bearing 1/2”
0.4’’ thick Shaft Collar
Needle Thrust Bearing
Flat Washer
Rotary Shaft with Retaining Ring Grooves. 303 Stainless Steel, ½” Diameter
Status: All shafts have been cut to length (4.5’’)
Remaining Work: All shafts need to have pin hole drilled
Hours: 0/1
Completion Date: 2/6/19
Grade 5 Steel Serrated Flange Head Cap Screws
Gearbox Sprocket
Roller Chain ANSI #25, 1/4 “ Pitch
0.25’’ thick Spacer
Status: Laser Cut Prototype has been made
Remaining Work: Aluminum spacers need to be lathed
Hours: 0/4
Completion Date: 2/6/19
38t Aluminum Plate Sprockets
= COTS Parts
= Completed
= In Progress
Legend
= Future Work
Notes: Needs dimensions + more specific on the screws, spacers, sprockets. Add un exploded view and then explode

## Slide 23: Manufacturing Status: Shaft Mounts
= COTS Parts
= Completed
= In Progress
Legend
= Future Work
1.75’’ long Steel Socket Cap Screws
1’’ long 0.125’’ diameter Alloy Steel Dowel Pin
Aluminum Bar
Hours: 2/10
Completion Date: 2/6/19
Wheel Assembly: 3 per side
Status:
All 12 pieces have been cut to dimensions
Remaining Work:
Need to mill out corner pieces
Need to drill 6 holes (pin, 4 screws, shaft)
Need to cut to divide part
Shaft Mounts: 6 per side
2.875’’
0.9’’
0.5’’
0.75’’
Notes: Pin > to hold the shaft from the torque
Put the picture of the whole CSR and zoom the shaft mount part.
Talk about the critical dimensions (tolerances, etc, GD&T stuff). How much can they be off?
Point out the pin on the exploded view shaft
Clearance, tolerance, .501

## Slide 24: Overview and Scope
Subsystem | Manufactured Parts | Means of Manufacturing | Quantity Needed | Quantity Completed | Expected Time [completed/total hours] | Completion Date
Chassis | Aluminum Baseplate | CNC | 1 | 0 | 0 / 4 | 2/14/19
Chassis | Housing | Laser Cut | 1 | 1 | 2 / 2 | 2/1/19
Chassis | 80/20 Struts | Bandsaw/mill | 6 | 6 | 2 / 2 | 1/29/19
Drive Train | Rotary Shafts | Bandsaw/mill | 6 | 6 | 2 / 2 | 2/6/19
Drive Train | Shaft Mounts | Bandsaw/mill | 12 | 12 complete with bandsaw, 0 complete with mill | 2 / 10 | 2/6/19
Drive Train | Spacers | Lathe | 4 | 0 | 0 / 4 | 2/6/19
Drive Train | Tensioner Mount/Base | Mill | 4 | 0 | 0 / 4 | 2/6/19
Drive Train | Tensioner Arm | Mill | 4 | 0 | 0 / 2 | 2/6/19
Drive Train | Drive Train | Assembly | 2 | 0 | 0 / 5 | 2/24/19
Remaining Hours for Drive Train + Chassis = 27 hours

## Slide 25: Mobility Electronics
The Mobility System Runs through the DUE
15.2V Battery utilized to power the motors and the linear actuator (requires a 24 V step-up regulator)
11 digital pins and 6 analog pins
This is one example of the electrical schematic. There are more in the backup slides.
Power
Ground
PWM
Digital
Arduino DUE Shield
Linear Mass Stage Motor Controller
Step- up Regulator (24 Vout)
AndyMark 775 Redline Motor
Motor Controller
LIPO 15.2 V/ 7500 MAH
Linear Actuator
Redline Encoder
= Completed
= In Progress
= Future Work
Notes: Label main components. Power source, controller, battery, etc. with bigger text to show how connections are going from where to where. Also mention this is only one of many. Have another slide discussing wire dimensions, connection type, voltage, amperage, etc. Also thinking about physical connection of harnessing, cabling, etc. As well as how it’ll fit in the chassis

## Slide 26: Software

## Slide 27: Why ROS?
  Integration Needs
    Communication
      Communicating over TCP/IP protocols between different machines
    Environment Sensing
      Detecting objects using LiDAR and Ultrasonic
    GNC
      Remote user control, video stream, and GPS accuracy
    Mobility
      Motor control, linear mass stage, and speed controller
  Implementation
    Mode architecture
      Different states of operation
    Modular node development
      Independent process for single dedicated purpose
    Parameter Server
      Shares same parameters across nodes
    Parallel execution of nodes
      Multiple tasks occur at once
Notes:   What is the Robotic Operating System (ROS)?
    Collection of tools, libraries, and conventions to simplify integration among different software functionality

## Slide 28: Software Status
Quick Recap:
Nodes written in Python or C++, then ROS is used to integrate them
  All nodes run in parallel
Each node has checks to determine if mode change is necessary.
  Dependent on thresholds, flags, etc.
All nodes are constantly checking for mode changes
Main Concerns:
  360 LiDAR Node
  Driving Function
Hours: 1/5
Completion Date: 2/16/19
Hours: 10/15
Completion Date: 2/6/19
Hours: 1/5
Completion Date: 2/16/19
Hours: 15/23
Completion Date: 2/19
Hours: 2/10
Completion Date: 2/16/19
Hours: 0/7
Completion Date: 3/20/19
Hours: 3/8
Completion Date: 3/3/19
Notes: She wants us to still indicate progress like we are, but she wants us to verbally explain this progress more. We need to indicate software pieces that will take more/less time than others and how far along we are when we say they are "in progress.“
Need to show that data going to ASUS will not overload it. Add data budget in the backup slide. Look at bit rates, memory, etc.

## Slide 29: Status: 360° LIDAR Sensor
  General Status:
      RPLIDAR software successfully integrated to run sensor in basic operation
      Off-ramp decision date (Feb 17) relies on 2 critical aspects of 360° LIDAR software development
        Can the ASUS Tinker Board process the RPLIDAR data fast enough?
        Can the RPLIDAR achieve a low enough angular resolution to satisfy requirement SENS.3.1.2 (required < 1.54°)
  1. Data Processing Speed
  2. Angular Resolution
      Comparative test between Microsoft Surface Pro 3 (overly capable machine) versus ASUS Tinker Board (onboard computer)
  Tinker Board outperformed Surface Pro 3
  Slightly less consistent
      In basic operation, RPLIDAR achieves angular resolution of ~ 1.00° but will likely increase with larger data load on the ASUS
      Possibility of requirement failure if motor control is not implemented
  No motor control implemented
  General Takeaway:
    Currently planning to take off-ramp on February 17
  About 8 expected hours remaining
    Have put in 15 hours
Notes: She wants the 360 lidar slide to revolve around the off-ramp. What are the conditions of the off-ramp? Why have we evaded those conditions? When do we expect to be certain that we don't need to take the off-ramp? Very busy slide. Need to animate and mayb cut down if possible. Talk about main concerns, and more on the status

## Slide 30: Status: Driving Functions
General Status:
  Serial Driven Driving and Semi-Autonomous (Cruise) Driving Complete
  Speed defined as –400 to 400
Remaining Work:
  Integrate motor linear speed from encoders
  Write PID controller
    Expect to Finish March 4, 2019
    Hours: 0/5
Main Concerns:
  Discrepancy between power supply amperage draw and motor controller current sensor readings
Mitigations:
  Characterize current error
  Hard code offset
Serial Control
Encoder Read-In
PID Controller
Current readings from the motor controller when commanding both motors
Notes: Expand on PID information, talk about how it’s not necessary, but it is improving the performance. How we plan on getting values. Try to meet with Ahmed, Lawrence, or Holzinger about controlling stuff.

## Slide 31: Budget

## Slide 32: Cost Plan
Subsystem Expenses
Mobility - $1519.02
Sensing - $490.92
Comms - $859.25
CDH - $173.30
Power - $401.21
Misc/Printing ~ $1000.00 (estimated)
Expenses to Date: $3,443.70
Original Budget: $5000.00
Budget w/ EEF Funds: $6000.00
Remaining Funds: $1556.30
Notes: Fix red, add misc

## Slide 33: Major Procurements
Mobility: Chassis, Wheels, Motor, Shafts, Drivetrain
Sensing: Lidar, Ultrasonic, Magnetometer/Accelerometer, GPS
Comms: Radios, Antennas, POE Adapters
C&DH: ASUS Computer, Arduino Due, Motor Controller, Encoder
Power: Mobility Battery, Sensing Batteries, Comms Batteries, C&DH Batteries
Items left to order: 3D Printing, Spare Motors, Voltage Regulator

## Slide 35: Manufacturing Status: Chassis
= COTS Parts
= Completed
= In Progress
Legend
= Future Work
.25” Laser Cut Acrylic Sheet
Status: Completed
CNC Aluminum
Status: Acrylic prototype has been made
Remaining Work: The real aluminum still need to be made using CNC
1”x1” T-Slotted Framing Single Rail 6105 Aluminum (80/20)
Status: Completed
1” Long Silver Corner Bracket for High Rail T-Slotted Framing

## Slide 36: Manufacturing Status: Linear Mass Stage
= COTS Parts
= Completed
= In Progress
Legend
= Future Work
M4x70mm Screws
Linear Stage Actuator
500 mm (19.7")
500 mm (2.125")
7"
Low-Carbon Steel Bars.
Status: Material has been procurred.
Remaining Work: Bars must be cut and drilled.
3.5"

## Slide 37: Project Heritage
The Jet Propulsion Laboratory’s Fire Tracker System is a system that is designed to be a low-cost, hands-off approach to forest fire identification.
There have been three previous years of heritage:
  INFERNO (2015-2016)
    - Built a semi-autonomous drone capable of transporting and deploying sensor packages
  CHIMERA (2016- 2017)
    - Built a landing, securing, and deployment system for the inherited semi-autonomous drone from INFERNO
  DRIFT (2017-2018)
    - Developed a mother rover to secure, carry, and level the semi-autonomous drone from INFERNO using the landing platform from CHIMERA
Note: Blue used for emphasis
Notes: Wingate: take this out

## Slide 38: Definitions
Pathpoint – A point after a mobility command is received and executed by the CSR.
  This point is recorded onboard the CSR and sent to the GS as a GPS coordinate.
  An operator from the ground station initially issues the command.
  Previously referred to as ‘waypoint’, and changed for clarity
Obstacle – Roots, trees, rocks, shrubs, and inclined slopes with type A terrain (only leaves are present on type A terrain)
  Traversable Obstacles
  Any root or rock less than 2.4 inches (6 cm) - (6 cm is based on average root diameter from ‘Tree Root Systems’ from the Arboricultural Advisory and Information Service)
  Non-Traversable Obstacles
  All trees
  All shrubs
  All roots and rocks greater than 2.4 inches
Discontinuity – A 9 inch wide gap with a depth larger than 2.4 inches. The width was previously 12 inches, however a model proved that the MR could only cross a 9 inch discontinuity (.229 m).
Note: Blue used for emphasis

## Slide 39: Terrain Definition

## Slide 40: Success Levels
Criteria | Level 1 | Level 2 | Level 3
Video/ Image | The imaging system on the CSR shall capture a FOV greater than 100° The imaging system shall send time-stamped images to the MR/GS | The CSR shall send videos to the MR/GS The MR shall toggle the video capture from the CSR on or off | The CSR shall send continuous video feed to the MR and GS
Control | The CSR shall navigate by receiving control commands from the GS The CSR shall perform a 360° turn The CSR shall drive forward and reverse | The CSR shall navigate to a LOI and shall detect obstacles en route to the LOI, but manual control is needed to circumvent the obstacles. | The CSR shall autonomously return to the last known GPS location if connection to the GS and MR is lost.
Note: Only main success levels are shown, the rest are in backup slides
Note: Blue used for emphasis
Notes: If sensing system is not used, we can reach control 2

## Slide 41: Success Levels
Criteria | Level 1 | Level 2 | Level 3
Control | The CSR shall navigate by received control commands from the GS The CSR shall perform a 360 degree turn The CSR shall drive forward and reverse | The CSR shall navigate to a LOI and shall detect obstacles en route to the LOI, but manual control is needed to circumvent the obstacles. | The CSR shall autonomously return to the last known GPS location if connection to the GS and MR is lost.
Communication | The CSR shall verify connection to the MR/GS. The CSR shall send at least one GPS data packet to MR/GS upon command. The CSR shall have functional communication up to a 250 meter radius from the deployment point in an open area. The CSR shall be able receive control commands from MR/GS | The CSR shall record and send waypoint locations after encountering an obstacle | The CSR shall transmit continuous video feed. The CSR shall verify its location from the LOI within +/- 5 meters The CSR shall communicate through type D terrain up to a 250 meter radius from the deployment point
Note: Blue used for emphasis

## Slide 42: Success Levels Continued
Criteria | Level 1 | Level 2 | Level 3
Environment | The CSR shall traverse the following: Open areas Up to 20 degree incline slopes | The CSR shall traverse the following: Type A underbrush Roots up to a 2.4 inch(6 cm) diameter | The CSR shall traverse the following: Type D underbrush Up to a 9 inch wide discontinuities with depths greater than 2.4 inches (6 cm)
Range | The CSR shall drive up to a 250 meter radius from the deployment point on flat terrain | The CSR shall drive up to a 250 meter radius from the deployment point on flat terrain with obstacles present | The CSR shall be able to drive in a 250 meter radius from the deployment point at a 20 degree inclined slope
Video/ Image | The imaging system on the CSR shall capture a FOV greater than 100 degrees The imaging system shall send time-stamped images to the MR/GS | The CSR shall send videos to the MR/GS The MR shall toggle the video capture from the CSR on or off | The CSR shall send continuous video feed to the MR and GS

## Slide 43: CONOPS: Loss of Comms
43
October 2018
Requirements
Functions
CSR detects no comms
1
CSR initiates last recorded pathpoint as a new temporary LOI
2
Upon arrival it will stop, and wait for acquisition of communications
5
CSR turns to point towards new temporary LOI
3
Comm between GS and MR
Comm between GS and CSR
Comm between CSR and MR
Autonomously controlled path
Legend
Stop and request user intervention
Pathpoint
Mission Terrain
Manually controlled path
CSR proceeds to travel towards new LOI
4
Child Scout Rover
Last recorded Pathpoint
Temporary location of Interest
=
=
Front of CSR
Front of CSR
Front of CSR
Upon acquisition of signal, the operator takes control of the CSR
6
3
1
2
4
5
Ground
Station
6

## Slide 44: Design Recap: Child Scout Rover
Mobility:
2 Motors with a Drive Train
Linear Mass Stage
Guidance & Navigation:
GPS Antenna
GPS Module
Magnetometer
Controls:
ASUS Tinker Board
Arduino Due
CSR Physical Properties Summary:
Overall Dimensions: 28 in x 15 in x 11 in
Total Mass: 17 kg
Note: Blue indicates component being outlined
Section Cut View
= Outlines components
Note: Internal component placement are subject to change

## Slide 45: Design Recap: Child Scout Rover
15.5 in
11 in
10in
Front View
Bottom View
28 in
Mobility:
2 Motors with a Drive Train
Linear Actuator with 5 kg Mass Stage
Environmental sensing:
Single beam LiDAR (right above front wheels)
Fisheye Lens Camera
Ultrasonic Sensors
360° RP LiDAR
Guidance & Navigation:
GPS Module
GPS Antenna
Magnetometer/Accelerometer
Note: Blue indicates component being outlined
15.5 in
8 in
20.2 in
Diagonal View
= Outlines components
Single beam LiDARs are fixed at the same angle and height
2.4 in

## Slide 46: Mobility – Chain Tensioner "Slip" Analysis
Project Overview
Summary
Backup Slides
Baseline Design
Feasibility Studies
Purpose:
Will a moment arm acting on the chain tensioner from the chain cause the tensioner arm to slip?
Baseline Assumptions:
Right wheel is driving the chain counter-clockwise
Offset angle of tensioner, θ, will go up to 10 degrees
Slack in chain is caused by two extra ¼” chain links
(Shigley’s Mechanical Engineering Design, 10th Ed.)
(Shigley’s Mechanical Engineering Design, 10th Ed.)
Helicoiled ¼-20 screw has the same preload as a non-helicoiled ¼-20 screw.
Worst case of 13.2 Nm of torque acting on the wheel, as per obstacle analysis model
Known:

## Slide 47: Mobility – Chain Tensioner "Slip" Analysis (cont.)
Project Overview
Summary
Backup Slides
Baseline Design
Feasibility Studies
Solving (moment about mounting screw):
Solving (holding strength of screw):

## Slide 48: Mobility – Shaft Mount Drawing
Project Overview
Summary
Backup Slides
Baseline Design
Feasibility Studies
Purpose:
The shaft mount is the only component with a critical dimension.

## Slide 49: Communication

## Slide 50: Overview and Scope
Mechanical:
  Parts being manufactured: Mount
    All mounts are being 3D printed
  Parts being purchased: All parts: POE Injector, Ubiquiti Radios, Antennas, Batteries
Software:
  Software being written: ROS Nodes for the ground station and for the CSR’s main computer.
  Software integration: ROS Nodes must be integrated with the greater main loop
ASUS Ethernet Port
1 of 1
Notes: what parts are being manufactured vs. purchased, what is involved in their manufacture, where and how they are being manufactured).

## Slide 51: Local Area Network Comm Setup
General Status:
  Established communication between GS laptop and CSR controller
  Able to publish and subscribe messages via radio link
Remaining Work:
  Conduct radio link over 250m
    Record latency and receiver power levels
Main Concerns:
  Self interference
  Latency (Time Synchronization)
Mitigations:
  Establish CSR controller as time server
  Replace one antenna port with dummy resistance

## Slide 52: GPS Setup
General Status:
  Created the GPS RTK Base Station
    Outputs RTCM messages from GS deployment
Remaining Work:
  Receive RTCM messages at 500 bytes/sec at the CSR deployment
  Compare GPS accuracy between RTK and no RTK data
Main Concerns:
  CSR GPS module will not receive RTCM messages at the rate that is demanded
Mitigations:
  Buffer RTCM messages in case speed is not met

## Slide 53: Electronics

## Slide 54: Sensing System Electronics
Power
Ground
Analog
Digital

## Slide 55: GNC System Electronics
Power
Ground
UART

## Slide 56: Communications System Electronics
Power
Ground
Ethernet

## Slide 57: Arduino Due - ASUS Integration
ASUS Tinker Board
  RK3288 ARM Cortex-A17
    3.3V Max (Mode Change)
      6 Output Pins
    USB Serial Communication (Data)
      Transmit/Receive
Arduino Due
  Atmel ARM Cortex-M3
    3.3V Max (Mode Change)
      6 Input Pins
    USB Serial Communication (Data)
      Transmit/Receive
Notes: Mainly to show that asus and Arduino are switching modes at the same time. Put in backup

## Slide 58: Controller Data Usage
System Monitoring Tool (Glances)
  Free software that monitors operating system management
    CPU usage, RAM usage, Disk space usage, Network usage, etc.
Notes: Data budget showing what each mode requires and what the controller can provide during each state.

## Slide 59: Test Results

## Slide 60: ASUS Thermal Test
Setup: Results:
This test has determined the maximum ambient temperature that components surrounding the ASUS will have to face. Since the chasis will not be completely sealed, these results are characteristic of a worst case scenario. For precaution, a heat sink or fan may be added to the system, so surrounding components do not overheat

## Slide 61: HC-SR04 Ultrasonic Component Test
This test has determined the accuracy of the ultrasonic sensor is less than 2 cm, which is characteristic of the accuracy we will need to successfully detect the presence of a discontinuity
Results:
Notes: Add x axis

## Slide 62: Off Ramp Option- Ultrasonic Sensors
Front of CSR
Detection Area
Deadline 02/17/2018
Integration Specifications:
3 Parallax Inc PING))) Ultrasonic Distance Sensors
1 Digital I/O PWM pin required per sensor
Data Processing in Arduino Sketch on Arduino Due
 | Required Specifications | Achieved Specifications | Requirements Satisfied
In-Plane Object Detection Parallax PING))) Ultrasonic Distance Sensor | Range – 3.125 ft (0.9525 m) Field of View – 103.5° Smallest Detectable Object – 1 in | Range – 9.85 ft (3 m) Field of View – 40*3 = 120° Smallest Detectable Object – 0.25 – 0.75 in (determined from tests from manufacturer) | SENS.3.1 SENS.3.1.1 SENS.3.1.2

## Slide 63: Off Ramp Option – Ultrasonic Sensors
Front of CSR
Detection Area
PWM Integration:
Utilizes 1 I/O pin per device for PWM control
Does not require specific digital PWM pins on the Arduino
  Digital PWM is controlled with one trigger and sensor has its own procedure

## Slide 64: Single Beam LiDAR Component Test
Results:

## Slide 65: Single Beam LiDAR Component Test
Results Analysis:
  The LiDAR inaccuracies were found to be too great and may be attributed to the test setup rather than the LiDAR itself
Reducing Error
  The power supply from the Arduino was suspected to be noisy, so the setup was altered so the power supply and ground were switched to the breadboard, but this had no effect on the results
  Further attempts to eliminate the noise/error will include additional tests with a filter (1 µF capacitor) located in between the ground and PWM input
  If this filter has no effect on the results, the circuit components may be soldered to eliminate breadboard losses
Setup: