## Slide 1: NanoSAM III Test Readiness Review
Company Customer: Ball Aerospace
Jaykob Velasquez & Jim Baer
Advisor: Chris Roseman
Presenters: Evan Hiemstra, Robert MacFarland, Amanda Nelson, Donny Wolfe, Andrew Haskett, Raymie Fotherby
Not Presenting: Austin Bathgate, Peter DiCerbo, Alex Israel
Notes: All of us

## Slide 2: Presentation Outline
Overview Schedule Test Readiness Budget
Project Overview
Schedule
Test Readiness
  Optical Alignment
  Vibration Testing
  Electronics and Software
Budget
Notes: Amanda

## Slide 3: Overview

## Slide 4: Aerosol Density Measurement Background
Overview Schedule Test Readiness Budget
[6]
(1978-1993)
SAM 1975 (ASTP)
SAM-II 1978
SAGE-I, -II, -III 1981-

## Slide 5: NanoSAM Project Background
Description Requirements Risks V&V Planning
NanoSAM II
(2020-2021)
Reduced size to 0.5U, split electronics board and initial vibration and thermal analysis
[6]
Notes: Merge slides 4 & 5

## Slide 6: NanoSAM III Goal From the Customer
Overview Schedule Test Readiness Budget
Preserve instrument performance through vibration testing
Improve structure of the NanoSAM II 0.5U design
Optimize mirror mounting bolt torque
Create vibe-proof filter mounts
Iterate on NanoSAM II electronics board
Notes: Baer: Goal: Preserve performance through vibration testing
How: Improve Structure of NanoSAM 2 0.5 U design
Add mirror registration features
Optimize mirror mounting bolt torque
Create vibe-proof filter mounts
Build vibe-proof “null optic” for testing
Iterate NanoSAM 2 electronics board

## Slide 7
Notes: Clean this up
This video takes a long time. Is it really necessary. The board has seen this before. How about a still with a brief reference to the previous presentation.
The hardest thing to do is to throw out good material once the time limit is exceeded.

## Slide 8: Project CONOPs
Overview Schedule Test Readiness Budget
Notes: This excellent video takes a lot of the limited time.

## Slide 9: Objectives
Overview Schedule Test Readiness Budget
Objective | Level 1 | Level 2 | Level 3
Payload Integration | Electronics interface with COTS CubeSat. | Same as Level 1. | Electronics and structure interface with COTS CubeSat.
Vibration Testing | No predicted resonant frequencies within test range. Vibe test performed, and resonant frequencies ID’d. | Same as Level 1. | Full 3-axis random vibe test performed & analyzed. No resonant frequencies within test range.
Optics | Optics designed to achieve 0.74 MTF pre and post L1 Vibration Testing. | Thermal study conducted to minimize deformation from temperature fluctuation. | Optics designed to achieve 0.74 MTF post L3 Vibration Testing and thermal vacuum testing.
Notes: “Pertubation” or “deformation” instead of “distortion” which has a technical definition in optics

## Slide 10: Objectives
Overview Schedule Test Readiness Budget
Objective | Level 1 | Level 2 | Level 3
Launch Ready | All systems functional and MTF of 0.74 post L1 vibe test. | Same as Level 1. | All systems functional and MTF of 0.74 post L3 vibe test and thermal vacuum test.
Electronics Boards | Provides all power and control functions from NS II without white wire fixes. | Same as Level 1. | Includes thermal control system to regulate bus temperature.
Data Capture | Electronics and software system correctly captures and stores data. | Required memory and data budget determined from downlink study. | Data can be transferred from payload to standard bus RF/Comms system.

## Slide 11: FBD
Overview Schedule Test Readiness Budget
Notes: Evan
Baer:

## Slide 12: Baseline Design Updates
Notes: Evan

## Slide 13: Major Design Changes
Overview Schedule Test Readiness Budget
Orthogrid walls* to prevent drumming in structure walls
Aligned aperture plate with mirror to 75 ㎛tolerance
Resized bus mount holes to fit standard CubeSat interface
Designed tool to aid in shimming process
*Orthogrid panels are hollowed-out structures, similar to isogrid, which utilize rectangular patterns instead of triangular patterns to maintain strength while reducing weight

## Slide 14
Overview Schedule Test Readiness Budget
5.32 cm
9.33 cm
9.91 cm
Notes: Evan - dimensions, remove sides, structure

## Slide 15
Overview Schedule Test Readiness Budget
Orthogrid walls
Resized bus mount holes
Notes: Evan - dimensions, remove sides, structure

## Slide 16
Overview Schedule Test Readiness Budget
Return Sphere
Filter Mounts
OAP Pins
Holding Tool
Centered Aperture

## Slide 17: Major Design Changes - Electronics
Overview Schedule Test Readiness Budget
Large electrical overhaul of “white wire” fixes
  Retained:
    Microcontroller
    Software Structure
    Flash Memory Configuration
    Photodiode Measurement Circuit Topography
    Current Sense Monitor w/ Small Configuration Changes
  Eliminated:
    Additional 16 bit ADC (redundant data and only require 12 bit resolution from Teensy)

## Slide 18: Critical Project Elements
Overview Schedule Test Readiness Budget
CPE | Rationale
Structure - robust to vibration | Instrument must function after launch and be aligned to collect quality data
Optics - match SAM-II instrument performance | NanoSAM can provide SAM-II quality data at smaller cost & size
Electronics & Software | Electronic boards must communicate with COTS bus to correctly collect mission data

## Slide 19: Schedule

## Slide 20: Schedule - Build and Testing
Overview Schedule Test Readiness Budget
Notes: 1st alignment Feb 25, next March 4, another week of margin
First vibe test March 17, Alignment check test March 18th
Contingency dates: March 28th, Alignment Check April 1st

## Slide 21: Full Schedule
Overview Schedule Test Readiness Budget

## Slide 22: Test Readiness

## Slide 23: Optical Alignment Testing - Purpose
Overview Schedule Test Readiness Budget
Requirements: 4 (4.0, 4.2, 4.2.2, 4.2.3)
  4.0/4.2 : NS3 will have optical performance equivalent to or surpass that of SAM-II’s idealized optical performance in alignment verification tests
  4.2.2: The optical alignment must be within the allowable max displacement error
Align optics system with interferometer, conduct vibration testing, then conduct alignment testing again to determine and resolve the performance of the optical system due to vibration effects
Notes: Optical alignment will be conducted to measure and reduce the misalignment of the system
Characterize adequate performance to resolve vibration effects

## Slide 24: Optical Alignment Testing - Overview
Overview Schedule Test Readiness Budget
Initial alignment of NS3 bench on Feb. 25th, March 4th
  Reduce Zernike Coefficients using interferometer using newly manufactured optical bench (including coated sphere, OAP with optimized 2 in-lb of torque)
  Two four hour sessions
Vibrational Testing either March 17th or 28th
Final alignment testing March 18th or April 1st
  Confirm optical requirements hold after vibration testing
  Repeat alignment procedure driving down Zernike Coefficients and RMS
  Only one session predicted to be needed
Notes: the test is measuring how much degradation is induced by vibration exposure.

## Slide 25: Optical Alignment Testing - Facilities
Overview Schedule Test Readiness Budget
Optical Testing Lab at Ball Aerospace, Boulder campus
Sessions are coordinated with our customer, Jaykob Velasquez

## Slide 26: Optical Alignment Testing - Test Fixtures
Three Axis Mount
Tip-tilt Stage
Optical Breadboard
OAP, Mounting Plate, Optical Bench
Torque Wrench
Note - Mounting plate will be replaced with NanoSAM III side wall for alignment of the full system with the pressure mount.
Reflecting sphere
Ball Aerospace Equipment
NanoSAM III Equipment
Notes: It isn't so much that the force is reproducible as it holds the stack in two directions while the force is applied to hold the third and fix those two by friction.

## Slide 27: Optical Alignment - Previous Alignment Sessions
Optics team has conducted 3 previous alignment sessions
  All sessions with previous optics bench
  3rd session determined relationship between torque and deformation of OAP
  Experimentally determined 2 in-lb as the ideal torque amount for the OAP
Notes: Slide 26 Suggestion: Simplify and make text larger. Include only Z9 Z10 and RMS in big legend in open space on graph. Minimum RMS is the goal

## Slide 28: Optical Alignment - Risk Reduction
Detailed alignment procedure and calculations created to streamline testing process while in lab

## Slide 29: Optical Alignment Testing - Risk Reduction
Overview Schedule Test Readiness Budget
Full clean room garb is required for testing in Ball facilities
Optimal torque specifications determined will reduce deformation risk in alignment.

## Slide 30: Vibration Testing - Purpose
Overview Schedule Test Readiness Budget
Requirements: 1.0 (1.1.1, 1.1.2), 3.0 (3.2, 3.4), 4.0 (4.2)
  1.0: System will survive (i.e. components will remain intact, in place, and functional) through a 20-2000 Hz random vibration range simulating a launch
  3.0: Electronics components will survive random vibrations simulating a launch
  4.0: Optical components will survive random vibrations simulating a launch

## Slide 31: Vibration Testing - Purpose
Overview Schedule Test Readiness Budget
Testing will be conducted after alignment of the optical systems and prior to a second test ascertaining whether alignment has been retained post-vibration and that the optical instrument will survive
Ensure the subsystems and overall system can survive a launch-like environment
NASA-STD-7001b Random Vibration

## Slide 32: Vibration Testing - Test Fixtures
Overview Schedule Test Readiness Budget
Designing mounting bracket specifically for simulating the mounting configuration the NanoSAM III instrument would be in when integrated with COTS systems
Mounting bracket attaches to vibration table and to NanoSAM III instrument

## Slide 33: Vibration Testing - Facilities
Overview Schedule Test Readiness Budget
Utilizing the vibration tables in the Aerospace building and accelerometers provided
May team up with other teams to share costs of testing and of any additional accelerometers that could be needed
Altius Space Systems’ Vibration Table used by NS-II

## Slide 34: Vibration Testing - Overview
Overview Schedule Test Readiness Budget
Perform baseline sine sweep vibration on mounting bracket so we can isolate, remove natural frequency of bracket in analysis
3 random vibration tests - once per axis
  Accelerometers will be placed in areas of interest and areas of concern due to possible resonance from modeling (filter mount, thermal isolators, side walls, PCBs, diode block)
  Performed at intervals from NASA-STD-7001b
Accelerometer output will be put through a Fast Fourier Transform (FFT)
  Looking for frequencies in 20 - 2000 Hz random vibration range
Notes: Vibe table is unidirectional so have to vibrate on each axis

## Slide 35: Vibration Testing - Risk Reduction and Results
Overview Schedule Test Readiness Budget
Iterative modeling allows better understanding of system behavior during vibration
  Redesigned components based on CDR feedback to increase natural frequencies of components, overall system
ANSYS results from last year were fairly accurate in modeling real results, can satisfy our requirements even with 30% error
  NS-II: 7.3% error at location of ωn,1 (840 Hz ANSYS, 901.1 Hz actual)
  NS-III: ωn,1 = 2930 Hz = 1.465*ωmax_range worst sim
  NS-III: ωn,1 = 5736.5 Hz = 2.868*ωmax_range best sim
Notes: Orthogrid walls
Hole size change - my bad!
Wider isolator panels?

## Slide 36: Electronics and Software Testing - Purpose
Overview Schedule Test Readiness Budget
Major design requirements:
2.0: Electronics and software will collect and store data
3.0: Electronics system will control and power all payload subsystems, while remaining resilient to launch (vibration) and operation (thermal) environment.
Notes: Electronics system will control and power all payload subsystems, while remaining resilient to launch and operation environment.
Picture idea: show electronics design/FBD, picture of teensy, pcb design pic, icons for thermal testing(fire),
At CDR we showed our that conceptual design satisfied these requirements, now we will explain the testing process proposed to verify them
At CDR we showed our that conceptual design satisfied these requirements, now we will explain the testing process proposed to verify them

## Slide 37: Electronics and Software - Test Breakdown
Overview Schedule Test Readiness Budget
Subcategories:
E-TEST1: Photodiode Characterization
E-TEST2: Teensy 4.0 Standalone Verification
E-TEST3: Analog Subcircuit Verification / PCB Integration
E-TEST4: Digital I/O and Flash Storage Testing
Tests 1 & 2 performed prior to PCB arrival (can begin early as Feb. 23)
Tests 3 & 4 conducted after PCB arrival (estimated March 11)
PCBs installed in payload and run after vibration testing to verify continued functionality
← Photodiode (THOR Labs FD11A)
Teensy 4.0 Microcontroller ↓
Notes: STAR: Placed to let PAB know we won’t really dive into vibration testing in this electronics section

## Slide 38: Electronics and Software - Photodiode Characterization
Overview Schedule Test Readiness Budget
Photodiode response varies with temperature and reverse bias voltage
  NanoSAM III operates 0 - 50 °C with 5 V reverse bias
  Datasheets only have response at 25 °C with 10 mV reverse bias
Equipment:
5V Power Supply ✔ | Assorted Passive Components ✔
Multimeter ✔ | Breadboard ✔
Laser (power and wavelength well characterized) ⍻ | Photodiode ✔
Notes: For the laser, our teammate Raymie has spoken with the EE department about securing a He-Ne laser for use
Concern: not yet sure if we can access laser outside of lab to apply testing at various temperatures
General trend of doubled response for every 10 °C temperature increase
-Must know response variation to counteract it with software and record proper solar attenuation measurements

## Slide 39: Electronics and Software - Photodiode Characterization
Overview Schedule Test Readiness Budget
Setup
  Photodiode placed in breadboard with -5V bias
  Photodiode current output sent to transimpedance amplifier to create voltage
  He-Ne (632.8 nm) laser beam with Abeam < Adiode aligned incident with the photodiode active area
    Active area smallest dimension = 1.1mm
    Typical beam diameter = 0.48 - 0.52 mm
Notes: Transimpedance setup required as current is ~pA which generally cannot be measured with standard multimeter
Transimpedance setup will use the same R and C values as in actual design.
Datasheet value is at 25degC
Most beams have 0.5 mm diameter, so no area problem

## Slide 40: Electronics and Software - Photodiode Characterization
Overview Schedule Test Readiness Budget
Process
  Measure output voltage at:
    3 temperatures
    3 well characterized laser power levels
  Verify linear current to optical power relation
  Extrapolate to mission wavelength (1020 nm)
Results
  Known photodiode response variation with temperature
  Known relation between incident optical power and output voltage (current) to compare to datasheet
TEST
(632, 0.44)
MISSION
(1020, 0.4)
Notes: Nano SAM II did not perform this characterization and used thermal data from a completely different photodiode
Transimpedance setup required as current is ~pA which generally cannot be measured with standard multimeter
Transimpedance setup will use the same R and C values as in actual design.
Datasheet value is at 25degC
Most beams have 0.5 mm diameter, so no area problem
Will have 0.4/0.44 = 90.9% current produced per optical watt compared to test wavelength
If needed, adjust R and C in amplifier

## Slide 41: Electronics and Software Testing - Teensy 4.0 Standalone Verification
Overview Schedule Test Readiness Budget
Microprocessor collects analog data and sends data to storage and communications
  Can identify software bugs and microprocessor issues before PCB arrives
Equipment:
5 V Power Supply ✔ | Breadboard ✔
Variable Power Supply ✔ | Computer ✔
TTL UART to USB converter (Adafruit 954) ✔ | Assorted Passive Electronic Components ✔
Teensy 4.0 Underside 🡱
Adafruit 954 Adapter 🡳
Notes: Adafruit adapter most important for data to board through pins as it steps down 5 V to 3.3 V to not damage board

## Slide 42: Electronics and Software Testing - Teensy 4.0 Standalone Verification
Overview Schedule Test Readiness Budget
Setup
  Power Teensy 4.0 with 5V and connect to computer through USB during analog testing
  Variable power supply used to simulate voltages for analog testing
Process - Analog
  Simulate 3 voltages for each analog subcircuit
  Compare recorded measurements to actual values
+
-
Analog Input Pins A0 - A9 (6 req.)
Notes: Or to CPU via digital out pin and GND during TTL UART testing setup
Adafruit Adapter allows read in of 3.3 V TTL UART to a 5 V CPU input
We use 6 Ain pins: 3 for the three thermocouples, 1 for battery voltage, 1 for bus current, 1 for photodiode
I.e. Send some voltages corresponding to photodiode incident optical power and ensure the Teensy 4.0 returns optical power values as characterized in E-TEST 1 for the test voltages

## Slide 43: Electronics and Software Testing - Teensy 4.0 Standalone Verification
Overview Schedule Test Readiness Budget
Process - Digital
  Load mock data file to Teensy via USB
  Output data via Dx (referenced to ground) to computer via probe
  Repeat for 3 files
  Compare sent and received data, count any bit mismatches
  Repeat, but input through Dy pin and output via USB
Results
  Analog input testing verifies the microcontroller can process analog data
  Digital testing confirms the microprocessor is set up to send and receive TTL UART signaling
Notes: Intermediate test to ensure we can send proper UART data to the RS-422 transceiver - this is why we’re doing it
Adafruit Adapter allows read in of 3.3 V TTL UART to a 5 V CPU input
** Possibly use Arduino language instead of MATLAB for read in.
through the TTL UART USB adapter - removed from bullett 3 but just know we have an adapter to accomplish this

## Slide 44: Electronics and Software Testing - Analog Subcircuit Verification and PCB Integration
Overview Schedule Test Readiness Budget
By the time the PCB arrives, we have already:
  Verified the photodiode response
  Verified the Teensy 4.0 correctly reads analog voltages
Need to verify PCB connections and voltages
Repeat E-TEST3 after integration and vibration testing
Equipment:
Populated PCBs w/ Test Ports ⍻ | USB Cable ✔
12V Power Source ✔ | Computer ✔
Multimeter with small probes ⍻ | 
*Subcircuit Schematics in Backup Slides
12V Bus
PCB
Multimeter
Notes: Speak with Trudy to confirm access to needle probes
PCB is in creation so I left it marked yellow (intermediate status)

## Slide 45: Electronics and Software Testing - Analog Subcircuit Verification and PCB Integration
Overview Schedule Test Readiness Budget
Setup
  Power PCB stack with 12V power supply
  Connect Teensy 4.0 to computer for data verification
Process
  Verify all PCB power lines on both boards (+/- 5 and 3.3 V) using the multimeter
  Verify expected voltages are produced by all analog subcircuits
    Bus Current
    Bus Voltage
    Photodiode Circuit
    Thermal Measurement
    Thermal Management
12V Bus
PCB
Multimeter
Notes: IMPORTANT***”Let’s expand on the thermal measurement & management circuit, as the photodiode circuit testing will be analogous to E-TEST1 and the remaining analog circuits of item 2 are trivial to test”

## Slide 46: Electronics and Software Testing - Thermal Circuits
Overview Schedule Test Readiness Budget
Thermal Measurement
  Place PCB stack and all 3 thermocouples in temperature controlled environment until steady state is reached
    Record temperature from thermocouple
    Repeat for 3 temperatures
Thermal Regulation
  Verify that the three heaters turn on at temperatures below 2.5°C and off above 5.5°C
    Place outside or in freezer with T < 2.5°C and monitor thermocouples and digital state of heater
    System verified if heaters switch on and temperature increases
10 W Photodiode Heater (L)
1.5W Board Heating Resistor (R) [X4]
Notes: Adjust thermocouple R - T relation if necessary
Code will be written to pull a thermal measurement after a user specified time, allowing the Teensy to remain in oven and collect measurement
Could get a very accurate 0C thermal measurement if placed in sealed container in ice water - I’m scared to do this however
Useful notes:
Bounds are set to allow hysteresis and ensure we never drop below acceptable operating temperatures
No concern regarding over temperature
If can head outside where we have convection - system should be validated for vacuum application

## Slide 47: Electronics and Software Testing - Analog Subcircuit Verification and PCB Integration
Overview Schedule Test Readiness Budget
Results
  Following success of E-TEST3 pre vibration testing, the team can confirm:
    All analog subcircuits (including the power system) are functioning as expected
    PCB layout / continuity is confirmed
    Teensy 4.0 is fully integrable with analog subcircuits on the PCB
  The items of E-TEST3 will be repeated following vibration of the entire payload
    Will confirm PCB and electronic components are launch ready
    If E-TEST3 is successful, we have verified FR 3.0

## Slide 48: Electronics and Software Testing - Digital I/O and Flash Storage
Overview Schedule Test Readiness Budget
Expansion on E-TEST2 Software testing
Process
  Activate data collection mode
  Disconnect from computer and wait 2 hours for data capture
  Reconnect RS-422 output to computer USB
  Initiate data transfer mode and analyze collected data
Results
  E-TEST4 will verify that the electronics system can capture, store, and transfer data from each sensor (FR 2.0)
128 Mb Flash Memory Chip

## Slide 49: Electronics and Software Testing - Risk Reduction and Results
Overview Schedule Test Readiness Budget
E-TEST1 and E-TEST2 allow software debugging and photodiode characterization to occur in parallel with PCB assembly
  Iterative software development will allow fast turnaround
Most critical electronics components have already arrived
  Remaining testing devices are being sourced

## Slide 50: Budget

## Slide 51: Cost Plan as of TRR
Overview Schedule Test Readiness Budget
Current Budget (2/13/22):
$2,238.94 remaining
22.2% of the budget are Optical components - this is due to the high cost of the off-axis parabolas and windows
Lower costs overall since CDR estimate due to shipping over-estimate

## Slide 52: Cost Plan as of TRR
Overview Schedule Test Readiness Budget
Largest expected expense will be E-board manufacturing and return sphere coating, causing a 9% increase for Manufacturing & Testing
Increase in Electronics, estimate for remaining small unordered components (resistors)
Still plenty of funds for additional materials/components or higher manufacturing costs

## Slide 53: Critical Components
Overview Schedule Test Readiness Budget
All of our critical components have already arrived!
This includes enough major electronic components for 4 boards (2 extra)
Extra optical components in case of anomaly
Raw materials for the structure were relatively cheap, and usually arrive within 3 business days if more is ever needed

## Slide 54: Pending Components
Overview Schedule Test Readiness Budget
Only approximately $45 worth of passive electronic components have yet to be ordered
Now only limited by manufacturing of structure and special components (return sphere chrome coating and E-boards)
Extra budget in place for additional purchases if needed

## Slide 55: Questions?

## Slide 56: Vibration/Design ANSYS Results - Backup Slides
Orthogrid Patte
Orthogrid Pattern 1 Results - 2929.9 Hz
Orthogrid Pattern 2 Results - 3428.3 Hz
Orthogrid Pattern 3 Results - 3468.9 Hz

## Slide 57: Vibration/Design ANSYS Results - Backup Slides
Orthogrid Pattern 4 Results - 4686.4 Hz
Orthogrid Pattern 5 Results - 5736.5 Hz

## Slide 58: Optics Backup Slides - Cut Shims
Focus shim (top)
In-plane shim (bottom right)
Out-of-plane shim
(bottom left)
1 - 8, 1.5, 10, 12, 15 mil widths, 7 of each width for each shim type

## Slide 59: Major Design Changes - Electronics
Overview Schedule Test Readiness Budget
Power System - Efficiency and Noise
  Current calculations ensure our system is not current deficient on any line ✓
    Largest issue of last year’s design
  Switching converters → LDO regulators to greatly improve power efficiency (91% vs 42%)
  Theoretical noise reduced to < 0.1*LSB = 86 uV
    Theoretical 5.62 uV on noisiest line (LTSpice)
  Use of SHDN / RUN pins on -5V line and ICs to further reduce power draw
Fine Tuned Thermal Measurement Circuit (w/ Zero Drift Op-Amps)
12 V Thermal Management System
Battery Voltage Monitor
Characterize Photodiode (I vs T)
RS-422 Compatibility
Vibration Resilient PCB & Mounting Scheme
*Subcircuit Schematics in Backup Slides 55 - 60

## Slide 60: Electronics Backup Slides - Photodiode Characterization
Overview Schedule Test Readiness Budget
Setup
  Photodiode is placed in breadboard with -5V bias
  Photodiode current output sent to transimpedance amplifier setup to create voltage
  He-Ne (632.8 nm) laser beam with Abeam < Adiode is aligned incident with the photodiode active area to be switched on
Process
  At 3 different & well spaced thermal values measure:
    The output voltage due to reverse bias and extrapolate to the dark current value
    The voltage produced when the laser is incident at three well characterized power levels
    Extrapolate to mission wavelength (1020 nm)
Results
  We now know how photodiode response varies with temperature
  We have an accurate relation between incident optical power and output voltage (current) to compare against the datasheet value
TEST
(632, 0.44)
MISSION
(1020, 0.2)
Notes: Transimpedance setup required as current is ~pA which generally cannot be measured with standard multimeter
Transimpedance setup will use the same R and C values as in actual design.
Datasheet value is at 25degC
Most beams have 0.5 mm diameter, so no area problem

## Slide 61: Electronics Backup Slides - Power System

## Slide 62: Electronics Backup Slides - Current Sense Monitor

## Slide 63: Electronics Backup Slides - Battery Voltage

## Slide 64: Electronics Backup Slides - Thermal Measurement

## Slide 65: Electronics Backup Slides - Thermal Management

## Slide 66: Electronics Backup Slides - Photodiode Circuit

## Slide 67: Budget Spreadsheet
https://docs.google.com/spreadsheets/d/1B1svmDuzSfzn3HrgvEBAslalyRTiLjUBkwg8rXMZBvw/edit#gid=0