## Slide 1: PRELIMINARY DESIGN REVIEW OCTOBER 20TH, 2021 ASEN 4018-011
Customer:
Richard Schaden
Faculty Advisor:
Dr. Donna Gerren
Presenters:
Fernando Chavez, Finn Bailis, Emerson Beinhauer, Christl Haley, Carlin Hornbostel, Tomaz Remec
Additional Team Members:
Nathan Braunstein, Jake Pendergast, Tristan Martinez, Julia Tucker

## Slide 2: PRESENTATION OUTLINE
Project Overview Emerson Beinhauer
Feasibility: Design Christl Haley, Carlin Hornbostel, Tomaz Remec
Feasibility: Testing Fernando Chavez
Feasibility: Manufacturing Finn Bailis
Feasibility: Budget Finn Bailis
Feasibility Conclusions Emerson Beinhauer
Future Work Emerson Beinhauer
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: We can always change this -- but we do need to decide for sure at some point

## Slide 3: Background Mission Statement Concept of Operations Functional Requirements Critical Project Elements Feasibility Elements PROJECT OVERVIEW Presented by: Emerson Beinhauer

## Slide 4: PROJECT BACKGROUND
Customer Richard Schaden sees need for clean-sheet, zero-emission aircraft
Gap in the market for fully electric mid-sized transport aircraft
Concern: General Aviation industry’s contribution to Global Warming, 100LL production, future travel, nonrenewable propulsion source
Beyond Aviation: All Electric Cessna 172
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: 2 hour endurance and 75 nautical mile range should be discussed here since they were mission specs
It's no surprise that air travel is a very popular form of transportation which continues to grow over the years. Unfortunately though air travel is one of the more environmentally damaging activities as it is responsible for various amounts of carbon dioxide and greenhouse gas emissions which contribute to things like global warming. For this reason transportation industries have been looking at different alternatives for gas for quite some time and this is no different for the aviation industry. The desire for a zero emissions aircraft would be valuable and alot of research has gone into solutions for both large scale commercial operations as well as small scale trainers. There is a bit of a niche market where the design space has been left a bit unexplored in the mid size general aviation industry which is where our project comes into play.

## Slide 5: MISSION STATEMENT
No Emission, Low Drag Airframe (NELDA), will provide the customer, Richard Schaden, a clean-sheet airframe design concept for a general aviation airplane which includes drawings, scale models, and aircraft performance parameters. The design will emphasize fully-electric powertrain considerations and aerodynamic efficiency.
Customer Specified NGO’s
Need: Clean-sheet design
Goal: Explore design parameter space to estimate performance of an optimized clean-sheet design
Objective: Airframe design; model test; analysis
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: To summarize this our mission statement is as follows.No Emission, Low Drag Airframe (NELDA), will provide the customer, Richard Schaden, a clean-sheet airframe design concept for a general aviation airplane, which includes drawings, scale models, and a feasibility analysis. The design will emphasize fully-electric powertrain considerations and aerodynamic efficiency.

## Slide 6: CONCEPT OF OPERATIONS
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: On the aircraft design portion of this project the following mission outline and concept of operations have been identified. Our client would like an aircraft that can carry 6 passengers at a speed of 150kts for 2 hours with ….
Increase words in CONOPS on bottom (Font Size?)

## Slide 7: FUNCTIONAL REQUIREMENTS
Number | Name | Description
FR1 | Classification | The designed aircraft shall be classified as a Class I Light, General Aviation aircraft that emits zero greenhouse gases during standard operation.
FR2 | Crew | This General Aviation aircraft shall accommodate one crew member and five passengers.
FR3 | Mission Performance | The aircraft shall have a maximum range and endurance comparable to or exceeding the performance of six-passenger electric aircraft currently under certification.
FR4 | Wind Tunnel Model (WTAV) | A non-powered, scale model of the airframe design will be constructed for the purpose of comparative wind tunnel analysis in the PILOT Lab Wind Tunnel.
FR5 | Glider Model (CSD) | A non-powered, larger scale glider model of the airframe design will be constructed for the purpose of stability analysis and verification.
FR6 | Stability | The full-scale aircraft shall be designed to be statically and dynamically stable.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: For this reasons the following functional requirements have been identified…
Scaling CG and adjusting weight
Emphasize how we are using the wind tunnel for comparative analysis only
WTM - comparative analysis

## Slide 8: CRITICAL PROJECT ELEMENTS
Number | Name | Description
CPE1 | Electric Aircraft Design Space Analysis | Similar aircraft must be researched to establish baselines and bases of comparison
CPE2 | Airframe Design | Aerodynamically efficient; six passengers; 150 kias; fully electric
CPE3 | Computational Simulation | MATLAB, SolidWorks CFD, and AAA will serve as a guide for analysis, prediction, verification, design/model iteration
CPE4 | Manufacturing | Scale models will need to be constructed for Practical Testing
CPE5 | Practical Testing | Wind Tunnel Aerodynamic Validation (WTAV), and Characteristic Stability Demonstration (CSD)
CPE6 | Budget | Course funding limitation: $5,000 (Not a customer requirement)
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 9: FEASIBILITY ELEMENTS
D
T
M
B
Section | CPEs | Requirements | Feasibility
Design | CPE1, CPE2, CPE3 | FR1, FR2, FR3, FR6 | ✅ or ✖?
Testing | CPE5 | FR4, FR5, FR6 | ✅ or ✖?
Manufacturing | CPE4 | FR4, FR5 | ✅ or ✖?
Budget | CPE6: Course funding limitation is $5,000 |  | ✅ or ✖?
Feasibility will be tracked through each section with this bar on the bottom right (green = feasible)
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 10: Powertrain Clean-Sheet Design Motivation Baseline Configuration AAA Weight Analysis Computational Analysis Aerodynamic Analysis Computational Fluid Dynamics (CFD) DESIGN FEASIBILITY Presented by: Carlin, Christl, and Tomaz
Notes: Based on the entire scope of the project and after meeting with PAB, engineers, etc we have determined the following are critical project feasibility elements

## Slide 11: POWERTRAIN (SOLID STATE BATTERIES)
Volumetric Energy Density | Specific Energy
580 Wh/kg | 1377 Wh/L
Why is NELDA only an airframe design?
NELDA’s goal is to design a particularly low-drag airframe capable of housing a cutting edge battery bank
However, known weight, volume, and power output of this battery bank is crucial to the aircraft design
In-depth battery chemistry/performance analysis is outside of the project scope
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 12: CLEAN-SHEET DESIGN MOTIVATION
Why not retrofit an existing airframe for zero-emissions capability?
Mr. Schaden retrofitted a Cessna 172 Skyhawk with lithium ion batteries equal in weight and volume to the fuel it would have otherwise carried
While successful, the newly electric aircraft was far from optimal
  Low endurance/range stemming from substantial drag
  Airframe was not designed around efficiency, rather ease of manufacture
  Design space was poorly understood due to limited diversity with limited experience
D
T
M
B
FR1: The designed aircraft shall be classified as a Class I Light, General Aviation aircraft that emits zero greenhouse gases during standard operation.
FR3: The aircraft shall have a maximum range and endurance comparable to or exceeding the performance of six-passenger electric aircraft currently under certification.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Design space CASE STUDY- Most aircraft are designed around engines, the current design space accounts for fuel and in order to be most effective to our client we need to look at all options available. I.e. if we don't need to account for fuel how does the design space open up - by looking at all options we could find something a design point a designer/engineer overlooked when designing an aircraft which needs fuel.
Most general aviation aircraft are designed safe in the knowledge that engines with an abundance of power are available, and thus efficiency is not truly optimized. Our customer tasked us with reevaluating the

## Slide 13: CLEAN-SHEET DESIGN MOTIVATION
R | Range
E | Energy
𝜂total | Efficiency
L/D | Lift-to-Drag ratio
m | Mass
g | Acceleration due to gravity
*Full derivation in BackUp Slides
D
T
M
B
FR1: The designed aircraft shall be classified as a Class I Light, General Aviation aircraft that emits zero greenhouse gases during standard operation.
FR3: The aircraft shall have a maximum range and endurance comparable to or exceeding the performance of six-passenger electric aircraft currently under certification.
Adapted version of Breguet Range Equation with no decrease in induced drag due to fuel loss
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Describe variables and talk through it and go through why it was used
Put this before and justify motivation so AAA goes after
Still need to describe the equation

## Slide 14: BASELINE CONFIGURATION
Independent Trade Studies → Not final design decisions
D
T
M
B
Trade | Baseline Selection
Wing Vertical Mount | Mid Mounted
Wing Horizontal Mount | Aft
Wing Shape | Rectangular
Aspect Ratio | 10-14
Wing Airfoil Shape | N-22
Wing Dihedral | Positive Dihedral (Γ > 0)
Tail Configuration | V-Type
Landing Gear | Fixed Tricycle Configuration
Power Source | Solid State Batteries
Primary Material | Carbon Fiber Reinforced Plastic
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
*** Just Preliminary Reference
Notes: Baseline design from CDD
Describe Canard in this slide
Why those are in there
Midmounted wing, aft,
WHY each parameter is chosen

## Slide 15: AAA WEIGHT ANALYSIS
D
M
T
B
D
T
M
B
FR3: The aircraft shall have a maximum range and endurance comparable to or exceeding the performance of six-passenger electric aircraft currently under certification.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Circle design point ✅
HOW TO DESCRIBE THE GRAPH
1.) Where did the data come from?
2.) Point and state axes
3.) Describe the legend 4.) Describe the trends
5.) Results
6.) Conclusions

## Slide 16: AAA WEIGHT ANALYSIS
Comparison of Two Linear Relationships
Summation of Empty, Payload, and Crew Weight to determine Takeoff Weight
Logarithmic Regression of Relationship Between Takeoff and Empty Weight
D
T
M
B
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Does empty weight include batteries?
HOW TO DESCRIBE THE GRAPH
1.) Where did the data come from?
2.) Point and state axes
3.) Describe the legend 4.) Describe the trends
5.) Results
6.) Conclusions

## Slide 17: AAA WEIGHT ANALYSIS
Performance Plot
D
M
T
B
D
T
M
B
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: HOW TO DESCRIBE THE GRAPH
1.) Where did the data come from?
2.) Point and state axes
3.) Describe the legend 4.) Describe the trends
5.) Results
6.) Conclusions

## Slide 18: AAA PERFORMANCE VERIFICATION
AAA Range and Endurance Estimates Verified with Computational Models
Variable | NELDA | Cessna 206 | Percent Difference
Takeoff Weight [lbs] | 3,800 | 3,600 | +5.5%
Empty Weight [lbs] | 2,650 | 2,116 | +25%
Power Required [hp] | 346 | 310 | +11.6%
Oswald’s Efficiency | 0.8908 | 0.75 | +14%
Wing Span [ft] | 45.7 | 34.9 | +31%
Wing Area [ft2] | 174 | 174 | 0%
D
M
T
B
D
T
M
B
FR3: The aircraft shall have a maximum range and endurance comparable to or exceeding the performance of six-passenger electric aircraft currently under certification.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 19: COMPUTATIONAL ANALYSIS
MATLAB Models
Started with baseline weights, wing area, and AR used in AAA
Capable of returning aerodynamic characteristics including Lift-to-Drag Ratio, Span Efficiency Factor, CL, CD , and CL/CD vs 𝛂 plots, CDo and Range Estimates
Assist the design team with independently verifying and validating AAA results
Gives the team insight into the interdependencies of design choices
D
M
T
B
D
T
M
B
FR3: The aircraft shall have a maximum range and endurance comparable to or exceeding the performance of six-passenger electric aircraft currently under certification.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: 1 sentence explanation of vortex panel/pllt
Vortex panel: ideal flow over thick airfoils using
Pllt:

## Slide 20: COMPUTATIONAL ANALYSIS
RANGE
Range estimated computationally using extrapolated battery efficiency and energy density estimates
Range = 150 NM
R | Range | ebat | Battery Energy Density
E0,tot | Total Energy at takeoff | WOE | Empty Weight
𝜂2 | Propulsive Efficiency | WPL | Payload Weight
𝜂3 | Battery Efficiency | L/D | Lift-to-Drag Ratio
g | Acceleration due to gravity |  | 
D
T
M
B
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Carlin
Eta 1 and eta 1 are propulsive and battery efficiency, L/D is lift to drag
ebat is energy density of the battery, E,tot is total energy at takeoff, and Woe and Wpl are the operating empty and payload weights respectively

## Slide 21: AERODYNAMIC ANALYSIS
AAA vs. Computational model comparison
AAA Range and Endurance Estimates Verified with Computational Models
Variable | AAA | Matlab Model | Percent Difference
L/D | 9.79 | 8.67 | -12.9%
CD0 | 0.0391 | 0.01828 | -113.9%
Oswald’s Efficiency | 0.8908 | 0.9728 | +8.2%
D
M
T
B
D
T
M
B
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Compare matlab results to AAA results
Comment from Jake: Maybe add tiny bit of verbiage here about the differences in models, emphasize why these 3 parameters are the most important, and maybe why we don't have other variables in this table
Under estimation
Under estimation of Cd0 due to:
Over estimation of Oswalds due to:

## Slide 22: COMPUTATIONAL FLUID DYNAMICS
Limitations
Precision
  Design team cannot be confident in results due to lack of knowledge in the models underlying CFD software
  Different programs/models vary in precision due to a variety of factors
    Requires intricate understanding of the models to account for inconsistencies
Practical Utility
  Limited due to complex geometries, aforementioned limitations, etc.
D
T
M
B
FR3: The aircraft shall have a maximum range and endurance comparable to or exceeding the performance of six-passenger electric aircraft currently under certification.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 23: COMPUTATIONAL FLUID DYNAMICS
Value
Qualitative analysis of flow
  Flow visualization
  Can observe general trends such as localized
  Relative velocity/pressure hotspots
Individual component modeling
  Effect of wingtips/winglets on downwash vortices
  Aerodynamic fairings on landing gear
D
T
M
B
FR3: The aircraft shall have a maximum range and endurance comparable to or exceeding the performance of six-passenger electric aircraft currently under certification.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 24: FEASIBILITY TRACKING: DESIGN
D
T
M
B
Section | CPEs | Requirements | Feasibility
Design | CPE1, CPE2, CPE3 | FR1, FR2, FR3, FR6 | ✅
Preliminary Concern | CPEs | Addressed? | Feasibility
AAA Baseline Weight/Performance | CPE1, CPE2 | Yes: Work Needed | ✅
Computational Analysis | CPE1, CPE2 | Yes: Work Needed | ✅
Aerodynamic Analysis | CPE2 | Yes: Work Needed | ✅
CFD | CPE3 | Yes: Very Limited Utility | ✅
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: provide evidence that the project objectives, is feasible, i.e. can be accomplished within the constraints of technology and the senior projects course (time, skills, money, facilities, etc.).

## Slide 25: Wind Tunnel Testing Wind Tunnel Testing Sensors Glider Testing TESTING FEASIBILITY Presented by: Fernando Chavez
Notes: Put testing before manufacturing

## Slide 26: WIND TUNNEL TESTING
D
T
M
B
Wind Tunnel Aerodynamic Validation (WTAV)
Quantitative aircraft model comparison between NELDA & Cessna 206
  Limited precision due to test section size and airflow speeds
  Verification and validate computational models
  Evaluate design decisions to predict full scale efficacy (i.e. wing shape, winglets, gear)
Rationale emphasis:
  Prove aerodynamic efficiency against an existing six-passenger GA aircraft (Cessna 206)
FR3: The aircraft shall have a maximum range and endurance comparable to or exceeding the performance of six-passenger electric aircraft currently under certification.
FR4: A non-powered, scale model of the airframe design will be constructed for the purpose of comparative wind tunnel analysis in the PILOT Lab Wind Tunnel.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: What do you specifically mean by “still a need for verification and validation’???

## Slide 27: WIND TUNNEL TESTING
Aerolab Educational Wind Tunnel
Wind Tunnel Specifications
Test Section Dimensions:
  12” x 12” x 24” (30.5cm x 30.5cm x 61cm)
Airspeed:
  10 → 145 mph (4.5 → 65 m/s)
  Nominal speed of 25 → 40 m/s with test subject (rough estimate)
D
T
M
B
FR3: The aircraft shall have a maximum range and endurance comparable to or exceeding the performance of six-passenger electric aircraft currently under certification.
FR4: A non-powered, scale model of the airframe design will be constructed for the purpose of comparative wind tunnel analysis in the PILOT Lab Wind Tunnel.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: It is important to note that NELDA will have priority access to Wind Tunnel
Airspeed will be maximized by reducing blockage area in test section
  Depends on hardware (sensor + test-stand) setup and selection
  Depends on Size of NELDA or Cessna 206 models (i.e Test Subject)
  Depends on Variation in AoA of test subject

## Slide 28: WIND TUNNEL TESTING
Aerolab Educational Wind Tunnel
D
T
M
B
Desired Data
Aerodynamic Forces
  Lift Force
  Drag Force
    Minimize boundary layer effects
    Minimize downwash due to wingtip vortices
  Moments
Post Processing
  MATLAB
    Directly compare lift (NELDA model vs. Cessna 206 model)
    Build and compare drag polar
    Compare Lift/Drag Ratio
FR3: The aircraft shall have a maximum range and endurance comparable to or exceeding the performance of six-passenger electric aircraft currently under certification.
FR4: A non-powered, scale model of the airframe design will be constructed for the purpose of comparative wind tunnel analysis in the PILOT Lab Wind Tunnel.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Aerodynamic Forces
  Lift will be obtained by extracting the Normal force measured by one of the three sensors discussed in the following slide.
    This force will be calculated at the Cp, CG, and AC of the model with simple corrections
  Drag will be obtained by extracting the Axial force measured by one of the three sensors discussed in the following slide.
    Test subject shall not exceed a wingspan of 80% of the test section
  Moments will be obtained by extracting them directly from one of the three sensors discussed in the following slide
    Pitching moment will help characterize longitudinal stability (only as supplemental data)
      Will be able to tell of aircraft model is stable and/or trimmable
Post Processing
  Drag Polar
    Goal is to demonstrate improvement in drag polar through direct comparison (our design model vs Cessna 206 model)
      Skin Friction and Drag due to Flow Separation (C_D0)
      Form Drag
        Parasite Drag (C_Dp)
        Induced Drag (C_Di)
  Lift/Drag Ratio
    Help characterize range and endurance (only as supplemental data)

## Slide 29: WIND TUNNEL TESTING SENSORS
Sting ⅜ EWT
ATI Nano17
ATI Gamma
Maximum Load Capacities
D
T
M
B
FR3: The aircraft shall have a maximum range and endurance comparable to or exceeding the performance of six-passenger electric aircraft currently under certification.
FR4: A non-powered, scale model of the airframe design will be constructed for the purpose of comparative wind tunnel analysis in the PILOT Lab Wind Tunnel.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Sting ⅜ EWT
  Test Process:
    Vary AoA by 10 degrees (-5 < 0 < 5 degrees)
      Compute Total Lift and Drag
      Drag Polar
        C_D0 will be calculated at zero lift AoA
        All other drag will be calculated when varying AoA
    Side Force (Y) and Rolling Moment (Tx) can be calculated with a switch
ATI Nano17 Titanium
  Test Process:
    Requires platform integration, test stand, and a mechanical way to vary AoA
    Note the Force and Moment Limitations
ATI Gamma
  Test Process:
    Same as ATI Nano but note the Forces/Moment Magnitudes
    We would need to collaborate with Josh and LA’s to develop LabView Code adaptation

## Slide 30: WIND TUNNEL TESTING SENSORS
Sensor | Pros | Cons
Sting ⅜ EWT | Can compute all three forces High force and moment limits Integrated Hardware & Software | Pre-set blockage area Lack of roll moment
ATI Nano17 Titanium | Can compute all forces and moments LabView code is already available Was recently calibrated (see backup slide) | Force and moment magnitude is highly limited Requires platform integration, test-stand, and a mechanical way to vary angle of attack
ATI Gamma | Can compute all forces and moments Very high force and moment limits | Would require collaboration with Josh Mellin and LA’s to develop LabView code adaptation Requires platform integration, test-stand, and a mechanical way to vary angle of attack
D
T
M
B
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Sting ⅜ EWT
  Pros:
    We can flip an adjuster to get side force (Y) and yaw moment (Tz)
    Hardware is ready to use (can easily vary AoA)
    LabView Code is already available
  Cons:
    Force and Moment magnitude limitations (which are too bad)
    Sensitivity < ATI Instrumentation
ATI Nano17 Titanium
  Pros:
    Hardware adaptation will be more simple than ATI Gamma
  Cons:
    Force and Moment magnitude limitations ***Seems very low so it will depend on models
ATI Gamma
  Pros:
    Most expensive → best accuracy
  Cons:
    Labview adds another level of complexity to the testing-team
    Requires a more complex physical adaptation than ATI Nano
Conclusions
  Using Sing ⅜ EWT will be very useful to compute C_D0 and C_Di (by varying AoA)
  ATI Nano17 Titanium may fall short on force and moment magnitude capabilities
  ATI Gamma would be great for computing C_D0 but requires significant hardware and software development. This may be something we can consider for a higher level of success.

## Slide 31: GLIDER TESTING
D
T
M
B
Characteristic Stability Demonstration (CSD)
Qualitative demonstration of stability in NELDA design
Verification & Validation for mathematical/computational models
Demonstrate endurance based on glide ratio
FR3: The aircraft shall have a maximum range and endurance comparable to or exceeding the performance of six-passenger electric aircraft currently under certification.
FR5: A non-powered, larger scale glider model of the airframe design will be constructed for the purpose of stability analysis and verification.
FR6: The full-scale aircraft shall be designed to be statically and dynamically stable.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Using a glider test to qualitatively measure stability, and quantitatively measure range and endurance by extrapolating data from a rangefinder.
This test will also serve to verify and validate the mathematical and computational models
This test will accomplish functional requirements 3, 5, and 6, which demonstrate the improved performance over current electric aircraft and verification of stability

## Slide 32: GLIDER TESTING
Characteristic Stability Demonstration (CSD)
Team decided against accelerometers to measure flight data because of risk of added scope
One camera parallel to flight path, one camera perpendicular to flight path to qualitatively measure stability
Rangefinder to determine practical glide ratio
Launch from roof of aero building (with faculty assistance)
Use table bungee launch system provided by IRISS
D
T
M
B
FR3: The aircraft shall have a maximum range and endurance comparable to or exceeding the performance of six-passenger electric aircraft currently under certification.
FR5: A non-powered, larger scale glider model of the airframe design will be constructed for the purpose of stability analysis and verification.
FR6: The full-scale aircraft shall be designed to be statically and dynamically stable.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: For the stability test, accelerometers were considered to determine exact pitch, yaw, and roll forces. The team decided against this because of the extensive addition to the scope that this would create
Instead, the team will use cameras to qualitatively measure stability, using visual evidence of dutch roll, etc.
An on-board rangefinder will be used to determine the the range and endurance by measuring the launch height, distance travelled, and time of flight
The test will be conducted at the aero building, and will be launched from the roof with faculty assistance. The glider will be launched from the same launch mechanism every test
Garmen camera was trash, so look into better sensors

## Slide 33: FEASIBILITY TRACKING: TESTING
Value
Qualitative analysis of flow
  Flow visualization
  Can observe general trends such as localized
  Relative velocity/pressure hotspots
Individual component modelling
  Effect of wingtips/winglets on downwash vortices
  Aerodynamic fairings on landing gear
D
T
M
B
Section | CPEs | Requirements | Feasibility
Testing | CPE5 | FR4, FR5, FR6 | ✅
Preliminary Concern | Addressed? | Feasibility
WTAV Logistics | Yes: Work Needed | ✅
WTAV Data Utility | Yes | ✅
CSD Logistics | Yes: Work Needed | ✅
CSD Data Utility | Yes | ✅
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: provide evidence that the project objectives, is feasible, i.e. can be accomplished within the constraints of technology and the senior projects course (time, skills, money, facilities, etc.).

## Slide 34: Models Overview Construction Processes MANUFACTURING FEASIBILITY Presented by: Finn Bailis

## Slide 35: MANUFACTURED MODELS
Wind Tunnel Aerodynamic Validation Models (Nelda and 206) (WTAV) | Characteristic Stability Demonstration Model (CSD)
Geometrically scaled to maximum b = 8.8” Requires geometry within 1% accuracy Must be sufficiently smooth (Print/Mill layers < 100 microns) | Geometrically scaled to maximum b = 3’ (MTOW scaled by the same factor) Requires geometry within 5% accuracy of CAD model Must have all CG locations within 5% accuracy of full-scale airframe
D
T
M
B
FR4: A non-powered, scale model of the airframe design will be constructed for the purpose of comparative wind tunnel analysis in the PILOT Lab Wind Tunnel.
FR5: A non-powered, larger scale glider model of the airframe design will be constructed for the purpose of stability analysis and verification.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Geometry with 1% accuracy might be hard

## Slide 36: WTAV MODEL CONSTRUCTION
3D Printed: Uniform composition,
SLA print on Form 3 or Form 3L
Typical lead times, 2-3 weeks
Typical cost, $100-$200 per print (f-22 quote)
Full completion time estimate: 3-4 weeks
Sting Test insert must also be machined and assembled
Required Materials:
Form 3L SLA printer:
2 prints, 3 wk. lead time, ~$120 each
DLMS aluminum printer:
2 prints, 1 wk. lead time, ~$680 each
Sting Test Insert:
2 columns, Lathe Machined 1 wk. ~$50 each
D
T
M
B
FR4: A non-powered, scale model of the airframe design will be constructed for the purpose of comparative wind tunnel analysis in the PILOT Lab Wind Tunnel.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 37: CSD MODEL CONSTRUCTION
Complex foam, strut and laminate composition
  General structure to be CNC milled out of high density foam
  Then manually reinforced with carbon fiber rods and epoxy coated
  Full construction completion time estimate: 3 weeks/unit
Required Materials:
Carbon fiber struts:
4, 5 and 6 mm x 400 mm, ~$13 each
High Density foam:
3’ x 3’ x 6” blocks, ~$200
Epoxy Resin:
1 Liter, ~$65
D
T
M
B
FR5: A non-powered, larger scale glider model of the airframe design will be constructed for the purpose of stability analysis and verification.
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Cost estimates because estimated earlier

## Slide 38: FEASIBILITY TRACKING: MANUFACTURING
Value
Qualitative analysis of flow
  Flow visualization
  Can observe general trends such as localized
  Relative velocity/pressure hotspots
Individual component modelling
  Effect of wingtips/winglets on downwash vortices
  Aerodynamic fairings on landing gear
D
T
M
B
Section | CPEs | Requirements | Feasibility
Manufacturing | CPE4 | FR4, FR5 | ✅
Preliminary Concern | Addressed? | Feasibility
WTAV Materials | Yes | ✅
WTAV Construction | Yes: Work Needed | ✅
CSD Materials | Yes | ✅
CSD Construction | Yes: Work Needed | ✅
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: provide evidence that the project objectives, is feasible, i.e. can be accomplished within the constraints of technology and the senior projects course (time, skills, money, facilities, etc.).

## Slide 39: Bills of Materials BUDGET FEASIBILITY Presented by: Finn Bailis

## Slide 40: BILL OF MATERIALS
D
T
M
B
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Instrumentation and materials
Look at what materials Finn uploads tonight

## Slide 41: FEASIBILITY CONCLUSIONS Presented by: Emerson Beinhauer Feasibility Summary

## Slide 42: FEASIBILITY CONCLUSIONS
Section | CPEs | Requirements | Feasibility
Design | CPE1, CPE2, CPE3 | FR1, FR2, FR3, FR6 | ✅
Testing | CPE5 | FR4, FR5 | ✅
Manufacturing | CPE4 | FR4, FR5 | ✅
Budget | CPE6: Course funding limitation is $5,000 |  | ✅
D
T
M
B
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Ask the question what do we want from this slide? Given the fact that we haven't had the opportunity to design an airplane and we have previously discussed what is feasible in all of the feasibility slides does the PAB just want us to reiterate what was previously discussed here. (ex: we showed that we had three ways of testing in the wind tunnel but we haven't decided on one yet). This is a very important slide per the rubric we just dont know how to approach this

## Slide 43: Design Manufacturing Testing Logistics FUTURE WORK Presented by: Emerson Beinhauer

## Slide 44: FUTURE WORK
Aircraft Design
  Additional models & more rigorous model testing
    Model modification
    Sensitivity analyses on each design parameter
  Stability Model Generation and Testing
  Validation of different design iterations with computational models
    Finalize aircraft design parameters
    Drawings → CAD
Testing
  Test plan selection and testing procedures documentation
Manufacturing
  Workshops, specific requirements, materials → WTAV, CSD
Finance & Project Management
  Finalized budget, Gantt chart, Work Breakdown Structure
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 45: ACKNOWLEDGEMENTS
Dr. Jelliffe Jackson
Dr. Kathryn Wingate
Dr. Brian Argrow
Dr. Donna Gerren
Dr. John Farnsworth
Professor John Mah
Matt Rhode
KatieRae Williamson
Project Advisory Board
Colin Claytor
Emma Markovich
Richard Schaden
Instructor Bobby Hodgkinson
Josh Mellin
Trudy Schwartz
Michael Rhodes
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 46: BACK UP SLIDES
Similar Aircraft | Aero Analysis Method | WTAV Testing | CSD Testing
AAA Nomenclature | Powertrain | WTAV Manufacturing | CSD Manufacturing
AAA Drag Polars | Range | Wind Tunnel Specs | Trade Studies
AAA Performance | Baseline Code | N-22 Airfoil | References
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 47: AERODYNAMIC ANALYSIS
Methodology
Drag:
Utilized PLLT to obtain Cd_i
Utilized skin friction drag coefficient method to obtain CD0
Incorporated C_di, Cd0, and landing gear into final model of Drag
Utilized PLLT to find e
Lift:
Utilized PLLT and Vortex Pannel to obtain C_L
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Carlin: good job describing why we have these models (double check AAA, understand where those results come from)
Run through both plots as well as zero lift AOA
Consistency with AOA and alpha
Equations
HOW TO DESCRIBE THE GRAPH
1.) Where did the data come from?
2.) Point and state axes
3.) Describe the legend 4.) Describe the trends
5.) Results
6.) Conclusions

## Slide 48: AERODYNAMIC ANALYSIS
Cd0 Derivation
Empirical Data used to determine Skin Friction Coefficient
  Cfe: 0.0045
Sw: Wing Area
S_wet,W: Wetted area of wing
  Approximated with 2*S
S_wet,F: Wetted area of Fuselage
  df: Fuselage Diameter
  lf: Length of Fuselage
  λ_F = lf/df
Cd0: 0.01828
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Carlin: good job describing why we have these models (double check AAA, understand where those results come from)
Run through both plots as well as zero lift AOA
Consistency with AOA and alpha
Equations
HOW TO DESCRIBE THE GRAPH
1.) Where did the data come from?
2.) Point and state axes
3.) Describe the legend 4.) Describe the trends
5.) Results
6.) Conclusions

## Slide 49: AERODYNAMIC ANALYSIS
N-22 Airfoil Cl vs Alpha
Assumptions:
  N-22 airfoil
  Compressibility and Viscous effects considered negligible
  Cl obtained using Vortex Panel Method
Input Variables:
  Root chord: 5 feet
  Airspeed: 150 knots
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Carlin: good job describing why we have these models (double check AAA, understand where those results come from)
Run through both plots as well as zero lift AOA
Consistency with AOA and alpha
Equations
HOW TO DESCRIBE THE GRAPH
1.) Where did the data come from?
2.) Point and state axes
3.) Describe the legend 4.) Describe the trends
5.) Results
6.) Conclusions

## Slide 50: AERODYNAMIC ANALYSIS
N-22 Airfoil Lift vs Weight:
Assumptions:
  N-22 airfoil
  C_l obtained using PLLT
    Wing is represented by single finite strength vortex
Input Variables:
  Root chord: 5 feet
  Tip chord: 2.5 feet
  Airspeed: 150 knots
  Wing Span: 45 feet
  Lift Slope and Zero Lift AOA
  Density
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Carlin: good job describing why we have these models (double check AAA, understand where those results come from)
Run through both plots as well as zero lift AOA
Consistency with AOA and alpha
Equations
HOW TO DESCRIBE THE GRAPH
1.) Where did the data come from?
2.) Point and state axes
3.) Describe the legend 4.) Describe the trends
5.) Results
6.) Conclusions

## Slide 51: AERODYNAMIC ANALYSIS
N-22 Airfoil Cd vs. Alpha:
Assumptions:
  N-22 airfoil
  C_l, e: obtained using PLLT
Input Variables:
  C_l vector from Vortex Panel
  Aspect Ratio: 12
  e: 0.9728
  Cd0: 0.01828
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Carlin: Run through both plots
HOW TO DESCRIBE THE GRAPH
1.) Where did the data come from?
2.) Point and state axes
3.) Describe the legend 4.) Describe the trends
5.) Results
6.) Conclusions

## Slide 52: AERODYNAMIC ANALYSIS
N-22 Airfoil Cl/Cd:
Assumptions:
  N-22 airfoil
  C_l: obtained using PLLT
  C_d derivation on previous slide
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: Carlin: Run through both plots
HOW TO DESCRIBE THE GRAPH
1.) Where did the data come from?
2.) Point and state axes
3.) Describe the legend 4.) Describe the trends
5.) Results
6.) Conclusions

## Slide 53: SIMILAR ELECTRIC AIRCRAFT (6-P)
A summary
Variable | Y6SPlus | Bell Nexus 6HX | Lilium Jet | VA-X4
Cruise Speed [kts] | 110 | 155 | 152 | 130
Endurance [min] | 60 | 50.5 | 53 | 40
Range (nm) | 70 | 130 | 135 | 87
Passengers | 6 | 6 | 6 | 5
Wing Span [ft] |  | 40 | 45.6 | 49.2
Y6S Plus
Bell Nexus 6HX
Lilium Jet Air Taxi
VA-X4
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP
Notes: This slide to be referenced if the PAB has questions about FR3 - comparative range and performance for electric “aircraft”, even though these are all VTOLs

## Slide 54: Summary of Flyable, Manned A/C
Source: https://www.sciencedirect.com/science/article/abs/pii/S0376042118300356

## Slide 55: SIMILAR ELECTRIC AIRCRAFT
Pipistrel Alpha Electro
Variable | Alpha Electro
Takeoff Weight [lbs] | 1,213
Empty Weight [lbs] | 811
Power Required [hp] | 67
Cruise Speed [kts] | 85
Endurance [min] | 60
Passengers | 2
Wing Span [ft] | 34.5
Wing Area [ft2] | 102.4
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 56: SIMILAR ELECTRIC AIRCRAFT
Pipistrel Velis
Variable | Velis
Takeoff Weight [lbs] | 1,320
Empty Weight [lbs] | 941
Power Required [hp] | 77
Cruise Speed [kts] | 90
Endurance [min] | 50
Passengers | 2
Wing Span [ft] | 102.4
Wing Area [ft2] | 35
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 57: SIMILAR ELECTRIC AIRCRAFT
Phoenix Air Phoenix
Variable | Air Phoenix
Takeoff Weight [lbs] | 1,042
Empty Weight [lbs] | 650
Power Required [hp] | 100
Cruise Speed [kts] | 130
Endurance [min] | -
Passengers | 2
Wing Span [ft] | 49
Wing Area [ft2] | -
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 58: SIMILAR ELECTRIC AIRCRAFT
Zunum Aero
Variable | Aero
Takeoff Weight [lbs] | 11,500
Empty Weight [lbs] | 8,200
Power Required [hp] | 1,341
Cruise Speed [kts] | 
Endurance [min] | 120
Passengers | 12
Wing Span [ft] | 52
Wing Area [ft2] | -
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 59: SIMILAR ELECTRIC AIRCRAFT
Yuneec International E430
Variable | E430
Takeoff Weight [lbs] | 1,037
Empty Weight [lbs] | 551
Power Required [hp] | 54
Cruise Speed [kts] | 49
Endurance [min] | 150
Passengers | 2
Wing Span [ft] | 45
Wing Area [ft2] | 122
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 60: SIMILAR ELECTRIC AIRCRAFT
Liaoning Ruixiang RX1E
Variable | RX1E
Takeoff Weight [lbs] | 1,102
Empty Weight [lbs] | 595
Power Required [hp] | 40
Cruise Speed [kts] | 59
Endurance [min] | 60
Passengers | 2
Wing Span [ft] | 47.5
Wing Area [ft2] | 130
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 61: SIMILAR ELECTRIC AIRCRAFT
Bye Aerospace EFlyer 2
Variable | EFlyer 2
Takeoff Weight [lbs] | 1,900
Empty Weight [lbs] | 1,460
Power Required [hp] | 121
Cruise Speed [kts] | 55-120
Endurance [min] | 210
Passengers | 2
Wing Span [ft] | 38
Wing Area [ft2] | 129
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 62: SIMILAR ELECTRIC AIRCRAFT
Samad Q-Starling
Variable | Q-Starling
Takeoff Weight [lbs] | 2,300
Empty Weight [lbs] | 1,920
Power Required [hp] | 241
Cruise Speed [kts] | 250
Endurance [min] | 100
Passengers | 2
Wing Span [ft] | 26
Wing Area [ft2] | 936.5
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 63: SIMILAR ELECTRIC AIRCRAFT
Lilium Air Taxi
Variable | Air Taxi
Takeoff Weight [lbs] | ~3,112
Empty Weight [lbs] | ~2,867
Power Required [hp] | 1,300
Cruise Speed [kts] | 151
Endurance [min] | 54
Passengers | 7
Wing Span [ft] | 45.6
Wing Area [ft2] | -
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 64: SIMILAR ELECTRIC AIRCRAFT
Voltaero Cassio 1
Variable | Cassio 1
Takeoff Weight [lbs] | 5,511
Empty Weight [lbs] | 3,800
Power Required [hp] | 400
Cruise Speed [kts] | 200
Endurance [min] | 210
Passengers | 9
Wing Span [ft] | -
Wing Area [ft2] | -
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 65: SIMILAR ELECTRIC AIRCRAFT
Eviation Alice
Variable | Alice
Takeoff Weight [lbs] | 16,500
Empty Weight [lbs] | 14,000
Power Required [hp] | 1,716.5
Cruise Speed [kts] | 250
Endurance [min] | 106
Passengers | 9
Wing Span [ft] | 63
Wing Area [ft2] | -
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 66: AAA NOMENCLATURE
Variable | Name | Determination
𝜆W | Taper Ratio | Chosen to be 0.5 from trade studies
ADP | Coefficient for Total Drag Polar | Chosen to be 0
BDP | Coefficient for Total Drag Polar | = 1/(𝝿*AR*e)
ADP_clean | Coefficient for Drag Polar with Clean Configuration | Chosen to be 0
BDP_clean | Coefficient for Drag Polar with Clean Configuration | = 1/(𝝿*AR*eclean)
ADP_L_dwn | Coefficient for Drag Polar when Landing with Gear Down | Chosen to be 0
BDP_L_dwn | Coefficient for Drag Polar when Landing with Gear Down | = 1/(𝝿*AR*eL)
ADP_TO_dwn | Used to determine Drag Polar when Taking Off with Gear Down | Chosen to be 0
BDP_TO_dwn | Used to determine Drag Polar when Taking Off with Gear Down | = 1/(𝝿*AR*eTO)
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 67: AAA NOMENCLATURE
Variable | Name | Determination
ARW | Wing Aspect Ratio | Chosen from trade studies
a | Regression Coefficient used to determine Parasite Area from Wetted Area | Based on desired skin drag coefficient of 0.008
b | Regression Coefficient used to determine Parasite Area from Wetted Area | Based on desired skin drag coefficient of 0.008
c | Regression Coefficient used to determine Wetted Area From Takeoff Weight | Roskam’s research on single engine propeller aircraft
d | Regression Coefficient used to determine Wetted Area From Takeoff Weight | Roskam’s research on single engine propeller aircraft
f | Parasite Area based on Wetted Area [ft2] | log(f) = a + b*log(SWet)
CGR23.77 | FAR 23.77 (All Engines Operative) Climb Gradient | FAR 23 Requirement
Cfe | Equivalent Skin Friction Coefficient | = 0.0055 because Light Aircraft Single Engine
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 68: AAA NOMENCLATURE
Variable | Name | Determination
CD0 | Zero Lift Drag Coefficient | = Cfe * (Swet/Sw) considers current flight configuration
CD0_1 | Class 1 Zero Lift Drag Coefficient | = Cfe * (Swet/Sw) considers entire aircraft
ΔCD0_1 | Change in Class 1 ZeroLift Drag | Chosen for design considerations and trade studies
CD0_clean | Clean Configuration Zero Lift Drag | = Cfe * (Swet/Sw) considers clean configuration
CD0_clean,M | Clean Configuration Parasite Drag corrected for Mach Effects | 
CD_min | Class 1 Minimum Drag Coefficient | = CD0 + BDP*CL_min2
CD_1 | Airplane Steady State Drag Coefficient | = CD0_1 + BDP*CL_12
CD0_L_dwn | Landing with Landing Gear Down and Flaps Zero Lift Drag | = Cfe * (Swet/Sw) considers landing gear and flaps while landing
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 69: AAA NOMENCLATURE
Variable | Name | Determination
ΔCD0_L_dwn | Change in CD0 with landing gear down while landing with flaps | Chosen for design considerations and trade studies
CD0_TO_dwn | Takeoff with Landing Gear Down and Flaps Zero Lift Drag | = Cfe * (Swet/Sw) includes landing gear and flaps during takeoff
ΔCD0_TO_dwn | Change in CD0 with landing gear down during takeoff | Chosen for design considerations and trade studies
CL_plot_min | Minimum coefficient of lift for constraint plots | Chosen for design considerations and optimization of plots
CL_plot_max | Maximum coefficient of lift for constraint plots | Chosen for design considerations and optimization of plots
ΔCL_Cl-max | Change in Maximum Lift Coefficient During Climb | Chosen for design considerations and trade studies
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 70: AAA NOMENCLATURE
Variable | Name | Determination
ΔCL_max | Change in Maximum Lift Coefficient | Chosen for design considerations and trade studies
CL_max_clean | Maximum Lift Coefficient for Clean Configuration | Roskam’s research on single engine propeller aircraft
CL_max_L | Maximum Lift Coefficient at Landing | Roskam’s research on single engine propeller aircraft
CL_max_S_cln | Maximum Lift Coefficient at Stall for Clean Configuration | Roskam’s research on single engine propeller aircraft
CL_max_S | Maximum Lift Coefficient at Stall with Flaps | Roskam’s research on single engine propeller aircraft
CL_max_TO | Maximum Lift Coefficient at Takeoff | Roskam’s research on single engine propeller aircraft
CL@C_D_min | Maximum Lift Coefficient at Min drag coefficient | = sqrt((CD_Min - CD0)/BDP)
CL_1 | Airplane Steady State Lift Coefficient | = (n*Wcurrent)/(q1*SW)
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 71: AAA NOMENCLATURE
Variable | Name | Determination
e | Total Span Efficiency Factor | Roskam’s research on single engine propeller aircraft
eclean | Clean Configuration Span Efficiency Factor | Roskam’s research on single engine propeller aircraft
eL | Landing Span Efficiency Factor | Roskam’s research on single engine propeller aircraft
eTO | Takeoff Span Efficiency Factor | Roskam’s research on single engine propeller aircraft
FTO | Power Ratio at Takeoff | Power at Takeoff/Max Power
F5000 | Power Ratio at 5000 ft Altitude | Power @ 5000 ft/Maximum Power
FCr | Power Ratio at Cruise | Power at Cruise/Maximum Power
FM | Power Ratio During Maneuver | Power at Maneuver/Maximum Power
FMaxCont | Power Ratio for Maximum Continuous Thrust | Maximum Continuous Power/ Maximum Power
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 72: AAA NOMENCLATURE
Variable | Name | Determination
hcr | Cruise Altitude | Chosen from current electric aircraft competition
hL | Altitude at Landing | Altitude at Rocky Mountain Regional Airport
hM | Altitude for Maneuver | Altitude at Rocky Mountain Regional Airport, assuming maneuver during takeoff in case of emergency
hS | Altitude at Stall Out | Altitude at Rocky Mountain Regional Airport, assuming stall during takeoff in case of emergency
hTO | Altitude at Takeoff | Altitude at Rocky Mountain Regional Airport
L/D | Lift to Drag Ratio for the Aircraft | = CL_1/CD_1
MCr_Max | Critical Mach Number During Cruise | = VCr_Max/628.27 (628.27 kts = Speed of Sound @ 14,000 ft)
MM | Maneuver Mach Number | = VM/648.26 ( 648.26 kts = Speed of Sound @ 5,673 ft)
ƞ⅀prop | Propeller Efficiency Factor | Determined from current propeller market
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 73: AAA NOMENCLATURE
Variable | Name | Determination
nM | Number of g’s pulled during maneuver | = 1/cos(15°) [15° is a FAR 23 Requirement for banked turns]
q1 | Dynamic Pressure [lbs/ft2] | = 0.5*⍴*VCr_max2
RC/Vs2 | FAR 23.67 Requirement | Rate of Climb/(Stall Speed)2
SL | Landing Distance | = 0.6 * STO
STO | Takeoff Distance | Runway at Rocky Mountain Regional Airport
STOG | Ground Roll Distance | = STO/1.66
SW | Wing Area [ft2] | Optimal design point on performance plot
SWET | Aircraft Wetted Area [ft2] | log(SWET) = c + d*log(WTO)
ΔT | Change Temperature | Chosen for design considerations and trade studies
ΔTTO | Change Temperature @ Takeoff | Chosen for design considerations and trade studies
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 74: AAA NOMENCLATURE
Variable | Name | Determination
TurnRate | Turn Rate during Maneuver [rad/s] | = g*sqrt(nM2 - 1)/VM
U1 = VCr_Max | Cruise Speed [kts] | Provided by customer
VL | Landing Approach Velocity [kts] | = 1.4 * SL
VM | Maneuver Speed [kts] | = 1.4 * VS
VS | Stall Speed with Flaps [kts] | FAR 23 requirement to have stall speed of 61 kts
WE | Empty Weight [lbs] | Intersection of regression and sum
WCr/WTO | Mid Cruise to Takeoff Weight Ratio | Equal to 1 because no weight lost during mission
WL/WTO | Landing to Takeoff Weight Ratio | Equal to 1 because no weight lost during mission
WM/WTO | Maneuver to Takeoff Weight Ratio | Equal to 1 because no weight lost during mission
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 75: AAA NOMENCLATURE
Variable | Name | Determination
WS/WTO | Stall to Takeoff Weight Ratio | = 1 because no weight lost during mission
WTO | Takeoff Weight [lbs] | Intersection of regression and sum
(W/S)TO_S_cln | Wing Loading for Takeoff Weight at Stall for Clean Configuration | = 0.5 * CL_max_S_cln * ⍴ * VS_Clean2
(W/S)L | Wing Loading for Landing with Flaps | = 0.5 * CL_max_L * ⍴ * VL2
(W/S)TO_S | Wing Loading for Takeoff Weight at Stall with Flaps | = 0.5 * CL_TO * ⍴ * VCr_max2
VS_clean | Stall Speed with Clean Configuration [kts] | FAR 23 Requirement of 61 kts for a stall speed
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 76: AAA DRAG POLAR CALCULATIONS
Takeoff, Flaps, Gear Down Drag Polars:
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 77: AAA DRAG POLAR CALCULATIONS
Landing, Flaps, Gear Down Drag Polars:
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 78: AAA DRAG POLAR CALCULATIONS
Clean Configuration Drag Polars:
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 79: AAA DRAG POLAR CALCULATIONS
Current Flight Condition Drag Polars:
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 80: AAA DRAG POLAR CALCULATIONS
All Drag Polar Inputs:
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 81: AAA DRAG POLAR CALCULATIONS
All Output Drag Polars:
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 82: AAA FLIGHT REQUIREMENTS AND PERFORMANCE
Takeoff Requirements:
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 83: AAA FLIGHT REQUIREMENTS AND PERFORMANCE
Climb Requirements:
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 84: AAA FLIGHT REQUIREMENTS AND PERFORMANCE
Cruise Requirements:
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 85: AAA FLIGHT REQUIREMENTS AND PERFORMANCE
Maneuver Requirements:
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 86: AAA FLIGHT REQUIREMENTS AND PERFORMANCE
Stall Speed Requirements:
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 87: AAA FLIGHT REQUIREMENTS AND PERFORMANCE
Landing Requirements:
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 88: AAA FLIGHT REQUIREMENTS AND PERFORMANCE
1st Iteration Wing Geometry:
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 89: WTAV MODEL CONSTRUCTION
 | Form 3 | Form 3L
Build Volume | 14.5 × 14.5 × 18.5 cm (5.7 × 5.7 × 7.3 in) | 33.5 × 20 × 30 cm (13.2 × 7.9 × 11.8 in)
Resolution | 25 μm | 25 μm
Access | ITLL | Outsourced
Cost | ~$25 | ~$100
Print Time | 10-15 hours | 2-3 weeks
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 90: CSD MODEL CONSTRUCTION
CNC Machining of high density foam is feasible with the mills available to us at both the ITLL and Aerospace manufacturing center.
Extensive work with learning SolidCam and Solid Works will be crucial in achieving these models.
Components such as the tail and wings can be manufactured several times for replacements.
Each piece will be assembled using glue and struts when applicable
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 91: LITHIUM METAL SOLID STATE BATTERIES
Necessary Assumptions:
Composition: Anode Lithium metal (β-Li), solid electrolyte (β-Li3PS4) and active cathode (Li(Ni0.6Co0.2Mn0.2)O2
Efficiency: 90 percent Efficiency was assumed for all battery types
Formability: The Cathode, Electrolyte and Anode layers are not only sufficiently thin but also pliable to configure in most simple Geometries (i.e. a wing)
Volumetric Energy Density | Specific Energy
580 Wh/kg | 1377 Wh/L
-Benjamin J. Brelje∗
Joaquim R.R.A. Martins
University of Michigan, Department of
Aerospace Engineering, MI, USA
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 92: BRUSHLESS ELECTRIC PROPULSION UNIT
 | MagniX 350 | Design Requirement
Continuous Power Output | 280 kW / 381 Hp | 346 Hp -AAA
Max. Power Output | 350 kW / 476 Hp | ~
Continuous Torque | 1410 Nm | ~
Max. Torque | 1610 Nm | ~
Output RPM | 1200-2300 RPM | ~
Dry Weight | 112 kg / 246 lbs | TBD
Operating Volt. | 500-800 VDC | ~
Service Ceiling | 35,000 ft | 20,000 ft
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 93: ELECTRIC AIRCRAFT RANGE EQUATION 1
Source: Electric Flight – Potential and Limitations, Martin Hepperle, German Aerospace Center
Full Source: Microsoft Word - MP-AVT-209-09.doc (dlr.de)
Back
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 94: ELECTRIC AIRCRAFT RANGE EQUATION 2
Source: Range Equation for Hybrid-Electric Aircraft with Constant Power Split
Full Source: Electric Range
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 95: BASELINE METHODOLOGY CODE
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 96: BASELINE METHODOLOGY CODE
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 97: BASELINE METHODOLOGY CODE
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 98: BASELINE METHODOLOGY CODE
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 99: WIND TUNNEL SPECIFICATIONS
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 100: WIND TUNNEL - SUPPORTING STABILITY DATA
Can we determine stability using the wind tunnel?
  No, the data we use may only be considered supporting data
    Pitch stiffness may be determined for both the NELDA design model and the Cessna 206 model. This may be computed by directly extracting the pitch moment measured by any of the three sensors under consideration
    Lateral stability couples roll and yaw moments which falls beyond the scope of the wind-tunnel test
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 101: ATI SIX-AXIS FORCE/TORQUE SENSOR
Calibrated Ranges (+ or -)
Measurement Uncertainty (95% confidence Level, percent of full-scale load)
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 102: SCALABILITY
Reynold’s Number
𝜌uL
𝜌 = density u = airspeed L = chord length 𝜇 = viscosity
Calculate at cruising altitude for our design
Use same Re to backsolve for u (flow speed)
Can also backsolve for L based on approximate u
  Used for getting appropriate scale based on wind tunnel airspeed approximation
𝜇
= Re
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 103: CHARACTERISTIC STABILITY DEMONSTRATION MODEL
The CSD model will be constructed to proportionally identical geometry of both the Wind Tunnel model as well as full scale airframe
It’s purpose is to deliver a physical validation of both stability and aerodynamics.
With lack of higher quality instrumentation (wind tunnels) and sufficient confidence in computational analysis (CFD), the design team has no physical validation of stability and weak physical validation of aerodynamics.
Although glide ratios, L/D, mode analysis, and other quantitative values could be extrapolated from this test, the team does not find them sufficiently useful and therefore exempt this model from the levels of success. However, thorough, qualitative analysis will be done on the testing of the CSD model
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 104: GLIDER TEST LAUNCH SYSTEM
WAITING TO HEAR BACK FROM DEPT PEOPLE
IRISS bungee launch system
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 105: MATERIALS TRADE STUDY METRICS
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 106: MATERIALS TRADE STUDY RESULTS
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 107: LANDING GEAR TRADE STUDY METRICS
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 108: LANDING GEAR TRADE STUDY RESULTS
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 109: TAIL CONFIGURATION TRADE STUDY METRICS
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 110: TAIL CONFIGURATION TRADE STUDY RESULTS
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 111: DIHEDRAL TRADE STUDY METRICS
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 112: DIHEDRAL TRADE STUDY RESULTS
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 113: ASPECT RATIO TRADE STUDY METRICS
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 114: ASPECT RATIO TRADE STUDY RESULTS
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 115: AIRFOIL TRADE STUDY METRICS
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 116: AIRFOIL TRADE STUDY RESULTS
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 117: REFERENCES
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 118: SIMILAR AIRCRAFT REFERENCES
Pipistrel Alpha Electro: Pipistrel
Pipistrel Velis: AOPA
Phoenix Air Phoenix: Phoenix Air, Phoenix Air USA
Zunum Aero: Zunum
Yuneec International E430: Avia.Pro
Voltaero Cassio 1: Future Flight, Voltaero
Liaoning Ruixiang RX1E: All Aero
Bye Aerospace EFlyer 2: Aerospace Technology
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 119: SIMILAR AIRCRAFT REFERENCES
Converted Cessna 172: Beyond Aviation
Samad Q-Starling: Samad Aerospace
Lilium Air Taxi: Lilium
Eviation Alice: Eviation
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 120: MANUFACTURING REFERENCES
3D prints: Xoemetry©
Machinable Foam: General Plastics Manufacturing©
Tooling/ Mills: Aerospace Manufacturing center & ITLL Machine Shop
  Required CNC mills:
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP

## Slide 121: AERODYNAMIC MODELING REFERENCES
206 Parameters1, 206 Parameters2
Drag Prediction
Electric Range
Airfoil Data
Iterative Design Methods
Landing Gear Drag
Wing Geometry 101
OVERVIEW | DESIGN | TESTING | MANUFACTURING | BUDGET | CONCLUSIONS | FUTURE WORK | BACK UP