## Slide 1
TEST READINESS REVIEW
FEBRUARY 15TH, 2022
ASEN 4028-011
Customer:
Richard Schaden
Faculty Advisor:
Dr. Donna Gerren
Presenters:
Emerson Beinhauer, Finn Bailis, Tristan Martinez,
Jake Pendergast, Julia Tucker, Fernando Chavez
Additional Team Members:
Nathan Braunstein, Finn Bailis, Christl Haley,
Carlin Hornbostel, Tomaz Remec

## Slide 2: OVERVIEW Presented by: Emerson Beinhauer, Finn Bailis
Project Purpose and Objectives
CONOPS
FBD
Baseline Design
CPEs
Levels of Success
Project Updates

## Slide 3: PROJECT PURPOSE & OBJECTIVES
Generate novel design of a fully-electric 6-passenger aircraft that outperforms similar market competitors while being capable of production within the next
5 years
Demonstrate this design can achieve the customer’s requested mission profile through well established heritage models
Utilize the capability of the PILOT wind tunnel to extrapolate small-scale data for full-scale applications via comparative models
  Same scale Cessna-206 vs. NELDA’s Design due to Wind Tunnel limitations
Analysis via aircraft dynamic models demonstrate that the aircraft design is statically and dynamically stable
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Utilize the capability of the PILOT wind tunnel to extrapolate small-scale data for full-scale applications via comparative models
Same scale Cessna-206 vs. Nelda’s design

## Slide 4: CONOPS (MISSION PROFILE)
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: On the aircraft design portion of this project the following mission outline and concept of operations have been identified. Our client would like an aircraft that can carry 6 passengers at a speed of 150kts for 2 hours with ….
Mission CONOPS is good, but for our specific class CONOPS we want to go for more of the final validation and tests that we have to do
  Second phase is more of a testing plan / project plan
  We'll be testing both models, each warrant their own conops? Then what does it look like when we test our WTAV model, then Glider
Need to state in the mission CONOPS that these parameters are what our full fledged aircraft is designed to accomplish, not necessarily what our project is going to do

## Slide 5: CONOPS (PROJECT)
MATLAB Performance Models
Full Scale Design
Wind Tunnel Aerodynamic Validation (WTAV)
Characteristic Stability Demonstration (CSD)
Glider Models
1st Semester
2nd Semester
Analysis for V&V
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: In order to be successful…

## Slide 6: FUNCTIONAL BLOCK DIAGRAM
T E S T I N G/
V A L I D A T I O N
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP

## Slide 7: BASELINE DESIGN
AFT, MID- MOUNTED WING
AFT PROP (4 BLADES)
VERTICAL STABILIZER
TRICYCLE LANDING GEAR
CANARD
WINGLETS
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: NATE - CAD with Dimensions

## Slide 8: BASELINE DESIGN
Table of major baseline specs on following page , when time allows this will be a full scale drw of complete model
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Say wingspan/length in feet

## Slide 9: CRITICAL PROJECT ELEMENTS
Element | Description | Functional Req
Electrical Powertrain System (EPS) | All performance parameters of the electrical powertrain system (batteries, motor, avionics) are demonstrably feasible within ~5 years. | FR1 - Classification
Airframe Design (AIRD) | Aerodynamically efficient; 6 passengers; 150 kias cruise; fully electric, performance enables 2 hr endurance, 150 nautical mile range. | FR1 - Classification FR2 - Crew FR3 - Performance
Computational Simulation + Stability Models (CSM) | MATLAB, AAA, and dynamic stability models will serve as a guide for analysis, prediction, verification, and design/model iteration. | FR3 - Performance FR6 - Stability
Small Scale Testing (SST) | Wind Tunnel Aerodynamic Validation (WTAV): comparative data collection, and Characteristic Stability Demonstration (CSD): stability visualization | FR4 - WTAV (Wind Tun.) FR5 - CSD (Glider)
Manufacturing (MFCT) | Scale models will need to be constructed for the WTAV and CSD tests | FR4 - WTAV (Wind Tun.) FR5 - CSD (Glider)
Budget (BUD) | Course funding limitation has a limit of $5,000; will drive SST model quality | Course
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Jake

## Slide 10: LEVELS OF SUCCESS - TESTING
Project Element |  | Level 1 | Level 2 | Level 3 | Level 4
Small Scale Testing (SST) | WTAV (WT Models) C206 vs. NELDA | L/D underperforms C206 | Similar L/D comparison; (± 5%) | Increased L/D (> 5%) | Increased L/D (> 10%)
 | CSD (Gliders) | No usable measurements obtained | Predicted modes not demonstrated | Qualitative demonstration of predicted modes (visual) | Quantitative demonstration of predicted modes (data)
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP

## Slide 11: LEVELS OF SUCCESS - MANUFACTURING
Project Element |  | Level 1 | Level 2 | Level 3 | Level 4
Manufacturing (MFCT) | WTAV (WT Models) | Low fidelity models | Safe for AeroLab WT Testing (≥ 130 ft/s) | Precise to ± 0.01 in | Precise to ± 0.001 in
 | CSD (Gliders) | Trimmed prototype (foam) | Trimmed prototype (foam w/gear + winglets) | 3D Printed Fuselage | Onboard Sensors
 | Glider CG | Precise to ± 0.7 in | Precise to ± 0.5 in | Precise to ± 0.3 in | Precise to ± 0.1 in
 | Glider Dimensions |  |  |  | 
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP

## Slide 12: PROJECT UPDATES
Table of major baseline specs on following page , when time allows this will be a full scale drw of complete model
(WTAV) Wind Tunnel Aerodynamic Validation
NELDA model complete
  Interfaces smoothly with the Sting EWT Sensor
Usable Cessna 206 CAD unavailable
  Solution: Outsourced 3D printed model
  Status: 3D printed adapter for Sting sensor required (CAD in progress)
Auxiliary Components (Post IDR)
A “car-top” test of the WTAV (wind tunnel) models will be required to demonstrate wind tunnel safety
  Solution: 3D printed car sting mount
  Status: CAD complete
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Say wingspan/length in feet

## Slide 13: PROJECT UPDATES (CONT.)
(CSD) Foam Glider Prototype
Wings and canard cannot be CNC machined
  Solution: Hot-wire cutting
  Status: CAD complete
  Contingency Plans: Airfoil Cutter; Outsourcing (MohrComposites)
Auxiliary Components (Post IDR)
The CSD (Glider) model winglets cannot be machined or cut from foam
  Solution: SLA 3D printing
  Status: CAD complete
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Say wingspan/length in feet

## Slide 14: SCHEDULE Presented by: Jacob Pendergast
GANTT Chart
Wind Tunnel Models
Glider Models
Risk Off-Ramps
Notes: Jake

## Slide 15: PROJECT SCHEDULE - GANTT
High Level Project Gantt Chart
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Quick overview of full schedule
Emphasis on testing schedule
Margin defined with reason
Critical path shown

## Slide 16: PROJECT SCHEDULE - WT Models
Planned | In Progress | Complete
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Jake
Quick overview of full schedule
Emphasis on testing schedule
Margin defined with reason
Critical path shown

## Slide 17: PROJECT SCHEDULE - GLIDER MODELS
Planned | In Progress | Complete
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Jake
Quick overview of full schedule
Emphasis on testing schedule
Margin defined with reason
Critical path shown

## Slide 18: SCHEDULING: RISK OFF-RAMPS
Wind Tunnel Model Tolerances
  Risk: 3D Printed Models improperly toleranced to STING fitting requirements
  Mitigation: Construction / Iteration upon multiple NELDA and CESSNA models w/ additional allocated budget
Glider Manufacturing Risks
  Risk: Inability to manufacture fuselage and/or wings to appropriate tolerances
  Mitigation: Sourcing of additional manufacturing methods
    3D Printed Fuselage
    CNC Cut Wings (Using UAV Lab Machine)
Glider Testing Suitability
  Risk: Multiple days of unfavorable testing conditions (high winds, muddy ground, inclement weather)
  Mitigation: Appropriate scheduling margin, expedited manufacturing of initial models
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Jake

## Slide 19: TEST READINESS Presented by: xxx
Testing Limitations
Testing Overview
WTAV
Preloading Verification Test
Car Top Safety Test CSD
CG Testing
Notes: Emerson

## Slide 20: TESTING LIMITATIONS
Structural Analysis
Aerodynamics
Powertrain
Testing
Battery Performance Testing
Stability and Control Flight Testing
Crew/Human
Factors Studies
Avionics & Controls Testing
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Emerson

## Slide 21: TESTING LIMITATIONS
Wind Tunnel
Small-scale comparative testing
Glider
Characteristic Stability Demonstration
Going to focus on main customer requirements:
Aerodynamics & Stability
1/64 Scale
1/14 Scale
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Emerson

## Slide 22: TESTING OVERVIEW
Element | Requirement | Test | Description
Small Scale Testing (SST) | FR 4.0 | Wind Tunnel Testing (WTAV) | Comparative Aerodynamic Validation in the Wind Tunnel
Small Scale Testing (SST) | DR 4.2.2 | Preloading Verification Test | Verify Preloading Methodology
Manufacturing (MFCT) | DR 4.1.3 | “Car-top” Safety Test | Ensure structural safety of the WT models
Small Scale Testing (SST) | FR 5.0 | Glider Testing (CSD) | Characteristic Stability Demonstration
Manufacturing (MFCT) | DR 5.1.1 | CG Test | Ensure accurate CGs in glider models
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Jake

## Slide 23: (SST) WIND TUNNEL TESTING
FR 4.0: A non-powered, scale model of the airframe design will be constructed for the purpose of practical wind tunnel
analysis in the PILOT Lab Wind Tunnel
Rationale/Motivation:
Validate NELDA aerodynamic performance with L/D comparisons to Cessna 206
Satisfy customer requirement
Aerolab Educational Wind Tunnel
Test Section Dimensions
12” x 12” x 24”
Input
Airflow Speed Voltage
(Max = 10 Volts)
Model Scale: 1⁄64
Desired Data
N = Normal Force [± 0.1 N]
A = Axial Force [± 0.1 N]
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Nando

## Slide 24: (SST) WIND TUNNEL TESTING
FR 4.0: A non-powered, scale model of the airframe design will be constructed for the purpose of practical wind tunnel
analysis in the PILOT Lab Wind Tunnel
AoA Test Range
+5°
-5°
 | C206 | NELDA | % Diff
L/D | TBD | TBD | Levels of Success
Rationale/Motivation:
Validate NELDA aerodynamic performance with L/D comparisons to Cessna 206
Satisfy customer requirement
Sting ⅜ EWT
Aerodynamic Forces
Lift - Normal [± 0.1N]
Drag - Axial [± 0.1 N]
Desired Data
Expected Results (Scale = 1/64):
L = Ncos(⍺) - Asin(⍺)
D = Nsin(⍺) + Acos(⍺)
Lift-to-Drag % Similarity
L1. Underperforms
L2. Similar (± 5% margin)
L3. > 5% Improvement
L4. > 10% Improvement
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Nando

## Slide 25: (SST) WIND TUNNEL TESTING - FBD
Power
FR 4.0: A non-powered, scale model of the airframe design will be constructed for the purpose of practical wind tunnel
analysis in the PILOT Lab Wind Tunnel
Inlet
Fan
Diffuser
Sting ⅜ EWT Sensor
Pitot Tube
Command (speed)
Dynamic Pressure
Data (pressure)
Data
(load cell voltages)
Experimental Load Outputs
LabView Console - GUI
Command
(speed)
Data
(forces)
LabView
= Start/Stop
= Measurement
= Environment
Control
-Normal Force
-Axial Force
-Pitching Moment
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Nando

## Slide 26: (SST) WIND TUNNEL TESTING - PROCEDURE
FR 4.0: A non-powered, scale model of the airframe design will be constructed for the purpose of practical wind tunnel
analysis in the PILOT Lab Wind Tunnel
Emergency Procedure
Press master shutoff button if:
Fan overspeeds
Debris/unstable/broken artifacts
Failed attachments
Post-Test
Save and export datafile
Remove test set-up
Clean room and store hardware
Test
Dismount Safety Net
Input airflow speed voltage
Vary angle of attack (AoA)
Pre-Test Safety Run
Input airflow speed voltage
Confirm data collection
Check for unstable attachments
Test Setup
Adjust angle of attack AoA = 0° (bullseye level)
Initialize LabVIEW
Mount safety net
Pre-Test Actions
Reserve Wind Tunnel
Install Sting ⅜ EWT
Mount & Secure model to Sting Sensor
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Nando

## Slide 27: (SST) WIND TUNNEL TESTING - SENSOR
Scale factor below 500 grams
(5 Newtons) highly variant
Need to exceed this minimum to get more accurate data
NELDA expects to achieve less than 100 grams (1 Newton) of axial force
 | Erroneous Region
 | Desired Region
Sting ⅜ EWT Sensor
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Tristan

## Slide 28: (SST) PRELOADING VERIFICATION TEST
DR 4.2.2: The test instruments should be capable of capturing aerodynamic forces above
the minimum resolution inherent to such instruments
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Tristan

## Slide 29: (SST) PRELOADING VERIFICATION TEST
Rationale/Motivation:
Demonstrate and verify preloading methodology
Procedures:
Control: Run Wind Tunnel at varied voltages and AoAs for assembly
(no preload)
Wrap rubber band around prefabricated F-16 model and back of Sting sensor
Run Wind Tunnel at varied voltages and AoAs for preloaded assembly
Compare preloaded data with control (no preload)
  Establish baseline expectations for data accuracy and precision
DR 4.2.2: The test instruments should be capable of capturing aerodynamic forces above
the minimum resolution inherent to such instruments
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Tristan

## Slide 30: (SST) PRELOADING VERIFICATION TEST - RESULTS
DR 4.2.2: The test instruments should be capable of capturing aerodynamic forces above
the minimum resolution inherent to such instruments
Expected Results:
Proof that we can achieve 5 N of constant preloading force and collect data
  Status: In Progress
See a statistically significant improvement in RMS error
  Status: In Progress
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Tristan
With the F-16 test, the preloading method has been validated to give the desired forces

## Slide 31: (SST) PRELOADING VERIFICATION TEST - RISKS / SAFETY
Risks:
  3D Printed Models structurally fail during WT experiment(s)
    Addressed with “Car-top” Testing
  Rubber band breaks
    External Sting ⅜ EWT Preloading Test
    Pre-Testing with net in place
Emergency Procedures
  Deactivate wind tunnel using master shut-off switch
DR 4.2.2: The test instruments should be capable of capturing aerodynamic forces above
the minimum resolution inherent to such instruments
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Tristan

## Slide 32: (MFCT) CAR TOP SAFETY TEST
Rationale/Motivation:
Verify structural integrity of WT models
(NELDA + C206)
  Risk: Unproven model could break inside WT and damage the equipment
Procedure:
Manufacture Sting sensor replica mount
Mount assembly to car sunroof
Run slow car test (~20 mph)
Step to higher speed car tests (40+ mph) with video recording (~5 mph increments)
Establish FOS > 1.2x WT Test Speed
DR 4.1.3: The scaled models of each aircraft shall be capable of withstanding relative air velocities up to 55 mph
3D-PRINTED STING MOUNT REPLICA
CLAMPS TO ROOFTOP
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Jake
Ensure the wind tunnel model is structurally sound
(Describe test fixture. Are we holding it, making “fake” sting?)
(Diagram of test fixture)
Procedures:
Start on slower roads (30-40 MPH)
Work up to faster speeds (40-50 MPH)
Test on highway (50+ MPH)

## Slide 33: (MFCT) CAR TOP SAFETY TEST
NETTING AFIXED BEHIND MODEL
Expected Results
Pass: Models withstand up to 1.2x the maximum
expected WT speeds (~55mph X 1.2 = 66mph)
Fail: Models fail at speeds < 66 mph
  Video recording to provide failure point
Safety
Risks
  Cannot have any loose / lost articles in test
  Need to avoid other vehicles
Mitigation
    Apparatus is snug - Inspect mount and fasteners
    Test on a private or closed road
    Safety net attached behind model
DR 4.1.3: The scaled models of each aircraft shall be capable of withstanding relative air velocities up to 55 mph
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Jake

## Slide 34: (SST) GLIDER TESTING
Rationale/Motivation:
Validate airframe stability
Practical demonstration of configuration feasibility and performance when in an unpowered glide
Desired Data
Position, Velocity, Time (3 dimensions)
Expected Results
Qualitative demonstration of longitudinal/lateral dynamic modes
  Limitations: Lightweight model, variable conditions, reduced dynamic similarity
FR 5.0: A non-powered, larger scale glider model of the airframe design will be constructed for the purpose of stability
analysis and verification
NELDA’s most important test for design validation
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Tristan/Julia

## Slide 35: (SST) GLIDER TESTING
FR 5.0: A non-powered, larger scale glider model of the airframe design will be constructed for the purpose of stability
analysis and verification
Procedure:
Manufacture foam prototype
Start with low altitude low velocity launches
(Experimental Trim)
Progress to launch from roof of Aerospace Engineering Building (with faculty assistance)
Film each launch from two angles, side and front for post processing via LoggerPro
Measure distance traveled using a rangefinder (Bushnell Medalist: +/-1m Precision)
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Tristan/Julia

## Slide 36: (SST) GLIDER TESTING
Test Day Procedure:
Camera Operators Ready
Timer Ready
Flight Path Cleared
Launch Glider
Record Data (video of flight, time of flight, and distance traveled using rangefinder)
Repeat as necessary
FR 5.0: A non-powered, larger scale glider model of the airframe design will be constructed for the purpose of stability
analysis and verification
Flight path
Camera 1
Camera 2
Launch point
Timer
Rangefinder
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Tristan/Julia

## Slide 37: (SST) GLIDER TESTING - LOGGERPRO
Track glider flight in two separate orthogonal planes (X-Z, Y-Z)
Obtain position,
velocity, time data
Analyze data and compare
to stability models
EXAMPLE
FLIGHT PATH
X
Z
Validation of predicted
stability characteristics via comparison to 1st Semester stability models
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Tristan/Julia

## Slide 38: (SST) GLIDER TESTING - SAFETY
Testing Logistics
Risk of impact with personnel if landing zone not clear
  Mitigation: Rope off expected flight test area, clearance from AES Building Manager
Glider Model Structures (expected points of failure)
FR 5.0: A non-powered, larger scale glider model of the airframe design will be constructed for the purpose of stability
analysis and verification
Risks | Mitigation Strategies
Foam fuselage failure | Multiple foam gliders constructed
Wing/Canard failures | Carbon Fiber spar reinforced wings
 | High strength foam adhesive
Gear/Winglet failures | Replacement 3D printed parts
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn:

## Slide 39: (MFCT) GLIDER TESTING - SCALING
Geometry (Linear scaling)
CSD glider models must be accurately scaled
Wingspan = 3.5 ft → Scale Factor: 1/14
Weight (Non-linear scaling)
Scale Factor: (1/14)3 → Assembly weight = 1.5 lbs
CG must be implemented with properly scaled geometry
  Required for stability demonstration
DR 5.1.1: A larger scaled model of the aircraft design shall be constructed on a 1/14th scale
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn:

## Slide 40: [MFCT] CG TESTING
Rationale/Motivation
Ensure the glider models are properly scaled for stability demonstration
  Risk: Misaligned CG will yield inaccurate (unusable) data
  Mitigations:
    Highly accurate predictions from CAD
    Experimental Verification with CG Tests
High Level Approach
Model the Predicted CG and required CG for scaling (Complete)
Create a model to determine required Ballast location to ensure proper CG (Complete)
Experimentally Verify Glider CG location (Planned)
Update Ballast model to reflect results of CG location
DR 5.1.1: A larger scaled model of the aircraft design shall be constructed on a 1/14th scale
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn

## Slide 41: [MFCT] CG TESTING - EXPECTED RESULTS
Required Glider CG:
X: 12.6 ± 0.1 in
Y: 0.0 in
Z: 1.6 in ± 0.1
Expected Glider CG:
X: 12.6 ± 0.1 in
Y: 0.0 in
Z: 0.8 ± 0.1 in
DR 5.1.1: A larger scaled model of the aircraft design shall be constructed on a 1/14th scale
Expected Weight (No Ballast):
0.8 lbs
Required Weight:
1.5 lbs [ k = (1/14)3 ]
→ Ballast of 0.7 lbs
Expected Ballast Coordinates:
X: 12.6 ± 0.1 in
Y: 0.0 in
Z: 2.5 ± 0.1 in
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Required CG from Scaling
Predicted CG from CAD
Predicted Weight from CaD
Required Weight from Scaling
Predicted Ballast from Comp Models
Mention that if the test does not meet our predicted CG, then the process is iterated on to find the new Ballast Location

## Slide 42: [MFCT] LATERAL CG TEST
Procedures:
Attach two looped strings to a rigid pole or structure which have a distance equivalent to the length of the NELDA CSD Model
Hang the first looped string from the tail of the CSD model
Hang the second looped string to the push pin inserted in the nose of the aircraft
If needed, add small increments ballast weights to the lighter wing ~20% span from the fuselage until weight is laterally symmetric
DR 5.1.1: A larger scaled model of the aircraft design shall be constructed on a 1/14th scale
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn
https://www.scienceworld.ca/resource/finding-centre-gravity/
https://www.rc-airplane-world.com/balancing-rc-airplanes.html
Motivation/Rationale:
Ensure the model’s center of gravity is consistent with the full-scale model
Procedure:
Hang looped sting from the propeller of CSD
Hang second looped string in front of canard
  Or insert small rod/screw into nose of aircraft and hang string from there
Add ballast to lighter (higher) wing in small increments to the wings until the CSD is horizontally balanced
Finn:

## Slide 43: [MFCT] LATERAL CG TEST
DR 5.1.1: A larger scaled model of the aircraft design shall be constructed on a 1/14th scale
Approx. CG Location
Level Stick
String
> 8”
* Not to scale
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn
https://www.scienceworld.ca/resource/finding-centre-gravity/
https://www.rc-airplane-world.com/balancing-rc-airplanes.html
Motivation/Rationale:
Ensure the model’s center of gravity is consistent with the full-scale model
Procedure:
Hang looped sting from the propeller of CSD
Hang second looped string in front of canard
  Or insert small rod/screw into nose of aircraft and hang string from there
Add ballast to lighter (higher) wing in small increments to the wings until the CSD is horizontally balanced
Finn:

## Slide 44: [MFCT] LONGITUDINAL CG TEST
Procedures*:
Attach two looped strings to a rigid pole or structure which have a distance equivalent to the length of the fuselage for the NELDA CSD Model
Hang the first looped string to the push pin located at the desired center of gravity on the left side of the CSD fuselage
Hang the second looped string to the push pin located at the desired center of gravity on the left side of the CSD fuselage
If needed, add small increments ballast weights near the nose of the aircraft or move the ballast behind the CG to correct erroneous static margin
DR 5.1.1: A larger scaled model of the aircraft design shall be constructed on a 1/14th scale
Ballast
Ballast
T Pins
*Longitudinal CG Test performed AFTER Lateral
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn
https://www.scienceworld.ca/resource/finding-centre-gravity/
https://www.rc-airplane-world.com/balancing-rc-airplanes.html
Motivation/Rationale:
Ensure the model’s center of gravity is consistent with the full-scale model
Procedure:
Hang looped sting from the propeller of CSD
Hang second looped string in front of canard
  Or insert small rod/screw into nose of aircraft and hang string from there
Add ballast to lighter (higher) wing in small increments to the wings until the CSD is horizon tally balanced
Ballast:
Heavier layers of material to wrap the fuselage with (i.e thin sheet lead,etc)
Metals balls fixed with epoxy glue
Finn:

## Slide 45: [MFCT] LONGITUDINAL CG TEST
DR 5.1.1: A larger scaled model of the aircraft design shall be constructed on a 1/14th scale
Table
Table
Level Stick
Approx. CG Location
String
> 8”
* Not to scale
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn
https://www.scienceworld.ca/resource/finding-centre-gravity/
https://www.rc-airplane-world.com/balancing-rc-airplanes.html
Motivation/Rationale:
Ensure the model’s center of gravity is consistent with the full-scale model
Procedure:
Hang looped sting from the propeller of CSD
Hang second looped string in front of canard
  Or insert small rod/screw into nose of aircraft and hang string from there
Add ballast to lighter (higher) wing in small increments to the wings until the CSD is horizon tally balanced
Ballast:
Heavier layers of material to wrap the fuselage with (i.e thin sheet lead,etc)
Metals balls fixed with epoxy glue
Finn:

## Slide 46: (SST) GLIDER TESTING - 3D PRINTED MODEL
Stretch Goal (Higher Level of Success)
Generate 3D Printed Model pending results of Foam Prototype testing
  More precise geometry
  Stronger Assembly
DR 5.1.1: A larger scaled model of the aircraft design shall be constructed on a 1/14th scale
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Tristan/Julia

## Slide 47: BUDGET Presented by: Julia Tucker
Budget
Budget Breakdown
Glider Budget
WTAV Budget

## Slide 48: BUDGET
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: https://www.scienceworld.ca/resource/finding-centre-gravity/
https://www.rc-airplane-world.com/balancing-rc-airplanes.html
Motivation/Rationale:
Ensure the model’s center of gravity is consistent with the full-scale model
Procedure:
Hang looped sting from the propeller of CSD
Hang second looped string in front of canard
  Or insert small rod/screw into nose of aircraft and hang string from there
Add ballast to lighter (higher) wing in small increments to the wings until the CSD is horizontally balanced
Finn:

## Slide 49: BUDGET BREAKDOWN
 | Spent
 | Planned
 | Margin
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: https://www.scienceworld.ca/resource/finding-centre-gravity/
https://www.rc-airplane-world.com/balancing-rc-airplanes.html
Motivation/Rationale:
Ensure the model’s center of gravity is consistent with the full-scale model
Procedure:
Hang looped sting from the propeller of CSD
Hang second looped string in front of canard
  Or insert small rod/screw into nose of aircraft and hang string from there
Add ballast to lighter (higher) wing in small increments to the wings until the CSD is horizontally balanced
Finn:

## Slide 50: GLIDER BUDGET
Risks:
  Glider will break in testing
Safety Margin:
  Purchased enough materials for three glider models
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: https://www.scienceworld.ca/resource/finding-centre-gravity/
https://www.rc-airplane-world.com/balancing-rc-airplanes.html
Motivation/Rationale:
Ensure the model’s center of gravity is consistent with the full-scale model
Procedure:
Hang looped sting from the propeller of CSD
Hang second looped string in front of canard
  Or insert small rod/screw into nose of aircraft and hang string from there
Add ballast to lighter (higher) wing in small increments to the wings until the CSD is horizontally balanced
Finn:

## Slide 51: WTAV BUDGET
Risks:
  WTAV models will break in car-top testing
  WTAV models will break in wind tunnel testing
Safety Margin:
  Abundant materials for further iterations
  Abundant budget for further printing
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: https://www.scienceworld.ca/resource/finding-centre-gravity/
https://www.rc-airplane-world.com/balancing-rc-airplanes.html
Motivation/Rationale:
Ensure the model’s center of gravity is consistent with the full-scale model
Procedure:
Hang looped sting from the propeller of CSD
Hang second looped string in front of canard
  Or insert small rod/screw into nose of aircraft and hang string from there
Add ballast to lighter (higher) wing in small increments to the wings until the CSD is horizontally balanced
Finn:

## Slide 52
ACKNOWLEDGEMENTS
Dr. Jelliffe Jackson
Dr. Kathryn Wingate
Dr. Brian Argrow
Dr. Donna Gerren
Dr. John Farnsworth
Professor John Mah
Matt Rhode
Katie-Rae Williamson
Project Advisory Board
Colin Claytor
Emma Markovich
Richard Schaden
Bobby Hodgkinson
Josh Mellin
Trudy Schwartz
Michael Rhodes

## Slide 53
REFERENCES
Center of Gravity Tests
https://www.scienceworld.ca/resource/finding-centre-gravity/
https://www.rc-airplane-world.com/balancing-rc-airplanes.html

## Slide 54: BACK UP SLIDES
WBS |  |  | Glider |  | Static Margin
Gantt |  |  | Onboard Sensors |  | 
 |  |  |  |  | Stability
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP

## Slide 55: (SST) GLIDER TESTING - ONBOARD SENSORS?
Stretch Goal (Higher Level of Success)
Implement onboard sensors and electronics
  Obtain more precise position, velocity, time data
Accelerometers, Pickhawk, ArduPilot
  ArduPilot Software is very plug and play
Accelerometers can be obtained from AES Department
  (no further financial risk)
As of TRR, not fully prepared to complete this test, would have to be incorporated if everything else goes right
DR 5.1.1: A larger scaled model of the aircraft design shall be constructed on a 1/14th scale
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Tristan/Julia

## Slide 56: PROJECT SCHEDULE - GANTT
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Quick overview of full schedule
Emphasis on testing schedule
Margin defined with reason
Critical path shown

## Slide 57: PROJECT SCHEDULE - SPRING WBS
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Quick overview of full schedule
Emphasis on testing schedule
Margin defined with reason
Critical path shown

## Slide 58: (SST) GLIDER TESTING PROCEDURES
FR 5.0: A non-powered, larger scale glider model of the airframe design will be constructed for the purpose of stability
analysis and verification
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Tristan/Julia

## Slide 59: Glider Structures - Deflection
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP

## Slide 60: (MFCT) GLIDER TEST - SCALING
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn:

## Slide 61: Glider Structures - Spar
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP

## Slide 62: CESSNA 206 3D SCANNING
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn:

## Slide 63: FULL SCALE AIRCRAFT SECTION VIEW
BATTERY #2
BATTERY #1
MOTOR
AVIONICS PACKAGE
20.8”
30.0”
19.0”
20.0”
29.7”
20.0”
35.3”
20.1”
43.4”
48”
25.7”
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn:

## Slide 64: FULL SCALE AIRCRAFT FLOOR PLAN
BATTERY #2
BATTERY #1
NOSE
TAIL
FIREWALL
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn:

## Slide 65: FULL SCALE AIRCRAFT INTERIOR LAYOUT
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn:

## Slide 66
BASELINE DESIGN: CG
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP

## Slide 67: SCALED COMPONENT WEIGHTS - AAA
Element | Weight Factor | Full Scale Weight (lbs) | CSD Weight (lbs)
Wings | 0.1093 | 447.3 | 0.163
Fuselage | 0.1457 | 596.6 | 0.217
Canard | 0.0165 | 67.5 | 0.025
Vertical Tail | 0.0125 | 51.1 | 0.019
Fixed Equipment | 0.0506 | 207.0 | 0.075
Passengers | 0.2786 | 1,140.0 | 0.416
Landing Gear | 0.0543 | 222.3 | 0.081
Power Plant | 0.0600 | 245.8 | 0.090
Propeller | 0.0409 | 167.4 | 0.061
Batteries | 0.2318 | 949.0 | 0.346
Totals | 1.000 | 4,094 lbs | 1.492 lbs
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn:

## Slide 68: [MFCT] FOAM GLIDER WEIGHT BUDGET
Component | Weight [lbs] | CG Location (X, Y, Z) [in]
Fuselage | 0.258 | (10.971, 0, 1.873)
Foam Wing (x2) | 0.033 | (15.589, 0, 2.305)
Wing Spar | 0.080 | (14.949, 0, 2.243)
Winglet (x2) | 0.055 | (15.558, 0, 2.700)
Foam Canard (x2) | 0.007 | (6.130, 0, 0.168)
Foam Tail | 0.008 | (20.925, 0, 6.099)
Gear | 0.372 | (12.536, 0, -0.830)
Ballast |  | 
Total | 1.5 | (12.686, 0, 1.603)
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn:

## Slide 69: [MFCT] FOAM GLIDER ASSEMBLY CG
CG Location | Full Scale | CSD
X | 177.6 in | 12.686 in
Y | 0 in | 0 in
Z | 22.44 in | 1.603 in
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP

## Slide 70: CSD MANUFACTURING PRECISION ANALYSIS
Key Characteristics | Full Scale Value | Target Value | Allowed Margin
Wing Span | 47.38 ft = 568.56 in | 40.6114 in | +/- 0.01 in
Wing Root Chord | 5.26 ft = 63.12 in | 4.5086 in | +/- 0.01 in
Wing Tip Chord | 2.63 ft = 31.56 in | 2.2543 in | +/- 0.01 in
Canard Span | 6.43 ft = 77.16 in | 5.5114 in | +/- 0.01 in
Canard Root Chord | 3.34 ft = 40.08 in | 2.8629 in | +/- 0.01 in
Canard Tip Chord | 3 ft = 36 in | 2.5714 in | +/- 0.01 in
Fuselage Diameter | 5 ft = 60 in | 4.2857 in | +/- 0.01 in
Fuselage Length | 26.5 ft = 318 in | 22.7143 in | +/- 0.01 in
Vertical Tail Root Chord | 5.78 ft = 69.36 in | 4.9543 in | +/- 0.01 in
Vertical Tail Tip Chord | 4.05 ft = 48.6 in | 3.4714 in | +/- 0.01 in
Vertical Tail Span | 7.37 ft = 88.44 in | 6.3171 in | +/- 0.01 in
Landing Gear | 3.590 ft = 43.077 in | 3.0769 in | +/- 0.01 in
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn:

## Slide 71: CSD MANUFACTURING ASSEMBLY PROCEDURE
Fuselage Joining
  Utilizing a foamboard adhesive or general epoxy, glue the left and right fuselage components together.
  Use sign extrusions for alignment, clamp and let dry for 24 hours.
Wing/Canard Joining and attachment
  Join the left, right wing and spar together with an epoxy adhesive, let dry for 24 hours
  Insert wing into fuselage, pin into place, glue and let dry for 24 hours.
  Repeat steps 2.a & 2.b for the Canard
Landing gear attachment
  Using a loctite polyurethane adhesive, fill the landing gear channel with a bead of glue, insert the 3D printed part, clamp and let dry for 4 hours.
Vertical tail attachment
  Insert vertical tail into fuselage slot, pin into place, glue and let dry for 24 hours
Winglet attachment
  Finally, using the loctite adhesive, glue the tip chord profile face and insert each winglet, gold in place for 5 minutes then let dry for 4 hours
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Finn:

## Slide 72: Sub Test to Center of Gravity Tests
Procedures:
Cut out a block of foam with a weight of 1.5 lbs. Determine the center of gravity of this foam block. Mark the CG on each side of the block.
Insert a push pin straight into one side of the block at the location of the CG. Insert the other push pin into the foam block on the side parallel to the face with the push pin in it.
Tie the two ends of the fishing wire that has a length of approximately 40” in order to make a looped string.
Attach one end of the looped string to one of the push pins, wrap the string over the leveler on the tables, place the block underneath the leveler, and connect the other end of the wool string to the push pin on the other side.
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP

## Slide 73: (SST) WIND TUNNEL TESTING - PROCEDURE
FR 4.0: A non-powered, scale model of the airframe design will be constructed for the purpose of practical wind tunnel
analysis in the PILOT Lab Wind Tunnel
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Nando
Mandolorian

## Slide 74: WTAV Cessna 206 Sting Adapter
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Nando
Mandolorian

## Slide 75: TESTING LIMITATIONS
Wind Tunnel Testing: Scope and access both limited
  3ft x 3 ft unavailable for use and lacks instrumentation for our models
  Reynold’s Numbers dissimilar, so relying on comparative testing
  Specific Customer Requirement
Powertrain considerations are not the focus of the project
  Aerodynamic models rely on black-box assumptions for the powertrain
  Not feasible to run thermal tests (batteries), powertrain, or full-scale tests (structures)
Powered models are out-of-scope
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Emerson

## Slide 76: PROJECT SCHEDULE - GANTT
Dont delete anything
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Quick overview of full schedule
Emphasis on testing schedule
Margin defined with reason
Critical path shown

## Slide 77: (SST) WIND TUNNEL TESTING
FR 4.0: A non-powered, scale model of the airframe design will be constructed for the purpose of practical wind tunnel
analysis in the PILOT Lab Wind Tunnel
AoA Test Range
+5°
-5°
L/D | C206 | NELDA | % Diff
WT Model | unpredictable | unpredictable | Levels of Success
Lift-to-Drag % Similarity
L1. Unreadable
L2. > 25% margin
L3. ±15%
L4. ± 10%
Model Scale: 1⁄65
Rationale/Motivation:
Demonstrate drag reduction in NELDA model compared to a Cessna 206 model
Satisfy customer requirement
Sting ⅜ EWT
Aerodynamic Forces
Lift - Normal [± 0.1N]
Drag - Axial [± 0.1 N]
Desired Data
Input
Airflow Speed Voltage
(Max = 10 Volts)
Aerolab Educational Wind Tunnel
Expected Results
Test Section Dimensions
12” x 12” x 24”
OVERVIEW | SCHEDULE | TEST READINESS | BUDGET | BACK UP
Notes: Nando
25% is level 4: Notes other levels and corresponding percentages
Post Processing:
Drag Comparison
NELDA vs. Cessna 206
Check what specific design requirement this is
What and why ( possible 2 slides)
Rubric:
Describe the scope of the testing tasks in the project: what tests are being planned, specifically:
  what is being tested for (your rationale for performing the test),
  the design of the test fixtures,
  what test equipment and facilities are needed, and
  an overview of the test procedures.
Describe how the test(s) will reduce risk to your project, what results do you expect, and what
models will be validated.
Describe the status of the testing tasks, showing engineering details as needed to convey a solid
understanding of the design (and the ability to reduce risk), requirements to be verified or validated,
and what V&V is most important for project success.

## Slide 78: Dynamic Stability
PURPOSE | DESIGN | CPEs | DESIGN REQs | RISKS | V&V | PLANNING | BACK UP

## Slide 79: DYNAMIC STABILITY
Show predicted longitudinal response times and matrices from our dynamic stability code.
PURPOSE | DESIGN | CPEs | DESIGN REQs | RISKS | V&V | PLANNING | BACK UP
Notes: Split slides gen response/ind modes OR lon/lat depending on Rl/Sr
A
1: lon/lat GR, description of modes and motion of plane
2: selected modes (probably sp,ph,dr) w/ damp/ts, more in depth descriptions
B
1: lon modes, damp/ts for each, longer description of modes
2: lat modes, damp/ts for each

## Slide 80: DYNAMIC STABILITY
Show predicted longitudinal response times and matrices from our dynamic stability code.
PURPOSE | DESIGN | CPEs | DESIGN REQs | RISKS | V&V | PLANNING | BACK UP
Notes: Split slides gen response/ind modes OR lon/lat depending on Rl/Sr

## Slide 81: DYNAMIC STABILITY
Show predicted longitudinal response times and matrices from our dynamic stability code.
PURPOSE | DESIGN | CPEs | DESIGN REQs | RISKS | V&V | PLANNING | BACK UP
Notes: Split slides gen response/ind modes OR lon/lat depending on Rl/Sr

## Slide 82: DYNAMIC STABILITY
Show predicted longitudinal response times and matrices from our dynamic stability code.
PURPOSE | DESIGN | CPEs | DESIGN REQs | RISKS | V&V | PLANNING | BACK UP
Notes: Split slides gen response/ind modes OR lon/lat depending on Rl/Sr

## Slide 83: DYNAMIC STABILITY
Show predicted longitudinal response times and matrices from our dynamic stability code.
PURPOSE | DESIGN | CPEs | DESIGN REQs | RISKS | V&V | PLANNING | BACK UP
Notes: Split slides gen response/ind modes OR lon/lat depending on Rl/Sr

## Slide 84: DYNAMIC STABILITY
PURPOSE | DESIGN | CPEs | DESIGN REQs | RISKS | V&V | PLANNING | BACK UP

## Slide 85: DYNAMIC STABILITY
PURPOSE | DESIGN | CPEs | DESIGN REQs | RISKS | V&V | PLANNING | BACK UP

## Slide 86: DYNAMIC STABILITY
PURPOSE | DESIGN | CPEs | DESIGN REQs | RISKS | V&V | PLANNING | BACK UP

## Slide 87: DYNAMIC STABILITY
PURPOSE | DESIGN | CPEs | DESIGN REQs | RISKS | V&V | PLANNING | BACK UP

## Slide 88: DYNAMIC STABILITY
PURPOSE | DESIGN | CPEs | DESIGN REQs | RISKS | V&V | PLANNING | BACK UP