## Slide 1: NESSIE
NIGHTTIME ELEVATED SYSTEM FOR SATELLITE IMAGING AND EVALUATION

## Slide 2: Project Overview
      Space Domain Awareness (SDA)
Determine the orbital characteristics of objects in space
Currently there are only two methods
Radar
  Expensive
Telescopes
  Cheaper, but can be blocked by cloud cover
  Both are fully booked and can't collect enough data
Over 500,000 estimated objects in orbit
-https://www.nasa.gov/mission_pages/station/news/orbital_debris.html
Notes: So the the Problem- There are millions of objects in space, and many of these we don’t know there exact location or trajectory. This is dangerous because multi million or even billion dollar satellites are susceptible to collision. That’s where the Field of SSA comes in, to analyze these parameters and provide the necessary info to perform maneuvers to save space systems, but this isn't easy or cheap in general. Radar cost millions, and ground based telescopes can be occluded by cloud cover, which has lead to a global need for SSA platforms. So How do we solve this problem-

## Slide 3: Our Mission:
MANTA
Full-Scale SSA UAV
Operates at 18,000 ft
Fully realized optical payload
  Mass 15 lbs
  Contained in 12” cube
  Requires 132 W of Power
Scale 1 : 2.5
NESSIE
Proof of concept vehicle
Operates at 400 ft AGL
Payload bay capability
  Mass 1 lb
  Contained in 4.9” cube
  Requires 5.6 W of Power
Provide path to flight at full-scale
Notes: The initial mission was MANTA which was intended to get to 18,000 ft and had a 15 lb payload
we decided to move to a scale model since the initial vehicle was too large and costly for us to build
the model NESSIE will be a proof of concept that the project could work.

## Slide 4
1. System transportation
4. Pointing and stabilization check, autonomous flight
5. Point optical system, capture image, measure time and position
6. Store image and data
Dimness ≥ 13 apparent magnitude
3. Manual ascent above clouds, uplink from ground station
10 arcseconds object centroid identification accuracy, 3 sigma precision
2. Unload/ Assembly/ Prep.
Ground Station
Land 300 ft (100 yards) from takeoff spot
Loop
7. Start autonomous descent to Ground Station when battery is low.
End of mission 14 hours after first ascent
8. Manual landing, uplink from ground station
Constantly downlink position and status data to ground station
Stay on a 65,600 ft to 164,000 ft distance from takeoff spot
Max altitude 18,000 ft
Legend:
🡪 Requirements
🡪 Operations flow
Notes: This Figure illustrates the full mission scope where a team would go out to a location deploy the NESSIE system, collect SSA data for a time period and descend. So Where our team comes in this

## Slide 5
1. System transportation
4. Systems check, Manual flight
Max altitude 80 ft
Stay within 400 ft of takeoff spot
3. Manual ascent, uplink from ground station
2. Unload/ Assembly/ Prep.
7. Manual landing, uplink from ground station
Downlink position and status data to ground station
Land 300 ft (100 yards) from takeoff spot
End of mission when battery reaches ~20%
6. Start manual descent to Ground Station when battery is low.
Ground Station
5. Continuously collect acceleration data from onboard IMUs
Provide power and data connectivity to payload
Legend:
🡪 Requirements
🡪 Operations flow
Notes: This Figure represents the CONPOPS of our Sr. Project team.
Will drive out to a field
prep our A/c
Ascend it to 400ft
Conduct a comm check
Collect data for XXX mins
Descend and land saftley

## Slide 6: Levels of Success

## Slide 7: Design Description - Overall Outcome
Measured mass of the envelope, measured mass of the gongola, mass of the lifting gas, volume of the envelope, net lift of the envelope
Figure of NESSIE CAD with most important dimensions and description of functionality of most important parts
Notes: This is a top level description of the overall outcome of your design efforts. It should show what the whole system looks like, its key parameters (dimensions, mass, data rates, etc.), what the major elements or subsystems are, and most importantly, how it works. Include a functional block diagram. This provides the context and terminology for more detailed descriptions later in the presentation.

## Slide 8: Design Description - Overall Outcome
Gondola & avionics:
4S Lipo battery, 5,200 mAh
PixHawk 4 Mini
PixHawk Radio Kit
Arduino Nano 33 BLE
Total measured mass = 5.57 lbs.
Propeller blades and motors (2x):
Diameter = 1.3 ft.
Carbon fiber blades
Combined thrust = 14.8 lbf
Edge Connectors (3x):
3D Printed PLA
Measured combined mass = 0.22 lbs.
Envelope:
PVC film 7/1000” thick
Measured mass = 35.8 lbs.
Volume = 888 ft^3
Net lift = 19.2 lbs.
Dimensions: R = 7.5 ft, r = 2.5 ft.
Tail:
EPS foam coated with epoxy resin
Expected combined mass = 0.22 lbs.
Structural tubes (3x):
Carbon fiber
Measured combined mass = 3.06 lbs.
Notes: This is a top level description of the overall outcome of your design efforts. It should show what the whole system looks like, its key parameters (dimensions, mass, data rates, etc.), what the major elements or subsystems are, and most importantly, how it works. Include a functional block diagram. This provides the context and terminology for more detailed descriptions later in the presentation.

## Slide 9: Design Description - FBD
9
Ground Station
Pixhawk 4 Mini
Motor Shaft Servo
Elevator Servo
Release Valve
Motor 2
Motor 1
ESC 2
ESC 1
Battery
IMU Battery
PDB
5V BEC
GPS
Telemetry
IMU
Receiver
LEDs
Legend
Components
Processor
Sensor
5V Power
Data
Controls
Power
14.8V Power
MavLink
I2C
MavLink
UART
4.2 kB/s
Notes: This is a top level description of the overall outcome of your design efforts. It should show what the whole system looks like, its key parameters (dimensions, mass, data rates, etc.), what the major elements or subsystems are, and most importantly, how it works. Include a functional block diagram. This provides the context and terminology for more detailed descriptions later in the presentation.
BEC - Battery Eliminator circuit
PDB - distribution board
ESC - electronic speed control

## Slide 10: Design Description - Major changes from TRR
The lifting gas was switched to helium for safety concerns regarding handling the gas, and filling/deflating the envelope.
The envelope is 8.45 lbs lighter than expected, therefore a ballast was added to meet the design weight and prevent the blimp from flying over the height limit.
Servos, mechanical links, and gears had to be incorporated to the tail, and gondola to control the horizontal control surfaces, and to rotate the motor shaft, respectively.
Elevator servo links
Motor shaft gears
Ballast connected at the unused envelope connections
Notes: Highlight major changes made since TRR, and briefly explain why they were made.

## Slide 11: Design Description - Critical Project Elements
Critical Project Element (CPE) | Description | Reason
Optical system mount capacity | Provide sufficient payload bay for scaled optical system | A mount capacity is needed for the optical system that will take the images that are required to fulfill the mission.
Aircraft stability | Aircraft must be stable | Stability allows the optical system to remove any frequency of less than 6.7 Hz in order to take clear images of the desired objects
Aircraft control | Aircraft will be controllable | Control allows it to fly up to a commanded altitude and position, collect data, and then return, all while enduring wind gusts and other perturbations.
Aircraft structure | Aircraft will be structurally sound | A gondola must be built to carry electrical components and interfaced with the balloon.
Path forward | The team will provide legal and technical documentation to continue towards MANTA | The path forward is needed to allow the customer to know what process he must follow to be able to complete the mission as he desires
Notes: Identify the elements in the design that are critical for project success (critical project
elements), and explain why.
** I believe we have a value in terms of frequency. 6.7Hz

## Slide 12: Test Overview: Path Forward
Testing and Verification
Fall Semester
February
March
April
Gondola Shake Test
Gondola Control Surface Test
Avionics Test
Power Test
Manual Controller Test
Envelope
Test ✔
FOV Test ✔
Wind Speed Test ✔
Complete System Test:
Indoor Tethered Test
Outdoor Tethered Test
Outdoor Flight Test
Notes: Here we have the test along with the time and order they had/should get done. We ran behind on schedule due to manufacturing and had issues that couldn’t be debugged on time with the tests we ran which cause the february test to be unfinished.
Note: Gondola Shake Test is now Object Determination Test

## Slide 13: Test Overview: Parts/Hardware Operation Testing
Avionics Test:
Ensure all avionics are electrically connected
Ensure all avionics – servos are physically connected
Verify all surfaces are working properly with ground-control readout
Power Test:
Determine the amount of power the system will consume – run all avionics on full power and measure the current draw with ammeter
Quantify the amount of power needed for the final field test
Compare these values to the predicted model
Manual Controller Test:
Establish the connection between the avionics and the manual controller
Perform full surface check with inputs from the controller – verify that commands are received
Purpose: To verify that the hardware is properly working before any integrated testing

## Slide 14: Test Overview: Envelope Inflation Test
Test Description
Test duration of inflation time
  Pressurized air
Ensure no punctures/leaks
Instruments/Materials/Equipment Used
  Aircraft Balloon Envelope
  Building pressurized air outlets
Test Environment
  AERO Building North High Bay
Design/Functional/Requirements Relation
  FR 2 - System shall be capable of flying at 400 ft
  DR 3.1 - System shall provide sufficient lifting force

## Slide 15: Test Overview: Envelope Deflation Test
Test Description
Determine viability of deflating the balloon without external aid
  Release valve & Burn wire
Instruments/Materials/Equipment Used
Same as previous
Tape measure
  Height of envelope
Test Environment
AERO Building North High Bay
  Section cordoned off to avoid stepping on envelope
Design/Functional/Requirements Relation
DR 3.3.2 - System shall provide sufficient lifting force
PAB request for safety

## Slide 16: Test Overview: Object Determination Test
Formerly known as the Shaker Table Test
Test Description
Shake test designed to verify NESSIE is a platform suitable to capture space images
No model is necessary for verifying/validating
Instruments/Materials/Equipment Used
  Raspberry Pi, Monitor, Camera, shaker platform (cutting board) & mount, MATLAB
  Note we are not using the shaker table located in the pilot. 1D vibrations aren’t realistic enough.
Test Environment
  Test would have been conducted at home or in Aero conference room with no safety concerns.
Design/Functional/Requirements Relation
  FR1 - “ability to take images for orbit determination”

## Slide 17: Test Overview: Tethered Tests
Test Description
  Designed to provide a comprehensive test of integrated system in a controlled setting
    Tethers mitigate risk of fly-away due to uncertain performance during first tests
Instruments/Materials/Equipment Used
  NESSIE
  RC controller
  Helium gas
Testing Environment
  Indoor Flight Space/CU South Boulder
  No concerns related to helium lifting gas
  Most significant concerns are those related to puncture of the envelope
Design/Functional Requirements Relation
  Helps validate DR 1.1, 2.2, 3.3, 4.2, and 4.3 regarding in-flight controllability and ability to land

## Slide 18: Test Overview: Tethered Tests
Expected Test Procedure
Transportation to flight area
  Ensure travel time is factored in to allow for prompt 10:30 am start time
Test area set up
  Emplant mooring stakes (outdoor test only)
  Place ground tarp (outdoor test only)
  Assemble NESSIE structure
Fill NESSIE with helium gas
  Fill Procedure in backup slide here
  Once rigid, NESSIE’s gondola will be affixed to gas envelope.
NESSIE flight
  See next slide for this procedure
Nessie landing and recovery
  See next slide for this procedure
Gas venting/recapture
  Helium from NESSIE will be vented
Data recovery
  In-flight IMU data
  GPS and any available flight controller data
  Pilot qualitative comments on vehicle performance will be recorded

## Slide 19: Test Overview: Tethered Flight Tests
Expected Flight Procedure:
Tethered Flight
  NESSIE will fly to 4 ft AGL
Box Pattern
  NESSIE will fly in a small box pattern to establish control
  NESSIE is taking data for FR1 here
Reduce Altitude
  NESSIE will use its motors to descend to 4 ft AGL
Recapture
  NESSIE will be secured

## Slide 20: Test Overview: Outdoor Free Flight Test
Test Description
  Demonstrate system performance in its complete operational environment
Instruments/Materials/Equipment Used
  NESSIE
  RC controller
  Helium gas
Testing Environment
  CU South Boulder
  Table Mountain flight space is backup
  Limited potential for fly-away
    Performance will be better characterized
Design/Functional Requirements Relation
  Helps validate DR 1.1, 2.2, 3.3, 4.2, and 4.3 regarding in-flight controllability and ability to land
  Will focus heavily on collection of IMU data

## Slide 21: Test Overview: Outdoor Free Flight Test
Expected Test Procedure
Transportation to flight area
  Ensure travel time is factored in to allow for prompt 10:30 am start time
Test area set up
  Emplant mooring stakes
  Place ground tarp
  Assemble NESSIE structure
Fill NESSIE with helium gas
  Fill Procedure in backup slide here
  Once rigid, NESSIE’s gondola will be affixed to gas envelope.
NESSIE flight
  See next slide for this procedure
Nessie landing and recovery
  See next slide for this procedure
Gas venting/recapture
  Helium from NESSIE will be vented
Data recovery
  In-flight IMU data
  GPS and any available flight controller data
  Pilot qualitative comments on vehicle performance will be recorded

## Slide 22: Test Overview: Outdoor Free Flight Test
Expected Flight Procedure:
Untethered Flight
  NESSIE will fly to 80 ft AGL
Box Pattern
  NESSIE will fly in a box pattern to establish control
  NESSIE is taking data for FR1 here
Reduce Altitude
  NESSIE will use its motors to descend to 10 ft AGL
Recapture
  NESSIE will be recaptured and staked via its tethers.
At any time, if control is lost, emergency solenoid and burn wire can be used in this test.

## Slide 23: Test Results: Envelope Inflation Test
Test Description
  Verifies that leaks or tears in the envelope are non-existent or negligible
  Preliminary investigation into effects of diffusion
Data Type
  Volume over time recorded via time-lapse video
Sources of error/uncertainty
  Volume is based on height measurements in the video
  Envelope filled with air instead of helium, diffusion of helium molecules at a different rate than diffusion of air
Design/Functional Requirements Satisfied
  This test was mostly to verify there were no issues with the envelope before moving on to further testing
  Related to FR 2 and DR 3.1 regarding capability of operating at design altitude and maintaining lifting force

## Slide 24: Test Results: Envelope Inflation Test
Results:
No leaks detected
Effects of diffusion deemed negligible over course of testing period
Verification and Validation:
No change in volume of the envelope implies that lift will remain constant
Validates FR2 and DR 3.1

## Slide 25: Test Results: Envelope Inflation Test
Test Description
  This test is to determine the viability of deflating the balloon without external aid.
Data Type
  By measuring the height of the envelope, the volume of the balloon can be estimated, assuming a flat bottomed torus
Sources of error/uncertainty
  As the tape measure cannot be placed directly next to the top of the envelope, human error of 1” is involved in making the height measurements
  The balloon likely does not deflate exactly as predicted, further complicating percentage fill volume estimation
  Low number of data points
Design/Functional Requirements Satisfied
  The requirements were not satisfied for this particular test
    Balloon would take an unacceptable amount of time to deflate on its own
Notes:     At an estimated 6 hour deflation time, this means the balloon would take an unacceptable amount of time to descend and to finish outgassing. If using hydrogen, the balloon would have to be left to finish this deflation process due to the risk of static shock, making it difficult to practically use. Note that both of these issues are mitigated by lifting gas choice and burn-wire systems.

## Slide 26: Test Results: Envelope Deflation Test
Verification and Validation:
DR 3.3.2 Satisfied, NESSIE can descend safely
  Deflated to neutrally buoyant in 1.3 min
  Note this was air, assuming time is proportional to density helium would take 9.7 minutes
Once valves were pinched, deflation stopped, requiring physical assistance.
Start
2 hours in

## Slide 27: Test Results: Object Determination Test
Status: Incomplete
Phase 1: Shake camera → Blurry images + Data
Phase 2: Matlab → Obtain restored images
Phase 3: Image Process → Obtain 3σ capability
Phase 4: Confirm validation
Validation for FR1 is confirmed by comparing vibrational data from shaker test with vibrational data from integrated flight test.

## Slide 28: Test Results: Object Determination Test
1 Hz image
4 Hz image
6 Hz image
Phase II: Deconvolute Image & Restore
Phase I: Image Capture Expected Results

## Slide 29: Test Results: Tethered Tests
Expected Results:
Controllability of vehicle FR. 2, FR 3
Ability to land unharmed FR. 2
Successful data transfer from vehicle to station DR.4.3 & 4.2
Envelope supports intact FR.1
Power usage per minute DR.1
Verification and Validation:
Visual confirmation of vehicle reacting to controller input
Land at desired location at velocities under 3 m/s.
Verify that the vehicle is doing what the data is reading.
Envelope attachment hardware, and surroundings, with no visible damage.
Check the battery for remaining power/energy
Notes: I am mentioning that there is no wind therefore the landing verification velocity should be at 3 m/s or less.
***- I think it would be a good data to have and quantify.

## Slide 30: Test Results: Outdoor Free Flight Test
Expected Results:
Power usage per minute DR.1
Altitude control-ability FR. 3
5 mph gusts resistance FR. 2
Vibrational data returned from IMU FR. 1, DR.1
  Would require post-processing
Verification and Validation:
Check for battery remaining power*
Vehicle is capable of maintaining desired altitude within ±50 ft
Aircraft maintain stability with incoming wind shear
Vibrational data would confirm that flight is stable enough to take images sufficient for calculating initial orbit determination
Notes: *- Same as slide 23. Here to see the how much the incomming gusts affect power usage.
**- is 20ft a good range? Let me know what you think.

## Slide 31: Levels of Success Completed
Legend
Highly expected
Moderately expected
Notes: ✔

## Slide 32: Systems Engineering: Left Side of V
Feasibility
Study/
Concept
Exploration
Concept of Operations
System Requirements
High-Level Design
Detailed Design
Software/ Hardware
Development
Field Installation
Unit Device Testing
Subsystem
Verification
System Verification & Deployment
System Validation
Operations and Maintenance
System Validation Plan
System Verification Plan
Subsystem
Verification Plan
Unit/Device Test Plan
System Engineering V
Key Trade Studies
Developed the overall mission and design space
Dirigible rather than Fixed-wing
  Potential uptime, relative stability
Torus shaped balloon vs traditional
  Superior exposure times
Requirements Development:
Notional Payload Requirements
  Extensive optical and vibrational analysis to define this payload
  Drove vehicle size, geometry, needed stability, etc
Customer Derived
  Flight time, relative size (~carried by 3 people)
Regulations
  FAA 55 lb limit, altitude restrictions
Systems Engineering V, Left Hand Side:
Almost entirely completed in Fall semester
PDD, CDD, PDR, CDR, FFR
Notes: Summarize the systems engineering approach for the project (e.g. guided by the systems engineering “V”, conducted trades (briefly describe key trades that led to your team’s design), derived and flowed down requirements from functional objectives, developed Interface Control Documents, assessed risk (used FMEA or other approach) and etc.).

## Slide 33: Systems Engineering: Software/Hardware Development Status
Feasibility
Study/
Concept
Exploration
Concept of Operations
System Requirements
High-Level Design
Detailed Design
Software/ Hardware
Development
Field Installation
Unit Device Testing
Subsystem
Verification
System Verification & Deployment
System Validation
Operations and Maintenance
System Validation Plan
System Verification Plan
Subsystem
Verification Plan
Unit/Device Test Plan
System Engineering V
Subsystems
Avionics:
  Power: Battery, ESC, BEC interfaces
  Flight Controller: Connections to all relevant systems
  Radio: connection, control gains
  P/L IMU: connection, decoding, interface
  Actuators: Motors & servo connections, BEC power
Structure:
  Arms: Cut to length, Pin holes drilled
  Tail Boom: Extended with Al spline, pin holes drilled
  Gondola: Box cut and assembled
  T Connection: pipes turned to proper radius, milled to shape, welded
  Tail: H stab cut to shape/thickness, V stab cut, elevator cut, assembled
Balloon:
  Vendor Requirements, bought and paid for
  Interfaces: 3d printed attachments
  Additional Notes: Potential changes needed: Given the ongoing He vs H2 conversations w/ CU several potential modifications may have been needed, including adding valves(~10) and moving valve locations, and other potential changes
Legend:
Finished as of CU Closure
In-progress as of CU Closure
Notes: Summarize the systems engineering approach for the project (e.g. guided by the systems engineering “V”, conducted trades (briefly describe key trades that led to your team’s design), derived and flowed down requirements from functional objectives, developed Interface Control Documents, assessed risk (used FMEA or other approach) and etc.).

## Slide 34: Systems Engineering: Right Side of V
Feasibility
Study/
Concept
Exploration
Concept of Operations
System Requirements
High-Level Design
Detailed Design
Software/ Hardware
Development
Field Installation
Unit Device Testing
Subsystem
Verification
System Verification & Deployment
System Validation
Operations and Maintenance
System Validation Plan
System Verification Plan
Subsystem
Verification Plan
Unit/Device Test Plan
System Engineering V
All in progress as of Spring 2020
  Individual unit tests largely complete
    Largest was balloon
    Mostly Avionics
    Still missing BEC
  Subsystems Verification
    In progress
    Avionics waiting on lynchpin of BEC
    Structures getting close
  System Verification
    Test flights were scheduled for April 6th
  System Validation
    Would have involved post processing of test data, ensuring that images were sufficient
Notes: Summarize the systems engineering approach for the project (e.g. guided by the systems engineering “V”, conducted trades (briefly describe key trades that led to your team’s design), derived and flowed down requirements from functional objectives, developed Interface Control Documents, assessed risk (used FMEA or other approach) and etc.).

## Slide 35: Systems Engineering: Risk Assessment vs Challenges
FMEA Score | Risk | Actual Impact
20 | Battery overheats or explodes | This did not occur, even with extensive charging and discharging tests and being left idle for 2+ weeks
10 | Balloon Ruptures or Explodes | Despite relatively rough handling (gritty concrete floor, air was forced out by body weight,etc) during inflation/deflation tests, no damage was detected. Material was more robust and easier to patch than expected
15 | Storage Space Insufficient | This was never an issue, due to the fact that the balloon was only stored full once, and that space was relatively easy to obtain
5 | Costs Exceed Budget | Did not occur, but risk was underpredicted. Likelihood was taken to be small because EEF was assumed guaranteed and purchasing did not begin until Spring
3 | Shipping Time Too Long | Underestimated consequence and likelihood in planning phase, pushed schedule several times. Augmented by global pandemic
Tabulated Planned Risk Cases:
(Selected for relevance) (premitigation)
Major Unforeseen Risks:
A global pandemic
  Issues with Balloon material (massive delay)
  Delayed BEC
Helium vs Hydrogen question
  Hundreds of man-hours used for this
Modified FMEA risk matrix used by NESSIE
 | Consequence |  |  |  | 
 | 11 | 16 | 20 | 23 | 25
 | 7 | 12 | 17 | 21 | 24
 | 4 | 8 | 13 | 18 | 22
 | 2 | 5 | 9 | 14 | 19
 | 1 | 3 | 6 | 10 | 15
Likelihood
Notes: Summarize the systems engineering approach for the project (e.g. guided by the systems engineering “V”, conducted trades (briefly describe key trades that led to your team’s design), derived and flowed down requirements from functional objectives, developed Interface Control Documents, assessed risk (used FMEA or other approach) and etc.).

## Slide 36: Systems Engineering: Interface Control
Roughly based on SysML
  Based on hierarchy by subsystem
  Graphically derived from FBD shown above
  Specific interfaces detailed in text document
See Avionics Example:
Avionics Subsystem Interfaces Graphical Representation
Avionics Subsystem Interfaces Description and Specs

## Slide 37: Systems Engineering: Key Takeaways and Lessons Learned
Change management is essential
  A tool was implemented for the design
  Would have been useful in other aspects (Git or similar)
    All code
    LaTeX documents
    Presentations
Communication is key
Utilize ICD software, the above method was cumbersome and prone to errors
Creating a systems engineering plan laid out before beginning work is important
Example Row of Change Management tool used by NESSIE

## Slide 38: Project Management: Approach
Successes
Ability of team to work under pressure and strict timelines
Interpersonal/team related work and support
Challenges
Adequately scoping project
Nothing goes according to plan
College level bureaucracy
Lessons Learned
Avoid scoping/descoping during initial requirements meeting with customer
  If possible, take requirements, discuss with team afterwards, schedule follow-up meeting shortly after
Know capabilities going into meeting with customer
  Helps with scoping project
Approach
Be transparent
Let the team make decisions
  Interject or add commentary when appropriate/necessary
Be a guide
  Introduce topics of discussion
  Spur the conversation
Be a contributor and not a ‘boss’
Get buy-in from group before proceeding with ideas

## Slide 39: Project Management: Budget Analysis
Notes: Discuss reasons for major changes from CDR budget to FFR actual

## Slide 40: Project Management: Budget Analysis
Component | Cost | Estimated Shipping | Cost + Shipping | Budget | Margin
Gas Envelope | $1375 | $250 | $1625 | $1804 | ~10%
Helium (1882 cuft) | $1215 | $0 | $1215 | $1500 | ~20%
Carbon Fiber | $424 | $200 | $624 | $650 | ~4.5%
Batteries/Charger | $362.64 | $20 | $382.64 | $400 | ~4%
Propulsion | $341.8 | $0 | $341.8 | $421 | ~15%
Flight Controller | $210 | $0 | $210 | $210 | 0%
Tail and Pins | $110.97 | $0 | $110.97 | $120 | ~9%
MISC. |  |  | $325.99 | $395 | ~17%
Totals |  |  | $4835.24 | $5500 | ~12%
CDR Budget
TRR Actual
Component | Final Cost | Budget | Margin
Gas Envelope | $1500.00 | $1804 | ~17%
Helium (1882 cuft) | $1215.00 | $1500 | ~19%
Carbon Fiber | $1396.21 | $650 | ~-115%
Batteries/Charger | $393.08 | $400 | ~2%
Propulsion | $566.18 | $421 | ~-34%
Flight Controller | $207.95 | $210 | 1%
Tail and Pins | $159.30 | $120 | ~-33%
MISC. | $342.49 | $395 | ~13%
Remaining Budget: | -$72.26 |  | ~-1%
Totals | $5572.26 | $5500 | ~12%
Notes: Discuss reasons for major changes from CDR budget to FFR actual

## Slide 41: Project Management: Industry Project Cost Analysis
 | Fall 2019 Semester | Spring 2020 Semester
Hours Worked | 3051 | 1981*
Hourly Cost | $95,353.75 | $61,906.25*
Materials Cost | $ 5,772.26 | 
Overhead Rate (200%) | $190,707.50 | $123,812.50
Total Industry Cost | $477,552.26 | 
* Average used for last 6 weeks due to Covid-19 impact

## Slide 42: Thank You!!
Questions?