## Slide 1: Testing Readiness Review
Justin Alvey Ryan Bennett Emma Cooper
Sean Ellingson Pierre Guillaud Nash Jekot
Jacob Killelea Micah Svenson Kendall Worden
Optical Thermal Regulation System
Customer: General Atomics Advisor: Dr. Kathryn Wingate

## Slide 2: Project Overview

## Slide 3: Baseline Design
Create Thermal Profile
Simulated Electronics System
Reference Data System
V&V of Thermal Camera Data
OTheRS System
IR Cameras
Thermal Ctrl
Stack With Removable Imaging Wall
6 Trays Form the Electronics Stack
Full TestBed (Bay + Stack)
Single Tray

## Slide 4: CONOPS
Notes: thermal cameras will be mounted to the ceiling and floor of the bay, and image a single side of the rectangular electronics stack. Data will also be simulataneously taken from an array of thermistors mounted on the opposite side of the stack face. You can also see the camera has its own thermal managment system.
After the cameras captures an image, it is processed by stitching the images together, correcting for skew and extracting temperature infromation.
This information is then sent through a controller, which will send regulatory commands to LED’s as representative indicators of control ouput.
Data will also be sent to through a serial output, which will then be validated by comparing against the previously mentioned thermistor array.

## Slide 5: Functional Block Diagram

## Slide 6: Critical Project Elements
Critical Project Elements | Explanation
Image Capture and Processing System | Image capture allows for the system to read the thermal behavior while the processing allows for functions like stitching and hotspot identification.
Test Bed Structure | Structure allows the system to see a representation of the customer’s satellite bay.
Thermal Control of Camera | Ensure the camera will survive in final thermal chamber testing at the low range (-30°C).
Full-Stack Regulation | Customer desired functionality and shows response of the image processing abilities.

## Slide 7: Critical Project Elements - Updates
Critical Project Elements | Concerns/Updates Since MSR
Image Capture and Processing System | Image Stitching has been resolved. Temperature accuracy is now the main concern.
Test Bed Structure | Camera mounting modified to reduce geometric skew
Thermal Control of Camera | PCB are being manufactured
Full-Stack Regulation | PCB are manufactured, troubleshooting/integration in progress

## Slide 8: Levels of Success
Criteria | Camera | Image Processing | Elec/Comm/Ctrl | Test Bed
Level 1 | Camera system will sense temperatures between -30°C and 60°C and will fit within the interior of the given satellite | Software can differentiate between module trays in the stack being monitored while recording their temperature. Software can also facilitate spacial and thermal calibration of the OTheRS system | The control system will command representative indicators based on thermal data from the image processing system and will handle 2.5A.The entire system will also be able to operate on 28V of unregulated power | The test bed will have two different heated objects, whose temperature is read by both the thermal camera and thermistors in an ambient air, room temperature environment. This is a minimum to help ensure the camera can differentiate and monitor multiple components
Level 2 | Camera system will survive below a temperature of-30°C |  |  | System operates successfully when tested in thermal chamber between -30°C and 60°C
Level 3 |  | Software can determine temperature of components inside of the Avionics Bay |  | A range of coatings will be tested to determine effect on temperature readings

## Slide 9: Project Schedule

## Slide 10: Image Processing and Manufacturing
Critical Path
CAD Models
Machining Stack and Bay
Assembly
PFR
MSR
TRR
SFR
*No Machining after March 22nd
Hardware Testing
Image Stitching
Map Pixels
Hot Spot Identification
Temperature & Reflection calibration
Module Integration
Margin:
5 days for Modules, longer for those in concurrent development
1 Day Margin for machining tasks with a cutoff at 3/22
1 Week Margin for assembly tasks

## Slide 11: Other Project Elements
Critical Path
PFR
MSR
TRR
SFR
Camera Thermal Regulation
Simulation Electronics
Reference Data System
Critical Tests

## Slide 12: Test Progress

## Slide 13: Requirements

## Slide 14: Requirement Matrix
Test Category | Associated Requirements | Testing Overview
Datasheet Inspection | IMAG 1, THER 2, COM 2, TEST 2, TEST 4 | Verify materials and components meet requirements
Dimension Verification | IMAG 3, TEST 1, TEST 1.1, TEST 1.1.1 | Measure manufactured parts and setup to check physical replication of the bay
IP Output Check | IMAG 2, IMAG 3.1, PROC 1, PROC 1.1, PROC 2, PROC 4, PROC 4.1 | Verify algorithms are functioning as written and with designed test setup
Control and Communication | PROC 3, CONT 1, CONT 2, COM 1, COM 1.1, COM 2* | Use test cases and directly observe responses for components
Pre Acceptance Instrumentation | POW 2, THER 1, TEST 3 | Final system check prior to acceptance testing in a thermal chamber

## Slide 15: Test Flowchart
Datasheet Inspection
IP Unit Testing
Software Automation & Integration
Software Performance
Reflection Calibration
Hardware Software Testing
Manufacture Parts
Test Controls (Test Cases)
Test Comms (Observe/Test Case)
Lepton Thermal Management Verif.
Test Bed Integration
Acceptance Testing
Assembly
IP Output Check
Control and Comm
Dimension Verif.
Pre-Acceptance Instrumentation
Long Wire Testing
Legend
Major Testing
Requirement Retirement

## Slide 16: Completed Testing

## Slide 17: Image Stitching
Requirements:
  FR 6: The thermal imaging device(s) shall image critical stack electronics on at least a single side of the stack.
Purpose:
  Capture one side of the stack in a single grid
  Software must facilitate spatial calibration of the OTheRS system
Experimental Variables:
  Camera positioning
  Emissivity sticker layouts
Concerns:
  Data for the near-corners of stack are missing
Risk Mitigated:
  Inability to softcode a geometric stitch or repurpose software
Left Image
Right Image
Stitched Image

## Slide 18: Model Validation

## Slide 19: Thermal Model Overview
Purpose
  Predict temperature profiles for scenarios that require thermal chamber testing
  Understand impact of heat transport modes on the system
Concerns:
  Complexity and time cost
  Loss of model fidelity to simplifications required to produce reasonable meshing
  Difficult to test in no-convection ambient
Experimental Variables:
  Temperature (component, ambient, bulk)
  Thermal resistance, emissivity, convection coefficients
Risk Mitigated:
  Source of information to verify camera data
  Visual representation of thermal changes expected to be seen during a test
Notes: MAKE SURE TO INCLUDE REQUIREMENTS AND RISK MITIGATED if necessary - *No requirements on this - Ryan*

## Slide 20: Assumptions to Testing
Model Assumption | Map to Test Setup
Negligible heat transfer across PCB | Error in this assumption measured by truth data taken across board surface
Ambient air temperature constant | To be measured at constant intervals through all ambient testing
Top tray will be hottest | Test will use a single tray from the final test setup
Reference data system accurate enough to quantify model error | Discrete measurement points can be compared between the model and test bed
Notes: negligable a key word.
2. Convection repeatability, assume at least 5% error (@65F, plus or minus 2.85)
SUPER DIFFICULT TO MODEL DUE TO CONVECTION IN THE ROOM, SO WE MIGHT AS WELL SAY IT DOESNT EXIST
3. Top tray will be the hottest due to convection in ambient, and thus the most susceptible to failing temperature boundary requirements
4
5. Reference data system will also provide the team with thermal contact resistance data!

## Slide 21: Thermal Model Setup
Equipment / Setup
  Single tray w/ 2 heaters, wiring, and 6 equally spaced thermistors
  Prototype test bed “box”
  Computer/Arduino/ADCs to collect thermistor data
Procedure:
  Construct single tray using low-resistance thermal epoxy and PCB for structural rigidity
  Measure and fix thermistors into place against tray wall with low-resistance thermal epoxy
    Quantify thermal resistance of epoxy application for model refinement
  Isolate the system and use thermistor data to ensure bulk thermal equilibrium
  Turn heaters on until steady state is reached

## Slide 22: Thermal Model Results
Quantitative temperature data at predetermined discrete points
  Provide transient temperature profile
    1x6 matrix as a function of time
    Expect to see impact of convection when ΔT sufficiently large
  Provide final steady state temperature profile
Technical experience required to construct and instrument full stack
Validity of model assumptions / boundary conditions

## Slide 23: Thermal Model Results (Steady State)
33 minutes to compute view factors and run
Heater location 50mm from each wall

## Slide 24: Planned Testing

## Slide 25: Long Wire Test Overview
Purpose:
  Customer concerned with signal integrity from cameras over long distances
  Long wires are needed connect cameras to processing hardware outside of thermal chamber
Experimental Variables:
  Wire length
Concerns:
  Need to ensure that wires are long enough to reach out of thermal chamber.
  Attenuation / Ringing / Propagation Delays affect signal integrity.
  Propagation delay can cause signals to become misaligned.
Risk Mitigated:
  Verify data is usable from the camera with longer wires
    Quantify how long wires can be before data unusable

## Slide 26: Long Wire Test Setup
Equipment / Setup
  Raspberry Pi, FLIR Lepton.
  Copper wire, wire cutters and strippers, pin sockets, maybe a soldering iron.
  High speed oscilloscope.
Procedure:
  Attach Lepton(s) over 3m of copper wire. Examine signal waveform, throughput, maximum achievable bus speed.
  Shorten wires (0.5 - 0.25m per test) until satisfactory throughput and bus speed achieved.
Results:
  Relationship between wire length and maximum clock speed.
  Qualitative examination of signal waveform.
  Quantitative understanding of SPI bus slave and propagation delays.

## Slide 27: Prediction of Propagation Delay Limit

## Slide 28: Software Performance Testing
Requirements:
  DR IMAG-2: Images of the stack shall be taken at no more than 90 second intervals.
  DR PROC-4.1: Automated image processing shall be completed between image captures as defined in DR-IMAG 2.
Purpose:
  Image processing must occur between image captures and in under 90 seconds
  Quantify how well we meet the requirements
Experimental Variables:
  Algorithm complexity for each image processing step
Concerns:
  Delays in processing could lead to a data backlog.
  Speed of data transmission over long wires could significantly impact necessary processing speed.
Risk Mitigated:
  Ensures that images can be processed and transmitted within the required time period.

## Slide 29: Software Performance Setup
Equipment/Setup:
  Raspberry Pi, FLIR Lepton(s), Laptop computer
  1 GB Ethernet-USB adapter
Procedure:
  Performance of the software will be tested through the Python timing library
  Unit tests of the software modules will be completed to develop a timing profile
Results:
  Quantitative timing analysis of the image processing software.
  Compare predicted run times to test results.
  Determine the most labor-intensive software modules and identify software bottlenecks
  Implement optimization strategies where necessary

## Slide 30: Reflection Error Overview
Requirements:
  DR-PROC 4: Temperature data shall be extracted from the thermal image
Purpose
  Calibrate temperature data from Lepton cameras
  Understand reflection impact on error
Concerns:
  Radiometry data is inaccurate due to reflection
  Correcting reflection error may require empirical characterization throughout the full temperature range.
  May require black body calibrator
Experimental Variables:
  TestBed temperature
  Reflectivity of surroundings
Risk Mitigated:
  Inaccurate temperatures measurements due to reflective environment

## Slide 31: Reflection Error Setup
Equipment
  Surface preparations
    Anti-Reflective preparations to all TestBed surfaces except imaged stack face
  Both initial and final testbed
Procedure:
  Capture images in non reflective environment
  Capture images in final environment
  Introduce correction factor to reduce effects of reflected radiation
Face to be imaged

## Slide 32: Coatings Performance Overview
Requirements:
  DR-PROC 4: Temperature data shall be extracted from the thermal image
Purpose:
  Quantify how well reflections are being mitigated on face under test
Experimental Variables:
  Surface Roughness
  Reflectivity (Absorptivity)
Concerns:
  Coatings may not have desirable or intended effects
  Budget may not support much continued testing
Risk Mitigated:
  Camera data accuracy can be improved
  Better information for picking coatings on final test bed

## Slide 33: Coatings Performance Setup
Equipment
  Surface preparations
    Initial test bed - Sticky notes, adhesives, colored paper, sand paper
Procedure:
  Power on OTheRS and begin taking data at nominal condition
    Nominal condition is heaters off at ambient temperature
  Turn heaters ON and take data
    Test until reference data system notes a 15°C change from nominal condition on bare surface

## Slide 34: Coatings Performance Results
Metrics to score coatings
  Is reflection mitigated (accuracy increased)?
    Temperature of thermal imaging device compared with bare Aluminum test camera data
  Is the thermal behavior captured by the thermal imaging device?
    Temperature of reference data system compared with thermal imaging device
  Are material properties changing?
    Temperature of reference data system compared with bare Aluminum test reference results
Data required
  Matrix of reference data system results over the course of the test
  Camera data during the course of the test
  Historical data from previous tests
    Score the data relative to base condition
    Score the data relative to other surface preparations

## Slide 35: Acceptance Testing

## Slide 36: Thermal Chamber Overview
Requirements:
  FR 1: OTheRS shall return a thermal data map for multiple components between -30°C and 60°C.
  FR 2: OTheRS shall provide regulatory commands when components are outside -20°C to 50°C.
Purpose:
  Test system functionality at required temperature range
Experimental Variables:
  Chamber Temperature
  Dwell Time
Concerns:
  Customer has not updated team on chamber status
    Wiring pass throughs
    Scheduling conflicts

## Slide 37: Thermal Chamber Setup
Equipment / Setup
  Final test bed
  Customer’s thermal chamber
Procedure
  Hot Test
    Dry gas purge the chamber
    Power on OTheRS system
      Plan to run at 0.5A with 25 Ohm resistors (6.25W)
    Set thermal chamber to 50°C
      Check system output for commands
      Check thermal response on reference data system
    Set chamber to 60°C
      Observe command response over thermal change
      Verify system is functional at 60C
  Cold Test
    Similar test but has following differences
      Initial chamber set at -20°C
      Final chamber set at -30°C
Notes: Looks good to me ryan - sean

## Slide 38: Thermal Chamber Results
Primary Metric
  Temperature of reference data system compared with thermal imaging device
    Look at both mean and max changes as a function of time
Required Data
  Reference Data System
    Grid (matrix) of thermistors measurements over the duration of the test
  Image Processing
    Matrix of thermal data for the entire face under test
Expected Results
  Expect error between reference data and Lepton
  Both should follow these trends with varying accuracy:
    Horizontal trend when heaters are not powered
    As heaters are powered, expect a minimal linear trend
    Linear trend expected as the chamber temperature changes

## Slide 39: Required Testing Facilities

## Slide 40: Facility Matrix
Test Plan Section | Test Plan Name | Required Facilities
Model Validation | Thermal Model | Top tray (Final Test bed) Initial Test bed Outer Bay Structure
Planned Testing | Long Wire | High speed oscilloscope (≥ 150 MHz) Soldering iron or wire stripper
 | Software Performance | Raspberry Pi with IP modules loaded
 | Reflection Error | Initial Testbed, Final Testbed, anti-reflective paper, Thermal Chamber
 | Coatings Performance | Initial testbed (Preliminary Tests) Final testbed (Continued Tests)
Acceptance Testing | Thermal Chamber | Final Test bed Customer’s Thermal Chamber

## Slide 41: Safety

## Slide 42: Safety
Monitor the temperature via the reference data periodically
Only run two of the 96 power resistors at a time.
Have an LED that indicates when the stack walls are over 38°C, and therefore, should not be touched
Temperature and Burn:
2. Grounding the testbed
Solderless crimp Terminal
The Test bed will be grounded through the utilization of solderless crimp terminals.
These will connect to the aluminum surface and then to a grounding terminal.
Heater PCB

## Slide 43: Budget

## Slide 44: Cost Breakdown as of TRR
IP Cost | $713.01
Ref Data Cost | $167.54
Sim Elec Cost | $228.00
Elec Cost | $447.91
Structural | $2,252.00
Remaining | $1,191.54

## Slide 45: Future Cost Planning
Future Costs
  Thermal Paste
Lepton Margin
  $571.13 To cover replacing both Leptons in case of failure
Coatings
  Remaining budget after future costs ($503.41) will be used for research coatings

## Slide 46: Questions?

## Slide 47: BackUp Slide Deck

## Slide 48: Mechanical Structure

## Slide 49: TestBed - Tray

## Slide 50: TestBed - Tray

## Slide 51: TestBed - Tray

## Slide 52: TestBed - Tray

## Slide 53: TestBed - Stack

## Slide 54: TestBed - Stack

## Slide 55: TestBed - Outer Bay

## Slide 56: TestBed

## Slide 57: TestBed - Entire Configuration

## Slide 58: TestBed - Entire Configuration

## Slide 59: Design of Testbed

## Slide 60: Tolerances
± 0.01 inch = 0.254 mm
16.538° ± 3° (vertical angle, camera mount)
52° ± 7° (horizontal angle, camera mount)
Most important components to minimize tolerance:
Stack walls - want to keep heat isolated to inside the stack
Bay walls - want to keep system isolated, don’t want outside light entering testbed
Camera mount - want to be able to image entire side of stack

## Slide 61: Thermal Model

## Slide 62: Thermal Model
Wiring and Realistic Heater Performance

## Slide 63: Thermal Model - Steady State
Assumptions Made:
Convection coefficient constant @ 10 W/(m2 K)
εAl = .1 (assuming unoxidized Al 6061-T6)
εHeater = .92 (ceramic porcelain)
PCB and tray holes can be neglected for meshing simplification
Important Values
55,609 nodes (using node to surface contact, Jacobian 4-point)
Ambient temperature set to 65F (291K)
Global mesh size 12mm with .6mm tolerance

## Slide 64: Thermal Model Assumptions
No conduction across PCB
  Increases model complexity for heat paths
  Impact can be quantified using temperature measurements across board
Air temperature is constant at the building’s set temperature(18C/65F)
  Will give repeatability for convection
  Must be measured at time of test (Account for 5% error on this assumption)
    Likely through nominal (initial) period in the test
Top tray is being verified in test
  Primary heat transport is via convection
    Allows for more heat transport to and away from surfaces
    Significantly increases model complexity compared to space environment
  Test can be performed in ambient environment
Reference data system can be used to quantify error
  Discrete measurement points can be compared between the model and test bed
Notes: Edits have been made

## Slide 65: Thermal Model Overview
Purpose
  Predict temperature profiles for scenarios that require thermal chamber testing
  Understand impact of heat transport modes on the system
Concerns:
  Complexity and time cost
  Loss of model fidelity to simplifications required to produce reasonable meshing
Experimental Variables:
  Temperature (component, ambient, bulk)
  Thermal resistance, emissivity, convection coefficients
Risk Mitigated:
  Source of information to verify camera data
  Visual representation of thermal changes expected to be seen during a test
Notes: MAKE SURE TO INCLUDE REQUIREMENTS AND RISK MITIGATED if necessary - *No requirements on this - Ryan*

## Slide 66: Thermal Model Validation
Isolate tray from ambient environment and heat sources
  Preliminary test bed used to insulate/remove sources
    Can modify model parameters to remove convection/radiation to ambient environment
Heat using same power and resistors as the model for the same time period
Measure test using reference data system
  Thermistors in final test bed
Quantify error in model as a function of time and temperature
  Can look at entire time length of test or as a function of the temperature during the test
    Does it change with internal heat or time during test?
Quantify error of initial assumption of constant temperature
Quantify error of initial assumption of constant convection coefficient

## Slide 67: Thermal Model Setup
Equipment / Setup
  Computer w/ SolidWorks Simulation Package
Procedure:
  Simplify model by removing screw holes, wire pass throughs, square internal corner cuts
  Make assumptions and determine boundary conditions
  Specify component material and base properties
  Set up thermal paths
    Power resistor to stack/air
    Stack to stack/air/bay
    Bay to bay/stack/air/ambient
  Define steady state or transient simulation condition
  Define mesh parameters, including mesh tolerance and FEM matrix size
Results:
  Visual and quantitative temperature data
    To be compared with thermistor data at known surface points

## Slide 68: Thermal Model Setup
As is:
  Steady state
  Single tray and bay wall @ tray height
  Unoxidized Al 6061-T6, ceramic porcelain, and PCB substrate
    εAl = .1, εHeater = .92, εPCB = 0
    U = 10 W/(m2 K)
  Global mesh size 12mm with .6mm tolerance
  55,609 nodes (using node to surface contact, Jacobian 4-point)
  Ambient and bulk temperature set to 65F/18C (291K)
  Heaters set to 6.25W heat power each
  PCB conduction, convection, radiation ignored
    PCB mounting tabs also ignored
In Progress:
  Transient single tray
  Steady state full stack w/ bay
To Do:
  Transient full stack w/ bay

## Slide 69: Full Stack Regulation System

## Slide 70: Integration Plan

## Slide 71: Full Stack Regulation System Schematic

## Slide 72: Propagation Delay Limitations: 2-20 MHz
Notes: Akin’s 6th law of spacecraft design (Mar’s Law): Everything is linear if plotted log-log with a fat magic marker

## Slide 73: Reference Data System

## Slide 74: Integration Plan

## Slide 75: Budget

## Slide 76
Purchases Made Up Until MSR |  |  |  |  | Purchases Made Up Until MSR |  |  |  | 
Sub-System | Part | Unit Price | Qty | Total | Sub-System | Part | Unit Price | Qty | Total
IP/Camera | FLIR Lepton 3.5 | $301.01 | 2 | $610.02 | Ref Data | Sparkfun RedBoard | $19.95 | 1 | $24.95
IP/Camera | Lepton 3.5 Breakout | $0.00 | 2 | $0.00 | Ref Data | Resistors - CRGCQ0402F18K | $0.10 | 80 | $8.00
IP/Camera | High Emmisivity Stickers | $53.00 | 1 | $62.99 | Ref Data | Custom PCB | $10.00 | 3 | $30.00
IP/Camera | Raspberry Pi 3b | $40.00 | 1 | $40.00 | Sim Elec | Custom PCB | $8.00 | 10 | $85.00
Structural | Aluminum 6061-T6 Plates .04"x2'x4' in (Bay) | $59.90 | 10 | $639.00 | Sim Elec | Power Resistor - 71-RS01025R00FE73 | $1.19 | 100 | $119.00
Structural | Toggle Clamps | $19.99 | 4 | $87.96 | Sim Elec | Power Driver Board | $8.00 | 3 | $24.00
Structural | Aluminum 6061-T6 Plates (1/16") - 25.5"x24" | $69.50 | 3 | $248.50 | Sim Elec | D-Type Connectors | $0.00 | 0 | $0.00
Structural | Aluminum 6061-T6 Plates (1/16")13.5"x25" | $69.50 | 3 | $208.50 | Electronics | Buck Converter | $6.99 | 2 | $13.98
Structural | Aluminum 6061-T6 Plates (1/16") 24"x13.5" | $49.50 | 3 | $148.50 | Electronics | Wiring - 12 Gauge | $15.95 | 2 | $36.90
Structural | Foam Insulation | $32.60 | 1 | $32.60 | Electronics | D-type Connector | $1.57 | 0 | $0.00
Structural | AL 6061 Plate | $59.90 | 2 | $119.80 | Electronics | AC Adapter | $19.99 | 1 | $19.99
Structural | AL 6061 Sheet Metal | $101.75 | 3 | $305.25 | Electronics | USB for Arduino | $34.99 | 1 | $34.99
Structural | M2 Tap Starting | $16.53 | 2 | $33.06 | Electronics | MOSFET 60V | $0.71 | 10 | $15.05
Structural | M2 Tap Closed | $16.53 | 2 | $33.06 | Electronics | IC LED DRIVER | $2.33 | 3 | $6.99
Structural | 18-8 Stainless Steel Slotted Flat Head Screws | $7.79 | 1 | $7.79 | Electronics | MOSFET 55V | $1.08 | 3 | $3.24
Structural | Paper Tape | $9.89 | 1 | $9.89 | Electronics | CAP ALUM 47UF 20% 63V RADIAL | $0.33 | 4 | $1.32
Structural | Threaded Rod 40x6 H44815E | $1.08 | 10 | $10.80 | Electronics | TE Connectivity Amp Connectors | $1.04 | 3 | $3.12
Structural | Nut Hex H140009E | $0.08 | 20 | $1.62 | Electronics | CONN HEADER R/A | $3.70 | 6 | $22.20
Structural | MS Metric Phil Pan M2X12 H4307E | $0.30 | 32 | $9.50 | Electronics | 25W Chassis Resistors | $3.08 | 2 | $6.16
Structural | MS Metric Phil Pan M2X8 H4306E | $0.24 | 19 | $4.62 | Electronics | Thermocouple BreakOuts | $12.76 | 2 | $25.52
Ref Data | Thermistors - Vishay NTCLE413 | $1.39 | 45 | $70.55 | Electronics | Power Resistor Kit | $4.76 | 1 | $4.76
Ref Data | Screw Terminals | $0.80 | 10 | $10.00 | Electronics | MOSFET Transistors | $2.03 | 10 | $20.30
Ref Data | ADC - ADC128D818 | $4.68 | 3 | $19.04 | Electronics | Arduino Uno | $23.38 | 1 | $23.38

## Slide 77: Test Backup Testing Backup

## Slide 78: Planned Testing

## Slide 79: Adhesive Testing
Purpose:
  Find amount of adhesive used to fix thermistors to stack surface
Procedure:
  Fix thermistors to sheet of aluminum using variable amount of adhesive
  Heat plate to constant temperature
    Use no adhesive as baseline
  Find thickness cutoff that gives values within 5% of actual value
Facilities Needed:
  Constant heat source
    Ovens or hot plates can be used
Concerns:
  Thermal paste could corrupt temperature measurements
Risk Mitigated:
  Know thermistor readings are within 5% of accurate

## Slide 80: Planned Testing - IP

## Slide 81: Software Test - Identify Thermal Hotspots
Purpose:
  Test that the software can recognize thermal hotspots within the thermal image
  Identify thermal hotspots to make LED control decisions
  Temperature data shall be extracted from the image
Procedure:
  Load thermal images to the software
  Break apart the data in smaller chunks, find local temp max and mins
  Select data that is representative of the stack face
  Export resulting decisions over RS232 serial communication
Concerns:
  The software not being able detect thermal hotspots is a major concern
Risk Mitigated:
  The OTheRS system must be thermally regulated!

## Slide 82: Automated Software Testing
Purpose:
  Test completed software module timing requirements on the RasPi
  Image processing will be completed between image captures
Procedure:
  Load completed software modules to the Raspi
  Determine the timing requirement of the cohesive software
Facilities Needed:
  Initial Test Bed
  2 operational Lepton Cameras
  1 raspberry pi + software
Concerns:
  The software not being able to successfully complete within 90 sec
Risk Mitigated:
  Software that takes too long will fail requirements

## Slide 83: Unit Testing
Purpose:
  Test software modules on the Raspberry Pi
  Image stitching (multiple images) to find a (quality) representative image of the stack
  Verify that the
Problem:
  Corners of the stack are not seeable on the near camera
Procedure:
  To create a seperate profile for the corners from the far camera
Facilities Needed:
  2 FLIR Lepton 3.5
  Test bed
  Raspberry pi
Concerns:
  Horizontal skew causes bad data because corners are only seen from the far camera
Risk Mitigated:
  OTheRS system needs to capture a representative image of the stack

## Slide 84: Reflection Error Results
Heat testing:
  Resulting radiometry images and resulting temp data
Local Minimum: 20.9 C
Local Maximum: 50.9 C
Significant reflection still compromises temperature data
The error in degrees due to reflection has yet to be determined

## Slide 85: Acceptance Testing

## Slide 86: Thermal Chamber Testing
Talk through thermal chamber testing at GA
Big concern:
  We don’t have specific information on the customer’s chamber
    data/power run throughs (system integration with chamber)
    availability
      We were told we can use this whenever but have not heard a response from the customer
Allows for system to test most important customer given requirements
2 seperate plans (one high, one low)
  High test (60 C)
    Set chamber at 45C, run heaters until 60C is measured on the reference data system
      Between 50 and 60C, the regulatory commands should be sent
  Low test (-30 C)
    Set chamber to -35C, run heaters until at least -20C is measured on the reference data system
      Between -30 and -20C, the regulatory commands should be sent
Running at 0.5A with 25 Ohm resistors
  Will get time for 15C change from initial testing on test bed with thermocouples

## Slide 87: Thermal Chamber

## Slide 88: Coatings

## Slide 89: Preliminary Coatings Testing
4 types of coating families selected for testing on prototype test bed
  Bare Aluminum
    Baseline case
  Sticky Notes
    Replicate Customer case
  Tape
    Increase conduction from sticky note test
  Sanded Face
    Find dependency on surface roughness
Metrics established to score coatings
  Are material properties changing?
    Temperature of reference data system compared with bare Aluminum test
  Is accuracy increased or reflection mitigated?
    Temperature of thermal imaging device compared with bare Aluminum test
  Is the thermal behavior captured by the thermal imaging device
    Temperature of reference data system compared with thermal imaging device

## Slide 90: Continued Coatings Testing
Testing on the final testbed will have dependencies on findings from preliminary testing
Testing will be completed on the final test bed design
Coatings to be tested
  Slide in sheet of Aluminum 6061
    Quantify effect of thermal contact resistance
  Material variation
    Vary material attached to face being imaged
  Surface coatings
    Time and budget constraints
    Intention to test coatings with similar space grade variants
      Aids the customer for their application