## Slide 1: SpaceNet Critical Design Review
Fall 2020
+
Notes: Jordan
Presenting:
Colin R. (TDOA and TLE)
Tyler P. (SDR and network environment)
Benji (antennas)
~Ryan P. (everything GPS PPS)
Forest (electronics and software)
Jordan (finance LASP)
Sam (TDoA and TLE)
Ryan B. (CAD)

## Slide 2
Plot from the ESA space debris portal https://sdup.esoc.esa.int/discosweb/statistics/
Planned LEO/GEO Missions
Objects
Year
Increasing number of objects in Low Earth Orbit (LEO)
CubeSats
Commercial Constellations (Starlink, OneWeb)
Debris
High fidelity phased-array sensors are limited
Expensive
Limited field of view
Can only focus on a single object at a given time
Time consuming to build and operate
Notes: Jordan

## Slide 3
What is SpaceNet?
A Low-Cost network of Software Defined Radio(SDR) equipt ground stations for monitoring LEO space domain
This type of network could be used to monitor LEO space domain relieving high fidelity sensors
The system would produce two-line element sets(TLE) that could be compared to expected orbits to determine if something is out of place
Notes: Jordan

## Slide 4
This Project
4 unit proof of concept for this type of low-cost, low-fidelity ground station network
This project will produce 4 functional ground units that can record UHF/L-Band satellite Quadrature signal (IQ) data from 2 target satellites
The recorded data will be used to produce both a position estimation and orbit estimate
Notes: Jordan

## Slide 5
SpaceNet
Concept of Operations (CONOPS)
7. Time delay is used to estimate satellite position
8. Position used to estimate orbit
1. Sensors are temporarily deployed
2. Sensors synchronize to UTC time
4. Transmissions are received by sensors
3. Satellite transmits during flyby
6. Time delay of signal arrival is calculated from UTC time
Sensor A Data
Sensor B Data
GO CU!
GO CU!
5. Transmissions are identified post test
Notes: Jordan

## Slide 6: Conceptual Block Diagram
Notes: Make sure that we explain the particle filter and Gibbs are two different method (Tyler)

## Slide 7: Conceptual Block Diagram
Notes: Tyler

## Slide 8: Conceptual Block Diagram
Notes: Tyler

## Slide 9
Sensor Unit Design
Dual Band
Wall Powered
20 Million samples per second
100ns UTC time synchronization
32Gb storage
~6 passes of data
$1000 per unit
3.8’
9.11lbs
Notes: Ryan B

## Slide 10
RF Front end
Dual Band Antennas
400-470 MHz, 1.6 GHz
2-Way RF Switch
Computer Controlled switch to swap between bands
Dual Low noise amplifiers
One for each band
HackRF SDR
SDR for IQ reception
Notes: Ryan B

## Slide 11
Structure
PVC Antenna Mount
NEMA 4 Rated Enclosure
Ensures dry environment
Clear Lid
Allows GPS reception
NEMA 4 cord grips
Allows RF and power delivery while maintaining water resistance
Notes: Ryan B

## Slide 12
Electronics
and Data Handling
NEO 6m GPS chip
Provides synchronization to UTC
Power Strip
Converts 120V AC to the required source voltages
5V Power Bus
Provides 5V power to LNAs, RF switch and gps chip
Raspberry Pi 4
Handles Data storage and SDR control
Notes: Ryan B

## Slide 13: Conceptual Block Diagram
Notes: Tyler

## Slide 14: Software Flowdown
Notes: We are using two methods to predict an orbit because TDoA and gibbs method in tern loose accuracy if the flyby is not directly overhead. The particle filter can cope with this but it's something we are unfamiliar with and can computationally taxing. For the project we don't need both to verify fullment of the requirements but we may need both to produce an acceptable orbital requirement.

## Slide 15
Particle Filter
Simulates orbit states and calculates likelihood based on noisy measurements.
TDoA
Produces positional estimates based on time delay of signal arrival.
Time Delay
Gibbs Method
Uses three position vectors to estimate a velocity vector.
Notes: We are using two methods to predict an orbit because TDoA and gibbs method in tern loose accuracy if the flyby is not directly overhead. The particle filter can cope with this but it's something we are unfamiliar with and can computationally taxing. For the project we don't need both to verify fullment of the requirements but we may need both to produce an acceptable orbital requirement.

## Slide 16
SpaceNet Block Diagram

## Slide 17: Conceptual Block Diagram

## Slide 18
Critical Project Element | Why is This Critical?
Environmental Readiness | Testing time will be dictated by satellite’s orbital passes. The sensor unit must be ready to operate in rain, snow and the temperatures expected during spring semester in Boulder

## Slide 19
Critical Project Element | Why is This Critical?
Environmental Readiness | Testing time will be dictated by satellite’s orbital passes. The sensor unit must be ready to operate in rain, snow and the temperatures expected during spring semester in Boulder
RF Front End | The RF front enables UHF and L-band signal reception. The reception must be good enough to discern the transmission from the noise floor

## Slide 20
Critical Project Element | Why is This Critical?
Environmental Readiness | Testing time will be dictated by satellite’s orbital passes. The sensor unit must be ready to operate in rain, snow and the temperatures expected during spring semester in Boulder
RF Front End | The RF front enables UHF and L-band signal reception. The reception must be good enough to discern the transmission from the noise floor
Timing Synchronization | The received data must be alignable such that time delay can be measured with extreme precision. Error here has a large impact on positional predictions

## Slide 21
Critical Project Element | Why is This Critical?
Environmental Readiness | Testing time will be dictated by satellite’s orbital passes. The sensor unit must be ready to operate in rain, snow and the temperatures expected during spring semester in Boulder
RF Front End | The RF front enables UHF and L-band signal reception. The reception must be good enough to discern the transmission from the noise floor
Timing Synchronization | The received data must be alignable such that time delay can be measured with extreme precision. Error here has a large impact on positional predictions
Position Vector Estimate using TDoA | Time Delay of Arrival(TDoA) ranging is used to produce the positional information required for orbital prediction

## Slide 22
Critical Project Element | Why is This Critical?
Environmental Readiness | Testing time will be dictated by satellite’s orbital passes. The sensor unit must be ready to operate in rain, snow and the temperatures expected during spring semester in Boulder
RF Front End | The RF front enables UHF and L-band signal reception. The reception must be good enough to discern the transmission from the noise floor
Timing Synchronization | The received data must be alignable such that time delay can be measured with extreme precision. Error here has a large impact on positional predictions
Position Vector Estimate using TDoA | Time Delay of Arrival(TDoA) ranging is used to produce the positional information required for orbital prediction
Orbital determination | Two methods: Gibbs and Particle Filter. Both produce orbital predictions that are the final product of the project

## Slide 23
Critical Project Element | Key Requirements
Environmental Readiness | Sensor unit shall keep dry environment in operational position given rain or snow Sensor unit shall keep internal temperature above 0°C Sensor unit shall be within a 5x5x5’ space
RF Front End | RF front end shall meet system noise temperature(G/T) requirements RF front end shall meet Link margin requirements Antennas shall have minimum azimuth beam width of 30°
Timing Synchronization | The on Board Computer shall be able to handle expected data rates The SDR shall be able to capture >2.4M samples per second The data shall be alignable to within 420ns time
Position Vector Estimate using TDoA | TDoA shall predict orbital position within 100 km of the true position. Sensors shall be placed far enough to produce accurate measurements
Orbital Determination | TLE will be calculated from satellite passover capable of predicting a future passover within 1 day. Expected time of day to within ±45 min, azimuth start angle to within ±30 deg, max elevation angle to within ±15 deg.
Notes: Key requirements are what are needed to ensure design meets functionality, the zero degrees is driven by the raspberry pi not the gps or the hackrf

## Slide 24: Environmental Readiness Testing time will be dictated by satellite’s orbital passes. The sensor unit must be ready to operate in rain, snow and the temperatures expected during spring semester in Boulder
Notes: Ryan B

## Slide 25
Key Driving Requirements
DR2.2.
The deployed sensor unit and antenna shall fit within a 5x5x5’ space
5x5x5’
DR1.2.
The sensor unit packaging shall be capable of maintaining an internal operating temperature range of 0-50 degrees Celsius
0° C
50° C
❆
<
<
DR1.1.
The sensor unit packaging shall be able to maintain a dry environment in rain and snow
Notes: Ryan B

## Slide 26: NEMA-4 Enclosure
Thermal:
Notes: Ryan B
T2 = Maximum(HOT) operating temperature and Minimum(COLD) operating temperature

## Slide 27
3.8’
9.11lbs
Sensor unit is within the required 5x5x5’ space
Notes: Ryan B

## Slide 28: RF Front End The RF front enables UHF and L-band signal reception. The reception must be good enough to discern the transmission from the noise floor
Notes: Benji
Next, we will be looking into Spacenet’s RF Front end Design requirements and the subsystem’s satisfaction met by our team’s analysis

## Slide 29
Key Driving Requirements
DR4.1.
Antenna(s) will have have 360° azimuth field of view
Linx Technologies
DR4.2.
Antenna(s) will have have minimum beamwidth of 30°
>30°
Notes: Benji
As seen here, there are two driving design requirements that categorize the antenna’s main parameters. Design requirement 4.1 states that the selected antennas will have a 360 degree azimuth field of view to allow for maximum signal reception, while design requirement 4.2 requires a beamwidth greater than 30 degrees, as to have better field of reception horizon to horizon.

## Slide 30: Antenna Specifications Selected antennas provide the required beamwidths and frequency ranges
L-Band
Azimuth FOV: 360°
Beamwidth: 65°
L-Band response: 1.2 GHz
Gain: 8 dBi
UHF
Azimuth FOV: 360°
Beamwidth: 48°
UHF Response: 400-490 MHz
Gain: 9 dBi
Notes: Benji
As seen from the antennas selected for both the L-Band and UHF Band signals, the design requirements of both a 360 degree Azimuth Field of View and a Beamwidth above 30 degrees is met by both antennas, with the UHF antenna having a beamwidth of 48 degrees, and the L-Band antenna having a beamwidth of 65 degrees.
UHF 400-470 $38.90 prime
https://www.amazon.com/dp/B0823WNV96/ref=sspa_dk_hqp_detail_aax_0?psc=1&spLa=ZW5jcnlwdGVkUXVhbGlmaWVyPUFWMEJaMjFRMVkxRkomZW5jcnlwdGVkSWQ9QTA1OTQ2NjlJOE9QSzhVVVdNVEwmZW5jcnlwdGVkQWRJZD1BMDU2NzAwNTFVQ05MSU5WNVNGWjYmd2lkZ2V0TmFtZT1zcF9ocXBfc2hhcmVkJmFjdGlvbj1jbGlja1JlZGlyZWN0JmRvTm90TG9nQ2xpY2s9dHJ1ZQ==

## Slide 31
Key Driving Requirements
DR3.1.
Each sensor unit shall have a minimum UHF system noise temperature of -20dB/K with a target value of -15 dB/K
DR3.2.
Each sensor unit shall have a minimum L-band system noise temperature of -17dB/K with a target value of -13 dB/K
Overall UHF noise temperature
> -20 dB/k
Overall L-band noise
temperature
> -17 dB/k
(G/T) = Gaina - Losses - 10log( ∑ Tx )
Gaina
Tline 1
Tline 2
Tline 3
Tswitch
Tlna
Lline 1
Lline 2
Lline 3
Lswitch
Llna
Notes: Benji
In addition to the field of view design requirements, the design requirements for gain-over-noise are important, as is it figure of merit in the characterization of antenna performance, where G is the antenna gain in decibels at the receive frequency, and T is the equivalent noise temperature of the receiving system in kelvins. Per the requirements given by our customer, the minimum and target bounds for the gain-over-noise ratio utilizing the UHF band was -20 db/K to -15 dB/K, and our selected antenna was calculated to have a ratio of -17.15 dB/K. The minimum and target bounds for the gain-over-noise ratio utilizing the L band was -17 db/K to -13 dB/K per the customer’s design requirements, and our selected L-Band antenna was calculated to have a ratio of -15.62 dB/K.

## Slide 32: System Noise Temperature Results
UHF
Satellite Target: CSIM
Frequency: 437.25 MHz
Data Rate: 9.6kbps
Based on UHF hardware:
Gaina = 9 dBi
Losses = 1.76 dB
Ts = 275 °K
Calculated G/T = -17.15 dB/K
L-Band
Satellite Target: Iridium NEXT
Frequency: 1616 MHz
Data Rate: 64kbps
Based on L-band hardware:
Gaina = 8 dBi
Losses = 1.76 dB
Ts = 243 °K
Calculated G/T = -15.62 dB/K
> -20 dB/k
> -17 dB/k
Notes: Benji
In addition to the field of view design requirements, the design requirements for gain-over-noise are important, as is it figure of merit in the characterization of antenna performance, where G is the antenna gain in decibels at the receive frequency, and T is the equivalent noise temperature of the receiving system in kelvins. Per the requirements given by our customer, the minimum and target bounds for the gain-over-noise ratio utilizing the UHF band was -20 db/K to -15 dB/K, and our selected antenna was calculated to have a ratio of -17.15 dB/K. The minimum and target bounds for the gain-over-noise ratio utilizing the L band was -17 db/K to -13 dB/K per the customer’s design requirements, and our selected L-Band antenna was calculated to have a ratio of -15.62 dB/K.

## Slide 33
Key Driving Requirements
DR3.3./3.4.
Each sensor unit shall have a minimum UHF & L-Band link margin of 3dB
Satellite
TX Power
Sensor
RX Power
Required Power
Path loss
Line loss
Line loss
Signal Power Over Transmission
> 3dB
Transmission Path
Signal Power
Notes: Benji
In addition to the gain-over-noise ratio design requirements, our customer stated that our link margins for both the L-band and UHF antennas needed to be above 3dB.

## Slide 34
UHF
Satellite Target: CSIM
Frequency: 437.25 MHz
Data Rate: 9.6kbps
Calculated Link Margin = 20.5 dB
L-Band
Satellite Target: Iridium NEXT
Frequency: 1616 MHz
Data Rate: 64kbps
Calculated Link Margin = 9.2 dB
Link margins for both UHF and L-band are > 3 dB
based on our hardware selection, satellite characteristics, and expected atmospheric losses
Link Margin Results
Notes: Benji
Through link margin analysis using the energy per bit to noise power spectral density ratio, it was found that both antennas satisfy the link margin design requirements, with the UHF antenna recieving satellite CSIM’s RF signal with a link margin of 19.9 dB, and the L-Band antenna recieving the satellite Iridium NEXT’s RF signal with a link margin of 11.2 dB

## Slide 35: Timing Synchronization The received data must be alignable such that time delay can be measured with extreme precision. Error here has a large impact on positional predictions
Notes: Forest:
In terms of time synchronization we want to make sure the there is extreme precision between the sensor units timing and to have as little time delay as possible. Overall any time error will have large impact on the position that we predict for the satellite

## Slide 36
Key Driving Requirements
DR5.1.
The data shall be alignable to within 420ns time
Local Clock A
Local Clock B
< 420ns error
DR5.2.
The system shall be able to capture >2.4M samples per second
>2.4M samples per second
Time
Voltage
Voltage
Notes: We have 2 main driving requirements to ensure that we have proper time synchronization:
-The first is that the data between the sensor units can be aligned within 420 ns of error
- The second is that we can capture 2.4 million samples per second or more.

## Slide 37
GPS produces timing pulses every second (PPS)
PPSs are universally synchronized with nanosecond precision
Notes: We will be accomplishing this by using a GPS Chip that produces a PPS signal in order to synchronize timing to nanosecond precision. As you can see from the image, the PPS signal is 1 second long and occur at the same time on each gps unit .

## Slide 38
PPS is filtered to remove DC component
Notes: We will filter the PPS to remove the DC component of the signal. This will limit the amount of time the signal is high for. this is is important because this limits the amount of data were going to change and modify.

## Slide 39
HPF-PPS is superimposed onto analog data between tuner and demodulator on the SDR
Notes: Here we can see signal is superimposed into the SDRs analog stream with the GPS. Filtering the data prevents the signal from being held high longer, this will save more data that would be affected and potentially lost.

## Slide 40
Provides a recognizable, synchronized RF signature that can be used for data alignment
Frequency Spectrogram
PPS Enabled
PPS Disabled
Time
dB
Notes: The filtered signal provides a recognizable and universally synchronized Rf signature between all 4 Sensor units that can be used to align the data in post. In the bottom part of the picture here we can see the raw data with the PPS disabled, the top part is with the PPS enabled, this can visally be seen with the this blue lines running horizontally, with each line representing one second intervals.

## Slide 41
HackRF can record
20M samples per second
PPS can be aligned with
2 sample precision
~100ns alignment precision
Notes: The chosen SDR the hackRF samples at 20 million samples per second which meets our requirement of at least 2.4 million samples per second. . From tests, we can see that the RF signature from the PPS can be aligned with 2 sample precision. These two factors give us a 100 ns time synchronization which is well below our requirement of 420 ns.

## Slide 42: Position Vector Estimate using TDoA Time Delay of Arrival(TDoA) ranging is used to produce the positional information required for orbital prediction
Notes: Colin

## Slide 43
where:
pi is the pseudorange: pi = cΔt1,i
r is the unknown position of the satellite
𝜏 is the unknown time for the signal to reach the first sensor from the satellite
rs,i is the known position of the i’th sensor
Δt1,iis the time differential of arrival from sensor 1
Key Driving Requirements
DR5.3.
Sensors shall be placed at least 100 km distance apart
> 100 km
DR5.3 comes from an analysis done for PDR that found that the sensor units must be at least 100 km apart in order for the timing accuracy required to be feasible. The final locations of the units were decided upon based on this requirement and accessibility.
TDoA
Needs 4 sensor units seeing the same RF signal
(4 unknowns {x, y, z, t} → need 4 equations)
p1 + c𝜏 = || rs,1 - r ||
p2 + c𝜏 = || rs,2 - r ||
p3 + c𝜏 = || rs,3 - r ||
p4 + c𝜏 = || rs,4 - r ||
Notes: Colin

## Slide 44: FR5. Recorded data can be used to produce an orbital position within 100km absolute error of a known satellite
Primary source of TDoA error is how accurately we can time stamp incoming signals for later post processing
GPS provides time synchronizing pulse per second (pps) signal
SDR needs to be capable of stamping pps timing signals onto input data and achieving a data rate of 20MHz (50ns)
  500ns timestamp accuracy provides us a large timing margin
Error greater than 100km: 0.54%
Error greater than 100km: 0.38%
Error greater than 100km: 9.58%
Notes: Colin

## Slide 45: Orbital Determination Two methods: Gibbs and Particle Filter. Both produce orbital predictions that are the final product of the project
Notes: Colin

## Slide 46: FR6. A TLE will be calculated from a satellite passover. TLE will predict a future passover occurring within a day of TLE calculation. This prediction will include expected time to within ±45 minutes, azimuth start angle to within ±30o, and max elevation angle to within ±15o.
In order to produce a TLE within the characteristics detailed by FR6, the TDoA accuracy requirement detailed in FR5 must also be satisfied. If the timing requirements for FR5 are met, the timing requirements for FR6 are also met. This means the design decisions driven by FR5 also satisfy our requirements for FR6.
HackRF SDR
NEO 6m GPS chip
Notes: Colin

## Slide 47
Almost Certain
Likely
Unlikely
Rare
Insignificant
Minor
Major
Severe
Particle Filter Complexity
GPS Loses Lock
Supply Chain
Out of Memory
Hardware Damage/Failure
RF Noise
Dropped Samples
Cold SDR Clock
10
11
Gibbs Method Accuracy
1
2
3
4
5
8
7
6
9
Major Risks (mitigated) | 
1 | GPS loses lock for more than a minute
2 | SDR is out of stock/lead time is too long/dead on arrival
3 | Raspberry Pi is out of stock
4 | SDR clock is cold
5 | SDR drops samples
6 | PPS lost to noise
7 | Electrical short, water damage, antenna mount fails
8 | Raspberry Pi runs out of memory
9 | System noise greater than expected
10 | Particle filter is not complete
11 | Three out of plane position estimates for Gibb’s.

## Slide 48
Major Risks | Major Risks | Mitigation | Likelihood | Impact
1 | GPS loses lock for more than a minute | Many data passes, timing extrapolation | Likely | Major
2 | SDR is out of stock/lead time is to long/dead on arrival | Order ASAP, other sufficient SDR options | Unlikely | Severe
3 | Raspberry Pi is out of stock | Order ASAP, other suppliers | Unlikely | Severe
4 | SDR clock is cold | Ensure components maintain operating range | Almost Certain | Insignificant
5 | SDR drops samples | High sampling rate, long sample duration | Likely | Insignificant
6 | PPS lost to noise | Rare based on tests performed with RTL SDR | Rare | Insignificant
7 | Electrical short, water damage, antenna mount fails | Proper weather and electrical proofing | Rare | Severe
8 | Raspberry Pi runs out of memory | Proper estimates of data rate and OS size | Unlikely | Severe
9 | System noise greater than expected | Plenty of margin in link budget | Rare | Minor
10 | Particle filter is not complete | It is not our only orbital prediction method | Likely | Severe
11 | Three out of plane position estimates for Gibb’s. | Data smoothing | Likely | Severe

## Slide 49
Major Risks (mitigated) | 
1 | GPS loses lock for more than a minute
2 | SDR is out of stock/lead time is too long/dead on arrival
3 | Raspberry Pi is out of stock
4 | SDR clock is cold
5 | SDR drops samples
6 | PPS lost to noise
7 | Electrical short, water damage, antenna mount fails
8 | Raspberry Pi runs out of memory
9 | System noise greater than expected
10 | Particle filter is not complete
11 | Three out of plane position estimates for Gibb’s.
Almost Certain
Likely
Unlikely
Rare
Insignificant
Minor
Major
Severe
Particle Filter incomplete
GPS Loses Lock
Supply Chain
Out of Memory
Hardware Damage/Failure
RF Noise
Dropped Samples
Cold SDR Clock
10
11
Gibbs Method Accuracy
1
2
3
4
5
8
7
6
9

## Slide 50: Environmental Readiness Testing time will be dictated by satellite’s orbital passes. The sensor unit must be ready to operate in rain, snow and the temperatures expected during spring semester in Boulder
Notes: Ryan B

## Slide 51
Model - Overview
NEMA 4: Ensures internals are protected from water/snow, and are suitable for outdoor conditions
Notes: Ryan B. (Probably still need to do some sort of testing to ensure water proof as a whole and when cord crips and cords are in place( Temporarily in Place))

## Slide 52
Verification Method - Test | 
Overview: Units will be left out in planned positions and turned on for a period of 24 hours. Proves DRs 1.1-1.2 are satisfied. Success Criteria: If after 24 hours, if sensor is still operating nominally (i.e. powered on and reporting data), and temperature data shows that the box remained within the temperature requirement then the test will be marked as a success. | Measurements: Temperature within the box during the 24 hour time period. Concerns: Box will remain within the operating temperature of all components during the full 24 hours
Notes: Find a better way to quantify Outdoor Sun case (keeping a constant temperature): Ryan B

## Slide 53: RF Front End The RF front enables UHF and L-band signal reception. The reception must be good enough to discern the transmission from the noise floor

## Slide 54
Verification Method - Test Level 1 | 
Overview: Holding the antenna a few feet above ground while attached to a receiver or transceiver and a Wattmeter, sweep across the acceptable frequency range plus measurements on either side of the frequency limits, which will result in peaks and nulls more pronounced in the antenna’s intended frequency range than way outside the band. Success Criteria: Frequency Range sweep results in pronounced peaks and nulls in Watts, and the frequency ranges are confirmed. | Concerns: Wattmeter will result in too much noise, and peaks/nulls won’t be identified
Notes: Benji

## Slide 55
Verification Method - Test Level 2 | 
Overview: As a fully integrated unit, the hardware will be used to see an RF signal from the UHF and L band satellite targets on a individual unit basis. Success Criteria: An RF signal can be seen in the data recorded by the SpaceNet unit. | Measurements: Observation of RF data from the integrated unit. Concerns: Unit must be fully operational for test to occur.
Notes: Benji
Test level two will be conducted on a individual unit basis, and the full set of subsystems will be used to see the RF signal from both the UHF and L-Band Satillites. Success of this test will be based off of the data recorded by the unit, and the main concerns of the test are the need for a fully integrated unit for testing.

## Slide 56: Timing Synchronization The received data must be alignable such that time delay can be measured with extreme precision. Error here has a large impact on positional predictions

## Slide 57
Key Driving Requirements
DR5.1.
The data shall be alignable to within 420ns time
Local Clock A
Local Clock B
< 420ns error
DR5.2.
The system shall be able to capture >2.4M samples per second
>2.4M samples per second
Time
Voltage
Voltage
Notes: Forest:
To restate the driving key requirements for time synchronization, we want to be able to align the data within 420 ns as well as be able to capture 2.4 M samples per second.

## Slide 58: Verification test for DR5.2.
SDRs will be fitted with GPS modules and set to sample at 2.4M samples.
Recorded data. And compare recorded number of samples to the set rate.
Standard deviation of this error will be used to verify alignment precision.
Recorded
Num Samples
Notes: Forest:
Our first test will involve fitting the SDR with the GPS module and setting the sample rate to 20M samples per second.
Well record the data and compare the recorded number of samples to a set rate.
We’ll be able to count how many samples in-between the pulses from the GPS. This should be 20M samples which exceeds our key requirement of 2.4 M samples.
Standard Deviation will be used to verify alignment.

## Slide 59: Verification test for DR5.1.
GPS+SDRs will be set up close enough together that the system should be unable to perceive the time delay of signal arrival
A signal will be sent out to both SDRs
The received signals should appear identical due to local proximity
SDR+GPS
Transmitter
TIME [s]
Signals align within
< 2 samples
SDR+GPS
Notes: Forest:
The second test that we will be doing is placing 2 SDR’s next to each other and transmitting a signal to them. Due to their proximity, we shouldn’t be able to tell which SDR received the unit first and the signals should align within 2 samples which result in 100 ns alignment precision. This satisfies our requirement of less than 420 ns of error.

## Slide 60: Position Vector Estimate using TDoA Time Delay of Arrival(TDoA) ranging is used to produce the positional information required for orbital prediction
Notes: Sam (Intro: Hello, me Sam, safety lead and software engineer. I will be discussing the verification and validation our positioning model.)

## Slide 61: Position Vector Estimate using TDoA Model - Overview
Inputs: Time each sensor unit detects the satellites signal and the position of each unit in ECEF coordinates.
Process: Time differential are taken with respect to one “source” unit and add noise to the time. Theses time delays are passed through an iterative equation set based on an initial guess.
Outputs: A position vector from the satellite’s orbital position.
Notes: Sam: Our current model takes each sensors position vector in ECEF coordinates and the time of arrival of the signal to each sensor. The times of arrival are then compared relatively to produce the ‘time delay of arrival’ to each sensor. The position vector of the target satellite is then output.

## Slide 62: Position Vector Estimate using TDoA Verification Method - Test
Overview: Sensor units will be placed in Pueblo, Boulder, Aurora, and Virginia Dale (Approx. 100 km radius). Units will be turned on and will record four passes of an overhead target satellite. Pass data will be stored locally on each sensor unit and post processed. TDoA position vectors will be produced during this post processing utilizing all four gathered data sets. Success Criteria: Publically available TLE data set will be propagated. Propagated position vectors will be compared to calculated TDoA positions and serve as the reference to determine satisfaction of the functional requirement. If the magnitude of error between propagated and calculated position vectors during a moment in time can be achieved below 100km, the test[1] is a success | Measurements: GPS provides pps time synchronization and SDR provides a sampling rate of >10MHz timestamp to provide at least 100 ns timing resolution Concerns: FR4 Nominal operation of all four sensor units during satellite candidate passover
[1]Test will be performed for both UHF and L-Band satellite candidates | 
Notes: Sam: Our sensor units will be placed in Pueblo, Boulder, Aurora and Virginia Dale to satisfy DR. 5.3 (100 km radius). The pass’ data is stored locally, centralized, and then post-processed to produce a position vector approximation at the centerpoint of the pass. This approximation is then compared to propagated public domain TLE sets to determine the absolute positioning error at the pass’ midpoint.
If the absolute error between the approximation and true position at that point is within 100km, the test is considered a success.
There are two major points of concern here: Maintaining of timing sync. and nominal operation of all four sensors during a passover. Timing sync. Is critical as RF signals propagate at the speed of light, meaning a small timing error can produce a massive positioning error.

## Slide 63: Orbital Determination Two methods: Gibbs and Particle Filter. Both produce orbital predictions that are the final product of the project
Notes: Sam: Now, for the verification of FR6.

## Slide 64: Orbital Determination Model - Overview
Inputs:
STK used to generate exact position vector data for a simulated passover for both satellite candidates.
Process:
Simulated error is applied to exact position data consistent with the TDoA position estimate accuracy requirement (100 km magnitude error)
Data points selected to maximize positional angular separation and fed into Gibbs method. Application of Gibbs method results in a State Vector from which orbital elements can be backed out of.
Outputs
Orbital elements formatted and rearranged to produce a TLE estimate.
Notes: Sam: We have been using STK to generate precise positioning data for passovers. The position vectors at each horizon and the pass’ midpoint are then processed using Gibb’s method to produce the orbital elements of the target. These orbital elements make up the second line of the two line element set.

## Slide 65: Orbital Determination Verification Method - Test
Overview: Following a successful test for FR5, TDoA positional vector data for the duration of the satellite candidate passover will be analyzed and used to produce an approximate TLE. Success Criteria: This calculated TLE will then be compared to a publically available TLE. Both TLEs will be propagated forward utilizing the SGP4 model[1] and the predictive capability of our calculated TLE will be compared. If our calculated TLE is able to predict future passover opportunities within the thresholds defined by FR6, the test[2] will be considered a success. [1]Simplified General Perturbations model 4(SGP4) includes the effects of drag and other orbital decay mechanisms for near earth objects with an orbital period less than 225 min. [2]Test will be performed for both UHF and L-Band satellite candidates | Measurements: TDoA positional data calculated during test for FR5 Concerns: FR4, FR5 TDoA data must have been calculated for the target at multiple points during a passover Nominal operation of all four sensor units during satellite candidate passover
Notes: Sam: Using data from a successful test of FR5, a TLE set will be produced and propagated using SGP4 to visualize a passover. The true passover and the calculated passover will be compared, similarly to the figure in the lower right. If the calculated passover is able to predict a future passover within 45 minutes time accuracy, 30 degrees azimuth accuracy at the start of the passover and 15 degrees elevation at the midpoint, such that the system will be able to detect, identify, and repeat this process, the test will be considered a success.

## Slide 66
Ryan Prince Project Manager | Colin Ruark Asst. Project Manager
Jordan Gage Financial Lead | Keith Poletti Lead Analyst
Tyler Pirner Network Lead | Noah Francis Software Lead
Benji Smith Systems Engineer | Sam Firth Safety Lead
E Forest Owen Data/Power Lead | Ryan Burdick Manufacturing Lead
Israel Quezada-Cordova Electrical Lead | 

## Slide 67
Work Breakdown Structure (WBS)

## Slide 68
Electronics
Software
Hardware/RF
Notes: Not the correct timeframe, will add once more tasks are in the developement stage of the clickup

## Slide 69: Cost Plan
Item | Description | Price
Raspberry Pi 4 Model B (4 GB) | on-board computer | $55.00
HackRf One | software defined radio | $299.95
SD Card | 32Gb SD card for OS and data storage | $10.29
L-Band Low Noise Amp | ZX60-242GLN-S+ | $74.82
UHF Low Noise Amp | SPF5189Z RF amplifier | $15.00
L-Band Antenna | 1.2 GHz 8 dBi flat patch antenna | $50.00
UHF Antenna | HYS YAGI antenna high gain 9dBi UHF | $50.00
Electronic RF Logic Switch | F2932EVBI evaluation board | $83.13
Housing | WH-16 hinged nema enclosure | $50.75
GPS Module | GPS module GPS NEO-6M | $39.95
Miscellaneous Electronics Hardware | power supply, cords, ProtoBoards, etc. | ~$69.34
Miscellaneous Hardware | mounting hardware, screws, etc. | ~$50
Four Unit Cost
$3392.92
Single Unit Cost
$ 848.23
Remaining Development Budget
$800

## Slide 70: Cost Plan
Item | Description | Price
HackRf One | Software Defined Radio | $299.95
L-Band Antenna | 1.2 GHz 8 dBi Flat Patch Antenna - SMA Male Connector | $50.00
Computer controlled RF logic switch | F2932EVBI Evaluation Board | $83.13
Total Risk
$ 50.00
Margin per unit
$400
The HackRF may be out of stock from our original provider. Testing a copy from Banggood to prevent $30 cost increase and save $200
If L-band link does not close a different antenna is required for the new frequency.
The specific board is in limited supply may cause a $20 cost increase.
Risk is within allowable margin

## Slide 71: Test Plan
Date | Test | Description
2/1/21 | RF Front End(DR 3.1/2/3/4 ) | Proves that single unit hardware can see RF signals in the desired bands.
2/1/21 | Component level Time Synchronization testing(DR 5.1) | Proves that the timing mechanism is operating as expected on the SDR
2/1/21 | Component level On board OS and script testing(DR 5.2) | Proves the auto start and SDR interfacing scripts are operational
2/8/21 | Fully Integrated Single Unit RF Test (DR 5.2) | Proves that single fully integrated unit can receive RF signals, handle the data rates, and sample at the expected frequency.
2/9/21 | Environment Survival Test (DRs 1.1-1.2) | Proves that a single fully integrated unit can survive the environment.
3/22/21 | Fully Integrated Remaining Units RF Test (DR 5.2) | Proves all fully integrated units can see RF signals, handle the data rates and sample at the expected frequency.
3/23/21 | Remaining Units Environment Survival Test (DRs 1.1-1.2) | Proves all fully integrated units can survive environment.
4/5/21 | Full Suite Time Synchronization Test (DR5.1) | Proves timing between units is sufficiently synchronized before moving them to final testing locations
4/12/21 | TDoA Accuracy Test (DR 5.3 & FR5) | Proves data measured by 4 units can be turned into a orbital position of sufficient accuracy when compared to a truth data set.
4/19/21 | TLE Accuracy Test | Further processes the data to prove the data collected and algorithms used produce a TLE of sufficient accuracy when compared to a truth TLE.
*Note: None of the above tests require access to special facilities or hardware not available to the team. The final two tests require a significant bit of transportation to ensure sufficient separation of the SpaceNet units.

## Slide 72: Backup Slides
Notes: Should clean up backup slides before submitting

## Slide 73
Link-Margin is derived:
Where:
ISL is the Isotropic Signal Level at the ground station(UHF:143.8dBW L-Band:-154.2dBW
G/T is the same a prior calculated G/T(UHF:-20dB/K, L-Band:-17dB/K)
L pointing is the pointing loss of the antenna(UHF:9.5dB, L-band: 9.5dB)
KB is Boltzmann Constant(-228.6dW/K/Hz)
Z is the data rate(UHF:9.7kbps, L-band:2.4kbps)
Eb/No|min is the required signal to noise ratio to detect the modulation technique(UHF:8.4dB, L-band:15.7dB)
Notes: Should probably be moved in support of section 2.4

## Slide 74
Elevation Angle [Deg]
Notes: Benji

## Slide 75: RF Front-End

## Slide 76: Power & Data Budget - option 2

## Slide 77: Data Transfer Bottlenecks: Raspberry Pi 4
The rate at which the Pi 4 can transfer data through its GPIO ports is heavily controlled by the programming language, and by the interrupt configuration used:
  Python (upper right figure)
    Typically ~ 50 kHz
  C
    Typically ~ 131 MHz
The rate at which the Pi 4 can transfer data through its USB 3.0 ports is comparatively shown in the bottom right figure
  Read: 363 MBps
  Write: 323 MBps
Link
Notes: Graph sources:
https://magpi.raspberrypi.org/articles/raspberry-pi-4-specs-benchmarks
https://medium.com/@ghalfacree/benchmarking-the-raspberry-pi-4-73e5afbcd54b
Github Raspberry Pi 4 experiment: https://github.com/hzeller/rpi-gpio-dma-demo#direct-output-loop-to-gpio
SD card site: https://www.raspberrypi.org/forums/viewtopic.php?t=157743

## Slide 78: Data Transfer Bottlenecks: SDR and GPS Module
HackRF One
The HackRF One is capable of receiving and transmitting on a frequency range of 1MHz to 6GHz with output power of 30 mW to 1 mW depending on the band.
Ublox NEO 7M
The maximum reference output clock per the data sheet is 10 MHz.
Has also been reported to be stable at 13 MHz.
Link

## Slide 79: Power Pipeline
Component | Voltage Required (V) | Current Required (mA) | Power Source
Raspberry Pi | 5 | 3000 | Outlet
SDR | 5 | 500 | Outlet
LNA x2 | 5 | 210 | USB (1)
GPS | 5 | 40 | USB (2)
Switcher | 2.7 - 5 | 0.26 | USB (2)
Notes: Power Sttrip: USB: 5 V at 2.4 Amps per port
Outlet: 125 V at 10 A between the two ports

## Slide 80: Data Pipeline
Notes: LNA and Switcher are Analog compoints
SDR has ADC we should be working with about 30 MB/s
The USB data transfter rate has a 625 MB/s
The SD Card were using has a max write speed of BLANK

## Slide 81: Power & Data Pipeline

## Slide 82: Power Pipeline
Notes: Power Sttrip: USB: 5 V at 2.4 Amps per port
Outlet: 125 V at 10 A between the two ports

## Slide 83: Data Pipeline
Notes: LNA and Switcher are Analog compoints
SDR has ADC we should be working with about 20 MB/s
The USB data transfter rate has a 625 MB/s so were good there
The SD Card were using has a max write speed of BLANK
----> Limited to Pis capabliity of 28MB/s > 20MB/s
Alot of this is dependent on how we program the pi

## Slide 84
Like list of nutrition facts go here:
Dual Band capable SDR equipt Sensor Unit
height
weight
frequencies
FOV
Receive data rates
Positional accuracy
Hardware sub sys
  Power/Data
  RF
  Structure

## Slide 85: Baseline Sensor Unit Design
HackRF One
SDR that will handle RF communications
Raspberry Pi 4 & Power Supply
On Board Computer for data collection and transfer
Neo-7M GPS
Breakout Board
Used to synchronize data timestamps
Nema 4 Enclosure
Rated housing ensures component protection. Clear top enables GPS lock
Antenna Switcher
Used to switch between the antennas.
Power Strip
Used to distribute power to components within the box
Power Regulator Board
Used to supply steady voltage too.. (add)
Internal Mounting Plate
Used to secure hardware within the box
Do we have an updated model that has 2 LNAs and a switch?
LNA’s
Used to improve G/T metric ensuring adequate reception of satellite transmission.

## Slide 86
Almost Certain
Likely
Unlikely
Rare
Insignificant
Minor
Major
Severe
1
2
3
4
5
6
7
9
8
Particle Filter Complexity
GPS Loses Lock
Supply Chain
Out of Memory
Hardware Damage/Failure
RF Noise
Dropped Samples
Cold SDR Clock
10
Expected to occur regularly during operation
Expected to occur at some point
Not likely in normal operation
Could happen, but probably will not
Minor flaw that does not impact operation | Affects TDoa accuracy but will remain in spec | Pushes TDoA accuracy out of spec | Could cause system failure
Risk Matrix
11
Gibbs Method Accuracy

## Slide 87: TDoA/TLE Backup Slides

## Slide 88
Local regression using weighted linear least squares and a 2nd degree polynomial model to smooth out TDoA data for TLE element calculation

## Slide 89: Worst Case Scenario Monte Carlo TDoA Plots
Covariance Ellipse Closest approach
Covariance Ellipses First Horizon
Covariance Ellipses Second Horizon

## Slide 90: Sensor Separation
Separation affects time delay of arrival for each sensor.
The sensors were placed on circles of radius Rn at cardinal directions(North, East, South, West).
R1
R2
Rn

## Slide 91
As sensor unit separation increases, positional error decreases.
To reach the 10 km requirement, the sensor must be placed on a circle with radius 60 km
60km separation is feasible
Acceptable Sensor Separation
( > 60 km)

## Slide 93: Relating to introducing error into calculated TLE model
Select an error vector direction uniformly:
Then select the corresponding error vector magnitude from a Gaussian
distribution for each position vector:
We then add these error vectors to their corresponding position vectors.
As the TLE calculation model matures, we will be able to bypass this artificial error distribution method and feed simulated TDoA position data generated by propagating expected sources of TDoA error directly into orbital determination methods.

## Slide 94
Particle Filter
Two main sources factor into our ability to calculate an accurate TLE:
Position vector from TDoA
Filtered Position and Velocity from Particle filter
Determined velocity and position are ran through a TLE converter to get the final TLE.
Details of Particle Filter:
Converges on a point based on probability distribution over time.
Currently working for 2D case of a harmonic oscillator and orbital dynamics
Need to implement SGP4 perturbations

## Slide 95: Early Development of Orbital PF

## Slide 96: Early Development of Orbital PF Residuals

## Slide 97: Orbital PF One Orbit Comparisons
*Gibbs shown here DOES NOT have smoothing on TDoA Data
Side View
Top View

## Slide 98: Thermal Backup Slides

## Slide 99
Results:
Thermal Analysis Equations:
Notes: Where Qdot is coming from (eff = 0)
Min & Max assume (eff .8, 1.2)

## Slide 100
Thermal Verification Method - (Additional Tests Included) | 
Overview: (2 Tests) Units will be fully constructed (all components integrated) and run at room temperature for a period of 4 hours. Use corresponding data to more accurately model the heat produced by the operating components. (Repeat testing for Cold (0 Celsius) and Hot(Outdoor in Sun) environments) Units will be left out in planned positions and turned on for a period of 24 hours. Proves DRs 1.1-1.2 are satisfied. Success Criteria: If after 24 hours, if sensor is still operating nominally (i.e. powered on and reporting data), and temperature data shows that the box remained within the operating temperature of all components then the test will be marked as a success. | Measurements: Infrared temperature readings every half hour for room temperature test. Temperature within the box during the 24 hour and 6 hour time period. Concerns: Box will remain within the operating temperature of all components during the full 24 hours
Notes: Find a better way to quantify Outdoor Sun case (keeping a constant temperature)

## Slide 101: Structures Backup Slides

## Slide 102
Verification Method - Test | 
Overview: Units will be placed in mounting position (upright) and subjected to a flow of water via a hose on each seem between the lid and box and on each external face (excluding the bottom) for periods up to 10 minutes Success Criteria: If after the period of 10 minutes and each seem and side being subjected to an onset of water the box shows no sign on ingress of water internally the test will be deemed a success. | Measurements: N/A Concerns: The box internals remain dry