## Slide 1: SBMS Stored Battery Monitoring System Preliminary Design Review October 18th, 2021 ASEN 4018-012 Team 6 Customer: EnerSys ABSL Presenters: Richard Folsom, Ben Gavin, Joseph Harrell, Jamie Henault, Shreeyash Nadella, Nathan Zhao Additional Team Members: Ian Adler, Devin Geegan, Evan Meany

## Slide 2: Presentation Outline
Project Description (Nathan)
Evidence of Baseline Feasibility
  Communication Signal & Processor Feasibility (Shreeyash)
  Power Source Feasibility (Joseph)
  Voltage Sensor Feasibility (Jamie)
  Temperature Sensor Feasibility (Ben)
  Financial Feasibility (Richard)
Status Summary & Remaining Studies (Richard)
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 3: Project Description

## Slide 4: Project Motivation
EnerSys ABSL batteries
  Storage
  Health Deterioration
Quality checks
  Bagging Process
  Time-consuming
Task: SBMS
  Wireless Monitoring System
  Report on battery and environment health
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 5: Project Objectives
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 6: Concept of Operations (CONOPS)
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 7: Functional Block Diagram (FBD)
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 8: System Critical Project Elements
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Temperature and voltage sensors
CPE1
Sensing Hardware
Means to transmit data wirelessly
CPE2
Wireless Communication Hardware
Software to command data transfer
CPE3
Wireless Communication Software
Interface correctly between components and customer’s
battery
CPE4
System Integration
Operate off an external power source
CPE5
Power Source
Tested/validated to ensure function
CPE6
Testing and Validation

## Slide 9: System Functional Requirements
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Measure voltage
FR1
Voltage Sensing
Measure temperature
FR2
Temperature Sensing
Communicate when voltage and/or temperature
reach an undesirable state
FR3
Alerts
Continue operation after sanitization and
bagging process performed by customer
FR4
Sustainability
Transmit and receive data wirelessly
FR5
Wireless Capability
Be battery-powered
FR6
Operations
Receive data with a timestamp
FR7
Tracking

## Slide 10: Baseline Design (Storage)
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
K470 Zarges Box
Styrofoam Layer
Heat/Vacuum Sealed Bag
Monitoring System
Silicon IC Temperature Sensor
Silicon IC Temperature Sensor

## Slide 11: Baseline Design (Monitoring System)
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Voltage from Battery
Silicon IC Temperature Sensor
Silicon IC Temperature Sensor
Active Voltage Sensor
Nordic Semiconductor Processor
Lithium Polymer Battery
Bluetooth Low Energy

## Slide 12: Feasibility: Communication Signal & Processor

## Slide 13: Communication: Reasoning & Approach
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Required by customer → Communication Signal must be analysed for feasibility
Feasibility assessed by chip’s range and ability to send information
Low power consumption
Metric | Description | CPE | Requirement
Signal Strength | The wireless signal shall be received at least 3 ft outside of an aluminum box. | 2,3 | 5.4, 5.5
Data Transfer Accuracy | Temperature and voltage data shall be transmitted wirelessly. | 2,3 | 5.2, 5.3
Power Consumption | The SBMS shall operate for one year. | 3 | 6.1

## Slide 14: BLE Signal Strength Experiment
Nordic Semiconductor BLE scanned BLE beacon:
  Inside enclosed metal container
  Inside open metal container
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Experimental Setup with open metal container and enclosed metal container [15][17][18][19]

## Slide 15: Candidate Processors
Processor | Idle Power Consumption | Cost | RAM | BLE Compatible?
nRF52840[15] | 1.5 uA | $10-13 | 256 KB | Yes
nRF5340[14] | 1.7 uA | $7-10 | 512 KB | Yes
nRF52805[16] | 1.1 uA | $2-4 | 24 KB | Yes
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 16: Main Takeaways
BLE is feasible within range requirements
The processors are feasible within cost, power, and BLE constraints
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 17: Feasibility: External Power Source

## Slide 18: Design Requirements: External Power Source
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Battery must satisfy DR 6.1
Feasibility proven by estimating required battery capacity
Metric | Description | CPE | Requirement
Battery Capacity | External battery shall operate for one year without charging | 5 | 6.1

## Slide 19: Estimated Required Battery Capacity
Required Battery Capacity | 2.36 Ah
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Processor Wake (IP) | Processor Sleep (Is) | Communications (IC ) | Voltage Sensors (IV) | Temperature Sensors (IT) | Wake Time (tw) | Factor of Safety
541 μA[6] | 67.7 μA | Included in IP | 400 μA[2],[5],[11] | 20 μA[10] | 60 s | 2

## Slide 20: Power Draw Simulation
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Monte Carlo of extreme scenario
Sizing ratio for wake to sleep mode

## Slide 21: Feasibility: External Power Source
Battery Examples | Battery Capacity | Dimensions
Zeee 8000mAh 11.1V 100C 3S RC[7] | 8 Ah | 5.43 x 1.85 x 1.41 in
Youme Lipo 4S Battery[8] | 3 Ah | 5.35 x 1.77 x 1.26 in
Ryobi 18-Volt ONE+[9] | 1.5 Ah | 5.32 x 3.12 x 3.42 in
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
External Power Source is feasible
  COTS LiPo batteries exist that satisfy this requirement
  Power systems are ~$60

## Slide 22: Feasibility: Voltage Sensor

## Slide 23: Voltage Sensor: Reasoning & Approach
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Voltage measurement critical in understanding the health of the battery
Feasibility assessed by sensor’s ability to accurately measure a specific range of DC input voltages
Metric | Description | CPE | Requirement
Range | Voltage sensor shall have a range of at least 20-33.6V. | 1 | 1.1
Accuracy | Voltage sensor shall have a sensitivity of at least 0.1V. | 1 | 1.2
Compatibility | Voltage sensor shall measure DC voltage. | 1, 4 | 1.4

## Slide 24: Possible Sensors
Sensor | Voltage Relative Error | Voltage Range
Adafruit INA260 Voltage Sensor[1] | ±1% | 0 to 36V
DFRobot Gravity: I2C Digital Wattmeter[2] | ±0.2% | 0 to 26V
Team Concept Design RK73G2ATTD2002C Resistor (R1)[3] RK73G2ATTD4701C Resistor (R2)[4] OPA2205 Buffer[5] | ±0.25% tolerance ±0.25% tolerance ±15μV (max) input offset voltage | Vmax = 50V Vmax = 24.24V Vs,min= 4.5V, Vs,max= 36V, -7 to 7V recommended
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 25: Measured Voltage Accuracy for Adafruit
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Monte Carlo Simulation
Actual Voltage (VA)
  Random value from 0 to 36V
Percent Error (E)
  Random value from -1% to +1%
Absolute Voltage Error (VE)
  VE = VA*E

## Slide 26: Measured Voltage Accuracy for Adafruit Continued
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Updated Monte Carlo Simulation
Actual Voltage (VA)
  Random value from 20 to 33.6V
Absolute voltage error increases with increasing voltage

## Slide 27: Measured Voltage Accuracy for Adafruit Continued
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Updated Monte Carlo Simulation
Voltage Divider Addition
  Brings sensor input voltage down from 20-33.6V to about 3.8-6.4V

## Slide 28: Main Takeaways
Performed same analysis for remaining sensors
All three sensors are feasible options
  Adafruit Voltage Sensor
    Measures DC voltage
    Needs voltage divider to meet accuracy requirement
  DFRobot Voltage Sensor
    Measures DC voltage
    Needs voltage divider to meet range requirement
  Team Concept Design
    Measures DC voltage
    High precision components allow for all requirements to be met
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 29: Feasibility: Temperature Sensor

## Slide 30: Temperature Sensor Reasoning & Approach
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Required by customer → Sensor must be analyzed for feasibility
Feasibility assessed by range, accuracy & ability to send data to a processor
Metric | Description | CPE | Requirement
Range | Sensor must be accurate within 0-20°C range. | 1 | 2.1
Accuracy | Sensor must have an accuracy of 0.1°C. | 1 | 2.2
Compatibility | Sensor must interface with processor. | 1, 4 | 2.3

## Slide 31: Possible Temperature Sensors
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Sensor | Range (°C) | Accuracy (°C) | Compatibility
TI TMP117[12] | -55 to 150 | 0.1 from -20 to 50 | 1.8 to 5.5V, Digital I2C-SMB Signal
Smartec SMT172[13] | -45 to 130 | 0.1 from -20 to 60 | 2.7 to 5.5V, Digital PWM Signal
TMP117 Accuracy[12]
SMT172 Accuracy[13]

## Slide 32: Main Takeaways
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Feasible within course duration & team skills.
Feasible within facilities.
Feasible within project budget.
COTS sensors meet design requirements & easily interface with a microcontroller.

## Slide 33: Feasibility: Financial

## Slide 34: Budget Estimates for Financial Feasibility
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
[15]
[15]
[15]
[1]
[13]
[8]
[8]
[20]

## Slide 35: Status Summary & Remaining Work

## Slide 36: Status Summary
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
 | Feasibility Proven?
Communication Signal | 🗸
Processor | 🗸
Power System | 🗸
Voltage Sensor | 🗸
Temperature Sensor | 🗸
Financial | 🗸

## Slide 37: Remaining Work
Trade studies
  Processor
  LiPo Battery
  Voltage Sensor
  Temperature Sensor
Processor Research
  No built-in sleep mode
  Need to research implementation
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Integration Considerations
  Full circuit design w/ sensors
  Wireless transmission of the data
Prototyping
  Chassis Box
  Voltage sensor
  Processor Software

## Slide 38: Acknowledgements
EnerSys ABSL Team
Jacqueline Maldonado, Brice Lucero, Travis Mault, Ryan Pritchard
Team Advisor
Dr. Jean Koster
Projects Advisory Board
Dr. Jelliffe Jackson, Dr. Jade Morton, Christopher Roseman,
Dr. Jean Koster, Dr. Melvin Rafi, Professor Matt Rhode
Additional Support
Professor Trudy Schwartz, Professor Bobby Hodgkinson,
Emma Markovich, Colin Claytor
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 39: Thank You! Questions?

## Slide 40: References
Siepert, B., “Adafruit INA260 Current + Voltage + Power Sensor Breakout,” Adafruit Learning System. Available: https://cdn-learn.adafruit.com/downloads/pdf/adafruit-ina260-current-voltage-power-sensor-breakout.pdf
“Gravity: I2C Digital Wattmeter,” DFRobot. Available: https://media.digikey.com/pdf/Data%20Sheets/DFRobot%20PDFs/SEN0291_Web.pdf
“RK73G2ATTD2002C,” Digikey Electronics. Available: https://www.digikey.com/en/products/detail/koa-speer-electronics-inc/RK73G2ATTD2002C/13577087
“RK73G2ATTD4701C,” Digikey Electronics. Available: https://www.digikey.com/en/products/detail/koa-speer-electronics-inc/RK73G2ATTD4701C/13576067
“OPA2205 2-µV, 0.04-µV/°C, Low-Power, Super Beta, Bipolar, e-trim™ Op Amp,” Texas Instruments. Available: https://www.ti.com/lit/ds/symlink/opa2205.pdf?HQS=dis-mous-null-mousermode-dsf-pf-null-wwe&ts=1633294801543&ref_url=https%253A%252F%252Fwww.mouser.com%252F
“Online Power Profiler for Bluetooth Le.” Online Power Profiler for Bluetooth LE - Opp - Online Power Profiler - Nordic DevZone. Available: https://devzone.nordicsemi.com/nordic/power/w/opp/2/online-power-profiler-for-bluetooth-le
“Zeee 8000mAh 11.1V 100C 3s RC Lipo Battery” . Available: https://www.amazon.com/Zeee-8000mAh-Battery-Traxxas-Associated/dp/B07K1B79P3
“Youme 11.1V RC Lipo Battery Pack, 3S Lipo Battery 6500mah 60C with TRX Plug for Traxxas Slash X-Maxx RC Buggy Truggy Crawler Monster Car ，Helicopter，Airplane (2packs) Ship from USA, Battery Packs - Amazon Canada.” Youme 11.1V RC Lipo Battery Pack, 3S Lipo Battery 6500mAh 60C with TRX Plug for Traxxas Slash X-Maxx RC Buggy Truggy Crawler Monster Car ，Helicopter，Airplane (2Packs) Ship from USA, Battery Packs - Amazon Canada. Available: https://www.amazon.ca/Youme-Battery-6500mAh-Traxxas-%EF%BC%8CHelicopter%EF%BC%8CAirplane/dp/B07ZM8K3NM
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 41: References Continued
9.“Ryobi 18-Volt One+ Lithium-Ion Compact Battery Pack 1.3AH” Available: https://www.amazon.com/Ryobi-18-Volt-Lithium-Ion-Compact-Battery/dp/B07G7D9JVN
10. “Temperature Sensors.” STMicroelectronics Available: https://www.st.com/en/mems-and-sensors/temperature-sensors.html#:~:text=The%20digital%20temperature%20sensors%20feature,55%20to%20%2B125%20%C2%B0C
11. “INA260,” Texas Instruments. Available: https://www.ti.com/product/INA260#description
12. “TMP117 Datasheet,” Texas Instruments, Revised April 2021. Available: https://www.ti.com/product/TMP117
13. “SMT172 Datasheet,” Smartec, Last Updated March 20, 2017. Available: https://www.smartec-sensors.com/cms/media/Datasheets/Temperature/SMT172-datasheet.pdf
14. “nRF5340,” Nordic Semiconductors. Available: https://www.nordicsemi.com/-/media/Software-and-other-downloads/Product-Briefs/nRF5340-SoC-PB.pdf?la=en&hash=3A89851C4F094917E874D092CF68DB27E51A5E4A
15. “nRF52840,” Nordic Semiconductors. Available: https://www.nordicsemi.com/-/media/Software-and-other-downloads/Product-Briefs/old-versions/nRF52840PBv20.pdf?la=en&hash=516968A8D06D7F41C8B14B6639DD9E14099E2853
16. “nRF52805,” Nordic Semiconductors. Available: https://www.nordicsemi.com/-/media/Software-and-other-downloads/Product-Briefs/nRF52805-SoC-PB.pdf?la=en&hash=747490E125E4A9D0B79B47B7C03FD9D6ED4150C1https://www.nordicsemi.com/-/media/Software-and-other-downloads/Product-Briefs/nRF52805-SoC-PB.pdf?la=en&hash=747490E125E4A9D0B79B47B7C03FD9D6ED4150C1
17. “BLE,” Special Interest Group. Available: https://www.bluetooth.com/
18. “Measuring Tape,” The Tape Store. Available: https://www.thetapestore.co.uk/knowledgebase/How/How_to_Read_a_Tape_Measure.html
19. “Metal Box,” Amazon. Available: https://www.amazon.com/metal-box/s?k=metal+box
20. “Gantter | Project Planning & Task Management Software”. Ganter. Available: https://www.gantter.com/pricing/
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 42: Backup Slides

## Slide 43: Requirements
FR | DR | Requirement
1 |  | System shall measure voltage
 | 1.1 | Voltage sensor shall have a range of at least 20-33.6V
 | 1.2 | Voltage sensor shall have a sensitivity of 0.1V
 | 1.3 | Voltage sensor shall connect to the customer’s 8S3P battery
 | 1.4 | Voltage sensor shall measure DC voltage
2 |  | System shall measure temperature
 | 2.1 | Temperature sensor shall have a range of at least 0-20oC
 | 2.2 | Temperature sensor shall have a sensitivity of 0.1oC
 | 2.3 | Temperature sensor shall measure the temperature of the battery environment
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 44: Requirements Continued
FR | DR | Requirement
3 |  | System shall communicate when voltage and temperature reach an undesirable state
 | 3.1 | Alert shall be generated when voltage exceeds 33.6V
 | 3.2 | Alert shall be generated when voltage drops below 20V
 | 3.3 | Alert shall be generated when temperature exceeds 20oC
 | 3.4 | Alert shall be generated when temperature drops below 0oC
4 |  | System shall continue operation after sanitization & bagging process performed by customer
 | 4.1 | System shall survive dry nitrogen purging at room temperature and a pressure of 2psi
 | 4.2 | System shall remain intact during vacuum and heat sealing process
5 |  | System shall transmit and receive data wirelessly
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 45: Requirements Continued
FR | DR | Requirement
 | 5.1 | Data communication process shall be autonomous
 | 5.2 | System shall send/receive voltage measurements to on-site system wirelessly
 | 5.3 | System shall send/receive temperature measurements to on-site system wirelessly
 | 5.4 | System shall send signals through the K470 Universal Aluminum Box (provided by the customer) that the battery is stored in
 | 5.4.1 | System shall send signals through a secondary K470 Universal Aluminum Box next to the one it is being stored in
 | 5.5 | Data shall be transmitted over a distance of at least three feet
6 |  | System shall be battery-powered
 | 6.1 | External battery shall operate for one year without charging
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 46: Requirements Continued
FR | DR | Requirement
 | 6.2 | External battery shall draw negligible charge from stored battery
7 |  | System shall save received data with a timestamp
 | 7.1 | System shall save raw data
 | 7.1.1 | System shall save specific voltage and temperature values, so long as requirement 7.1 is met
 | 7.2 | Data shall be sent once an hour by default configuration
 | 7.2.1 | System shall have a configurable transmission frequency option
 | 7.2.1.1 | A user interface shall be made to input configuration changes
 | 7.3 | Data shall be presented in a .txt file
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 47: Communication Signal Trade Study
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 48: Processor Trade Study
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 49: Power Source Trade Study
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 50: Voltage Sensor Trade Study
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 51: Temperature Sensor Trade Study
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 52: Noise Avoidance
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 53: nRF5340[14]
Link to datasheet
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 54: nRF52840[15]
Link to datasheet
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 55: nRF52805[16]
Link to datasheet
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 56: Additional Power Draw Simulations
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 57: Current Draw Derivation
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 58: Detailed Current Estimates
Wake time current draw source: https://devzone.nordicsemi.conordic/power/w/opp/2/online-power-profiler-for-ble
77uA
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 59: Adafruit[1],[11]
Specification
Compatible with 3V and 5V logic
Can measure DC current up to +15A
Can measure DC voltages up to +36V
  Not for use with AC voltages
Measurements taken with better than 1% accuracy
Uses an INA260 chip
  Operates from a 2.7 to 5.5V supply
  Draws 310μA (typical) of supply current
Voltage across an integrated 2mΩ, 0.1% shunt resistor is measured by the internal 16-bit ADC
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 60: DFRobot[2]
Specification
Input Voltage (VCC) : 3.3V~5.5V
  Voltage Range (IN+ or IN- relative to GND): 0 ~ 26 V
  Voltage Resolution: 4 mV
  Voltage Relative Error: <±0.2% (Typical)
  Current Range: 0 ~ ±8A (Bidirectional current)
  Current Resolution: 1mA
  Current Relative Error: <±0.2% (Typical, manual calibration required)
  Power Range: 0 ~ 206 W
  Power Resolution: 20 mW (Hardware) / 4 mW (Software)
  Quiescent Current: 0.7 mA
  Interface: Gravity I2C (logic level: 0-VCC)
  I2C Address: Four options 0x40, 0x41, 0x44, 0x45
Dimension: 30.0mm*22.0mm
Weight: 4g
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 61: Team Design - Resistors[3],[4]
or 4.7 kOhms
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 62: Team Design - Buffer[5]
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 63: Voltage Divider Transfer Function and Power Calculations
Power
  P = 0.125W = V2/R so V = (PR)0.5
  R1 = 20kΩ so Vmax = (0.125*20000)0.5 = 50V
  R2 = 4.7kΩ so Vmax = (0.125*4700)0.5 = 24.24V
Circuity
  Voltage divider with R1 = 20kΩ and R2 = 4.7kΩ
  So Vint=((R2)/(R1+R2))*Vin
  Same voltage divider used for all three sensor circuits
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 64: Accuracy Calculations with Added Voltage Divider
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup
Actual Voltage (V1)
  Random value from 20 to 33.6V
Expected Resistances
  R1,exp= 20kΩ
  R2,exp= 4.7kΩ
Expected Intermediate Voltage (V2,exp)
  V2,exp = (R2,exp*V1) / (R1,exp + R2,exp)
Resistor Tolerances (R1,tol, R2,tol)
  Random values from -0.25% to +0.25%
Actual Resistances (R1,act, R2,act)
  R1,act = R1,exp + R1,exp * R1,tol
  R2,act = R2,exp + R2,exp * R2,tol
Actual Intermediate Voltage (V2,act)
  V2,act = (R2,act*V1) / (R1,act + R2,act)
Sensor Percent Error (E)
  Random value from -1% to +1%
Intermediate Voltage Error (VI)
  VI = V2,act*E
Measured Voltage (V3)
  V3 = V2,act + VI
Absolute Voltage Error (VE)
  VE = V3 - V2,exp
**See Slide 27 for Schematic

## Slide 65: Measured Voltage Accuracy for DFRobot
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 66: Measured Voltage Accuracy for Team Designed Voltage Sensor
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 67: Texas Instruments TMP117[12]
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup

## Slide 68: Smartec SMT172[13]
Presentation Outline Project Description Feasibility Analysis Status Summary & Remaining Studies References & Backup