## Slide 1: SBMS Stored Battery Monitoring System Critical Design Review December 1st, 2021 ASEN 4018-012 Team 6 Customer: EnerSys ABSL Presenters: Ian Adler, Ben Gavin, Devin Geegan, Jamie Henault, Evan Meany, Nathan Zhao Additional Team Members: Richard Folsom, Joseph Harrell, Shreeyash Nadella

## Slide 2: Presentation Outline
Project Purpose and Objectives
Design Solution
Critical Project Elements
Design Requirements Satisfaction
  Wireless Communication & Software Design
  Sensors & Electrical Design
  External Power Source
Project Risks
Verification and Validation
Project Planning
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 3: Project Purpose and Objectives

## Slide 4: Project Motivation
EnerSys ABSL batteries
  Storage
  Health Deterioration
Quality checks
  Bagging Process
  Time-consuming
Mission Statement:
  SBMS shall measure the voltage of an 8S3P battery and the temperature of the 8S3P’s environment and wirelessly send this data to an on-site system
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 5: Concept of Operations (CONOPS)
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 6: Design Solution

## Slide 7: Baseline Design (Storage)
K470 Zarges Box
Styrofoam Layer
Heat/Vacuum Sealed Bag
Monitoring System
SMT172
SMT172
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
25-pin dsub connector

## Slide 8: Baseline Design (Monitoring System)
Custom
PCB
nrf52840
Bluetooth Low Energy
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
nrf52840
MakerFocus 10000 mAh Lithium Polymer Battery
PCB with built-in voltage sensor and connections to 8S3P & SMT172 temp sensors
Top-Down View
Side View
MakerFocus 10000 mAh Lithium Polymer Battery
MiniBoost 5V

## Slide 9: Baseline Design (Monitoring System)
Top-Down View
Side View
110 mm
70 mm
60 mm
100 mm
76.2 mm
15.24 mm
46.04 mm
110 mm
50 mm
11 mm
16.8 mm
21.9 mm
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
50.8 mm

## Slide 10: EnerSys Storage Schematic
On-site computer is 3-15 ft from the stored battery
Temperature conditions are ~58°F (15°C)
Secondary Nordic dongle plugged into customer computer
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 11: Functional Block Diagram (FBD)
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 12: Critical Project Elements

## Slide 13: System Critical Project Elements
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
CPE | Description | FR
CPE1 | System shall measure temperature and voltage. | FR1, FR2
CPE2 | System shall have the necessary hardware for wireless communication. | FR5
CPE3 | System shall have the necessary software for wireless communication. | FR3, FR5, FR7
CPE4 | All parts of system shall integrate with one another. | All FRs
CPE5 | System shall be battery-powered. | FR6
CPE6 | System shall be validated for functionality. | All FRs

## Slide 14: Design Requirements Satisfaction

## Slide 15: Driving Requirements
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
FR | Description | Satisfied?
1 | System shall measure voltage | 
2 | System shall measure temperature | 
5 | System shall transmit and receive data wirelessly | 
6 | System shall be battery-powered | 
7 | System shall save received data with a timestamp | 

## Slide 16: Wireless Communication Critical Experiments/Analyses
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
FR | Description | Satisfaction Strategy
5 | Wireless Communication | Simulate the design environment to ensure sufficient signal strength and analyze the feasibility of data rate/packet size
7 | Data Saving | Demonstrate scope of the code

## Slide 17: DR 5.4 & 5.5 Satisfaction [Communications Experiment]
Flashed code to advertise out of ZARGES case
Tested the signal strength at different distances and transmission strengths
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
DR 5.4: System shall send signals through the K470 Universal Aluminum Box
DR 5.5: Data shall be transmitted over a distance of at least three feet

## Slide 18: DR 5.2 & 5.3 Satisfaction [BLE Data Packet Format]
1B Preamble
4B Access Address
Protocol Data Unit
  2B Header
  4B MIC
  1B OP
  16B UUID
  2B Length, Type
  4B Volt/Temp Data
3B CRC
~37B Total
250 kbps Data Rate
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
DR 5.2: System shall send/receive voltage measurements to on-site system wirelessly
DR 5.3: System shall send/receive temperature measurements to on-site system wirelessly
BLE Packet Format[22]

## Slide 19: DR 5.1, 7.1, & 7.2 Satisfaction [In-Box Code Flow]
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
DR 5.1: Data communication process shall be autonomous
DR 7.1: System shall save raw data
DR 7.2: Data shall be sent once an hour by default configuration

## Slide 20: DR 5.1, 7.1, & 7.2 Satisfaction [On-Site Code Flow]
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
DR 5.1: Data communication process shall be autonomous
DR 7.1: System shall save raw data
DR 7.2: Data shall be sent once an hour by default configuration

## Slide 21: Communication Requirement Satisfaction Summary
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
DR | Description | Satisfied?
5.1 | Autonomous Communication | Code flowchart achieves autonomy
5.2/5.3 | Send/Receive Voltage and Temperature | System will be able to send usable values through the ADC and the size of this data fits within the BLE framework
5.4 | Transmit Through K470 Box | Communications experiment showed signal could transmit through ZARGES case
5.5 | Transmit 3 Feet | Communications experiment showed that the signal strength was usable for all strengths at 3ft
7.1 | Save Raw Data | Code flowchart shows that on-site device will communicate with computer through serial ports
7.2 | Data Sent Every Hour | Handled by watchdog timer within code flowchart

## Slide 22: Electronics and Power Source Critical Analyses
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
FR | Description | Satisfaction Strategy
1 | Voltage Sensor | Measurement accuracy analyzed using error model
2 | Temperature Sensor | Measurement range and accuracy guaranteed by manufacturer
6 | Power Circuit | Current draw from customer battery analyzed using MOSFET datasheet and circuit calculations

## Slide 23: Electrical Wiring Diagram
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 24: Circuit Schematic
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 25: PCB Design
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 26: DR 1.1, 1.2, 2.1 & 2.2 Satisfaction [Sensor Range & Accuracy]
DR 1.1: Voltage sensor shall have a range of at least 20-33.6V
DR 1.2: Voltage sensor shall have a sensitivity of 0.1V
DR 2.1: Temperature sensor shall have a range of at least 0-20oC
DR 2.2: Temperature sensor shall have a sensitivity of 0.1oC
Temperature Error Chart From Manufacturer[4]:
Voltage Sensor Error Model Results:
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 27: DR 6.1 Satisfaction [Power Supply Lifetime]
System will have a backup battery selected with a digitally controlled SPDT IC switch
Switch output will be fed into a voltage sensor so the processor can monitor its power source
The MAX4544 chip is ideal with its nanoamp supply and leakage currents[16]
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
DR 6.1: External battery shall operate for one year without charging

## Slide 28: DR 6.1 Satisfaction [Power Supply Lifetime] (cont.)
To limit power consumption during sleep, a MOSFET will cut off power to the temperature sensors
The MOSFET in the power source voltage sensor will only be on for the duration required to make a measurement
The buffers in the voltage sensors can be shut down so the sensor circuits draw reduced power when not measuring
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
DR 6.1: External battery shall operate for one year without charging

## Slide 29: DR 6.2 Satisfaction [Negligible Draw from Stored Battery]
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Assume MOSFET always leaking:
  MOSFET ZGVD current <= 1uA[15]
  1uA * 24hr/day * 365 day/yr = 8.8mAh/yr
Assume voltage sensor on 1 min/hr:
  24V / 1.118MΩ = 21uA
  21uA * 24hr/day * 365 day/yr / 60 = 3.1mAh/yr
Max allowable current draw = 23mAh/yr
  8.8mAh/yr + 3.1mAh/yr = 11.9mAh/yr
DR 6.2: External battery shall draw negligible charge from stored battery

## Slide 30: Sensor/Circuitry Requirement Satisfaction Summary
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
DR | Description | Satisfied?
1.1 | 20 to 33.6V Range | Resistors bring this range into the acceptable ADC input range
1.2 | 100mV Accuracy | Voltage error model
1.3 | System - Battery Connection | Connector provided by customer will be wired to SBMS
1.4 | DC Voltage Measurements | Voltage sensor converts DC input to DC signal for ADC
2.1 | 0 to 20°C Range | Guaranteed by manufacturer
2.2 | 0.1°C Accuracy | Guaranteed by manufacturer over desired range
2.3 | Measures Battery Environment | Sensors will be taped against battery chassis at multiple points
6.1 | Power Supply Lifetime | Sensors shut down during sleep cycles / backup battery
6.2 | Low Draw from Stored Battery | Power draw calculations

## Slide 31: Power System Analysis/Experiment
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
FR | Description | Satisfaction Strategy
6 | Power Supply Lifetime | Power Modeling, Experimental Validation, Redundancy

## Slide 32: DR 6.1 Satisfaction [Power Supply Lifetime] - Current Draws
 | Current [mA] | Sources or Justification
Voltage Sensor + Peripherals | 0.010 (on) 0.003 (off) | LTC2063[14] & FDV303N[24] Datasheets
Temp. Sensor + Peripherals | 0.120 (on) 0.002 (off) | SMT172 Datasheet Active Draw[4]
Board - Wake | 6.400 | Nordic Semiconductors Datasheet, pg 62
Board - Sleep | 0.00084 | Nordic Semiconductors Datasheet, pg 59
Total - Wake | 6.530 | Calculated
Total - Sleep | 0.123 | Calculated
Required Yearly Supply | 1,240 mAh | Calculated:
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
DR 6.1 External battery shall operate for one year without charging

## Slide 33: DR 6.1 Satisfaction [Power Supply Lifetime] - Current Draws
 | Loss | Multiplier | Battery Size Required [mAh] | Sources or Justification
Required Supply | - | - | 1,240 | Prev. Slide
Low-Temp | 0% | 1 | 1,240 | Storage temp (58oF) is not cold enough to affect capacity
Temporal | 60% | 2.5 | 3,100 | ~5% loss in capacity per month
Discharge | 20% | 1.25 | 3,875 | ~80% of rated capacity is usable; Experimental validation
Converter | 20% | 1.25 | 4,844 | Boost 3.7V -> 5V Buck 5V -> 3.3V
FOS | - | 2 | 9,688 | -
Desired Size: | - | - | 10,000 mAh | -
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
DR 6.1 External battery shall operate for one year without charging
Selected Battery: MakerFocus 10,000 mAh Lithium Polymer Battery

## Slide 34: DR 6.1 Satisfaction [Power Supply Lifetime] - Battery Capacity
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
1000mAh Battery
Keithley 2460 Sourcemeter
DR 6.1 External battery shall operate for one year without charging

## Slide 35: Power System Requirement Satisfaction
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
DR | Name | Satisfied?
6.1 | Power Supply Lifetime | Battery with required size chosen based on power model and expected capacity proved by experimental modeling

## Slide 36: Driving Requirements Satisfaction
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
FR | Description | Satisfied?
FR1 | System shall measure voltage | Yes
FR2 | System shall measure temperature | Yes
FR5 | System shall transmit and receive data wirelessly | Yes
FR6 | System shall be battery-powered | Yes
FR7 | System shall save received data with a timestamp | Yes

## Slide 37: Project Risks

## Slide 38: Risk Scoring
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Severity Level | Definition
Minimal (1) | DRs & FRs Met
Minor (2) | 1 DR Failed
Major (3) | Multiple DRs Failed Under One FR
Serious (4) | Multiple DRs Failed Under Multiple FRs
Catastrophic (5) | FR(s) Failed
Numerical Value | Risk Level
1-3 | Acceptable Risk
4-6 | Requires Monitoring
8-12 | Requires Constant Mitigation
15-25 | Unacceptable Risk
Likelihood Level
Extremely Improbable (1)
Low Likelihood (2)
Likely (3)
Highly Likely (4)
Almost Certain (5)
x
=

## Slide 39: Risk Table
Risk ID | Risk Description | Effect | Likelihood | Severity
1 | NRF development board backordered | Will be difficult to debug code, which could lead to various design requirement failures | 2 | 4
2 | Temperature chamber at EnerSys cannot be used | Temperature range requirement cannot be verified | 4 | 2
3 | Wireless communication with on-site system fails due to an obstruction | Data cannot be received by on-site system for processing | 2 | 5
4 | External battery has lower capacity than stated by manufacturer/system draws more power than expected | Battery will be drained sooner than expected, causing the whole system to die | 3 | 5
5 | Unable to interface with customer computer due to computer state | Data will be received, but it cannot be saved to on-site system and sent to customer | 4 | 5
6 | Temperature sensor backordered | Unable to measure temperature of the system | 3 | 5
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 40: Risk Matrix (Pre-Mitigation)
Almost Certain |  |  |  |  | 
Highly Likely |  | 2 |  |  | 5
Likely |  |  |  |  | 4, 6
Low Likelihood |  |  |  | 1 | 3
Extremely Improbable |  |  |  |  | 
 | Minimal | Minor | Major | Serious | Catastrophic
Severity
Likelihood
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Key
NRF development board backordered
EnerSys temp chamber unusable
Wireless communication failure
External battery failure
Computer interface failure
Temp sensor backordered

## Slide 41: Risk Matrix for Risk ID 1 (Post-Mitigation)
Almost Certain |  |  |  |  | 
Highly Likely |  |  |  |  | 
Likely |  |  |  |  | 
Low Likelihood | 1 |  |  | 1 | 
Extremely Improbable |  |  |  |  | 
 | Minimal | Minor | Major | Serious | Catastrophic
Likelihood
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Risk: NRF development board backordered
Mitigation Strategy: Order ASAP and use existing hardware owned by team members
Outcome: Debugging can be done early on with existing hardware, allowing the system to be tested before additional boards arrive, so design requirements can be met with confidence
Severity

## Slide 42: Risk Matrix for Risk ID 2 (Post-Mitigation)
Almost Certain |  |  |  |  | 
Highly Likely | 2 | 2 |  |  | 
Likely |  |  |  |  | 
Low Likelihood |  |  |  |  | 
Extremely Improbable |  |  |  |  | 
 | Minimal | Minor | Major | Serious | Catastrophic
Severity
Likelihood
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Risk: Temperature chamber at EnerSys cannot be used
Mitigation Strategy: Rent temperature chamber from Espec for nearly $1,000
Outcome: Major increase in project budget, but temperature range can be verified

## Slide 43: Risk Matrix for Risk ID 3 (Post-Mitigation)
Almost Certain |  |  |  |  | 
Highly Likely |  |  |  |  | 
Likely |  |  |  |  | 
Low Likelihood | 3 |  |  |  | 3
Extremely Improbable |  |  |  |  | 
 | Minimal | Minor | Major | Serious | Catastrophic
Severity
Likelihood
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Risk: Wireless communication failure
Mitigation Strategy: Store data to flash memory of in-box controller until communication is possible; increase signal power to blast through obstruction
Outcome: Sensor measurements still accounted for and will be received once communication with on-site system is reestablished

## Slide 44: Risk Matrix for Risk ID 4 (Post-Mitigation)
Almost Certain |  |  |  |  | 
Highly Likely |  |  |  |  | 
Likely |  |  |  |  | 4
Low Likelihood |  |  |  |  | 
Extremely Improbable | 4 |  |  |  | 
 | Minimal | Minor | Major | Serious | Catastrophic
Severity
Likelihood
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Risk: External battery failure
Mitigation Strategy: Test battery prior to integration to ensure that discharge curve is as expected Include safety factor of 2 Include a backup battery
Outcome: Reduced likelihood as battery is truly larger than needed, and reduced severity as there is a backup

## Slide 45: Risk Matrix for Risk ID 5 (Post-Mitigation)
Almost Certain |  |  |  |  | 
Highly Likely |  |  |  |  | 5
Likely |  |  |  |  | 
Low Likelihood |  |  |  |  | 
Extremely Improbable |  |  |  |  | 5
 | Minimal | Minor | Major | Serious | Catastrophic
Severity
Likelihood
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Risk: Computer interface failure
Mitigation Strategy: Ensure computer is constantly plugged in/charging and that sleep mode has been disabled
Outcome: Customer computer will not be able to enter power saving sleep mode, but will successfully receive data

## Slide 46: Risk Matrix for Risk ID 6 (Post-Mitigation)
Almost Certain |  |  |  |  | 
Highly Likely |  |  |  |  | 
Likely | 6 |  |  |  | 6
Low Likelihood |  |  |  |  | 
Extremely Improbable |  |  |  |  | 
 | Minimal | Minor | Major | Serious | Catastrophic
Severity
Likelihood
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Risk: Temperature sensor backordered
Mitigation Strategy: Have a backup chip (TMP117)
Outcome: System will be able to measure temperature, but our team will have to port an arduino library to the NRF hardware which will require additional coding

## Slide 47: Risk Matrix (Post-Mitigation) Summary
Almost Certain |  |  |  |  | 
Highly Likely | 2 |  |  |  | 
Likely | 6 |  |  |  | 
Low Likelihood | 1, 3 |  |  |  | 
Extremely Improbable | 4 |  |  |  | 5
 | Minimal | Minor | Major | Serious | Catastrophic
Severity
Likelihood
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Key
NRF development board backordered
EnerSys temp chamber unusable
Wireless communication failure
External battery failure
Computer interface failure
Temp sensor backordered

## Slide 48: Verification and Validation

## Slide 49: Subsystem Verification - Sensors
DR 1.2: Voltage sensor shall have a sensitivity of 0.1V
DR 2.2: Temperature sensor shall have a sensitivity of 0.1oC
Objective
  Calibrate software to sensors
  Confirm both sensors work within accuracy tolerance
  Compare with error models
Plan
  Input power supply voltage into sensor then measure output with multimeter then check that measurements are within ±0.1V of one another
  Record temperature measured by sensor and by F150 precision thermometer, then check that measurements are within ±0.1oC of one another
Measurements
  Voltage of power supply at 20V, 25V & 33.6V
  Temperature of room and controlled chamber
Pass Criteria
  Both sensor measurements are within sensitivity tolerance
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 50: Subsystem Verification - Physical Integrity
DR 4.1: System shall survive dry nitrogen purging at room temperature and a pressure of 2psi
DR 4.2: System shall remain intact during vacuum and heat sealing process
Objective
  Maintain system functionality after passing through a cleaning environment
Plan
  Attach system to battery and insert into a bag
  Remove air from bag and then seal bag shut by applying heat
Measurements
  Voltage and temperature measurements of system in bag
Pass Criteria
  Measurements are taken while inside vacuum and heat sealed environment
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 51: Subsystem Verification - Communication Signal
Objective
  Establish and maintain communication with receiver outside of K470 box
  Compare with experiment
Plan
  Attach system to battery and insert into K470 box
  Take measurements with system then send measurements through K470 using BLE
Measurements
  Voltage and temperature measurements of system inside box
Pass Criteria
  Measurements taken inside K470 box are transmitted via BLE to receiver outside of K470 box
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
DR 5.4: System shall send signals through the K470 Universal Aluminum Box (provided by the customer) that the battery is stored in

## Slide 52: Subsystem Verification - Alert System
FR 3: System shall communicate when voltage and/or temperature reach an undesirable state
Objective
  Communicate with customer when an undesired state is reached
Plan
  Attach system to placeholder battery and insert into a temperature chamber to reach undesirable temperature levels
  Attach system to a voltage supply to reach undesirable voltage levels
Measurements
  Voltage and temperature measurements of system
Pass Criteria
  Measurements taken while inside an undesirable state will issue a warning to the customer
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 53: Subsystem Verification - Power Supply
DR 6.1: External battery shall operate for one year without charging
Objective
  Maintain system functionality for one year of use without charging/changing power supply
  Compare with power model
Plan
  Attach battery to Keithley 2460 SourceMeter and apply resistance for discharge over a chosen time
Measurements
  Discharge curve in volts vs mAh
Pass Criteria
  Battery is shown to provide power for chosen fraction of one year when enduring scaled amount of the estimated total load
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 54: System Validation - Day In The Life
Objective
  Simulate a 24 hour period that the system would undergo in typical use
Plan
  Attach system to battery and insert into K470 box
  Take measurements with system then send measurements through K470 using BLE
  Continue for 24 hours with no human intervention
Measurements
  Voltage and temperature measurements of system inside box
Pass Criteria
  Measurements taken inside K470 box are transmitted via BLE to receiver outside of K470 box over entire period
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 55: Project Planning

## Slide 56: Work Breakdown Structure (WBS)
SBMS
Project Management
Fall Final Report
Test Readiness Review
AIAA Conference Paper
Spring Final Review
Project Final Report
Testing
Voltage
Temperature
Power
Alerts
Configurability
Communication Signal
Survivability
Day-in-the-life (On-Campus)
Day-in-the-life (EnerSys)
Electronics & Hardware
Ordering
Breadboard Prototyping
PCB Integration
System Container Printing
Software
In-Box Processing
In-Box Dongle
In-Box Configuration
On-Site Data Processing
On-Site Dongle
On-Site Configuration
On-Site GUI
Communication Timing
Advertising
Battery Relay
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 57: Spring Semester Work Plan
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 58: Spring Semester Work Plan: First Month
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 59: Cost Plan
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 60: Cost Plan
(mls)
(mls)
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 61: Test Plan
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Test Name | CPE Addressed
Sensor Functionality | 1
Survivability | 4
Communication Signal | 2,3
Alert System | 1,2,3
Power Supply | 5
Scheduling
Location | Anticipated Date | Hazards or Challenges
Electronics Lab | February 2022 | Calibrating measurement system
Pilot Lab | April 2022 | Achieving a perfect vacuum seal
Pilot Lab | March 2022 | N/A
Pilot Lab | February 2022 | N/A
Electronics Lab | March 2022 | N/A

## Slide 62: Test Plan
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Test Name | CPE Addressed
Full System Test | All
Day In The Life | All
Handover | All
Scheduling
Location | Anticipated Date | Hazards or Challenges
Electronics Lab | April 2022 | N/A
Electronics Lab | April 2022 | Maintaining test environment overnight
EnerSys Facilities | April 2022 | Transmitting through several K470 boxes if needed

## Slide 63: Acknowledgements
EnerSys ABSL Team
Jacqueline Maldonado, Brice Lucero, Travis Mault, Ryan Pritchard
Team Advisor
Dr. Jean Koster
Projects Advisory Board
Dr. Jelliffe Jackson, Dr. Jade Morton, Dr. Christopher Roseman,
Dr. Jean Koster, Dr. Melvin Rafi, Professor Matt Rhode
Additional Support
Professor Trudy Schwartz, Professor Bobby Hodgkinson,
Emma Markovich, Colin Claytor
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 64: References
“ERA3AEB113V,” Newark. Available: https://www.newark.com/panasonic-electronic-components/era3aeb113v/surface-mount-thin-film-resistor/dp/62W8736
“ERA-3AEB302V,” Mouser. Available: https://www.mouser.com/ProductDetail/Panasonic/ERA-3AEB302V?qs=%2Fha2pyFaduhb05ESoU1Edd%252B%252BYQj5NEVJ4yV8H3JHdTrOH%252BIkW8jYRA%3D%3D
“TMP117 Datasheet,” Texas Instruments, Revised April 2021. Available: https://www.ti.com/product/TMP117
“SMT172 Datasheet,” Smartec, Last Updated March 20, 2017. Available: https://www.smartec-sensors.com/cms/media/Datasheets/Temperature/SMT172-datasheet.pdf
“nRF52840,” Nordic Semiconductors. Available: https://www.nordicsemi.com/-/media/Software-and-other-downloads/Product-Briefs/old-versions/nRF52840PBv20.pdf?la=en&hash=516968A8D06D7F41C8B14B6639DD9E14099E2853
“Air - Thermal Conductivity vs. Temperature and Pressure.” Engineering ToolBox. Available: https://www.engineeringtoolbox.com/air-properties-viscosity-conductivity-heat-capacity-d_1509.html
“Thermal Conductivity of Metals, Metallic Elements and Alloys.” Engineering ToolBox. Available: https://www.engineeringtoolbox.com/thermal-conductivity-metals-d_858.html
“Properties of Silicon and Silicon Wafers.” El,Available: https://www.el-cat.com/silicon-properties.htm
“The Thermal Conductivity of Unfilled Plastics – C-Therm Technologies Ltd..” C, 10 Dec. 2020/ Available: https://ctherm.com/resources/newsroom/blog/the-thermal-conductivity-of-unfilled-plastics/
Measurement of the Effective Radial Thermal ... - NASA. Available: https://tfaws.nasa.gov/wp-content/uploads/TFAWS18-IN-08_Paper.pdf
Townsend, Kevin. “Introduction to Bluetooth Low Energy.” Adafruit Learning System. Available: https://learn.adafruit.com/introduction-to-bluetooth-low-energy/gatt
“RF Wireless World.” BLE Advertising Packet Format | BLE Data Packet Format, Available: https://www.rfwireless-world.com/Terminology/BLE-Advertising-and-Data-Packet-Format.html
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 65: References (cont.)
13. “MCS0402MD1004BE000,” Digikey. Available: https://www.digikey.bg/en/products/detail/vishay-dale/MCS0402MD1004BE000/14324215
14. “LTC2063” Analog Devices. Available: https://www.analog.com/en/products/ltc2063.html#product-overview
15. “FDV303N - Digital FET” ON Semiconductor. Available: https://www.onsemi.com/pdf/datasheet/fdv303n-d.pdf
16. “MAX4544” Maxim Integrated. Available: https://www.maximintegrated.com/en/products/analog/analog-switches-multiplexers/MAX4544.html
17. “RP73PF1E118KBTD,” Digikey. Available: https://www.digikey.com/en/products/detail/te-connectivity-passive-product/RP73PF1E118KBTD/8261060
18. “10,000 mAh Battery”, Makerfocus. Available: https://www.makerfocus.com/products/makerfocus-3-7v-lipo-battery-10000mah-lithium-rechargeable-battery-9065115-with-micro-ph2-0-plug-for-raspberry-pi-ups-board?_pos=1&_sid=6a377f236&_ss=r
19. “CGA3E2X7R1H104K080AA,” Digikey. Available: https://www.digikey.com/en/products/detail/tdk-corporation/CGA3E2X7R1H104K080AA/2443144
20. “61301011821,” Mouser. Available: https://www.mouser.com/ProductDetail/Wurth-Elektronik/61301011821?qs=W%252B2sBeLta1ZhlLR0YCzonQ%3D%3D
21. “Adafruit MiniBoost 5V @ 100mA Charge Pump - AP3602A,” Adafruit. Available: https://www.adafruit.com/product/3661?gclid=Cj0KCQiA7oyNBhDiARIsADtGRZZnpuExyqBrbn59R64kl9sqkQ00pMlgd3CpbBy_UVoWxRPjFBfqlyYaAh3SEALw_wcB
22. Lindh, J., “Bluetooth low energy Beacons,” Texas Instruments. Available:
https://www.ti.com/lit/an/swra475a/swra475a.pdf?ts=1638134655301&ref_url=https%253A%252F%252Fwww.google.com%252F
23. “JST Right-Angle Connector - Through-Hole 2-Pin,” Sparkfun. Available: https://www.sparkfun.com/products/9749
24. “onsemi FDV303N,” LCSC Electronics. Available: https://lcsc.com/product-detail/MOSFETs_onsemi-FDV303N_C80498.html
25. “Student PCB Sponsorship & Discounts,” Advanced Circuits. Available: https://www.4pcb.com/pcb-student-discount.html
26. “PLA,” MakerBot. Available: https://store.makerbot.com/3d-printers-materials/method-spools/pla-material
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 66: References (cont.)
27. “8 inch 200mm Impulse Bag Sealer, Manual Bag Sealer Heat Seal Closer, Adjustable Timer Electric Heat Seal Closer Packaging Sealer with 2 Free Replacement Kit, Blue,” Amazon. Available: https://www.amazon.com/Impulse-Sealer-Adjustable-Electric-Replacement/dp/B08GCBNN9W/
28. “GERYON Vacuum Sealer, Automatic Food Sealer Machine for Food Savers w/Starter Kit|Led Indicator Lights|Easy to Clean|Dry & Moist Food Modes| Compact Design (Black),” Amazon. Available: https://www.amazon.com/GERYON-Automatic-Machine-Starter-Indicator/dp/B07B4X61Z4/ref=sr_1_5?keywords=vacuum%2Bsealer&qid=1638161536&sr=8-5&th=1
29. “Saleae Logic Pro 8,” Saleae. Available: https://usd.saleae.com/products/saleae-logic-pro-8?variant=7076781686844
30. ”Nordic Semiconductor USB CDC ACM” Nordic Infocenter. https://infocenter.nordicsemi.com/index.jsp?topic=%2Fcom.nordic.infocenter.sdk5.v15.2.0%2Fusbd_cdc_acm_example.html
31. “PySerial” Python. https://pyserial.readthedocs.io/en/latest/
32. “Simple Mail Transfer Protocol” Python. https://docs.python.org/3/library/smtplib.html
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 67: Thank You! Questions?

## Slide 68: Backup Slides

## Slide 69: SBMS Organizational Chart
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Project Manager
Jamie Henault
Finance Lead
Richard Folsom
Customer
EnerSys ABSL
Advisor
Dr. Jean Koster
Systems Engineer Lead
Nathan Zhao
Power Lead
Ian Adler
Data Processing Lead
Joseph Harrell
Testing/Validation Lead
Devin Geegan
Sensor + Hardware Lead
Ben Gavin
Communications Lead
Evan Meany
Commands Lead
Shreeyash Nadella
Subteam
Nathan Zhao
Shreeyash Nadella
Joseph Harrell
Subteam
Nathan Zhao
Ben Gavin
Richard Folsom
Joseph Harrell
Subteam
Nathan Zhao
Ben Gavin
Devin Geegan
Evan Meany
Subteam
Jamie Henault
Richard Folsom
Subteam
Ian Adler
Jamie Henault
Richard Folsom
Shreeyash Nadella
Subteam
Nathan Zhao
Ian Adler
Joseph Harrell
Evan Meany

## Slide 70: Requirements
FR | DR | Requirement
1 |  | System shall measure voltage
 | 1.1 | Voltage sensor shall have a range of at least 20-33.6V
 | 1.2 | Voltage sensor shall have a sensitivity of 0.1V
 | 1.3 | Voltage sensor shall connect to the customer’s 8S3P battery
 | 1.4 | Voltage sensor shall measure DC voltage
2 |  | System shall measure temperature
 | 2.1 | Temperature sensor shall have a range of at least 0-20oC
 | 2.2 | Temperature sensor shall have a sensitivity of 0.1oC
 | 2.3 | Temperature sensor shall measure the temperature of the battery environment
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 71: Requirements Continued
FR | DR | Requirement
3 |  | System shall communicate when voltage and temperature reach an undesirable state
 | 3.1 | Alert shall be generated when voltage exceeds 33.6V
 | 3.2 | Alert shall be generated when voltage drops below 20V
 | 3.3 | Alert shall be generated when temperature exceeds 20oC
 | 3.4 | Alert shall be generated when temperature drops below 0oC
4 |  | System shall continue operation after sanitization & bagging process performed by customer
 | 4.1 | System shall survive dry nitrogen purging at room temperature and a pressure of 2psi
 | 4.2 | System shall remain intact during vacuum and heat sealing process
5 |  | System shall transmit and receive data wirelessly
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 72: Requirements Continued
FR | DR | Requirement
 | 5.1 | Data communication process shall be autonomous
 | 5.2 | System shall send/receive voltage measurements to on-site system wirelessly
 | 5.3 | System shall send/receive temperature measurements to on-site system wirelessly
 | 5.4 | System shall send signals through the K470 Universal Aluminum Box (provided by the customer) that the battery is stored in
 | 5.4.1 | System shall send signals through a secondary K470 Universal Aluminum Box next to the one it is being stored in
 | 5.5 | Data shall be transmitted over a distance of at least three feet
6 |  | System shall be battery-powered
 | 6.1 | External battery shall operate for one year without charging
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 73
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Requirements Continued
FR | DR | Requirement
 | 6.2 | External battery shall draw negligible charge from stored battery
7 |  | System shall save received data with a timestamp
 | 7.1 | System shall save raw data
 | 7.1.1 | System shall save specific voltage and temperature values, so long as requirement 7.1 is met
 | 7.2 | Data shall be sent once an hour by default configuration
 | 7.2.1 | System shall have a configurable transmission frequency option
 | 7.2.1.1 | A user interface shall be made to input configuration changes
 | 7.3 | Data shall be presented in a .txt file

## Slide 74: Voltage Sensor Error Setup & Requirements
DR 2.1 | Voltage sensor shall have a sensitivity of 0.1V
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
8S3P[13][17]
R1 = 1MΩ
R2 = 118kΩ
Vmax(1) = 50V
Vmax(2) = 200V
Pmax(1,2) = 0.1W
External Battery[1][2]
R1 = 11kΩ
R2 = 3kΩ
Vmax(1,2) = 75V
Pmax(1,2) = 0.1W

## Slide 75: Voltage Sensor Error Calculations
Actual Voltage (V1)
  Random value from 20 to 33.6V
Expected Resistances
  R1,exp= 1MΩ
  R2,exp= 118kΩ
Expected Intermediate Voltage (V2,exp)
  V2,exp = (R2,exp*V1) / (R1,exp + R2,exp)
Resistor Tolerances (R1,tol, R2,tol)
  Random values from -1% to +1%
Actual Resistances (R1,act, R2,act)
  R1,act = R1,exp + R1,exp * R1,tol
  R2,act = R2,exp + R2,exp * R2,tol
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Actual Intermediate Voltage (V2,act)
  V2,act = (R2,act*V1) / (R1,act + R2,act)
Op-amp Error (Vop,err)
  Random value from -5μV to +5μV
Actual Intermediate Voltage (V3,act)
  V3,act = V2,act + Vop,err

## Slide 76: Voltage Sensor Error Calculations (cont.)
ADC Differential Nonlinearity Error (ED)
  Random Value from -0.95 to +1.3
ADC Integral Nonlinearity Error (EI)
  Random Value from -10 to +10
ADC Gain Error (EG)
  Random Value from -0.03 to +0.03
ADC Total Error (EADC)
  EADC = (ED + EI + EG + 1)*V3,act / 212
Actual Final Voltage (V4,act)
  V4,act = V3,act + EADC
Absolute Voltage Error (VE)
  VE = V4,act - V2,exp
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Absolute Voltage Error Scaled Back up to Input Voltage Range (VE,scaled)
  VE,scaled = (R1,exp + R2,exp)*(VE / R2,exp)

## Slide 77: PCB Isometric View & Voltage Sensor Location
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
External Battery Voltage Sensor
8S3P Customer Battery Voltage Sensor

## Slide 78: Electronics/Hardware Bill of Materials
Component | Product | Source | Price/Unit [$]
Op Amp[14] | LTC2063 | Mouser | 2.92
N-ch MOSFET[15] | FDV303N | LCSC | 0.43
Temp Sensor[4] | SMT172 | Newark/Ebay | 3.79
1M Resistor[13] | MCS0402MD1004BE000 | Digikey | 0.51
118k Resistor[17] | RP73PF1E118KBTD | Digikey | 0.59
3k Resistor[1] | ERA-3AEB302V | Mouser | 0.34
11k Resistor[2] | ERA3AEB113V | Newark | 0.33
Power Converter[21] | MiniBoost 5v | Adafruit | 2.95
Battery Switch[16] | MAX4544 | Digikey | 2.89
Battery Connector | 25-pin Dsub | ABSL | N/A
100nF Capacitor[19] | CGA3E2X7R1H104K080AA | Digikey | 0.10
10-pin Header[20] | 61301011821 | Mouser | 0.68
Power Supply Connector[23] | JST PH2 | Sparkfun | 0.95
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 79: Temp Sensor Configuration
Circuit Board
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Heat Shrink Tubing
Processor
MOSFET
SMT172
G
D
S
V
GND
DATA
GND
GPIO
GPIO
VDD
200 mm

## Slide 80: Smartec SMT172[4] - Chosen Temperature Sensor
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 81: Texas Instruments TMP117[3] - Backup Temperature Sensor
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 82: Temperature Sensor Accuracy Comparison
Sensor | Range (°C) | Accuracy (°C) | Compatibility
TI TMP117[3] | -55 to 150 | 0.1 from -20 to 50 | 1.8 to 5.5V, Digital I2C-SMB Signal
Smartec SMT172[4] | -45 to 130 | 0.1 from -20 to 60 | 2.7 to 5.5V, Digital PWM Signal
TMP117 Accuracy[3]
SMT172 Accuracy[4]
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 83: CAD Housing Unit
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 84: CAD Electronics Compartment
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 85: DR 6.1 Satisfaction - Current Draw Derivation
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 86: DR 6.1 Satisfaction - Detailed Current Estimates
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 87: DR 6.1 Satisfaction - Detailed Current Estimates
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 88: DR 6.1 Satisfaction - Detailed Current Draw Estimates
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 89: DR 6.1 Satisfaction - Detailed Current Loss Estimates
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 90: DR 6.1 Satisfaction - Reconsidering Options - NiMH, Li-ion
NiMH
  large ‘memory effect’, limited reusability
Li-ion
  Marginally Safer, Higher Capacity Per Volume
NiMH will not be considered
Li-ion will be considered alongside Lipo
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 91: DR 6.1 Satisfaction - COTS Choice
 | Battery #1 (LiPo) | Battery #2 (LiPo) | Battery #3 (Li-ion) | Battery #4 (Li-ion)
Cell Capacity [mAh] | 3,700mAh | 10,000mAh | 2000mAh | 3000mAh
Dimensions [in] | 1.3 x 3.8 x 0.4 | 4.4 x 2.6 x 0.3 | 1.34 x 0.63d | 2.8 x 0.7d
Energy [mAh / in3] Density | 1,872 | 2,900 | 1,188 | 728
Meets Requirements (Temp, Size, C rate) | ✔️ | ✔️ | ✔️ | ✔️
Available From | Amazon | Makerfocus, Amazon | Amazon | Amazon
Cost per unit | $61 / (4 pc) | $30 / (1 pc) | $30 / (4 pc) | $34 / (2 pc)
Total Purchase Cost (1 full system) | $122 | $60 | $60 | $136
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 92: Thermal Analysis Requirements
DR 2.1 | Temperature sensor shall have a range of at least 0-20oC
DR 2.3 | Temperature sensor shall measure the temperature of the battery environment
DR 3.3 | Alert shall be generated when temperature exceeds 20oC
With our system operating in the environment of the battery, it cannot generate enough heat to send the system outside of its measurable range. So, the heat generated by SBMS must have a small effect on the temperature of the battery environment to satisfy the three design requirements above.
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 93: Thermal Circuit
Temperature Sensor (8)
Wall
(1)
Wall
(1)
Wall
(1)
Air
(5)
Air
(7)
Connector
(3)
PCB
(4)
Battery
(6)
Battery
(6)
Nordic
(2)
Temperature Sensor (8)
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 94: Thermal Analysis Setup
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Part | Thermal Conductivity [ ] | Area [mm2] | Length [mm]
Wall (1) | kABS = 0.2[9] | 6667.5 | 5
Nordic Dongle (2) | kCU = 386[7] | 771.843 | 2.388
Connector (3) | kCU = 386[7] | 30.03 | 5
PCB (4) | kCU = 386[7] | 2510.64 | 2.30
Air Cavity (5) | kAir = 0.025[6] | 6667.5 | 16.8
Battery (6) | kLiPo = 0.43[10] | 6000 | 11
Air Cavity (7) | kAir = 0.025[6] | 6667.5 | 25.6
Temperature Sensor (8) | kSi = 148[8] | 3.927 | 5

## Slide 95: Thermal Analysis Calculations & Results
Individual Resistances:
Total Resistance:
  Rtot = 0.004299
  Temperature Increase = ~0.142℃
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
R1 | R2 | R3 | R4 | R5 | R6 | R7 | R8
3.745 | 0.00799 | 0.431 | 0.00246 | 100.787 | 47.636 | 153.581 | 0.00860

## Slide 96: Signal Interference Requirements
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
DR 5.2 | System shall send/receive voltage measurements to on-site system wirelessly
DR 5.3 | System shall send/receive temperature measurements to on-site system wirelessly
With multiple systems operating in one room, the signals sent from each system must be differentiable to satisfy the two design requirements above.

## Slide 97: Signal Interference UUID Code
Data Packet Format
GATT[11]
  Service
  Characteristic ***
    UUID Pseudorandom Code
    Unique
  Value
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 98: Reading Sensor Input and Transmitting it
Process
Used AnalogDiscovery2 to generate a square wave
Used the GPIO pin on NRF52840 to take in the analog signal
Used the onboard SAADC (successive approximation analog to digital converter) peripheral to convert the analog signal to a digital signal
The discrete digital values were written to a characteristic
The characteristic was subscribed to using the NRF connect app, and the values were compared with the expected values of the analog signal
Process Satisfies requisite Design Requirements
DR 1.4 | System shall measure DC voltage
DR 5.2 | System shall send/receive voltage measurements to on-site system wirelessly
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 99: Saving Data
Process
nRF52840 USB CDC ACM[30] module capable of outputting data to the customer PC serial port
Python pySerial[31] module capable of receiving serial port output as data
Python capable of generating timestamp and writing text file
Process Satisfies requisite Design Requirements
DR 7.1 | System shall save raw data
DR 7.1.1 | System shall save specific voltage and temperature values, so long as requirement 7.1 is met
DR 7.3 | Data shall be presented in a .txt file
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 100: Generating Alerts
Process
Conditional Statement to determine if alert needs to be generated
Python has Simple Mail Transfer Protocol (SMTP)[32] functionality
  Capable of sending alert email to designated recipients
Process satisfies requisite Design Requirements
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
DR 3.1 | Alert shall be generated when voltage exceeds 33.6V
DR 3.2 | Alert shall be generated when voltage drops below 20V
DR 3.3 | Alert shall be generated when temperature exceeds 20oC
DR 3.4 | Alert shall be generated when temperature drops below 0oC

## Slide 101: GUI Requirements
DR 7.2 | Data shall be sent once an hour by default configuration
DR 7.2.1 | System shall have a configurable transmission frequency option
DR 7.2.1.1 | A user interface shall be made to input configuration changes
Our team will create a GUI for the customer to input transmission frequencies into to satisfy the three design requirements above.
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 102: GUI Creation and Layout
HTML
Simple graphics
Implementation of alert system
Live feed of measurements
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Temp Low
Temp High
Volt Low
Volt High
Duration
Email

## Slide 103: Battery Selection
DR 4.1 | System shall survive dry nitrogen purging at room temperature and a pressure of 2psi
DR 4.2 | System shall remain intact during vacuum and heat sealing process
DR 6.1 | External battery shall operate for one year without charging
Selected Battery: 10Ah makerfocus lipo battery
Battery has required capacity for one year of continuous operation
Battery is durable which makes it more likely to survive the sealing/bagging process
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 104: Processor Selection
Chosen Processor | Idle Power Consumption | Cost | RAM | BLE Compatible?
nRF52840[5] | 1.5 μA | $10-13 | 256 KB | Yes
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 105: nRF52840[5]
Link to datasheet
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 106: Risk Mitigation Table
Risk ID | Risk | Mitigation Strategy | Outcome
1 | NRF development board backordered | Order ASAP and use existing hardware owned by team members | Debugging can be done early on with existing hardware, allowing the system to be tested before additional boards arrive, so design requirements can be met with confidence
2 | EnerSys Temperature chamber cannot be used | Rent temperature chamber from Espec for nearly $1,000 | Major increase in project budget, but temperature range can be verified
3 | Wireless communication with on-site system fails due to an obstruction | Store data to flash memory of in-box controller until communication is possible; increase signal power to blast through obstruction | The voltage and temperature measurements are still accounted for and will be received once communication with on-site system is reestablished
4 | External battery has lower capacity than stated by manufacturer/system raws more power than expected | Test battery before integration to ensure that discharge curve is as expected, include safety factor of 2, include a backup battery | Battery will only be implemented if it has expected capacity, large safety factor ensures that there is more power than needed if it is lower than expected, second battery ensures backup if one fails
5 | Unable to interface with customer computer due to computer state | Ensure computer is constantly plugged in/charging and that sleep mode has been disabled | Customer computer will not be able to enter power saving sleep mode, but will successfully receive data
6 | Temperature sensor backordered | Have a backup chip (TMP117) | System will be able to measure temperature, but our team will have to port an arduino library to the nrf hardware which will require additional coding
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup

## Slide 107: Risk Matrix Mitigation Summary
Almost Certain |  |  |  |  | 
Highly Likely | 2 | 2 |  |  | 5
Likely | 6 |  |  |  | 6 4
Low Likelihood | 1 3 |  |  | 1 | 3
Extremely Improbable | 4 |  |  |  | 5
 | Minimal | Minor | Major | Serious | Catastrophic
Severity
Likelihood
Overview Design Solution CPEs Requirements Satisfaction Risks Verification & Validation Project Planning References Backup
Key
NRF development board backordered
EnerSys temp chamber unusable
Wireless communication failure
External battery failure
Computer interface failure
Temp sensor backordered