## Slide 1: SBMS Stored Battery Monitoring System Test Readiness Review February 14th, 2022 ASEN 4018-012 Team 6 Customer: EnerSys ABSL Presenters: Ian Adler, Ben Gavin, Devin Geegan, Jamie Henault, Evan Meany, Nathan Zhao Additional Team Members: Richard Folsom, Joseph Harrell, Shreeyash Nadella

## Slide 2: Presentation Outline
Overview
Schedule
Test Readiness
  Voltage/PCB Stress Testing
  Power System Testing
  Communication Signal Testing
  Day-in-the-Life Testing at EnerSys
Budget
Overview Schedule Test Readiness Budget References Backup

## Slide 3: Overview

## Slide 4: Project Motivation
EnerSys ABSL batteries
  Storage
  Health Deterioration
Quality checks
  Bagging Process
  Time-consuming
Mission Statement:
  SBMS shall measure the voltage of an 8S3P battery and the temperature of the 8S3P’s environment and wirelessly send this data to an on-site system
Overview Schedule Test Readiness Budget References Backup

## Slide 5: Concept of Operations (CONOPs)
Overview Schedule Test Readiness Budget References Backup

## Slide 6: Key Levels of Success
Overview Schedule Test Readiness Budget References Backup
Level 1 | Level 2 | Level 3
Wireless communication through air | Wireless communication through one aluminum box | Wireless communication through two aluminum boxes
Sense temperatures from 0-20OC | Sense temperatures with accuracy of 0.15OC | 
Sense voltages from 20-33.6V | Sense voltages with accuracy of 0.1V | 
Powered by an external battery | Battery life lasts for a year | 
Send raw sensor data to receiver | Send specific voltage and temperature values to receiver hourly | Transmission frequency is configurable

## Slide 7: System Critical Project Elements
CPE | Description | FR
CPE1 | System shall measure temperature and voltage. | FR1, FR2
CPE2 | System shall have the necessary hardware for wireless communication. | FR5
CPE3 | System shall have the necessary software for wireless communication. | FR3, FR5, FR7
CPE4 | All parts of system shall integrate with one another. | All FRs
CPE5 | System shall be battery-powered. | FR6
CPE6 | System shall be validated for functionality. | All FRs
Overview Schedule Test Readiness Budget References Backup

## Slide 8: Functional Block Diagram (FBD)
Overview Schedule Test Readiness Budget References Backup

## Slide 9: Baseline Design (Storage)
K470 Zarges Box
Styrofoam Layer
Heat/Vacuum Sealed Bag
Monitoring System
SMT172
SMT172
25-pin D-sub connector
Overview Schedule Test Readiness Budget References Backup
176 mm
96 mm

## Slide 10: Baseline Design (Monitoring System)
Custom
PCB
nrf52840
Bluetooth Low Energy
nrf52840
MakerFocus 10000 mAh Lithium Polymer Battery
PCB with built-in voltage sensor and connections to 8S3P & SMT172 temp sensors
Top-Down View
Side View
MakerFocus 10000 mAh Lithium Polymer Battery
MiniBoost 5V
Overview Schedule Test Readiness Budget References Backup

## Slide 11: Baseline Design (Monitoring System)
Top-Down View
Side View
110 mm
70 mm
60 mm
100 mm
76.2 mm
15.24 mm
46.04 mm
110 mm
50 mm
11 mm
16.8 mm
21.9 mm
50.8 mm
Overview Schedule Test Readiness Budget References Backup

## Slide 12: EnerSys Storage Schematic
On-site computer is 3-15 ft from the stored battery
Temperature conditions are ~58°F (15°C)
Secondary Nordic dongle plugged into customer computer
Overview Schedule Test Readiness Budget References Backup

## Slide 13: Schedule

## Slide 14
Overview Schedule Test Readiness Budget References Backup
SBMS Spring Schedule

## Slide 15: Electronics Test Schedule
Overview Schedule Test Readiness Budget References Backup
3/2
3/4
3/10

## Slide 16: Software and Full-System Test Schedule
Overview Schedule Test Readiness Budget References Backup
4/1
2/9

## Slide 17: Test Readiness

## Slide 18: Project Testing Tasks
Overview Schedule Test Readiness Budget References Backup
Test | Test Purpose | Related FRs | Status
Voltage/PCB Stress | Ensure that SBMS can measure voltage accurately and survive being turned on/off repeatedly | 1 | In-Progress
Temperature | Ensure that SBMS can measure temperature | 2 | In-Progress
Alert System | Ensure that SBMS can generate alerts when temperature and/or voltage reach an undesirable state | 3,7 | Complete
Survivability | Ensure that SBMS can survive the customer’s bagging process | 4 | In-Progress
Communication Signal | Ensure that system can wirelessly transmit + receive data, as well as change the frequency at which data is sent | 5,7 | In-Progress
Power System | Ensure the SBMS can operate on its external battery | 6 | In-Progress
Day-in-the-Life (CU) | Ensure that all subsystems can function as a cohesive unit | 1,2,3,4,5,6,7 | In-Progress
Day-in-the-Life (EnerSys) | Ensure that full system works as expected in the design environment | 1,2,3,4,5,6,7 | In-Progress

## Slide 19: Voltage/PCB Stress Testing
Test Rationale
  Verify that voltage sensor measures in required range with required accuracy
  Perform highly accelerated life test to demonstrate reliability of PCB and expose design weaknesses
Necessary Equipment and Facilities
  Aerospace Electronics Lab
    Sorensen XPH35-4D DC Dual Power Supply
    Keysight 34461A Digital Multimeter
Overview Schedule Test Readiness Budget References Backup
DR 1.1: Voltage sensor shall have a range of at least 20-33.6V
DR 1.2: Voltage sensor shall have a sensitivity of at least 0.1V
CPE 1: System shall measure temperature and voltage
Test Fixture Design
Deadline: 3/2
In-Progress

## Slide 20: Voltage/PCB Stress Testing Continued
Test Procedure Overview
  Voltage Testing
    Use power supply to simulate 8S3P voltage
    Measure sensor voltage with desktop multimeter
    Save voltage measured by the SBMS
    Compare measurements over desired range
  PCB Stress Testing (Highly Accelerated Life Test)[2,3]
    Cycle power to board 18000x
    Each power cycle, test functionality of all peripherals
    Failure indicated by peripherals becoming unresponsive, unexpected sensor readings, and overheating
Overview Schedule Test Readiness Budget References Backup
FR 1: System shall measure voltage
Deadline: 3/2
In-Progress
DR 1.1: Voltage sensor shall have a range of at least 20-33.6V
DR 1.2: Voltage sensor shall have a sensitivity of at least 0.1V
CPE 1: System shall measure temperature and voltage

## Slide 21: Voltage/PCB Stress Testing Continued
Expected Results and Model Validation
  System expected to measure voltage accurately, with breakdown at higher voltages
  Will validate the 98.8% success rate predicted by the Monte Carlo simulation
Risk Reduction
  Proves voltage sensor can meet DRs 1.1 & 1.2
  Proves PCB can handle stress of mission duration
  Eliminates risk that PCB will break or measure inaccurate voltages
Overview Schedule Test Readiness Budget References Backup
Deadline: 3/2
In-Progress
DR 1.1: Voltage sensor shall have a range of at least 20-33.6V
DR 1.2: Voltage sensor shall have a sensitivity of at least 0.1V
CPE 1: System shall measure temperature and voltage

## Slide 22: Power System Testing
Test Rationale
  Show battery capacity is as expected
  Show current draw is as expected
Necessary Equipment and Facilities
  Aerospace Electronics Lab
    Ammeter - Keysight 34461A
      1uA range, 1pA resolution[8]
    Sourcemeter - Keithley 2460
Overview Schedule Test Readiness Budget References Backup
DR 6.1: External battery shall operate for one year without charging
CPE 5: System shall be battery-powered
Test Fixture Designs
Deadline: 3/13
In-Progress
Current Draw:
Battery Capacity:

## Slide 23: Power System Testing Continued
Test Procedure Overview
  PCB Current Draw Testing
    Connect ammeter between power supply and PCB
    Run wake and sleep modes
    Record current draws
  Battery Capacity Testing
    Connect battery to sourcemeter
    Set current draw < C-rating
    Allow to discharge
    Extract CSV data from sourcemeter
Overview Schedule Test Readiness Budget References Backup
Deadline: 3/13
In-Progress
DR 6.1: External battery shall operate for one year without charging
CPE 5: System shall be battery-powered

## Slide 24: Power System Testing Continued
Expected Results and Model Validation
  6.5 mA wake
  33 uA sleep
    No DC/DC converter
    = 1,240 mAh / year
  8,000mAh before dropping below 3.0V
    Data recorded by Sourcemeter
Risk Reduction
  Device won’t turn off before mission complete
Overview Schedule Test Readiness Budget References Backup
Deadline: 3/13
In-Progress
Capacity Used = Current Draw [mA] * Duration [hrs]
DR 6.1: External battery shall operate for one year without charging
CPE 5: System shall be battery-powered

## Slide 25: Communication Signal Testing
Test Rationale: Verify that system can transceive given the required parameters
Overview Schedule Test Readiness Budget References Backup
DR 5.4: System shall send signals through a K470 Universal Aluminum Box
DR 5.5: Data shall be transmitted over a distance of at least three feet
DR 7.2.1: System shall have a configurable transmission frequency option
CPE 2: System shall have the necessary hardware for wireless communication
CPE 3: System shall have the necessary software for wireless communication
On-Site System
Deadline: 4/1
In-Progress
Zarges K470 Box
In-Box System
EnerSys 8S3P Battery
Controller
Controller

## Slide 26: Communication Signal Testing Continued
Overview Schedule Test Readiness Budget References Backup
Deadline: 4/1
In-Progress
DR 5.4: System shall send signals through a K470 Universal Aluminum Box
DR 5.5: Data shall be transmitted over a distance of at least three feet
DR 7.2.1: System shall have a configurable transmission frequency option
CPE 2: System shall have the necessary hardware for wireless communication
CPE 3: System shall have the necessary software for wireless communication
Test Procedure Overview
  Setup both systems and verify with LEDs
  Send preset voltage and temperature values from In-Box to to On-Site system
  Verify voltage/temperature values
  Change frequency configuration and repeat steps above (verify that configuration change is correct)

## Slide 27: Communication Signal Testing Continued
Expected Results/ Model Validation
  System will wirelessly transmit and receive data correctly
  System will correctly be configurable
Risk Reduction
  Proves that system can send/receive communications through K470 Box
  BLE functions with other peripherals running
  Both systems can both send and receive
Overview Schedule Test Readiness Budget References Backup
Deadline: 4/1
In-Progress
DR 5.4: System shall send signals through a K470 Universal Aluminum Box
DR 5.5: Data shall be transmitted over a distance of at least three feet
DR 7.2.1: System shall have a configurable transmission frequency option
CPE 2: System shall have the necessary hardware for wireless communication
CPE 3: System shall have the necessary software for wireless communication

## Slide 28: Day-in-the-Life at EnerSys
Test Rationale
  Validate that all system components are fulfilling customer requirements
Necessary Equipment and Facilities
  EnerSys Cold Storage
    8S3P battery
    Zarges K470 box
    Computer
Risk Reduction
  System is autonomous
Expected Results
  .txt file of data
Overview Schedule Test Readiness Budget References Backup
All FRs
All CPEs
Experimental Test Design
Deadline: 4/16
In-Progress

## Slide 29: Day-in-the-Life at EnerSys Continued
Test Procedure Overview
  Put in-box system and battery through a physical integrity test
  Insert bagged system and battery into Zarges K470 box inside of foam casing
  Leave system alone for 24 hours while it takes temperature and voltage measurements
  System will send voltage and temperature measurements to on-site system in a .txt file
Overview Schedule Test Readiness Budget References Backup
All FRs
All CPEs
Deadline: 4/16
In-Progress

## Slide 30: Budget

## Slide 31: Cost Plan
$84.48
$145.39
$197.45
Overview Schedule Test Readiness Budget References Backup
Future Expenses
 | CDR Estimate | Actual | Updated Estimate
Total Spent | $3,933.14 | $1908.66 | $2,106.11
Remainder | $1,066.86 | $3,091.34 | $2,893.89

## Slide 32: Acknowledgements
EnerSys ABSL Team
Jacqueline Maldonado, Brice Lucero, Travis Mault, Ryan Pritchard
Team Advisor
Dr. Jean Koster
Projects Advisory Board
Dr. Jelliffe Jackson, Dr. Jade Morton, Dr. Christopher Roseman,
Dr. Jean Koster, Dr. Melvin Rafi, Professor Matt Rhode
Additional Support
Professor Trudy Schwartz, Professor Bobby Hodgkinson,
Emma Markovich, Colin Claytor
Overview Schedule Test Readiness Budget References Backup

## Slide 33: References
“SMT172 Datasheet,” Smartec, Last Updated March 20, 2017. Available: https://www.smartec-sensors.com/cms/media/Datasheets/Temperature/SMT172-datasheet.pdf
Peterson, Z. “Overview of Electrical Stress Test Methods for PCBAs,” Altium, Last Updated January 6 2022. Available: https://resources.altium.com/p/overview-electrical-stress-test-methods-pcbas
“HALT Testing: Highly Accelerated Life Testing,” Delserro Engineering Solutions. Available: https://www.desolutions.com/testing-services/reliability-tests/highly-accelerated-life-testing-halt/
“ERA3AEB113V,” Newark. Available: https://www.newark.com/panasonic-electronic-components/era3aeb113v/surface-mount-thin-film-resistor/dp/62W8736
“ERA-3AEB302V,” Mouser. Available: https://www.mouser.com/ProductDetail/Panasonic/ERA-3AEB302V?qs=%2Fha2pyFaduhb05ESoU1Edd%252B%252BYQj5NEVJ4yV8H3JHdTrOH%252BIkW8jYRA%3D%3D
“MCS0402MD1004BE000,” Digikey. Available: https://www.digikey.bg/en/products/detail/vishay-dale/MCS0402MD1004BE000/14324215
“RP73PF1E118KBTD,” Digikey. Available: https://www.digikey.com/en/products/detail/te-connectivity-passive-product/RP73PF1E118KBTD/8261060
“Digital Multimeters 34460A, 34461A, 34465A, 34470A,” Keysight. Available: https://www.keysight.com/zz/en/assets/7018-03846/data-sheets/5991-1983.pdf
“How do I calculate the accuracy of a multimeter?,” Keysight. Available: https://edadocs.software.keysight.com/kkbopen/how-do-i-calculate-the-accuracy-of-a-multimeter-577940567.html
“Sorensen XPH Series,” SignalTestInc. Available: http://www.signaltestinc.com/v/vspfiles/assets/datasheet/Sorensen_XPH_Datasheet.pdf
“Keithley 2460 - SMU Source Meter (100V, 7A, 100W),” Tequipment. Available: https://www.tequipment.net/Keithley/2460/Source-Measure-Unit/SMU/?gclid=Cj0KCQiAr5iQBhCsARIsAPcwROMDU8VrN-KGo1gyjo0cOUJ-vs6973bQGY2TBfrGFfXZKLKNpRh4ugEaAr94EALw_wcB
“LTC2063” Analog Devices. Available: https://www.analog.com/en/products/ltc2063.html#product-overview
“onsemi FDV303N,” LCSC Electronics. Available: https://lcsc.com/product-detail/MOSFETs_onsemi-FDV303N_C80498.html
“nRF52840,” Nordic Semiconductors. Available: https://www.nordicsemi.com/-/media/Software-and-other-downloads/Product-Briefs/old-versions/nRF52840PBv20.pdf?la=en&hash=516968A8D06D7F41C8B14B6639DD9E14099E2853
Overview Schedule Test Readiness Budget References Backup

## Slide 34: Thank You! Questions?

## Slide 35: Backup Slides

## Slide 36: Contents
Overview Schedule Test Readiness Budget References Backup
Test Readiness (Continued)
  Power Testing
    Current Draw Model Background
    Battery Capacity Experimental Model Background
    COTS Battery Choice
    Test Equipment
    Test Failure Approach
  Communication Signal Testing
    Experimental Model Background
    Test Failure Approach
Budget
  Detailed Plan
Overview
  Organizational Chart
  Work Breakdown Structure
  Requirements
  Levels of Success
Test Readiness
  Temperature Testing
  Alert System Testing
  Survivability Testing
  Day-in-the-Life Testing (CU Boulder)
  Voltage Sensor Testing
    Error Model Background
    PCB Layout and Test Sites
    Test Equipment
    Test Failure Approaches

## Slide 37: SBMS Organizational Chart
Project Manager
Jamie Henault
Finance Lead
Richard Folsom
Customer
EnerSys ABSL
Advisor
Dr. Jean Koster
Systems Engineer Lead
Nathan Zhao
Power Lead
Ian Adler
Data Processing Lead
Joseph Harrell
Testing Lead
Devin Geegan
Electronics + Hardware Lead
Ben Gavin
Communications Lead
Evan Meany
Commands Lead
Shreeyash Nadella
Subteam
Nathan Zhao
Shreeyash Nadella
Joseph Harrell
Subteam
Nathan Zhao
Ben Gavin
Richard Folsom
Joseph Harrell
Subteam
Nathan Zhao
Ben Gavin
Devin Geegan
Evan Meany
Subteam
Jamie Henault
Richard Folsom
Subteam
Ian Adler
Jamie Henault
Richard Folsom
Shreeyash Nadella
Subteam
Nathan Zhao
Ian Adler
Joseph Harrell
Evan Meany
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 38: Work Breakdown Structure (WBS)
SBMS
Project Management
Fall Final Report
Test Readiness Review
AIAA Conference Paper
Spring Final Review
Project Final Report
Testing
Voltage
Temperature
Power
Alerts
Communication Signal
Survivability
Day-in-the-life (On-Campus)
Day-in-the-life (EnerSys)
Electronics & Hardware
Custom PCB+Attachments
In-Box System Container
Software
In-Box Processing
In-Box Dongle
In-Box Configuration
On-Site Data Processing
On-Site Dongle
On-Site Configuration
On-Site GUI
Communication Timing
Advertising
Battery Relay
On-Site Dongle
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 39: Requirements
FR | DR | Requirement
1 |  | System shall measure voltage
 | 1.1 | Voltage sensor shall have a range of at least 20-33.6V
 | 1.2 | Voltage sensor shall have a sensitivity of 0.1V
 | 1.3 | Voltage sensor shall connect to the customer’s 8S3P battery
 | 1.4 | Voltage sensor shall measure DC voltage
2 |  | System shall measure temperature
 | 2.1 | Temperature sensor shall have a range of at least 0-20oC
 | 2.2 | Temperature sensor shall have a sensitivity of 0.15oC
 | 2.3 | Temperature sensor shall measure the temperature of the battery environment
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 40: Requirements Continued
FR | DR | Requirement
3 |  | System shall communicate when voltage and temperature reach an undesirable state
 | 3.1 | Alert shall be generated when voltage exceeds 33.6V
 | 3.2 | Alert shall be generated when voltage drops below 20V
 | 3.3 | Alert shall be generated when temperature exceeds 20oC
 | 3.4 | Alert shall be generated when temperature drops below 0oC
4 |  | System shall continue operation after sanitization & bagging process performed by customer
 | 4.1 | System shall survive dry nitrogen purging at room temperature and a pressure of 2psi
 | 4.2 | System shall remain intact during vacuum and heat sealing process
5 |  | System shall transmit and receive data wirelessly
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 41: Requirements Continued
FR | DR | Requirement
 | 5.1 | Data communication process shall be autonomous
 | 5.2 | System shall send/receive voltage measurements to on-site system wirelessly
 | 5.3 | System shall send/receive temperature measurements to on-site system wirelessly
 | 5.4 | System shall send signals through the K470 Universal Aluminum Box (provided by the customer) that the battery is stored in
 | 5.4.1 | System shall send signals through a secondary K470 Universal Aluminum Box next to the one it is being stored in
 | 5.5 | Data shall be transmitted over a distance of at least three feet
6 |  | System shall be battery-powered
 | 6.1 | External battery shall operate for one year without charging
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 42
Requirements Continued
FR | DR | Requirement
 | 6.2 | External battery shall draw negligible charge from stored battery
7 |  | System shall save received data with a timestamp
 | 7.1 | System shall save raw data
 | 7.1.1 | System shall save specific voltage and temperature values, so long as requirement 7.1 is met
 | 7.2 | Data shall be sent once an hour by default configuration
 | 7.2.1 | System shall have a configurable transmission frequency option
 | 7.2.1.1 | A user interface shall be made to input configuration changes
 | 7.3 | Data shall be presented in a .txt file
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 43: Detailed Levels of Success
Overview Schedule Test Readiness Budget References Backup
Level 1 | Level 2 | Level 3
Wireless communication through air | Wireless communication through one aluminum box | Wireless communication through two aluminum boxes
Sense temperatures from 0-20OC | Sense temperatures with accuracy of 0.15OC | 
Sense voltages from 20-33.6V | Sense voltages with accuracy of 0.1V | 
Powered by an external battery | Battery life lasts for a year | 
System interfaces with customer battery |  | 
Send raw sensor data to receiver | Send specific voltage and temperature values to receiver hourly | Transmission frequency is configurable
Data is saved to a .txt file with a timestamp |  | Data is presented in a GUI
Alert generated to indicate poor battery health | Alerts autonomously emailed to customer | 
Back

## Slide 44: Test Readiness: Temperature Testing
Test Rationale
  Verify that temperature sensor can measure in required range with required accuracy
Necessary Equipment & Facilities:
  Sensor integrated into harness
  PCB populated with temp sensing peripherals
  Processor w/ headers
  F150 Precision Thermometer
  EnerSys ABSL Thermal Chamber
DR 2.1: Temperature sensor shall have a range of at least 0-20oC
DR 2.2: Temperature sensor shall have a sensitivity of 0.15oC
CPE 1: System shall measure temperature and voltage
Overview Schedule Test Readiness Budget References Backup
Deadline: 3/8
In-Progress
Back

## Slide 45: Test Readiness: Temperature Testing Continued Test Readiness: Temperature Testing
Test Procedure Overview (Range)
  Configure dongle to continuously measure and transmit temperature before placing SBMS in temperature chamber
  Increase chamber temperature from 0-20°C by 1°C every 5 minutes
  Record temperature throughout test to ensure that SBMS can measure within the required range
Test Procedure Overview (Accuracy)
  Record the temperature of the electronics lab with the F150 Precision Thermometer
  Transmit and save the temperature measured by the processor attached to the team temperature sensor
  Record this value and ensure that it is within 0.15oC of the first measurement
  Repeat this process two more times in the senior projects room and the PILOT lab to ensure that when the temperature changes, the system can still give the necessary accuracy
Deadline: 3/8
In-Progress
DR 2.1: Temperature sensor shall have a range of at least 0-20oC
DR 2.2: Temperature sensor shall have a sensitivity of 0.15oC
CPE 1: System shall measure temperature and voltage
Back
Overview Schedule Test Readiness Budget References Backup

## Slide 46: Test Readiness: Temperature Testing Continued
Expected Results and Model Validation
  Both sensors report temperature within 0.15°C of each other after reaching steady state in each environment
  Sensor performance guaranteed by manufacturer
Risk Reduction
  To satisfy FR2, temperature sensing range & accuracy must be characterized - test will reduce risk associated with satisfying FR2 by assessing both metrics
Deadline: 3/8
In-Progress
Temperature Error Chart From Manufacturer[1]:
DR 2.1: Temperature sensor shall have a range of at least 0-20oC
DR 2.2: Temperature sensor shall have a sensitivity of 0.15oC
CPE 1: System shall measure temperature and voltage
Back
Overview Schedule Test Readiness Budget References Backup

## Slide 47: Test Readiness: Smartec SMT172[1] - Chosen Temperature Sensor
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 48: Test Readiness: Temperature Sensor Configuration
Overview Schedule Test Readiness Budget References Backup
Circuit Board
Heat Shrink Tubing
Processor
MOSFET
SMT172
G
D
S
V
GND
DATA
GND
GPIO
GPIO
VDD
200 mm
Back

## Slide 49: Test Readiness: Approach to a Failed Temperature Sensor Test
Overview Schedule Test Readiness Budget References Backup
Bias in sensor readings will be calibrated for with adjustments to the conversion equation provided by the manufacturer.
Non-linearities over the desired range will be smoothed out with adjustments to the equation mentioned above.
Undesirable noise will be eliminated by increasing the number of signal periods from which a single value is averaged.
Back

## Slide 50: Test Readiness: Alert System and Data Logging
Test Rationale
  Verify that alerts shall be generated when temperature (DR 3.1,3.2) and voltage (DR 3.3,3.4) fall out of acceptable range
  Verify that data shall be saved in a text file format (DR 7.1,7.1.1,7.3)
Test Equipment
  Computer
  Arduino Uno
Overview Schedule Test Readiness Budget References Backup
FR 3: System shall communicate when voltage and/or temperature reach an undesirable state
FR 7: System shall save received data with a timestamp
CPE 3: System shall have the necessary software for wireless communication
Complete
Deadline: 2/18
Back

## Slide 51: Test Readiness: Alert System and Data Logging
Test Procedure
  Program arduino to communicate selected data
  Input email address that will receive alert
  Input lower/upper bounds for both values
    First where data is within bounds to ensure no alert is generated
    Second where data is not within bounds
  Verify that designated email address has received the alert
  Verify that data is saved
Overview Schedule Test Readiness Budget References Backup
Complete
Deadline: 2/18
FR 3: System shall communicate when voltage and/or temperature reach an undesirable state
FR 7: System shall save received data with a timestamp
CPE 3: System shall have the necessary software for wireless communication
Back

## Slide 52: Test Readiness: Alert System and Data Logging
Expected Results and Model Validation
  The SBMS will be able to generate alerts for both an undesired temperature and voltage state
  Undesired states will be input through the SBMS GUI system
  Data will be saved
  GUI layout will match design presented at CDR
Risk Reduction
  Proves alert system will satisfy FR 3 and its associated DRs
  Ensure SBMS’ email address privacy has optimal settings
  Data is not lost
Overview Schedule Test Readiness Budget References Backup
Complete
Deadline: 2/18
Temp Low
Temp High
Volt Low
Volt High
Duration
Email
FR 3: System shall communicate when voltage and/or temperature reach an undesirable state
FR 7: System shall save received data with a timestamp
CPE 3: System shall have the necessary software for wireless communication
Back

## Slide 53: Test Readiness: Survivability Testing
Test Rationale
  System will undergo sanitization and bagging process during its mission
  Must ensure functionality remains after dry nitrogen purging and heat seal
Necessary Equipment and Facilities
  ESD compliant plastic bag
  Vacuum/heat sealer
  Dry nitrogen canister
FR 4: System shall continue operation after sanitization and bagging process performed by the customer
CPE 6: System shall be validated for functionality
Test Fixture Design
Deadline: 4/6
In-Progress
Back
Overview Schedule Test Readiness Budget References Backup

## Slide 54: Test Readiness: Survivability Testing Continued
Test Procedure Overview
  Ensure functionality prior to test
    Capable of sensing data
    Capable of wirelessly sending data
  Place monitoring system attached to a battery inside plastic bag
  Purge system with dry nitrogen to remove moisture
  Vacuum seal the bag to remove excess air and dust
  Heat seal the bag shut to keep the environment secluded
  Monitor computer to ensure data is still being transmitted
Deadline: 4/6
In-Progress
FR 4: System shall continue operation after sanitization and bagging process performed by the customer
CPE 6: System shall be validated for functionality
Back
Overview Schedule Test Readiness Budget References Backup

## Slide 55: Test Readiness: Survivability Testing Continued
Expected Results and Model Validation
  System will continue operation
Risk Reduction
  Ensures system will be able to survive in the expected environment
  Reduces concern of manufacturing failure
Deadline: 4/6
In-Progress
FR 4: System shall continue operation after sanitization and bagging process performed by the customer
CPE 6: System shall be validated for functionality
Back
Overview Schedule Test Readiness Budget References Backup

## Slide 56: Test Readiness: Approach to a Failed Survivability Test
Overview Schedule Test Readiness Budget References Backup
Structural Failure
  If the housing unit cannot withstand the vacuum sealing pressure, the team will revisit the CAD model to thicken the width of the unit
  If the housing unit cannot withstand the heat sealing process, an alternative material will be used
Functionality Failure
  If the electronics do not maintain functionality, the team can look into an extra insulation layer underneath the housing unit
Back

## Slide 57: Test Readiness: Day-in-the-Life Testing at CU Boulder
Same test setup and procedure as Day-in-the-Life at EnerSys, except not in cold storage
  System will also be monitored every 3 hours during testing
Expected Results
  .txt file containing data
Test Rationale
  System will operate autonomously
  Monitoring will allow the team to find any issues when running for an extended period
Overview Schedule Test Readiness Budget References Backup
All FRs
All CPEs
Deadline: 4/11
In-Progress
Back

## Slide 58: Test Readiness: Approach to a Failed Day-in-the-Life Test
This is for both the CU and EnerSys located tests
Functionality Failure
  If the in-box system is not able to establish communication with the on-site system
    Zarges K470 box will be removed
    In-box system will still undergo bagging process but will be placed in the foam casing with no Zarges K470 box around it
    This will eliminate the interference caused by the metal lining on the Zarges K470 box
      With significantly less interference, the in-box system should be able to establish communication with the on-site system
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 59: Test Readiness: Voltage Sensor Error Model Setup
DR 2.1 | Voltage sensor shall have a sensitivity of 0.1V
8S3P[6][7]
R1 = 1MΩ
R2 = 118kΩ
Vmax(1) = 50V
Vmax(2) = 200V
Pmax(1,2) = 0.1W
External Battery[4][5]
R1 = 11kΩ
R2 = 3kΩ
Vmax(1,2) = 75V
Pmax(1,2) = 0.1W
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 60: Test Readiness: Voltage Sensor Error Model Calculations
Actual Voltage (V1)
  Random value from 20 to 33.6V
Expected Resistances
  R1,exp= 1MΩ
  R2,exp= 118kΩ
Expected Intermediate Voltage (V2,exp)
  V2,exp = (R2,exp*V1) / (R1,exp + R2,exp)
Resistor Tolerances (R1,tol, R2,tol)
  Random values from -1% to +1%
Actual Resistances (R1,act, R2,act)
  R1,act = R1,exp + R1,exp * R1,tol
  R2,act = R2,exp + R2,exp * R2,tol
Actual Intermediate Voltage (V2,act)
  V2,act = (R2,act*V1) / (R1,act + R2,act)
Op-amp Error (Vop,err)
  Random value from -5μV to +5μV
Actual Intermediate Voltage (V3,act)
  V3,act = V2,act + Vop,err
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 61: Test Readiness: Voltage Sensor Error Model Calculations Continued
ADC Differential Nonlinearity Error (ED)
  Random Value from -0.95 to +1.3
ADC Integral Nonlinearity Error (EI)
  Random Value from -10 to +10
ADC Gain Error (EG)
  Random Value from -0.03 to +0.03
ADC Total Error (EADC)
  EADC = (ED + EI + EG + 1)*V3,act / 212
Actual Final Voltage (V4,act)
  V4,act = V3,act + EADC
Absolute Voltage Error (VE)
  VE = V4,act - V2,exp
Absolute Voltage Error Scaled Back up to Input Voltage Range (VE,scaled)
  VE,scaled = (R1,exp + R2,exp)*(VE / R2,exp)
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 62: Test Readiness: PCB Layout
Overview Schedule Test Readiness Budget References Backup
External Battery Voltage Sensor
8S3P Customer Battery Voltage Sensor
External Battery Connectors
Power Converter
Dongle Connector
Battery Switch
Temperature Processing
Back

## Slide 63: Test Readiness: PCB Voltage and Stress Test Attachments
Overview Schedule Test Readiness Budget References Backup
To (-) input on power supply
To (+) input on power supply
To (-) input on multimeter
To (+) input on multimeter
Back

## Slide 64: Test Readiness: Sorensen XPH35-4D DC Dual Power Supply[10]
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 65: Test Readiness: Keysight 34461A Digital Multimeter[8,9]
Overview Schedule Test Readiness Budget References Backup
Voltage Accuracy Note
35ppm of 20V is 20*35*(1/1,000,000) = 0.0007V
35ppm of 33.6V is 33.6*35*(1/1,000,000) =0.001176V
Expected accuracy of multimeter in SBMS’ voltage range is 0.001176 - 0.0007V which is << 0.1V, so the multimeter reading can be taken as the “true” value
Back

## Slide 66: Test Readiness: Approach to a Failed Voltage Test
Overview Schedule Test Readiness Budget References Backup
Accuracy Failure
  Small failure (~0.2V achieved instead of 0.1)
    Talk with the customer about changing the requirement. Couldn’t reach temperature accuracy of 0.1oC due to resolution, and the customer was happy to let us change this to 0.15oC, so we would aim for this same small change in voltage
  Large failure (>0.2V achieved)
    Do some circuit debugging to see where accuracy issues are coming from (i.e. op-amp, voltage divider, etc.) and possibly change these components / associated trace length on PCB for increased accuracy
Range Failure
  High-side failure
    Look into components that can handle higher voltages/power to avoid component breakdown
  Low-side failure
    Look into components that can handle a smaller resolution
Back

## Slide 67: Test Readiness: Approach to a Failed PCB Stress Test
Overview Schedule Test Readiness Budget References Backup
PCB Stress Failure
  If shorts, burns, or component failures are seen, our team may increase the width of traces or add a ground plane to ensure that there isn’t too much resistance in any line or heat generation along the board
  May need to add more capacitors to help manage the power being repeatedly applied to the board
Back

## Slide 68: Test Readiness: Power System Current Draw Model
 | Current [mA] | Sources or Justification
Voltage Sensor + Peripherals | 0.010 (on) 0.003 (off) | LTC2063[12] & FDV303N[13] Datasheets
Temp. Sensor + Peripherals | 0.120 (on) 0.002 (off) | SMT172 Datasheet Active Draw[1]
Board - Wake | 6.400 | Nordic Semiconductors Datasheet, pg 62
Board - Sleep | 0.00084 | Nordic Semiconductors Datasheet, pg 59
Total - Wake | 6.530 | Calculated
Total - Sleep | 0.123 | Calculated
Required Yearly Supply | 1,240 mAh | Calculated:
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 69: Test Readiness: Power System Current Draw Model Continued
 | Loss | Multiplier | Battery Size Required [mAh] | Sources or Justification
Required Supply | - | - | 1,240 | Prev. Slide
Low-Temp | 0% | 1 | 1,240 | Storage temp (58oF) is not cold enough to affect capacity
Temporal | 60% | 2.5 | 3,100 | ~5% loss in capacity per month
Discharge | 20% | 1.25 | 3,875 | ~80% of rated capacity is usable; Experimental validation
Converter | 20% | 1.25 | 4,844 | Boost 3.7V -> 5V Buck 5V -> 3.3V
FOS | - | 2 | 9,688 | -
Desired Size: | - | - | 10,000 mAh | -
Selected Battery: MakerFocus 10,000 mAh Lithium Polymer Battery
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 70: Test Readiness: Power System Current Draw Model (Derivation)
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 71: Test Readiness: Power System Current Draw Model (Detailed Current Draw Estimates)
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 72: Test Readiness: Power System Current Draw Model (Detailed Current Draw Estimates)
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 73: Test Readiness: Power System Current Draw Model (Detailed Current Draw Estimates)
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 74: Test Readiness: Power System Current Draw Model (Detailed Current Loss Estimates)
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 75: Test Readiness: Power System Current Draw Model (COTS Battery Choice)
 | Battery #1 (LiPo) | Battery #2 (LiPo) | Battery #3 (Li-ion) | Battery #4 (Li-ion)
Cell Capacity [mAh] | 3,700mAh | 10,000mAh | 2000mAh | 3000mAh
Dimensions [in] | 1.3 x 3.8 x 0.4 | 4.4 x 2.6 x 0.3 | 1.34 x 0.63d | 2.8 x 0.7d
Energy [mAh / in3] Density | 1,872 | 2,900 | 1,188 | 728
Meets Requirements (Temp, Size, C rate) | ✔️ | ✔️ | ✔️ | ✔️
Available From | Amazon | Makerfocus, Amazon | Amazon | Amazon
Cost per unit | $61 / (4 pc) | $30 / (1 pc) | $30 / (4 pc) | $34 / (2 pc)
Total Purchase Cost (1 full system) | $122 | $60 | $60 | $136
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 76: Test Readiness: Power System Battery Capacity Experimental Model
1000mAh Battery
Keithley 2460 Sourcemeter
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 77: Test Readiness: Keithley 2460 SMU Sourcemeter[11]
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 78: Test Readiness: Approach to a Failed Power System Test
Overview Schedule Test Readiness Budget References Backup
Battery Failure
  If battery capacity is less than desired, our team can connect batteries in parallel to increase capacity to acceptable values
  If battery is defective, our team will test the other batteries in the batch, and if necessary purchase a different brand of battery
Current Draw Failure
  If current draw is higher than expected, there are at least two options:
    Diagnose the electrical issue and make appropriate changes
    Connect more batteries in parallel, increasing capacity to meet the need
Back

## Slide 79: Test Readiness: Communication Signal Experimental Model
Flashed code to advertise out of ZARGES case
Tested the signal strength at different distances and transmission strengths
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 80: Test Readiness: Approach to a Failed Communication Signal Test
Overview Schedule Test Readiness Budget References Backup
Signal Strength Failure
  If signal is not strong enough to go through the Zarges case, our team will increase the transmission power until it is able to do so - we will revisit battery capacity if this issue occurs
Back

## Slide 81: Detailed Cost Plan
Overview Schedule Test Readiness Budget References Backup
Back

## Slide 82: Detailed Cost Plan Continued
Overview Schedule Test Readiness Budget References Backup
*Black arrow indicates items that were not included at CDR
*Dark green indicates items that have been received
*Light green indicates items to be purchased in the future
Back