## Slide 1: S P E C T E R Preliminary Design Review
October 14th, 2021
ASEN-011 Team 9
Company Customer
L3Harris
Faculty Advisor
Professor John Mah
Presenters
Gabriel Feldman, Sam Alvis, Vivien Blumofe, Zach Harris, Andrew Komitor, Ajay Dhindsa
Additional Team Members
Hanna Galimanis, Nick Spens, Mary Hanson, Josef Michelson, Noah Avery

## Slide 2: Table of Contents
Project Overview
Baseline Design
Enclosure Feasibility
Electronics Feasibility
Optics Feasibility
Image Processing Feasibility
Orbit Determination Feasibility
Algorithm Feasibility
Status Summary and Strategy
Appendix

## Slide 3: Project Overview
Project Overview
Baseline Design
Feasibility of Design
Summary and Strategy

## Slide 4: Motivation
Space situational awareness (SSA)
January 1st, 2021: Over 18,000 human made objects in Earth Orbit
  Approximately 500 are in GEO
Geosynchronous Earth Orbit (GEO) holds critical satellites for communication, weather, and military purposes
  Orbits with semi-major axis of roughly 42,000 km
  Orbital Period of 1 day
  Many unknown/unidentified satellites
Mission Statement
Key Terms
Objectives
CONOPS
Project Overview
Motivation
FBD
GEO Visualization from esa.int
Notes: Riebeek, H.
“Catalog of earth satellite orbits”.
NASA.
https://earthobservatory.nasa.gov/features/OrbitsCatalog

## Slide 5: Purpose & Mission Statement
Purpose: collect data on satellites in GEO and determine if a significant event has occurred or is imminent
  Maneuvers
  Close encounters between two or more satellites (including docking and collisions)
  Breakups
The Satellite Position Estimation Collision Tracking & Event Recognition (SPECTER) mission will monitor satellite movements in geosynchronous orbit to provide space domain awareness.
Mission Statement
Key Terms
Objectives
CONOPS
Project Overview
Motivation
FBD

## Slide 6: Key Terms
TLE: Two-Line (Orbital) Element Set
POL: Pattern of Life
  Includes a satellite's position, velocity, light curve intensity and color data over time. Created from historical data categorizing satellite behavior.
L3Harris POL Plot Example
Time scale: ~1 month (07/08/2021 - 08/09/2021)
… = Semi-major axis [km]
… = Longitude [deg]
… = Inclination [deg]
… = Longitude Ascending Node [deg]
Mission Statement
Key Terms
Objectives
CONOPS
Project Overview
Motivation
FBD
L3Harris, Project Introduction Presentation

## Slide 7: Objectives
Subsystem | Capability | Level 3 Success
Software - Algorithm | Detect Pattern of Life (POL) | Autonomously compare observed orbital behaviors against historical POLs, distinguish changes, and characterize events
Software - Data | Camera Data Collection and Storage | Camera subsystem sends data to cloud to be analyzed autonomously
Communication and Software | Tip and Cue | Autonomously send alerts based on recognized events
Mechanical - Enclosure | Enclosure for System | Enclosure autonomously responds to weather conditions
Electronics | Power | Power on camera subsystem autonomously
Mission Statement
Key Terms
Objectives
CONOPS
Project Overview
Motivation
FBD

## Slide 8: Concept of Operations
Mission Statement
Key Terms
Objectives
CONOPS
Project Overview
Motivation
FBD

## Slide 9: Concept of Operations - Step 1
Mission Statement
Key Terms
Objectives
CONOPS
Project Overview
Motivation
FBD

## Slide 10: Concept of Operations - Step 2
Mission Statement
Key Terms
Objectives
CONOPS
Project Overview
Motivation
FBD

## Slide 11: Concept of Operations - Step 3
Mission Statement
Key Terms
Objectives
CONOPS
Project Overview
Motivation
FBD

## Slide 12: Concept of Operations - Step 4
Mission Statement
Key Terms
Objectives
CONOPS
Project Overview
Motivation
FBD

## Slide 13: Concept of Operations - Step 5
Mission Statement
Key Terms
Objectives
CONOPS
Project Overview
Motivation
FBD

## Slide 14: Functional Block Diagram
Mission Statement
Key Terms
Objectives
CONOPS
Project Overview
Motivation
FBD
Notes: Also may want to remove pointer, if it’s not a part anymore
TRACE A PATH: (Command, Comm, Control, Weather Protection; Sensor, Processing, Orbit, AStro, ED, Comm, Cue

## Slide 15: Baseline Design
Project Overview
Baseline Design
Feasibility of Design
Summary and Strategy

## Slide 16: Baseline Design - Outside
Side View
Vent Holes
Colored Opaque Acrylic
Front View
Side View
Back View
Data Flow Diagram
Critical Project Elements
Baseline Design
18 inches
18 inches
24 inches
20 in.
Notes: Flesh out, combine with project breakdown

## Slide 17: Baseline Design - Components
Inside of Enclosure
Sensor/Camera
Linear Actuator
Sensor Mount
Lens
Electronics
Brackets
Battery
Data Flow Diagram
Critical Project Elements
Baseline Design
Sensor + lens approximate dimensions:
  Length: 10.2 inches
  Diameter: 3.6 inches
Notes: Flesh out, combine with project breakdown

## Slide 18: Data Flow Block Diagram
Data Flow Diagram
Critical Project Elements
Baseline Design

## Slide 19: Critical Project Elements
CPE | Importance
1. Weather Protection | An enclosure is needed to protect the internal subsystems (optical and electronics) from IPX-1 elements
2. GEO Observation | SPECTER must be capable to observe satellites to facilitate data collection
3. Data Collection | Data collection is required for future POL comparison
4. POL Determination | POL’s are necessary to monitor for deviations from expectations
5. Comparison of Collected Data to Historical Data | The system must be able to use the astrometric and photometric data output from the image processing subsystem to compare to historical data.
6. Event Detection | To alert end users of a POL deviation, the SPECTER system must have the capability to detect the event.
7. Tip and Cue | The SPECTER system must be able to alert end users of POL deviations
Data Flow Diagram
Critical Project Elements
Baseline Design
Notes: More description of elements, as well as the motivations listed here

## Slide 20: Feasibility of Baseline Design
Project Overview
Baseline Design
Feasibility of Design
Summary and Strategy

## Slide 21: Feasibility Overview
Feasibility Studied | CPE | Feasibility
Enclosure (weather protection) | 1 | ??
Electronics | 2-6 | ??
Image Processing | 3,4,5 | ??
Orbit Determination | 4,5 | ??
Optical Assembly | 2,3 | ??
Algorithm | 4,5,6 | ??
Notes: Transfer green, yellow, red chart to here in initial unfilled out form

## Slide 22: Enclosure Feasibility
Project Overview
Baseline Design
Feasibility of Design
Summary and Strategy

## Slide 23: Enclosure Driving Requirements
FR 8 | An enclosure shall protect the camera and its associated electronic equipment.
DR 8.1 | The enclosure shall maintain a moisture level below IPX-1, where IPX-1 is defined as water resistance against drops of water falling vertically.
DR 8.2 | The enclosure shall provide solar protection during the day.
Enclosure Characteristics
Driving Requirements
Door Actuation

## Slide 24: Enclosure Characteristics
Material
  Colored Acrylic (waterproof)
Weather and Sun Protection
  Passive
    Slanted roof to prevent water pooling
      IPX-1 protection is from vertical dripping water, so enclosure does not need to be fully watertight
    Colored acrylic to shield from sunlight
  Autonomous
    Connection to weather app for sunrise/sunset times, rain
      If rain is predicted, the enclosure will not open
      If clear skies are predicted, cloud cover will be measured before the enclosure opens
    IR thermometer to determine cloud cover
      Cloudy skies are around 10°C warmer than clear skies
Cover
  Linear actuator to slide cover behind window
Enclosure Characteristics
Driving Requirements
Door Actuation
Enclosure exterior

## Slide 25: Door Actuation
Coefficient of Friction of Acrylic: 0.4-0.5
Weight of hole cover: 0.4 lbs
  6x6 inch piece of acrylic with density of 0.043lb/cu. in
Force due to friction:
  0.4*0.5 = 0.2 lbs needed
Linear actuator found can move up to 330 lbs
330 lbs > 0.6 lbs ✅
Enclosure Characteristics
Driving Requirements
Enclosure Characteristics
Driving Requirements
Door Actuation
Linear actuator and door cover

## Slide 26: Electronics Feasibility
Project Overview
Baseline Design
Feasibility of Design
Summary and Strategy

## Slide 27: Electronics Driving Requirements
FR 3 | Collected astrometric and photometric data shall be stored.
DR 3.1 | The system shall support storage of imported historical data and collected data.
FR 4 | The system shall be able to use the astrometric data output from the image processing subsystem to compare to historical data.
DR 4.5 | Collected astrometric data shall be processed by a processor within 5 minutes.
DR 5.3 | Collected photometric data shall be processed by a processor within 5 minutes.
Requirements
Location & Communication Analysis
Power Feasibility

## Slide 28: Location and Communication Analysis
Will need to upload data on order of kB
  4G or 5G will meet these requirements
Data Coverage:
  3G & Below - not widely available
  4G - broad range, far outside of cities
  5G - only in cities/densely populated areas
Light Pollution:
  Naked Eye Limiting Magnitude (NELM)[7]
  NELM ~ 7
    In suburban sky, NELM ~ 5
  Telescope limit of ~ 14 (see optics feasibility)
    In suburban sky, limit would be reduced to ~12
    Too low for GEO satellite observations!
Requirements
Location & Communication Analysis
Power Feasibility
Verizon Coverage around Boulder [10]
Light Pollution Map [11]
Notes: Need to explain why this requirement is here, first! (4g, 5 Mbit, light pollution)
Must list

## Slide 29: Location and Communication Analysis
Denver
Denver
Denver
Needs 4G coverage, low light pollution
Also proximity to Boulder
Candidate Spots: Lyons, Nederland
Boulder
Boulder
Nederland
Lyons
Power Feasibility
Requirements
Location & Communication Analysis
Notes: Need to explain why this requirement is here, first! (4g, 5 Mbit, light pollution)
Must list

## Slide 30: Power Feasibility
Opening Cover
  Linear actuator
  36 W max
Normal Operations
  Onboard computer, camera, and IR thermometer
  101.0075 W max
Battery
  720 Wh
  7.13 h (Worst Case)
Opening Cover
(Worst Case)
Normal Operations
(Worst Case)
Requirements
Location & Communication Analysis
Power Feasibility

## Slide 31: Optics Feasibility
Project Overview
Baseline Design
Feasibility of Design
Summary and Strategy

## Slide 32: Optics Driving Requirements
FR 1 | The system shall observe satellites in geosynchronous orbit
DR 1.1 | The camera subsystem shall point the camera with an accuracy that ensures the target satellite will be in the field of view
FR 3 | Collected astrometric and photometric data shall be stored
Design Options
Optics
Lens
Driving Req.
LSM
Summary

## Slide 33: Limiting Stellar Magnitude (LSM)
Majority of GEO Satellites in range m = 11-14
Customer requires 13, 14-15 ideal
Aperture diameter (D) most important for urban areas
Assumptions:
  Optical System is in ‘stare’ mode thus relative velocity is (⍵) = velocity of Satellite
  GEO Satellites have circular orbits
  Satellites treated as spheres
[3] Coder, Holzinger, 2016)
13 <
-30
-25
-20
-15
-10
-5
0
10
15
20
25
5
Sun
Full Moon
Naked
Eye Limit
GEO Satellites
Apparent Magnitude ( mv )
Design Options
Optics
Lens
Driving Req.
LSM
Summary
Notes: Better explain, use < to highlight values versus goal. Greater than
Equation too dense?

## Slide 34: Design Options
Canon EOS Ra + TBDmm f/TBD = TBD LSM
ZWO ASI2600Mc + TBD mm f/TBD = TBD LSM
+
+
=
=
?
?
Design Options
Optics
Lens
Driving Req.
LSM
Summary
ZWO, ASI2600MC Pro (color)
Canon, EOS Ra

## Slide 35: Optic Options in Consideration
Design Options
Optics
Lens
Driving Req.
LSM
Summary

## Slide 36: Lens & Sensor Selection
Design Options
Optics
Lens
Driving Req.
LSM
Summary
Notes: Not enough info to stand alone
Line at 13, shade the good section
Add in 13 minimum (or maximum?) requirement

## Slide 37: Summary: Optical Feasibility
Canon EOS Ra + Sigma 135mm f/1.8 = 14.335 LSM
ZWO ASI2600Mc + Sigma 135mm f/1.8 = 14.142 LSM
+
+
=
=
✅
✅
Both systems feasible for detecting GEO satellites
Design Options
Optics
Lens
Driving Req.
LSM
Summary
BH Photo Video, Sigma 135mm f/1.8 DG HSM Art Lens
BH Photo Video, Sigma 135mm f/1.8 DG HSM Art Lens
ZWO, ASI2600MC Pro (color)
Canon, EOS Ra

## Slide 38: Image Processing Feasibility
Project Overview
Baseline Design
Feasibility of Design
Summary and Strategy

## Slide 39: Image Processing Driving Requirements
FR 4 | The system shall be able to use the astrometric data output from the image processing subsystem to compare to historical data.
FR 5 | The system shall be able to use the photometric data output from the image processing subsystem to compare to historical data.
DR 5.3, DR 4.5 | Collected data shall be processed by a processor within 5 minutes.
Requirements
IPF 1
IPF 2
IPF 3
Astrometry.net Output

## Slide 40: Image Processing Feasibility
Sensor Image
Sensor Image
tn-1
Astrometry.net
Astrometry.net
RAn-1/Decn-1
RAn/Decn
tn
GEO Satellites
+
=
Requirements
IPF 1
IPF 2
IPF 3
Astrometry.net Output
Notes: Too fast! combine!

## Slide 41: Image Processing Feasibility
Image at tn
Image at tn-1
Requirements
IPF 1
IPF 2
IPF 3
Astrometry.net Output

## Slide 42: Image Processing Feasibility
Image at tn
Image at tn-1
Requirements
IPF 1
IPF 2
IPF 3
Astrometry.net Output
Notes: What’s going on here?

## Slide 43: Astrometry.net Output
: Star
: Star with location known
Requirements
IPF 1
IPF 2
IPF 3
Astrometry.net Output
(nova.astrometry.net)
Notes: Mention astrometry.net gives location data but not satellite data without extra processing done by us.

## Slide 44: Orbit Determination Feasibility
Project Overview
Baseline Design
Feasibility of Design
Summary and Strategy

## Slide 45: Orbit Determination Driving Requirements
FR 6 | The software subsystem shall have the capability to detect an event.
DR 6.1 | The software subsystem shall have the capability to predict a close approach between two satellites.
DR 6.1.1 | Once a potential satellite close approach is identified the system will extrapolate how long it will take until the two objects are at their closest point.
DR 6.1.2 | The satellite close approach shall be detected when satellites are within a 25 km range.
DR 6.1.3 | The time prediction for a satellite close approach shall be detected within a 5 km margin of error.
Requirements
Gooding Method
ODTK Use Cases
Angle Estimation

## Slide 46: Orbit Determination Feasibility - ODTK Use Cases
Determine TLE (Two Line Element) of satellite given angle measurements
  Inputs: Angle measurements from Imaging System
  Outputs: TLE (Two Line Element)
a - Semi-Major Axis e - Eccentricity 𝜈 - True Anomaly i - Inclination Ω - Right Ascension of Ascending Node 𝜔 - Argument of Periapsis
Predict close approach between two satellites
  Inputs: Two Satellites NORAD-ID’s
  Outputs: Prediction of two objects being within 25km of each other
    How long until the two objects are at the closest point
    5km error margin on distance prediction
Illustration Via Wikipedia
Requirements
Gooding Method
ODTK Use Cases
Angle Estimation
Notes: Bold ideal parameters
Point out ideal ones on chart?

## Slide 47: Astrometry.net Angle Estimation
Method of Angle Determination from Ground Station
Given:
  Center of Image (RA, Dec)
  Pixel Scale (169 arcsec/pixel)
Use algorithm to convert pixel coordinates to RA/Dec angle pairs of satellites.
Requirements
Gooding Method
ODTK Use Cases
Angle Estimation

## Slide 48: ODTK Equations and Assumptions: Gooding Method
Assumption: Two-Body Problem
Inputs:
  Requires 3 distinct pairs of 2-angle measurements.
    Right Ascension & Declination (𝛼j , 𝛿j)
    Azimuth & Elevation (𝜍j, 𝜂j)
  Time between each measurement
  Location of site where the measurements were taken
Outputs:
  Position Vector of Satellite, r2
  Velocity Vector of Satellite, v2
ODTK Function: GoodingIOD
Input (𝛼1 , 𝛿1) (𝛼2 , 𝛿2) (𝛼3 , 𝛿3)
Output [r2 ] [v2]
Requirements
Requirements
Gooding Method
ODTK Use Cases
Angle Estimation
Notes: Equations? Just input to output feels weird

## Slide 49: Algorithm Feasibility
Project Overview
Baseline Design
Feasibility of Design
Summary and Strategy

## Slide 50: Algorithms Driving Requirements
FR 2 | The software subsystem shall determine the POL of satellites in geosynchronous orbit from historical data.
FR 4 | The system shall be able to use the astrometric data output from the image processing subsystem to compare to historical data.
FR 5 | The system shall be able to use the photometric data output from the image processing subsystem to compare to historical data.
FR 6 | The software subsystem shall have the capability to detect an event.
Requirements
Algorithms Flow Chart
Algorithms Machine Learning

## Slide 51: Algorithms Flowchart
Thresholding
Statistical Analysis
Machine Learning
Image Processing Output
POL Estimation
Nominal Position, Velocity,
Light Intensity, Color Data
Mean, Variance
Maximum &
Minimum Allowable Values
Pattern Recognition,
Object Classification, Convolutional Techniques
Deviation
No
Yes
Send Alert
Store Data
Requirements
Algorithms Machine Learning
Algorithms Flow Chart
Notes: We will take two images
How confidence??? Metric?
Visualize threshold?
P(detected) = P(detected | occured) + P(detected | !occured)
^? ^tied to confidence ^false positive

## Slide 52: Algorithms Machine Learning
Nominal State
Close Approach
Maneuver
Docking
Collision
Astrometric Input Data
Photometric Input Data
Additional Input Data
Hidden Layer(s)
Input Layer
Output Layer
Model Visualization
Two-Line Elements
Visual Magnitude/Color Data
Raw Image Data
Classification
Requirements
Algorithms Flow Chart
Algorithms Machine Learning
Notes: Say this: 70% of data will be training, 30% of data will be testing in terms of historical data
TensorFlow: intuitive high-level API, lets developers easily build and deploy ML powered applications.

## Slide 53: Status Summary and Strategy
Project Overview
Baseline Design
Feasibility of Design
Summary and Strategy

## Slide 54: Feasibility Summary
Feasibility Studied | CPE | Status
Weather Protection | 1 | Feasibility Confirmed
Power | 2-6 | Feasibility Confirmed (Pending Battery Life)
Optical System | 3,4,5 | Feasibility Confirmed
Orbit Determination | 4,5 | Feasibility Confirmed
Image Processing | 2,3 | Feasibility Confirmed
Algorithm | 4,5,6 | Feasibility Confirmed
Feasibility Summary
Acknowledgements
Budget & Finance
Future Work

## Slide 55: Budget & Finance
$5000 from Aerospace Department
  Covers optics, supporting electronics, housing.
$493 from EEF
  Covers processor
Lens and Sensor are large (and unavoidable) money sinks
Power is costly due to needed battery life
Processor needed for image processing
  Reduces data transmission to just astrometric and photometric data
  Sending whole images would be too slow
Feasibility Summary
Acknowledgements
Budget & Finance
Future Work
Notes: Pie chart budget, overview by subsystem
Send to backup (not if funding is close, or EEF is key!)

## Slide 56: Timeline/Future Work
Hardware
Enclosure
  Thermodynamic considerations
  Finalize Design - Before CDR
Optical
  Select Sensor
  Select Lens Brand
  Determine adapter requirements
Software
Processing
  Develop a working local Astrometry.net code
Orbit Determination
  Develop accurate method of angle estimation
  Automate usage of ODTK
  Implement Kalman Filter
Analysis
  Develop thresholding and statistical analysis software
  Write/train the machine learning event detection system
Feasibility Summary
Acknowledgements
Budget & Finance
Future Work

## Slide 57: Acknowledgements
L3Harris
Edward T. Brown
Advisors
Professor Mah
Dr. Jelliffe Jackson
Dr. Kathryn Wingate
Dr. Holzinger
Dr. Coder
Teaching Assistants
Emma Markovich
Colin Claytor
Feasibility Summary
Acknowledgements
Budget & Finance
Future Work

## Slide 58: Questions?

## Slide 59: Appendix

## Slide 60: Appendix Table of Contents
Organization
Electronics
Optics
Orbital Determination
Enclosure
Mount
Algorithm

## Slide 61: Organization

## Slide 62: References
[1] Astrometry.net: https://iopscience.iop.org/article/10.1088/0004-6256/139/5/1782
[2] Lockheed Martin Probabilistic Assessment of Space Threats (PAST): https://amostech.com/TechnicalPapers/2019/Machine-Learning-for-SSA-Applications/DiBona.pdf
[3] Coder, R. D. & Holzinger, M. J. (2016), “ Multi-objective design of optical systems for space situational awareness,” Acta Astronautica, 128, 669–684. https://doi.org/10.1016/j.actaastro.2016.07.008
[4] MLX90614 IR Thermometer Datasheet. https://www.sparkfun.com/datasheets/Sensors/Temperature/SEN-09570-datasheet-3901090614M005.pdf
[5] Night Radiative Cooling. https://asterism.org/wp-content/uploads/2019/03/tut37-Radiative-Cooling.pdf
[6] Clouds Energy Budget https://mynasadata.larc.nasa.gov/mini-lessonactivity/analyzing-cloud-effects-earths-energy-budget-student-activity
[7] Wikipedia: https://en.wikipedia.org/wiki/Bortle_scale
[8]Astrometry.net: http://nova.astrometry.net/
[9] Linear actuator: https://www.amazon.com/ECO-WORTHY-Actuator-Maximum-Mounting-Brackets/dp/B00NM8H5VO/ref=sr_1_4?_encoding=UTF8&c=ts&dchild=1&keywords=Linear+Motion+Actuators&qid=1633542200&s=industrial&sr=1-4&ts_id=350654011
[10] Verizon Coverage around Boulder: https://www.nperf.com/en/map/US/5574991.Boulder/3255.Verizon-Wireless/signal/
[11] Light Pollution Map: https://www.lightpollutionmap.info/#zoom=7.67&lat=40.1837&lon=-105.1400&layers=B0FFFFFFTFFFFFFFFFF
[12] Geostationary Ring: https://www.esa.int/ESA_Multimedia/Images/2008/03/The_geostationary_ring
[13] Orbital Elements: https://en.wikipedia.org/wiki/Argument_of_periapsis#/media/File:Orbit1.svg
[14] Gooding’s Method: https://link.springer.com/content/pdf/10.1007/BF00049379.pdf
[15] Comparison of Method: https://conference.sdo.esoc.esa.int/proceedings/sdc8/paper/129/SDC8-paper129.pdf
[16] Modified Gooding: https://www.researchgate.net/publication/254199485_Modifications_to_the_Gooding_Algorithm_for_Angles-Only_Initial_OrbitDetermination
[17] Batch Filtering: https://www.sciencedirect.com/science/article/pii/S0898122113004471
[18] Kalman Filtering: https://vtechworks.lib.vt.edu/bitstream/handle/10919/49102/Keil_EM_T_2014.pdf?sequence=1
[19] Kalman Filtering: https://arxiv.org/ftp/arxiv/papers/1609/1609.05225.pdf
[20] AGI: https://help.agi.com/odtk/LinkedDocuments/GoodingAnglesOnly.pdf
[21] AGI: https://help.agi.com/stk/11.0.1/Content/stk/importfiles-11.htm
[22] Pixel Coordinate Transformation: https://www.aanda.org/articles/aa/pdf/2002/45/aah3860.pdf

## Slide 63: Objectives
Subsystem | Capability | Level 1 | Level 2 | Level 3
Software - Algorithm | Detect Pattern of Life (POL) | Compare observed orbital behavior against historical POLs - inclination, semi-major axis, direction of burn, frequency of burn, brightness, and RGB value | Autonomously Distinguish POL change | Autonomously Characterize Events
Software - Data | Camera Data Collection and Storage | Camera subsystem stores data on hard drive to be physically collected and analyzed manually | Camera subsystem sends data to cloud to be downloaded and manually inputted to algorithm and analyzed | Camera subsystem sends data to cloud to be analyzed autonomously
Communication and Software | Tip and Cue | Manually send alerts to the end user based on POL deviations | The same as level 1 | Autonomously send alerts based on recognized events
Mechanical - Enclosure | Enclosure for System | Cover for the camera and lens | Enclosure with weather and sun resistance | Enclosure autonomously responds to weather conditions
Electronics | Power | Manually power on camera subsystem | Power on camera subsystem remotely | Power on camera subsystem autonomously

## Slide 64: Team Structure
Gabriel Feldman
Project Manager
Mary Hanson
Design Lead
Josef Michelsen
Electronics Lead
Nick Spens
Controls Lead
Andrew Komitor
Algorithms Lead
Vivien Blumofe
Manufacturing Lead
Hanna Galimanis
Testing Lead
Ajay Dhindsa
Astrodynamics Lead
Zach Harris
Data Flow Lead
Noah Avery
Systems Lead
Sam Alvis
Finance Lead
Sam Alvis
Vivien Blumofe
Sam Alvis
Nick Spens
Zach Harris
Noah Avery
Andrew Komitor
Zach Harris
Ajay Dhindsa
Andrew Komitor
Vivien Blumofe
Nick Spens
Josef Michelsen
Gabriel Feldman
Hanna Galimanis
Zach Harris
Gabriel Feldman
Gabriel Feldman
Vivien Blumofe
Hanna Galimanis
Nick Spens
Josef Michelsen
Andrew Komitor
Ajay Dhindsa
Noah Avery
Vivien Blumofe
Mary Hanson
Mary Hanson
Sam Alvis

## Slide 65: Project Breakdown Structure
Notes: Combine with 13 and 14

## Slide 66: Electronics

## Slide 67: Power Feasibility
Power Usage | Voltage Difference (VDC) | Average Power Required (W) | Maximum Required Power (W)
Linear Actuator | 12 | 9.6 | 36
Onboard Computer | 19 | Variable | 65
Camera | 12 | 5.75 | 36
IR Thermometer | 5 | 0.0075 | 0.0075
Total | 36 | Variable | 101.0075 < Max Available Power
Power Source | Voltage Difference (VDC) | Voltage Difference (VAC) | Power (Wh) | Worst Case Total Run Time (h)
Ecoflow River | 20,13.6, 2x5 | 3x120 | 720 | 7.13
Notes: Table, not list
Power, voltage, name, etc.
State W < W_max
Fix graph, label levels, make the lower voltage time more visible (Also should be W not V??)

## Slide 68: Processor Feasibility
Requirement | Description | Feasibility
Data storage | 64 Gb of storage >~50 Gb required | Feasible
Processing Power | Wraith and Ghost tested on a 2.9 Ghz processor with processing times of ~10 seconds<Our 3.6 Ghz processor | Feasible

## Slide 69: Temperature considerations
Operating Temperatures
  Linear Actuator: -26 to +65 C
  Power Source: -20 to 45 C
  Onboard Computer: 0 to +50 C
  Sensor: - 5 C to 50 C
Average Environmental Temp: (March)
  Nederlands: 6 / -9 ˚C
  Lyons: 13 / 2˚C
Will need to analyze weather data to determine optimal testing days
  Days with no precipitation
  Clear Days (little to no clouds)

## Slide 70: Optics

## Slide 71: Chart Depicting Focal Length FOV Capability
Provided By : User
https://www.nikonians.org/reviews/fov-tables

## Slide 72: Dedicated Astrophotography Sensor Parameters
Mirrorless
Full frame
26.1 Megapixels
RGB
Pixel size: 3.76µm square

## Slide 73: Hobbyist Sensor Parameters
Mirrorless
Full frame
30.3 Megapixels
RGB
Pixel size: 5.36µm square

## Slide 74: Control Variables
(Coder, Holzinger, 2016)
Design Variables
F-number (N)
aperture diameter (D)
pixel size (p)
D
f
1920
1080
_ µm
N = f/D
P
Notes: Box N, D, p in equation (or terms they impact)

## Slide 75: Optical System Nomenclature
Symbol | Value [units] | Description
SNRalg | 6 | Signal to Noise Ratio
mi | 40 (pixels) | Initial # of pixels occupied by space object (SO) image
𝜱alg | 5.6*E10 (photons/s/m2) | Photon Flux Density
qp,sky | 120 (e−/s/pixel) | Photon Flux per pixel from background radiant intensity
qp,dark | 0.00391 (e−/s/pixel) | Photon flux of CCD (Charge Coupled-Device) dark current
𝛕atm | 0.69 | Transmittance of optics atmosphere
𝛕opt | 0.9 | Transmittance of optics assembly
QE | 0.66 | Quantum Efficiency

## Slide 76: Orbital Determination

## Slide 77: Orbit Determination Full Requirements Breakdown

## Slide 78: ODTK Equations and Assumptions: Gooding Method Derivation
General Methodology
Using three pairs of angles, determine unit vectors ȓ1 and ȓ3
Find position vector rj of the groundstation.
Assume value for range, 𝜌1 and 𝜌3 . Use range and unit vectors to determine position vectors R1 and R3 of satellite
𝜌jȓ1 = Rj - sj
Where sj is the position vector of the groundstation.
Notes: Equations? Just input to output feels weird

## Slide 79: ODTK Equations and Assumptions: Gooding Method Derivation
General Methodology
Begin Iteration
Generate Estimated Orbit by solving Lambert’s Problem
  From Lambert’s Problem, will receive estimate of v1 of satellite
  Now have complete orbit made from R1 and v1
Propagate R1 and v1 to obtain estimates for R2 and v2
  Calculate 𝜌2 as an estimate of the true range vector 𝜌2
Iterate 𝜌1 and 𝜌3 via Newton-Raphson Method to obtain better estimate of 𝜌2
End
Notes: Equations? Just input to output feels weird

## Slide 80: Orbit Determination - GoodingIOD
Angle pair option 1:
  αj = right ascension (ground or space based)
  δj = declination (ground or space based)
  tj = time tag
  sj = platform position
Angle pair option 2:
  ςj = azimuth (ground based)
  ηj = elevation (ground based)
  tj = time tag
  sj = platform position
Note: j = 1,2,3 and t1 < t2 < t3 and must be “sufficiently large”
Notes: Reference: https://help.agi.com/odtk/LinkedDocuments/GoodingAnglesOnly.pdf

## Slide 81: Orbit Determination: GoodingIOD Time Delay Error
Reference: AGI
Notes: Reference: https://help.agi.com/odtk/LinkedDocuments/GoodingAnglesOnly.pdf

## Slide 82: Orbit Determination: GoodingIOD Error σ = 2.5 arcsec
Reference: AGI
Notes: Reference: https://help.agi.com/odtk/LinkedDocuments/GoodingAnglesOnly.pdf

## Slide 83: Orbit Determination: GoodingIOD Error σ = 5 arcsec
Reference: AGI
Notes: Reference: https://help.agi.com/odtk/LinkedDocuments/GoodingAnglesOnly.pdf

## Slide 84: Enclosure

## Slide 85: Alternative Enclosure Design
Enclosure roof is made of a tarp attached to two motor-driven wheels. The enclosure design was changed due to:
More moving parts means more changes of failure
Don’t need to move camera so don’t need to have full view of sky, only where camera is pointing

## Slide 86: Infrared Thermometer
An IR thermometer pointed along the camera's line of sight will remotely determine the temperature of the sky
A cloudy sky reflects heat back to Earth, while a clear sky does not:
Cloudy skies are around 10°C warmer than clear skies
If skies are cloudy, observations will not be taken
Image from My NASA Data
Enclosure Characteristics
IR Thermometer
Driving Requirements
Door Actuation
Notes: visuals

## Slide 87: Infrared Thermometer Characteristics
MLX90614 Infrared Thermometer:
5V DC
0.02 °C resolution
Sensor temperature range -40 to +125 °C
Observation range -70 to +380 °C
Image from Sparkfun
Notes: visuals

## Slide 88: Acrylic Characteristics
Density: 0.043 lb/in^3
Temperature range: -40° to 170° F
Tensile Strength: 10,500 psi
Image from McMaster-Carr

## Slide 89: Mount

## Slide 90: Mount Driving Requirements
FR 9 | The system shall have the capability to move the electro-optical subsystem.
DR 9.1 | The electro-optical subsystem shall be able to change azimuth angles to collect data on geosynchronous satellites.
DR 9.2 | The electro-optical subsystem shall observe the elevation angles needed to collect data on geosynchronous satellites.
Driving Req.
Feasibility Summary

## Slide 91: Mount Feasibility
Magnus VPH-20 Video Pan & Tilt Fluid Head
Functionality checks
  Pan (azimuth angle) capabilities - manual
    360°
  Tilt (elevation angles) capabilities - manual
    180°
Load checks
  Supports 11 lbs loads
  Individual pan-and-tilt tension control and locks
  Locking pins
Interface checks
  3/18” -16 tripod mount thread
  1/4" -20 camera screw
Baseline Design Mount
✅
✅
✅
Driving Req.
Feasibility Summary

## Slide 92: Mount Full Requirement Breakdown

## Slide 93: Pervious Mount Choice (Not in Consideration)
Bescor MP-101 Motorized Pan & Tilt Head
Connection interfaces
  Supports 6 lbs
  ¼”-20 camera mount screw
  ¼”-20 tripod mount screw
  Remote for control
Power
  4 AA batteries (what will be used)
  PS-260 AC power supply (will not be used)
Pan (azimuth angle) capabilities
  +/- 170°
Tilt (elevation angles) capabilities
  +/- 15°
Baseline Design Mount

## Slide 94: Algorithm

## Slide 95: Image Processing Feasibility
Image at tn
Image at tn-1
Notes: What’s going on here?

## Slide 96: Budget

## Slide 97: Budget
Part | Part Description | Cost | Budget | Margin
Optics |  | $3,398.00 | $3,400.00 | $2.00
Lens | 135 f/1.8 lens | $1,399.00 | $1,400.00 | $1.00
Sensor | ZWO ASI 2600 MC Pro | $1,999.00 | $2,000.00 | $1.00
Electronics |  | $493.00 | $1,593.00 | $1,100.00
Processor | Udoo | $493.00 | $493.00 | $0.00
Communications |  |  | $100.00 | $100.00
Power |  |  | $1,000.00 | $1,000.00
Housing |  | $0.00 | $500.00 | $500.00
Acrylic |  |  | $100.00 | $100.00
Mount |  |  | $100.00 | $100.00
Motor |  |  | $100.00 | $100.00
Other |  |  | $200.00 | $200.00
Other |  | $0.00 | $0.00 | $0.00
Astrodynamics Software | ODTK, for Astrodynamic analysis | $0.00 |  | 
TOTAL |  | $3,891.00 | $5,493.00 | $1,602.00
Notes: Pie chart budget, overview by subsystem
Send to backup (not if funding is close, or EEF is key!)