## Slide 1: S P E C T E R Test Readiness Review
February 16th, 2022
ASEN-011 Team 9
Company Customer
L3Harris
Faculty Advisor
Professor John Mah
Presenters
Hanna Galimanis, Noah Avery, Vivien Blumofe, Mary Hanson, Sam Alvis, Andrew Komitor, Gabriel Feldman
Additional Team Members
Josef Michelsen, Nick Spens, Zach Harris, Ajay Dhindsa

## Slide 2: Table of Contents
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 3: Project Overview
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 4: Purpose & Mission Statement
Purpose: collect data on satellites in GEO and determine if a significant event has occurred or is imminent
  Maneuvers
  Close encounters between two or more satellites (including docking and collisions)
  Breakups
The Satellite Position Estimation Collision Tracking & Event Recognition (SPECTER) mission will monitor satellite movements in geostationary orbit to provide space domain awareness.
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 5: Concept of Operations
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 6: Concept of Operations
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 7: Concept of Operations
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 8: Concept of Operations
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 9: Concept of Operations
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 10: Concept of Operations
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 11: Image Software CONOPS
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 12: Objectives
Subsystem | Capability | Level 3 Success
Software - Algorithm | Detect Pattern of Life (POL) | Autonomously compare observed orbital behaviors against historical POLs, distinguish changes, and characterize events
Software - Data | Camera Data Transfer and Storage | Camera subsystem sends data to server to be analyzed autonomously
Communication and Software | Tip and Cue | Autonomously send alerts based on recognized events
Mechanical - Enclosure | Enclosure for System | Enclosure autonomously responds to weather conditions
Electronics | Collection and Processing | Collect and Process image data autonomously
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 13: Functional Block Diagram
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 14: Enclosure Design - Exterior
24 in
20 in
18 in
18 in
IR Thermometer
Sparkfun MLX90614
Padlock
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 15: Enclosure Design - Cutaway
Lens
Canon 135mm lens
Sensor
ZWO ASI 2600 MC Pro
Linear Actuator
Eco Worthy 6 inch Linear Actuator
Battery
EcoFlow RIVER Battery
Computer
Beelink Mini PC
Arduino Uno
Camera Mounting System
ZWO Holder Ring + Neewer Professional Panoramic Ball Head
IR Thermometer
Sparkfun MLX90614
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 16: Critical Project Elements
CPE | Importance
1. GEO Observation | SPECTER must be capable to observe satellites to facilitate data collection
2. Data Collection | Data collection is required for future POL comparison
3. POL Determination | POL’s are necessary to monitor for deviations from expectations
4. Event Detection | The system must be able to use the astrometric and photometric data output from the image processing subsystem to compare to historical data. To alert end users of a POL deviation, the SPECTER system must have the capability to detect the event.
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 17: Project Updates
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 18: Updates
New POC Dr. Thomas Gemmer
  Sr. Specialist, Astrodynamics Systems Development - Space Domain Awareness (SDA) Division
Acrylic enclosure finger joints for increased rigidity
Onboard processor delayed
CAD close-up of finger joints
CAD of structure with finger joints
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 19: Schedule
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 20: Gantt Chart
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 21: Test Readiness
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 22: Major Tests to be Conducted
Type | Test Name | CPE and FR | Completion Date | Status
Subsystem - Optics | OPT.7: LSM | CPE 1 FR 1 | 2/20/22 | Ready to Test
Subsystem - Data Flow | DAT.2: Integrated Communications | CPE 2 FR 3 | 3/20/22 | Not Started
Subsystem - Orbit Determination | ORB.1: Semi-Major Axis Determination | CPE 3 FR 4 | 3/20/22 | Not Started
Subsystem - Algorithm | ALG.2: Semi-Major Axis POL ALG.7: Maneuver Event Detection | CPE 2 FR 3 | 3/20/22 | Not Started
System - Structure & Optics | STR.3: Stability Test | CPE 1 FR 1 | 2/20/22 | Manufacturing
System | SYS.5: Full System Day in the Life (Field Testing) | CPE All FR All | 4/10/22 | Not Started
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 23: Testing Phase 1: Component Testing
Component | Test Name | Completion Date | Status
Lens | OPT.2: Optical Alignment | 2/7/22 | Completed
Lens | OPT.3: Sharpness | 2/7/22 | Completed
Lens | OPT.4: Focus Accuracy | 2/7/22 | Completed
Lens | OPT.5: Distance Focus | 2/7/22 | In Progress
Linear Actuator | STR.1: Force | 2/7/22 | In Progress
IR Sensor | ELE.1: IR Sensor | 2/13/22 | Completed
Temp Sensor | ELE.2: Temp Sensor | 2/13/22 | Completed
Humidity Sensor | ELE.3: Humidity Sensor | 2/13/22 | Completed
Image Processing | DAT.2: Image Processing | 2/16/22 | In Progress
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 24: Completed Component Tests Summary
OPT.2: Optical Alignment (Completed 2/9/22)
  PASS: By visual inspection - the center circle is in focus and has no warping
OPT.3: Sharpness (Completed 2/3/22)
  PASS: By visual inspection - lockers in aero workshop are clear and in focus
OPT.4: Focus Accuracy (Completed 2/3/22)
  PASS: By visual inspection - the number “10” is in focus
Project Overview
Project Updates
Schedule
Test Readiness
Budget
Pass
Fail

## Slide 25: Completed Component Tests Summary
ELE.1: IR Sensor (Initial Test 2/12/22)
ELE.2: Temp Sensor (Initial Test 2/12/22)
ELE.3: Humidity Sensor (Initial Test 2/12/22)
  Testing in Progress: Sensors work but accuracy cannot yet be confirmed
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 26: Testing Phase 2: Subsystem Testing
Subsystem | Test(s) Name | Completion Date | Status
Optics | OPT.1: Basic Functionality OPT.6: Pointing OPT.7: LSM* | 2/20/22 | Completed - Appendix Not Started - On Track In Progress - Presented
Structures | STR.2: Thermal Model* STR.4: Water Protection | 2/20/22 | Not Started - On Track Not Started - On Track
Orbit Determination | ORB.1-7: All Keplerian Element Tests ORB.8: Close Approach Event Prediction | 3/20/22 | In Progress - Presented Not Started - On Track
Electronics | ELE.4: Power Interface ELE.5: Power Failure ELE.6: Communication/Data Interface | 2/20/22 | Not Started - On Track Not Started - On Track Not Started - On Track
Data Flow | DAT.1: Communications DAT.3: Alert Timing* | 3/20/22 | In Progress - Presented In Progress
Algorithm | ALG.1-6: POLs ALG.7-10: Events | 3/20/22 | In Progress - Presented In Progress - Presented
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 27: OPT.7: Limited Stellar Magnitude
Objective: Validate that the LSM model correctly predicts the LSM of the system
Setup, Facilities, and Equipment
  Outside aerospace building at night, lens, sensor, computer, tripod
Procedure
  Setup the lens, sensor, computer system
  Use live feed to adjust the settings (focus, gain, exposure)
  Point the system 40˚ elevation south and collect 10 images
  Run collected image through ASTAP to obtain name of objects in the image
Success Criteria
  Confirm an object with a LSM ≥ 13
CPE 1 GEO Observation
FR 1 The system shall observe satellites in geostationary orbit
Test By Date: 2/20/22 Status: Ready to test
Sensor
Lens
Laptop/ Capture API
Tripod
12v Power & USB
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 28: Optics Status
Tasks Completed:
Sensor takes clear images w/ ASICAP
Sensor successfully integrated with NINA
Risk Description | Mitigation | Pre-mit. | Post-mit.
System does not achieve required LSM of 13, 13-15 ideal | Test OPT.7 Success: Validates the system can observe an LSM in the required range | 12 | 3
Tasks To Do:
Capture clear images with the optic system at night
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 29: DAT.2: Integrated Communication Test
Objective Confirm communication functionality between the onboard (where data is collected) and offboard computer (where data is processed)
Setup, Facilities, and Equipment
  Senior projects room, onboard and offboard computer, 4G hotspot and coverage
Procedure
  Connect onboard computer to 4G hotspot
  On onboard computer assign Test.csv for upload
  Run Google API upload on the onboard system
  Run Google API download on offboard system
Success Criteria
  Download script matches uploaded script
  Whole process is under a minute
CPE 2 Data Collection
FR 3 Collected astrometric and photometric data shall be stored
Test By Date: 3/20/22 Status: Not Started
Google Drive API
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 30: DAT.2 Integrated Communications Status
Tasks Completed:
Upload functionality
Download functionality
Test .CSV file created
Risk Description | Mitigation | Pre-mit | Post-mit
Data is corrupted or the wrong file is transferred | Test DAT.2 Success: Validates the system can transmit correct data without corruption | 15 | 5
Tasks To Do:
Receive 4G hotspot
Automated File ID Recovery
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 31: ORB.1: Semi-Major Axis Determination
Objective: Verify the semi-major axis of a satellite can be determined
Setup, Facilities, and Equipment
  Senior projects room, computer, L3 data set, historical data, Python, ODTK
Procedure
  Obtain Right Ascension / Declination (𝛼, 𝛿) angle pair measurements from the provided L3 data set
  Perform orbit determination with ODTK
  Compare the calculated semi-major axis to spacetrack historical database to determine difference
Success Criteria
  Calculated semi-major axis is within 100 km of historical semi-major axis
CPE 3 POL Determination
FR 4 Use astrometric data from the image processing subsystem to compare to historical data
Test By Date: 3/20/22 Status: In Progress
L3 Data Set
Historical Data Set
ODTK API
Results
Error
ID: 26624
ODTK Data
Historical Data
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 32: Orbit Determination Status
Tasks Completed:
Tested ODTK Program Functionality
Performed manual orbit determination with ODTK
Risk Description | Mitigation | Pre-mit | Post-mit
Accurate orbital determination methods are needed to perform event detection | ORB.1 Success: Validates the orbital determination can predict within a tolerable error, giving confidence in further event classification | 16 | 3
Tasks To Do:
Complete API in Python for automation
Complete integration with other software / hardware
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 33: ALG.2: Semi-Major Axis POL
Objective Verify the system has the ability to create Semi-Major Axis (a) POL deviations
Setup, Facilities, and Equipment
  Senior projects room, computer, test data, historical data from Space-Track.org
Procedure
  Create semi-major axis POL for 50 different satellites using historical truth data
  Run test data through the algorithm to find deviations in POL
Success Criteria
  By visual inspection and error analysis, confirm the numerical deviations are consistent with what is expected.
  Ensure that type-I and type-II error rates are both below 10% for success
CPE 3 POL Determination
FR 2 Software shall determine the POL of satellites in geostationary orbit from historical data
Test By Date: 3/20/22 Status: Not Started
Historical Data Set
L3Harris Data
POL Script
Results
Error
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 34: ALG.7: Maneuver Event Detection
Objective Verify the system has the ability to detect a maneuver.
Setup, Facilities, and Equipment
  Senior projects room, computer, test data, historical data from Space-Track.org
Procedure
  Identify 50 historical data sets - 25 w/ known maneuver, 25 w/ known lack of maneuver
  Input each test data set into the algorithm
  Document whether the system alerts or not
Success Criteria
  Algorithm should detect the 25 maneuvers
  Ensure that type-I and type-II error rates are both below 10% for success
CPE 4 Comparison of Collected Data to Historical Data
FR 6 The software subsystem shall have the capability to detect an event
Test By Date: 3/20/22 Status: Not Started
Historical Data Set
Analysis
Event Detection
Alert and Confidence
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 35: ALG.7: Maneuver Event Detection
CPE 4 Comparison of Collected Data to Historical Data
FR 6 The software subsystem shall have the capability to detect an event
Test By Date: 3/20/22 Status: Not Started
Before Prediction
After Prediction (99.6% accuracy)
Classification
Classification
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 36: Algorithm Risk
Risk Description | Mitigation | Pre-mit. | Post-mit.
The algorithm can’t create a POL | ALG. 2 Success: Validates the system can detect deviations in semi-major axis POL with minimal false positives and negatives | 20 | 8
Deviation detection is necessary to alert end user and satisfy mission objective | ALG. 7 Success: Validates the system can detect maneuvers with minimal false positives and negatives | 20 | 8
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 37: Algorithm Status
Tasks Completed:
  Thresholding Algorithm
  Machine Learning Thresholding Analogue
  Recurrent Neural Network Initial Model
Tasks to Complete:
  Recurrent Neural Network Refined Model
  Bootstrapping Algorithm (for RGB values)
  Error Analysis
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 38: Testing Phase 3: System Testing
Test Name | Completion Date | Status
STR.3: Stability | 2/20/22 | Manufacturing - Presented Here
Full System Software Test | 3/6/22 | Not Started - On Track
Structure View Test | 3/6/22 | Not Started - On Track
Full System Test | 3/6/22 | Not Started - On Track
Full System Day in the Life (Field Testing) | 4/10/22 | Not Started - Presented Here
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 39: STR.3: Stability Test Plan
Objective: Verify that during standard operations the sensor is stable and image collection is not disturbed
Setup, Facilities, and Equipment
  Outside the aerospace building, structure, all components
Procedure
  Place the structure with all internal components outside
  Point the structure at a wall or building with a geometric pattern
  Run the system for three hours and collect 180 images
Success Criteria
  No images taken during the test are blurred or distorted
CPE 1 GEO Observation
FR 1 The system shall observe satellites in geostationary orbit
Test By Date: 2/20/22 Status: Manufacturing
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 40: Structure Stability Risk
Risk Description | Mitigation | Pre-mit. | Post-mit.
If On-Board Electronics cause internal vibrations/movement the captured images could be distorted | STR. 3 Success: Test proves onboard electronics do not cause detectable internal vibrations/movements | 20 | 4
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 41: SYS.5: Field Testing
Objective Confirm that the full system functions as expected during operations for eight hours overnight
Setup, Facilities, and Equipment
  Exterior location, full system, back up computer
Procedure
  Follow packing procedure and transport the system to test location
  Deployment procedure to secure the components
  Power-on procedure to power-on and calibrate
  Operations procedure to place the system in an operations mode
  Leave the system outside and running for eight hours
  Collect the system using packing procedure
CPE All CPE’s
FR All Functional Requirements
Test By Date: 4/10/22 Status: Not Started
Offboard
Computer
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 42: SYS.5: Field Testing
Success Criteria
  System continuously takes clear images for 8 hours
  Electronics collects and stores temperature and humidity data
  RA and Dec are calculated for all images taken
  Onboard computer uploaded data and offboard computer downloads data within 1 minute of image capture
  Orbit determination method calculates all Keplerian orbital elements
  Algorithm event detection has type-I and type-II errors less than 10%
CPE All CPE’s
FR All Functional Requirements
Test By Date: 4/10/22 Status: Not Started
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 43: Risk Mitigation - Tests Summary
Severity |  |  |  |  |  | 
 |  | Negligible 1 | Minor 2 | Moderate 3 | Major 4 | Severe 5
 | Very Likely 5 |  |  |  | Enclosure | 
 | Likely 4 |  |  |  | OD | Alg
 | Possible 3 |  |  |  | Optics | Data Comm.
 | Not Likely 2 |  | Enclosure |  | Alg | 
 | Rare 1 |  |  | OD Optics |  | Data Comm.
Likelihood Level
System Risk | Test
Optics | OPT. 7 LSM Test
Enclosure | STR. 3 Stability Test
Data Comm. | DAT.2 Integrated Communications Test
OD | ORB. 1 Semi-Major Axis Test
Algorithm | ALG. 2 Semi-Major Axis POL ALG. 7 Maneuver Event Detection
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 44: Major Tests to be Conducted
Type | Test Name | CPE and FR | Completion Date | Status
Subsystem - Optics | OPT.7: LSM | CPE 1 FR 1 | 2/20/22 | Ready to Test
Subsystem - Data Flow | DAT.2: Integrated Communications | CPE 2 FR 3 | 3/20/22 | Not Started
Subsystem - Orbit Determination | ORB.1: Semi-Major Axis Determination | CPE 3 FR 4 | 3/20/22 | Not Started
Subsystem - Algorithm | ALG.2: Semi-Major Axis POL ALG.7: Maneuver Event Detection | CPE 2 FR 3 | 3/20/22 | Not Started
System - Structure & Optics | STR.3: Stability Test | CPE 1 FR 1 | 2/20/22 | Manufacturing
System | SYS.5: Full System Day in the Life (Field Testing) | CPE All FR All | 4/10/22 | Not Started
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 45: Budget
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 46: Budget Updates Procurement Updates
$1017.21 in margin
  $439 of that due to EEF
  Also $250 set aside for gas (conservative)
  All sections under budget (structure, electronics, optics, other)
Enough margin to cover any single part failure - except the sensor!
  Sensor is most critical part!
All parts sourced, almost all procured!
Processor (Critical - Electronics)
  Beelink PC through Amazon
  Miscommunication w/ Aero Finance
Linear Actuator (Critical - Structures)
  6” ECO-WORTHY Linear Actuator
  Accidentally ordered 2” Actuator due to link
  Miscommunication w/ Aero Finance
Other Parts Arriving Soon
  Wires (Amazon as well)
  Mobile Hotspot (Originally not need until field test, now to be ordered this week)
Future Purchases
  Lens Warmer (Not needed until field test)
  Hotspot Data Plan (Not needed until field test)
Project Overview
Project Updates
Schedule
Test Readiness
Budget

## Slide 47: Questions?

## Slide 48: Appendix

## Slide 49: Risk Description
System Risk | Risk Description | Test
Optics | An LSM of 13 is required for the optical system, with 13 - 15 ideal | OPT. 7 LSM Test
Enclosure | The enclosure must be stable in order for the optical system to capture sharp images | STR. 3 Stability Test
Data Communication | Data is corrupted or the wrong file is transferred. | DAT.2 Integrated Communications Test
OD | Accurate orbital determination methods are needed to predict event detection | ORB. 1 Semi-Major Axis Test
Algorithm | The algorithm must be able to create a POL and detect a deviation from created POLs | ALG. 2 Semi-Major Axis POL ALG. 7 Maneuver Event Detection

## Slide 50: Optics

## Slide 51: Dedicated Astrophotography Sensor Parameters
ZWO ASI2600MC Pro (color)
Mirrorless
Full frame
26.1 Megapixels
RGB
Pixel size: 3.76µm square
6248×4176 @ 3.51fps
Exposure Range: 32μs-2000s
Read Noise: 1.0-3.3e
QE peak: over 80%
Dimensions: 90mm Diameter
Weight: 700g

## Slide 52: Limiting Stellar Magnitude (LSM)
Majority of GEO Satellites in range m = 11-14
Customer requires 13, 14-15 ideal
Aperture diameter (D) most important for urban areas
Assumptions:
  Optical System is in ‘stare’ mode thus relative velocity is (⍵) = velocity of Satellite
  GEO Satellites have circular orbits
  Satellites treated as spheres
[3] Coder, Holzinger, 2016)
13 <
-30
-25
-20
-15
-10
-5
0
10
15
20
25
5
Sun
Full Moon
Naked
Eye Limit
GEO Satellites
Apparent Magnitude ( mv )
Notes: Better explain, use < to highlight values versus goal. Greater than
Equation too dense?

## Slide 53: Optic Options in Consideration

## Slide 54: Lens & Sensor Selection
Notes: Not enough info to stand alone
Line at 13, shade the good section
Add in 13 minimum (or maximum?) requirement

## Slide 55: Control Variables
(Coder, Holzinger, 2016)
Design Variables
F-number (N)
aperture diameter (D)
pixel size (p)
D
f
1920
1080
_ µm
N = f/D
P
Notes: Box N, D, p in equation (or terms they impact)

## Slide 56: Optical System Nomenclature
Symbol | Value [units] | Description
SNRalg | 6 | Signal to Noise Ratio
mi | 40 (pixels) | Initial # of pixels occupied by space object (SO) image
𝜱alg | 5.6*E10 (photons/s/m2) | Photon Flux Density
qp,sky | 120 (e−/s/pixel) | Photon Flux per pixel from background radiant intensity
qp,dark | 0.00391 (e−/s/pixel) | Photon flux of CCD (Charge Coupled-Device) dark current
𝛕atm | 0.69 | Transmittance of optics atmosphere
𝛕opt | 0.9 | Transmittance of optics assembly
QE | 0.66 | Quantum Efficiency

## Slide 57: Electronics

## Slide 58: Schematic

## Slide 59: Sampling Rate, Resolution, and Accuracy
 | Resolution | Accuracy | Sampling Rate
IR Thermometer | 0.02 C | 0.5 C | 5 min
Temp Sensor | 0.1 C | 0.5 C | 5 min
Humidity Sensor | 0.1% | 2% | 5 min
Astrophotography Sensor | 6248×4176 pixel | NA | 3.51fps

## Slide 60: Power Source
Ports
3 x AC Output 120Vac (50Hz/60Hz)
2 x USB-A Output 5Vdc, 2.4A
1 x USB-A Fast Charge 5V/2.4A, 9V/2A, 12V/1.5A
1 x USB-C Output 5Vdc, 9Vdc, 12Vdc, 20Vdc , 5A
1 x Car Power Output 13.6Vdc 10A
2 x DC5521 Output 13.6Vdc, 3A
Specs
Discharge Temperature -20 to 45 C
720Wh capacity
Lithium-ion cell chemistry
Performance begins to degrade below 0 C

## Slide 61: Processor
Ports
4 x USB 3.0
1 x DC Jack ()
1 x RJ45
1 x Type-C
1 x Clear CMOS
1 x Audio Jack
2 x HDMI
Specs
CPU - i5-8279U 2.4GHz, Turbo 4.1GHz
CPU Core - 4 Cores 8 Threads
Operating System - Windows 10 Pro
Storage - 512GB
RAM - 16G

## Slide 62: Proof of Processor Capability
Actual Processor - Intel Core i5-8279U - 2.4 GHz with 4.1 GHz max
Test Processor 1 - Intel Core i7-4500U - 1.8 GHz with 2.4 GHz max
ASTAP = 32% max of test processor 1 CPU usage , 1.1 second run time
NINA = 13.5% max of test processor 1 CPU usage , 3.3 second run time (plate solving)
Test Processor 2 - i5-1135G7 -- 2.4 GHz with 4.2 GHz max
Satellite Identification = 40% max of test processor 2 CPU usage , 11 second run time

## Slide 63: Power Analysis
Maximum Power Draw = 93W
Run Time with Maximum Power Draw = 7.74 Hours
Reasonable Assumptions:
CPU (28W Thermal Design Power, TDP)will never be maxed out with our low computation requirements
GPU (15W TDP) will never be maxed out with no need for graphics processing

## Slide 64: Temperature considerations
Operating Temperatures
  Linear Actuator: -26 to +65 C
  Power Source: -20 to +45 C
  Onboard Computer: -10 to +45 C (30-90% Humidity)
  Sensor: -5 C to +50 C
Average Environmental Temp: (March)
  Nederlands: 6 / -9 ˚C
  Lyons: 13 / 2˚C
  Brainard Lake: 3/-10˚C
  Clear Lake (Cabin):
Will need to analyze weather data to determine optimal testing days
  Days with no precipitation
  Clear Days (little to no clouds)
  Wind Speeds less than 35 mph

## Slide 65: Communication
Location Requirements:
Expecting to transmit below 1 kbs
Low light pollution (need coverage in suburban to rural areas)
Using a Moxee 4G Mobile Hotspot as well as a Simple Mobile / T-Mobile Plan
FCC map of T-Mobile coverage confirms at least 1-5 Mbps coverage in many locations around Boulder
Notes: FCC provides data on regions with at least 1-5 Mbps coverage
Light pollution maps based on

## Slide 66: Linear Actuator Control
L298N
Dual channel H-Bridge driver
Accepts external power supply
Controls polarity of output to motor using any two regular digital high-low arduino pins
Controls speed using PWM pin
Usable as a 5V power supply when given 7V or more

## Slide 67: Temperature Comparison between Sensors

## Slide 68: Software

## Slide 69: Software CONOPS
Image at tn
Image at tn-1
Image Processing
Right Ascension
Declination
Timing
RGB
Brightness
ODTK
Keplerian Elements
(a, e, i, 𝜃, Ω, ω)
Orange = Data to be processed
Green = Data ready for algorithm
Blue = Process / Function
ML Algorithm
Tip and Cue
Historical Keplerian elements
Statistical
Thresholding
Upload to Drive
Download from Drive
Project Overview
Project Updates
Schedule
Test Readiness
Budget
Notes: vivien? I can do this but i'm not sure what goes in the last bubble

## Slide 70: Machine Learning Justification
Time dependence of data
Pattern recognition
Regression
Project Overview
Baseline Design
Requirement Satisfaction
Risk
V&V
Project Planning

## Slide 71: DAT.1 Communications Software Test
Objective:
  This test will confirm the communication functionality of the Google API Software.
Setup, Facilities, and Equipment:
  Senior Project Room, 2 laptops, Google API Code
Procedure:
  Assign Test.csv to be uploaded
  Run Google API upload script
    Time the runtime of script to time of successful upload
  Check drive for file
  On another laptop run Google API download script
    Time the runtime to time of download
  Compare downloaded script to uploaded script
Success Criteria:
  The correct file is uploaded on one laptop and downloaded on another without corruption.

## Slide 72: DAT.3 Image Processing Production Test
Objective:
  This test will determine if the image processing system on the onboard computer works as expected.
Setup, Facilities, and Equipment:
  Senior Projects Room, Optical Sensor, and Onboard Computer
Procedure:
  Run sample images through standalone image processing script
  Verify that the correct pixels are identified as satellites
  Run sample images through ASTAP
  Manually convert pixel coordinates to RA and Dec values
  Turn on on-board computer
  Start process timer
  Pass sample images through embedded script sequence
  Verify that the RA and Dec output is correct by comparison to earlier values
  Record process time
Success Criteria:
  Images are processed in under 20 seconds
  RA/Dec of all known satellites are recorded and packaged for sending.

## Slide 73: DAT.4 Alert Timing Test
Objective:
  This test ensures that an event can be detected and an alert sent within 90 minutes of the event occurring
Setup, Facilities, and Equipment:
  Senior Projects room, field team in location with 4G Cellular Coverage and the onboard and offboard systems
Procedure:
  Travel to location with 4G cellular service
  Begin the onboard script
    Time the processing
    Time Uploading
  Have the offboard system back in boulder begin their onboard script
    Time the download
  Compare the data sent and received
  Resume the onboard script
    Time the analysis
    Time till email is received (Tip and Cue)
  Compare the data packaged with that analyzed
Success Criteria:
  Alert email is sent within 90 minutes with requisite data

## Slide 74: Software Overview

## Slide 75: Data Inputs/Outputs

## Slide 76: Computation Resources - Time Constraints
5 Minute Time constraint for analysis of each image
Need time taken to compute and proof/graphs of worst/best case computation time scenarios.
1 hour to send alert to L3

## Slide 77: Computation Resources-Completed Models
Tip and Cue Model
Plate Solving Model
Photometric Collection Model
Astrometric Collection Model
Photometric Analysis Model
Astrometric Analysis Model
Arduino Model

## Slide 78: Computation Resources-To Be Completed Tests
Full Software Test
Day-In-The-Life
Communication Model with Google API
Satellite Determination
ODTK API
NINA Scraper

## Slide 79: Tip and Cue Model Output

## Slide 80: Plate Solving Model Results
File Size | 4.6 GB
Blind Solve Test Speed | 3.1 seconds
Reliability | 100% (When compared to Astrometry.net)

## Slide 81: Data Budget

## Slide 82: Example Packet

## Slide 83: NINA Camera API

## Slide 84: NINA/ASTAP Plate Solver

## Slide 85: ODTK Reports - Position Uncertainty

## Slide 86: ODTK Reports - Position Uncertainty Report

## Slide 87: Testing Appendix

## Slide 88: Functional Requirements
FR 1 | The system shall observe satellites in geostationary orbit
FR 2 | The software subsystem shall determine the POL of satellites in geostationary orbit from historical data
FR 3 | Collected astrometric and photometric data shall be stored
FR 4 | The system shall be able to use the astrometric data output from the image processing subsystem to compare to historical data
FR 5 | The system shall be able to use the photometric data output from the image processing subsystem to compare to historical data.
FR 6 | The software subsystem shall have the capability to detect an event
FR 7 | An alert shall be sent with enough time to allow for an actionable response if there is a deviation from any POL
FR 8 | An enclosure shall protect the camera and its associated electronic equipment

## Slide 89: Functional Requirements and Motivation
FR 1: Observe satellites in geostationary orbit | In order to collect data on satellites the system must have the capability to observe them in orbit.
FR 2: Determine the POL from historical data | The ability for the system to detect a deviation from a satellite’s expected movements requires a previously established POL for new data to be compared to.
FR 3: Collect & store astrometric & photometric data | Customer defined design requirement. The data must be stored in order to continue the creation of a baseline POL.
FR 4: Use the astrometric data | A successful system will be able to detect a deviation from the astrometric POL. A deviation will be detectable by comparing the astrometric POL to recently collected astrometric data.
FR 5: Use the photometric data | A successful system will be able to detect a deviation from photometric POL. A deviation will be detectable by comparing the POL to recently collected photometric data.
FR 6: Detect an event | Customer defined. For SPECTER to be successful, the system must be able to detect satellite events.
FR 7: Alert for deviation from any POL | The system needs to have the ability to communicate alerts to the end user to inform them of an anomaly within a timely manner.
FR 8: Protect the camera and associated electronics | The sensor and associated electronic equipment need to be protected from damage by weather and incident solar radiation.
Notes: Blue on sheet

## Slide 90: Critical Project Elements
CPE | Importance
1. GEO Observation | SPECTER must be capable to observe satellites to facilitate data collection
2. Data Collection | Data collection is required for future POL comparison
3. POL Determination | POL’s are necessary to monitor for deviations from expectations
4. Comparison of Collected Data to Historical Data | The system must be able to use the astrometric and photometric data output from the image processing subsystem to compare to historical data.
5. Event Detection | To alert end users of a POL deviation, the SPECTER system must have the capability to detect the event.
Notes: Zach

## Slide 91: V&V Overview
Project Overview
Baseline Design
Requirement Satisfaction
Risk
V&V
Project Planning
… = Component Test
… = Subsystem Test
… = System Test
… = Model Validation
Notes: Hanna Galimanis

## Slide 92: Testing Phase 1: Component Testing
Component | Test Name | Completion Date | Status
Lens | OPT.2: Optical Alignment | 2/7/22 | Completed - Appendix
Lens | OPT.3: Sharpness | 2/7/22 | Completed - Appendix
Lens | OPT.4: Focus Accuracy | 2/7/22 | Completed - Appendix
Lens | OPT.5: Distance Focus | 2/7/22 | In Progress
Linear Actuator | STR.1: Force | 2/7/22 | In Progress
IR Sensor | ELE.1: IR Sensor | 2/7/22 | Completed - Appendix
Temp Sensor | ELE.2: Temp Sensor | 2/7/22 | Completed - Appendix
Humidity Sensor | ELE.3: Humidity Sensor | 2/7/22 | Completed - Appendix
Image Processing | DAT.2: Image Processing | 2/16/22 | In Progress
Notes: Blue on sheet

## Slide 93: Testing Phase 2: Subsystem Testing
Subsystem | Test(s) Name | Completion Date | Status
Optics | OPT.1: Basic Functionality OPT.6: Pointing OPT.7: LSM* | 2/20/22 | Completed - Appendix Not Started In Progress - Presented
Structures | STR.2: Thermal Model* STR.4: Water Protection | 2/20/22 | Not Started Not Started
Orbit Determination | ORB.1-7: All Keplerian Element Tests ORB.8: Close Approach Event Prediction | 3/20/22 | In Progress - Presented Not Started
Electronics | ELE.4: Power Interface ELE.5: Power Failure ELE.6: Communication/Data Interface | 2/20/22 | Not Started Not Started Not Started
Data Flow | DAT.1: Communications DAT.3: Alert Timing* | 3/20/22 | In Progress - Presented In Progress
Algorithm | ALG.1-6: POLs ALG.7-10: Events | 3/20/22 | In Progress - Presented In Progress - Presented
Notes: Yellow on sheet

## Slide 94: Testing Phase 3: System Testing
Test Name | Completion Date | Status
STR.3: Stability |  | 
Full System Software Test | 3/6/22 | Not Started
Structure View Test | 3/6/22 | Not Started
Full System Test | 3/6/22 | Not Started
Full System Day in the Life (Field Testing) | 4/10/22 | Not Started - Presented Here
Notes: Red on sheet

## Slide 95: Optics (OPT) V&V Overview
Test Number | Test Name | Completion Date
OPT.1 | Basic Optics Functionality Test | 2/20/22
OPT.2 | Optical Alignment Test | 2/7/22
OPT.3 | Sharpness Test | 2/7/22
OPT.4 | Focus Accuracy Test | 2/7/22
OPT.5 | Distance Focus | 2/7/22
OPT.6 | Pointing | 2/20/22
OPT.7 | LSM | 2/20/22
OPT.8 | Optics Day in the Life | 2/20/22

## Slide 96: Procedures and Checklists to be Completed
Packing Procedure and Checklist
Deployment Procedure and Checklist
Power-on Procedure and Checklist
Operations Procedure and Checklist

## Slide 103: Structure (STR) V&V Overview
Test Number | Test Name | Completion Date
STR.1 | Force | 2/7/22
STR.2 | Thermal | 2/20/22
STR.3 | Stability | 2/20/22
STR.4 | Water | 2/20/22
STR.5 | Transport | N/A

## Slide 108: Orbit Determination (ORB) V&V Overview
Test Number | Test Name | Completion Date
ORB.1 | Semi-Major Axis Determination | 3/20/22
ORB.2 | Eccentricity Determination | 3/20/22
ORB.3 | Inclination Determination | 3/20/22
ORB.4 | True Anomaly Determination | 3/20/22
ORB.5 | RAAN Determination | 3/20/22
ORB.6 | Argument of Periapsis Determination | 3/20/22
ORB.7 | Fully Keplerian Orbital Element Calculation | 3/20/22
ORB.8 | Event Prediction - Close Approach | 3/20/22

## Slide 109
500 km

## Slide 110: Electronics (ELE) V&V Overview
Test Number | Test Name | Completion Date
ELE.1 | IR Sensor | 2/7/22
ELE.2 | Temperature Sensor | 2/7/22
ELE.3 | Humidity Sensor | 2/7/22
ELE.4 | Power Interface Check | 2/20/22
ELE.5 | Power Failure | 2/20/22
ELE.6 | Communications and Data Interface Check | 2/20/22

## Slide 116: Data (DAT) V&V Overview
Test Number | Test Name | Completion Date
DAT.1 | Communications | 3/20/22
DAT.2 | Image Processing Products | 2/7/22
DAT.3 | Alert Timing | 3/20/22

## Slide 121: Algorithm (ALG) V&V Overview
Test Number | Test Name | Completion Date
ALG.1 | Inclination POL | 3/20/22
ALG.2 | Semi-Major Axis POL | 3/20/22
ALG.3 | Direction of Burn POL | 3/20/22
ALG.4 | Frequency of Burn POL | 3/20/22
ALG.5 | Brightness POL | 3/20/22
ALG.6 | RGB POL | 3/20/22
ALG.7 | Maneuver Event Detection | 3/20/22
ALG.8 | Close Approach Event Detection | 3/20/22
ALG.9 | Docking Event Detection | 3/20/22
ALG.10 | Breakup Event Detection | 3/20/22

## Slide 122: ALG.1: Inclination POL
Req | CPE | Test Description | Measurements | Setup | Facilities | Equipment
FR 2 | POL Determination | This test will confirm that the inclination POL can be created using historical data. | By visual inspection and error analysis, confirm the created POL matches an L3 Harris provided POL for the same satellite over the same period of time. | Create POL for five different satellites using historical data. Plot the POL. Compare the plotted POL to a L3 Harris provided POL and determine the error between the two. | Senior Projects Room | N/A

## Slide 123: ALG.2: Semi-Major Axis POL
Req | CPE | Test Description | Measurements | Setup | Facilities | Equipment
FR 2 | POL Determination | This test will confirm that the semi-major axis POL can be created using historical data. | By visual inspection and error analysis, confirm the created POL matches an L3 Harris provided POL for the same satellite over the same period of time. | Create POL for five different satellites using historical data. Plot the POL. Compare the plotted POL to a L3 Harris provided POL and determine the error between the two. | Senior Projects Room | N/A

## Slide 124: ALG.3: Direction of Burn POL
Req | CPE | Test Description | Measurements | Setup | Facilities | Equipment
FR 2 | POL Determination | This test will confirm that the direction of burn POL can be created using historical data. | By visual inspection and error analysis, confirm the created POL matches an L3 Harris provided POL for the same satellite over the same period of time. | Create POL for five different satellites using historical data. Plot the POL. Compare the plotted POL to a L3 Harris provided POL and determine the error between the two. | Senior Projects Room | N/A

## Slide 125: ALG.4: Frequency of Burn POL
Req | CPE | Test Description | Measurements | Setup | Facilities | Equipment
FR 2 | POL Determination | This test will confirm that the frequency of burn POL can be created using historical data. | By visual inspection and error analysis, confirm the created POL matches an L3 Harris provided POL for the same satellite over the same period of time. | Create POL for five different satellites using historical data. Plot the POL. Compare the plotted POL to a L3 Harris provided POL and determine the error between the two. | Senior Projects Room | N/A

## Slide 126: ALG.5: Brightness POL
Req | CPE | Test Description | Measurements | Setup | Facilities | Equipment
FR 2 | POL Determination | This test will confirm that the brightness POL can be created using historical data. | By visual inspection and error analysis, confirm the created POL matches an L3 Harris provided POL for the same satellite over the same period of time. | Create POL for five different satellites using historical data. Plot the POL. Compare the plotted POL to a L3 Harris provided POL and determine the error between the two. | Senior Projects Room | N/A

## Slide 127: ALG.6: RGB POL
Req | CPE | Test Description | Measurements | Setup | Facilities | Equipment
FR 2 | POL Determination | This test will confirm that the RGB POL can be created using historical data. | By visual inspection and error analysis, confirm the created POL matches an L3 Harris provided POL for the same satellite over the same period of time. | Create POL for five different satellites using historical data. Plot the POL. Compare the plotted POL to a L3 Harris provided POL and determine the error between the two. | Senior Projects Room | N/A

## Slide 128: ALG.7: Maneuver Event Detection
Req | CPE | Test Description | Measurements | Setup | Facilities | Equipment
FR 6 | Event Detection | This test will confirm that a satellite maneuver can be detected. | For the five datasets where there was a maneuver - the algorithm should detect it. For the five datasets where there was not a maneuver - the algorithm should not detect it. The confidence level for each data set should also be captured. | Identify ten historical data sets. Five where there is a known maneuver and five where there is no known maneuver. Input each data set into the algorithm one at a time. Capture whether the system alert the system alerts or not, and the confidence level of that prediction. | Senior Projects Room | N/A

## Slide 129: ALG.8: Close Approach Event Detection
Req | CPE | Test Description | Measurements | Setup | Facilities | Equipment
FR 6 | Event Detection | This test will confirm that a close approach between two satellites can be detected. | For the five datasets where there was a close approach - the algorithm should detect it. For the five datasets where there was not a close approach - the algorithm should not detect it. The confidence level for each data set should also be captured. | Identify ten historical data sets. Five where there is a known close approach between two satellites and five where there is no known close approach between two satellites. Input each data set into the algorithm one at a time. Capture whether the system alert the system alerts or not, and the confidence level of that prediction. | Senior Projects Room | N/A

## Slide 130: ALG.9: Docking Event Detection
Req | CPE | Test Description | Measurements | Setup | Facilities | Equipment
FR 6 | Event Detection | This test will confirm that a docking between two satellites could be detected. | For the two datasets where there was a docking - the algorithm should detect it. For the two datasets where there was not a docking - the algorithm should not detect it. The confidence level for each data set should also be captured. | Identify four historical data sets. Two where there is a known docking between two satellites and two where there is no known close approach between two satellites. Input each data set into the algorithm one at a time. Capture whether the system alert the system alerts or not, and the confidence level of that prediction. | Senior Projects Room | N/A

## Slide 131: ALG.10: Breakup Event Detection
Req | CPE | Test Description | Measurements | Setup | Facilities | Equipment
FR 6 | Event Detection | This test will confirm that a satellite breakup could be detected. | For the two datasets where there was a breakup - the algorithm should detect it. For the two datasets where there was not a breakup - the algorithm should not detect it. The confidence level for each data set should also be captured. | Identify four historical data sets. Two where there is a known breakup and two where there is no known breakup. Input each data set into the algorithm one at a time. Capture whether the system alert the system alerts or not, and the confidence level of that prediction. | Senior Projects Room | N/A

## Slide 132: ALG.11: POL Deviation
Req | CPE | Test Description | Measurements | Setup | Facilities | Equipment
FR 6 | Event Detection | This test will confirm that the system has the ability to detect deviations in POL. This will be done from the inclination, semi-=major axis, direction of burn, frequency of burn, brightness and RBG value. | For five data sets where there is no deviation in POL - the algorithm does not label a deviation and does not find the time. For the five data sets where there is a deviation in POL - the algorithm correctly labels that there is one and identifies the time. | Identify ten historical data sets for each type of POL. Five where there is a known deviation and five where there is no known deviation. Input each data set into the algorithm one at a time. Capture whether the system alerts the system alerts or not, the time of the alert, and the confidence level of that prediction. | Senior Projects Room | N/A

## Slide 133: System (SYS) V&V Overview
Test Number | Test Name | Completion Date
SYS.1 | Full System Software Test | 3/6/22
SYS.2 | Structure View Test | 3/6/22
SYS.4 | Full Systems Test | 3/6/22
SYS.5 | Full System Day in the Life (Field Testing) | 4/10/22

## Slide 134: SYS.1: Full System Software Test
Req | CPE | Test Description | Measurements | Setup | Facilities | Equipment
ALL | ALL | This test will confirm all the integrated software works as expected on the electronics. | By visual inspection, confirm the software performs as expected. | Connect and power all the necessary electronics. Input an image into the software system. Have the image go through all the required software. Confirm the expected output is received. | N/A | All structures components All electronics components Onboard and offboard computer Power

## Slide 135: SYS.2: Structure View Test
Req | CPE | Test Description | Measurements | Setup | Facilities | Equipment
ALL | ALL | This test will confirm the optical system has the required FOV for image processing and POL/event detection. | By visual inspection, confirm the image had the expected FOV and the algorithm was able to function as expected. | Set up the whole system outside at night. Take three images, five seconds apart. Send the three images through the data processing and algorithms. | N/A | All structures components All electronics components Onboard and offboard computer Power

## Slide 136: SYS.3: Full System Test
Req | CPE | Test Description | Measurements | Setup | Facilities | Equipment
ALL | ALL | This test will confirm that for 24 images, the full system functions as expected. | Store all the images taken, all the data out of the image processing system, all the decisions weather to alert or not, temperature, humidity, and IR data all on the onboard computer. On the offboard computer, store if the system alerts. After the test, analyze the all data together and confirm the system performed as expected. | Set up the whole system outside at night. Take 24 images. Send the 24 images through the entire data processing and algorithms systems. Store all noted data on the onboard and offboard computer. | N/A | All structures components All electronics components Onboard and offboard computer Power

## Slide 137: SYS.4: Full System Day in the Life (Field Testing)
Req | CPE | Test Description | Measurements | Setup | Facilities | Equipment
ALL | ALL | This test will confirm that for eight hours overnight, the full system functions as expected. | Store all the images taken, all the data out of the image processing system, all the decisions weather to alert or not, temperature, humidity, and IR data all on the onboard computer. On the offboard computer, store if the system alerts. After the test, analyze the all data together and confirm the system performed as expected. | Set up the whole system outside at night for eight hours. Send the images through the entire data processing and algorithms systems. Store all noted data on the onboard and offboard computer. | N/A | All structures components All electronics components Onboard and offboard computer Power

## Slide 138: Off-Site Test Plans
Follow the packing procedure to pack all the components for transportation
Transport the system to the testing location
Follow the deployment procedure to set up the structure, electronics, optics system, and software (in order to get a full eight hours of testing this will need to happen between 8pm - 12am)
Follow the power-on procedure to configure and calibrate the system into a mode that is ready for operations
Follow the operations procedure to place the system in an operations mode
Leave the system outside and running for eight hours
Collect the system and follow the packing procedure to pack all the components for transportation

## Slide 139: Safety Appendix

## Slide 140: Battery Overview
EF ECOFLOW River battery
  Charging: Wall outlet
  Outputs: Onboard computer, Sensor
8-cell AA battery holder
  Charging: N/A
  Outputs: Backup for the Arduino, Linear Actuator

## Slide 141: Battery Test Plans
Power Interface Check - by 2/20/22, senior projects room
Power Failure Check - by 2/20/22, senior projects room
Full System Test - by 3/6/22, outside aerospace building
Full system day in the life (field testing) - by 4/10/22, remote

## Slide 142: Battery Checklist
Charging Procedure
  Plug into wall outlet and monitor until fully charged
    1.6 hours to fully charged
Power On Procedure
  Confirm battery is charged and powered off
  Plug the onboard computer into the first AC Port
  Plug sensor into the second AC Port
  Power on the battery

## Slide 143: Off-Site Test Overview
Location: Someone's known property in Lyons (final location to be determined)
Personal: 4-5 people (one person from each subteam, rotating)
Equipment: Entire SPECTER System
Transportation: Personal vehicle
Dates: Five or six days between 3/1/22 - 3/20/22 (depending on weather)

## Slide 144: Off-Site Test Plans
Follow the packing procedure to pack all the components for transportation
Transport the system to the testing location
Follow the deployment procedure to set up the structure, electronics, optics system, and software (in order to get a full eight hours of testing this will need to happen between 8pm - 12am)
Follow the power-on procedure to configure and calibrate the system into a mode that is ready for operations
Follow the operations procedure to place the system in an operations mode
Leave the system outside and running for eight hours
Collect the system and follow the packing procedure to pack all the components for transportation

## Slide 145: Off-Site Checklist (In Progress)
Packing Procedure and Checklist
Deployment Procedure and Checklist
Power-on Procedure and Checklist
Operations Procedure and Checklist

## Slide 146: Off-Site Testing CONOPS

## Slide 147: Budget Appendix
Notes: Sam A

## Slide 148
Notes: Sam A
Red highlight margins
Orange Highlight criticals
Mention wires, warmer, hotspot (not highlighted)
ALL OTHER PARTS ORDERED AND RECEIVED! HIGHLIGHT THAT!
Put whole slide into backup
Just need to make clear of what items we are waiting on and what we actually need to spend more money on etc.