## Slide 1: GAINS General Atomics Inertial Navigation System
Presenters:
Bennett Grow, Cannon Palmer, Tucker Peyok, Alfredo Restrepo, Kaylie Rick, Ross White, Addison Woodard
Team Members:
Ben McHugh, Alex Pichler, Derek Popich, Jason Popich, Brian Trybus
Sponsor:
General Atomics (GA)
Faculty Advisor:
Dr. Dale Lawrence
December 7, 2022
Critical Design Review

## Slide 2: Agenda
Project Overview
  Change of Scope
Design Solutions
Critical Project Elements
  Project Risk
Design Requirements/Satisfaction
Verification & Validation
Project Planning

## Slide 3: Project Overview

## Slide 4: Mission Statement
Project GAINS aims to develop an Inertial Navigation System (INS) prototype for installation on cube-satellites in cislunar applications. The GAINS prototype will be developed to maximize accuracy of estimated position and velocity with the aid of external error corrections.

## Slide 5: Mission Objectives
2
1
3
Provide accurate inertial position and velocity to a CubeSat in a cislunar orbit with an INS, outside of GPS range
Modularity, such that the system can be installed in a variety of standardized General Atomics cubesats
Ground segment to receive INS data and display trajectory in a Graphical User Interface (GUI)

## Slide 6: Full Mission CONOPS
2. Cislunar orbit
3. INS activation
4a. INS based position maintenance and navigation
KEY
4b. Ground station contacts, every 2 hours
Ground station
Uplink/Downlink
1. Launch
Trajectory
In Scope
6 hrs of contact
6 hrs of contact
6 hrs of contact
2 hrs Loss of Contact
2 hrs LoC
2 hrs LoC
24 hrs

## Slide 7: GAINS Project CONOPS
Parent Cubesat
Downlink computed AD data package
Positional Drift Corrections, maximum 2 hours LOC
GAINS
Computation
Measurement
Computed AD solution and data
Positional Drift Corrections
Star Tracker
Attitude Drift Corrections @ 10Hz
Satellite polling @ 100Hz
(Position and velocity calculations)
Ground Station
Storage
GS Contact Maintained
GS Contact Achieved (send all storage)
Truth Data & Communication emulation for testing
Overview
CPE/Risk
In Scope
In Scope
Design

## Slide 8: GAINS Change of Scope
Sensor Selection
  Unable to find sensors that meet customer’s position/velocity requirements through the 2 hour loss-of-contact window
  Called multiple vendors to discuss sensors not available on websites
  Completed studies on increasing the number of sensors to improve accuracy
Multiplicative Extended Kalman Filter (MEKF) for a 6 Degree of Freedom system in a cislunar trajectory
  Determined to be over-complicated for meeting adjusted customer requirements
Cislunar Orbit
  Changed to circular lunar orbit for modeling/dynamic accuracy

## Slide 9: Design Solution

## Slide 10: System Functional Block Diagram

## Slide 11: Electronics Design - PCB Functional Block Diagram

## Slide 12: Electronics Design - Sensors
Accelerometer | Gyroscope
Due to 7200 seconds between updates, we are unable to find an accelerometer with all of the following specs required to meet accuracy constraints: Bias (0g offset) ≤ 0.55 mg Velocity Random Walk ≤ 1 mm/sec/Hr Scale Factor ≤ 1% Bias Repeatability ≤ 0.1 mg Using the following 2 accelerometers for modelling: ADXL 355 from Analog Devices Inc. Dimensions = 6mm x 6mm x 2.05 mm SDI 1521 from Silicon Devices Inc. Dimensions = 8.9mm x 8.9mm x 4.2mm | Error not as significant due to 10Hz attitude corrections from star tracker Selected: IAM 20380 from TDK InvenSense Bias (0g offset) = 10 deg/s Noise Spectral Density = 0.010 deg/s/√Hz Dimensions = 3mm x 3mm x 0.75mm

## Slide 13: Flight Software Design
Kalman Filter
Combine weighted prediction and measurement to estimate position and velocity at 100 Hz
Written in C for bare-metal flashing and speed
Time
𝛿velocity
Error Correction
Upward trending random walk-off
Kalman Filtered Error Correction
2 hrs
0.4 m/s
Sensor Data
Parent CubeSat
Kalman Filter
Predict
Measure
Weight P & M
Final Estimate
Ground Station

## Slide 14: Mechanical Concept Design
Estimate Housing Maximum Weight = 217 g
Aluminum 6061
  Shielding Effective Material
  2 mm Al Sheet Brazed Together
  Estimated Clean Weight: 172 grams
Onyx ESD
  Ideal Material Resistance Range: 105 -107 Ω
    Prevents Discharge to PCB via Human Contact
  3D Printed
  Estimated Clean Weight: 45 grams
Mounting Flanges
  Mountable on Both GA Spacecraft and for Testing
  Not Required to Fit in 3x10x10 cm Envelope
Driving Requirement | 
C.1 | INS shall not exceed 3 x 10 x 10 cm in size
C.2 | INS shall not exceed 500 g
1.2.5 | Structure shall resist EMI from a 4 GHz S-band antenna using gaps smaller than 7.45 mm
2.1.4 | Structure shall have 6 mounting flanges/brackets

## Slide 15: Ground Software - GS Flowchart

## Slide 16: Critical Projects Elements/Project Risk

## Slide 17: Critical Project Elements
Critical Element | Constraint Rationale
E1: Accuracy | The GAINS system should have a peak position error of no more than 1 km and peak velocity error of no more than 0.1 0.4 m/s.
E2: Calculation | The GAINS system will have to calculate estimate its inertial position and velocity in real time using measurements from its integrated sensors.
E3: Communication | The GAINS system must have uplink and downlink capabilities with the ground station, as well as data transmission to the parent satellite.
E4: Display | The GAINS ground station must include a Graphical User Interface (GUI) with a real time status, trajectory, and power on/off switches.
E5: Integration | The GAINS system must be compatible with a variety of GA’s satellite bus structures have flanges for mounting to the parent satellite.
E6: Testing | The GAINS system shall be tested to ensure project elements fulfill customer mission objectives.

## Slide 18: CPE 1
E1: Accuracy | The GAINS system should have a peak position error of no more than 1 km and peak velocity error of no more than 0.4 m/s.
Critical to deliver states with high accuracy to General Atomics
Sensor calibration using accuracy error and sensor bias models
Kalman Filter (KF)
  Sensor error (bias, repeatability, VRW) is mitigated through the KF
  Weighting sensor measurements with ground station updates allows for improved state estimates
  KF development researched and computational requirements modelled
Trajectory modeling on the ground provides predictions for KF error correction during LOC periods

## Slide 19: CPE 2
Critical to provide parent satellite with 100 Hz state updates
Kalman Filter
  Non-linear position determination (MEKF equations, out of scope)
  Utilize Clohessy-Wiltshire equations to model a circular lunar orbit
  Accelerometer measurements and ground station update inputs
Utilizing Dr. Holzinger & PhD students for support
Developed code outline in C for testing on dev. boards to estimate computational requirements
E2: Calculation | The GAINS system will estimate its inertial position and velocity at 100 Hz using measurements from its integrated sensors.

## Slide 20: CPE 4
Critical to display relevant trajectory information to General Atomics’ engineers
NASA JPL CppSpice Data gives planet locations and gravitational effects
GUI displays live data and enables live control of the simulation
GUI will control connection activity and enable different control modes to be activated
E4: Display | The GAINS ground station must include a Graphical User Interface (GUI) with a real time status, trajectory, and power on/off switches.
*This is only an initial model intended to show functionality of the Graphics Render Engine, Gui, and CppSpice Orbital Data Implementation

## Slide 21: Risk Matrix (New Scope)
Very Likely |  |  | Lack of Kalman Filter expertise | Accelerometer drift/uncertainty | 
Likely |  |  |  |  | 
Possible |  |  |  |  | 
Unlikely |  |  |  | Part lead time/delivery | 
Very Unlikely |  |  | Budget |  | Part availability
 | Negligible | Minor | Moderate | Significant | Severe
Risk Level
Acceptable
Concerning
Unacceptable
Impact/Consequence
Probability

## Slide 22: Design Requirements/Satisfaction

## Slide 23: Electronics - Accuracy Model
Velocity Error Derivation
Position Error Derivation

## Slide 24: Electronics - Velocity Accuracy Model Derivation
KEY
Scale Factor
Velocity Random Walk
Angle Random Walk
Accelerometer Bias
Gyro Bias
t = 0.1 s
t = 2 hr
Total change in velocity felt over time interval
Velocity error at calibration

## Slide 25: Electronics - Position Accuracy Model Derivation
KEY
Scale Factor
Velocity Random Walk
Angle Random Walk
Accelerometer Bias
Gyro Bias
t = 0.1 s
t = 2 hr
Total change in position felt over time interval
Position error at calibration
Velocity error at calibration

## Slide 26: Electronics - Dominant Error Source
Accelerometer | Velocity Error (m/s) | Calibration Error Term (m/s) | Sensitivity (Scale Factor) Term (m/s) | Accelerometer Bias Term (m/s) | Velocity Random Walk Term (m/s) | Attitude Terms (m/s)
SDI 1521 | 8.706 | 0 | 0.00017 | 8.7 | 0.0058 | 1.8e-8

## Slide 27: Electronics - Dominant Error Source
Accelerometer | Velocity Error (m/s) | Calibration Error Term (m/s) | Sensitivity (Scale Factor) Term (m/s) | Accelerometer Bias Term (m/s) | Velocity Random Walk Term (m/s) | Attitude Terms (m/s)
SDI 1521 | 8.706 | 0 | 0.00017 | 8.7 | 0.0058 | 1.8e-8
Accelerometer | Position Error (m) | Calibration Error Term (m) | Sensitivity (Scale Factor) Term (m) | Calibration error Term (m) | Accelerometer Bias Term (m) | Velocity Random Walk Term (m) | Attitude Terms (m)
SDI 1521 | 31029.2 | 0 | 1.2 | 0 | 31000 | 28 | 7.3e-10

## Slide 28: Electronics - Bias Calibration Model
Assuming that we can calibrate the bias to the physical limit of the ADC (1 LSB), we can reduce the bias error as follows:
Where R is the range of the sensor (accel. or temp.) and β is the number of bits in the ADC

## Slide 29: Electronics - Lifetime Drift (Repeatability)
After a sensor is calibrated, it drifts roughly with the square root of time.
Unlike temperature calibrations, these drift calibrations cannot be made mid flight.
The model used for repeatability was suggested by the ADXL355 datasheet:
Where D is the sensor lifetime drift and t is time since calibration

## Slide 30: Electronics - Model Results
0.61% Bias Estimation (Calibration of accelerometer done by a team of doctoral graduates)
- Source: “Estimation of Deterministic and Stochastic IMU Error Parameters” by Derya Unsal and Kerim Demirbas
8.7 m/s, and 31 km error at calibration (out of requirement)
0.0019% Best Bias Estimation possible
  (within 1 LSB of the ADC)
Drifts out of requirement after 64 seconds
x104

## Slide 31: FSW- Kalman Filter Model
Predict state at next time step
Extrapolate prediction uncertainty
Determine Kalman gain - weight prediction and measurements
Update prediction with weighted measurements
Update the prediction uncertainty
Kalman filters estimate state using multiple sources of measurements and their uncertainty
Update
Predict

## Slide 32: FSW - Multiplicative Extended Kalman Filter
The following capabilities would require a Multiplicative Extended Kalman Filter (MEKF):
3 axis accelerometer
3 axis gyroscope
Coupled, nonlinear system
The state vector would need 19 variables:
The full MEKF is not required to meet adjusted customer requirements

## Slide 33: GAINS Change of Scope Recap
INS
Parent S/C
Expected Trajectory
Known Trajectory
Inertially measured trajectory change
Computed AD solution and data
Positional Drift Corrections
THRUST
Re-scoped orbit

## Slide 34: Thrust Addition Benefits
Integrating noise for entire 2 hour LOC produces error values exceeding the customer requirements.
Integrating for thrusting period only results in error values below customer requirements.
  Sensor repeatability has less time to drift

## Slide 35: Electronics - Model Results (New Scope)
Modeled after THEMIS Satellites: 4 Monopropellant Hydrazine Cold Gas Thrusters
Assumed ΔV required for lunar maintenance burn = 10 m/s
Typical burn duration of 73 seconds
Repeatability value at calibration now within customer requirements!

## Slide 36: FSW - New Scope
Modelling as a circular orbit allows use of the Clohessy–Wiltshire equations. (This avoids implementing a full non-linear MEKF)
Allows our Kalman Filter state vector to be reduced to 6 variables:
Attitude information is provided from star tracker at 10 Hz

## Slide 37: FSW - Compute Time Estimates
Testing on Arduino Due (Atmel SAM3X8E ARM Cortex M3, 84 MHz)
Full MEKF test with 25 variable state vector:
0.1882 seconds/cycle (~5 Hz [100 Hz required])
Compilation size: 30 kB
SRAM usage: 47 kB (floats not doubles)
Testing rescoped model with 6 variable state vector on same Arduino Due:
0.006 seconds/cycle (~166 Hz)
Compilation size: 30 kB
SRAM usage: 8 kB (floats not doubles)
Only tests Kalman filter equations,
  excludes I/O, memory operations, communications, sensor interactions, state transition matrix calculations

## Slide 38: Verification & Validation

## Slide 39: Tabletop Test - Models
Velocity Random Walk | Temperature Calibration | Repeatability
Kalman Filter uses this value to establish discrete error bounds in weighting process | Calibration of bias error change over various temperatures will greatly reduce the accuracy estimates | Understand how the accelerometer will drift between calibrations Verify accuracy is within customer requirements

## Slide 40: Tabletop Test
INS
Ground Station
Fg
Purpose | Description
Baseline accelerometer Velocity Random Walk (VRW) value, and characterize sensor specific uncertainties to increase accuracy Quantify accelerometer Repeatability value through testing runs with power cycles between | Secure INS on static surface for two hours on each axis at a constant temperature Process data to determine VRW Same test procedure to be followed with Temperature Variation Test in order to determine associated dependence
Success Criteria: Baseline VRW values established for each axis for incorporation in software.

## Slide 41: 5-Axis CNC Test
Hurco VM10Ui (ITLL Model)
Purpose:
Determine sensor misalignment, scale factor, and bias for software-sensor calibration
Characterize accuracy of position and velocity estimation by comparing to known values of the CNC machine
Ground Station
INS
Success Criteria: Scale factor, misalignment properties, and bias for software calibration obtained along with sensor accuracy.

## Slide 42: 5-Axis CNC Test - Description
Test bed range of motion is sufficient for GAINS to be rotated and translated along each axis of the accelerometer
Description:
Mount INS to CNC fixture plate
Measure accelerations and rotational velocities through pre-coded path
Perform data uplink and downlink with the ground station
Remove INS and compare measured trajectory to true motions of the CNC

## Slide 43: Project Planning

## Slide 44: WBS
INS
Housing
Ground Station
Flight Software
PCB
KF creation
Star tracker data fabrication
KF tuning
Real time Testing
Data exchange testing
Accelerometer selection
Gyroscope selection
Error characterization
Altium PCB design
PCB review
PCB fabrication
Component testing
Component calibration
Integrated testing
Basic GUI design
Planetary model incorporation
Render engine development
Orbital simulation
Thrust modeling
Compatibility testing
Simulation Integration
Real time testing
GUI refinement
Data exchange testing
Requirements definition
Accessibility method
EMI characterization
ESD characterization
Material requirement definition
PCB thermal analysis
Material selection
Prototyping
Fabrication
Hardware integration
Test mounting fabrication
Tabletop Test
5 Axis CNC Test
Management
PDD
PDR
CDR
Fall Final Report
IDR
AIAA Abstract
AIAA Submission
TRR
AES Industry Symposium
SFR
Spring Final Report
Sr. Symposium!
GAINS
Deliverables
Budget
Initial mass allocation
Initial power allocation
Finalize Bill of Materials
P-Card approval
Purchase plan finalization
Ordering
KEY: Completed Work In Work Future Work

## Slide 45: Updated Work Plan
Component Selection
Testing Campaign
Kalman Filter Development/Tuning
GUI/Truth Orbit Development
Housing Fabrication
PCB Fabrication/Testing
Fall Break
Winter Break
Spring Break
CDR
FFR
IDRs
TRR
AIAA Paper
SFR
Symposium!

## Slide 46: Cost Plan
Part Type | Part Name | Qty | Cost/unit | Total Cost
3-axis Accelerometer | SDI 1521 | 2 | $450 | $900
3-axis Gyroscope | IAM-20380 | 2 | $14.93 | $29.86
Microcontroller | TBD | 2 | < $25 | $50
PCB | TBD | 3 | ~ $30 | $90
Flash Memory | GD5F1GQ4UFYIGR | 2 | $4.84 | $9.68
Dev-Board | TBD | 1 | < $100 | $100
Housing Material | Aluminum 6061/ Onyx ESD | 64 ㎤/ 10.1 ㎤ | < $30/ $35 | $65
Testing Supplies | Various, TBD | - | ~ $100 | $100
Misc. (fasteners, ports, shipping, etc) | Various | - | ~ $200 | $200
Total projected cost Electronics: |  |  |  | $1479.54
Total projected cost Mechanical: |  |  |  | $135
Subsystem | Allocated Budget | Remaining Budget | Budget margin
Electronics | $2480 | $1250.46 | 50.42%
Mechanical | $1200 | $1135 | 94.6%
Shipping | $320 | $170 | 53%
Total: | $4000 | $2555.46 | 63.9%
*All components were determined to be available with feasible lead times for next semester

## Slide 47: Major Test Overview
Test | Facilities Required | Access?
Tabletop Test | Static surface, undisturbed for 2 hours | Yes
5-Axis CNC Test | 5-Axis CNC machine, mounting hardware | Yes - Team member is an ITLL machine shop employee
Temperature Variation Test | Temperature controlled environment, ability to monitor/record temperature and sensor readings, static surface, undisturbed for 2 hours | Yes, same facility as Tabletop Test. Still evaluating Temperature Control methods
*All other tests will be component level tests, achieved with Aerospace Electronics Lab facilities

## Slide 48: Questions?

## Slide 49: Backup

## Slide 50: Mechanical Backup Slides

## Slide 51: Mechanical - Overview
GAINS Enclosures Anticipated Environment
Closed in Spacecraft
Assuming the use of an S-Band antenna, the requirement would be to reduce the interference of Electromagnetic radiation in the range of 2GHz - 4GHz.
  Distance of S-Band assumed to be less than 1 meter
Ambient Temperature = 0°C to 60°C
  Flat point of contact with spacecraft is assumed to follow given constraint
Ambient Temperature = 0°C- 60°C
INS
S-Band Antenna
Illustration of anticipated environment described by General Atomics
Notes: Basic illustration of…
the heat produced by our PCB
The exact set up
Hence mounted inside the spacecraft and not exposed to space
where the ambient temperature takes place
Aka where our initial heat transfer is coming from akaa we are given the assumption that the surface point of contact with SC will also be the same temp
our mounting on the GA satellite
The “S-band antenna” producing 2 GHz to 4GHz emitted towards the INS (doesn’t have to be an s-band but show that their is radiated interference by an antenna on SC

## Slide 52: Mechanical Design
Key Features:
3 Pieces
  Aluminum Base
  Aluminum Lid
  Onyx ESD Bedding
Base and Lid Hozintonally Bolted Together
Bedding for PCB Mounting
  PCB Screwed On
  Bedding held flat via Lid
Mounting Flanges
  Mountable on Spacecraft
  Mountable for Testing Requirement
    Featured Illustration on Testing Section
PCB Board Accessible
  Access PCB via Removable Top
  PCB and Bedding Fully Removable
Shielded Connectors
Notes: Backup

## Slide 53: Mechanical Design- Additional CAD
e

## Slide 54: Mechanical - Electromagnetic Compatibility
Customer Requirement: “Assuming the use of an S-Band antenna, the requirement would be to reduce the interference of Electromagnetic radiation in the range of 2GHz - 4GHz.”
“Electromagnetic Compatibility (EMC) is the ability of electrical or electronic equipment/systems to function in the intended operating environment without causing or experiencing performance degradation due to unintentional Electromagnetic Interference (EMI).”
INS instruments affected by EMI:
MEMS Accelerometer (ADXL355 - 3-axis Accelerometer)
MEMS Gyroscopes (IAM-20380 - 3-axis Gyroscope)
EMI Shielding Rule of Thumb: To prevent signal transmission, holes need to be no larger than 1/10 of the wavelength
Wavelength: 0.1499 m and 0.07495 m respectively
Maximum allowable gap: 10% of wavelength
1.49 cm at 2 GHz
0.745 cm at 4 GHz
Concept design feature no holes, hence protectant EMI Gaskets will be decided upon possible manufacturing imperfections
Source: https://www.radioing.com/eengineer/intro.html
Wavelength:
c = speed of light
f = frequency
Notes: Source of definition: https://www.radioing.com/eengineer/intro.html
“Assuming the use of an S-Band antenna, the requirement would be to reduce the interference of Electromagnetic radiation in the range of 2Ghz- 4Ghz.”
One rule of thumb often used for Faraday cages to prevent transmission is that the holes need to be no larger than 1/10 of the wavelength of the signal.

## Slide 55: Mechanical - Shielding Effectiveness Setup
Shield Effectiveness (SE): An enclosure ability to diminish the exposed electromagnetic field
The Required Attenuation Shield Effectiveness [dB]:
= The radiated field strength received without barrier
= The radiated field strength received with barrier
S-Band Antenna radiated field strength: XXX [v/m]
Acceptable Field Strength of MEMS Gyroscope: XXXX [v/m]
Minimum Shielding Effectiveness Required: XX [dB]
Near field application
At frequencies from 30 to 100 MHz, aluminum foil provides at least 85 dB of shielding effectiveness.
Higher frequency requires higher shield thickness
Source: T.L. Clark, M.B. McCollum, D.H. Trout,
and K. Javor: Marshall Space Flight Center Electromagnetic
Compatibility Design and Interference Control
(MEDIC) Handbook

## Slide 56: Mechanical - Designed Shielding Effectiveness
Four Types of possible EMI:
Conduction - Electric Current
Radiation - Electromagnetic Field
Capacitive Coupling - Electric Field
Inductive Coupling - Magnetic Field
Total Shielding Effectiveness of Designed Enclosure increases:
Thickness of the shield
Conductivity of the shield
Permeability of the shield
Joints and apertures will degrade shielding effectiveness (SE) of the material
Source: R.W. Evans, Design Guidelines for Shielding Effectiveness,
Current Carrying Capability, and the Enhancement
of Conductivity of Composite Materials

## Slide 57: Mechanical - Shielding Effectiveness
Attenuation due to absorption factor:
Loss due to reflection factor (Negative Number):
Near-field re-reflection correction factor:
Total Shield Effectiveness:
Outside
Enclosure
Inside
Reflection
Incident Wave
Reflected wave
Transmitted Wave
Re-Reflection
Source: R.W. Evans, Design Guidelines for Shielding Effectiveness,
Current Carrying Capability, and the Enhancement
of Conductivity of Composite Materials
Notes: Explain the meaning of each term (possibly backup slide)
Source: “Design Guidelines for Shielding Effectiveness,
Current Carrying Capability, and the Enhancement
of Conductivity of Composite Materials PDF”
Possibly make nomenclature

## Slide 58: Mechanical - Electrostatic Discharge (ESD)
Electrostatic Discharge (ESD) Damage: The discharge of build up of electrostatic charge between two components
Electrostatic discharge improperly disperse towards components in attempt to reach ground
  Fatal towards vulnerable components
    Sensitivity of components may vary
Main Concern:
Discharge while in physical contact (testing) with the INS Housing
  Build-up of electrostatic charge in human body
ESD Standard Practices:
Grounded wrist straps
Handle with anti-static gloves
Notes: Intended to be a back up slide

## Slide 59: Mechanical - Electrostatic Discharge Vulnerability
GAINS Components Vulnerability:
ADXL355 - 3-axis Accelerometer
  Class 1C (HBM)
    Damage at 2000 Volts
    Moderately Sensitive
IAM-20380 - 3-axis Gyroscope
  Class 1C (HBM)
    Damage at 2000 Volts
    Moderately Sensitive
Flash Memory - GD5F1GQ4UFYIGR
  Class 3B (HBM)
    No concern
“Human Body Model (HBM): Model imitating the susceptibility of an electronic device from ESD caused by a human touch”
Source: electronicdesign.com
Notes: Intended to be a back up slide

## Slide 60: Mechanical - Electrostatic Discharge Protection
ESD Shielding Material of the Housing
Insulative Material (Undesirable)
  Enable electrostatic to build up
  Attempts to discharge at random
    Fatal
  Difficult to ground
Conductive Material (Acceptable)
  Enable electrostatic charges to discharge towards ground
    Low resistance leads to unsafe discharge
    Connect enclosure to ground enable discharge
Dissipative Material (Desirable)
  Materials with surface resistivity 10^2 ohms to 10^7 ohms disperse static charge
  Connect enclosure to ground to enable safer discharge
Source: terrauniversal.com

## Slide 61: Mechanical - Thermal Analysis Setup
Thermal Analysis conducted to have an understanding of thermal implications on design
Customer constraints on Design
  Maximum Power Usage is 1 Watt
  Ambient Temperature is 0°C to 60°C
  10x10x3 Cubic Centimeter Volume
Analysis Assumptions
  STM32F21xxx - LQFP144 processor
  Power dissipated is 0.7 Watts
    0.5 Watts for microcontroller; 0.2 Watts for everything else
  Still air convection
  Air - Wall - Air Thermal Resistance System
    2 mm enclosure wall thickness
Governing Equations:
Source: Nikhil Seshasayee, Understanding Thermal Dissipation and Design of a
Heatsink PDF
Notes: For EMI and ESD shielding, shielding diminishes with any apertures, hence the thermal model will assume a closed enclosure. Will explain more in the respective slides

## Slide 62: Mechanical - Thermal Analysis Results
Initial model results were promising!
  Maximum Allowed Junction Temperature from Microprocessor Specs: 125°C
  Minimum Estimated Junction Temperature (@ 0°C): 28°C
  Maximum Estimated Junction Temperature (@ 60°C): 88°C
  Estimated Heat Energy Flow: ~0.35 Watts
Notes:
  Reminder that this was used to estimate worst case!
    70% of power going into processor assumed lost
    Effects are vertical through 10 x 10 squared centimeter area. No provisions were made for added conduction benefits through PCB and bottom of enclosure
  Minimum junction temperature would be 0°C with no power dissipation!
  Care should be taken to minimize power dissipation of electronics but there is 37°C buffer to work with
Notes: For EMI and ESD shielding, shielding diminishes with any apertures, hence the thermal model will assume a closed enclosure. Will explain more in the respective slides

## Slide 63: Mechanical - Thermal Analysis Setup (Backup Slide)
Ambient Temperature = 0°C- 60°C
Ambient Temperature = 0°C- 60°C
Before INS turns on:
Ambient Temperature = 0°C- 60°C
After INS turns on:
PCB
PCB
1 Watt
Max. Temperature = 88°C
Estimated Heat Energy Flow: ~0.35 Watts
Enclosure
Enclosure
Spacecraft
Spacecraft

## Slide 64: Planned Evaluation Criteria Weight Justification
Feasible: This criterion refers to the total amount of equipment required to execute the plan, availability, and manufacturability.
EMI Shielding: This criterion refers material’s raw resistance to Electromagnetic Interference (EMI). Note: Alternatives are available.
ESD Shielding: This criterion refers material’s raw dispersion of Electrostatic Discharge (ESD). Note: Alternatives are available.
Density: This criterion refers estimated mass in the concept design.
Cost: Total cost of the material.
Notes: Repeatability: This criterion refers to the ease of re-manufacturing various prototypes. (debating on it because i feel like feasible section takes care of it)

## Slide 65: Mechanical - Planned Material Trade Matrix
Trades
Evaluation Criteria | Weight | Onyx ESD | Aluminum 6061 | Nylon 12 | ABS
Feasible | 30% | 3 | 3 | 2 | 2
EMI Shielding | 15% | 1 | 3 | 1 | 1
ESD Shielding | 15% | 3 | 2 | 2 | 1
Density | 20% | 3 | 2 | 3 | 3
Cost | 20% | 3 | 3 | 3 | 3
Total |  | 2.7 | 2.65 | 2.25 | 2.1
Trade Matrix Scale
3: Desirable
2: Acceptable
1: Undesirable
Notes: Tried to keep this color neutral
Nylon 12 required coating for ESD dissipation
ABS Plastic: Acrylonitrile butadiene styrene
ABS was considered to due being a common material for PCB enclosures

## Slide 66: Flight Software Backup Slides

## Slide 67: Flight Software Design
Kalman Filter
Combine weighted prediction and measurement to estimate position and velocity at 100 Hz
Written in C for bare-metal flashing and speed
Sensor Data
Parent CubeSat
Kalman Filter
Predict
Measure
Weight P & M
Final Estimate
Ground Station
∬a
(Sensor readings)
Measurements
(GND updates)
Error in prediction
Notes: Square root filtering? Look into this

## Slide 68: FSW - Kalman Filter Model
Actual Value
Sensor Measurements
t, time
Value
KF Estimate
Initial Estimate ± Error
What is a Kalman Filter?
Kalman filtering is an iterative mathematical process to quickly estimate a value such as your velocity or position using some model and measurements in “real-time”.
Driving Requirement | 
0.1 | Position shall be determined within 1 km sigma of true position
0.2 | Velocity shall be determined within 0.4 m/s sigma
0.3 | INS shall support data polling from parent satellite at 100 Hz or greater

## Slide 69: FLOPS
Floating Point Operations Per Second
Assuming 25 variable state vector, 6 measurements
Hand calculated 13,757,200 FLOPS
Does not take into account:
External libraries
I/O interfacing
Reading/writing from memory
Rescoped model, 6 state, 6 measurements
Hand calculated 468,600 FLOPS (~30x smaller)

## Slide 70: FLOPS
https://mediatum.ub.tum.de/doc/625604/625604

## Slide 71: State Extrapolation Equation
= Predicted system state vector at time step n+1
= Estimated system state vector at time step n
= Control vector (or input vector), essentially a measurable deterministic input to the system
= State Transition Matrix
= Control Matrix, or the Input Transition Matrix
The state extrapolation equation will give a prediction of the state one step in time forward using the current state vector estimate and system inputs.

## Slide 72: Covariance Extrapolation Equation
= The uncertainty of the last estimate - covariance matrix of the current state
= The uncertainty estimate of the prediction - covariance matrix for the next state
= State Transition Matrix
= Process Noise Matrix
The covariance extrapolation equation is a measure of how uncertain are we about that prediction for the state one step in time forward that we just calculated in the State Extrapolation Equation.

## Slide 73: Kalman Gain Equation
= The Kalman Gain
= The prior estimate uncertainty (covariance) matrix of the current state (predicted at the previous step)
= The Observation Matrix
= The Measurement Uncertainty (Measurement Noise Covariance Matrix)
The Kalman Gain is the weight given to the measurements and the current-state estimate. Essentially, the higher the kalman gain the more weight the measurements have on the outcome of the estimate or the more impact that the measurement will have on the next state prediction as opposed to the state prediction from the State Extrapolation Equation. The lower the Kalman Gain, the less the measurements influence the estimate and the more that the prediction from the State Extrapolation equation influences.

## Slide 74: State Update Equation
= The Estimated System state vector at time step n
= The Predicted system state vector at time step n - 1
= The Kalman Gain
= The Measurement Vector
= The Observation Matrix
The State Update Equation is the actual state estimate based on the predicted system state vector and the measurements weighted by the Kalman Gain.

## Slide 75: Covariance Update Equation
= The estimate uncertainty (covariance) matrix of the current state estimate
= The prior estimate uncertainty (covariance) matrix of the current state (predicted at the previous state)
= The Kalman Gain
= The Observation Matrix
= The Measurement Uncertainty (Measurement Noise Covariance Matrix)
= The Identity Matrix
The covariance update equation is a measure of how uncertain are we about the estimate we just calculated with the State Update Equation.

## Slide 76: FSW - Time Prediction (New Scope)
Kinematics
Bias Instability
Scale Factor
Single axis accelerometer decoupled model

## Slide 77: FSW - Process Noise Covariance Matrix

## Slide 78: Electronics Backup Slides

## Slide 79: Microcontroller Trade - Overview
Microcontrollers (MCUs) have the most promising CPU profile to fulfil our requirements:
Complex matrix calculations at 100Hz
Power constraint of 1W
Microprocessors are not a viable option as they draw too much power, FPGAs are too complex to use and whole integrated boards are too big and have unnecessary peripherals.
Notes: Jasmin comments:
Get something concrete in here

## Slide 80: Microcontroller Trade - Approach
Our research showed that a regular, trade-matrix based approach to part selection was not viable, as the most important characteristics (processing power and power consumption) are incredibly difficult to accurately quantify.
We thus used the quantifiable part values, such as size, number of I/O pins, comm. protocols etc. to establish a group of MCUs that work for our purpose.
Among different MCUs, ARM Cortex M architecture chips have come out on top when considering our requirements and system needs, as they are purpose-designed for low power consumption and high performance and check all other boxes.

## Slide 81: Microcontroller - Testing
In order to gauge if the ARM cortex M chips have enough processing power to fulfil requirements, we performed testing on the Arduino DUE, which uses an ARM M3 MCU, to establish a baseline for obtainable computing power.
This was accomplished by writing a script in C to represent the KF-computations needed to achieve our requirements.
The test shows that even with an ARM M3 chip, we are able to meet requirements, and have a large margin of error as we will use an ARM M4 chip, which our research shows has a calculation speed 5 times faster than the M3. The exact test results can be found on slide “FSW - Compute Time Estimates”
We will move from estimates to definitive numbers are we obtain a ARM M4 chip MCU with a dev-board to test it on.

## Slide 82: Electronics - Microcontroller Trade
Evaluation Criteria | STM32F3 (ARM M4) | STM32L4+ (ARM M4) | LCP1800 (ARM M3) | Arduino Due (ARM M3) | Necessity
Clock Speed (MHz) | 72 | 120 | 180 | 84 | -
Op. Voltage (V) | 2 - 3.6 | 1.7 - 3.6 | 1.8 - 3.6 | 3.3 | -
Max. Power Consumption (mW) | 38.8 | 64.8 | 75 | 1270 | < 850
FPU | Yes | Yes | No | No | -
Connectivity / I/O pins | I2C, SPI / 24 - 80 | I2C, SPI / 28 - 136 | I2C, SPI / 49 - 164 | I2C, SPI / 42 | I2C, SPI / >20
Flash memory / SRAM (KB) | 32 - 512 / 16 - 80 | 512 - 2048 / 320 - 640 | 128 - 1024 / 136 - 200 | 512 / 96 | > 30 / > 47
Dev board available? | Yes | Yes | No | Yes | Yes

## Slide 83: Electronics - Weighted Flash Memory Trade Matrix
($6.27)
Evaluation Criteria | Weight | GD5F1GQ5xExxG | W25Q02JV-DTR | S35ML04G3 | TC58BVG2S0HBAI6
Storage | 0.2 | 1 | 2 | 3 | 3
Cost (dollars) | 0.08 | 3 | 2.5 | 3 | 3
Max Power Consumption (W) | 0.18 | 3 | 1 | 2 | 2.5
Erase Time (ms) | 0.08 | 3 | 1 | 2 | 3
Comms Protocol | 0.1 | 3 | 3 | 3 | 1
Type | 0.18 | 3 | 1 | 3 | 3
Operating Voltage (V) | 0.18 | 3 | 2 | 2 | 2
Weighted Total: |  | 2.60 | 1.70 | 2.56 | 2.53
Notes: Mention we have the math available in a backup slide!!
Into detail why analog vs digital

## Slide 84: Electronics - Accelerometer Trade
Evaluation Criteria | Weight | SDI 1521 | SDI 1527 | ADXL355 | ADXL357
Dimensions (cm) | 0.1 | 0.89 x 0.89 x 0.42 | 0.89 x 0.89 x 0.42 | 0.6 x 0.56 x 0.22 | 0.6 x 0.56 x 0.22
Power (mW) | 0.2 | 32.5 | 25 | 0.72 | 0.72
Cost (dollars) | 0.1 | $465 | $650 | $36.38 | $70.85
Bias (mg) | 0.1 | 5 | 4 | 25 | 125
Bias Repeatability (m/s^2) | 0.3 | 0.03924 | 0.04905 | 0.24525 | 1.22625
Noise Spectral Density (µg / √Hz) | 0.1 | 7 | 10 | 22.5 | 75
Output Type | 0.1 | Analog | Analog | I²C, SPI | I²C, SPI
Total |  | 2.5 | 2.5 | 2.4 | 2

## Slide 85: Electronics - Accuracy Model General Feasibility
VectorNav provided general values for each sensor grade
Project only feasible for navigation grade
Only sensor available to us are consumer and some industrial
Notes: Done - Backup

## Slide 86: Electronics - Bias Term Calibration
Raw Accelerometer Data
Base Calibrated Data
Temperature Calibrated Data
Calibrated Data vs Lifetime plot
Base Bias Subtraction
Bias change with Temperature Subtraction
Notes: Done - Backup

## Slide 87: Electronics - Temperature Variations
We assume that the kalman filter can estimate the temperature variation of variables to the same degree (within 1 LSB of temperature sensor) at all temperatures. Therefore, a temperature control design solution is not necessary.
Notes: Done - Backup

## Slide 88: Electronics - Best Possible Calibration Accuracy
Notes: Done - Backup

## Slide 89: Electronics - Realistic Calibration Accuracy
Notes: Done - Backup

## Slide 90: Electronics - “Realistic Calibration”
A table top calibration of accelerometers and gyroscopes was done by a team of doctoral graduates. “Estimation of Deterministic and Stochastic IMU Error Parameters” by Derya Unsal and Kerim Demirbas
Accelerometer Bias Calibration Error Average | Gyro Bias Calibration Error Average
0.6187 % | 0.0478 %
Notes: Done - Backup

## Slide 91: Electronics - Accelerometer vs Gyro Influence
Because we get attitude updates from the star tracker every 0.1 seconds while we get telemetry updates every 2 hours, the gyroscope contributions to accuracy error is negligible compared to the accelerometer contribution to accuracy error.
Notes: Done - Backup

## Slide 92: Electronics - Number of Sensors
Only the velocity random walk and angle random walk terms (random noise terms) are reduced by 1/sqrt(N) with multiple sensors, therefore, including multiple sensors is not a feasible design solution
Notes: Done - Backup

## Slide 93: Electronics - Single vs Multi-axis Sensors
Complexities
  Alignment calibration, 3 different boards, Sample overlapping, more IO pins
Accelerometer | Number of Axes | Range (g) | Noise Density (μg/sqrt(Hz)
ADXL 103 | 1 | 3.4 | 110
ADXL 355 | 3 | 4 | 22.5
SDI 2012 | 1 | 4 | 10
SDI 1521 | 3 | 4 | 7
Notes: Not Done - Backup. If we want to expand to 3 axis then we can, Power consumption shouldn’t be an issue.

## Slide 94: Electronics - Thrusting Model
Modelled after the Themis Satellites:
Mass = 128 kg
4 Monopropellant hydrazine thrusters at 4.4 N each = 17.6 N
ΔV required for lunar maintenance orbit = 10 m/s
Using the ΔV equation, this leads to a burn time of 73 seconds
Sources: https://www.eoportal.org/satellite-missions/themis#spacecraft
https://ntrs.nasa.gov/api/citations/20070035736/downloads/20070035736.pdf
https://en.wikipedia.org/wiki/Delta-v#:~:text=Delta%2Dv%20is%20produced%20by,%2C%20delta%2Dv%20sums%20linearly
Assuming constant mass and thrust
Notes: Done - Backup

## Slide 95: Electronics - Accuracy Model with Thrusting
The descope will assume that the INS is only on during the duration of the burn
Notes: Done - Backup

## Slide 96: Error Verification Using Allan Variance
Allan Variance is a statistical approximation found using consecutive data points over a specific period of time σ2
This variance is related to quantization noise, angle random walk (or velocity random walk), bias instability, rate random walk, and rate ramp
Quantization Noise
Angle Random Walk
Bias Instability
Rate Random Walk
Drift Rate Ramp
Notes: Done - Verification

## Slide 97: Electronics - Allan Variance Computation
Using N consecutive data points with a sample time of t0
Form consecutive clusters of size n (n < N/2) with time
Cluster Average:
Next Cluster Average:
Allan Variance:
Notes: Done - Backup

## Slide 98: Ground Software Backup Slides

## Slide 99: Ground Software - FSW / GS Communications
E3: Communication | The GAINS system must have uplink and downlink capabilities with the ground station, as well as data transmission to the parent satellite.
(p,v,a) = (position, velocity, acceleration) | (θ,⍵,⍺) = angular (p,v,a)
Data Downlink: [timestamp, (p,v,a,θ,⍵,⍺), kalman uncertainties (p,v,a,θ,⍵,⍺)] = 1 + 9 + 9 + 18 = 37 states
Data Uplink: [timestamp, (p,v,a,θ,⍵,⍺), sigma error values (p,v,a,θ,⍵,⍺), operation mode] = 1 + 9 + 9 + 18 + 1 = 38 states
Data Rate: 460 kbps Full Duplex
38 states * 8 bytes per double * 7200 seconds * 100 Hz / 460000 bps = ~8 minutes of upload / download time

## Slide 100: Ground Software - FSW / GS Communications
Evaluation Criteria | Weight | USB-C | USB 3 | USB 2 | Ethernet (Cat 6) | HDMI
Average Data Bit Rate (Gbit/s) | 0.3 | 10 | 5 | 0.5 | 2 | 5
C++ Integration Complexity | 0.2 | Simple | Simple | Simple | Medium | Difficult
Max Length (meters) | 0.1 | 2 | 3 | 5 | 100 | 13
Duplex | 0.2 | Full | Full | Half | 4 2-way channels | Full
Microcontroller Support | 0.2 | On Board | Through Adapter | Through Adapter | Through Adapter | Through Adapter
Negligible Properties: Price, Power Supplied, Packets Supported

## Slide 101: Ground Software - FSW / GS Communications
Evaluation Criteria | Weight | USB-C | USB 3 | USB 2 | Ethernet (Cat 6) | HDMI
Average Data Bit Rate (Gbit/s) | 0.3 | 3 | 3 | 2 | 3 | 3
C++ Integration Complexity | 0.2 | 3 | 3 | 3 | 2 | 1
Max Length (meters) | 0.1 | 2 | 2 | 3 | 3 | 3
Duplex | 0.2 | 3 | 3 | 1 | 3 | 3
Microcontroller Support | 0.2 | 3 | 2 | 2 | 2 | 2
Sum (0-3) | 1 | 2.9 | 2.7 | 2.1 | 2.6 | 2.4
Negligible Properties: Price, Power Supplied, Packets Supported

## Slide 102: Ground Software - N-Body Model
The N-Body Model is a dynamic simulation of particles under influences by external forces
  Will take in Acceleration, Velocity, and Position Vectors at a final point from onboard INS computed calculations
  Acceleration vector will be modified to reflect gravitational acceleration
  The model then propagates with an integrator for the next 24 hours
  New trajectory X, Y, Z position estimations are then sent to graphical user interface
Model will use ephemeris data from the NAIF SPICE data
Validation of model will come from NASA GMAT comparisons
  NASA General Mission Analysis Tool useful to design orbital trajectories and missions

## Slide 103: Ground Software - N-Body Model
GAINS Ground Software will use N-Body Naive Propagation (particles only affected by force of gravitation)
Gravitational Acceleration of Body is then found by dividing by mass of spacecraft.
When the gravitational acceleration vector is found, the gravitational vector is added to initial acceleration vector of SC to get a final acceleration vector for state propagation

## Slide 104: Ground Software - Numerical Integration
Model of 2nd Order Differential Equation: Spring Mass System
Timestep: 0.1 seconds over 30 seconds
Approximate position
Verify accuracy with INS

## Slide 105: Ground Software - Numerical Integration
RK4 works to average four slopes from two consecutive timesteps to approximate the next point.
Customizable and compatible with C++ (No ode45 on c++)
Implements the linear multistep method - “Adam-Bashforth” Method

## Slide 106: Admin Backup Slides

## Slide 107: Human Resources
Professor Dale Lawrence
Trudy Schwartz
Sebastian Wankmuller
Professor Eric Bogatin
Professor Marcus Holzinger
Samuel Fedeler
Professor Penina Axelrad
Matt Rhode
Professor Katherine Wingate
Notes: Ahmed and McMahon

## Slide 108: Old Work Plan
Mechanical
Flight Software
Ground Software
Electronics

## Slide 109: Old Gantt - Mechanical

## Slide 110: Old Gantt - Flight Software

## Slide 111: Old Gantt - Electronics

## Slide 112: Old Gantt - Ground Software

## Slide 113: Timeline (Path Taken)
Models tie customer requirements to sensor specs
Customer Requirements
Mathematical models
Sensor Specs
Customer Requirements | Mathematical Models | Sensor Specs
1 km position accuracy, 0.4 m/s velocity accuracy 1 W power budget >=100 Hz computation output | Accuracy Model Kalman filter computation estimate Allan Variance Bias Calibration Model | ADC bits 0g bias Random Noise Repeatability Clock speed

## Slide 114: Risk Matrix (Old)
Very Likely |  |  | Lack of expertise | Sensor drift, sensor uncertainty | 
Likely |  |  |  |  | 
Possible |  |  |  |  | Part availability
Unlikely |  | Testing safety |  | Schedule | 
Very Unlikely |  |  | Budget |  | 
 | Negligible | Minor | Moderate | Significant | Severe
Risk Level
Acceptable
Concerning
Unacceptable
Impact/Consequence
Probability