## Slide 1: GAINS General Atomics Inertial Navigation System
Presenters:
Ben McHugh, Tucker Peyok, Alfredo Restrepo, Kaylie Rick, Brian Trybus, Addison Woodard
Team Members:
Bennet Grow, Cannon Palmer, Alex Pichler, Derek Popich, Jason Popich, Ross White
Sponsor:
General Atomics (GA)
Faculty Advisor:
Dr. Dale Lawrence
March 6, 2023
Test Readiness Review

## Slide 2: Agenda
Project Overview
Project Updates
Schedule
Test Readiness
  Environmental Temperature Test
  Controlled Positioning Test
Budget

## Slide 3: Project Overview
Notes: Recap the project descriptions that appeared in the PDD, CDD, and PDR. It should be a concise overview that assumes the review board has not just reviewed these earlier documents. That is, the CDR should stand alone as a description of the project from concept through design solution. Typically, this overview will include a CONOPS, updated to help explain the project purpose and specific objectives as quickly and clearly as possible.

## Slide 4: Mission Statement
Project GAINS aims to develop an Inertial Navigation System (INS) prototype for installation on cube-satellites in cislunar applications. The GAINS prototype will be developed to maximize accuracy of estimated position and velocity with the aid of external error corrections.
Notes: Addi
Say what INS is: Sensor suite with computations
Cislunar = orbit trajectory between the Earth and Moon

## Slide 5: Mission Objectives
2
1
3
Provide accurate inertial position and velocity to a CubeSat in a cislunar orbit with an INS, outside of GPS range
Modularity, such that the system can be installed in a variety of standardized General Atomics CubeSats
Ground segment to receive INS data and display trajectory in a Graphical User Interface (GUI)
Notes: Addi
*2. Modularity such that the size and power provide a standardize

## Slide 6: Full Mission CONOPS
2. Lunar orbit
3. INS activation
4a. INS based position maintenance and navigation
KEY
4b. Ground station contacts, every 2 hours
Ground station
Uplink/Downlink
1. Launch
Trajectory
In Scope
6 hrs of contact
6 hrs of contact
6 hrs of contact
2 hrs Loss of Contact
2 hrs LoC
2 hrs LoC
24 hrs
Notes: Addi

## Slide 7: GAINS Project CONOPS
Parent Cubesat
Downlink computed AD data package
Positional Drift Corrections, maximum 2 hours LOC
GAINS
Computation
Measurement
Computed AD solution and data
Positional Drift Corrections
Star Tracker
Attitude Drift Corrections @ 10Hz
Satellite polling @ 100Hz
(Position and velocity calculations)
Ground Station
Storage
GS Contact Maintained
GS Contact Achieved (send all storage)
Truth Data & Communication emulation for testing
Overview
In Scope
In Scope
Notes: Addi

## Slide 8: Critical Project Elements
Critical Element | Constraint Rationale
E1: Accuracy | The GAINS system should have a peak position error of no more than 1 km and peak velocity error of no more than 0.4 m/s.
E2: Calculation | The GAINS system will estimate its inertial position and velocity in real time using measurements from its integrated sensors.
E3: Communication | The GAINS system must have uplink and downlink capabilities with the ground station, as well as data transmission to the parent satellite.
E4: Display | The GAINS ground station must include a Graphical User Interface (GUI) with a real time status, trajectory, and power on/off switches.
E5: Integration | The GAINS system must have flanges for mounting to the parent satellite.
E6: Testing | The GAINS system shall be tested to ensure project elements fulfill customer mission objectives.

## Slide 9: System FBD

## Slide 10: Project Updates
Notes: 20%
• Provide a chart of ALL tests that have or will be performed. Indicate which ones have been completed.
• Review the whole project schedule in the form of the Gantt chart, showing overall progress toward goals. In this case, the status should be described with an emphasis on testing. Highlight any major changes in the project schedule since CDR, and indicate shifts in critical path or margins.

## Slide 11: Baseline Design Progress
GAINS Enclosure
GAINS PCB
GAINS GUI
*Orbital mode shown, testing and symposium view also in development
Notes: Addi
*2. Modularity such that the size and power provide a standardize

## Slide 12: Schedule
Notes: 20%
• Provide a chart of ALL tests that have or will be performed. Indicate which ones have been completed.
• Review the whole project schedule in the form of the Gantt chart, showing overall progress toward goals. In this case, the status should be described with an emphasis on testing. Highlight any major changes in the project schedule since CDR, and indicate shifts in critical path or margins.

## Slide 13: Gantt Chart
TODAY
Subsystem Critical Path
Dependency
Milestone
KEY

## Slide 14: All Test Overview
 | Test Name | Model/ Reference | Requirements Verified | Equipment/ facilities | Status
Unit/Device | Component Checks | Datasheets | 1.2.1 | Multimeter, Power Supply | In progress
 | Flight software functionality test | Matlab Kalman Filter | 1.2.2, 1.2.3, 1.2.4 | N/A | In progress
 | GUI Functionality Test | GUI Concept | 1.3 | N/A | Start date: 3/10
Subsystem | Electronic Circuit Functionality | Altium Model | 1.2.1 | Breadboard, Power Supply, Multimeter | In progress
 | Flight Software and Electronics Integration | Computation Speed Model | 1.2.7 | N/A | Start date: 3/10
 | Mechanical and Electronics Integration | CAD Model | 1.2.1 | Ruler, Scale, Multimeter | In progress
 | Flight Software and Ground Software Communication | Data rate, Packet loss | 1.2.3, 1.2.7, 1.3.1 | N/A | Start date: 3/10
System | Next Slide... |  |  |  | 

## Slide 15: All Test Overview
 | Test Name | Model/ Reference | Requirements Verified | Equipment/ facilities | Status
System | Tabletop Calibration | Bias Drift, Velocity Random Walk Model, Repeatability | 1.2.1, 1.2.3, 1.2.4 | Table, Computer | Start date: 3/10
 | Environmental Temperature | Bias Drift with Temperature Model, Datasheets | 1.2.1, 1.2.3, 1.2.4 | Oven + Freezer or General Atomics Thermal Chamber | Start date: 3/17
 | Controlled Positioning | Bias Drift, VRW, Temperature | 1.2.1, 1.2.3, 1.2.4, 1.2.7 | 3-axis CNC | Start date: 3/24
*No test is completed just yet. Components are just now arriving, and unit testing will begin March 1st.
Requirements available
in Backup Slides

## Slide 16: Test Readiness
Notes: 60%
Select two to three major tests that will be performed. These should be tests that are verifying top level driving requirements or validating high level mission objectives, buying down operational risk, or closing the loop on a model. Typically this involves tests that integrate multiple subsystems and are at the system level of testing. Ensure that you can measure the performance of your design- (how fast, what range, what current, what latency, etc) as opposed to measuring a simple binary outcome.
For these two to three tests, cover:
• What is being tested and why: your rationale for performing the test in terms of requirements to be verified or mission objectives to be validated.
• Highlight critical pre-requisite tests planned/completed that will or do demonstrate this test will be successful. (For example, the components are operating within datasheet ranges, signals could be sent and received, etc) This should not be a deep dive, but rather a quick summary that can be completed in 1 to 2 minutes.
• Describe the scope of the testing tasks in the project specifically:
o the design of the test fixtures, selection and calibration of sensors, data acquisition plans
o test equipment and/or facilities are needed
o an overview of the test and safety procedures
• Describe how the test(s) will reduce risk to meeting requirements, expected results, and how models will be validated. Include clear pass/fail criteria ALONG with expected performance measurements.

## Slide 17: Environmental Temperature Test
Notes: 60%
Select two to three major tests that will be performed. These should be tests that are verifying top level driving requirements or validating high level mission objectives, buying down operational risk, or closing the loop on a model. Typically this involves tests that integrate multiple subsystems and are at the system level of testing. Ensure that you can measure the performance of your design- (how fast, what range, what current, what latency, etc) as opposed to measuring a simple binary outcome.
For these two to three tests, cover:
• What is being tested and why: your rationale for performing the test in terms of requirements to be verified or mission objectives to be validated.
• Highlight critical pre-requisite tests planned/completed that will or do demonstrate this test will be successful. (For example, the components are operating within datasheet ranges, signals could be sent and received, etc) This should not be a deep dive, but rather a quick summary that can be completed in 1 to 2 minutes.
• Describe the scope of the testing tasks in the project specifically:
o the design of the test fixtures, selection and calibration of sensors, data acquisition plans
o test equipment and/or facilities are needed
o an overview of the test and safety procedures
• Describe how the test(s) will reduce risk to meeting requirements, expected results, and how models will be validated. Include clear pass/fail criteria ALONG with expected performance measurements.

## Slide 18: Environmental Temperature Test
Overview:
  Characterize SDI 1521-L accelerometer bias with respect to accelerometer temperature sensor
  Calibrate out bias error to minimize position and velocity error for all operational temperatures (0°C to 60 °C)
  Verify internal temperature does not exceed 125°C and harm microprocessor
C.9 | INS environment shall be in a temperature range of 0-60 degrees Celsius
SDI 1521-L Temperature (°C)
Bias Error vs. SDI 1521-L Temperature
Bias Error [m/s2]
Cooling test
Heating test
Sample (uncalibrated) bias error curve
Datasheet defined potential bias error bounds
Ambient Temperature
Start Date: 3/17

## Slide 19: Environmental Temperature Test
Rationale/Motivation:
  Accelerometer bias is the dominant error source in final position and velocity accuracy
  Characterizing this bias will allow the Kalman Filter to more accurately compute the INS position and velocity

## Slide 20: Environmental Temperature Test
AΣΛ F150
Borrowed from AES Electronics shop
Home Oven
Team member's house
Home Freezer
Team member's house
2 Thermocouples
Borrowed from AES Electronics shop
Prerequisite Tests:
  Individual sensor operation verification
  Temperature sensor calibration
  Flight/Ground software communication
  Full PCB sub-system test
  Test chamber temperature control baseline
Test Needs:
  Hot temperature chamber (oven at 60°C)
  Cold temperature chamber (freezer at 0°C)
  External temperature measurement device (precision thermocouple, ±0.015 °C accuracy)
  Two thermocouples
  Completed GAINS product
Notes: Mention accuracy of thermocouple (0.001 deg C idk), mention calibration of thermocouple

## Slide 21: Environmental Temperature Test
High-Level Test Procedure:
Set environmental chamber to minimum/maximum of requirement range
Validate temperature with thermometer
Place GAINS in chamber, begin collecting data
Keep in environment until thermal equilibrium, finish collecting data
Remove GAINS and thermometer, analyze results
Generate bias change in temperature curve, integrate with Kalman filter
Re-run test with temperature calibration
Repeat for each axis of the accelerometer
GAINS
GAINS
60 °C
(140 °F)
0 °C
(32 °F)
Ground Station
Precision Thermometer
(AΣΛ F150)
Safety Considerations:
Handle GAINS with oven mitts after hot temperature test
Abort test if internal GAINS temperature exceeds allowable component temperatures

## Slide 22: Environmental Temperature Test
Expected Results:
GAINS Acceleration of Gravity Measurement
0 60
Temperature (°C)
Acceleration (g)
1
GAINS Acceleration of Gravity Measurement
0 60
Temperature (°C)
Acceleration (g)
1
SDI 1521-L Temperature (°C)
Bias Error vs. SDI 1521-L Temperature
Bias Error [m/s2]
Cooling test
Heating test
Prior to Calibration: Bias error to increase positively under hot conditions, and increase negatively under cold conditions
Post Calibration: Decreased Biases for 0°C to 60°C range, more accurate final INS position and velocity prediction

## Slide 23: Environmental Temperature Test
Validation Criteria:
  Pass: GAINS accelerometer bias drift does not exceed 0.4mg after temperature calibration, internal temperature does not exceed 125°C
    Largest possible bias = 20mg
    Max allowable velocity error = 0.39 m/s
    Minimum calibration = 0.4 mg or 0.004 m/s
  Fail: GAINS bias drift exceeds 0.4mg, internal temperature exceeds 125°C, test chamber fails to reach temperature thresholds, corrupt data
Risk reduction of requirement satisfaction:
  Post calibration, accelerometer accuracy will increase
    Accelerometer temperature bias will be characterized for expected thermal environment

## Slide 24: Controlled Positioning Test
Notes: 60%
Select two to three major tests that will be performed. These should be tests that are verifying top level driving requirements or validating high level mission objectives, buying down operational risk, or closing the loop on a model. Typically this involves tests that integrate multiple subsystems and are at the system level of testing. Ensure that you can measure the performance of your design- (how fast, what range, what current, what latency, etc) as opposed to measuring a simple binary outcome.
For these two to three tests, cover:
• What is being tested and why: your rationale for performing the test in terms of requirements to be verified or mission objectives to be validated.
• Highlight critical pre-requisite tests planned/completed that will or do demonstrate this test will be successful. (For example, the components are operating within datasheet ranges, signals could be sent and received, etc) This should not be a deep dive, but rather a quick summary that can be completed in 1 to 2 minutes.
• Describe the scope of the testing tasks in the project specifically:
o the design of the test fixtures, selection and calibration of sensors, data acquisition plans
o test equipment and/or facilities are needed
o an overview of the test and safety procedures
• Describe how the test(s) will reduce risk to meeting requirements, expected results, and how models will be validated. Include clear pass/fail criteria ALONG with expected performance measurements.

## Slide 25: Controlled Positioning Test
Overview:
  Position and velocity accuracy estimation of the GAINS with simulated ground station contact, and loss of contact periods
  Real time trajectory plotting of the GAINS on the GUI
E1: Accuracy | The GAINS system should have a peak position error of no more than 1 km and peak velocity error of no more than 0.4 m/s.
Start Date: 3/24

## Slide 26: Controlled Positioning Test
Rationale/Motivation:
  Accurate position and velocity estimation is critical to mission success, and a top-level requirement by the customer
  Characterize the effect of error sources in the electronics on position and velocity accuracy (i.e. Bias Calibration, Velocity Random Walk, Scale Factor, Repeatability)
E1: Accuracy | The GAINS system should have a peak position error of no more than 1 km and peak velocity error of no more than 0.4 m/s.

## Slide 27: Controlled Positioning Test
Prerequisite Tests:
  All other component, subsystem, and system tests
Test Needs:
  5 axis CNC Machine
  Pre-coded path (G-code)
    Programming language used in CNC machines to control movements and operations
  Camera to record revolution time
  Completed GAINS product
Hurco VM10Ui
ITLL
G-coded Path
Team member written
Video Camera on Fixed Structure
Team member provided

## Slide 28: Controlled Positioning Test
Methodology:
  CNC trajectory will follow a circular path to impart a constant acceleration on the INS, simulating the Themis Satellite's Hydrazine gas thrusters
    Assumed ΔV required for lunar maintenance burn = 10 m/s
    Typical burn duration = 73 sec
    Centripetal Acceleration Magnitude = 0.137 m/s2
Test Specifications:
  5-Axis CNC Hurco VM10Ui:
    Max feed rate = 28 m/min
    Minimum Bed Dimension (Y): 0.406 m
  Test Trajectory:
    Tangential Velocity: 8.604 m/min
    Trajectory Diameter: 0.3 m
    Revolutions: 11.108
0.406 m
0.15 m
0.533 m
GAINS

## Slide 29: Controlled Positioning Test
High-Level Test Procedure:
Import pre-coded path to Ground Software for plotting and comparison to INS readings
Place the GAINS in CNC
Run coded path
  Simulate positional changes in 2 axes (spacecraft thrusting)
  Use video recording to correlate time with CNC start and stop
Monitor GUI trajectory plot, simulate loss of contact
Path ends, remove GAINS, analyze data
Repeat for each body axis of interest
Safety Considerations:
Secure GAINS onto CNC fixture
Training and qualification to operate CNC
Implement measures to ensure the proper organization and routing of GAINS cables to prevent entanglement

## Slide 30: Controlled Positioning Error Analysis
Gerror
INSpos
Perror
Gpos
INSpos
Perror
Gpos
Gerror
Error Analysis:
  The GAINS calculated position will be compared to the commanded position of the CNC
  CNC error in that commanded position will be added generate our final positional error.
  The time derivative of our positional error throughout the test will yield the velocity error
Notes: Mention CDR velocity measurement concern in script

## Slide 31: Controlled Positioning Test
Expected Results:
  Position and velocity measurements accurate under various acceleration scenarios
    Relative to the path defined by the CNC input G-Code
  Characterize the effect of various error sources
    Bias Calibration, Velocity Random Walk, Scale Factor, and Repeatability
  Final position and velocity accuracy value
    Integrated into expected bias of the Kalman Filter as a function of time
Acceleration (m/s2)
GAINS Test Acceleration
0 120
Time (s)
0
0.137

## Slide 32: Controlled Positioning Test
Validation Criteria:
  Pass: Satisfy mission accuracy requirements of the INS
    Position error less than 1 km
    Velocity error less than 0.4 m/s
  Fail: Corrupt data, incomplete test, accuracy requirement not met
    Revisit tabletop test to insure proper calibration of INS
    Investigate test set up for potential error sources
    Monitor test in real-time to detect any unexpected behavior or deviations from the programmed path
Risk reduction of requirement satisfaction:
  Kalman Filter will be minimizing error through simulated thrusting period, error will be within customer requirements.

## Slide 33: Budget
Notes: 10%
• Provide an update on all project expenses including status of parts/materials procurement and the financial budget.

## Slide 34: Budget
Part Type | Part Name | Qty | Cost/unit | Total Cost | Purchased? | Received?
3-axis Accelerometer | SDI 1521-L | 5 | $180 | $900 | Yes | Yes
3-axis Gyroscope | IAM-20380HT | 10 | $11.91 | $119.10 | Yes | No
Microcontroller | Teensy 4.1 w/ Ethernet Hat | 4 | $41.50 | $166 | Yes | Yes
PCB | “GAINS PCB” | 3 | ~ $30 | $90 | No | No
Flash Memory | GD5F1GQ4UFYIGR | 2 | $4.84 | $9.68 | No | No
Dev-Boards | Accel/Gyro Dev | 2 | ~ $30 | $60 | No | No
Housing Material | Aluminum 6061 (1.25” x 12” x 12”) | 180 in3 | $127.52 | $127.52 | Yes | Yes
Misc. (cables, ports, shipping, etc) | Various | - | ~ $200 | $200 | No | No
Total Projected Cost: |  |  |  | $1662.62 |  | 
TOTAL | $4000 | 
SPENT: | $1312.62 | 33%
REMAINING: | $2687.38 | 67%
*Purchased/Received statuses may change between submission and presentation.

## Slide 35: Backup

## Slide 36: Top Level Requirements

## Slide 37: Level 1 Requirements

## Slide 38: Level 2 Requirements

## Slide 39: Centripetal Motion vs. Linear Motion
Centripetal Motion
Simulate the acceleration effects of Themis Satellite's Hydrazine gas thrusters
  Typical burn duration: ~ 73 seconds
Relevant position and velocity approximations
Subjected to an extended duration of acceleration for relevant testing
  Enable various acceleration scenarios
An illustrative representation aimed at depicting the projected acceleration trend corresponding to the described motion.
GAINS
ac
Body x-axis
t > 0 [s]
GAINS
ac
Body x-axis
t >> 0 [s]
centripetal acceleration

## Slide 40: Centripetal Motion vs. Linear Motion
Linear Motion
  INS exhibits linear reciprocating motion
  Short-duration, high-amplitude acceleration events
  Discrepancy between the expected trajectory of the INS during thrusting periods
An illustrative representation aimed at depicting the projected acceleration trend corresponding to the described motion.

## Slide 41: CNC Trajectory Math
Body frame force vector rotates around the z-axis
Feed-rate required to meet required ac :

## Slide 42: PCB and Breakout Boards
PCB Design
Accelerometer Breakout Board
Gyroscope Breakout Board

## Slide 43: Electronics FBD

## Slide 44: Flight Software FBD

## Slide 45: Ground Software FBD

## Slide 46: Mounting for CNC Testing

## Slide 47: Mounting for CNC Testing
*Not moving in anticipated path
Generalized illustration purposes only