## Slide 1: Critical Design Review
THE ICEBOX
Lewis bittner, Willy gettinger, collin hayes,
reina krumvieda, Alayna Lauffer, ZaK reichenbach,
fabrizio roberts, Andrew sapuppo, Amir tillis
SPONSORS: LOCKHEED MARTIN, AEROSPACE CORPORATION, BALL AEROSPACE
1

## Slide 2: Project Purpose and Objectives
1
Project Description
2
Project Purpose
3
CONOPS
CPE & Risks
Verification & Validation
Planning
Purpose
Solution
Requirements
2
2

## Slide 3: Project Scope
Project Description
CONOPS
Project Scope
Project Definition
Concept
- 3 High Level Objectives
- Architecture in the cislunar regime
- Systems of systems infrastructure
- Multi-objective analysis
Deliverables
- Software analysis of system
- Hardware demonstration
3
Notes: Our objective is to create a cost-effective way to supply fuel and refined byproducts for lunar missions better than current methods (launching fuel from Earth)

## Slide 4: Project Definition
Problem
- Need for fuel and resources on the Moon
- Sustain long term missions
Solution
- Cost-effective supply of fuel and refined byproducts for lunar missions
- More cost effective and timely to lunar customers than current methods
Project Description
CONOPS
Project Scope
Project Definition
4
Notes: Problem
There is a need for fuel and resources on the Moon to sustain long term missions (> a few weeks)
Solution:
Our objective is to create a cost-effective way to supply fuel and refined byproducts for lunar missions better than current methods (launching fuel from Earth)

## Slide 5: Project Description: Systems of Systems Analysis
High Level Objectives
Fuel mining, production, and storage logistics and services
Space-based power logistics and services
Return on investment
Specific Objectives
Generate fuel and other resources to sustain lunar missions and sell to customers
Receiving enough power to operate the infrastructure with some margin
Reduce cost of resources, and supply/sell additional power to customers
Project Description
CONOPS
Project Scope
Project Definition
5

## Slide 6
Project Description
CONOPS
Project Scope
Project Definition
6
1. Collect solar energy to charge flywheels and supply power to infrastructure
2. Collect regolith from surface with drum excavator rover
3. Process regolith using hydrogen reduction and water electrolysis
4. Supply customers on surface, or transport to orbit to supply orbital missions via kinetic launch system
CONOPS: The Icebox Lunar Refueling Infrastructure (Size is not to scale)
Shackleton crater (NOT TO SCALE)

## Slide 7: Design Solution
1
Functional Block Diagrams
2
Pareto Frontier
3
Chosen Architecture
7
CPE & Risks
Verification & Validation
Planning
Purpose
Solution
Requirements

## Slide 8: Functional Block Diagram Legend
Start
Option
Input; output
Model; Process; Function
Transition; Organization
FBD
Pareto Frontier
Architecture
8

## Slide 9
9

## Slide 10
10

## Slide 11
11

## Slide 12: Pareto Frontier Model
FBD
Pareto Frontier
Architecture
- Developed model to iterate through technology trade space of each sub-systems
- Model operated by calculating material through put in kg/hr and power consumption in kW primarily in addition in each of these categories:
- Efficiency - Cost
- Lifetime
- Scores were then summed respectively between all subsystems, to create a final array infrastructure score.
- 2304 different infrastructure options from varying the models
12
Notes: Collin

## Slide 13: Pareto Infrastructure Objectives
FBD
Pareto Frontier
Architecture
All Possible Infrastructure Scores
Objective Space Infrastructure Scores
13
13
Notes: Collin

## Slide 14: Objective Space: Decision
Maximize Fuel Production
Select Most Profitable Model
14
Maximum Fuel Production
Most Profitable
FBD
Pareto Frontier
Architecture
Notes: Collin

## Slide 15: What - Chosen Architecture
Solution
The best working architecture provided from the Pareto Frontier
- Drum excavator style rover
- Hydrogen reduction with water electrolysis
- All ground-based power from solar arrays - Flywheel energy storage
- Spin launch delivery
FBD
Pareto Frontier
Architecture
15
Notes: Collin
Ground based power: (Orbital was deemed too expensive)

## Slide 16: Critical Project Elements and Risks
1
Architecture
2
Risks
1
CPEs
CPE & Risks
Verification & Validation
Planning
Purpose
Solution
Requirements
16
Notes: Holzinger feedback:
ID 4-6 specific risks and mitigation strategy for each of those risks
- can go through with test inspection or analysis and verify we are meeting level 2 reqs
Next Semester
- Hardware demonstration for Level 2 Requirements

## Slide 17: Critical Project Elements "Level 0 Requirements"
CPE​ | Description​
Land Rights and Policy​ | Minimum policy to make infrastructure possible​
Fuel Mining, Processing, and Storage System​ | Mining system, transportation system, processing system, storage system, method of distribution​
Space Based Power System​ | Power collection, power storage, power transmission to other systems​
Return on Investment​ | Cost, necessity, value​
Multi-level Objective Analysis​ | Model inputs, outputs, constraints​
Risk Reduction Hardware Demonstration​ | Assess and mitigate infrastructure risk​
CPE - Level 0
Risk Matrix
Risk Mitigation
17
Notes: F – mention policy

## Slide 18: Risk Matrix
CPE - Level 0
Risk Matrix
Risk Mitigation
18
Notes: F – note main risks

## Slide 19: Risk Matrix
19
Notes: F

## Slide 20: Risk Mitigation
RISKS
T9: Lack of efficient energy storage
T8: Excavation system breaks
T7: Rover flips or gets stuck
MITIGATION STRATEGY
Create flywheel for storing energy instead of chemical batteries → *most feasible*
Have repair robots or send astronaut technicians → high cost, inefficient
CPE - Level 0
Risk Matrix
Risk Mitigation
20
Notes: F

## Slide 21: Design Requirements and their Satisfaction
1
Requirements
2
Models
CPE & Risks
Verification & Validation
Planning
Purpose
Solution
Requirements
21

## Slide 22: Level 1 Requirements
Requirements
Must provide...
~1000 kg of fuel per hour
power operation architecture
Must...
profit over lifespan of the system
Justification
- Meaningful amount of fuel to customers
- Architecture requires specific power requirements
- Business must be profitable throughout lifetime
Models
Level 1
Level 2
Architecture
22
Notes: F - Afterwards, remind why we chose what architecture we did based on these

## Slide 23: Why - Chosen Architecture ~ Ground System ~
Models
Level 1
Level 2
Architecture
Drum excavator for maximizing fuel production
  - simpler and less expensive than other options (robotic arm, astronaut miners, pareto tested mining methods)
  - most efficient & profitable
  Hydrogen reduction
  - minimizes weight of needed reactant therefore reducing processing cost
  Spin launch for delivery
  - minimizes amount of fuel to sell to customers
  - substitute for using rocket fuel for launches
23
Notes: Description of what is most important to success of the project and why these elements were chosen to focus on in this presentation
Convey your understanding of how the system works and what design features, attributes, or characteristics are most important to that functionality

## Slide 24: Why - Chosen Architecture ~ Power System ~
Models
Level 1
Level 2
Architecture
Ground based solar arrays
  - solar panels reliable and used in nearly all space applications
  - cheaper and more feasible (solar arrays for satellites size of ISS)
  Flywheel energy storage system
  - High specific energy (storage)
  - higher temperature operating range than conventional batteries
  - longer lasting than batteries since no discharge efficiency
  - Moon surface vacuum → less friction and higher efficiency
24
Notes: Collin
Description of what is most important to success of the project and why these elements were chosen to focus on in this presentation
Convey your understanding of how the system works and what design features, attributes, or characteristics are most important to that functionality

## Slide 25: Ground: Excavation Model
Assumptions:
  - Size limitation from "Over the Dusty Moon" Challenge
    - Lunar dust smaller than 20 microns
  - 1 of 3 typical mining tools compared at a time
  - Constant motor RPM between conveyor and drum style methods
  - Reasonable estimates for excavation rate based of size and rates from other company and industry listings
Models
Level 1
Level 2
Architecture
25

## Slide 26: Ground: Excavation Model
Outputs:
- Excavator productivity
- Bucket, Drum, Conveyor
  -
Inputs
  - Regolith Properties
  - Excavator Properties
  -
Models
Level 1
Level 2
Architecture
26

## Slide 27: Ground: Processing Model
Assumptions:
  - 500 kg loss from storage 1 to 2
  - Regolith starting at lunar surface temp at Equator during day: 260 K
  - Ideal stoichiometry & reaction conditions
  - No slag or excess CO2 produced
  - Perfect Scaling
  - No surface film
  - Adiabatic containers
Models
Level 1
Level 2
Architecture
27
Notes: F

## Slide 28: Ground: Processing Model
  Carbothermal Reduction:
  - Methane Reduction
  - Carbon Monoxide Reduction
  - Water Electrolysis
  Overall: Faster, Requires less Power
  Hydrogen Reduction:
  - Hydrogen Reduction
  - Water Electrolysis
  Overall: Cheaper, More Efficient
Models
Level 1
Level 2
Architecture
28
Notes: F

## Slide 29: ROI: Introduction
Definition: Return on Investment (ROI) is a key measure of the profit derived from any investment.
Model Goal: To calculate the ROI for different infrastructure models, technology combinations, and products to find the infrastructure that will be the most profitable.
29
Models
Level 1
Level 2
Architecture

## Slide 30: ROI: Integration
ROI is dependent on the integration of all subsystems
Each sub-system has cost associated with it, such as operating cost, development cost, and other extraneous cost.
30
Models
Level 1
Level 2
Architecture

## Slide 31: ROI Model Assumptions:
There is a limited time span in which the infrastructure will be able to operate.
Lifetime Revenue is calculated based on the value of kilograms of resources mined over the lifetime of the infrastructure.
Lifetime Revenue is independent of customer demand over time.
  This is due to the predicted demand to be on the moon.
  A Depot/Reserve style operation in which customers can buy when they arrive.
31
Models
Level 1
Level 2
Architecture

## Slide 32
Business Model
Chart: Predicted Customer Use over Time
| 2024 | 2025 | 2026 | 2027 | 2028
Predicted Customer Use | 1 | 3 | 6 | 15 | 20
Motto: "Mine, Store, Deliver“
Model: Business to Consumer via Depot/Reserve Business Model
Customer Demand: Increasing over time as Mission Increase to moon.
Lifetime Profit: ~1.1 Billion USD
Annualized ROI: Variable and Dependent on Customer Use
32
Models
Level 1
Level 2
Architecture

## Slide 33
33
Models
Level 1
Level 2
Architecture

## Slide 34
Infrastructure Cost Model
Ground Technology Lifespan
Ground Technology Output
Conversion
Ground Subsystems:
Mining, Processing, & Transport Cost/kg
Power Technology Lifespan
Power Output
Conversion
Power: Cost/kJ
34
Models
Level 1
Level 2
Architecture
Notes: Lewis- Initial cost to moon
Fabrizio- Processing and Initial
Andrew- Cost to get customer

## Slide 35: ROI: Code Integration
Due to a lack of experience, planning, communication, and varying assumptions. The integration of different subsystems did not go as expected.
This created a delay and hardships when attempting to create the pareto. The attempt to standardized the code took time and went subsystem by subsystem.
Unfortunately, ROI was the last system to be integrated. With the given timeframe, the Infrastructure Cost model developed was unable to be integrated due to time and complexity.
35
Models
Level 1
Level 2
Architecture

## Slide 36: ROI: Outcome
The outcome of this is a non-standardized cost considerations for each sub-system, with limited consistency between systems.
The cost does not factor in key variables such as system lifespan and cost per operating unit. (Ex: $/kg)
The cost passed through do considering Development, Launch, and other major cost excursions.
Overall, we feel that the cost we considered, are of such a magnitude and scale, that the error is still within an acceptable range.
36
Models
Level 1
Level 2
Architecture

## Slide 37
Lifetime Revenue Model
Ground Technology Output
Conversion
Ground Technology Lifespan
Resource Abundance on Moon
Launch Cost Model
37
Models
Level 1
Level 2
Architecture

## Slide 38
Launch Cost Model
38
Purpose: Finding the selling price of products, by comparing the cost of getting resources to the moon via launching.
Product Cost = Launch Cost + Guestimate Mass *(Product Cost on Earth)
Falcon 9 Launch Cost
Maximum Payload
Product Cost on Earth based on Market
Models
Level 1
Level 2
Architecture

## Slide 39: Level 2 Requirements
Requirements
Rover must collect 16200 kg of regolith per hour
Processing must be able to process all the regolith collected by the rover
Power systems must provide habitat with continuous power to operate (28kW or more)
Power system must store enough energy for processing system (805402.79 Watts)
Justification
This is the capability of our processing model, and running the processing plant always will be optimal for the architecture
This will drive processing scale
Habitat needs 28kW to run, otherwise people die
The processing system runs in waves, and will require power storage so that it can begin to run one cycle
Models
Level 1
Level 2
Architecture
39
Notes: Note on rover collection
- requirement of fuel is diff from requirement of regolith

## Slide 40: Level 2 Requirements
Requirements
Power system must be able to store enough power to operate spin launch (3x10^9 Joules)
Power system must be able to store 3-4 days-worth of reserve power for contingency purposes
Spin launch must be able to send 1000* kg of fuel in a single launch
Full return on investment before architecture components must be replaced
Justification
Power is required for spin launch to operate
Provide a safety buffer for the crew in the event of an emergency
Spin launch structure and dynamics must be capable of sending significant amounts of fuel
If we need to replace components before we make a profit, profit isn't feasible
Models
Level 1
Level 2
Architecture
40
Notes: From Holzinger:
- our Level 2 Reqs are similar to other team's level 1 ( we need less detail)
- overall performance reqs
- Showing verification: thing we designed meets particular performance value (quantifiable) necessary for whole system to work
- show this with test inspection or analysis

## Slide 41: Verification and Validation
1
Analysis of System
2
Hardware Demonstration
CPE & Risks
Verification & Validation
Planning
Purpose
Solution
Requirements
41

## Slide 42: Analysis of System
Detailed Analysis
- Optimize architecture
- Refine detail
- Develop CONOPS to outline architecture operations
- Develop hardware demonstration for high-risk component
Power Analysis
Analysis of System
Hardware Demonstration
42
Notes: Collin
Now with a chosen architecture, we can begin to analyze it in detail

## Slide 43: Power Analysis
PROS
- Constant Power Output
- High Efficiency
- Long Life
(no chemical battery degradation)
(no temperature variability)
- High Energy and Power Density
CONS
- More Expensive
- Requires More Space
- Heavier
Power Analysis
Analysis of System
Hardware Demonstration
Flywheel for Energy Storage
43
Notes: Collin

## Slide 44: Hardware Demonstration
Fly Wheel Components:
- Rotor
- Axle
- Motor
- Generator
- Magnetic Bearings
- AC to DC converter
Power Analysis
Analysis of System
Hardware Demonstration
44
Notes: Holzinger feedback
- solar one doesn't help with reduction of risk
- spin launch too dangerous and hard (and how many times could we test it? Is it easy? )
- flywheel sounds the best (detailed dynamical models talking about what important parameters are – how good are bearings (to make sure doesn't lose energy, magnetic?)

## Slide 45: Project Planning
Cost Plan
3
Work Plan
4
Lessons Learned
1
Test Plan
2
CPE & Risks
Verification & Validation
Planning
Purpose
Solution
Requirements
45

## Slide 46: Test Plan
Test 1: Motor Spins Up Rotor
  - Can it maintain angular velocity needed to hold enough power during the moon's night cycle?
Test 2: Recover Energy with Generator
  - How much energy can we recover?
Test 3: Optimize Design to Maximize Efficiency
  - Can it store energy longer than a conventional battery at sub-freezing temperatures?
Lessons Learned
Plans
46

## Slide 47: Cost Plan
- 24V Solar Panel: $125
- 24V DC motor: $250
- High power magnets: $60
- Brake rotor: $50
Lessons Learned
Plans
- 24V to 5V step-down voltage converter: $30
- Mounting Infrastructure: ~$400
- Total Price: ~ $1000
47

## Slide 48: Work Plan
Hardware demo schedule:
- Buy...
(1) Solar panel to power motor to spin axle
(2) Disk break or mill a heavy aluminum disk
- Attach...
(1) Disk to milled or bought axle and levitate with magnets
(2) Magnets and coiled wire housing to axle to generate electricity
Lessons Learned
Plans
48

## Slide 49
Overall Work Plan
Hardware
Software
AIAA
Projects
Deadlines
Key:
Lessons Learned
Plans
49

## Slide 50
Overall Work Plan
Lessons Learned
Plans
50

## Slide 51
Overall Work Plan
Lessons Learned
Plans
51

## Slide 52: Lessons Learned
- Poor Initial Integration of Various Subsystem Pareto's
  Massive assumptions
  Different coding structure/organization across models
- Team Communication
  Coordination and Planning
Lessons Learned
Plans
52

## Slide 53: Thank you. Questions?
53

## Slide 54: Backup Slides
54

## Slide 55: Hardware Demo Feedback from Wingate
  Fly Wheel:
  How easy is it to make or buy?
  How much time would that take?
  If it takes too long or too much work, then might be out of scope
  Talk to Bobby or Rhode to discuss feasibility of testing within the time given next semester
  Spin Launch:
  Gravity is different on earth
  What variable are we analyzing (velocity?)
  Are we launching a liquid or a solid?
    If a liquid, it will be too difficult to imitate the dynamics
    If launching a solid this this might be doable
  If this is doable on earth and the dynamics will be the same – good relations between earth and space – we could probably do this

## Slide 56
56
Notes: Collin

## Slide 57: Power: Orbit Model
Assumptions:
  Circular restricted 3 body problem
  Lunar Synodic Period = 29.53 days
  Length Unit (LU) = 389703 km, Time Unit (TU) = 382981 s, Moon Radius = 1737.1 km
Inputs:
  Initial state vector
  Orbital period
Output:
  Array of orbit state vector over time
57

## Slide 58: Power: Orbit Model
Used Cislunar Toolkit and JPL three body orbit resource:
  Found orbits with synodic based periods
  Used single shooter to find exact initial state
Halo orbit, L2 centered, Northern
Period = 7.38 days
  quarter of moons synodic orbit
Butterfly orbit
Period=14.7 days
  Half of moons synodic orbit
58

## Slide 59: Power: Orbit Model
Distant Prograde orbit, P2 centered
P = 1.845 days
  1/8 of moons synodic orbit
Lyapunov Orbit, L2 centered
Period = 29.53 days-synodic orbit
59

## Slide 60: Power: Orbital Storage
Battery:
  Scaled based on EaglePicher Technologies LP341000 due to high discharge rate
  Very high-power density, lithium-ion cell
  30% discharge to conserve battery and prevent degradation
Supercapacitor:
  Scaled based on in-orbit demonstration of super capacitors in Acta Astronautica [1]
  98% discharge, cyclable for much longer than batteries
  No risk of explosion
Inputs:
  Energy Required
Outputs:
  Cost
  Mass
  Discharge Time
[1] Gonzalez-Llorente, Jesus, et al. “In-Orbit Feasibility Demonstration of Supercapacitors for Space Applications.” Acta Astronautica, vol. 174, 2020, pp. 294–305., https://doi.org/10.1016/j.actaastro.2020.05.007.
60

## Slide 61: Power: Beaming Model
Assumptions:
  Microwave Power Beaming
  Circular transmitter and receiving apertures
  Largely scalable
  No atmospheric loss
61

## Slide 62: Power: Solar Model
Assumptions:
  Dimensions and masses of solar panels are similar to the ISS’ solar panels
  Final solar panel efficiency will be closer to maximum laboratory efficiencies (40%)
  Time in eclipse negligible
Inputs: Power needed to sustain satellite alone
Outputs: Req'd solar array area --> use this for reasonable estimates of how much more power can be used for energy transmission
62

## Slide 63: Ground: Thermal Model
Assumptions:
- All surface area is covered by analyzed thermal hardware
- Utilizing same thermal hardware values as the Polar Ice Explorer (PIE)
- Thermal Balance: Qrad - Q_IR - Qalbedo - Qsolar - Pdisp
63

## Slide 64: Ground: Thermal Model
Inputs:
- Thermal Hardware Properties
- Costs
- Power
Outputs
- Efficiency
- Thermal Balance
64

## Slide 65: Ground: Thermal Model
0: SSM
1: White Paint
3: AgTeflon
4: Heat Switch
5: Louvre
65
Notes: 1 : SSM Efficiency: 2.138417574608068, Thermal Balance: -49.92390737899452, Max SA: 4.200000000003538
2 : White Paint Efficiency: 2.302860265033709, Thermal Balance: -49.61128773090717, Max SA: 3.7000000000035396
3 : AgTeflon Efficiency: 2.48377648651714, Thermal Balance: -49.972067751231485, Max SA: 10.55000000000356
4 : Heat Switch Efficiency: 3.070699432660468, Thermal Balance: -48.82412097930145, Max SA: 3.4000000000035406
5 : Louvre Efficiency: 7.607039503496532, Thermal Balance: 49.922932736462684, Max SA: 5.850000000003532
6 : Lourvre + Heat Switch Efficiency: 7.768097591729311, Thermal Balance: 47.641170445705654, Max SA: 0.25000000000354433
7 : Deployable Radiator (Black Paint) Efficiency: 8.507351865304582, Thermal Balance: 49.8994421823287, Max SA: 5.800000000003532
8 : Deployable Radiator (Solar Cell) Efficiency: 8.755686999344068, Thermal Balance: 49.249396727272384, Max SA: 0.3500000000035443
9 : Deployable Radiator (MLI) Efficiency: 8.768649783703593, Thermal Balance: 49.981303767110475, Max SA: 5.250000000003534
10 : Deployable Radiator (White Paint) Efficiency: 8.794535129870068, Thermal Balance: -49.90741589626119, Max SA: 12.300000000003585
11 : Deployable Radiator (White Paint + Heat Switch) Efficiency: 8.843352471006511, Thermal Balance: 49.964136347394025, Max SA: 6.150000000003531
12 : Deployable Radiator (MLI) Efficiency: 8.91061467541584, Thermal Balance: -49.52277383763646, Max SA: 5.550000000003533
13 : Deployable Radiator (MLI) Efficiency: 8.914809417225479, Thermal Balance: 49.44575677272746, Max SA: 1.350000000003545
14 : Deployable Radiator (MLI + Heat Switch) Efficiency: 8.92216720489179, Thermal Balance: -49.715824587067594, Max SA: 3.7500000000035394

## Slide 66: Ground: Thermal Model
Equations:
-
-
-
-
Variables:
66

## Slide 67: Ground: Transportation
Assumptions:
  (1) Costs does not account for building/developing vehicles or infrastructure
  (2) To account for Moon's gravity assume we can multiply the amount of mass spin lauch can lauch into orbit on Earth by this ratio to get moon equilvalent g/gm
  Deliverables:
  (1) Extra cost for The Ice Box per sale [$]
  (2) Extra ONE TIME cost for The Ice Box [$]
  (3) Extra cost for customer per sale [$]
  (4) Extra ONE TIME cost for customer [$]
  (5) Amount of product that can be transported per sale [kg]
  (6) If method of getting product to orbit is reusbale how much [kg]'s of fuel
  # or [J]'s of energy needed per sale
67

## Slide 68: Ground: Transportation
Calculations
  Price to bring 1 kg to moon's surface:
  - Using Saturn V / SLS
  - Using Falcon Heavy
  - Using Starship
  Kg per hour and ROI of system:
  - Using Apollo 11/Blue Origin Lunar lander
  - Using Straship Lunar lander
  - Using spin launch system
68