## Slide 1: Final Oral Review

## Slide 2: Project Purpose
Notes: Katie

## Slide 3: TOMCAT Mission Raytheon Mission
Test Commands
Test Telemetry
Low-Earth Orbit
30 km
Test Commands
Test Telemetry
TOMCAT Ground System
Raytheon Test Ground System
Notes: Katie

## Slide 4
30 km
TOMCAT Ground Station
TOMCAT Flight System
⬆ Take Data Commands
⬇ Science / Health Data
GOAL: Constant 2-way
communication
Notes: Katie

## Slide 5: Levels of Success
Level 1 (L1)
Wired benchtop communication
Level 2 (L2)
Wireless communication (short range)
Level 3 (L3)
Wireless communication (long range)
Balloon survivability
Notes: Katie

## Slide 6: Top Level Design
Notes: Katie

## Slide 7: Post-TRR Changes
Thermal Design:
Finalized plans to address overheating
In the TOMCAT Satellite
Primary concern
Copper strip
acts as heat pipe
Secondary concerns
Notes: Srikanth

## Slide 8: Satellite Model: Physical Specifications
33.1 mm
111.1 mm
114.2 mm
TOMCAT Slice
ThinSat Kit Slice
Full Satellite
Mass: estimated 650g
Notes: Srikanth

## Slide 9: Satellite Model: Electrical Specifications
Payload Board
Comm Board
Specification | Result | Margin
Link Margin: | 31.30 dB-Hz (downlink) | 3.13
 | 15.53 dB-Hz (uplink) | 1.55
Data Rate: | 72,000 bps (downlink) | N/A
 | 128 bps (uplink) | N/A
Battery Capacity: | 4046 mAh | 1.12
Absolute Max Current: | 3 A | 1.8
Battery
Notes: Srikanth

## Slide 10: FBD and Data Flow
Microcontroller
Signal Processing Software
Flight Software
IMU
Battery
COMM
Hardware
SDR
COMM
Hardware
SDR
Laptop
Signal Processing Software
Ground Software
TOMCAT Ground Station
TOMCAT Flight System
Custom TOMCAT
PCB
Notes: Srikanth

## Slide 11: FOR Critical Elements
Microcontroller
Signal Processing Software
Flight Software
IMU
Battery
COMM
Hardware
SDR
COMM
Hardware
SDR
Laptop
Signal Processing Software
Ground Software
TOMCAT Ground Station
TOMCAT Flight System
Custom TOMCAT
PCB
Thermal Materials
Notes: Srikanth

## Slide 12: Communications Testing
Notes: Srikanth

## Slide 13: Communications Testing
Link Budget Model
Short Range Test
Verify
Wireless Transmission Performance
Model Components
Bit Error Rate
Data Rate
Long Range Test
Verify
Wireless Transmission with Increased Noise
Model Components
Bit Error Rate
Data Rate
Power Test
Verify
Expected Power Outputs
Model Components
Total Power Output
Component Power
Wired Tests
Verify
COMM Software
Hardware Functionality
Model Components
Modulation Technique
Component Gain
Component Loss
Function Requirement 2: The payload shall communicate with the ground system during the balloon flight
Notes: Lauren

## Slide 14: Testing Overview - COMMS Wired
Component Testing
Low Pass Filter
Low Noise Amplifier
Power Amplifier
Custom COMM PCB
Functional Requirement 2:
The payload shall communicate with the ground system during the balloon flight
Primary Objectives
Characterize the performance of critical communication system components in terms of expected attenuation, losses, and gains
Update Link Budget model as necessary
Notes: Lauren

## Slide 15: Testing Overview - COMMS Power
Component Testing
SDRs
Total Transmit Power
Functional Requirement 2:
The payload shall communicate with the ground system during the balloon flight
Primary Objectives
Compare the power output to what is reported in the datasheets and what is propagated through the chain
Update Link Budget model as necessary
Notes: Lauren

## Slide 16: Testing Results - COMMS Power
SDR Power Test
Power output: 0 dBm
Full Transmit Chain
Test Supplies
One SDR
  Transmitter
Spectrum Analyzer
RF Chain
Attenuators
  40 dB
Location
Dr. Palo’s Lab
Models Verified
Link Budget Model
Goals:
Validate power transmission level from SDRs and from entire transmission RF chain
Expected Results:
Model Assumptions:
SDR Power output matches what is reported in the datasheet
Power Changes through chain are as is expected from the component performance previously documented
Power output (onboard): 33 dBm
Power output (ground): 27 dBm
Notes: Lauren
Dr. Rainville suggested 17 dB margin -- to keep this, ground chain can go down to 15 dBm onboard should not change.

## Slide 17: Testing Overview - COMMS Long Range
Functional Requirement 2:
The payload shall communicate with the ground system during the balloon flight
COMM Long Range Testing
Long Range Test
(7 Kilometers)
Attenuated Test
(7 Kilometers)
Primary Objective
Characterize wireless communication performance capabilities with increased noise and range
Notes: Lauren

## Slide 18: Testing Results - COMMS Long Range
Long Range Test
(7 Kilometers)
Test Supplies
Two SDRs
RF Chain
Attenuators
  140 dB
Antennae
Location
US 36 Overlook
LASP roof
Models Verified
Link Budget Model
Goals:
Validate RF design is capable of fulfilling link budget wirelessly long range
Introduce system to real world interference
Attenuated Test
(7 Kilometers)
Expected Results:
Changes to Model:
Expect transmission over Boulder to be subject to a higher noise level than transmitting into near space
The model will not be updated based on this test
Data Rate (Uplink): 256 bps
Data Rate (Downlink): 144 kbps
Bit Error Rate (Uplink): 10^(-6) per bit
Bit Error Rate (Downlink): 10^(-5) per bit
Notes: Lauren

## Slide 19: Link Budget Model vs. Results
Component performance matches datasheet (gain, loss, output power)
Could increase or decrease predicted Link Margin
Link Budget Model Assumptions
Impact on Results
Environmental noise matches what is as predicted with the free space loss equation
Not likely for long range tests with antennas pointed across Boulder
Likely will not receive signal for 7km attenuated test
Noise will be higher than predicted (unable to predict how much higher due to variability in this open ISM band)
Notes: Lara

## Slide 20: Thermal Testing
Notes: Lauren

## Slide 21: Thermal Testing Overview
Preliminary Thermal Modeling
Steady-State 1D Model
Characterize performance of insulation
Baseline Physical Model
Create a model to characterize temperature
Cold Tests
Verify baseline physical model
Improve physical model
Provide test platform for battery
Integrated Cold Test
Verify physical models
Meet requirement 3, 3.1
Characterize actual component performance
Functional Requirement 3:
The payload shall survive and operate in the environment during all stages of the balloon flight
Notes: Lara

## Slide 22: Preliminary Thermal Model
Takeaways:
Insulation will raise the temperature
Testing is needed for more accurate temperatures
Steady-State, 1D is a poor assumption
Notes: Lara

## Slide 23: Baseline Physical Model
TOMCAT Test Specimen (Control Configuration)
Power Resistors
Thermocouples
Control Test:
  No insulation, acrylic backing
Insulation Test:
  3/16 inch polystyrene
Test Conditions:
  Dry ice inside cooler
  Ambient temperature of -60°C
  No direct contact between dry ice and test specimen
Notes: Lara

## Slide 24: Baseline Physical Model
Takeaways:
No margin on battery, imperfect model may cause errors
Risk of cold temperatures affecting battery performance
*Full results in backup slides
Notes: Lara
TAKEAWAY: Presents the test results for the battery area, shows why we added thermal as a risk (no margin on low temp even with insulation).
First present the tests, then the test setup (bottom left), then the plot. Present the axes first, then the colors, then the actual results.
Battery temperature cannot go below -10 according to power budget.
Rest of results are in the backups

## Slide 25: Cold Test #2
Takeaways:
Improvement of baseline physical model
Addition of components leads to risk of overheating
*Images of test set up in backup slides
Notes: Lara
Proper insulation and fully stocked ThinSat reduces risk of cold temperatures
Cold Test #3 is emphasized in Power backup slides (more of a battery cold test than a full thermal system test)
Heat needs to be transferred away from SDR

## Slide 26: Thermal Integration Test
Integration Testing
Fully Integrated Thermal Test
Thermal day in the life test
Battery state of charge test
Component thermal monitoring
Models Verified
Preliminary Thermal Model
Physical Models
Component Datasheets
Test Supplies
Thermocouples (minimum 3)
All ThinSat Hardware
DAQ and LabView Software
Location
LASP Freezer or BioServe Freezer
Goals:
Validate physical thermal models
Verify Requirements 3 and 3.1
Ensure all components operate under thermal environment
Results:
Thermocouple temperature readings for each component
Data should be similar to physical model (Cold Tests)
Notes: Lara
Testing Overview

## Slide 27: Thermal Model vs. Results
Resistive strips dissipate heat throughout entire length.
Actual components may have smaller areas of heat concentration.
Physical Model Assumptions/Errors
Impact on Results
Convection inside cooler may not replicate actual conditions.
Error would not change for integration test, but would show up in balloon flight.
All components assumed to draw maximum power.
Components may draw less power, lowering amount of heat dissipated.
Notes: Lara

## Slide 28: Integration Testing
Notes: Lara

## Slide 29: Testing Overview - Full System
Full System Long Range Integration Testing
CU East Campus to US 36 Overlook
Primary Objective
Simulate and characterize actual flight performance with full integration of subsystems
Fully Assembled Ground Station
Fully Assembled and Independent ThinSat Module
7 km
Notes: Lauren

## Slide 30: Testing Results - Full System
Long Range Test
(7 Kilometers )
Bit Error Rate (Uplink: 256 bps Downlink: 144 kbps)
Data Rate (Uplink: 10^(-6) per bit Downlink: 10^(-5) per bit )
Batteries can support ~5 hours of operation
Commands sent from ground and executed on onboard
Telemetry collected and transmitted to ground station
Test Supplies
COMM System
  Hardware
  Software
Power System
Thermal System
Ground Software
Flight Software
Location
US 36 Overlook
LASP roof
Goals:
Validate full system integration
Verify all requirements are met
Expected Results:
Notes: Lauren

## Slide 31: Systems Review
Notes: Lauren

## Slide 32: Project Formulation
Design Iteration
September
Project Formulation
Integration and Test
October
March
April
Scope development
Requirements derivation
  5 major functional requirements
  37 additional design sub-requirements
Technical and logistical trade studies
  Custom PCB vs. Off-the-shelf
  Communications Frequency
  Balloon flight: Indiana vs. Gateway
Notes: Katie

## Slide 33: Design Iteration
Design Iteration
September
Project Formulation
Integration and Test
October
March
April
Develop and continuously update CAD model
  Help ensure candidate designs fulfil physics size requirements and limitations
Develop software architecture and flowchart
  Guide software design and interface to meet project requirements
Component testing where possible
  Verify and validate models as soon as possible
  Modify design as needed to meet requirements
Notes: Katie

## Slide 34: Integration and Test
Design Iteration
September
Project Formulation
Integration and Test
October
March
April
System testing to ensure proper assembly
  Make sure combined components still meet requirements
Characterization of the design
  Creating a “datasheet” for the customer
  Not just checking the V+V box, but quantifying how well requirements were met
  Quantifying effectiveness of the models
Notes: Katie

## Slide 35: Risk Evolution
Risks identified at CDR were similar, but not exact
  Thermal: ❄️ → 🔥
  PCB: Shifted from failure to delays (mostly caused by COVID-19 in China)
  Structure: New risk! Failure on landing would not impact ability to fulfill comm requirements, but does jeopardize survivability requirements
Shipping
CDR Risks
Current Risks
Shipping
Thermal
PCB Delays
Structure
Notes: Katie

## Slide 36: Lessons Learned
Clear requirements!
  Allow requirements to guide design
  Major example: KubOS vs. Lightweight FSW
KubOS was not specified as a requirement. Either should have been or switch to Lightweight should have been made sooner
Make sure to limit project scope
  Some scope creep from customer (handled fairly well)
  Hidden source of creep from within team
Examples include added complexity of Comm PCB, requirements for testing some systems to desired levels (structures, communications system)
Notes: Katie

## Slide 37: Management
Notes: Katie

## Slide 38: Fundamentals of Team Leadership
Project management triangle
Treat time, cost, and quality like currency. Trade off between all 3 to meet requirements
Remove roadblocks
Team leads manage their subsystems, ensure nothing gets in their way
Fail early, fail often
The sooner you can make a mistake, the more time there is to learn from it and fix it
Time
Quality
Cost
Note: Cost only tradable because of recognizing utility of the additional Raytheon funding early.
Not often available in Senior Projects
Notes: Cole

## Slide 39: Management Analysis
Major Success:
Parallel development
Fast design pivots
Technical and leadership roles for all
Major Shortcomings:
Team member isolation
Backend/prep obscured
Summary:
Aggressively on schedule, often to the detriment of team morale
Smooth sailing on the surface, but at the cost of behind-the-scenes work going largely unnoticed
Notes: Cole

## Slide 40: Budget Comparison
CDR Financials:
Total Cost: $4,725
Final Financials:
Total Cost: $5,961
Major Differences:
Thinsat Kit: $3,000 → $1,000
No more balloon launch
Payload Board: $860 → $1,611
Custom assembly charges
Communications: $530 → $2,273
Communications PCB, more spare parts
+ $1,236 costs
Notes: Cole

## Slide 41: Equivalent Project Cost
Total Hours:
4149 hrs
Material Costs:
$5961
Equivalent Labor:
$129,656
Overhead (200%):
$259,313
4149 hrs
Winter Break
COVID
$394,930
Notes: Cole

## Slide 42: Questions?
Notes: Cole

## Slide 43: Backup Slides

## Slide 44: Main Table of Contents
CONOPS
Levels of Success
Post-TRR Changes
Top Level Design
FBD and Data Flow
Comm Testing Overview
Transmit Power Testing
Range Testing
Comms Modeling vs. Testing
Thermal Testing Overview
1D Analytical Model
Physical Baseline Model
Cold Test #2
Cold Integration Test
Thermal Modeling vs. Testing
Full System Testing
Systems V
Risk Evolution
Management Review
Budget

## Slide 45: Backup Table of Contents
Comm Hardware
Comm Software
Flight Software
Ground Software
Payload Board
Power
Science
Structures
Thermal
Finance

## Slide 46: Comm Hardware

## Slide 47: Testing Results - COMM Wired
Low Pass Filter
Attenuation Testing
Loss Testing
Test Supplies
Two SDRs
  Transmitter
  Spectrum Analyzer
Low Pass Filter
Attenuators
  40 dB
Location
Electronics Lab
Expected Insertion Loss
1.38 dB
Actual Insertion Loss
1 dB
Margin is acceptable!
Since we are below the expected insertion loss
Models Verified
Link Budget Model

## Slide 48: Testing Results - COMMS Wired
915.0
915.2
914.8
Frequency [ MHz]
914.9
915.1
915.3
914.7
0
10
20
30
40
50
Output Gain [ dB]
Low Noise Amplifier
Gain Testing
Test Supplies
Two SDRs
  Transmitter
  Spectrum Analyzer
Low Noise Amplifier
Attenuators
  40 DB
Location
Electronics Lab
Expected Gain
38.5 dB
Actual Gain
31.5 +/- 0.5 dB
Margin is acceptable!
Power at SDR expected to be -93 dBm in the worst-case scenario
Expected: 38.5 dB
Actual: 31.5 dB
Changes to Model
Link Budget updated by replacing expected values with actual values (worst case scenario)
Notes: Lauren

## Slide 49: Testing Results - COMMS Wired
Power Amplifier
Gain Testing
Test Supplies
Two SDRs
  Transmitter
  Spectrum Analyzer
Power Amplifier
Attenuators
  40 DB
Location
Electronics Lab
Models Verified
Link Budget Model
Expected Gain
20 dB
Actual Gain
18 +/- 0.5 dB
Margin is acceptable!
Power at SDR expected to be -93 dBm in the worst-case scenario
915.0
915.2
914.8
Frequency [ MHz]
914.9
915.1
915.3
914.7
0
10
20
Output Gain [ dB]
Expected: 20 dB
Actual: 18 dB
Changes to Model
Link Budget updated by replacing expected values with actual values (worst case scenario)

## Slide 50: Testing Overview - COMMS Short Range
Short Range Testing
Bench Top Test (1 Meter)
Attenuated Test (1 Meter)
Field Test (30 Meters)
Functional Requirement 2:
The payload shall communicate with the ground system during the balloon flight
Primary Objective
Characterize changes in noise over various ranges that may not have been present in the wired tests.
Determine impact on system functionality.
Notes: Lauren

## Slide 51: Testing Results - COMMS Short Range
Field Test
(30 meters)
Lab Bench
(1 meter)
Data Rate (Uplink): 256 bps
Data Rate (Downlink): 144 kbps
Bit Error Rate (Uplink): 10^(-6) per bit
Bit Error Rate (Downlink: 10^(-5) per bit
Attenuated Test
(1 meter)
Test Supplies
Two SDRs
RF Chain
Attenuators
  140 dB
Two Antennae
Locations
Electronics Lab
BioTech Field
Models Verified
Link Budget Model
Goals:
Validate RF design is capable of communicating wirelessly
Introduce system to real world interference
Expected Results:
Model Assumptions:
Referenced text provided for ASEN 3300 for noise values
Noise over distance can be assumed to follow free space loss equation
Notes: Lauren

## Slide 52: Comm Software

## Slide 53: Communications Software Testing
Simulation Testing
Wired Testing
Models Verified
Signal Processing Model
Target Data Rate: 144 kbps
Result: 218 kbps
Test Supplies
Two SDRs
Attenuators
  40 dB
Functional Requirement 2:
The payload shall communicate with the ground system during the balloon flight

## Slide 54: Flight SW

## Slide 55: Communications Testing
Link Budget Model
Integration Testing
Verify
Full System Integration
Model Components
GNU Radio Software, IMU Hardware, and KubOS Software integration
Communications Test
Verify
Commandability and Health Status
Model Components
Health Beacon
CCSDS Packets
UDP Command/Response
Database Access
IMU Test
Verify
IMU Data Retrieval/Storage
Model Components
Parsing IMU data
Storing IMU data on KubOS Database
Function Requirement 4: The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight.
Notes: Manuel

## Slide 56: FSW Communications Testing
Software Module Testing
Sample UDP packet across Beaglebone
Receiving command from GNU Radio
Retrieving sample data from database and send it to GNU Radio via UDP
Health Beacon
System Integration
Integration between IMU and GNU Radio with actual data and CCSDS formatting
Commandability of KubOS database
Assessment of ThinSat’s health
Functional Requirement 4:
The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight.
Notes: Manuel

## Slide 57: FSW Communications Testing
Sample UDP
packet across Beaglebone
Testing Status
Establish a connection between GNU/KubOS
Send an example UDP Packet across
CCSDS format packet header
Health Beacon
Testing Status
Generate Health data
Downlink health regularly
Retrieving sample data from DB and send it to GNU Radio via UDP
Testing Status
Store telemetry in DB
Call data from DB
Send stored telemetry to GNU Radio upon command
Receiving command from GNU Radio
Testing Status
Create command to collect data
Properly processed command from GNU
Models Verified
FSW Command and Collection
Test Supplies
Laptop
Beaglebone
SDR
Supplies:
  MiniUSB
  FTDI cable
  Jumper wires
Notes: Manuel

## Slide 58: FSW IMU Testing
Software Integration
IMU data fully accessible to KubOS and stored in database
Software Module Testing
Parse IMU Data from XBus
Output IMU data to Socket in C/C++
Python IMU API listens to Socket
IMU data stored in database
Functional Requirement 4:
The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight.
Notes: Manuel

## Slide 59: FSW IMU Testing
Parse IMU Data from XBus
Testing Status
Find I2C address and bus number of IMU
Build Xsens gcc project on Beaglebone
Output IMU data to Socket in C/C++
Testing Status
Create Socket in C/C++
Python IMU API listens to Socket
Testing Status
Read from Socket in Python
Data in KubOS format
Storing data in DB
Testing Status
Accessing IMU data using API
Storing/Retrieving to/from DB
Models Verified
IMU Data Processing
Test Supplies
Laptop
Beaglebone
IMU
Supplies:
  MiniUSB
  FTDI cable
  Jumper wires
Notes: Manuel

## Slide 60: Sample UDP Packet across Beaglebone
Objective
Establish a connection between GNU/KubOS, and send an example UDP Packet across
Key Requirements
FR 4 The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight
How it Reduces Risk
Demonstrates ability to perform crucial tasks required of our FSW system, and proves how KubOS is a useful middleman to process commands/telemetry requests
Status: Completed
Result: Full Success - A UDP socket was opened from KubOS, a ping of 6 bytes of data were written over the opened socket, then the socket was opened back up and the data was read from the socket

## Slide 61: Receiving command from GNU Radio
Objective
Send a ping command (created in the Ground Software) from GNURadio to be received, processed, and forwarded by the Comms Service in KubOS
Key Requirements
FR 4 The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight
How it Reduces Risk
Demonstrates the Flight Software’s ability to receive a command over a UDP socket from GNURadio, then forward that command to another KubOS service
Status: Incomplete
Result: For a Full Success: Read the ping command from the UDP socket, then ping the requested service and receive a pong response to ensure the command was received
Test Supplies
Laptop
Beaglebone
SDR
Supplies:
  MiniUSB
  FTDI cable
  Jumper wires
Location
Electronics Lab

## Slide 62: Retrieving sample data from DB and send it to GNU Radio via UDP
Objective
Retrieving sample data from the Telemetry Database with a query, then sending that data over an opened UDP socket to GNURadio
Key Requirements
FR 4 The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight
How it Reduces Risk
Demonstrates the Flight Software’s ability to communicate smoothly between its services as well as an external software.
Confirms that the system will be able to downlink stored IMU telemetry data during the balloon flight
Status: Incomplete
Test Supplies
Laptop
Beaglebone
SDR
Supplies:
  MiniUSB
  FTDI cable
  Jumper wires
Location
Electronics Lab
Result: For a Full Success: Query the telemetry database manually, receive a JSON response, then sent the response through the UDP socket to GNURadio and get a confirmation

## Slide 63: Health Beacon
Objective
Measure/Assess overall health of software components of KubOS in a periodic fashion.
Key Requirements
FR 4 The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight
How it Reduces Risk
Reduces uncertainty and impact of bit errors in commands received from the ground, allowing the ground team to understand if it’s a problem with Flight Software or Signal Processing/Communications System.
Status: Incomplete
Test Supplies
Laptop
Beaglebone
SDR
Supplies:
  MiniUSB
  FTDI cable
  Jumper wires
Location
Electronics Lab
Result: For a Full Success: Query the Monitor and Applications services to gain health data such as memory/RAM, Applications status, etc. then send these continually and successfully to GNURadio

## Slide 64: CCSDS Packet Formatting
Objective
Format packet header in required CCSDS protocol
Key Requirements
FR 4 The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight
How it Reduces Risk
Demonstrates ability to correctly format our ground station commands and requested telemetry in space industry protocol
Status: Completed
Result: Full Success - Completed CCSDS formatting of a dummy data packet with hexadecimal information
Test Supplies
Laptop
Location
Lucas and Katie’s Desk

## Slide 65: Parse IMU Data from XBus
Objective
Collect Euler Angles from XSens IMU at specified rate and make sure data is supported by KubOS.
Key Requirements
FR 4 The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight.
How it Reduces Risk
Demonstrates ability to correctly collect our telemetry data to be sent to our GNU Radio at later stage upon command
Status: Completed
Result: Full Success - Collected 40 seconds of continuous measurements of euler angles ( 1 measurement per gcc project execution )
Test Supplies
Laptop
Beaglebone
IMU
Supplies:
  MiniUSB
  FTDI cable
Location
Manuel’s Desk
Notes: Manuel

## Slide 66: Storing/Retrieving IMU data in KubOS DB
Objective
Storing real IMU data into KubOS Telemetry Database Service at a specific data rate ( 1 measurement per ~0.045 seconds )
Key Requirements
FR 4 The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight
How it Reduces Risk
Demonstrates ability to store all telemetry generated during flight in order to confirm scientific model, and measure the error rate of our comms system
Status: Completed
Result: Full Success - Stored 40 seconds worth of real IMU data into KubOS database. Retrieved database data for verification/validation purposes.
Test Supplies
Laptop
Beaglebone
IMU
Supplies:
  MiniUSB
  FTDI cable
Location
Manuel’s Desk
Notes: Manuel

## Slide 67: Error Handler - Bit Errors/Flips
Objective
Detect improperly formatted command and send a flag response to ground station, as the request to the database raises a system error.
Key Requirements
FR 4 The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight
How it Reduces Risk
Prevent runtime errors of waiting indefinitely for a database response and mitigating risk of full system collapse/freeze as a result of error.
Status: Incomplete
Test Supplies
Laptop
Beaglebone
Supplies:
  MiniUSB
  FTDI cable
Location
Electronics Lab
Result: For a Full Success: Handle without wider system interference improperly formatted commands through flag telemetry

## Slide 68: Error Handler - Full System
Objective
Detect full system error - no commanability of KubOS database and absence of Health beacon - and reboot system with appropriate timestamp.
Key Requirements
FR 4 The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight
How it Reduces Risk
Mitigate full system error during flight and, consequent, inability to confirm science model and communications systems.
Status: Incomplete
Test Supplies
Laptop
Beaglebone
Supplies:
  MiniUSB
  FTDI cable
Location
Electronics Lab
Result: For a Full Success: Handle full system corruption without intervention from ground station.

## Slide 69: FSW Requirement Flow
Communications Testing
Full System Integration Tests
IMU Testing
Functional Requirement 4:
The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight.

## Slide 70: Ground SW

## Slide 71: Ground SW Testing
Functional Requirement 2: The payload shall communicate with the ground system during the balloon flight
Ball COSMOS Ground Software Model
Integration Testing
Verify
Full System Integration between ground and flight softwares
Model Components
- GNU Radio Software
- COSMOS Software
- KubOS Software
COSMOS Application Tests
Verify
Command sending, telemetry graphing, and telemetry logging all function smoothly
Model Components
Command & Telemetry Server
Command Sender Tool
Telemetry Grapher Tool
Telemetry Extractor Tool
CCSDS formatted packets
Notes: Lucas

## Slide 72: GSW Command Testing
Software Capability Testing
CCSDS command format verified
Command Sender application
Command & Telemetry Server Connection Testing
System Integration
Command sent over UDP to GNU Radio Software
Collect command sent directly through FSW to the IMU
Command sent through full system, including Comm hardware
Functional Requirement 2:
The payload shall communicate with the ground system during the balloon flight
Notes: Lucas

## Slide 73: GSW Command Component Testing
Command
Sender
Testing Status
Creating CCSDS formatted command
Sending a command to an example external target
Command & Telemetry Server
Testing Status
Configure the server to connect to a target over a UDP port
Establish a connection with GNU Radio Software
Models Verified
CCSDS Formatted Packets
Test Supplies
Chromebook
COSMOS
Notes: Lucas

## Slide 74: GSW Command Tests
Screenshot of COSMOS Command Sender
Command Sending Test:
Created a target system to interface with in COSMOS
Configured the system to take example data measurements
Used the Command Sender tool to send a command to the system to start a collection of telemetry
Notes: Lucas

## Slide 75: GSW Telemetry Component Testing
Software Capability Testing
CCSDS telemetry packet format verified
Telemetry Grapher, Telemetry Viewer, & Telemetry Extractor applications
Command & Telemetry Server Connection Testing
System Integration
Telemetry received over UDP with an external system
Data packet received from IMU through direct connection
Telemetry sent through full system, including Comm hardware
Functional Requirement 2:
The payload shall communicate with the ground system during the balloon flight
Notes: Lucas

## Slide 76: GSW Telemetry Component Testing
Telemetry Grapher
Testing Status
Graph example incoming live telemetry
Command & Telemetry Server
Testing Status
Connect to a target over a UDP port
Start/stop logging incoming data
Connect specifically with GNU Radio Software
Models Verified
CCSDS Formatted Packets
Test Supplies
Chromebook
COSMOS
Telemetry Viewer
Testing Status
View example incoming live telemetry
Telemetry
Extractor
Testing Status
Extract logged telemetry from .bin to .txt files

## Slide 77: GSW Telemetry Tests
Screenshot of COSMOS Telemetry Grapher
Telemetry Viewing Test:
Created a target system in COSMOS
Began taking real-time data through a UDP port into the Command & Telemetry Server
Used Telemetry Grapher tool to plot real-time telemetry
Notes: Lucas

## Slide 78: GSW Telemetry Tests
Screenshot of logged telemetry data
Telemetry Logging Test:
Created a target system to interface and began collecting live telemetry
Manually started and stopped logging in the Command & Telemetry Server
Extracted the telemetry data into a text file using the Telemetry Extractor tool
Verified the data was logged successfully
Notes: Lucas

## Slide 79: GSW Final Integration Test Plan
Stage 1: KubOS ping test
Connect with the Beaglebone as a target in COSMOS
Send a ping command from the command sender
Use the telemetry viewer to read the pong response
Stage 2: CCSDS
Repeat the steps of Stage 1, but this time packetize the command in CCSDS format to be read in by KubOS
Equipment:
Chromebook with COSMOS and GNURadio
BeagleboneBlack PCB with KubOS and GNURadio
Comms Hardware
Location:
Senior Projects Room
Electronics Lab
Stage 3: Full System
Send a collect telemetry data through the GNU Radio software, then the Comms Hardware, then KubOS, then the IMU, and back
Verify the data is correct and the error is within expected range
Test Not Completed

## Slide 80: GSW Final Integration Test Results
Stage 1: KubOS ping test
Encounter no errors while sending the command, and receive a “pong” response from KubOS
The ground system can at the least, communicate with the payload
Stage 2: CCSDS
Encounter no errors packetizing/depacketizing CCSDS formatted uplink/downlink
The payload can be communicated with in the format we want
Stage 3: Full System
Retrieve IMU data from the BBB within the error margin expected
The ground system and payload have the ability to accomplish all communications on the balloon flight
Test Not Completed
Functional Requirement 2:
The payload shall communicate with the ground system during the balloon flight
Legend
________ Ideal Test Results
________ How FR2 is satisfied
Notes: Tells us how the ideal results of this test would have satisfied the functional requirement

## Slide 81: GSW Requirement Flow
CCSDS Formatted Packets Verification
Full System Integration Tests
COSMOS Application Testing
Functional Requirement 2:
The payload shall communicate with the ground system during the balloon flight
Notes: Lucas

## Slide 82: Payload Board

## Slide 83: Payload Board Testing
PCB Bring-Up, Troubleshoot, Debug, and Integration
Integration Testing
Verify
Full System Integration with the battery
Model Components
1.3 V output
3.3 V output
5 V output
Battery V input
Software Test
Verify
Software can control I/O to send/receive data from IMU and SDR
Model Components
Same as FSW to verify that software behavior is consistent with the dev board
Boot Test
Verify
Hardware powers on and MCU functions with KubOS
Model Components
Indicator LEDs
Shell access
Function Requirement 4: The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight.
Notes: Manuel

## Slide 84: Payload Board Boot Test (P/F)
After visually inspecting the PCB and populating the board:
Apply power to the board and visually inspect indicator LEDs
Flash KubOS and test the presence of a shell terminal
Partially populated payload board
Objective: Confirm MCU hardware design and assembly was done correctly.

## Slide 85: Payload Board Software Test
Testing FSW on the board:
Conduct FSW tests on the payload board and confirm consistent behavior
UART0 serial login prompt on MCU that has been successfully flashed
Objective: Learn if connections to the IMU and SDR were made correctly

## Slide 86: Payload Board Integration Test
Integration testing with battery power:
Board fits in thinsat bus
Voltage measurements:
  1.3 V output
  3.3 V output
  5 V output
  Battery V input
Battery wired to PCB w/ example oscilloscope wired to take 5 V output measurement
Objective: Find out if PCB dimensions are correct and power electronics design is adequate.

## Slide 87: Payload Board Revisions
A payload board test failure may result in the need for a new revision
Alternate PCB vendors were considered:
  PCBWay was being affected by COVID-19
  Used Oshpark to create rev. B of comm board
  Advanced Circuits

## Slide 88: Payload Board Requirement Flow
FSW follows expected behavior
Payload Board Integrates w/ System
Payload Board Boots KubOS
Functional Requirement 4:
The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight.

## Slide 89: Power
Notes: Test Overview (15%):
Describe the testing tasks in the project: what tests were conducted, specifically what each test was designed to determine (relate to requirements), and how and where the tests were conducted. Organize the discussion to focus on what tests were most important and why (relate to project success). Do not spend much time on simple acceptance tests, but dwell on more informative characterization and model validation tests, since these convey more understanding of the important engineering aspects of project success.
Adjustments:
Focus on describing in detail the tests planned, the data that would have been gathered
Test Results: (45%):
Present test results in a concise format that explains what the results are and how they compare to what was expected from prior analysis/modeling, and how they compare to project requirements, i.e. the test data should show how well your design requirements have been satisfied and validation of predictions from model(s). Include estimates of uncertainty in the data, and its implications on requirements verification.
Describe how the tests provide a validation of your project functional requirements. Did you achieve what your customer said they wanted in the PDD? If not, provide an engineering explanation of why, i.e. back up your explanation with engineering reasoning, data, etc. In this course, achieving all functional requirements is not as important as understanding why (and being able to convey it).
Adjustments:
Focus on how the data would be used to verify and validate the requirements, along with how the data would be used to verify and refine the modeling done during the design phase.
Include information on test procedure (location, facilities, instruments, etc.)

## Slide 90: Power System Testing
Cold Testing
Cold Test #2
Cold Test #3
Integration Testing
Battery with PCB Test
ThinSat without Battery
ThinSat with Battery
Functional Requirement 3:
The payload shall be operational throughout the duration of the balloon flight
Characterization Testing
Battery Characterization Test
PCB Power Distribution Test
All battery tests that didn’t require the PCB were completed

## Slide 91: Power System Testing
Battery Discharge Model
Characterization Test
Verify
Manufacturer Specifications
Model Components
Voltage Range
Current Draw Range
Total Capacity
ThinSat with Battery
Verify
Peak Current
Actual Performance
Model Components
Current Draw Range
Total Capacity
Cold Test #3
Verify
Worst case expected capacity
Model Components
Total Capacity
Varying Temperatures
Varying Discharge Current
Cold Test #2
Verify
Expected capacity in ThinSat
Model Components
Total Capacity
Function Requirement 3: The payload shall be operational throughout the duration of the balloon flight

## Slide 92: System Level Power Budget
Category | Component | Voltage Req. [V] | Max Current Draw [A] | Max Power Draw [W] | Max Energy Required (2hrs) [Wh]
Science | XSens MTi-3 AHRS | 3.3 | 0.015 | 0.0495 | 0.099
 |  | Science Total: | 0.015 | 0.0495 | 0.099
Comms | SDR | 5 | 0.9 | 4.5 | 9
 | LNA | 5 | 0.152 | 0.76 | 1.52
 | Power Amp | 5 | 0.05 | 0.25 | 0.5
 |  | Comms Total: | 1.102 | 5.51 | 11.02
FSW/OBC | MCU | 5 | 0.5 | 2.5 | 5
 |  | FSW/OBC Total: | 0.5 | 2.5 | 5
 |  | Total: | 1.617 | 8.0595 | 16.119
 |  | 50% Margin: | 2.4255 | 12.08925 | 24.1785
Required Capacity in Room Temperature Test: 3267 mAh (with 20% margin and built in 30% add. capacity)
Required Capacity in Cold Temperature Test: 2613 mAh (without built in 30% add. capacity)

## Slide 93: Battery Discharge Model
Battery Discharge Model:
Shows expected voltages and available capacities at varying temperatures
From Cold Test #2, the expected temperature of the battery is between 0°C and 23°C
Expected Battery Discharge

## Slide 94: Component Level Power Requirements
Voltage Conversion: | [A] |  | [A]
Current Through 5V Converter: | 1.6119 | Current Through 3.3V Converter: | 0.065
With 20% Margin: | 1.93428 | With 20% Margin: | 0.078
Battery Specifications: | [V] |  | [A]
Typical Battery Voltage | 7.4 | Typical current draw: | 1.633682432
Low Battery Voltage | 5 | Max current draw: | 2.41785
Maximum Current Draw Expected: 2.42 A - leaves 0.58 A (20%) margin for any peaks in current draw

## Slide 95: Cold Testing
Models Verified
Battery Discharge Model
Test Supplies
Battery Pack
Ammeter
Voltmeter
BNC Cables
iMAX B6AC Charger
Breadboard
Dry Ice
4 Thermocouples
Cold Test #3
Capacity Test
Voltage Test
Temperature Test
Cold Test #2
State of Charge Test
Temperature Test

## Slide 96: Cold Test #2
Objective
Verify that the battery is able to discharge in the low temperatures expected in the ThinSat during the balloon flight
Key Requirements
FR 3 The payload shall be operational throughout the duration of the balloon flight
How it Reduces Risk
Demonstrates that the battery is capable of powering all components in the low temperatures expected in flight
Result: Full Success - Battery did not reach 0% state of charge at any point during the 2 hour test
Status: Completed

## Slide 97: Cold Test #3
Objective
Verify that the battery is able to discharge in the low temperatures expected in the ThinSat during the balloon flight with updated discharge rate
Key Requirements
FR 3 The payload shall be operational throughout the duration of the balloon flight
Success Criteria
Full Success: Battery doesn’t fully discharge prematurely
How it Reduces Risk
Demonstrates that the battery is capable of powering all components in the low temperatures expected in flight
Full Success: Battery discharges more than the required 2500 mAh

## Slide 98: Cold Test #3
Objective
Verify that the battery is able to discharge in the low temperatures expected in the ThinSat during the balloon flight in the worst case scenario that the internal temperature is equal to the outside temperature
Key Requirements
FR 3 The payload shall be operational throughout the duration of the balloon flight
How it Reduces Risk
Demonstrates that the battery is capable of powering all components in the low temperatures expected in flight
Result: Full Success - Battery discharged over 3000mAh, with 2500 mAh being the minimum required
Status: Completed

## Slide 99: Battery Discharge Model vs Measurement
Model vs Measurement
Depth of discharge capacities were more accurate at room temperature
  Thermal Testing shows battery temperature more likely to be around room temp in flight
Model shows constant current discharge, while Measurement is constant power discharge
  Average discharge rate is the same, but is likely why plot shapes are slightly different
Most likely curve for balloon flight

## Slide 100: Component Testing
Models Verified
Battery and PCB Specifications
Test Supplies
Battery Pack
PCB
Ammeter
Voltmeter
BNC Cables
iMAX B6AC Charger
Breadboard
Battery Characterization Testing
Voltage Test
Capacity Test
Current Draw Test
PCB Power Distribution Test
Voltage Test
Current Draw Test

## Slide 101: Battery Characterization Test Logistics
Test Procedure for Voltage, Current, & Capacity
Complete the circuit as shown in the test diagram
Record initial state of charge and voltage
Record voltage and current draw every 5 minutes throughout test
Test ends when batteries stop discharging ~ 2.5 hours
Fully charge the batteries again and measure peak voltage
Test Supplies for Voltage, Current, & Capacity
Battery Pack
Ammeter
Voltmeter
BNC Cables
iMAX B6AC Charger
Breadboard
Electrical Setup for Characterization and Cold Test #3

## Slide 102: Battery Voltage Range Test
Objective
Verify that the battery range matches the manufacturer’s specifications: 8.4V max to 6V min
Key Requirements
FR 3 The payload shall be operational throughout the duration of the balloon flight
Success Requirements:
Full Success: The voltage range is within 5% of the rate range of 5V to 8.4V
How it Reduces Risk
Demonstrates that the battery is meets manufacturer specifications for voltage and will therefore act as expected
Status: Completed
Results: Full Success - Actual Voltage Range: 4.99V to 8.41V

## Slide 103: Battery Capacity Test
Objective
Verify that the battery capacity matches the manufacturer’s specifications: 4080 mAh
Key Requirements
FR 3 The payload shall be operational throughout the duration of the balloon flight
Success Criteria
Full Success: Battery capacity is within 100 mAh of the rated max 4080 mAh
Partial Success: Battery capacity is greater than or equal to the required 3626 mAh
How it Reduces Risk
Demonstrates that the battery is meets manufacturer specifications for voltage and will therefore act as expected
Results: Full Success - Actual Capacity: 4046 mAh
Status: Completed

## Slide 104: Current Draw Test
Objective: Verify that the battery current draw does not exceed the rating from the battery manufacturer
Key Requirements:
FR 3 The payload shall be operational throughout the duration of the balloon flight
Levels of Success:
Full Success: Max Current Draw is below 2.5A
Partial Success: Max Current Draw is below 3A
Model Verified: System Level Power Budget
How it Reduces Risk: Demonstrates that the battery is meets manufacturer specifications for voltage and will therefore act as expected
Results: Full Success - Max Current Draw: 1.704 A
Status: Completed

## Slide 105: PCB Power Distribution Test
Objective
Verify that PCB converts power from a power supply to 5V and 3.3V, and verify current draw requirements are met
Key Requirements
FR 3 The payload shall be operational throughout the duration of the balloon flight
  Current Requirements: 2.0A from 5V out, .08A from 3.3V out
Associated Model
Component Level Power Budget
Success Criteria
Full Success: 2.0A and .08A available from 5V and 3.3V ports respectively
Partial Success: Greater than 1.6A and .065A available from 5V and 3.3V ports respectively
How it Reduces Risk
Demonstrates that PCB is able to supply adequate power to all subsystems
Status: Uncompleted
Results Matrix For Test:
Component | Current [A] | Success? Y/N
3.3 V Out |  | 
5 V Out |  | 

## Slide 106: Integration Testing
PCB Tests
PCB with Power Supply
PCB with Battery
Models Verified
Battery Discharge Model
Component and System Level Power Budget
Full System Tests
ThinSat with Power Supply
ThinSat with Battery
Full System Cold Test

## Slide 107: PCB with Battery Test
Objective: Verify that PCB converts power from the battery to 5V and 3.3V, and verify current draw requirements are met
Key Requirements:
FR 3 The payload shall be operational throughout the duration of the balloon flight
  Current Requirements: 2.0A from 5V out, .08A from 3.3V out
Associated Model: Component Level Power Budget
Success Criteria:
Full Success: Greater than 2.0A and .08A available from 5V and 3.3V ports respectively
Partial Success: Greater than 1.6A and .065A available from 5V and 3.3V ports respectively
How it Reduces Risk: Demonstrates that PCB is able to supply adequate power to all subsystems from battery
Results Matrix for Test:
Component | Current [A] | Success? Y/N
3.3 V Out |  | 
5 V Out |  | 
Status: Uncompleted

## Slide 108: ThinSat with Battery Test
Objective: Verify that the battery can fully power the ThinSat with all systems running
Key Requirements:
FR 3 The payload shall be operational throughout the duration of the balloon flight
Success Criteria:
Full Success: All subsystems are fully operational throughout the test
How it Reduces Risk: Demonstrates battery is capable of fully powering the ThinSat
Results:
Status: Uncompleted
Example Current Draw Plot

## Slide 109: ThinSat with Battery Test Model Improvement
Objective: Verify that the battery can fully power the ThinSat with all systems running
Model Verification:
Test verifies that the battery is capable of discharging even during peak power situations
Test verifies system performance during peak demand
Model Improvement:
Instead of constant power draw, this test allows for a model that uses time-varying power draw
This test tells us:
  How close we are to the 3A current rating for the battery
  When to expect peak power draw
Multiple tests would tell us the margin we have from peak power draw to exceeding the 3A limit
Results:
Example Current Draw Plot

## Slide 110: Full System Integration
Objective: Verify that the ThinSat is fully operational in the Cold Test environment with all subsystems operating as they will during the Balloon Launch
Key Requirements:
FR 3 The payload shall be operational throughout the duration of the balloon flight
Success Criteria:
Full Success: All subsystems are fully operational throughout the test
How it Reduces Risk: Demonstrates the ThinSat can fully satisfy Functional Requirement 3 and validates that FR 3 is sufficient to the ThinSat operation in a high-altitude environment
Results:
Status: Uncompleted
Example Discharge Draw Plot

## Slide 111: Science

## Slide 112: Science Testing Conducted
Sample IMU Testing
Configured SparkFun IMU
Uploaded sample “mission code” with Arduino
Specified data types to send
FR3.4: The IMU shall generate rate telemetry during ascent and descent.
COMPLETED
Notes: Testing Overview

## Slide 113: Science Testing Planned
FR3.4: The IMU shall generate rate telemetry during ascent and descent.
Full System Integration Testing
IMU integrated onto Payload Board
Integration between IMU and GNU Radio with actual data and CCSDS formatting
Work halted before this milestone
Physical integration is successful
Communication to MCU is correctly configured
Data is transferred in proper format
IDEAL OUTCOME
If physical connection was unsuccessful:
Re-evaluate IMU mount model, reattach to MCU
Revise the anchoring points
If communications incorrectly configured:
Review pin connections on IMU, make corrections
Refer to datasheets for I2C specifications
Review bit-by-bit breakdown
If data format improper
Revise Python code outputs
Refer to datasheet for specification of data type
Notes: Testing Overview

## Slide 114: Science Testing Planned
FR3.4: The IMU shall generate rate telemetry during ascent and descent.
Work halted before this milestone
Final Cold Test
Whole system integrated, including IMU
IMU does not drop below operating temperatures
  Data is being consistently generated
  Data is accurate
IMU does not exceed operating temperatures
  Data is being consistently generated
  Data is accurate
IDEAL OUTCOME
If temperature drops below:
Request copper wire interaction with IMU/payload board
Revise quality/quantity of thermal insulation
Revise internal layout of TOMCAT for closer proximity to battery
If temperature exceeds:
Request keeping copper wires away from payload board
Revise quality/quantity of thermal insulation
Revise internal layout of TOMCAT for further distance from battery
Notes: Testing Overview

## Slide 115: Science Testing Planned
FR3.4: The IMU shall generate rate telemetry during ascent and descent.
Level Two Full System Testing
Fully-simulated balloon flight
IMU & MCU communicating using mission code
Work halted before this milestone
Mission code accurately detects ascent/descent
Downlinked data is in correct format
  Ascent/Descent data
  Accelerometer data
  Gyroscopic data
IDEAL OUTCOME
If mission code inaccurate:
Review and study testing data which detected the flaw
  Re-construct algorithm to account for the conditions
Conduct IMU-only test using BeagleBone Black as MCU to test revised mission code in simplified, controlled environment
Test revised mission code against historical ASEN 1400 data
If downlinked data in incorrect format:
Review IMU datasheet for data-type specifications and syntax
Communicate between FSW and GSW to determine if expected data types and sizes are matching up
Notes: Testing Overview

## Slide 116: Science Model Algorithm
Mission: Determine phase of flight based on acceleration data
  Phases: Pre-Flight, Ascent, Descent, Post-Flight
Algorithm:
Pre-Flight phase
  Acquire ten seconds of data to acquire average pre-flight motion
  Ascent begins when the three-second average acceleration doubles the pre-flight average
Ascent phase
  Acquire 100 seconds of data to characterize ascent motion
  Descent begins when the three-second average acceleration exceed 4x the ascent average
Descent phase
  Descent continues until 3 second difference in acceleration is less than 0.1g
Post-Flight phase
Notes: Testing Overview

## Slide 117: Science Model Algorithm
Turn on IMU, begin data generation
Send rotation, magnetometer, pitch/roll/yaw to
SD card
MCU analyzes vertical acceleration data to determine flight phase
I2C
MCU receives data packets
MCU sends mission status data to communications hardware
for telemetry
When
|aZ| > 2⋅PFAVG
then
“ascent”
Start
“pre-flight”
When
|aZ| < 4⋅ASCAVG
then
“descent”
When
|Δax,Δay,ΔaZ| < .1g
then
“post-flight”
Notes: Testing Overview

## Slide 118: Science Model Algorithm
DESCENT
PRE-FLIGHT
ASCENT
POST-FLIGHT
Notes: Testing Overview

## Slide 119: Structures

## Slide 120: Structures Testing
Models Verified
Strength Interpolation, Datasheets
Whip Test
ThinSat remains attached to flight string
Drop Test
Components do not break free
Minimal damage to the frame
Test revealed that additional battery support and/or external frame padding would be necessary
Test not conducted due to drop test destroying frame. Would have been conducted with a new frame

## Slide 121: Drop Test
Functional Requirement 3.2
15 ft
The frame broke in a few spots:
  Through hole for bolt
  Corners near impact
  Where the balloon mount meets the frame
Pre-Impact
Post-Impact
Notes: Survivability:
Components do not break loose of their attachment mechanism
Structure does not sustain significant damage

## Slide 122: Larger Pictures

## Slide 123: Modelling
Impulse = Force x Time = ΔMomentum
?
Pre-Test:
Joint Strength: 57 Newtons
Force values need an impact time
Impact time approximation: 1 ms
Predicted needing 2.5 times more support than what was known to be good
Post-Test
Impact time measured: 2-8 ms
Number of joints required:
  Payload Board: 5 joints
  Comm HW: 4 joints
Second test with external padding can be performed
Time = No. of Frames x (sec/Frame)
Notes: Payload board has 7 joints
Comm HW has 4 joints

## Slide 124: Component Connection Calculations
Bearing in Bolt
Bearing in Member
Shear of Bolt
Edge Shearing of Member
Tensile Yielding of Member
Weakest failure mode yields at:
57 Newtons
Notes: Section: Manufacturing (60%)
Purpose: Provide CAD model / Diagram of system —> Highly detailed, include everything
Rubric: The manufacturing status was presented with strong engineering support for all important tasks and address the critical elements of the design. (52 - 60 pts)
Takeaway:
Slide Primary Author:
Presenter:

## Slide 125: Whip Test
Expectations:
  Should work as connector is known to be good from previous missions
Failure Points:
  Knot slips past retaining bar
  Mounting adapter shears off
    This happened on drop test
Solutions to Failure:
  Larger knot or smaller gap
  Increase area connecting adapter to frame
Functional Requirement 3
Notes: Mounting Hardware: Flight tube, Washers x2, Paper clips x2

## Slide 126: Thermal

## Slide 127: Preliminary Thermal Modeling
Requirement 3
The payload shall survive and operate in the environment during all stages of the balloon flight
Requirement 3.1
The payload shall be able to withstand the temperature range of flight (-56°C to 38°C).
Assumptions
Steady State, 1D Thermal Model
Standard Atmosphere
Accounts for radiation, convection, conduction (with insulation)
Does not account for sun loading or Earth’s albedo

## Slide 128: Preliminary Thermal Modeling
Constants/Known Values
Overview
SDR
FSW
MCU
Baseline
Science
Top Level
Next Steps
Backup

## Slide 129: Preliminary Thermal Modeling
Modeling with No Insulation
Overview
SDR
FSW
MCU
Baseline
Science
Top Level
Next Steps
Backup
Notes: This looks good Lara! -Katie
Thanks!

## Slide 130: Preliminary Thermal Modeling
Modeling with Insulation
*Method also applies to SDR, though the SDR was modeled in a box with different dimensions.
Overview
SDR
FSW
MCU
Baseline
Science
Top Level
Next Steps
Backup
Notes: This looks good Lara!

## Slide 131: Preliminary Thermal Modeling
No insulation: components become too cold
Insulation needed to keep temperatures within operating range

## Slide 132: Baseline Test
*Thermocouple 2 fell off during insulation test, therefore not shown.
Notes: TAKEAWAY: This slide presents the test results for the SDR
Solid line is T2
Dashed line is T3

## Slide 133: Baseline Test
Notes: TAKEAWAY: This slide presents the test results for the payload
Solid line is T0
Dashed line is T1

## Slide 134: Cold Test #2
Resistive Heater simulating
Payload Board
Thermocouple
3D Printed Mock-Board

## Slide 135: Cold Test #2
Test Battery
Resistive Heater simulating SDR
Thermocouple
3D-Printed Mock Board
Thermocouple (underneath)

## Slide 136: Finance

## Slide 137: Finance Categorized Spending Breakout

## Slide 138: Finance Fall Semester Spending

## Slide 139: Finance Spring Semester Spending (1)

## Slide 140: Finance Spring Semester Spending (2)

## Slide 141: Finance Spring Semester Spending (3)

## Slide 142: Finance Spring Semester Spending (4)

## Slide 143: Finance Spring Semester Spending (5)