## Slide 1: Test Readiness Review

## Slide 2: Project Overview

## Slide 3: Project Objectives
Primary Objective: Design a Small Communications Satellite
Specific Objectives:
  Design software-defined radio (SDR) communication system
  Design system to perform and survive a balloon flight
  Design software to use CCSDS format (Space Packet Protocol)
  Manufacture system to ThinSat frame shape
114.2mm
111.1 mm
Notes: Jake

## Slide 4
30 km
TOMCAT Ground Station
TOMCAT Flight System
⬆ Take Data Commands
⬇ Science / Health Data
GOAL: Constant 2-way
communication
Notes: Jake

## Slide 5: FBD and Data Flow
Microcontroller
Signal Processing Software
Flight Software
IMU
Battery
COMM
Hardware
SDR
COMM
Hardware
SDR
Laptop
Signal Processing Software
Ground Software
TOMCAT Ground Station
TOMCAT Flight System
Custom TOMCAT
PCB
Notes: Matt

## Slide 6: Satellite Model
33.12 mm
111.1 mm
114.2 mm
TOMCAT Slice
ThinSat Kit Slice
Full Satellite
Notes: Matt

## Slide 7: Schedule

## Slide 8: MSR Updates - FSW Schedule
UDP Communication on BeagleBone
IMU Integrated and Data Parsed
Boot/Reset/Error Handling
Full System Testing (L1 Success)
HIL Simulated Flight
KubOS
Lightweight
Today
Notes: Cole

## Slide 9: Testing Schedule
Today
Complete
Behind
Notes: Cole

## Slide 10: Test Readiness

## Slide 11: Testing Pyramid
COMPONENT TESTING
INTEGRATION TESTING
FLIGHT TESTING
Communication Hardware
Communication Software
Payload Board Electrical Design
Battery Characterization
Science Sensor Algorithm
FSW Comm Service
FSW Telemetry Collection and Storage
Mass Model Drop Test
Thermal Cold Test
OBJECTIVE:
Build understanding, reduce risk
Notes: Cole

## Slide 12: Testing Pyramid
Communication Short Range Test
Communication Long Range Test
FSW IMU Data Parsing
FSW Comm CCSDS Packetization
Integrated Cold Test
COMPONENT TESTING
INTEGRATION TESTING
FLIGHT TESTING
OBJECTIVE:
Validate models, verify design
Meets L1 and L2 success criteria as well as all requirements
Notes: Cole

## Slide 13: Testing Pyramid
COMPONENT TESTING
INTEGRATION TESTING
FLIGHT TESTING
Full System Verification Test
Hardware-in-the-Loop Simulated Flight
Balloon Flight
OBJECTIVE:
Characterize project performance
Meets L3 success criteria
Notes: Cole

## Slide 14: COMM Hardware Testing
Component Testing
Low Pass Filter
Low Noise Amplifier
Power Amplifier
Custom COMM PCB
Short Range Testing
Bench Top Test
(1 Meter)
Attenuated Test
(1 Meter)
Field Test
(30 Meters)
Long Range Testing
Long Range Test
(7 Kilometers)
Attenuated Test
(7 Kilometers)
Functional Requirement 2:
The payload shall communicate with the ground system during the balloon flight
Notes: Trevor

## Slide 15: Component Testing
Low Pass Filter
Attenuation Testing
Loss Testing
Test Supplies
Two SDRs
  Transmitter
  Spectrum Analyzer
Low Pass Filter
Attenuators
  40 dB
Location
Electronics Lab
Expected Insertion Loss
1.38 dB
Actual Insertion Loss
1 dB
Margin is acceptable!
Since we are below the expected insertion loss
Models Verified
Link Budget Model
Notes: Trevor

## Slide 16: Component Testing
915.0
915.2
914.8
Frequency [ MHz]
914.9
915.1
915.3
914.7
0
10
20
30
40
50
Output Gain [ dB]
Low Noise Amplifier
Gain Testing
Test Supplies
Two SDRs
  Transmitter
  Spectrum Analyzer
Low Noise Amplifier
Attenuators
  40 DB
Location
Electronics Lab
Expected Gain
38.5 dB
Actual Gain
31.5 dB
Margin is acceptable!
Power at SDR expected to be -93 dBm in the worst-case scenario
Models Verified
Link Budget Model
Expected: 38.5 dB
Actual: 31.5 dB
Notes: Trevor

## Slide 17: Component Testing
COMM PCB
LNA Testing
Power Amplifier Testing
Models Verified
Link Budget Model
Test Supplies
Two SDRs
  Transmitter
  Spectrum Analyzer
COMM PCB
Attenuators
  40 dB
Location
Electronics Lab
Manufacturing in Progress
Footprint mismatch in Rev A
New board ordered
Arrives this week
Notes: Trevor

## Slide 18: Short Range Testing
Field Test
(30 meters)
Signal Strength (-53 dBm)
Lab Bench
(1 meter)
Signal Strength (6.81 dBm)
Attenuated Test
(1 meter)
Signal Strength (-93 dBm)
Test Supplies
Two SDRs
  Transmitter
  Spectrum Analyzer
RF Chain
Attenuators
  140 dB
Location
Electronics Lab
BioTech Field
Models Verified
Link Budget Model
Goals:
Validate RF design is capable of communicating wirelessly
Introduce system to real world interference
On Schedule:
Margin in schedule allows extra time to complete COMM PCB
Notes: Trevor

## Slide 19: Long Range Testing
Long Range Test
(7 Kilometers)
Signal Strength (-70 dBm)
Test Supplies
Two SDRs
  Transmitter
  Spectrum Analyzer
RF Chain
Attenuators
  140 dB
Location
US 36 Overlook
LASP roof
Models Verified
Link Budget Model
Goals:
Validate RF design is capable of fulfilling link budget wirelessly long range
Introduce system to real world interference
On Schedule:
No foreseeable scheduling conflicts
Attenuated Test
(7 Kilometers)
Signal Strength (-93 dBm)
Notes: Trevor

## Slide 20: Full System Verification Test
Full Integrated System
System Functionality
Test Supplies
TOMCAT ThinSat
TOMCAT Ground Station
Attenuators
  140 dB
Location
US 36 Overlook
CU Boulder
Test Variables
Command rate (1-10 cmd/sec)
Downlink rate (1-100 kbps)
Expectations
100% command accept rate
Less than 1e-6 bit error rate
Goal Beyond System Testing
Characterize performance
Datasheet for customer
Milestones Met
L2 Success
Requirements 2 and 4
Ready for Balloon Flight
[140 dB]
~7 km actual
100 km simulated
with attenuators
Notes: Lucas

## Slide 21: Budget

## Slide 22: Financials by Acquisition Status
Spent & In-Transit ($1,845.01)
ThinSat Kit: Est. delivery Mar 6, 2020
Payload Board: Est. delivery Mar 21, 2020
COMM Hardware: Est. delivery Mar 5, 2020
Power: Est. delivery Mar 10, 2020
Future Spending (~$200)
COMM Hardware: Est. purchase Mar 6, 2020
  Ground station materials
Coverage for any other breakages
Major Change Since MSR: ThinSat Kit price has decreased ($3,000 $1,000)
Notes: Lucas

## Slide 23: Financials by Subsystem
Notes: Lucas

## Slide 24: Test Review
Review of Major Test Activities

## Slide 25: Testing Pyramid
COMPONENT TESTING
INTEGRATION TESTING
FLIGHT TESTING
Finish up Communications component testing
Perform short- and long-range testing on full Communications system
Integrate tested subsystems
Perform Full System Verification (simulated flight)
Critical Upcoming Tasks:
Required for L1 Success and beyond
Builds Up To:
L3 Success: Balloon flight test
Notes: Cole

## Slide 26: Questions?

## Slide 27: Backup

## Slide 28: Main Table of Contents
Objectives
CONOPS
FBD
CAD
FSW Updates
Schedule
Testing Methodology
Comm Component Testing
Comm Integration Testing
Full System Verification Test
Budget
Test Recap

## Slide 29: Backup Table of Contents
Levels of Success
FSW Split Details
Risk Matrix (Testing)
Comm Component
Comm Integrated
Comm Software
KubOS Overview
KubOS IMU Tests
KubOS Database
KubOS UDP Packet
KubOS CCSDS
GSW Overview
GSW Commands
GSW Telemetry
Payload Board Fab
Payload Board Testing
Power Cold Test Result
Power Characterization
Power Integration
Power Budget
Science Algorithm
Xbus Packet Format
Structures Drop Test
Structures Whip Test
CAD Animation
Thermal Testing Overview
Thermal Model Recap
Thermal Baseline Testing
Thermal Cold Test #2 Results
Thermal Cold Test #3 Plan
Thermal Integrated Cold Test
Thermal Risks
Finance

## Slide 30: Systems
Backup Slides

## Slide 31: Levels of Project Success
Level 1 | Wired SDR communication (Full-system bench test) Formatted commands & telemetry 2-ways
Level 2 | Wireless short-range SDR communication (Full-system bench test 2) Command counters
Level 3 | Long-range SDR communication (Balloon flight) Command error detection Full system survives balloon flight environment

## Slide 32: Updates Since MSR
Flight Software Split into 2 teams:
  KubOS FSW: Raytheon preferred, longer development time
    Have to build on top of established framework
    Multiple services connected by GraphQL Endpoints
    3 languages (Rust, C++, Python), team unfamiliar with Rust
  Lightweight FSW: Faster development time, can use in place of KubOS for testing
    UDP connection between softwares
    2 languages (C++, Python)
Notes: Katie?

## Slide 33: KubOS FSW Margin
UDP Communication on BeagleBone
IMU Integrated and Data Parsed
Boot/Reset/Error Handling
Integration Test
Balloon Flight
Today
KubOS
Previous FSW risk mitigated!
Lightweight FSW can be used to meet L1 & L2 Milestones
KubOS FSW (Customer preferred) can be used for L3 Milestones as development continues
Notes: Cole?

## Slide 34: Top Level Testing Risks
Risks
Board Revs: Additional Payload Board revisions required
Comm Slip: Communications testing delays resulting in slower system verification
Both risks result in delays to L1 success completion and contribute to higher launch risks
Board Revs
Comm Slip

## Slide 35: Communications Hardware
Backup Slides

## Slide 36: LNA Gain Testing Plot
915.0
915.2
914.8
Frequency [ MHz]
914.9
915.1
915.3
914.7
0
-100
-80
-60
-40
-20
Output Gain [ dBFS]

## Slide 37: Component Testing
Power Amplifier
Gain Testing
Models Verified
Link Budget Model
Test Supplies
Two SDRs
  Transmitter
  Spectrum Analyzer
Power Amplifier
SMA Cables
Attenuators
  40 dB
Location
Electronics Lab
Expected Gain
20 dB (-67 dBFS)
Actual Gain
17.3 dB (-69.7 dBFS)
Effect on Link Margin
1 dB drop in uplink margin
16.67 dB -> 15.53 dB
Margin is acceptable!

## Slide 38: Communications Final Verification
Range Testing - range verification
Objective | Measure bit error rate as a function of downlink rate Verify Signal Processing Model Verify RF Chain Power Level
Plan | Vary: File send rate (1-100 kbps) Measure: Bit error rate
Materials | 2 LimeSDR Minis 2 Laptops 2 LNAs 2 Low Pass Filters 2 Power Amplifiers 140 dB Attenuation
5 km actual
100 km simulated
Test file transmit
[140 dB]
Test file receive
* This test occurs after wired, and short
range wireless testing
Test Setup
Notes: Presenter: Trevor
Not sure if this FBD is too small or should have its own slide. - LD
Takeaway: This test verifies the link budget

## Slide 39: Communications Software
Backup Slides

## Slide 40: Communications Software Testing
Simulation Testing
Wired Testing
Models Verified
Signal Processing Model
Target Data Rate: 144 kbps
Result: 218 kbps
Test Supplies
Two SDRs
Attenuators
  40 dB
Functional Requirement 2:
The payload shall communicate with the ground system during the balloon flight

## Slide 41: KubOS Flight Software
Backup Slides

## Slide 42: FSW Testing
Software Module Testing
Sample UDP packet across Beaglebone
CCSDS Packet formatting
Receive command from GNU Radio for sample data retrieval
Retrieving sample data from DB and sending it to GNU Radio through UDP
System Integration
Connection established between KubOS and GNU Radio Software on the Beaglebone
Integration between IMU and GNU Radio with actual data and CCSDS formatting
Functional Requirement 4:
The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight.

## Slide 43: FSW Testing
Sample UDP
packet across Beaglebone
Testing Status
Establish a connection between GNU/KubOS
Send an example UDP Packet across
CCSDS format packet header
Health Data
Testing Status
Generate Health data
Downlink health regularly
Retrieving sample data from DB and sending it to GNU Radio (UDP)
Testing Status
Store telemetry in DB
Call data from DB
Send stored telemetry to GNU Radio
Receiving command from GNU Radio for sample data retrieval
Testing Status
Create command to collect data
Properly process command from GNU
Models Verified
FSW Command and Collection
Test Supplies
Laptop
Beaglebone
SDR
Supplies:
  MiniUSB
  FTDI cable
  Jumper wires

## Slide 44: FSW IMU Testing
Software Module Testing
Parse IMU Data from XBus
Output IMU data to Socket in C/C++
Python IMU API listens to Socket
IMU data stored in database
Software Integration
IMU data fully accessible to KubOS and stored in database
Functional Requirement 4:
The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight.

## Slide 45: FSW IMU Testing
Parse IMU Data from XBus
Testing Status
Find I2C address and bus number of IMU
Build Xsens gcc project on Beaglebone
Output IMU data to Socket in C/C++
Testing Status
Create Socket in C/C++
Python IMU API listens to Socket
Testing Status
Read from Socket in Python
Data in KubOS format
Storing data in DB
Testing Status
Accessing IMU data using API
Storing/Retrieving to/from DB
Models Verified
IMU Data Processing
Test Supplies
Laptop
Beaglebone
IMU
Supplies:
  MiniUSB
  FTDI cable
  Jumper wires

## Slide 46: Parse IMU Data from XBus
Objective
Collect Euler Angles from XSens IMU at specified rate
Key Requirements
FR 4 The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight.
How it Reduces Risk
Demonstrates ability to correctly collect our telemetry data to be sent to our GNU Radio at later stage
Status: Completed
Result: Full Success
Find image

## Slide 47: Storing data in DB
Objective
Storing any data generated by KubOS Services to telemetry database
Key Requirements
FR 4 The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight
How it Reduces Risk
Demonstrates ability to store all telemetry generated during flight in order to confirm scientific model, and measure the error rate of our comms system
Status: Completed
Result: Full Success
Dummy data stored into Telemetry DB

## Slide 48: Sample UDP Packet across Beaglebone
Objective
Establish a connection between GNU/KubOS, and send an example UDP Packet across
Key Requirements
FR 4 The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight
How it Reduces Risk
Demonstrates ability to perform the backbone operation of our FSW system, that drives commands and telemetry requests
Status: Completed
Result: Full Success

## Slide 49: CCSDS Packet Formatting
Objective
Format packet header in required CCSDS protocol
Key Requirements
FR 4 The OnBoard Computer, SDR, and FSW shall perform all necessary software tasks for the balloon flight
How it Reduces Risk
Demonstrates ability to correctly format our ground station commands and requested telemetry in space industry protocol
Status: Completed
Result: Full Success
Maybe another pic that our project produced

## Slide 50: Ground Software
Backup Slides

## Slide 51: GSW Command Testing
Software Capability Testing
CCSDS command format verified
Command Sender application
Command & Telemetry Server Connection Testing
System Integration
Command sent over UDP to GNU Radio Software
Collect command sent directly through FSW to the IMU
Command sent through full system, including Comm hardware
Functional Requirement 2:
The payload shall communicate with the ground system during the balloon flight

## Slide 52: GSW Command Component Testing
Command
Sender
Testing Status
Creating CCSDS formatted command
Sending a command to an example external target
Command & Telemetry Server
Testing Status
Configure the server to connect to a target over a UDP port
Establish a connection with GNU Radio Software
Models Verified
CCSDS Formatted Packets
Test Supplies
Chromebook
COSMOS

## Slide 53: GSW Command Tests
Screenshot of COSMOS Command Sender
Command Sending Test:
Created a target system to interface with in COSMOS
Configured the system to take example data measurements
Used the Command Sender tool to send a command to the system to start a collection of telemetry

## Slide 54: GSW Telemetry Testing
Software Capability Testing
CCSDS telemetry packet format verified
Telemetry Grapher, Telemetry Viewer, & Telemetry Extractor applications
Command & Telemetry Server Connection Testing
System Integration
Telemetry received over UDP with an external system
Data packet received from IMU through direct connection
Telemetry sent through full system, including Comm hardware
Functional Requirement 2:
The payload shall communicate with the ground system during the balloon flight

## Slide 55: GSW Telemetry Component Testing
Telemetry Grapher
Testing Status
Graph example incoming live telemetry
Command & Telemetry Server
Testing Status
Connect to a target over a UDP port
Start/stop logging incoming data
Connect specifically with GNU Radio Software
Models Verified
CCSDS Formatted Packets
Test Supplies
Chromebook
COSMOS
Telemetry Viewer
Testing Status
View example incoming live telemetry
Telemetry
Extractor
Testing Status
Extract logged telemetry from .bin to .txt files

## Slide 56: GSW Telemetry Tests
Screenshot of COSMOS Telemetry Grapher
Telemetry Viewing Test:
Created a target system in COSMOS
Began taking real-time data through a UDP port into the Command & Telemetry Server
Used Telemetry Grapher tool to plot real-time telemetry

## Slide 57: GSW Telemetry Tests
Screenshot of logged telemetry data
Telemetry Logging Test: ✅
Created a target system to interface and began collecting live telemetry ✅
Manually started and stopped logging in the Command & Telemetry Server ✅
Extracted the telemetry data into a text file using the Telemetry Extractor tool ✅
Verified the data was logged successfully ✅

## Slide 58: Payload Board
Backup Slides

## Slide 59: Payload Board Testing
Board Testing
Manufacturing tests
Observe indicators for a successful flash of KubOS kernel on MCU
Software defined tests for confirming successful IMU connection
Software defined tests for successful SDR connection
System Integration
Use battery supplied power
Make SDR connections
Place into thinsat bus
Functional Requirement 4:
The payload shall perform all necessary software and hardware tasks for system operation

## Slide 60: Manufacturing Tests
Manufacturing Tests:
Altium files compiled w/o errors
Passed Altium design rules checks
Gerber files passed inspection
Assembly files passed inspection
Board passed visual inspection
Board passed electrical inspection
Screenshot of PCBWay Tests

## Slide 61: Software-Defined Testing
Software-Defined Testing:
Linux kernel flashed onto MCU indicated by debug outputs
Software defined tests moved from dev board to custom board
IMU software tests passed on custom board
SDR software tests passed on custom board
Screenshot of UART0 Serial login indicating successful Linux boot

## Slide 62: Power
Backup Slides
Notes: Describe the scope of the testing tasks in the project: what tests are being planned, specifically:
  what is being tested for (your rationale for performing the test)
  the design of the test fixtures
  what test equipment and facilities are needed
  an overview of the test procedures
Describe how the test(s) will reduce risk to your project, what results do you expect, and what models will be validated.
Describe the status of the testing tasks, showing engineering details as needed to convey a solid understanding of the design (and the ability to reduce risk), requirements to be verified or validated, and what V&V is most important for project success.

## Slide 63: Power System Testing
Cold Testing
Cold Test #2
Cold Test #3
Integration Testing
Battery with PCB Test
ThinSat without Battery
ThinSat with Battery
Functional Requirement 3:
The payload shall be operational throughout the duration of the balloon flight
Characterization Testing
Battery Characterization Test
PCB Power Distribution Test

## Slide 64: Cold Testing
Models Verified
Battery Discharge Model
Test Supplies
Battery Pack
Ammeter
Voltmeter
BNC Cables
iMAX B6AC Charger
Breadboard
Dry Ice
4 Thermocouples
Cold Test #3
Capacity Test
Voltage Test
Temperature Test
Cold Test #2
State of Charge Test
Temperature Test

## Slide 65: Cold Test #2
Objective
Verify that the battery is able to discharge in the low temperatures expected in the ThinSat during the balloon flight
Key Requirements
FR 3 The payload shall be operational throughout the duration of the balloon flight
How it Reduces Risk
Demonstrates that the battery is capable of powering all components in the low temperatures expected in flight
Result: Full Success - Battery did not reach 0% state of charge at any point during the 2 hour test
Status: Completed

## Slide 66: Cold Test #3
Objective
Verify that the battery is able to discharge in the low temperatures expected in the ThinSat during the balloon flight with updated discharge rate
Key Requirements
FR 3 The payload shall be operational throughout the duration of the balloon flight
Success Criteria
Full Success: Battery doesn’t fully discharge prematurely
How it Reduces Risk
Demonstrates that the battery is capable of powering all components in the low temperatures expected in flight
Completion Date: 3/6/20
Full Success: Battery does not reach 0% state of charge at any point during the 2 hour test

## Slide 67: Component Testing
Models Verified
Battery and PCB Specifications
Test Supplies
Battery Pack
PCB
Ammeter
Voltmeter
BNC Cables
iMAX B6AC Charger
Breadboard
Battery Characterization Testing
Voltage Test
Capacity Test
Current Draw Test
PCB Power Distribution Test
Voltage Test
Current Draw Test

## Slide 68: Battery Characterization Test Logistics
Test Procedure for Voltage, Current, & Capacity
Complete the circuit as shown in the test diagram
Record initial state of charge and voltage
Record voltage and current draw every 5 minutes throughout test
Test ends when batteries stop discharging ~ 2.5 hours
Fully charge the batteries again and measure peak voltage
Test Supplies for Voltage, Current, & Capacity
Battery Pack
Ammeter
Voltmeter
BNC Cables
iMAX B6AC Charger
Breadboard
Electrical Setup for Characterization and Cold Test #3

## Slide 69: Battery Voltage Range Test
Objective
Verify that the battery range matches the manufacturer’s specifications: 8.4V max to 6V min
Key Requirements
FR 3 The payload shall be operational throughout the duration of the balloon flight
Success Requirements:
Full Success: The voltage range is within 5% of the rate range of 5V to 8.4V
How it Reduces Risk
Demonstrates that the battery is meets manufacturer specifications for voltage and will therefore act as expected
Status: Completed
Results: Full Success - Actual Voltage Range: 4.99V to 8.41V

## Slide 70: Battery Capacity Test
Objective
Verify that the battery capacity matches the manufacturer’s specifications: 4080 mAh
Key Requirements
FR 3 The payload shall be operational throughout the duration of the balloon flight
Success Criteria
Full Success: Battery capacity is within 100 mAh of the rated max 4080 mAh
Partial Success: Battery capacity is greater than or equal to the required 3626 mAh
How it Reduces Risk
Demonstrates that the battery is meets manufacturer specifications for voltage and will therefore act as expected
Results: Full Success - Actual Capacity: 4046 mAh
Status: Completed

## Slide 71: Current Draw Test
Objective: Verify that the battery current draw does not exceed the rating from the battery manufacturer
Key Requirements:
FR 3 The payload shall be operational throughout the duration of the balloon flight
Levels of Success:
Full Success: Max Current Draw is below 2.5A
Partial Success: Max Current Draw is below 3A
Model Verified: System Level Power Budget
How it Reduces Risk: Demonstrates that the battery is meets manufacturer specifications for voltage and will therefore act as expected
Results: Full Success - Max Current Draw: 1.704 A
Status: Completed

## Slide 72: PCB Power Distribution Test
Objective
Verify that PCB converts power from a power supply to 5V and 3.3V, and verify current draw requirements are met
Key Requirements
FR 3 The payload shall be operational throughout the duration of the balloon flight
  Current Requirements: 2.0A from 5V out, .08A from 3.3V out
Associated Model
Component Level Power Budget
Success Criteria
Full Success: 2.0A and .08A available from 5V and 3.3V ports respectively
Partial Success: Greater than 1.6A and .065A available from 5V and 3.3V ports respectively
How it Reduces Risk
Demonstrates that PCB is able to supply adequate power to all subsystems
Completion Date: 3/13
Results Matrix For Test:
Component | Current [A] | Success? Y/N
3.3 V Out |  | 
5 V Out |  | 

## Slide 73: Integration Testing
PCB Tests
PCB with Power Supply
PCB with Battery
Models Verified
Battery Discharge Model
Component and System Level Power Budget
Full System Tests
ThinSat with Power Supply
ThinSat with Battery
Full System Cold Test

## Slide 74: PCB with Battery Test
Objective: Verify that PCB converts power from the battery to 5V and 3.3V, and verify current draw requirements are met
Key Requirements:
FR 3 The payload shall be operational throughout the duration of the balloon flight
  Current Requirements: 2.0A from 5V out, .08A from 3.3V out
Associated Model: Component Level Power Budget
Success Criteria:
Full Success: Greater than 2.0A and .08A available from 5V and 3.3V ports respectively
Partial Success: Greater than 1.6A and .065A available from 5V and 3.3V ports respectively
How it Reduces Risk: Demonstrates that PCB is able to supply adequate power to all subsystems from battery
Completion Date: 4/3
Results Matrix for Test:
Component | Current [A] | Success? Y/N
3.3 V Out |  | 
5 V Out |  | 

## Slide 75: ThinSat with Battery Test
Objective: Verify that the battery can fully power the ThinSat with all systems running
Key Requirements:
FR 3 The payload shall be operational throughout the duration of the balloon flight
Success Criteria:
Full Success: All subsystems are fully operational throughout the test
How it Reduces Risk: Demonstrates battery is capable of fully powering the ThinSat
Completion Date: 4/3
Results:
Battery Discharge Plot

## Slide 76: Full System Integration
Objective: Verify that the ThinSat is fully operational in the Cold Test environment with all subsystems operating as they will during the Balloon Launch
Key Requirements:
FR 3 The payload shall be operational throughout the duration of the balloon flight
Success Criteria:
Full Success: All subsystems are fully operational throughout the test
How it Reduces Risk: Demonstrates the ThinSat can fully satisfy Functional Requirement 3
Completion Date: 4/10
Results:
Battery Discharge Plot

## Slide 77: Battery Discharge Model
Battery Discharge Model:
Shows expected voltages and available capacities at varying temperatures
From Cold Test #2, the expected temperature of the battery is between 0°C and 23°C
Expected Battery Discharge

## Slide 78: System Level Power Budget
Category | Component | Voltage Req. [V] | Max Current Draw [A] | Max Power Draw [W] | Max Energy Required (2hrs) [Wh]
Science | XSens MTi-3 AHRS | 3.3 | 0.015 | 0.0495 | 0.099
 |  | Science Total: | 0.015 | 0.0495 | 0.099
Comms | SDR | 5 | 0.9 | 4.5 | 9
 | LNA | 5 | 0.152 | 0.76 | 1.52
 | Power Amp | 5 | 0.05 | 0.25 | 0.5
 |  | Comms Total: | 1.102 | 5.51 | 11.02
FSW/OBC | MCU | 5 | 0.5 | 2.5 | 5
 |  | FSW/OBC Total: | 0.5 | 2.5 | 5
 |  | Total: | 1.617 | 8.0595 | 16.119
 |  | 50% Margin: | 2.4255 | 12.08925 | 24.1785

## Slide 79: Component Level Power Requirements
Voltage Conversion: | [A] |  | [A]
Current Through 5V Converter: | 1.6119 | Current Through 3.3V Converter: | 0.065
With 20% Margin: | 1.93428 | With 20% Margin: | 0.078
Battery Specifications: | [V] |  | [A]
Typical Battery Voltage | 7.4 | Typical current draw: | 1.633682432
Low Battery Voltage | 5 | Max current draw: | 2.41785

## Slide 80: Science
Backup Slides

## Slide 81: Scientific Sensor Specifications
Sensor Model: Xsens MTi-3 Attitude & Heading Reference System (AHRS)
  Data Outputs:
    Temperature
    Timestamps
    Orientation (quaternion, rotation matrix, Euler angles)
    Acceleration (delta v, acceleration, free acceleration, acceleration HR)
    Angular Velocity (rate of turn)
Sensor Packet Type: Xbus (Xsens’ proprietary packetization method)
  Depacketized and transferred into CCSDS Space Packet Format by FSW
Sensor Communication Protocol: I2C

## Slide 82: Scientific Sensor Algorithm
Mission: Determine phase of flight based on acceleration data
  Phases: Pre-Flight, Ascent, Descent, Post-Flight
Algorithm:
Pre-Flight phase
  Acquire ten seconds of data to acquire average pre-flight motion
  Ascent begins when the three-second average acceleration doubles the pre-flight average
Ascent phase
  Acquire 100 seconds of data to average ascent motion
  Descent begins when the three-second average acceleration exceed 4x the ascent average
Descent phase
  Descent continues until 3 second difference in acceleration is less than 0.1g
Post-Flight phase

## Slide 83: Scientific Sensor Algorithm
83
Turn on IMU, begin data generation
Send rotation, magnetometer, pitch/roll/yaw to
SD card
MCU analyzes vertical acceleration data to determine flight phase
I2C
MCU receives data packets
MCU sends mission status data to communications hardware
for telemetry
When
|aZ| > 2⋅PFAVG
then
“ascent”
Start
“pre-flight”
When
|aZ| < 4⋅ASCAVG
then
“descent”
When
|Δax,Δay,ΔaZ| < .1g
then
“post-flight”

## Slide 84: Scientific Sensor Algorithm
84
ASCENT
DESCENT
POST-FLIGHT
PRE-FLIGHT

## Slide 85: Scientific Sensor Packetization
This is the composition of a standard Xbus message

## Slide 86: Scientific Sensor Testing
Sample IMU Testing
Configured SparkFun IMU
Uploaded sample “mission code” with Arduino
Specified data types to send
Full System Integration Testing
IMU integrated onto Payload Board
Integration between IMU and GNU Radio with actual data and CCSDS formatting
Functional Requirement 3.4
The IMU shall generate rate telemetry during ascent and descent.

## Slide 87: Structures
Backup Slides

## Slide 88: Drop Test
Functional Requirement 3.2
Purpose:
  Ensure component survivability
Equipment:
  Ladder
  Ruler
  High speed camera
Facilities:
  ITLL
15 ft
Notes: Survivability:
Components do not break loose of their attachment mechanism
Structure does not sustain significant damage

## Slide 89: Whip Test
Purpose:
  Comply with Gateway launch requirements
Equipment:
  String
  Mounting hardware
Facilities:
  Open space
Functional Requirement 3
Notes: Mounting Hardware: Flight tube, Washers x2, Paper clips x2

## Slide 90: Structures Testing
Models Verified
Strength Interpolation, Datasheets
Whip Test
ThinSat remains attached to flight string
Drop Test
Components do not break free
Minimal damage to the frame

## Slide 91: Assembly Animation

## Slide 92: Thermal
Backup Slides
Notes: Start with PDR model, progress through the two thermal tests, talk about future work and tests (integrated cold test?)

## Slide 93: Thermal Testing
Preliminary Thermal Modeling
Steady-State 1D Model
Baseline Test
Cold Testing
Cold Test #2
Cold Test #3
Integration Testing
Fully Integrated Thermal Test
Functional Requirement 3:
The payload shall survive and operate in the environment during all stages of the balloon flight

## Slide 94: Thermal Testing
Models Verified
Baseline Thermal Test, Datasheets
Cold Test #2
Maintain nominal operating temperatures
Characterize hot and cold areas
Baseline Cold Test
Maintain nominal operating temperatures
Obtain baseline data for future tests

## Slide 95: Thermal Testing
Cold Test #3
Confirm Cold Test #2 Results
Battery state of charge test
Fully System Thermal Test
Thermal day in the life test
Battery state of charge test
Component thermal monitoring
Models Verified
Baseline Thermal Test, Datasheets

## Slide 96: Thermal Modeling
Steady State, 1D Thermal Model
Accounts for radiation, convection, conduction (with insulation)
Does not account for sun loading or Earth’s albedo
Insulation required for above-nominal operating temperatures of both the payload and the SDR

## Slide 97: Thermal Modeling

## Slide 98: Baseline Test
Control Test:
  No insulation, acrylic backing
Insulation Test:
  3/16 inch polystyrene
Test Conditions:
  Dry ice inside cooler
  Ambient temperature of -60°C
  No direct contact between dry ice and test specimen.
Power Resistors
Thermocouples
Models Verified
Effect of Insulation on Temperature (Preliminary Model)
Test Status
Complete
Relevant Design Requirement:
The payload shall be able to withstand the ambient temperature range of flight (-56°C, 38°C)

## Slide 99: Baseline Test
Notes: Presenter: Lara
TAKEAWAY: Presents the test results for the battery area, shows why we added thermal as a risk (no margin on low temp even with insulation).
First present the tests, then the test setup (bottom left), then the plot. Present the axes first, then the colors, then the actual results.
Battery temperature cannot go below -10 according to power budget.
Adding insulation raises the temperature almost 15 C. Adding more layers should be able to keep the battery warm enough
Insulating the battery directly could also help keep it warm.
Further testing will explore more layers of insulation and/or different types of insulation.
Other option is to directly insulate battery
Rest of results are in the backups
Heritage data is in the backup slides
No TVAC - talked to Dr. Li, Jackson, and thermal engineers at LASP. Also, heritage flights have had no TVAC testing.
Talk about errors in test.

## Slide 100: Baseline Test
*Thermocouple 2 fell off during insulation test, therefore not shown.
Notes: TAKEAWAY: This slide presents the test results for the SDR
Solid line is T2
Dashed line is T3

## Slide 101: Baseline Test
Notes: TAKEAWAY: This slide presents the test results for the payload
Solid line is T0
Dashed line is T1

## Slide 102: Cold Test #2
Relevant Design Requirement:
The payload shall be able to withstand the ambient temperature range of flight (-56°C, 38°C)
Models Verified
Baseline Test Results
Test Status
Complete
Notes: Proper insulation and fully stocked ThinSat reduces risk of cold temperatures
Heat needs to be transferred away from SDR

## Slide 103: Cold Test #3
Relevant Design Requirement:
The payload shall be able to withstand the ambient temperature range of flight (-56°C, 38°C)
Models Verified
Baseline Test Results
Test Status
Incomplete
Objective: Characterize battery performance at low temperatures
Key Requirements:
FR 3 The payload shall be operational throughout the duration of the balloon flight
Success Criteria:
Full Success: Battery doesn’t fully discharge prematurely
How it Reduces Risk: Demonstrates integrated ThinSat can operate in extreme environment of near-space
Expected Completion Date: March 6th, 2020
Notes: Proper insulation and fully stocked ThinSat reduces risk of cold temperatures
Heat needs to be transferred away from SDR

## Slide 104: Integrated Cold Test
Relevant Design Requirement:
The payload shall be able to withstand the ambient temperature range of flight (-56°C, 38°C)
Models Verified
Baseline Test Results, Cold Test #2 Results
Test Status
Incomplete
Expected Completion Date: April 10th, 2020
Objective: Verify Requirements 3 and 3.1, ensure all components operate under thermal environment
Key Requirements:
FR 3 The payload shall be operational throughout the duration of the balloon flight
Success Criteria:
Full Success: All subsystems are fully operational throughout the test
How it Reduces Risk: Demonstrates integrated ThinSat can operate in extreme environment of near-space
Notes: Proper insulation and fully stocked ThinSat reduces risk of cold temperatures
Heat needs to be transferred away from SDR

## Slide 105: Thermal Risk Status
Cold: Cold temperatures result in off-nominal operation of components and loss of battery performance
Heat: Heat from the SDR or payload board is localized and builds up in components, leading to overtemps and component failure
Mitigations:
  Test results show cold temperature is a low risk
  Added copper heat sink will reduce heat risk
Heat
Cold

## Slide 106: Finance
Backup Slides

## Slide 107: Finance Fall Expenditures

## Slide 108: Finance Spring Expenditures

## Slide 109: Finance Spring Expenditures

## Slide 110: Finance Spring Expenditures