## Slide 1: HERMES Hazard Examination and Reconnaissance Messenger for Extended Surveillance
Testing Readiness review
March 4th, 2019
Presenters: Alexis Sotomayor , Alex Sandoval , Ashley Montalvo, Quinter Nyland
Customer: Barbara Streiffert and Jet Propulsion Laboratory (JPL)
Advisor: Dr. Kathryn Anne Wingate
Team: Alexander Sandoval, Alexis Sotomayor, Ashley Montalvo, Brandon Santori, Brindan Adhikari, Chase Pellazar, Colin Chen, Junzhe He, Katelyn Griego, Marcos Mejia, Michely Tenardi, Quinter Nyland
Notes: Intro: conops: design

## Slide 2: Project Purpose and Objectives
Notes: 2 minutes, 28 mins left

## Slide 3: Project Motivation and Statement
The mother rover created by DRIFT is large and difficult to navigate through forest like areas.
The HERMES team will design, build and test a child scout rover (CSR) that will deploy, take images/videos of the surrounding terrain, determine a viable path to a location of interest (LOI), and upon arrival to the LOI, the CSR will send the viable path to the mother rover.
CHIMERA
DRIFT
Note: Blue used for emphasis

## Slide 4: CONOPS: Arriving to Location of Interest
4
4
October 2018
Ground
Station
Requirements
Functions
Mother Rover
LOI
Up to 250 m radius (820 ft)
1
2
Deploy from Ground Station and drop a pathpoint
1
Receive Location of Interest (LOI) from GS
2
Upon arrival it will stop, and notify the GS and drop a pathpoint
5
User commands CSR to point towards LOI
3
Comm between GS and MR
Comm between GS and CSR
Comm between CSR and MR
Autonomously controlled path
Legend
Stop and request user intervention
Pathpoint
Mission Terrain
Manually controlled path
User commands CSR to travel towards the LOI in semi autonomous mode. The CSR will travel until it reaches the LOI.
4
3
5
En route to the LOI, the CSR may encounter one or more of the following:
Obstacles
Discontinuities
Slopes
Loss of communications
Child Scout Rover
4
Notes: Fix picture,

## Slide 5: CONOPS: Other Terrain
5
= Point where sensor detects
obstacle or discontinuity
= Pathpoint
= Stop and request
user intervention
= Manual Control
= Autonomous Control
If the CSR detects an obstacle, the CSR will stop
The user will take control, and manually control the CSR around the obstacle
  Every time the CSR turns, a pathpoint is recorded
After traveling around the obstacle, the user commands the CSR to point towards the LOI, and command it into semi- autonomous mode
1
2
3
Obstacle
Operator manually controls CSR around obstacle
1
2
3
Non-Traversable Obstacles
1
3
4
Up to 9 inches wide
Greater than 2.4 in deep
CSR crosses autonomously
If the CSR detects a discontinuity, the CSR will stop
The user will then send a command to the CSR to enter the discontinuity traversal mode
Then the CSR autonomously crosses the discontinuity
  A pathpoint is recorded since a mobility command was received and executed
After crossing the discontinuity, the CSR stops and requests user intervention
1
2
3
4
2
User sends command to change mode
Discontinuities
Slopes
If the CSR detects a slope, the CSR will stop
The user will control the CSR to get onto the slope and command the CSR into semi autonomous mode
The CSR will travel on the slope in semi autonomous mode
Once the CSR detects flat ground, it will stop
The user will control the CSR to return to flat ground
1
2
3
4
5
Up to a 20° slope
2
3
4
5
Operator manually controls the CSR onto or off-of slope
1
Notes: Fix picture

## Slide 6: Functional Block Diagram

## Slide 7: Functional Requirements
Requirement ID | Description
CSR.1 | The CSR shall receive commands from the GS
CSR.2 | The CSR shall send video, GPS coordinates, and sensor data to the GS through mission defined terrain
CSR.3 | The CSR shall drive to a location of interest through mission defined terrain
CSR.4 | The CSR shall travel back to the last reported pathpoint upon loss of communications with the GS
CSR.5 | The CSR shall take video in position hold
Notes: CSR.2 – specify sensor data

## Slide 8: Critical Project Elements
Critical Project Element (CPE) | Rationale
Mobility | The CSR must be able to travel forward and backwards and perform 360° turns.
Software | The CSR software must read in, process, and execute commands from the GS. The CSR must also process data on-board to react to obstacles and discontinuities.
Guidance, Navigation, and Control (GNC) | The CSR must be controlled remotely by one operator, and must read its own attitude accurately.
Environment Sensing | The CSR must accurately sense the terrain and obstacles around it to navigate around them.
Communications | The CSR must communicate with the GS to send the viable path, images and videos to the GS.

## Slide 9: Success Levels
Criteria | Level 1 | Level 2 | Level 3
Control | The CSR shall navigate by received control commands from the GS The CSR shall perform a 360 ° turn The CSR shall drive forward and reverse | The CSR shall navigate to a LOI and shall detect obstacles en route to the LOI, but manual control is needed to circumvent the obstacles. | The CSR shall autonomously return to the last known GPS location if connection to the GS and MR is lost.
Communication | The CSR shall verify connection to the MR/GS. The CSR shall send at least one GPS data packet to MR/GS upon command. The CSR shall have functional communication up to a 250 meter radius from the deployment point in an open area. The CSR shall be able receive control commands from MR/GS | The CSR shall record and send waypoint locations after encountering an obstacle | The CSR shall transmit continuous video feed. The CSR shall verify its location from the LOI within +/- 5 meters The CSR shall communicate through type D terrain up to a 250 meter radius from the deployment point
= Completed

## Slide 10: Success Levels Continued
Criteria | Level 1 | Level 2 | Level 3
Environment | The CSR shall traverse the following: Open areas Up to 20 ° incline slopes | The CSR shall traverse the following: Type A underbrush Roots up to a 2.4 inch(6 cm) diameter | The CSR shall traverse the following: Type D underbrush Up to a 9 inch wide discontinuities with depths greater than 2.4 inches (6 cm)
Range | The CSR shall drive up to a 250 meter radius from the deployment point on flat terrain | The CSR shall drive up to a 250 meter radius from the deployment point on flat terrain with obstacles present | The CSR shall be able to drive in a 250 meter radius from the deployment point at a 20 ° inclined slope
Video/ Image | The imaging system on the CSR shall capture a FOV greater than 100 ° The imaging system shall send time-stamped images to the MR/GS | The CSR shall send videos to the GS The GS shall toggle the video capture from the CSR on or off | The CSR shall send continuous video feed to the GS
= Completed
= To be Completed

## Slide 11: Design Recap: System Interface
MR Comm System
1 6.5W 900MHz Ubiquiti Radio
MR Comm System
1 6.5W 900MHz Ubiquiti Radio
MR Comm System
1 6.5W 900MHz Ubiquiti Radio
MR
CSR
MR Software System
Function: ROS Slave Machine
CSR Software System
Function: ROS Host Machine
GS Software System
Function: ROS Slave Machine
Displays a GUI for operation
GS
= Wireless Comms.
= Outlines components
Mission Log
CSR Status
Command Options
Video Feed
Notes: I’d say emphasize less on comms and expand more on software. Fix, and talk better. Animate

## Slide 12: Design Recap: CSR Hardware
Drivetrain:
  Design
    One drivetrain per side
    Composed of 6 wheels, 2 chains, chain tensioners, sprockets, 1 motor + gearbox
Chassis:
  Design
    Top housing is 0.25” laser cut acrylic
    Bottom Chassis is 0.25” 6061 Aluminum (CNC)
Linear Mass Stage:
  Why?
    The COM is shifted as necessary using the linear mass stage to cross discontinuities. The mass is shifted when the ultrasonic sensors detect ground under a certain set of wheels.
  Design
    A COTS linear mass stage is utilized which is controlled by a stepper motor controller. The mass being used is 5 kg.
CSR Physical Properties Summary:
Overall Dimensions: 28 in x 15 in x 11 in
Total Mass: 17 kg
28 in
15.5 in
20.2 in
Notes: Don't assume anyone knows what everything is for. Why is the linear mass stage there? Why are we using ROS in the first place? Why do we need to operate in different modes? We need to make sure to build our presentation in such a way that everything has a purpose when it is presented.

## Slide 13: Design Recap: CSR Hardware
Single Beam LiDAR Sensors:
  Why?
    To detect discontinuities
360 ° Lidar Sensor:
  Why?
    To detect obstacles
Ultrasonic Sensor:
  Why?
    Used for crossing discontinuities to determine what position the mass
    from the linear mass stage should be in
    Placed on the bottom on the CSR (not shown in diagram)
GPS – RTK Sensor:
  Why?
    To determine the CSR’s position up to a 0.025 m accuracy
Magnetometer/ 3 Axis Accelerometer:
  Why?
    Magnetometer used for determining the CSR’s heading
    Accelerometer used to determine if the CSR is on level ground or a slope
Notes: Don't assume anyone knows what everything is for. Why is the linear mass stage there? Why are we using ROS in the first place? Why do we need to operate in different modes? We need to make sure to build our presentation in such a way that everything has a purpose when it is presented.

## Slide 14: Design Recap: Software Architecture
CSR can run in 6 different modes:
- Initialization
- Manual
- Semi-Autonomous
- Discontinuity Cross
- Loss of Comms
- LOI Reached
Benefits of the Mode Architecture:
- Allows for a reduction in the amount of code running at any point in time
- Allows for data to only be processed from sensors when needed
Notes: She expects us to explain why ROS is being used in a previous slide somewhere so that when we see the software diagram, it is not shocking to people looking at it.

## Slide 15: Scheduling

## Slide 16: Software Schedule
Current Day. March , 4 2019
= Completed
= Future Work
= In Progress
= Margin
= Milestone
Hours: 2/10
Hours: 0/5
Hours:8/15
Remaining hours: 20 hours
Note: Does not include integration of software
Unfinished Software

## Slide 17: Integration & Test Schedule
= Completed
= Future Work
= In Progress
= Margin
= Milestone
Current Day. March , 4 2019
Unit Testing
Subsystem Integrated Tests

## Slide 18: Integration & Test Schedule
Current Day. March , 4 2019
= Completed
= Future Work
= In Progress
= Margin
= Milestone
Mechanical integration
Full System Integration and Test
Spring Break
SFR
TRR

## Slide 19: Critical Path
Full System Integration and Test
March 2019
April 2019
February 2019
Jan 2019
Software
= Critical Path
Unit Testing
Mechanical integration
Subsystem Integrated Tests
Current Day. March , 4 2019

## Slide 20: Testing Readiness

## Slide 21: Overall Testing Status
Phase 1: Components and Subsystems Testing
Phase 2: Subsystem Integration and Testing
Phase 3: Full System Integration and Testing
1/14/19 - 2/24/19
Mobility Testing
  Motor validation - Torque curve characterization
  Coefficient of Friction Testing
  Linear Mass stage moving
C&DH and Software V&V
  Individual mode testing
  Driving software tests
GNC Testing
  GPS accuracy
  Magnetometer accuracy
  Camera operations testing
Sensing Testing
  Single beam accuracy
  360 ° lidar accuracy
  Ultrasonic sensor accuracy
Communications Testing
  Communications testing
  Attenuation characterization
2/24/19 - 3/19/19
Mobility Integration & Testing
  Motor mounting to chassis
  Drive train integration
  Forward & backwards motion
C&DH and Software Integration
  Loss of communication navigation testing
  Integrated mode testing
Sensing Integration
  Integrating all sensors and microcontrollers
3/19/19 - 4/22/19
Full System Integration
  Combined Environment maneuverability and object detection integration
Full System Mobility Testing
  Environmental maneuverability testing
  Endurance Testing
  Obstacle maneuverability testing
  Rover functional testing
= Completed
= In Progress
= Future Work
Notes: Tests that are planned, tests that have been completed
Current status of testing
  Might help in the form of a flowchart?

## Slide 22: Flow down from CPEs
Mobility
Software
GNC
Environment Sensing
Communication
CPEs
  Motor validation - Torque curve characterization
  Linear Mass stage moving
  Individual mode testing
  Driving software tests
  GPS accuracy
  Magnetometer accuracy
  Camera operations testing
  Single beam accuracy
  360 ° lidar accuracy
  Ultrasonic sensor accuracy
  Communications testing
  Attenuation characterization
Phase 1: Component Testing
  Motor mounting to chassis
  Drive train integration
  Forward & backwards motion
  ASUS and Arduino Integration tests
  Heading correction tests
  Loss of communication
  navigation testing
  Integrated mode testing
  Integrating all sensors and microcontrollers
Phase 2: Subsystem Testing
  Environmental maneuverability testing
  Endurance Testing
  Obstacle maneuverability testing
  Rover functional testing
  Combined Environment maneuverability and object detection integration
Phase 3: Full System Testing
Notes: Tests that are planned, tests that have been completed
Current status of testing
  Might help in the form of a flowchart?

## Slide 23: Phase 1 Tests

## Slide 24: Communications – Scope and Status
Purpose:
  To verify and validate the communications model and determine if video, GPS coordinates, and sensor data can be transmitted/received through open areas and wooded areas of 250 m.
Requirements being validated:
  Primary Model Requirements
    COMM 1.1: The CSR Communication system shall receive command packets up to 250 m in Mission Defined Terrain with no more than a 10 dB link margin
    COMM 2.3: The CSR Communication system shall send video from up to 250 m (820 ft) to the GS or the MR
  Secondary Model Requirements
    CSR 2 & CSR 5 (General mission requirements)
    SENS 5.1 - 5.1.2 (Camera related)
    COMM 2.1, COMM 2.2, 2.4, 2.5 (Sending video, GPS, and sensor data)
Status:
  COMPLETED & PASSED
Risk Reduction:
  By testing communications we can verify that the CSR can travel up to a 250 m distance
  Improve manually operated situational awareness from camera resolution and bandwidth
Notes: These requirements not listed should go in the back up slides

## Slide 25: Communications – Test Design
Testing for:
  Video stream delay
  Distance between radios
  Bandwidth consumption
Key Variables:
  Received signal strength
  Latency of communication
  Transmission rate
Procedure:
  Deploy GS equipment at distance 0 ft (0 m) and deploy CSR equipment at 828 ft (252.37 m)
  Transmit in open area (no trees), then transmit in tree area
  Transmit video and simulated sensor data from the CSR to the GS
Ground Station
Test Location:
Bear Creek Trail
828 ft
(252.37 m)
Comm. Link
CSR Radio
CSR POE
GS Radio
Child Scout Rover
CSR Camera
CSR ASUS
GS Laptop
GS POE
Notes: Key variables distance
Testing for latency
The design of the test fixtures
What test equipment and facilities are needed
What results do we expect?
An overview of the test procedures
Critical elements of the design

## Slide 26: Communications – Model
  Model Assumptions:
  Downlink and uplink parameters are equal
  The Radio Science Model used is a reliable source to calculate attenuation due to trees
      (“Radio wave propagation through vegetation: Factors influencing signal attenuation” Radio Science, Vol. 38, No.5. Retrieved from https://agupubs.onlinelibrary.wiley.com/doi/pdf/10.1029/2002RS002758)
Link Budget:
  Needed a link margin of 10 dB in open areas and in tree areas
  Maximum tree depth allowed is 70 m
Data Budget:
  Data being sent for only commands, video stream, and magnetometer heading
  Grayscale image to reduce bits per pixel
    640x480, 30 FPS
  Maximum data rate for our radios is ~6.5Mbps
Open Areas
Tree Areas
Notes: Validation of Model –Does it work?
Verification of Model - How well does it work?
Test Results
Critical elements of the design

## Slide 27: Communications – Model Validation
Tree Area Test:
  Average Transmission Rate: 3.264 Mbps
  Standard Deviation of the Mean: 0.077 Mbps
  Overall goal is to receive a signal strength above the radio’s receiver sensitivity which is -96 dBm
  Meeting a 10 dB link margin then requires a received strength of no less than -86 dBm
Chart: Signal Strength vs. Distance
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 820
Signal Strength (dBm) | -36 | -46 | -60 | -63 | -65 | -66 | -69 | -69 | -76 | -69 | -78 | -78 | -78 | -83 | -84 | -82 | -86
Chart: Latency vs. Distance
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 820
Latency (ms) | 8 | 13 | 22 | 13 | 9 | 37 | 22 | 20 | 36 | 13 | 59 | 101 | 97 | 212 | 92 | 151 | 226
  Results
    Minimum recorded signal strength was -86 dBm to meet a 10 dB link margin. Passes Comm 1.1.
    Transmission rate supported live video stream. Passes Comm 2.3.
    Video latency increased as distance increased.
  Tree Separation: 12.25 ft
Notes: Validation of Model –Does it work?
Verification of Model - How well does it work?
Test Results
Critical elements of the design

## Slide 28: Power – Scope and Status
Purpose:
To validate the mobility power model to ensure a mission can be completed successfully.
Requirements being validated:
  POW 3.1: The CSR Power system shall provide at least 5400 mAh to the CSR
Status:
  COMPLETED & PASSED
Risk Reduction:
  Test estimates mission duration and ensures the LiPO battery will not be over-discharged during mission

## Slide 29: Power – Test Design
Key Variables:
Constant Current
Testing for:
Battery life of 60 minutes
Equipment:
  7500 mAH, 100C LiPO battery
  Agilent N3301A DC Electronic Load
Procedure:
    Set the Agilent N3301A DC Electronic Load to continuously pull 5.4 A current from the battery
    Attached fully charged LiPO battery Electronic Load Tester
    Recorded voltage measurements every 30 seconds
    Stopped test when voltage readings drop to threshold voltage (12V)
Agilent N3301A DC Electronic Load
Notes: Held constant current, tested time. Talk more about the variables
The design of the test fixtures
What test equipment and facilities are needed
What results do we expect?
An overview of the test procedures
Critical elements of the design

## Slide 30: Power Model
Legend Red = 1 min Incline Slope Blue = Flat Ground Purple = 4 Second Obstacle Traversal
22,860 mA
11,200 mA
3000 mA
5.4 A
Total Current Consumption = 5.4Ah
Using power model on dirt
Integrate power spikes, gives Iavg
Notes: Still working on it, we had a few changes
-40 minute mock mission, when we integrate over all of these obstacle durations

## Slide 31: Power– Model Validation
Description of Model:
  Battery was discharged at a constant current of 5400 mA (Iavg) to determine the maximum mission duration
Model Assumptions:
  Average current being drawn
Test Results:
  Measured mission duration ~ 76 minutes > Desired mission duration = 40 minutes (1 hour with F.O.S)
  Performance exceeded expectations by 16 minutes
Notes: Validation of Model –Does it work?
Verification of Model - How well does it work?
Test Results
Critical elements of the design

## Slide 32: Sensing – Scope and Status
Purpose:
Determine the accuracy of all sensors (360° LiDAR, Single beam LiDARs, Ultrasonic sensors, GPS, and Magnetometer)
Requirements being validated:
SENS 3.1.2: The CSR Sensing system shall detect objects at least 1 inch wide
SENS 3.2: The CSR Sensing system shall detect discontinuities at least 2.4 inches (6.1 cm) deep
CDH 3.3: The CSR C&DH system shall determine if the CSR is within +/- 5 meters of the location of interest
CDH 3.4: The CSR C&DH system shall determine the heading of the CSR
Status:
  Single beam LiDARs, Ultrasonic sensors, GPS, Magnetometer tests - COMPLETED & PASSED
  360° LiDAR test - TO BE COMPLETED 3/7
Risk Reduction:
LiDAR and Ultrasonic accuracy measurements ensure obstacles and discontinuities can be detected at correct distance so CSR can stop in advance
GPS and magnetometer accuracies ensure the CSR is able to reach LOI within desired +/- 5 m

## Slide 33: Single Beam LiDAR – Test Design
Key Variables:
  Distance reading from LiDAR
Testing for:
  Accuracy of lidar
Equipment:
  Single beam LiDAR, Arduino Due, breadboard, power source, 1 KΩ resistor, 1 680 µF capacitor
LiDAR Lite
Arduino Uno
0
LiDAR Lite V3 Arduino Setup
Procedure:
  Set up LiDAR in combined I2C and PWM setup on breadboard and connect to power source
  While recording LiDAR data, hold notebook in front of LiDAR for 10 seconds at distances of 1 m increments
  Find average and std of measurements at each distance and subtract the actual distance to determine error
Circuit
Notes: Held constant current, tested time. Talk more about the variables
The design of the test fixtures
What test equipment and facilities are needed
What results do we expect?
An overview of the test procedures
Critical elements of the design

## Slide 34: Single Beam LiDAR – Performance Characterization
Sensor | Required Accuracy | Rationale | Measured Accuracy
Single beam LiDAR | Error must be < 23.7 cm (9.3 in) in ideal conditions | To detect a 22.9 cm (9 in) wide discontinuity | Error at 1 m: LiDAR 1: 6.91 cm +/- 0.25 cm LiDAR 2: 4.81 +/- 0.12 cm
2.4 in
9 in
9.3 in
After setup revision
Notes: Validation of Model –Does it work?
Verification of Model - How well does it work?
Test Results
Critical elements of the design

## Slide 35: Sensing– Performance Characterization
Sensor | Required Accuracy | Rationale | Measured Accuracy
GPS | Error must be < 5 m | Requirement based | Without correction: 1.26 +/- 0.1 m With correction: 1.79 +/- 0.1 m
Magnetometer | 2.29° < accuracy < 18.32° | To reach an LOI from: 250 m < 31 m | +/- 1.27° accuracy
Ultrasonic sensor | Error < 6.1 cm (2.4 in) | In order to detect a discontinuity | 0.05 cm error at 6.1 cm (2.4 in)
Notes: Validation of Model –Does it work?
Verification of Model - How well does it work?
Test Results
Critical elements of the design

## Slide 36: 360° LiDAR - Test Design
Rock
Cylinder Objects
B = 1 in
C < 1 in
A > 1 in
Gridded Cutting Mat
360 ° LiDAR
Measurement Angle
A
B
C
Adjustable
Distance
Testing for:
  Angular measurement error
  Distance measurement error
Key Variables:
  Shape of objects
  Size of objects
  Measured distance
Procedure:
  Procure objects and secure on cutting mat in pre-calculated locations
  Secure RPLIDAR at a desired measuring distance
  Perform 10 seconds of scans at 5 Hz to capture distance measurements of 50 scan frames
  Calculate angular measurement and distance measurement error for each expected measurement per scan
  Overlay captured data on expected results
Desired Measuring Distance
Facility: Lockheed Martin Room
Square Cardboard box
Notes: Reformat with emphasis on purpose, variables,measurements, etc.
The design of the test fixtures
What test equipment and facilities are needed
What results do we expect?
An overview of the test procedures
Critical elements of the design

## Slide 37: 360° LiDAR - Test Design
Square Cardboard box
Rock
Cylinder Objects
B = 1 in
C < 1 in
A > 1 in
Gridded Cutting Mat
360 ° LiDAR
Measurement Angle
A
B
C
= Expected LiDAR Data point
Testing for:
  Angular measurement error
  Distance measurement error
Key Variables:
  Shape of objects
  Size of objects
  Measured distance
= Recorded LiDAR Data point
Adjustable
Distance
Desired Measuring Distance
Zoomed in View
Recorded data point could have distance measurement error
Notes: Reformat with emphasis on purpose, variables,measurements, etc.
The design of the test fixtures
What test equipment and facilities are needed
What results do we expect?
An overview of the test procedures
Critical elements of the design

## Slide 38: Phase 2 Tests

## Slide 39: Hardware Integration – Scope and Status
Purpose:
To determine if the software modes work with the integrated hardware (motor, ASUS, Arduino DUE). This will be done by comparing commanded versus measured motor speeds.
Requirements being validated:
CDH.1.1: The CSR C&DH software shall identify the intended receiving subsystem (i.e. Mobility, Sensing, Communication) for received commands
CDH.1.2: The CSR C&DH software shall distribute commands to the intended receiving subsystem (i.e. Mobility, Sensing, Communication)
Status:
TO BE COMPLETED before 3/17
Risk Reduction:
Verifying the integration of hardware and software modes allows for further integration between the rest of the modes and hardware

## Slide 40: Hardware Integration – Test Design
Testing for:
Linear Velocity
Key Variables:
Software mode
Procedure:
Upload software to ASUS and Arduino DUE
Connect ASUS, Arduino DUE, motor controllers and motors
Command software into various modes where each mode corresponds to a different expected speed
Measure the speed at each mode with the encoders
Mode 1
Mode 2
Mode 3
ASUS
Motors
0 m/s
.5 m/s
1 m/s
Serial Command
Measurement
Encoders
Motor Controller
Arduino DUE

## Slide 41: Hardware Integration – Performance Characterization
Expected Results
Measured velocity should match the commanded velocity
    Commanded velocity is based on no load lab testing measurements
    Performance characterized by how closely commanded velocity matches expected RPM and linear velocity
The software mode will be verified based on the measured and commanded speed of the motors
Equipment
ASUS, Arduino DUE, motor controllers and motors, external power supply or mobility battery, keyboard and monitor
Facilities
Trudy’s Lab

## Slide 42: Phase 3 Tests

## Slide 43: Day In The Life Test (DITLT)
October 2018
Ground
Station
Requirements
Functions
25 meters from deployment point to LOI
Up to a 9 in wide, with a depth greater than 2.4 in
Comm between GS and CSR
LIDAR sensor
Autonomously controlled path
Stop and request user intervention
Pathpoint
Manually controlled path
Legend
Mission Terrain
Child Scout Rover
1
Plywood pieces stacked up to be 2.4 in. Inclined piece of plywood allows for a 20 ° slope
* Lengths not to scale
Length of CSR + .953 m
Length of CSR
2
3
4
1.42 m
.953 m
5
6
Receive Location of Interest (LOI) from GS
1
The CSR detects a discontinuity and stops
5
User commands CSR to point towards LOI
2
User commands CSR into semi autonomous mode
3
The CSR crosses the discontinuity after being commanded to from the GS
6
CSR travels up a 20 ° slope
4
20o Slope

## Slide 44: Day In The Life Test (DITLT)
Cardboard Box
* Lengths not to scale
The CSR will encounter an obstacle and stop
7
The user will take control, and manually control the CSR around the obstacle
  Every time the CSR turns, a pathpoint is recorded
8
After traveling around the obstacle, the user commands the CSR to point towards the LOI, and commands it into semi- autonomous mode
9
The CSR will travel towards the LOI, until it arrives within a 5 m radius. It will then stop and alert the GS
10
Comm between GS and CSR
LIDAR sensor
Autonomously controlled path
Stop and request user
intervention
Pathpoint
Manually controlled path
Legend
Mission Terrain
LOI
5m
.953 m
7
25 meters from deployment point to LOI
8
8
9
9
10
Each test will be individually tested between:
March 17th – April 9th
The full system test will be conducted between:
April 10th – April 20th

## Slide 45: Safety
Safety Risk | Mitigation | Procedure
Lose control of mobility system | Kill switch implementation | Operations
Over-discharge of battery | Check battery levels before and between tests | Operations
Circuit shortages | Ensure power is off until connections have been verified | Operations
Temporary electronics housing, metal components in contact with baseplate | Secure to CSR with adjustable Velcro/tape only on acrylic platforms | Operations
Hazards to exposed connections in testing phase | Tape all connections | Operations
Non-wireless communication USB cord | Have a member hold the USB above CSR and be cautious, do not let the cord drag or rapidly turn CSR | Operations
Damage when transporting CSR | Use the mobile toolbox when transporting the CSR | Transportation
Safety of team members | Must be able to carry up to 40 lbs, must wear closed toed shoes, carry only from middle two wheels | Transportation
Note: Blue means emphasis

## Slide 46: Budget

## Slide 47: Cost Plan
Subsystem Expenses
Mobility - $2255.71
Sensing - $1266.73
Comms - $731.00
CDH - $113.39
Power - $295.87
Misc - $120
Expenses to Date: $5254.49
Original Budget: $5000.00
Budget w/ EEF Funds: $6000.00
Remaining Funds: $745.51

## Slide 48: Cost Plan
Major Procurements
Mobility – Motors, Wheel, Chassis
Communication – Radios, Long Range Antennas
Power – Mobility System Battery, Testing Materials
CDH – Arduino Due, ASUS Computer
Sensing – 360 LiDAR, Single Beam LiDARs, Cameras, Replacement LiDAR
Future Procurements
360 LiDAR test set-up, DITLT Testing Materials (~$100)

## Slide 49
Notes: Can add video of the CSR driving

## Slide 50: Project Heritage
The Jet Propulsion Laboratory’s Fire Tracker System is a system that is designed to be a low-cost, hands-off approach to forest fire identification.
There have been three previous years of heritage:
  INFERNO (2015-2016)
    - Built a semi-autonomous drone capable of transporting and deploying sensor packages
  CHIMERA (2016- 2017)
    - Built a landing, securing, and deployment system for the inherited semi-autonomous drone from INFERNO
  DRIFT (2017-2018)
    - Developed a mother rover to secure, carry, and level the semi-autonomous drone from INFERNO using the landing platform from CHIMERA
Note: Blue used for emphasis
Notes: Wingate: take this out

## Slide 51: Definitions
Pathpoint – A point after a mobility command is received and executed by the CSR.
  This point is recorded onboard the CSR and sent to the GS as a GPS coordinate.
  An operator from the ground station initially issues the command.
  Previously referred to as ‘waypoint’, and changed for clarity
Obstacle – Roots, trees, rocks, shrubs, and inclined slopes with type A terrain (only leaves are present on type A terrain)
  Traversable Obstacles
  Any root or rock less than 2.4 inches (6 cm) - (6 cm is based on average root diameter from ‘Tree Root Systems’ from the Arboricultural Advisory and Information Service)
  Non-Traversable Obstacles
  All trees
  All shrubs
  All roots and rocks greater than 2.4 inches
Discontinuity – A 9 inch wide gap with a depth larger than 2.4 inches. The width was previously 12 inches, however a model proved that the MR could only cross a 9 inch discontinuity (.229 m).
Note: Blue used for emphasis

## Slide 52: Terrain Definition

## Slide 53: CONOPS: Loss of Comms
53
October 2018
Requirements
Functions
CSR detects no comms
1
CSR initiates last recorded pathpoint as a new temporary LOI
2
Upon arrival it will stop, and wait for acquisition of communications
5
CSR turns to point towards new temporary LOI
3
Comm between GS and MR
Comm between GS and CSR
Comm between CSR and MR
Autonomously controlled path
Legend
Stop and request user intervention
Pathpoint
Mission Terrain
Manually controlled path
CSR proceeds to travel towards new LOI
4
Child Scout Rover
Last recorded Pathpoint
Temporary location of Interest
=
=
Front of CSR
Front of CSR
Front of CSR
Upon acquisition of signal, the operator takes control of the CSR
6
3
1
2
4
5
Ground
Station
6

## Slide 54: Power Model Visualization
Obstacle Totals:
Current Draw: 22,860 mA
Time 2 min
Required Capacity: 762 mAh
Slope Totals:
Current Draw: 11200 mA
Time 6 min
Required Capacity: 1120 mAh
Flat Ground Totals:
Current Draw: 3000mA
Time 52 min
Required Capacity: 2600mAh
30 obstacles 2.4 inches in height
4 seconds per obstacle
Flat ground
52 min on gravel and dirt
Six 20 ° inclined slopes
1 minute per slope
Total Required Capacity: 5400 mAh
x6
x30

## Slide 55: Additional Testing

## Slide 56: Coefficient of Friction

## Slide 57: Test – Scope and Status
Purpose: Determine whether the coefficient of friction of the wheels meets the expected values for the mobility models.
Requirements being validated:
MOB 3.3: The CSR shall drive up or down a slope of up to 20 °s.
MOB 3.4.1: The CSR shall drive over an traversable obstacle up to 2.4 inch (0.06096 m) in height.
Status: Completed tests using unmodified wheels.
Risk Reduction: Validate models and coefficient range to ensure that the CSR can traverse terrain easily and without fatal slippage

## Slide 58: Test – Test Design
Facilities: Bobby's Lab
Equipment:
  2x4 Wood Planks
  Brick
  100 lbf scale, +/- 0.1 lbf accuracy
  CSR without chains installed
  Analog force gauge, 0.1 lbf accuracy
Procedure:
Place test material (wood or brick) onto scale
Tear the scale to set to 0 in order to only read the force from the CSR
Place the front wheel from the CSR onto the scale
Place excess wood under the remaining wheels to level the CSR
Record the weight on the scale
Add excess weight to the CSR and record scale again
Attach the force gauge with a string to the bottom axel of the wheel
Slowly pull the gauge parallel to the floor until slippage occurs and record force.
Expected Results:
µwood =0.7, µbrick =0.7
Scale
Brick
Wood
Wood
CSR
Force Gauge
Weight
Notes: The design of the test fixtures
What test equipment and facilities are needed
What results do we expect?
An overview of the test procedures
Critical elements of the design

## Slide 59: Test – Model Validation
Description of Model: The coefficient of friction was used to run the torque and power analysis of the CSR travelling over various terrains (flat ground, slopes, traversable obstacles.)
Model Assumptions: Assuming coulombic friction.
Test Results:
The coefficient of friction of brick well surpassed the estimated value of 0.6. The coefficient of friction of the wood averaged to be 4% lower than the estimated value. However, there was also significant deviation based on the orientation of the wood. Moving forward, the tires will be modified by slitting the rubber to increase traction.
 | Wood | Brick
Mean | 0.67 | 1.3
Standard Deviation % | 27% | 8.7%
Notes: Validation of Model –Does it work?
Verification of Model - How well does it work?
Test Results
Critical elements of the design

## Slide 60: Encoders

## Slide 61: Test – Scope and Status
Purpose:
Characterize motor controller defined speed range in terms of meters-per-second,
Track the speed of each motor to maintain constant speed over obstacles
Status:
Completed characterization for all speeds

## Slide 62: Test – Test Design
Facilities: Trudy's lab
Equipment: Motor controller, Arduino Due, AndyMark Motors, AndyMark Encoder, 10A Power Supply
Procedure:
Mount motor controller on arduino due
Mount encoders on motors
Wire encoders to Due (+5V, GND, 2 Digital Pins)
Run code to drive motors
  Serial input for different speeds
Track readings on arduino serial monitor
Expected Results: Current supplied to motors and encoder reading in RPS
Notes: The design of the test fixtures
What test equipment and facilities are needed
What results do we expect?
An overview of the test procedures
Critical elements of the design

## Slide 63: Test – Model Validation
Description of Model: Two points 90 °s from each other about the shaft of the motor. One can track the speed of the motor by tracking the time it takes for a point on the motor to pass one of these tracking points.
Model Assumptions: No noise
Validation of Model:
Test Results:
Encoder 1:
  Reaches noisy steady state within 1 minute of motor startup
Encoder 2:
  Reaches steady state within 1 minute of motor startup without noise
Notes: Validation of Model –Does it work?
Verification of Model - How well does it work?
Test Results
Critical elements of the design

## Slide 64: Encoder Plots

## Slide 65: GPS

## Slide 66: Test – Scope and Status
Purpose:
Ensure the GPS is meeting its accuracy requirements
Requirements being validated:
CDH 3.2: The CSR C&DH system software shall store the Location of Interest’s GPS coordinates in memory.
CDH 3.3: The CSR C&DH system shall determine if the CSR is within +/- 5 meters of the location of interest
Status: COMPLETED
Risk Reduction:
Verifies the GPS is accurate enough before final testing so the CSR can meet the requirement of reaching the LOI within +/- 5 meters

## Slide 67: Test – Test Design
Equipment:
GPS, ground station, ASUS Tinker board, Arduino Due, GPS RTK modules and antennas
Procedure:
Set up GPS, antennas, ASUS, and ground station
Place the GPS at a location that can be verified by google maps. Measure the GPS reading 50 times and take the mean and std of the results
Compare GPS and google maps reading to determine accuracy
Expected Results:
GPS expected to have accuracy of at least +/- 5 m
GPS "with correction" expected to be more accurate than GPS "without correction"
Results:
GPS accuracy without correction: 1.26 +/- 0.1 m
GPS accuracy with correction: 1.79 +/- 0.1 m
GPS setup with antennas
Ground station
Notes: The design of the test fixtures
What test equipment and facilities are needed
What results do we expect?
An overview of the test procedures
Critical elements of the design

## Slide 68: Ultrasonic

## Slide 69: Test – Scope and Status
Purpose:
Determine the accuracy of the Ultrasonic sensor
Requirements being validated:
SENS 3.2: The CSR Sensing system shall detect discontinuities at least 2.4 inches (6.1 cm) deep
Status: COMPLETED & PASSED
Risk Reduction:
Ultrasonic accuracy measurements ensure obstacles and discontinuities can be detected at correct distance so CSR can stop in advance

## Slide 70: Test – Test Design
Facilities:
Trudy's lab
Equipment:
Laptop, Arduino Due, Ultrasonic sensors, plywood, (tripod optional)
Procedure:
Place the plywood at measured distance from the ultrasonic sensor
Record the output reading from the ultrasonic sensor and compare with measured distance to find ultrasonic accuracy
Expected Results:
Ultrasonic sensor should have an accuracy of at least 2.4 in (6.1 cm)
Notes: The design of the test fixtures
What test equipment and facilities are needed
What results do we expect?
An overview of the test procedures
Critical elements of the design

## Slide 71: Test – Test Results
Ultrasonic sensor error is 0.05 cm at 6.1 cm (2.4 in) < required 6.1 cm (2.4 in) error
Distance [cm]
Notes: Validation of Model –Does it work?
Verification of Model - How well does it work?
Test Results
Critical elements of the design

## Slide 72: Magnetometer

## Slide 73: Test – Scope and Status
Purpose: Verify the magnetometer can report a heading within a specific accuracy of the actual heading.
Requirements being validated:
CDH.3.4: The CSR C&DH system shall measure heading within 2.39 degrees of the actual heading
Status:
Reports to required precision
Reports inaccurate heading

## Slide 74: Test – Test Design
Facilities: Senior Projects Room
Equipment:
Raspberry Pi 3B
Adafruit LSM303 Magnetometer/Accelerometer
5V USB Power Supply
Procedure:
Wire Raspberry Pi to monitor and power supply
Wire LSM303 to Raspberry Pi per hookup schematic
Run heading read-in script and record results
Expected Results:
Reports due south (180degrees) to within +/- 2.39 degrees
Pi 3v3 to sensor VIN
PI GND to sensor GND
PI SCL to sensor SCL
PI SDA to sensor SDA
Notes: The design of the test fixtures
What test equipment and facilities are needed
What results do we expect?
An overview of the test procedures
Critical elements of the design

## Slide 75: Test – Model Validation
Notes: Validation of Model –Does it work?
Verification of Model - How well does it work?
Test Results
Critical elements of the design

## Slide 76: Motor Test

## Slide 77: Test – Test Design
Facilities: Trudy's Lab
Equipment:
Motor Controller
(2x) Motors
Arduino Uno
Power Supply (10A)
Expected Results:
Forward command turns motors in same direction
Turn command turns motors in opposite direction
Backward command turns motors in same direction
Notes: The design of the test fixtures
What test equipment and facilities are needed
What results do we expect?
An overview of the test procedures
Critical elements of the design

## Slide 78: Test – Model Validation
Notes: Validation of Model –Does it work?
Verification of Model - How well does it work?
Test Results
Critical elements of the design

## Slide 79: Linear Moving Mass Test

## Slide 80: Test – Test Design
Facilities: Trudy's Lab
Equipment:
Linear Mass Stager
Linear Mass Controller
Multimeter
Power Supply (15 V)
5kg Steel Mass Configuration
Procedure:
Control moving mass from one end of stage to to the other; repeat 3 times
Results:
Maximum current consumption was 0.40 Amps
Average time for mass transition = 60 seconds
Backward command turns motors in same direction
Notes: The design of the test fixtures
What test equipment and facilities are needed
What results do we expect?
An overview of the test procedures
Critical elements of the design

## Slide 81: Single Beam LiDAR

## Slide 82: Test – Test Design
Facilities: Trudy's lab
Equipment:
Single beam LiDAR, Arduino Due, breadboard, power source, 1 KΩ resistor, 1 680 µF capacitor
Procedure:
Set up LiDAR in combined I2C and PWM setup on breadboard and connect to power source
While recording LiDAR data, hold notebook in front of LiDAR for 10 seconds at distances of 1 m increments
Find average and std of measurements at each distance and subtract the actual distance to determine error
Expected Results:
Single beam LiDAR accuracy less than 23.7 cm (9.1 in)
The given PWM Arduino wiring produced very inaccurate results
The given I2C Arduino wiring did produced "not acknowledging" errors
Combining the I2C and PWM Arduino wirings yielded accurate data
Realized the Arduino UNO was producing accurate LiDAR readings but the Arduino DUE was not
Notes: The design of the test fixtures
What test equipment and facilities are needed
What results do we expect?
An overview of the test procedures
Critical elements of the design

## Slide 83: Test – Test Results
Sensor | Required Accuracy | Rationale | Measured Accuracy
Single beam LiDAR | Error must be < 23.7 cm (9.3 in) in ideal conditions | To detect a 22.9 cm (9 in) wide discontinuity | Error at 1 m: LiDAR 1: 6.91 cm +/- 0.25 cm LiDAR 2: 4.81 +/- 0.12 cm
2.4 in
9 in
9.3 in
After setup revision with Arduino Uno
Notes: Validation of Model –Does it work?
Verification of Model - How well does it work?
Test Results
Critical elements of the design

## Slide 84: ASUS Thermal Test

## Slide 85: Test – Test Design
Facilities:
Trudy's Lab
Equipment:
ASUS tinker board, shoebox, thermocouples
Procedure:
Run complicated script on ASUS that will cause the component to heat up
Measure the internal temperature with thermocouples at different distances from the ASUS
Expected Results:
Internal temperature of the shoebox should not exceed the maximum working temperature of other internal electronic components (Arduino due, magnetometer, etc.)
Notes: The design of the test fixtures
What test equipment and facilities are needed
What results do we expect?
An overview of the test procedures
Critical elements of the design

## Slide 86: Test – Test Results
Description of Model:
Shown in the right are plots of both CPU temperature and ambient temperature over the test duration
Model Assumptions:
The script being run on the ASUS is more complicated than what will actually be running during our mission
Test Results:
Ambient temperature of the shoebox did not exceed 28 degrees celcius
This temperature does not exceed the maximum working temperature of any other electronic components
For precaution, a heat sink or a fan may be added to the CSR later on
Notes: Validation of Model –Does it work?
Verification of Model - How well does it work?
Test Results
Critical elements of the design

## Slide 87: Sensing Accuracy Summary

## Slide 88: Sensing– Performance Characterization
Required Accuracy | Results
Single beam LiDAR must have an error < 23.7 cm (9.3 in) in ideal conditions to detect a 22.9 cm (9 in) wide discontinuity | Measured Accuracy: Error at 1 m: LiDAR 1: 6.91 cm +/- 0.25 cm LiDAR 2: 4.81 +/- 0.12 cm
Ultrasonic sensor must have an error < 6.1 cm (2.4 in) in order to detect a discontinuity | Measured Accuracy: 0.05 cm error at 6.1 cm (2.4 in)
2.4 in
9 in
9.3 in
2.4 in
9 in
2.4 in
Notes: Validation of Model –Does it work?
Verification of Model - How well does it work?
Test Results
Critical elements of the design

## Slide 89: Sensing– Performance Characterization
Required Accuracy | Results
GPS must have an error < 5 m (requirement based) | Measured Accuracy: Without correction: 1.26 +/- 0.01 m With correction: 1.79 +/- 0.01 m
CSR stops at least 8 times (6 slopes, 2 discontinuities) which is ~ every 31 m Magnetometer must have at least an 2.29° < accuracy < 18.32° | Measured Accuracy: STD: 1.27°
CSR
x
LOI
5 m
5 m
θ
At x = 250 m, Θ = 2.29°
At x = 31 m, Θ = 18.32°
Notes: Validation of Model –Does it work?
Verification of Model - How well does it work?
Test Results
Critical elements of the design

## Slide 90: Safety Procedures – Operation Checklist
Check the charge of the LiPo battery before testing
In the testing phase: tape all exposed connections
Use Velcro to temporarily place all electronics being used on the CSR, making sure that any exposed metal is not touching the baseplate, the middle acrylic plate is a good place to house these in the testing phase
Tape wires as needs to secure them to the CSR to avoid interference with the drive train
Double check that the battery is secure, this is heavy and likely to move
Double check the connections from the battery to the electronics before turning the battery on
Again double check no metal is touching the baseplate
If the CSR does not respond to a “stop” command, two people must lift the baseplate in the front and back until kill switch is implemented
If the motors begin to stall for any reason, send a ”stop” command
2.
3.
4.
8.
7.
9.
6.
10.
With non-wireless communication, be cautious of the USB cord. Make sure someone is holding it during operation and do not command multiple turns.
5.
1.
Notes: Put one of these in the main slides

## Slide 91
Must be wearing closed toed shoes
Must be able to lift 40lbs
Check to ensure mass is in the middle position
Lift the CSR from only the middle two wheels
The toolbox must be utilized in order to transport the CSR long distances / outside
To protect all extruding parts, orient the front of the CSR with the handle of the toolbox
Secure the top of the toolbox when transporting outside
Do not place anything over 5lbs on the top of the CSR
When removing from the toolbox, again use the middle wheels
Safety Procedures - Transportation
1.
2.
3.
4.
5.
6.
7.
8.
9.

## Slide 92: Offramp – Ultra Sonic Sensors

## Slide 93: Offramp Ultra Sonic Sensors
2-6 of these Parallax Ultra Sonics Sensors will be used on the CSR for object detection.
Due to fast progress on Manufacturing, work has begun on the offramp option for Object Detection
Preparation in case 360 LiDAR is not able to be integrated properly
Each sensor only requires one pin (I/O)

## Slide 94: Off-Ramp Ultrasonic Lidar, Ground Interference
2.4 inches
Ultrasonic
20°
2.25 inches
The PING)))™ Ultrasonic Distance Sensor cannot accurately measure the distance to an object if the surface is reflective and has a shallow angle (Θ<45°) such that the sound does not reflect back
The ultrasonic sensor has a conic FOV of 20°, meaning it will hit the ground at this angle and not reflect back to the sensor
The smallest distance this occurs is at 2.25 inches, which is smaller than the 1 meter requirement and thus sufficient (the 1 meter required is the stopping distant requirement for the CSR upon its encounter with an obstacle)
Testing procedure to validate this

## Slide 95: PID Controller Development

## Slide 96: PID Controller – Required Constants
Known
Educated Guess

## Slide 97: PID Controller – Developing the Model
1) Fundamental Equations
2) Combine Equations
3) Laplace Transform for Open Loop Response

## Slide 98: PID Controller – Developing the Model
4) Block Diagram

## Slide 99: PID Controller – Control Development
Using Kp = 10, Ki = 10, Kd = 0.01