## Slide 1: Test Readiness Review
Presenters: Benjamin Elsaesser, Sheridan Godfrey, Andy Kain, Cedric Leedy
Team: Luke Beasley, Joseph Beightol, Benjamin Elsaesser, Sheridan Godfrey, Caleb Inglis, Jack Isbill, Andy Kain, Cedric Leedy, Chris Leighton, Daniel Mastick, Bailey Topp
Customer: TJ Sayer - Sierra Nevada Corporation (SNC) Advisor: Francisco Lopez Jimenez
Mechanically Engineered Grappling Arm to Capture Litter and Atmospheric Waste
Notes: Sheridan

## Slide 2: Overview
Overview
Schedule
Testing Readiness
Overview
Budget
Testing Readiness
Subsystems
Testing Readiness
Integration
Notes: SHeridan

## Slide 3: Project Motivation & Statement
MEGACLAW shall use a robotic arm equipped with an end effector to capture a grapple point, a flat plate spinning on a motor at a constant rate, which simulates a solar panel on a 6U CubeSat rotating about a single axis of rotation.
MEGACLAW is a proof of concept for mitigating debris by capturing then deorbiting debris or performing maintenance on broken spacecraft.​
Heritage: CASCADE, KESSLER
Notes: Present: Sheridan

## Slide 4
Robotic arm mounted to GSE base
Slip
Ring
Secondary Sensor
End effector
(EE)
Grapple point (GP)
mounted to turntable motor
Ground Support Equipment (GSE)
Primary Sensor
Baseline Design
x̂
ẑ
ŷ
Coordinate
Frame
Notes: Sheridan

## Slide 5: Hardware Baseline Overview
Robotic Arm, Slip Ring and EE with AR tags to be sensed by the Intel D435 (Located on GSE Base)
RGB
Depth Sensors
GP on rotating turntable with AR tags as well as colored markers to be sensed by the Pixy 2
Pixy 2
Slip ring
Pixy 2
Ball Joint Grippers
AR Tags
Grapple Point
Turntable Base
Colored markers
AR tag
Notes: Sheridan
Create: Sheridan
- update; account for slip ring
-Working on Solidworks model of arm with slip ring and mount, ball joints on ends, will update pic when complete
Cedric

## Slide 6
1. Intel D435 determines state of EE and GP using AR tags
2. Robotic arm actuates to commanded position
ẑ
3. At 10" from GP, secondary camera takes over to determine spin rate
CONOPS
Slip Ring
Secondary Camera
Primary Camera
Notes: Sheridan

## Slide 7
1. Intel D435 determines state of EE and GP using AR tags
2. Robotic arm actuates to commanded position
ẑ
3. Secondary camera takes over to determine spin rate
CONOPS
Secondary Camera
Slip Ring
Primary Camera
Notes: Sheridan

## Slide 8
3. Secondary camera takes over to determine spin rate
x̂
ŷ
4. EE is spun up to match GP spin rate
5. Arm actuates forwards and force sensors determine if successful grapple is achieved
CONOPS
Determined Spin Axis
(X,Y,Z) AR positions
Notes: Sheridan

## Slide 9
3. Secondary camera takes over to determine spin rate
4. EE is spun up to match GP spin rate
5. Arm actuates forwards and force sensors determine if successful grapple is achieved
ẑ
CONOPS
Notes: Sheridan

## Slide 10
3. Secondary camera takes over to determine spin rate
4. EE is spun up to match GP spin rate
5. Arm actuates forwards and force sensors determine if successful grapple is achieved
ẑ
CONOPS
Force Sensors
Force Sensors
Notes: Sheridan

## Slide 11
 | Control Loop Input | Control Loop Execution
Level 1 Success | Identify and report EE location at a rate of 0.916 [Hz] with a tolerance of 1.5 [cm]. | EE responds to given controlled input position, converging within 1.5 [cm].
Level 2 Success | Identify and report the locations of the EE and the stationary GP. | EE makes arbitrary contact with stationary GP on object within 255 [s].
Level 3 Success | Identify and report the location and angle of the EE and the rotating GP revolving at 0.578 [rad/s]. | Successful grapple of rotating GP, confirmed using force sensors on EE.
Levels of Success
Notes: Andy
Control loop input:
at a rate of 0.916 [Hz] with a tolerance of 1.5 [cm]
Present: Andy

## Slide 12: FBD
Notes: Andy

## Slide 13: FBD
Notes: Andy

## Slide 14: FBD
Notes: Andy

## Slide 15: FBD
Notes: Andy

## Slide 16: FBD
Notes: Andy

## Slide 17: Critical Hardware Update from MSR
GP attachment to rotating turntable has been updated to reduce risk of damaging GP or actuators
Magnetic attachment points will now secure the solar panel model to the turntable actuator
The breakaway grapple point will prevent damage to the system in the event of uncoordinated grapple
Grapple Point
Turntable Base
Detachment
Line
Embedded Magnets
Notes: Cedric
Jack
- add diagram showing magnets
Cedric

## Slide 18: Project Elements
​CPE​​ | ​Justification​ | Relation to Testing
Sensors – Accuracies​​ | Error tolerance is very small, multiple components contribute​ | Sensor mounts must be stable, interpretation software must be accurate
Sensors – Feature Recognition | Inability to find AR tags prevents closed loop operation | Software must be reliable enough to find AR tags in view
Software – State Determination | Converting sensor information to state information is sensitive | All implemented software must be accurate enough to grapple target
Actuator Thermal Requirements | Any damage to components in the project can cause week long delays​ | Emergency stop button and actuator limits must be understood and utilized
Software – Speed​​ | Image processing and 3D modeling are time intensive processes; minimum GP angular velocity sampling rate​ | All implemented software must be fast to meet time requirements
Software | Hardware | Software + Hardware
Notes: Cedric
Blue bad
Change third column to testing (not manufacturing)
CHRIS:
First up, under software, which we have highlighted in yellow, we have feature recognition – our software needs to be able to reliably recognize AR tags when they're in the frame, and that's obviously something we've had to think about as we've built our vision system – though it doesn't seem like it's going to be a problem.
Next, in terms of (Point at state determination) we've had to make sure that our software is accurately localizing the AR tags on our system in cartesian space, and reconstructing the state of the grappling point and end effector, and our maximum allowable error here is only about 1.5cm, so this is one of our primary focuses in the manufacturing of that subsystem, and once we've done some testing, we'll be able to tweak how this system works.
(Point at speed) We also have timing requirements that define a minimum speed our control loop can be operating at, and that's around 1 Hz. However, our separate subsystems are each running in excess of 10 Hz, so this isn't a huge worry for us anymore.
(Point at sensors accuracies) Kind of in a mix between hardware and software, another critical element is the sensor mounts being stable and our software having accurate information about how everything is situated relative to each other just because that affects our state determination and coordinate transformations.
(Finally, in terms of hardware), we were always worried about the thermal limits of the actuators in our arm, which we're addressing by making the arm shorter than it was last year, implementing an emergency stop button, and limiting the timespan of a grapple, and now I'll hand it over to Luke to talk about another piece of hardware that's given us some headaches.
Cedric

## Slide 19: Schedule
Overview
Schedule
Testing Readiness
Overview
Budget
Testing Readiness
Subsystems
Testing Readiness
Integration
Notes: Cedric

## Slide 20: Project Schedule – MSR to EOM (Original)
Delays in preliminary VICON testing; rolled into integration/testing schedule, which is now fleshed out
Notes: Cedric
Delays with VICON, tests got rolled into integration
We expected VICON to take a day to setup, but most has now been integration work in order to get setup

## Slide 21: Project Schedule – Testing (TRR to EOM)
Notes: Cedric

## Slide 22
Project Schedule
-
TRR to PFR
Notes: Cedric

## Slide 23: Test Readiness Overview
Overview
Schedule
Testing Readiness
Overview
Budget
Testing Readiness
Subsystems
Testing Readiness
Integration
Notes: Ben

## Slide 24: Overview
Component Tests | Subsystem Tests | Integration Tests
Actuation of individual motors | Sensor coordinate transfer test | Uncontrolled accuracy tests
Intel and Pixy functionality tests | Arm thermal test | Controlled accuracy tests
Infinite rotation of EE using slip ring | Intel D435 accuracy test | Secondary sensor and EE spin up tests
AR tag identification test | EE and GP state determination test | Full system levels of success test
Complete | Incomplete
Notes: Ben

## Slide 25: Test Readiness - Subsystems -
Overview
Schedule
Testing Readiness
Overview
Budget
Testing Readiness
Subsystems
Testing Readiness
Integration
Notes: Ben

## Slide 26: Intel D435 Accuracy Test
Intel D435 Mockup EE
VICON axes
Facility | RECUV Lab
Equipment | VICON, Pearl Markers, Intel D435
Measures | VICON vs Intel D435 location/orientation data (mm and °)
Requirement | Position error: <1.5 cm Orientation error: <10°
Expected Completion Date | 3/7
Purpose: Ensure that the accuracy requirements from DR 2.2 and DR 2.3 are met by the Intel D435
Notes: Add picture
Ben

## Slide 27: Intel D435 Accuracy Test Results
Position and body-axes determined by:
Intel D435
VICON
Notes: Point out the lag

## Slide 28: Intel D435 Accuracy Test Results
Tolerable error in position: 1.5 cm Tolerable error in orientation: 10°
Notes: -Talk about how the AR tag readings are lagging behind VICON due to VICON having a way faster feedback rate and how we're going to deal with it (not sure I have a super impressive answer for that)
-This is kind of preliminary and the calibration needs to be tweaked

## Slide 29: Arm Thermal Test
Purpose: Reduce the risk of actuators overheating and going into safety shut-off mode
Model Validation: This test will validate the thermal model that DR 3.1.1.1 (the arm shall finish its operations in under 255s) is based on.
Facility | N/A
Equipment | Arm, GSE, timer
Measures | Time till automatic shut-off (seconds)
Measurement time | > 600 seconds
Requirement time | < 255 seconds
Expected Completion Date | Completed as of 2/28
Notes: Sheridan
Used CASCADE heritage model, acknowledge that it is inaccurate due to invalid assumptions between their tests and our tests. Hard to figure out it was wrong until actually tested.
3.1.1.1 actuators shall operate no longer than 255s

## Slide 30: Arm Thermal Test
Expected Results: Based on CASCADE's thermal model actuators will last up to 255s
Results: At worst case 90 degrees, actuators lasted over 10 minutes.
Expected results inaccurate due to invalid assumptions.
Considering redefining requirement 3.1.1.1 but we are still confident we can perform the full system test in under 255s.
Notes: Sheridan
Used CASCADE heritage model, acknowledge that it is inaccurate due to invalid assumptions between their tests and our tests. Hard to figure out it was wrong until actually tested.
3.1.1.1 actuators shall operate no longer than 255s

## Slide 31: Test Readiness - Integration -
Overview
Schedule
Testing Readiness
Overview
Budget
Testing Readiness
Subsystems
Testing Readiness
Integration

## Slide 32: Controlled Accuracy Test
Purpose: Verify that the EE can reach a commanded position and orientation within ±15mm and ±9 degrees as specified by DR 2.2
Model Validation:
This test will validate that the arm's motion matches our simulation when feedback control is applied model
Expected Results:
DR 2.2 will be met
The test results will not match up with our original simulation results due to differences between the actuator error applied to the simulation and the real actuator error
Feedback Control Simulation Results
Notes: Add pre-req of uncontrolled (now in BUS)
Ben

## Slide 33: Controlled Accuracy Test Setup
Facility | RECUV Lab
Equipment | Arm, Pearl Markers, VICON, GSE
Measures | Position (mm) Orientation (degrees)
Measurement Accuracy | Position: ±1 mm Orientation: ±0.5 degrees
Requirement Accuracy | Position: ±15 mm Orientation: ±9 degrees
Expected Completion Date | 04/15
Purpose: Verify that the EE can reach a commanded position within the accuracy specified by DR 2.2
VICON Cameras
Pearl
Markers
Notes: Add pre-req of uncontrolled (now in BUS)
Ben

## Slide 34: Secondary Sensor + EE Spin Up Test
Purpose: Validate that the EE will spin up to a rate equal to that of the GP while maintaining the 90±10° offset as required by DR 2.3 and 2.3.1
Model Validation:
EE spin up controller will be validated by comparing test data to simulation results
Risk Reduction:
Meeting DR 2.3 will reduce the risk of damaging the GP by decreasing angular offset between the EE and GP when attempting to perform the grapple maneuver
Expected Results:
DR 2.3 will be met
Test results may not match up with the simulation results due to differences in the simulated system error and the actual error in the system.
EE Spin Up Simulation Results
Notes: Spinning up wrist to match rotation rate and 90 degree angle offset between EE and GP
Cedric

## Slide 35: Secondary Sensor + EE Spin Up Test Setup
Facility | RECUV Lab
Equipment | Arm, GP, Pixy2, Pearl Markers, VICON, GSE
Measures | Relative Orientation (degrees)
Measurement Accuracy | ±0.5 degrees
Requirement Accuracy | ±10 degrees
Expected Completion Date | 04/14
VICON
Cameras
Pearl
Markers
Pixy2
Grapple Point (GP)
Relative
Orientation
Notes: Spinning up wrist to match rotation rate and 90 degree angle offset between EE and GP
Cedric

## Slide 36: Budget
Overview
Schedule
Testing Readiness
Overview
Budget
Testing Readiness
Subsystems
Testing Readiness
Integration

## Slide 37: Updated Budget
Items not yet purchased:
Lighting for GSE
GitHub Pro for remainder of semester
Remaining funds:
$3,301.20
Notes: Cedric

## Slide 38: Questions?

## Slide 39: Back Up Slides

## Slide 40: Overview
Overview
Schedule
Testing Readiness
Software
Budget
Testing Readiness
Hardware
Testing Readiness
Integration
Notes: SHeridan

## Slide 41: Project Elements

## Slide 42: Updated CONOPS

## Slide 43: Software Baseline Overview
Control Loop represented in a software block diagram
Each function block is a software manufacturing deliverable
Notes: Cedric
Ben
- full software block diagram
Cedric

## Slide 44
Notes: Cedric
Ben
- full software block diagram
Cedric

## Slide 45
 | Control Loop Input | Control Loop Execution
Level 1 Success | Identify and report EE location at a rate of 0.916 [Hz] with a tolerance of 1.5 [cm] | EE responds to given controlled input position, converging within 1.5 [cm]
Level 2 Success | Identify and report EE location, and location of stationary GP at a rate of 0.916 [Hz] with a tolerance of 1.5 [cm] | EE makes arbitrary contact with stationary GP on object within 255 [s]
Level 3 Success | Identify and report EE location (with a tolerance of 1.5 [cm]) and angle (with a tolerance of 10 degrees), as well as rotating GP revolving at 0.578 [rad/s], at 0.916 [Hz] rate within 1.5 [cm] | Successful grapple of rotating GP at 0.578 [rad/s], confirmed using force sensors on EE
Levels of Success
Notes: Full Levels of success

## Slide 46: Schedule
Overview
Schedule
Testing Readiness
Software
Budget
Testing Readiness
Hardware
Testing Readiness
Integration
Notes: Cedric

## Slide 47: Test Readiness - Software -
Overview
Schedule
Testing Readiness
Software
Budget
Testing Readiness
Hardware
Testing Readiness
Integration
Notes: Ben

## Slide 48: GP Location Estimation Test
Purpose: Verify that the location and orientation of the grapple point can be determined as specified by DRs 2.2.1 and 2.3.2 using primary sensor data
Facility: RECUV Lab
Equipment: Intel D435
GP
Pearl markers
Measure: Position (mm)
Requirement Verification: DR 2.2.1
Notes: Add picture
Ben

## Slide 49: GP Location Estimation Test Status: Incomplete
Expected Result: The data recorded by VICON will have lower resolution that our simulation, but the mean and standard deviations of the test and simulation data will roughly match.
GP Location Estimation Simulation Results
Notes: Add short description of simulation
Ben

## Slide 50: Arm Thermal Test
CASCADE Actuator Thermal Model
Notes: Sheridan
Used CASCADE heritage model, acknowledge that it is inaccurate due to invalid assumptions between their tests and our tests. Hard to figure out it was wrong until actually tested.
3.1.1.1 actuators shall operate no longer than 255s

## Slide 51: Pixy2 Accuracy Test
Purpose: Verify that the Pixy 2 can calculate the GP's spin rate with accuracy specified by DR 2.3.1 (±0.33 °/s)
Model Validation:
This test will validate the determined spin rate by the Pixy2 is within our allowable tolerance.
Expected Results:
The spin rate determined by the actuator encoder data will be within 0.33 °/s to the spin rate determined by the Pixy2
DR 2.3.1 will be met.
Notes: Add picture
Move status to this slide
Andy

## Slide 52: Pixy2 Accuracy Test Setup
Purpose: Verify that the Pixy 2 can calculate the GP's spin rate with accuracy specified by DR 2.3.1 (±0.33 °/s)
Facility | Senior Design room
Equipment | Pixy2, Mockup solar panel, actuator, computer
Measures | Angle (deg), time (s)
Measurement Accuracy | Angle: 0.088°
Requirement Accuracy | Angular velocity: ±0.33 °/s
Expected Completion Date | March 6th, 2019
Notes: Add picture
Move status to this slide
Andy

## Slide 53: Test Readiness - Hardware -
Overview
Schedule
Testing Readiness
Software
Budget
Testing Readiness
Hardware
Testing Readiness
Integration

## Slide 54: Slip Ring Change from CDR
Slip Ring mass: 0.44 Kg
FOS decreased, but still acceptable
 | MX-64T | MX-64T | MX-28T Single Axis | MX-28T Dual Axis
Stall Torque [Nm] | 6 | 6 | 2.5 | 2.5
CDR Torque | 0.854 | 0.522 | 0.236 | 0.139
MSR Torque | 3.072 | 1.238 | 0.539 | 0.355
CDR FOS | ~7 | ~11 | ~10 | ~18
MSR FOS | ~2 | ~5 | ~4.5 | ~7

## Slide 55: Slip Ring Adapter Strength - Procedure
Verify that the slip ring adapter will not fail under stress
Print a spare slip ring adapter
Create procedure on Partner software
Insert slip ring mount on one side of the machine clamping the grip to the slip ring mount.
Slide the other grip and clamp down on the other side of the slip ring mount.
Click start test.
Confirm the mount does not slip within grips.
When the specimen breaks, click stop test, verify there is minimal load on specimen and remove it.
Notes: Add picture

## Slide 56: Slip Ring Adapter Torsion Test
Purpose: Verify the slip ring mount will not shear do to torsion from the slip ring.
Facility | ITLL 2B Plaza
Equipment | Intron Torsion Machine, Slip Ring mount
Measures | Torque (In-lb), time (s)
Completion Date | February 20th, 2019
Expected Results:​
The slip ring mount should be able to withstand more than 26.55 [In-lb] of torque.
Notes: Create: Andy
Add picture
Back Up

## Slide 57: Slip Ring Adapter Torsion Test Results
Purpose: Verify the slip ring mount will not shear do to torsion from the slip ring.
Torque Vs Time for slip ring mount test
Slip ring mount after completed test
Notes: Create: Andy
Add picture
Back Up

## Slide 58: GP Spin Rate Test
Purpose: Verify that the GP can spin up to the commanded rate within the accuracy specified by DR 3.4
Facility: RECUV Lab
Equipment: Grapple Point
Pearl Markers
VICON
Measure: Rotation Rate (rad/s)
Notes: Cedric
Allowable error
Validation

## Slide 59: GP Spin Rate Test - Procedure
Verify that the GP can spin up to the commanded rate within the accuracy specified by DR#
Attach a pearl marker to both top corners of the GP
Command the GP to rotate at a constant rate
Measure the GP's angle over time using VICON
Convert VICON data to angular velocity and subtract the commanded rate to get the rate error
Repeat trial N times for statistical significance
Notes: Add picture

## Slide 60: GP Spin Rate Test Status: Incomplete
Verify that the GP can spin up to the commanded rate within the accuracy specified by DR#
Expected Result: The actuator's internal velocity control loop will achieve the desired velocity with sufficient accuracy.
Concerns: There may be measurement errors introduced by inaccuracies in pearl marker placement and VICON's calibration.
Notes: Add picture

## Slide 61: EE Spin Rate Test
Purpose: Verify that the EE can spin up to the commanded rate within the accuracy specified by DR 2.3.1
Facility: RECUV Lab
Equipment: Wrist Actuator + EE
Pearl Markers
VICON
Measure: Rotation Rate (rad/s)
Notes: Cedric

## Slide 62: EE Spin Rate Test - Procedure
Verify that the EE can spin up to the commanded rate within the accuracy specified by DR#
Attach a pearl marker to both ends of EE grippers
Command the wrist actuator to rotate at a constant rate
Measure the EE's angle over time using VICON
Convert VICON data to angular velocity and subtract the commanded rate to get the rate error
Repeat trial N times for statistical significance
Notes: Add picture

## Slide 63: EE Spin Rate Test Status: Incomplete
Verify that the EE can spin up to the commanded rate within the accuracy specified by DR#
Expected Result: The actuator's internal velocity control loop will achieve the desired velocity with sufficient accuracy.
Concerns: There may be measurement errors introduced by inaccuracies in pearl marker placement and VICON's calibration.
Notes: Cedric
Add picture

## Slide 64: Sensor Transfer Test
Purpose: Verify that the errors introduced by transferring data between the primary and secondary camera frames is less than that specified by DR 2.4.2 and DR 2.4.3
Facility: RECUV Lab
Equipment: Fully assembled test bed
Assembled arm
Pixy2, Intel D435
Pearl markers
Measure: Position (mm)
Notes: Add picture
Andy

## Slide 65: Test Readiness - Integration -
Overview
Schedule
Testing Readiness
Software
Budget
Testing Readiness
Hardware
Testing Readiness
Integration

## Slide 66: Uncontrolled Accuracy Test
Purpose: Determining how accurately the EE arrives at a commanded position before applying the control law
Facility: RECUV Lab
Equipment: Arm
Pearl Markers
VICON
Measure: Position (mm)
Model Verification: This data will greatly aid in tuning the control law and provide us a baseline dataset allowing us to quantify the improvement that applying our control provides
Notes: Add picture
Ben

## Slide 67: Primary Sensor + Controlled Motion Test
Purpose: Validate that we can control the position of the EE using data from the primary sensor with the accuracy required by DR 2.2
Facility: RECUV Lab
Equipment: Arm
Intel D435
Pearl Markers
VICON
Measure: Position (mm)
Notes: Add picture
Ben

## Slide 68: Controlled Accuracy Test - Procedure
Verify that the EE can reach a desired position within the accuracy specified by DR#
Attach pearl markers to the EE and base coordinate frame
Command EE to a position within the arm's range of motion
Use VICON to measure the EE's position over time
Feed VICON data plus an error back into the control system to simulate the primary sensor data
Repeat test until statistical significance is achieved, varying the EE position each time
Subtract the commanded position from the VICON data in the base frame to obtain errors
Run arm simulation using tested commands and compare data
Notes: Add picture

## Slide 69: Pixy2 Accuracy Test - Procedure
Verify that the Pixy 2 can calculate the GP's spin rate with accuracy specified by DR 2.3.1
Notes: Add picture

## Slide 70: Spin Axis Alignment
MATLAB simulation incorporating error in measurements.
Measured X,Y,Z position from AR tags and intel
Black circle is true path of the AR tags on the GP
Path of AR tags on solar panel
Top View

## Slide 71: Spin Axis Alignment
MATLAB simulation incorporating error in measurements.
Calculated Spin Axis
Actual Spin Axis
Side View
Measured X,Y,Z position from AR tags and intel
Black circle is true path of the AR tags on the GP
Notes: Create: Cedric
Present: Sheridan
Example of the data Matlab will get from the intel sensing the AR tags, the blue dots are all XYZ position data pulled from the AR tags. These points are then averaged to get centroid location. A "best fit" plane is then found based on this centroid and the data points, and the spin axis is assumed to be the vector normal to this plane through the centroid
Accuracy plots are in backup slides

## Slide 72: Secondary Sensor + EE Spin Up Test - Procedure
Validate that we can spin up the EE such that it's rate and phase match that of the GP using data from the PIXY2 secondary sensor within the accuracy specified by DRs # and #
Notes: Add picture

## Slide 73: Secondary Sensor + EE Spin Up Test Status: Incomplete
Validate that we can spin up the EE such that it's rate and phase match that of the GP using data from the PIXY2 secondary sensor within the accuracy specified by DRs # and #
Expected Result: The control law in combination with feedback from the secondary sensor will match the rotation of the GP within the bounds specified by DRs # and # after N seconds
Concerns: The acceleration of the wrist actuator may render our control law ineffective.
Notes: Add picture

## Slide 74: Primary Sensor + Controlled Motion Test - Procedure
Validate that we can control the position of the EE using data from the primary sensor with the accuracy required by DR #
Attach pearl markers to the EE and base coordinate frame
Command EE to a position within the arm's range of motion, utilizing position data from the Intel D435 as feedback
Use VICON to measure the EE's position over time
Repeat test until statistical significance is achieved, varying the EE position each time
Subtract the commanded position from the VICON data in the base frame to obtain total errors
Subtract Intel D435 measurements from VICON measurements to obtain sensor errors
Run arm simulation using tested commands and compare data
Notes: Add picture

## Slide 75: Primary Sensor + Controlled Motion Test Status: Incomplete
Validate that we can control the position of the EE using data from the primary sensor with the accuracy required by DR #
Expected Result: The control law in combination with feedback from the primary sensor will reach the commanded position within the bounds specified by DR#
Concerns: We may encounter high settling times that require extensive tuning of the control system to fix
Notes: Add picture

## Slide 76: Full Integration Testing Procedure
1. Mount arm to GSE
2. Computer plugged into arm
3. Power plug in / Emergency off ready
4. ROS and controls ready
5. Cameras on
6. Actuate arm to starting position
7. Spin up GP
8. Track AR tags using Intel D435
9. Actuate arm
10. Switch to Pixy 2 at 3" from GP to tip of EE
11. Determine spin rate
12. Spin up EE
13. Switch back to Intel
14. Actuate arm forwards
15. Force sensors determine binary grapple
16. Magnets fail or system shut down
17. Power off

## Slide 77: GP Location Estimation Test - Procedure
Verify that the errors introduced by transferring data between the primary and secondary camera frames is less than that specified by DR#
Notes: Add picture

## Slide 78: Sensor Transfer Test - Procedure
Verify that the errors introduced by transferring data between the primary and secondary camera frames is less than that specified by DR#
Notes: Add picture

## Slide 79: Sensor Transfer Test Status: Incomplete
Verify that the errors introduced by transferring data between the primary and secondary camera frames is less than that specified by DR#
Notes: Add picture

## Slide 80: Uncontrolled Accuracy Test - Procedure
Determining how accurately the EE arrives at a commanded position before applying the control law
Attach pearl markers to the EE and base coordinate frame
Command EE to a position within the arm's range of motion
Use VICON to measure the EE's position over time
Repeat until statistical significance is achieved, varying the EE position each time
Subtract the commanded position from the VICON data in the base frame to obtain errors
Notes: Add picture

## Slide 81: Uncontrolled Accuracy Test Status: Incomplete
Determining how accurately the EE arrives at a commanded position before applying the control law
Expected Result: There will be significant errors between the measured and commanded positions. These errors are likely to be biased in the direction of the force of gravity acting on the arm.
Concerns: It will be difficult to determine how much of the error is caused by the inverse kinematics and how much is caused by the actuators.
Notes: Add picture

## Slide 82: Arm Thermal Test - Procedure
Verify the arm can remain actuated at 90° for at least 255 seconds.
Calibrate actuators
Command arm to hold the base actuator at 90° and all others at 0°
Hold this position until actuator thermal failure or until 10 minutes have elapsed.
Notes: Add picture

## Slide 83: Intel D435 Accuracy Test - Procedure
Verify the Intel's measurement accuracy
Notes: Add picture

## Slide 84: Full System Test
Verify the system can grapple the spinning mock solar panel.
Purpose: Run full system to
check level of success.
Facility: N.A.
Equipment: Fully assembled test bed
Assembled arm and GP
Test computer
Measure: Level of success
Notes: Add picture
Sheridan