## Slide 1
Advisor: Morteza Lahijanian Customer: Penina Axelrad (CCAR)
Senior Projects Team: Adam Boylston, Adrian Perez, Andrew Pfefer, Bao Tran, Ben Hagenau, Cameron Baldwin, Ian Thomas, Mathew van den Heever, Max Audick, Tanner Glenn, Ted Trozinski, Zhuoying Chen
FOR
Notes:   Make sure to introduce everyone…..

## Slide 2: Objectives
VISION is a working prototype device that will monitor CubeSats from a launch provider as they deploy. VISION will deliver timely Two-Line Elements which will reduce the time between deployment and identification and eliminate ambiguity amongst CubeSats.
Mission Statement:
Project VISION will improve Space Situational Awareness (SSA) by developing an in-situ, autonomous prototype that tracks and estimates individual CubeSat trajectories during deployment.
Notes: Feel free to reword

## Slide 3: Concept of Operation: Mission Overview
2
CubeSat TLE, state estimates
Deployer
VISION
Ground
Based Tracking
Systems
0: Launch
1: Dormant
3: CubeSat Deployment
4: Data Collection
2: Boot and Calibration
7: Data Relay
to Ground
8: Ground Tracking of Deployed CubeSat
6: Data Transfer to
Launch Provider
5. Data Processing
Deployed CubeSat
Deployer Orbit
CubeSat Orbit
Notes: Don’t animate and just throw it up

## Slide 4: VISION Team CONOPS
State Estimation
Calculate Orbital Elements
Generate TLEs
Sensor Data
Collection
Simulated
Sensor Data
Generation
Truth Data:
(SPG4)
Truth Data:
ASPEN Lab Vicon
Compare
Compare
VISION SYSTEM
Centroid Identification
Initial Conditions
Notes: Redo slide and focus on this
Break into we have software and hardware -> at a highlevel this is what we are doing in our project and how we will validate
Distinguish between us and vantage
For sure re-do this
Add ticker based on this slide

## Slide 5: Changes from VANTAGE (2018/19 Senior Project)
Integration of Subsystems
  Single power source
  PCB: Soldered-in components
  Raspberry Pi used to power/control
  Fully autonomous system
State Estimation Software  TLEs
  Implemented nonlinear batch filter
New Structure/Chassis
  Reduced size by 45%
  Complete design rework
  New external mounting mechanism
Simulation
  Non-linear CubeSat trajectories
Integrated GPS
  Attitude/Position determination
Testing
  Centroid detection
  Vibrational/Shock testing of chassis
    Advanced NASA TRL
Notes: Replace with visual representation

## Slide 6: Levels of Success
Level 1 | Level 2 | Level 3
All components fit within volumetric constraints of a chassis Mechanical Interface with NanoRacks Deployer | Chassis certified TRL-4 | Chassis certified TRL-5 Interfaces with multiple deployers
TLEs using known state data | TLEs using simulated optical data & attitude data | TLEs using experimental optical and deployer inertial state data
Stores raw sensor data | Store raw & processed data for 1 deployment | Electronics have a space-grade counterpart
Communicates data over interface | Flight software assigns markers & coordinate system | Integrated simulation and physical tests

## Slide 7: Critical Project Elements

## Slide 8: Critical Project Elements
  Software Simulation
    Simulate sensor data inputs in relevant environment
  Sensor Data Collection
    Automated data collection of sensors: TOF, Monochrome, GPS
  Data Processing
    Determine centroid positions and filter relative states
  TLE Estimation
    Deliverable to enable integration with existing SSA solutions
Notes: What is sensing? What are we processing? Why the software Simulation? Here is the end result….

## Slide 9: Functional Block Diagram
Notes: Keep?

## Slide 10: Design Overview

## Slide 11: Structural Overview
VISION
Deployment
System
CubeSat

## Slide 12: Structural Design Overview
Parameter | Dimension
Material | Al 7075
Mass | 3.27 kg
Vol | 5,204.1 cm³
Length | 38.16 cm
Height | 13.8 cm
Width | 11.1 cm
GPS Antenna
TOF Camera
Monochrome Camera

## Slide 13: Structural Overview
Notes: Could keep

## Slide 14: Electronics Overview – Telemetry System
Raspberry Pi
Intel NUC
Monochrome Camera
GPS
ToF camera
Deployer/Simulated PC
1. Before Launching CubeSats
2. Launch CubeSats
Sensors: Collect Data
NUC : Processing -> Transferring -> Turn off Automatically
3. Raspberry Pi: Transfer results to Deployer
Notes: Could

## Slide 15: Software Overview
TLE Calculation
TOF Data Collection
Optical Data Collection
TOF Data Processing
Image Processing
Relative State Estimation
Centroid Determination
State Estimation
TOF Centroids
Optical Centroids
CubeSat Relative State
Start
Deployer Inertial State
Inertial State Estimation
Orbital Element Estimation
CubeSat Inertial State
Assemble TLE
Deliver TLE
NORAD Designator
CubeSat Parameters
VANTAGE
VISION
End
Legend
Process
Input/
Output
Notes: We use centroids to estimate relative orbital states which are combined with the deployer inertial state to obtain in inertial estimates for each cubesat. These inertial estimates are then converted to orbital elements which make up the bulk of each TLE.

## Slide 16: Test Overview

## Slide 17: Testing Overview
TOF Camera Verification
GPS Verification
Avionics Voltage Breakdown
Vibrational Analysis Test
Centroid Determination Test
Attitude Test
Avionics Power System Test
State Estimation Verification
System Integration Test
Power: Hardware operation
Chassis: Increase TRL and survive a launch
Inertial Position: Proof of Concept for a SmallSat solution
State Estimation: Produces TLE
Subsystem Level
Component Level
System Level
Power
Chassis
Inertial State
State Estimation
Avionics Voltage Breakdown
Avionics Power System Test
State Estimation Verification

## Slide 18: Avionics Voltage Breakdown and Power Tests
Design Req.​ | Summary​
DR 4.2 ​ | The system shall operate with no more than 120VDC, 3Vpp ripple voltage, and 5A.​
DR 4.3​ | The system shall draw no more than 520 Watts.​
TOF Camera Verification
GPS Verification
Vibrational Analysis Test
Centroid Determination Test
Attitude Test
State Estimation Verification
System Integration Test
Subsystem Level
Component Level
System Level
Chassis
Inertial State
State Estimation
Avionics Voltage Breakdown
Avionics Power System Test
Power
Purpose:
  Avionics Voltage Breakdown Test:
    Verifies all output voltages are compatible with individual sensors
  Avionics Power System Test:
    Verifies the system can operate 15 min (one deployment cycle) under given wattage without damages on sensors and converters.

## Slide 19: Avionics Voltage Breakdown and Power Tests
PCB
(24-5V) & (24-12V) DC/DC
300 VDC Power Supply
Current Limit = 4 A
120V * 4A = 480 W
Oscilloscope
120-24
DC/DC
TOF Sensor
Breadboard Circuit
(24-5V) & (24-12V) DC/DC
Intel NUC
Raspberry Pi
GPS Receiver
Monochrome Camera
120 V
120 V
24.0 V
24.9 V
20.4-28.4V
5.0 V
4.8 V
4.7 – 5.2V
12.0 V
12.3 V
12-24V
GREEN - Expected Results
RED - Actual Results
PURPLE - Acceptable voltage range
Raspberry Pi
Intel NUC
Notes: Step through with animations and add information about acceptable voltage range and the power restrictions. How did we measure these things?

## Slide 20: Vibrational Analysis Test
TOF Camera Verification
GPS Verification
Avionics Voltage Breakdown
Centroid Determination Test
Attitude Test
Avionics Power System Test
State Estimation Verification
System Integration Test
Subsystem Level
Component Level
System Level
Power
Inertial State
State Estimation
Purpose:
  Verifies the chassis’ ability to survive a launch
  Component testing in relevant environment
  Information on environmental requirements for ICD
Design Req.​ | Summary​
DR-6.1 | Chassis structure shall reach an advanced TRL certification, or equivalent.
DR-6.2 | Chassis structure shall maintain structural integrity within a safety factor of 2.
TOF Camera Verification
GPS Verification
Avionics Voltage Breakdown
Centroid Determination Test
Attitude Test
Avionics Power System Test
State Estimation Verification
System Integration Test
Vibrational Analysis Test
Chassis

## Slide 21: Vibrational Analysis Test
Determine eigenfrequencies for vibe table force analysis
Test chassis in relevant environment to increase TRL
Also test NanoRacks acceleration spectral density (ASD) profile for launch environment
Mode: | 1 | 2 | 3 | 4 | 5
Frequency (Hz) | 887.73 | 926.21 | 1020.9 | 1044.1 | 1132

## Slide 22: Centroid Determination Test
GPS Verification
Avionics Voltage Breakdown
Vibrational Analysis Test
Attitude Test
Avionics Power System Test
State Estimation Verification
System Integration Test
Subsystem Level
System Level
Component Level
Design Req.​ | Summary​
DR-1.1​ | VISION shall characterize and differentiate up to 6 CubeSats of 1U and up to 3U sized CubeSats.​
DR-1.2​ | VISION shall estimate the centroid of each CubeSat of 1U up to 3U size​
Centroid Determination Test
Centroid Determination
TOF Camera Verification
Purpose:
  Verifies VISION’s capability to determine a centroid for up to 6 CubeSats in order to perform state estimation

## Slide 23: Centroid Detection Test Overview
Single Body Static Test
Orient CubeSat at known distance
Determine centroid
23
Multi-Body Static Test
Orient mock CubeSats
Determine centroid of each CubeSat
Determine system centroid
Sensor Suite
3D Printed CubeSat
Notes: Needs better narration, explain place, what we are VALIDATING
This is what is required,
Conduct this test to verify cameras are accurate, and giving appropriate inputs to the filter so that it is

## Slide 24: Centroid Detection Test: Expected Results
Potential Risks:
Monochrome capturing more than deployed CubeSats (ie. rail system, walls, external IR noise)
Software cannot identify CubeSats
Possible Solutions:
Dark blankets, different lighting to shade areas of room
Dynamically or manually crop sensor data
Sensor Suite
3D Printed CubeSat
Notes: These results are a sample data set of VANTAGE's modular test, we expect similar results. First animation: raw sensor data, second: centroid position of one cubesat over time, third: a table of average error, fourth: concerns and possible solutions
POTENTIAL SCRUB

## Slide 25: State Estimation Test
Req. | Summary
DR-2.2 | VISION shall estimate the inertial position of each CubeSat such that the STD conforms to the Inertial Position Uncertainty Map.
DR-2.6 | VISION shall produce Two-Line Elements that can be propagated using the SGP4 propagation tool.
TOF Camera Verification
GPS Verification
Avionics Voltage Breakdown
Vibrational Analysis Test
Centroid Determination Test
Attitude Test
Avionics Power System Test
System Integration Test
Subsystem Level
Component Level
System Level
State Estimation Verification
Notes: Goal of state estimation testing is to validate accuracy requirement to ensure estimates are useful when predicting where cubesats will be and being able to produce TLE

## Slide 26: State Estimation: Test Procedure
Orbit Simulation
C4D/Blensor
Centroid
Determination
State Estimation
Algorithm
Test Procedure
Centroids
TOF Point Clouds
Truth Motion
Notes: For these test we use simulated sensor data so we can model the expected dynamics.
Truth orbital data -> sensor modelling -> centroids -> filtering

## Slide 27: State Estimation: Test Procedure
Orbit Simulation
C4D/Blensor
Centroid
Determination
State Estimation
Algorithm
Test Procedure
Centroids
TOF Point Clouds
Truth Motion
Notes: Simulating truth data in all frames

## Slide 28: State Estimation: Test Procedure
Orbit Simulation
C4D/Blensor
Centroid
Determination
State Estimation
Algorithm
Test Procedure
Centroids
TOF Point Clouds
Truth Motion
Notes: Visually simulating cubesat deployment using true orbital data

## Slide 29: State Estimation: Test Procedure
Orbit Simulation
C4D/Blensor
Centroid
Determination
State Estimation
Algorithm
Test Procedure
Centroids
TOF Point Clouds
Truth Motion
Notes: Simulate TOF raw measurements using visual simulation

## Slide 30: State Estimation: Test Procedure
Orbit Simulation
C4D/Blensor
Centroid
Determination
State Estimation
Algorithm
Test Procedure
Centroids
TOF Point Clouds
Truth Motion
Notes: Compute centroids from simulated centroid data

## Slide 31: State Estimation: Test Procedure
Orbit Simulation
C4D/Blensor
Centroid
Determination
State Estimation
Algorithm
Test Procedure
Centroids
TOF Point Clouds
Truth Motion
Notes: Using centroids to estimate Cubesat motion

## Slide 32: State Estimation: Test Overview
Orbit Simulation
C4D/Blensor
Centroid
Determination
State Estimation
Algorithm
Test Procedure
Verification and Validation
Estimates and Covariance (DR-2.2)
Centroids
TOF Point Clouds
Truth Motion
Notes: Comparing filter results to truth data produced by orbit sim yields error on each axis and overlaid with filter covariance. The errors and covariance for the relative positions of an example run on each axis is shown here.
Compare covariance to uncertainty requirements map. Combinations of alongtack and cross plane uncertainties that reside in green region mean that estimates sampled from this distribution can be propagated accurately enough to be trackable by ground stations. Everything outside the green region cannot be.

## Slide 33: State Estimation: Performance Results
Req. | Summary
DR-2.2 | VISION shall estimate the inertial position of each CubeSat such that the STD conforms to the Inertial Position Uncertainty Map.
 | Along-track σ [m] | Cross-plane σ [m]
Max | 0.31 | 0.29
Min | 0.02 | 0.01
Notes: Using out preliminary data sets re observed results in the purple region. Each point in this region corresponds to uncertainties produced by the filter shown in this plot. We observed max erros of 0.31 and 0.29 m in the along track and crossplane.

## Slide 34: State Estimation: Performance Results
Req. | Summary
DR-2.2 | VISION shall estimate the inertial position of each CubeSat such that the STD conforms to the Inertial Position Uncertainty Map.
 | Along-track σ [m] | Cross-plane σ [m]
Max | 0.31 | 0.29
Min | 0.02 | 0.01
Notes: Using out preliminary data sets re observed results in the purple region. Each point in this region corresponds to uncertainties produced by the filter shown in this plot. We observed max erros of 0.31 and 0.29 m in the along track and crossplane.

## Slide 35: State Estimation: Test Overview
Orbit Simulation
C4D/Blensor
Centroid
Determination
State Estimation
Algorithm
Test Procedure
Verification and Validation
Run Time (DR-2.7)
Estimates and Covariance (DR-2.2)
Two-Line Elements (DR-2.6)
SPG4 Orbit Propagation
Centroids
TOF Point Clouds
Truth Motion
Notes: Now we validate that we can build TLE using the information we have. And then check that they can be propagate by the standard propagation method. We didn’t get to this but did propagate with 2-body and J2.

## Slide 36: State Estimation: Two-Line Element Results
1
Sat. #
INC
Epoch
RAAN
ECC
nd
ndd
BStar
Type
El. #
sum
AOP
M
n
Rev. #
sum
2
Req. | Summary
DR-2.6 | VISION shall produce Two-Line Elements that can be propagated using the SGP4 propagation tool.
Notes: TLE are composed of many quantities and we will only go into detail about the properties we are directly estimating.

## Slide 37: State Estimation: Two-Line Element Results
1
Sat. #
INC
Epoch
RAAN
ECC
nd
ndd
BStar
Type
El. #
sum
AOP
M
n
Rev. #
sum
2
Notes: These properties are designation numbers and drag parameters that will be know prior to launch for each cubesat

## Slide 38: State Estimation: Two-Line Element Results
1
Sat. #
INC
Epoch
RAAN
ECC
nd
ndd
BStar
Type
El. #
sum
AOP
M
n
Rev. #
sum
2
Deployment Epoch
Notes: The first property we handle is the epoch associated with the sate in the TLE which we obtain from time stamps collected during deployment.

## Slide 39: State Estimation: Two-Line Element Results
1
Sat. #
INC
Epoch
RAAN
ECC
nd
ndd
BStar
Type
El. #
sum
AOP
M
n
Rev. #
sum
2
Deployment Epoch
Semi-Major Axis
µ: 2.0 [m]
σ: 1.4 [m]
Eccentricity
µ : 2.4e-7
σ: 1.8e-7
Inclination
µ : 3.2e-7 [deg]
σ: 1.7e-7 [deg]
RAAN
µ : 6.9e-7 [deg]
σ: 3.7e-7[deg]
AOP
µ : 2.3e-4 [deg]
σ: 5.2e-4 [deg]
True Anomaly
µ : 2.3e-4 [deg]
σ: 5.2e-4 [deg]
Notes: The bulk of the TLE that we estimate are the orbital elements at that epoch that are produced from relative state estimates. We gathered statistics on the error in these quantities for the data that we have. The most important item is the error of the semi-major axis which is extremely sensitive to velocity. During development we reduced the error in this quantity by changing how we handled velocity inside the filter and adjusting tuning parameters.

## Slide 40: State Estimation: Propagation Results
Notes: In order to study propagation error in more detail we propagated the estimates forward in time. This figure shows the total propagation error and the uncertainty associated with it for a semi-major axis error of 1.27 meters. This Is an important value because SMA error causes a difference in orbital period and produces the secular drift observed here that accounts for the majority of propagation error growth with time.

## Slide 41: State Estimation: Propagation Results
Propagation Error Statistics
Take Away:
Average is 46.7 % better than typical error for NanoSat TLE. (Celestrack)
SMA is extremely sensitive to velocity errors.
Propagation error secular drift is a product of error in SMA
Tuning is sensitive to initial guess accuracy. (assumed accurate)
Average Propagation Error [m/day] | Standard Deviation [m/day]
302 | 220
Notes: We compared our results to the standard propagation error associated with smallsat TLE from celestrack which is on the order of 1000 to 2000 m/day. Using the data sets we had we observed an average 46% increase in accuracy. We also learned that SMA is sensitive to velocity and drives propagation error. Adding velocity measurements would improves results significantly (currently only using position estimates). With more information about the deployment velocity uncertainty, the filter can be tuned for each mission.

## Slide 42: System Integration Test
Req. | Description
DR-2.7 | VISION shall deliver TLE estimates within fifteen minutes after the end of the deployment period.
DR-3.1 | VISION Shall deliver a still image of each CubeSat in a deployment.
DR-4.4 | VISION Shall store all data gathered for the duration of the deployment period.
TOF Camera Verification
GPS Verification
Avionics Voltage Breakdown
Vibrational Analysis Test
Centroid Determination Test
Attitude Test
Avionics Power System Test
Subsystem Level
Component Level
System Level
State Estimation Verification
System Integration Test
Notes: Going to run through

## Slide 43: System Integration Test: Expected Results
Show full integration of VISION as a single package
Autonomous functionality after initialization
Test accuracy and uncertainty profiles of real sensors and state estimation software integration

## Slide 44: System Integration Test Overview
Overview of Test:
8 m
Compare

## Slide 45: System Integration Test Overview
Overview of Test:
8 m
Compare

## Slide 46: System Integration Test
Phase 1: Boot Up and Ready
Provide power to all components
Verify avionics are operational
System ready to collect data
Expected Results:
Validate Avionics Power System Test
results
 | NUC | Raspberry Pi | TOF
Required Range | 12-24 V | 4.7-5.2 V | 20.4-28.4 V
Measurement | 12.3 V | 4.8 V | 24.9 V
Notes: Show expected results are what we got in modular testing,

## Slide 47: System Integration Test
Phase 2: Data Capture and Centroid Detection
CubeSats move along track
Identify and track CubeSats
Capture data for 10 meters
Expected Results
Validate results from Centroid Determination Test
Notes: Show expected results are what we got in modular testing,

## Slide 48: System Integration Test
Notes: Show expected results are what we got in modular testing,

## Slide 49: System Integration Test
Phase 3: State Estimation
Quantify Noise Profile of sensor input
Assess automation/integration
of state estimation
Expected Results
Demonstrate filter improves relative
velocity estimates
Tune Filter
Notes: Show expected results are what we got in modular testing,

## Slide 50: System Integration Test
Notes: Show expected results are what we got in modular testing,

## Slide 51: System Integration Test
Phase 4: Communication and Final Results
Deliver Still Images
Verify TLEs were delivered in under
15 minutes
Expected Results:
Pictures of deployed CubeSats and
estimates delivered in under 15 minutes
Notes: Show expected results are what we got in modular testing,

## Slide 52: System Integration Test Overview
< [mm]
accuracy

## Slide 53: System Integration Test Results: Uncertainty Profile
3. Anderson-Darling Test
2. Compute Error In Centroids
1. Collect Centroids For Many Tests
4. Compute Standard Deviation Using all Error
Expected Results (from VANTAGE data)
  ~80% gaussian with 95% significance
  0.03 [m]
  [m]
  [m]

## Slide 54: Systems Engineering

## Slide 55: Systems Engineering Tools
Requirements Traceability Matrix
  Compliance, Req. Flowdown, Testing Methods, Validation Tracking, Version Control
Master Equipment List
  Subsystem Components, System Mass Tracking, Mass Contingency Value, Power Consumption
Risk Mitigation Matrix
  Major Risk, Severity & Probability, Mitigation Paths
Testing Req’s Allocation List
  Component Level Validation, Design Req. Allocation, Level of Success Tracing
Trade Study Tables
  Weighted Design Decisions, Sensitivity Analysis, Quantitative Design Analysis

## Slide 56: Verification & Validation Process
Dr. Axelrad Requirements
Centroid Detection & State Estimation Algorithm Design
Sensor Suite & Avionics Design
System Specification
State Estimation Requirements
Build Components & Software
System Integration Test
Test Centroid Detection & State Estimation
Test Components
System Integration
Compiling Software on NUC
Validation
System Integration Verification
Verification thru Simulation
Detail Design Verification
Unit Code Testing & Verification

## Slide 57: System Engineering Challenges & Issues
Risk: Hardware Failure
  Critical Components = $$$
  Made design decisions to allow for budget allocation
  Instances with high probability of component failure (PCB & TOF Camera)
Risk: Estimate Error
  Confidence in Measurements that don't match Estimate Error
  Expected Mitigation: Normalized Estimate Error Squared (NEES)  Uncertainty matches Error (Tuning the Filter)
  Results: COVID-19, confidence in uncertainty results not achieved
Key Lessons: Continuing Heritage Project
  Replicating results took more time than expected
  Offset between code
  Communication with heritage team members was difficult:
    TOF Code
    Simulation Code/Software Parameters
  Actions moving forward: Creating documentation of code parameters, functions, results, potential error, ICDs, system needs

## Slide 58: Trade Studies
Subystem/Component Quantitative Trade Study Table |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Internal |  |  | External |  |  | Tube Replacement |  |  | Modular |  | 
Metric | Weight | Performance | Score | Points | Performance | Score | Points | Performance | Score | Points | Performance | Score | Points
Required Volume | 10% | 5 | 0 | 0 | 10 | 10 | 1 | 10 | 10 | 1 | 5 | 0 | 0
Tolerancing/Manufacturability | 5% | 3 | 0 | 0 | 5 | 10 | 0.5 | 5 | 10 | 0.5 | 4 | 5 | 0.25
Development Time | 20% | 8 | 10 | 2 | 3 | 2.86 | 0.57 | 4 | 4.29 | 0.86 | 1 | 0 | 0
Universality | 20% | 9 | 8.57 | 1.71 | 4 | 1.42 | 0.28 | 3 | 0 | 0 | 10 | 10 | 2
Structural Integrity | 15% | 8 | 6.67 | 1.00 | 8 | 10 | 1.5 | 8 | 10 | 1.5 | 6 | 0 | 0
Opportunity Cost | 15% | 2 | 1.11 | 0.17 | 10 | 10 | 1.5 | 1 | 0 | 0 | 6 | 5.56 | 0.83
Thermal Management | 15% | 2 | 0 | 0 | 10 | 10 | 1.5 | 10 | 10 | 1.5 | 7 | 6.25 | 0.94
Wt. Total | 100.00% |  |  | 4.88 |  |  | 6.86 |  |  | 5.36 |  |  | 4.02
External Mounting/Interface
  Drove structure design
  Produced cheaper cost to deployer (Cubesat = $20k)
  More freedom to dictate volume
Onboard Processing Board
  Have experience with NUC model
  Provided storage space with margin
  Handles processing of Python/Matlab code
State Estimation Software
  Kalmann Filter initially selected
  Switched to Non-Linear Batch Filter
  Trade studies are performed with best of knowledge, but not concrete
Embedded System Trade Table |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | Nividia Jetson Nano |  |  | Intel NUC8I7BEH |  |  | Intel NUC8I7HNK |  |  | Intel NUC8I7HVK |  | 
Metric | Weight | Performance | Score | Points | Performance | Score | Points | Performance | Score | Points | Performance | Score | Points
Integration | 15% | ~ 4 [Weeks] | 5 | 0.75 | ~ 2 [Weeks] | 7.5 | 1.125 | ~ 2 [Weeks] | 7.5 | 1.125 | ~ 2 [Weeks] | 7.5 | 1.125
Performance | 30% |  | 5.4 | 1.62 |  | 4.566666667 | 1.37 |  | 6.8 | 2.04 |  | 6.8 | 2.04
RAM | 10% | 4 GB | 1.3 | 0.13 | 32 GB | 10 | 1 | 32 GB | 10 | 1 | 32 GB | 10 | 1
GPU Rank | 10% | 240 | 4.9 | 0.49 | 293 | 3.7 | 0.37 | 116 | 7.5 | 0.75 | 98 | 7.9 | 0.79
Benchmark CPU | 10% | 5732 | 10 | 1 | 3661 | 0 | 0 | 4271 | 2.9 | 0.29 | 4181 | 2.5 | 0.25
Storage Capabilities | 10% | 16 GB | 1.3 | 0.13 | >128 GB | 10 | 1 | >128 GB | 10 | 1 | >128 GB | 10 | 1
Heat Generation | 15% | 10 W | 10 | 1.5 | 28 W | 8 | 1.2 | 65 W | 3.9 | 0.585 | 100 W | 0 | 0
Power Consumption | 10% | 20 W | 9.2 | 0.92 | 78 W | 7 | 0.7 | 230 W | 1.2 | 0.12 | 212 W | 1.8 | 0.18
Interchangeability | 20% |  | 2 | 0.4 |  | 6 | 1.2 |  | 6 | 1.2 |  | 6 | 1.2
Wt. Total | 100.00% |  |  | 5.32 |  |  | 6.595 |  |  | 6.07 |  |  | 5.545
State Estimation Method Quantitative Trade Study Table |  |  |  |  |  |  |  |  |  |  | 
 |  | Weighted Least Squares |  | Recursive Least Squares |  | Classical Kalman Filter |  | Extended Kalman Filter |  | H_infinity Filter | 
Metric | Weight | Score | Points | Score | Points | Score | Points | Score | Points | Score | Points
Robustness | 30% | 1 | 0.3 | 1 | 0.3 | 3 | 0.9 | 4 | 1.2 | 5 | 1.5
Optimizability | 20% | 3 | 0.6 | 2 | 0.4 | 4 | 0.8 | 4 | 0.8 | 5 | 1
Learnability | 30% | 5 | 1.5 | 4 | 1.2 | 3 | 0.9 | 2 | 0.6 | 1 | 0.3
Computational Expense | 20% | 3 | 0.6 | 5 | 1 | 4 | 0.8 | 3 | 0.6 | 2 | 0.4
Wt. Total | 100.00% |  | 3 |  | 2.9 |  | 3.4 |  | 3.2 |  | 3.2

## Slide 59: Project Management

## Slide 60: Project Management
Traditional/Waterfall approach
  Initiation
    Systems Engineering
      Requirement development from customer wants/needs
    Team Development
      Subgroup teams built based on technical skill set
  Planning
    Design based on Requirements
      Heritage project completion with added features
  Executing
    Manufacturing
    Software automation/development
  Controlling
    Monitoring and Scheduling
    Testing and Integrating
  Closing
    V & V
      Closing the project with successful demonstration and reporting
Initiation
Planning
Executing
Controlling
Closing

## Slide 61: Management Takeaways
Teams
Team Building
Subgroup Building
Flexibility
Phases
Meetings
Preparation
Feedback
Schedule
Leads
Based on Skills/Desires
Based on major functions of project
Phases require varied managerial execution
Allow for subgroup execution
Varying frequency and duration through phases
Size and duration vary through phases as well
Self Chosen Roles
Phase Breakdown
Established realistic goals
PAB member reviews
Inter-project communication
PM chatter
Gantt Chart
Updating regularly kept big picture in view
Difficulties
Chaotic Meetings
  Established an agenda
  Subgroup development
  Calm and positive atmosphere
Communication
  Subgroups status between groups
    Increased status updates in meetings and action items

## Slide 62: Budget analysis
Item | Price
Intel NUC8i7BEH | $641.84
Aluminum Stock | $388.42
GPS Reciever and Antenna | $272.32
Cart Wheels | $156.00
PCB | $109.00
Most expensive Components Purchased:

## Slide 63: Compared Budget
$2,349.95
$4,313.66
$2,009.58
$2,304.08
Predicted Spending as of CDR
Actual Spending
Redundancy
Processor
Time of flight camera
Aluminum
Etc.

## Slide 64: “Industry” Cost
Project Hours:
  Recorded over 23 weeks
    Stopped the week of Mar 16
  Total Hours:
    3743 hrs
Entry Level Engineers
  Assumed Salary of $65k & 40hrs/week
  $31.25/hr
Cost of Manhours
  $116,968.75
Total of Materials
  Heritage Costs
    $2,772.00
  Material Costs
    $2,349.95
  Assume 200% Overhead
Total Industry Cost:
$116,968.75 (Manhours)
+$15,578.85 (Materials)
$132,547.60

## Slide 65: Backup Slides

## Slide 66: State Estimation: Filter Consistency Results
Monte-Carlo Truth Model Testing
  Chi-Squared Analysis of NEES: (normalized estimation error squared)
  Control Variable: [] -> dependent on initial guess error
Initial Position Estimate Error and Covariance
Take Away:
  Filter is tunable to produce statically significant results.
  Further refine based on knowledge of initial state.
  More Monte-Carlo data sets.
Notes: Estimation is a balancing act. There are many means to changing how the estimator weights measurements and nominal measurements to produce estimates and with an accurate level of confidence.
Tie back to needing white noise as an input

## Slide 67: Avionics Power Test - Still

## Slide 68: Electronics – Power Distribution Board

## Slide 69: GPS Verification and Attitude Determination Test
Purpose
  GPS Verification: Verifies the GPS can provide an inertial position
  Attitude Test: Verifies the method used to estimate VISION’s attitude
Req. | Description
DR-2.3 | The VISION system shall measure its own single axis inertial attitude using a civilian grade Global Positioning System.
DR-2.4 | The VISION system shall measure its own inertial position using a civilian grade Global Positioning System.
TOF Camera Verification
GPS Verification
Avionics Voltage Breakdown
Vibrational Analysis Test
Centroid Determination Test
Attitude Test
Avionics Power System Test
State Estimation Verification
System Integration Test
Subsystem Level
Component Level
System Level
Power
Chassis
Inertial State
State Estimation
Notes: In order to determine orbits, independent of the deployer, etc, be honest, conceptually, gps to know position, not accurate enough, level 3, put the structure together, feasibility analysis, not going to develop testing etc, COVID interrupted this, platform for further growth

## Slide 70: GPS Verification and Attitude Determination Test
Justification:
Must know pointing of cameras
Testing capability to provide attitude and position
Req. | Description
DR-2.3 | The VISION system shall measure its own single axis inertial attitude using a civilian grade Global Positioning System.
DR-2.4 | The VISION system shall measure its own inertial position using a civilian grade Global Positioning System.
α
α
1
2
Boresight Vector
“Ground” Plane
Antenna
Boresight Vector
Notes: PROBABLY TAKE OUT