## Slide 1
Offset S-duct PRopulsion Inlet
Team:
Tim Breda
Joey Derks
Zak Dmitriyev
Ryan Joseph
Dishank Kathuria
Harrison Methratta
Joshua Seedorf
Michael Vogel
William Watkins
John Wissler
Advisor: Professor John Mah
Customer: Air Force Research Laboratory
POC: Capt. Riley Huff

## Slide 2: Purpose and Objectives Section 1
Design Satisfaction
Project Risks
Design Solutions
Project Planning
Project Purpose
Verification & Validation
Notes: Sec 1 - 6 minutes

## Slide 3
Problem Statement
The purpose of the OSPRI project is to:
Design and build an S-duct inlet for use with the JetCat P100-RX turbojet engine, for the Air Force Research Lab’s (AFRL’s) Aerospace Propulsion Outreach Program (APOP)
Additionally, OSPRI will design and build a testing apparatus to measure total pressure and distortion distributions, and measure fuel flow and thrust produced
Motivation
Integrating engines into the fuselage would reduce exposed surface area and overall drag
S-ducts are susceptible to severe flow separation and poor total pressure recovery
The Air Force Research Lab (AFRL) has asked 12 schools to come up with potential solutions

## Slide 4: Functional Requirements
OSPRI functional requirements stem from the APOP’s Statement of Work provided to the CU Aerospace Engineering Department and the OSPRI team:
Design, build, and validate an S-duct inlet for use with the JetCat P100-RX turbojet engine that performs according to AFRL’s objectives.
Design, build, and validate a test rig capable of measuring critical inlet performance metrics and inform inlet design.

## Slide 5: Inlet Design Requirements
The inlet shall interface with the AFRL transition piece.
The nearest outside edge of the capture area shall have a 6-inch offset from the centerline of the engine.
The inlet shall have a total pressure recovery ≥98% across the RPM sweep of the engine.
The maximum thrust decrement of the engine shall be ≤5% while the inlet is attached.
The maximum TSFC increment of the engine shall be ≤5% while the inlet is attached.
The inlet shall have an axial length between 20 inches and 28 inches, with the objective being 20 inches (or shorter, if feasible).*
  Requirements changed from PDR

## Slide 6: Test Apparatus (TA) Design Requirements
The TA shall be capable of mapping the total pressure distribution at the inlet entrance, the Aerodynamic Interface Plane (AIP), and between the first and second turns, at a minimum.
The TA shall be capable of mapping the distortion distribution throughout the inlet.
The TA shall be capable of measuring key JetCat engine parameters.
  TA shall be capable of measuring the thrust produced by the engine.
  TA shall be capable of measuring the Thrust Specific Fuel Consumption (TSFC) of the engine.
The TA shall be capable of interfacing with multiple different inlet designs.

## Slide 7: Concept of Operations (CONOPS)

## Slide 8: Design Solutions Section 2
Design Satisfaction
Project Risks
Project Purpose
Project Planning
Design Solutions
Verification & Validation
Notes: Sec 2 - 2 minutes

## Slide 9: Inlet Design Solution Section 2.1
Design Satisfaction
Project Risks
Project Purpose
Project Planning
Design Solutions
Verification & Validation
Notes: Sec 2 - 2 minutes

## Slide 10: Design Process
Inlet Test Matrix to compare different designs.
Major Areas of Interest:
Area Ratio Comparison (At/AE)
Length Variation
Bell-Mouth Addition
Organizes and Streamlines CAD and CFD Process

## Slide 11: Inlet Design Critical Elements
CFD:
CFD Simulations and Modelling
Flow Control:
Passive Flow Control System
Geometry and Shape:
Major aspects affecting design and performance (Bell Mouth, Length, Area Ratio)
Manufacturing:
Method of Manufacturing

## Slide 12: Inlet Area Ratio
Initial Design: Converging Diverging Duct
Area ratio comparison (At/AE)
  Area ratios analyzed 0.25, 0.5, 0.75, 0.8, 0.9, 1
  Higher area ratios resulted in less flow separation
  Higher total pressure recovery
    60.4% -> 98.2%
  Chosen AR: 1

## Slide 13: Inlet Length
Initial Estimate: 12 < x < 24 in
Lengths of 20, 22, 24, 26, and 28 inches were tested
Chosen Length: 24 in

## Slide 14: Data Point Generation
X and Y coordinates are recorded in a 2D cross-section
Geometry coordinates are then transcribed into a .txt file
MATLAB is used to convert the coordinates into a blockMesh for CFD analysis
CFD run at desired conditions

## Slide 15: CFD Setup
Set-up
  Design in CAD
  Spline Smoothed in MATLAB
  Print into openFOAM compatible .txt
Algorithm
  SIMPLE (Semi-Implicit Method for Pressure-Linked Equations)
    Navier-Stokes and divergence of the Momentum Equation for pressure
  Steady-state solution
Assumptions
  No Slip Boundaries (Walls)
  Axial Static Free-Stream flow (e.g., 25m/s +x-dir)
  Static Pressure on Compressor Face

## Slide 16: CFD Results
Fidelity
  One section is 30 vertical cells, there are 200 sections.
  Spline Smoothed in MATLAB
Results
  Increased understanding of flow behaviour through s-duct
  Understanding expected changes from manipulated variables (throat area variation, length variation, etc.)
Limitations and Further Improvements
  More realistic boundary conditions
  Finer mesh and mesh grading towards interesting areas (ie. walls)
  3D internal flow
Notes: 2D flow analysis results, assumptions made, fidelity talk, what worked and what didnt
What information we gained and what information still needs to be sought

## Slide 17: Baseline Design 1
Re#: 250,000 (Turbulent Flow)
Length: 24 inches
At/A2 ratio: 1
Bellmouth: None
Velocity Magnitude (m/s)
Relative Pressure* to Compressor Face (m^2/s^2)

## Slide 18: Baseline Design 2
Length: 26 inches
At/A2 ratio: 1
Bellmouth: None
Re#: 250,000 (Turbulent Flow)
Velocity Magnitude (m/s)
Relative Pressure* to Compressor Face (m^2/s^2)

## Slide 19: Addition of Bellmouth
Accessory for a static test
Increased mass flow rate
Half Bell Design
  Helps maintain offset length
Notes: Running with a straw vs. running with a trash bag (Hahahahaha)

## Slide 20: Manufacturing - PLA (Prototyping)
FDM
  Advantages
    Fast
  Disadvantages
    Low Resolution
      Lulzbot Mini (2.0 - 0.18 mm)
      MarkTwo (0.1-0.2mm)
        Smaller print volume
    Extensive post-processing
      Acetone vapor treatment

## Slide 21: Manufacturing - SLA (Final Design)
SLA
  Advantages
    High Resolution
      Form3B - 0.025 - 0.05 mm
    Less intensive post-processing
      Build scaffolding will be needed
  Disadvantages
    Slow
      1-2 week lead time per print

## Slide 22: Manufacturing - SLA
Standard Resin
Clear - allows for visual flow analysis
More likely to fail due to deformation
Tough 2000 Resin
No clear options
Greater capacity for flexing

## Slide 23: Manufacturing- Assembly
Inlet printed in four 6 in sections
Sections assembled together using eight 5mm bolts
Modular design provides flexibility
Bellmouth can be removed

## Slide 24: Stress and Vibration Analysis
Restrained at ends only
1st failure mode at 396 Hz
Restrained at ends and throat
1st failure mode at 986 Hz
Tests conducted with Formlabs Standard (Clear) material properties
Inlet: L = 24 in AR = 1
Free standing Static

## Slide 25: Vortex Generators
Too difficult to model in CFD
Future testing using an iterative process
  Added to baseline
  Manufactured separately
  Epoxy or tape integration
Circumferential at first bend
Compare test results with baseline to analyze difference
Add if significant pressure recovery results are shown
Example of vortex gen. placement

## Slide 26: Final Assembly

## Slide 27: Test Apparatus Design Section 2.2
Design Satisfaction
Project Risks
Project Purpose
Project Planning
Design Solutions
Verification & Validation
Notes: Sec 2 - 2 minutes

## Slide 28: Test Apparatus Design Critical Elements
Pressure Measurement:
Static tap manufacturing, integration and flow separation identification
Slotted Inlet Concept:
Slotted inlet manufacturing and testing capabilities
Mass Flow Surrogate:
Engine condition replication using Electric Ducted Fans
DAQ & EDF Control:
Data Acquisition system and EDF control setup
Notes: Presented by: Michael
Timed: 30s
The testing apparatus has 4 critical elements,
First, we will look at pressure measurement, specifically static taps.
Second will be the slotted inlet concept feasibility of manufacturing and test capabilities.
We will also look at a mass flow surrogate to replicate operating engine conditions in the inlet,
And lastly we will look at the data acquisition system and the electric ducted fan control setup.

## Slide 29: Test Apparatus FBD
Legend

## Slide 30: Test Apparatus FBD
Legend

## Slide 31: Test Apparatus FBD
Legend

## Slide 32: Data Acquisition Hardware
myRIO - 1900
PWM capabilities (3 DIO)
  100kHz, 20 ns pulse width
Analog Signal capabilities (4 AI)
  500 kS/s
ADC capabilities (1 multiplexed)
  12 bit resolution
USB / Wireless (TCP/IP) Networking
Scanivalve DS 3217
16 input channels
0 - 750 psi pressure range
Ethernet TCP/IP & UDP Networking
±.05% on 5-500 PSI measurements
Notes: Scanivalve and pitot tube rail system??

## Slide 33: EDF Model and Control
Initial Mass Flow Approximation
Assumptions:
  pe = p∞
  v∞ = 0
  constant ve across fan
Used to select an EDF
Mass Flow Control for Testing
Experimentally relate RPM to mass flow
  Simple straight inlet
  Aim to match Jetcat mass flow
Closed-Loop RPM Control
  Mass flow can be affected by inlet
    Unreliable between designs
  Method used by the Jetcat

## Slide 34: Slotted Inlet Design
Pitot tube perpendicular to inlet walls at all times
Allows for full 2D range of motion across inlet cross section
  Rail slides primarily along x axis
  Y axis adjusted up or down along length of pitot tube
x
y
z

## Slide 35: EDF Selection
E-flite: Delta V 32
80 mm
2450g of thrust
Expected mass flow
  0.36 kg/s (need 0.23 kg/s)
  Factor of safety of 1.56
  Excluding motor area
Bell mouth can be removed to interface with transition piece

## Slide 36: EDF Control and Power
Speed Controller
E-Flite recommends an 80A ESC
  Max sustained current is 53A
  Estimates motor RPM via back EMF
6 Cell LiPo
  22.2V
  22000 mah
  25 minutes of runtime
Car batteries
  Two in series provide 24.0V
  2 x 55000 mAh
  2 hours of runtime

## Slide 37: EDF Control and Power
myRIO Control
Input: Controler sets throttle using LABView GUI
Output: 50 Hz PWM, 5-10% duty cycle
Throttle
Time
Arm ESC
(4s)
Ramp Up
Ramp Down
Test Setting
Safe

## Slide 38: Test Stand Frame
Compatible with EDF tests and the JetCat test stand (without effects on the load cell)
Material: Aluminum 30x30 extrusion
Adaptable to a variety of inlets for testing (modular design)
  Different lengths, offsets, etc
  Vertical and horizontal test configurations possible
Dimensions finalized
  Parts ordered (precut from factory)
  Cost: ~$200
Transition piece holder
Inlet holder short
Inlet holder long
750 mm
483.5 mm

## Slide 39: Design Satisfaction Section 3
Project Risks
Project Purpose
Project Planning
Design Solutions
Design Satisfaction
Verification & Validation

## Slide 40: Inlet Design Satisfaction Section 3.1
Project Risks
Project Purpose
Project Planning
Design Solutions
Design Satisfaction
Verification & Validation

## Slide 41: ≥ 98% Total Pressure Recovery
Primary scoring criteria for AFRL.
CFD program allows for the computation of total pressure throughout duct interior.
Trial and error method for characterizing ideal total pressure recovery within certain duct designs.
CFD results will be verified via experimentation.

## Slide 42: ≤ 5% Max Thrust & TSFC Decrement
Primary AFRL scoring criteria.
Inlet design must provide necessary mass flow across RPM sweep of the engine.
Addition of a removable bell mouth to ensure proper mass flow at static test conditions.
Upon inlet design verification (EDF, test stand integration), inlet will be attached to JetCat to ascertain TSFC and Max Thrust Decrement parameters.

## Slide 43: Short Axial Length
Secondary AFRL scoring criteria.
Modeled several iterations of baseline design in 2 inch increments to observe flow effects. (Flow separation, adverse pressure gradients, turbulence).
CFD simulations give credence to a 24 in length duct for ideal performance metrics.

## Slide 44: Test Apparatus Design Satisfaction Section 3.2
Project Risks
Project Purpose
Project Planning
Design Solutions
Design Satisfaction
Verification & Validation

## Slide 45: LABView GUI

## Slide 47: Total Pressure Measurement: Pitot Probe
Dwyer 167-6 pitot probe
  ⅛th inch diameter probe
  1.5 inch probe length
  6 inch insertion length
0.00098 ≤ Aprobe/Ainlet ≤ 0.0099
  Area of probe over area of inlet at minimum and maximum insertion
  Minimal flow interference
Probe accurate to within 0.5%
  Only accurate at minimum of 5 m/s airflow
  Accuracy converges above this speed
Total & static pressure measured using scanivalve

## Slide 48: Mapping Pressure Distribution
Major distortions expected at wall interface
  Observable using surface pressure taps
Minimal distortions expected at inlet center
  Observable using slot pitot

## Slide 49: TA interface with Multiple Inlets
Modular design
Holders capable of 2 and 3 degrees of freedom
  Allows for any inlet to be supported in vertical or horizontal orientations
  Different offsets are accommodated
  Can also hold different inlet lengths
To adjust in any dimension simply loosen and re-tighten bolts
  Made possible through special sliding nuts
750 mm
483.5 mm

## Slide 50: Project Risks Section 4
Design Satisfaction
Project Purpose
Project Planning
Design Solutions
Project Risks
Verification & Validation
Notes: Sec 5 -
Presented by: Will

## Slide 51: Inlet Risks and Mitigation
Inlet Material Failure
Soiling Effects
FLow leakage through surface or integration with TA
Risk Matrix |  | Impact |  |  | 
 |  | Insignificant | Minor | Major | Catastrophic
 | Certain >90% |  |  |  | 
 | Likely 30-85% |  | 3 | 2 | 
 | Unlikely 10-30% |  |  |  | 1
 | Rare <10% |  |  |  | 
Probability

## Slide 52: Inlet Risks and Mitigation
Inlet Material Failure
  Increase thickness to avoid failure
Soiling Effects
Flow leakage through surface or integration with TA
Risk Matrix |  | Impact |  |  | 
 |  | Insignificant | Minor | Major | Catastrophic
 | Certain >90% |  |  |  | 
 | Likely 30-85% |  | 3 | 2 | 
 | Unlikely 10-30% |  |  |  | 
 | Rare <10% |  |  |  | 1
Probability

## Slide 53: Inlet Risks and Mitigation
Inlet Material Failure
Soiling Effects
  Vortex Generator, Sand paper
Flow leakage through surface or integration with TA
Risk Matrix |  | Impact |  |  | 
 |  | Insignificant | Minor | Major | Catastrophic
 | Certain >90% |  |  |  | 
 | Likely 30-85% |  | 3 |  | 
 | Unlikely 10-30% |  |  | 2 | 
 | Rare <10% |  |  |  | 1
Probability

## Slide 54: Inlet Risks and Mitigation
Inlet Material Failure
Soiling Effects
Flow leakage through surface or integration with TA
  HVAC tape for short term, re-manufacture or design for long term
Risk Matrix |  | Impact |  |  | 
 |  | Insignificant | Minor | Major | Catastrophic
 | Certain >90% |  |  |  | 
 | Likely 30-85% |  |  |  | 
 | Unlikely 10-30% | 3 |  | 2 | 
 | Rare <10% |  |  |  | 1
Probability

## Slide 55: Test Apparatus Risks and Mitigation
Risk Matrix |  | Impact |  |  | 
 |  | Insignificant | Minor | Major | Catastrophic
 | Certain >90% |  |  |  | 
 | Likely 30-85% |  | 1 |  | 5
 | Unlikely 10-30% |  | 4 | 2 | 6
 | Rare <10% |  | 3 |  | 
Short EDF battery duration and performance
Too little mass flow from EDF surrogate
Inaccurate EDF mass flow control
Non-negligible error introduced with slotted inlet concept
JetCat engine unable to function for testing
Engine explosion (damage to compressor blades with test inlet)
Probability

## Slide 56: Test Apparatus Risks and Mitigation
Risk Matrix |  | Impact |  |  | 
 |  | Insignificant | Minor | Major | Catastrophic
 | Certain >90% |  |  |  | 
 | Likely 30-85% |  |  |  | 5
 | Unlikely 10-30% | 1 | 4 | 2 | 6
 | Rare <10% |  | 3 |  | 
Short EDF battery duration and performance
  Multiple batteries or DC power supply
Too little mass flow from EDF surrogate
Inaccurate EDF mass flow control
Not negligible error introduced with slotted inlet concept
JetCat engine unable to function for testing
Engine explosion (damage to compressor blades with test inlet)
Probability

## Slide 57: Test Apparatus Risks and Mitigation
Risk Matrix |  | Impact |  |  | 
 |  | Insignificant | Minor | Major | Catastrophic
 | Certain >90% |  |  |  | 
 | Likely 30-85% |  |  |  | 5
 | Unlikely 10-30% | 1 | 4 |  | 6
 | Rare <10% |  | 3 | 2 | 
Short EDF battery duration and performance
Too little mass flow from EDF surrogate
  Purchase new fan (larger than 80mm)
Inaccurate EDF mass flow control
Not negligible error introduced with slotted inlet concept
JetCat engine unable to function for testing
Engine explosion (damage to compressor blades with test inlet)
Probability

## Slide 58: Test Apparatus Risks and Mitigation
Risk Matrix |  | Impact |  |  | 
 |  | Insignificant | Minor | Major | Catastrophic
 | Certain >90% |  |  |  | 
 | Likely 30-85% |  |  |  | 5
 | Unlikely 10-30% | 1 | 4 |  | 6
 | Rare <10% |  | 3 | 2 | 
Short EDF battery duration and performance
Too little mass flow from EDF surrogate
Inaccurate EDF mass flow control
  Implement quality RPM sensor and integrate into closed loop control
Not negligible error introduced with slotted inlet concept
JetCat engine unable to function for testing
Engine explosion (damage to compressor blades with test inlet)
Probability

## Slide 59: Test Apparatus Risks and Mitigation
Risk Matrix |  | Impact |  |  | 
 |  | Insignificant | Minor | Major | Catastrophic
 | Certain >90% |  |  |  | 
 | Likely 30-85% |  |  |  | 5
 | Unlikely 10-30% | 1 |  |  | 6
 | Rare <10% | 4 | 3 | 2 | 
Short EDF battery duration and performance
Too little mass flow from EDF surrogate
Inaccurate EDF mass flow control
Not negligible error introduced with slotted inlet concept
  Reduce slot width, cover open slot and reduce pitot diameter
  Move from slotted concept to distinct locations
JetCat engine unable to function for testing
Engine explosion (damage to compressor blades with test inlet)
Probability

## Slide 60: Test Apparatus Risks and Mitigation
Risk Matrix |  | Impact |  |  | 
 |  | Insignificant | Minor | Major | Catastrophic
 | Certain >90% |  |  |  | 
 | Likely 30-85% |  |  |  | 
 | Unlikely 10-30% | 1 |  |  | 6
 | Rare <10% | 4 | 3 | 2 | 5
Short EDF battery duration and performance
Too little mass flow from EDF surrogate
Inaccurate EDF mass flow control
Not negligible error introduced with slotted inlet concept
JetCat engine unable to function for testing
  Send engine for JetCat approved service to get any issues fixed by qualified personnel
Engine explosion (damage to compressor blades with test inlet)
Probability

## Slide 61: Test Apparatus Risks and Mitigation
Risk Matrix |  | Impact |  |  | 
 |  | Insignificant | Minor | Major | Catastrophic
 | Certain >90% |  |  |  | 
 | Likely 30-85% |  |  |  | 
 | Unlikely 10-30% | 1 |  |  | 
 | Rare <10% | 4 | 3 | 2 | 5,6
Short EDF battery duration and performance
Too little mass flow from EDF surrogate
Inaccurate EDF mass flow control
Not negligible error introduced with slotted inlet concept
JetCat engine unable to function for testing
Engine explosion (damage to compressor blades with test inlet)
  Perform all initial inlet tests on EDF surrogate until aerodynamic effects are understood
Probability

## Slide 62: Verification & Validation Section 5
Design Satisfaction
Project Purpose
Project Risks
Design Solutions
Verification & Validation
Project Planning

## Slide 63: Inlet Verification and Validation Plan

## Slide 64: Test Stand Calibration and Verification Plan
EDF mass flow calibration
  Test several throttle settings for the EDF
    Straight inlet with bell mouth
  Calculate mass flow with pitot probe
    Steady 1-D approximation
  Record useful battery duration (EDF)
  Repeat the test with the Jetcat engine
  Identify the EDF settings which align with JetCat’s settings
Pitot Tube Verification
  Test in Aerospace wind tunnel
  Compare against pitot tubes and other pre calibrated and proven sensors
(D = 4in)
(D = 4in)

## Slide 65: CFD Calibration
Simple converging-diverging inlet
  Simple ASEN 2002 analytical calculations
    Estimate flow speeds at key locations (before throat, throat, after throat) with hand calculations
  Compare and verify
    CFD
    Analytical (back of the envelope)
    Experimental results
Balancing CFD calculations
  Higher Reynolds Number
P0 = P∞ = P1

## Slide 66: Turbine Engine Sensors Calibration
Load Cell
  Calibrate cell with known weights
  Run JetCat engine through RPM sweep without and without inlet test stand
  Ensures inlet test stand has negligible error on thrust data
Fuel Flow Sensor (fuel flow rate)
  Equiflow PFA Click Housing Flowmeter
  With JetCat fuel pump run into graduated cylinder at set rate with stopwatch for flow rate verification

## Slide 67: Project Planning Section 6
Design Satisfaction
Project Purpose
Project Risks
Design Solutions
Project Planning
Verification & Validation

## Slide 68: Org Chart
AFRL Rep: Capt Huff
Advisor: Professor John Mah
PM: Will Watkins
Systems Engineers:
Dishank Kathuria
Harrison Methratta
CFD: Zak Dmitriyev
Inlet Lead: Tim Breda
TA Lead: Michael Vogel
Structures:
Josh Seedorf
Testing: Joey Derks
Finance:
Ryan Joseph
Safety/Manufacturing: John Wissler

## Slide 69: Work Breakdown Structure
OSPRI
Test Apparatus
Initial Manufacture
Assembly
Inlet
JetCat Engine
Final Testing on JetCat
Initial Testing
Redesign
Verification
Stock Engine Runs
Integration with TA
Project Management
Fall Final Report
Manufacturing Status Review
Testing Readiness Review
Spring Final Review
Project Final Report
Data Analysis
Thrust
TSFC
Mass Flow
Sensors
CFD Design/Verification
EDF Mass Flow
Dimensional
Instrument Verification

## Slide 70: Work Plan
Notes: Presented by: WILL

## Slide 71: Cost Plan
Unused Funds - ($0) Plenty of extra room in budget to be reallocated
Inlet Manufacturing - ($0) This budget gives enough room for 25 prints at current estimates
Test Apparatus - ($225) Test stand fully purchased, room for another if necessary
Instrumentation - ($166) Most instruments borrowed from Aero Dept, plenty of budget in case
Engine Maintenance - ($250) Engine sent to JetCat & fixed. Extra budget given engine
$1,500
$1,000
$1,000
$500
$1,000

## Slide 72: Test Plan
Test | Date | Materials | Location | Special Access
Engine Operation | 1 Dec 2020 | JetCat Engine | Engine Test Cell | Yes - R2R Schedule*
TA Instrument Verification | 27 Dec 2020 | Test App, Wind Tunnel | Aero Wind Tunnel | Yes - R2R Schedule*
TA EDF Verification | 3 Jan 2020 | Test App, EDF, JetCat | Engine Test Cell | Yes - R2R Schedule*
Inlet EDF Testing | 17 Jan - 20 Feb 2020 | Test App, Inlet, EDF | Wind Tunnel | Yes - R2R Schedule*
Inlet JetCat Testing | 21 Feb - 20 Mar 2020 | Test App, Inlet, JetCat | Engine Test Cell | Yes - R2R Schedule*
* - R2R Schedule only allows Team OSPRI to be on campus 2 days/week

## Slide 73: Resources
[1] Lee, J., Cho, J. ”Effect of aspect ratio of elliptical inlet shape on performance of subsonic diffusing S-duct,” J Mech Sci Technol 32, 1153–1160 (2018). https://doi.org/10.1007/s12206-018-0218-5.
[2] Anderson, J., Introduction to Flight Eighth Edition, New York City:McGraw Hill education, 2016
[3] Sun, S., Guo, R.W. 2006. “Serpentine Inlet Performance Enhancement Using Vortex Generator Based Flow Control,” Chinese Journal of Aeronautics
[4] Tanguy, G. 2016. “Passive flow control study in a convoluted intake using Stereo Particle Image Velocimetry,” The French Aerospace Lab
[5] Kirk, A. M. 2006. “Active flow control in an advanced serpentine jet engine inlet duct Master's thesis”, Texas A&M University
[6] Shaw, R., “The Influence of Hole Dimensions on Static Pressure Measurements,” Department of Mechanical Engineering, University of Liverpool, 1 July 1959.
[7] “Delta-V 32 80mm (EFLDF32) Fan Unit Instructions,” Horizon Hobby, retrieved November 12, 2020.
[8] Reichert, B.A., and Wendt, B.J., 1994, “Improving Diffusing S-Duct Performance by Secondary Flow Control,” AIAA 32nd Aerospace Sciences Meeting and Exhibit.
[9] Basawaraj, Hosur, S., 2016. “CFD Analysis of Serpentine Inlet Duct to Enhance the Flow Properties Using Vortex Generator,” International Journal of Innovative Research in Science, Engineering and Technology
[10] Rabe, A. 2003. “Effectiveness of a Serpentine Inlet Duct Flow Control Scheme at Design and Off-Design Simulated Flight Conditions,” Virginia Polytechnic Institute and State University
[11] Anderson, B. H., and Gibb, J., "Vortex Generator Installation Studies on Steady State and dynamic Inlet Distortion," AIAA Paper 96-3279, July 1996.
[12] Dudek, J. C., "Empirical Model for Vane-Type Vortex Generators in an Navier-Stokes Code", AIAA Journal, Vol. 44, No. 8, pp 1779-1789,August 2006.
Notes: Presented by: Will

## Slide 74: Resources
[13] HARRINGTON-CRESSMAN, PETER J.M., “AIRCRAFT SYSTEM COMPARTMENT DIAGRAM.” Retrieved 10 September 2020. https://www.airlinereporter.com/2015/09/requiem-trijet-masterpiece-lockheed-l-1011-tristar/aircraft-system-compartment-diagram/
Notes: Presented by: Will

## Slide 75
Additional Slides

## Slide 76
AFRL Testing Conops

## Slide 77: Mass Flow Surrogation
Assumptions:
Circular cross section
Constant area cross section
Standard atmospheric conditions
Notes: Presented by: Joey Or Josh??

## Slide 78: Original Horizontal Slotted Inlet Concept
EDF mount
Probe mount rails
Inlet mounts rails
230 mm
760 mm
Vertical Test Setup
Notes: Joey Presented by: JOEY

## Slide 79: Test Stand Design Process

## Slide 80: Test Stand Design Process

## Slide 81: Test Stand Frame
Transition piece holder
Inlet holder short
Inlet holder long
750 mm
483.5 mm

## Slide 82: Test Stand Design Process
Worried about force from EDF on teststand mounts
https://us.misumi-ec.com/pdf/fa/2012/p2_0493.pdf
Notes: After using the flexure formula, and comparing the results to the values provided in the specifications, the 30x30mm extruded aluminum framing will have no issues holding up to the stresses of the EDF with this design at a 120 mm length and we will have 2 pillars to hold edf.

## Slide 83: EDF Control
Electronic Speed Control (ESC)
Exact components dependant on EDF
ESC Signal for RC EDFs
50 Hz PWM, 5-10% duty cycle
Notes: Maybe Use for the EDF control and Power slide above
Looking at EDF control, in the top right corner you can see the integration of the EDF with the test inlet and the electronic speed control or ESC, with a more detailed depiction of the EDF ESC interface in the bottom right.
We will be utilizing the ESC to control the EDF rpm and thus mass flow rate to maintain consistent testing conditions.
ESCs are commonly used in RC aircraft and as such the signals are fairly standardized, with ordinary edfs running off a 50 hz pulse width modulated signal, with a 5-10% duty cycle. Depending on the exact EDF the ESC and battery may vary.
Slide Please

## Slide 84: Sensor Trade Study

## Slide 85: Sensor Utilization Trade Study

## Slide 86: Mass Flow Surrogate Trade study

## Slide 87: Inlet Trade Studies

## Slide 88: Equflow Flow Measurement Instrument
Working closely with professor Trudy Schwartz to understand how to properly use the provided sensor
Instrument output is a square wave and counting the frequency will provide that flow rate measurement.
Typically use a microcontroller or NI DAQ with a counter/timer channel is used to read these types of square wave, encoder, etc measurements.
In the past teams have used the NI 9401 digital input module to read data.
Disposable to reduce clogging and inaccuracies. Will need to purchase new test sections for subsequent tests.
Max turbine flow rate: 0.36 L/min
Min turbine flow rate: 0.06 L/min (at idle)
0045 model flow rate: 0.1 - 1.8 L/min (with minimum flow of 0.06 L/min)
Pack of 10 Replacements (€ 400.00 ~ $470)
https://www.equflow.com/product/pfa-click-housing-flow-sensor
https://www.equflow.com/product/pfa-flow-tube-4-5-for-click-housing-tubeholder-clamp-10-pack-7-mm-hose-barb

## Slide 89: JetCat Engine FBD

## Slide 90: Integrated Engine Test
Pressure Distribution
Continuous 2D pressure data from slotted inlet allows for pressure distribution modelling
Load cell
25 lb load cell which functions to measure the turbine’s thrust. AES department provided equipment with Arduino to read data into computer program. Already integrated into test stand and functioning from previous years. Engine capable of 22.4 lbf of thrust.
Fuel Flow Sensor
The fuel flow sensor will only be required for integrated engine tests.
Notes: Presented by: Michael

## Slide 91: Test Apparatus Spending

## Slide 92: Instrumentation & Maintenance Spending

## Slide 93: Inlet Length Guide

## Slide 94: Vortex Generator Example Visualization [10]

## Slide 95: CFD Results (Design 05) using icoFoam
Length: 24 inches
At/A2 ratio: 0.25
Bellmouth: None
Re#: ~2350 (Transition-Turbulent Flow)
Notes: WIBBLY WOBBLY

## Slide 96: TA initial test plan
Test Inlet via CFD
  No location
Test Inlet via EDF test procedure
  Located in wind tunnel room (coordinate with Bobby, and Katie Rae/ Have accessed already)
  Scanivalve transducer
  Test stand in EDF configuration
  Data to collect:
    Static pressure from static taps
    Flow data from pitot tube in middle of inlet
    Ambient temperature
    Ambient pressure
  Info want from test:
    Air density
    Pressure distortion
    Mass flow
    Identification of flow separation (static ports)
3.Test Inlet via JetCat engine test procedure
  Located in Engine test cell (coordinate with Matt Rhode. Have had regular access already)
  Test stand in turbine configuration
  Data to collect
    Static pressure from static taps
    Flow data from pitot tube in middle of inlet
    Ambient temperature
    Ambient pressure
    Turbine thrust (load cell)
    Fuel flow
  Info want from test:
    Air density
    Pressure distortion
    Mass flow
    Identification of flow separation (static ports)
    Thrust specific fuel consumption