## Slide 1: WHiMPS
Windmill Hindrance and Maneuverable Propulsion System
Team:
Alec Bosshart
Isobel Griffin
Julia Kincaid
Andrew Meikle
Declan Murray
Alexandra Paquin
Andrew Robins
Liam Sheffer
Jon Weidner
Zoe Witte
Lucas Zardini
Nick Zellmann
Final Oral Review
Advisor: Dr. Donna Gerren
Customer: Air Force Research Laboratory
POC: 1LT Riley Huff
Notes: Presenter:

## Slide 2: Overview
Overview
Testing
Systems Engineering
Design Description
Project Management
Notes: Presenter: nick start

## Slide 3: APOP Demonstration
WHiMPS is participating in the annual AFRL sponsored Aerospace Propulsion Outreach Program (APOP) Demonstration
APOP is designed to use small gas turbine engines as a testbed to demonstrate technology that can solve problems experienced by the Air Force on larger gas turbine engines
Heritage projects:
ACES 2018
SABRE
2017
REAPER 2016
MEDUSA 2015
SPECS 2019
Notes: Presenter:

## Slide 4: Problem Statement
Problems
Prevent windmilling of the fan blades while under flight conditions of Mach 0.8 at 20k feet
Implement thrust vectoring capabilities of +/- 10 degrees to the JetCat P100-RX Engine
Motivation
Many small UAVs do not have the capability to fly long distances before completing a mission
  To solve this problem, the Air Force often carries drones to their operational environment with a larger carrier aircraft and deploys them from the larger aircraft. This creates the new problem of windmilling, which makes it difficult to start the engine.
Notes: Presenter:
Should we add in any kind of a picture here?

## Slide 5: Project Purpose Visualization
Notes: Presenter:

## Slide 6: Project Impact
Improve reliability of UAVs in Air Force applications
  Without any form of windmill prevention, the engines need to start at a very high RPM which causes major reliability issues
Increase operational lifespans of small jet engines
  When windmilling occurs, turbine shaft spins at a high RPM without any lubrication
Increase performance of drones
  Thrust vectoring impacts the maneuverability of drones
  Allows for additional control methods in addition to traditional rudder/elevators
Notes: Presenter:

## Slide 7: WHiMPS Concept of Operations
Notes: Presenter:
Tweak TV conops, include more detail about starting engine, etc.

## Slide 8: Levels of Success
Level | Windmill Prevention Mechanism | Thrust Vectoring Mechanism
1 | Simulation predicting selected WPM design is capable of preventing engine rotation from exceeding 0.5 RPM under flight conditions of Mach 0.8 at 20kft. Control software able to simulate ejection mechanism. | Simulations predicting zero change in nominal thrust at zero degrees of thrust deflection. Control software capable of vectoring thrust by 10 degrees in a single axis using simulated TVM. /
2 | Same as level 1 | Control software able to move physical TVM system to conditions representative of 10 degrees of vectoring in a single axis.
3 | Physical WPM capable of restricting turbine shaft to less than 0.5 RPM in test environment. Ejection in static environment successful. | Control software able to move physical TVM system to conditions representative of 10 degrees of vectoring in two perpendicular axis.
4 | Reach level 3 of success in both WPM and TVM with engine turned off.
5 | Reach level 4 on a functioning Jetcat P100-RX.
Notes: Presenter:

## Slide 9: Design Description
Overview
Testing
Systems Engineering
Design Description
Project Management
Notes: Presenter:

## Slide 10: Windmill Prevention Mechanism (WPM)
Design Theory: Prevent windmilling by preventing any uniform mass flow through the core of the engine using a covering mechanism
Challenges:
  Need to be able to deactivate remotely
    Accomplished through a spring-loaded ejection
    Deployed by signal from control panel using solenoids
  AFRL desired a system that would have minimal impact on drag and mass
    Fairing’s shape reduces drag
    Selected carbon fiber reinforced plastic to maximize strength to weight within our budget
Design inspiration: Rocket fairings
Notes: Presenter:

## Slide 11: Baseline Design - WPM
Solenoid Housing
Fairing
Fore Retention Ring
Solenoid Pins
Ejection Spring Location
11”
6.8”
Notes: Presenter:

## Slide 12: Windmill Prevention Mechanism (WPM) Fairing
Critical Element: Deflects flow around the body of the engine
Simplified design made for easy integration with JetCat engine
97mm
5mm thick
105mm long
Manufactured using Carbon Fiber reinforced Onyx
  Compressive Strength 320 MPA
  50% greater strength to weight than 6061 aluminum
Notes: Presenter:

## Slide 13: Windmill Prevention Mechanism (WPM) Fairing Ejection
Fairing mounted to engine using Fore Retention Ring
Deployed by retracting solenoid pins from fairing
Fairing will be ejected along the sides of the engine
  Assisted by internal springs
    Attached to inside of fairing, mounted against starter motor
  According to CFD, aerodynamic forces will aid in separating fairing and assist in deployment
Notes: Presenter:

## Slide 14: Thrust Vectoring Mechanism (TVM)
Design Theory: Deflect exhaust flow by turning paddles into the flow using an “X” configuration of 4 paddles
Challenges:
  Need to be able to relate thrust vectoring angle to paddle deflection angle
    Accomplished through model derived from aerodynamic principles and through CFD
  Air Force desired a solution that would not impact nominal thrust of the engine
    With paddles retracted, there will be no disturbance to exhaust flow
  System must be able to handle extreme thermodynamic and aerodynamic loads associated with exhaust of jet engines
    Material selection of stainless steel
Design Inspiration: Other paddle thrust vectoring technologies using 3 paddles
Notes: Presenter:

## Slide 15: Baseline Design - TVM
Paddle
Linkage Rod
Nozzle Sheath
Actuator Ring
Linear Actuator
Linear Potentiometer
Linear Potentiometer Arm
Actuator Pod
11”
6.8”
Notes: Presenter:

## Slide 16: Thrust Vectoring Mechanism (TVM) Paddles
Most critical element - Physically deflects exhaust flow
Simple design - trapezoid in 85° arc
Exposed to very high thermal stresses
Comprised of 17-4PH stainless steel
Design process began with flat square plate assumption.
  Create analytical model to predict paddle area requirements
Notes: Presenter:

## Slide 17: Thrust Vectoring Mechanism (TVM)
Notes: Presenter:

## Slide 18
Notes: Presenter:

## Slide 19: Electronics Overview
Main Control Board (MCB)
Provides WHiMPS’ data processing and power distribution
Integrated Communication Unit Panel (ICUP)
Extends actuators and potentiometers’ data and power lines from the MCB to the engine
Linear Potentiometer Breakout Board (LPBB)
Converts potentiometer analog output to a digital signal (I2C)
LPBB
Rev. B
MCB
ICUP
Notes: Presenter:
More information
Where they live in main system- more context and anything significant about the boards
Since these are simple, the schematics are in backup
Relate to the FBD
Vague descriptions
Keep referring to everything and what they are doing

## Slide 20: Electronics System CAD
LPBB
ICUP
Test cell safe room
MCB
Notes: Presenter:

## Slide 21: MCB Revision B
Important Functions:
The MCB will be located in the Engine Test Cell/Safe Room
This board has the Raspberry Pi 4
Power Selection (On/Off Switch)
Power Regulation (Converts 7.6V to 5V)
Power Protection (Zener Diode and PMOSFET in power path)
Temperature sensors and warning LEDs
Solenoid LEDs
Power LEDs
Power check FETs (1 for each motor driver)
Load Cells and Amplifier
Connects to ICUP
Notes: Presenter:

## Slide 22: ICUP Revision B
Important Functions:
The ICUP will be in a bracelet design around the Fore Retention Ring
Connects to the MCB
Motor Drivers/Linear Actuators
Connects to LPBB
5V to 2.5 V step down
Solenoids (Panels 2 and 4)
Temperature Sensors
1
MCB <-> ICUP
Actuator #1
Motor Driver #1
LPBB #1
2
Solenoid #1
Actuator #2
Motor Driver #2
LPBB #2
3
Actuator #3
Motor Driver #3
LPBB #3
4
Solenoid #2
Actuator #4
Motor Driver #4
LPBB #4
Notes: Presenter:

## Slide 23: LPBB Revision B
Important Functions:
4 boards
Located in the Actuator Ring
Contain the Linear Potentiometers
Connects to the ICUP
Converts analog output to digital
Notes: Presenter:

## Slide 24
Notes: Presenter:
How complex is it
How much did you write vs inherit
What were the main things that took time

## Slide 25: Software Development
The MCB software was the most time consuming
The LabVIEW for the WHiMPS was mainly focusing on completing calculations, and sending commands and receiving data from the MCB
The MCB software components that were expected to be the most difficult are:
  Feedback loop between the linear potentiometers and the linear actuators
  Bit banged serial driver for the load cells
It was difficult to have the LabVIEW and MCB Software development so separate, so determining who was in charge of which calculations and getting on the same page about data types and command dictionaries was something our team struggled with.
Notes: Presenter:

## Slide 26: System Integration Diagram
Notes: Presenter:

## Slide 27: Complete Engine System
6.8”
11”
Notes: Presenter:
Wholistic go over where everything is and functions of components

## Slide 28: Changes Since TRR
Switched from using stock Hall Effect sensor to laser tachometer for measuring RPM during WPM testing
  Confirmed with Jetcat that Hall Effect sensor would not sufficiently be able to measure engine RPM below 2,000 RPM
  Informed Lt. Trenter of this issue during his visit
Mitigations to thermal concerns of electronics were in progress when COVID shutdown occurred
  More detail on this will be discussed in the testing section
Notes: Presenter:

## Slide 29: Critical Project Elements
CPE | Critical Characteristics
Windmill Prevention Mechanism (WPM) | Prevents windmilling by preventing freestream air from entering the engine while deployed. Must be remotely disengaged.
Thrust Vectoring Mechanism (TVM) | Turns exhaust flow to vector engine’s thrust to a commanded vectoring angle.
Main Control Board (MCB) | During testing and product development, this will monitor WPM/TVM.
Integrated Communication Unit Panel (ICUP) | Minimizes amount of wires to reduce risk of human error and increases processing speed.
Software | Controls the incorporated mechanisms over the entire operational envelope.
Notes: Presenter:

## Slide 30: Remaining Work
Windmill Prevention
  Manufacture solenoid pins → 6 man hours
  Integrate system onto engine → 3 man hours
Thrust Vectoring
  Finish manufacturing components → 7 man hours
  Integrate final 3 paddles → 4 man hours
Electronics
  Receive and populate Rev. B of PCB’s → 5 man hours
  Subsystem test Rev. B of PCB’s → 15 man hours
Software
  Complete LabView → 20 man hours
  Complete MCB Software → 45 hours
Remaining testing will be covered in depth in the next section of this presentation
Notes: Presenter:
Discuss just items and total time left
We should also touch on plans for how we were going to get the software done

## Slide 31: Testing
Overview
Testing
Systems Engineering
Design Description
Project Management
Notes: Presenter:

## Slide 32: Engine Testing Progression
Stock Run
Understand engine operation
Stock w/ Dummy Paddle
Mitigate stock engine electronics risks and validate paddle thermal model
Vibration and Thrust Baseline /
Characterize vibration and thrust
Static TVM Test
Validate ability to vector thrust using paddles preset in deflected position
Dynamic TVM Test
Verify ability to vector thrust by commanding paddle movement during engine operation
APOP Replica Test
Verify fairing prevents airflow under pressure differential
SABRE Static WPM Test
Validate fairing function at Mach 0.8
SABRE Dynamic WPM test
Verification of ability to eject fairing at Mach 0.8
TVM and WPM Integration Tests
TVM Testing
WMP Testing
Notes: Presenter:
Moving the “X” next to integration tests because it was half off the screen

## Slide 33: Stock Engine and Dummy Paddle Test
Validated thermal model before implementation of hardware
Verified engine did not turn off when flow was deflected using dummy paddles
Equipment
  Engine, associated tanks and lines
  Test stand
  Paddles and attachment mechanisms
  Fuel and oil, in tank
  Thermocouples
  GSU and battery
Facilities
  CU Aerospace Test Cell
Notes: Presenter:

## Slide 34
Notes: Presenter:

## Slide 35: Stock Engine Test Thermocouple Data
Max Temp: 168°C
Notes: Note that 304 steel has a melting point of 1400C, but can be used in continuous manner up to 925C
Add model expectations and error bars

## Slide 36: Stock Engine Test Thermocouple Data
Max Temp: 79°C

## Slide 37: ICUP Temperature Analysis
Engine
Fore retention ring
145°C
Conduction through ring
Natural convection to ambient air
145°C
25°C
=
Ambient air at 25°C
Result: The temperature at the location of the boards can vary from 59°C to 125°C depending on the convective heat transfer coefficient.
Notes: Presenter:
Presenter - note that the convective heat transfer coefficient is determined experimentally, so we used values at both extremes of natural convection from a table. Best case scenario is the same as the worst case for forced convection, so a fan could reasonably keep us 30% below the temp limit. Thermal conductivity of material is also unknown, assumed a worst case of twice as high as ABS

## Slide 38: Electronics Thermal Mitigations
Electronics have approximate thermal limit of 95°C
Unable to test exact temperatures at electronics attachment locations, but a simple 1D heat transfer for a worst case scenario was conducted
  Analysis said that the temperature of the fore retention could exceed the electronics thermal limit, depending on the natural convection heat transfer coefficient
If we use the worst case scenario of convective heat transfer coefficients for forced convection, temperature of the boards would be 60°C
Insulating materials were investigated in the event that this analysis is incorrect due to approximations for convective and conductive heating coefficients that are typically determined experimentally
  Ceramic-based foam, provides 60°C temperature reduction -- HeatShields™
Notes: Presenter:
Definitively decide what we were going to do
Think about if someone next year wanted to implement this
Talk about the results of thermal testing
Tease the audience

## Slide 39: Engine Testing Progression
Stock Run
Understand engine operation
Stock w/ Dummy Paddle
Mitigate stock engine electronics risks and validate paddle thermal model
Vibration and Thrust Baseline /
Characterize vibration and thrust
Static TVM Test
Validate ability to vector thrust using paddles preset in deflected position
Dynamic TVM Test
Verify ability to vector thrust by commanding paddle movement during engine operation
APOP Replica Test
Verify fairing prevents airflow under pressure differential
SABRE Static WPM Test
Validate fairing function at Mach 0.8
SABRE Dynamic WPM test
Verification of ability to eject fairing at Mach 0.8
TVM and WPM Integration Tests
TVM Testing
WMP Testing
Notes: Presenter:
Moving the “X” next to integration tests because it was half off the screen

## Slide 40: Thrust Baseline Test
Collected thrust data at 100% throttle without exhaust deflection
Would have been used to compare with TVM tests under zero paddle deflection
  Used to validate FR1 - Thrust Vectoring
Equipment
  Engine, associated tanks and lines
  Test stand
  Paddles and attachment mechanisms
  Fuel and oil, in tank
  Thermocouples
  GSU and battery
Facilities
  CU Aerospace Test Cell
Notes: Presenter:

## Slide 41: Thrust Baseline Test Data
Max Thrust = 100N (JetCat)
Idle RPM = 40k
Max RPM = 154k
Idle Thrust =
3N (JetCat)
Notes: The prettiest data I ever did see :)
This step up is due to test profile not resolution

## Slide 42: Load Cell Measurement
Initial load cell testing showed finicky nature and low precision measurements on March 12th (day before shutdown)
  Further testing was planned to determine severity of load cell precision error
Current error is ±16.35N, which is ±25°
  Would prefer error of ±1° - requires error of ±0.7N
Expect losses due to friction along rail system
  Further testing using known masses and gravity to quantify error was planned
Notes: Presenter: consider moving

## Slide 43: Vibration Expectations
Vibration models made several predictions
  Engine frequency: 733.3 Hz ≤ f ≤ 2566.7 Hz
Material is modeled as T-600 Steel with a modulus of elasticity of ~200 GPa
  Paddle: f = 18.28 Hz
  Rod: f = 329 Hz
Actuator, screw, nozzle sheath, and housing will act as dampers to dissipate energy, further reducing risk of vibrational failure
Accelerometer would have provided vibration data for all engine states to confirm components would survive
Notes: Isobel added this in, not sure if it’s what we need, lemme know
Presenter:

## Slide 44: Engine Testing Progression
Stock Run
Understand engine operation
Stock w/ Dummy Paddle
Mitigate stock engine electronics risks and validate paddle thermal model
Vibration and Thrust Baseline /
Characterize vibration and thrust
Static TVM Test
Validate ability to vector thrust using paddles preset in deflected position
Dynamic TVM Test
Verify ability to vector thrust by commanding paddle movement during engine operation
APOP Replica Test
Verify fairing prevents airflow under pressure differential
SABRE Static WPM Test
Validate fairing function at Mach 0.8
SABRE Dynamic WPM test
Verification of ability to eject fairing at Mach 0.8
TVM and WPM Integration Tests
TVM Testing
WMP Testing
Notes: Presenter:
Moving the “X” next to integration tests because it was half off the screen

## Slide 45: Thrust Vectoring Mechanism (TVM) Paddles
Inform thickness/material with simple 1D heat transfer model
Refine design with FEA and CFD tools
Result: Max paddle temperature of 400°C
Notes: Presenter:

## Slide 46: Data Collected
Note: There was a failure of the kapton tape holding the thermocouple to the paddle. This resulted in a slight separation of the thermocouple of the paddle, which causes the decrease in temperature around t=90s
Max Temp: 185°C
Notes: Presenter:
Matt recommended trying to add a gap of air a few mm thick to the thermal model matches this, but I don’t think that’s super relevant

## Slide 47: Tape Failure
Before
After
Due to this failure, the team had plans to measure thermal data on an integrated paddle to validate the thermal model more accurately on the completed TVM system.
Notes: Presenter:
These image qualities are pretty bad when I zoom them in, but Matt said that pictures of the tape failure would be great. Wanted to add it in for now and potentially move it back later

## Slide 48: Engine Testing Progression
Stock Run
Understand engine operation
Stock w/ Dummy Paddle
Mitigate stock engine electronics risks and validate paddle thermal model
Vibration and Thrust Baseline /
Characterize vibration and thrust
Static TVM Test
Validate ability to vector thrust using paddles preset in deflected position
Dynamic TVM Test
Verify ability to vector thrust by commanding paddle movement during engine operation
APOP Replica Test
Verify fairing prevents airflow under pressure differential
SABRE Static WPM Test
Validate fairing function at Mach 0.8
SABRE Dynamic WPM test
Verification of ability to eject fairing at Mach 0.8
TVM and WPM Integration Tests
TVM Testing
WMP Testing
Notes: Presenter:
Moving the “X” next to integration tests because it was half off the screen

## Slide 49: Thrust Vectoring Model
Conservation of Momentum Model
CFD Model
θ = 11°
A = 850mm2
Paddles are at 20°
Nozzle
Paddle

## Slide 50: Static & Dynamic Thrust Vectoring Tests
Purpose: prove that paddles vector the thrust without altering the engine’s operation
  Verifies zero impedance at 0° and two-axis ±10° capabilities
Equipment
  Engine, associated tanks and lines
  Test stand w/ second axis
  Paddles and attachment mechanisms
  Fuel and oil, in tank
  Thermocouples
  GSU and battery
  Accelerometer
Facilities
  CU Aerospace Test Cell
Notes: Presenter:

## Slide 51: Paddle Deflection Calibration
Notes: Presenter:
Matt talked about how we should discuss how we know what our paddle angle is, and what our thrust vectoring angle is because these are the axis on the “expected data” slide

## Slide 52: Thrust Vectoring Test Stand
Modified existing test stand to include perpendicular sled to measure off-axis thrust
Based on the two load cell readings, thrust vectoring angle would have been calculated through trigonometry
Manufacturing was completed, friction analysis was planned
X
Y
Fa
Fr
𝜃
Fa
Fr

## Slide 53: Expected Data
Primarily collect thrust data from test stand load cells
  For dynamic test, also collect timing data for paddle deflections
Would have used load cell data to calculate thrust vector in different paddle deflection cases
  Would show if system met AFRL vectoring requirement
Would have provided vibrational profile via accelerometer
  Confirmed safe vibration ranges for components
Would be used to validate analytical and CFD models
  Compare thrust vector angle of models to actual angle at given paddle deflections
Used to validate FR1 - thrust vectoring requirement
Dynamic test would help validate FR3 - MCB control of mechanism
Notes: Presenter:
Error bars

## Slide 54: Engine Testing Progression
Stock Run
Understand engine operation
Stock w/ Dummy Paddle
Mitigate stock engine electronics risks and validate paddle thermal model
Vibration and Thrust Baseline /
Characterize vibration and thrust
Static TVM Test
Validate ability to vector thrust using paddles preset in deflected position
Dynamic TVM Test
Verify ability to vector thrust by commanding paddle movement during engine operation
APOP Replica Test
Verify fairing prevents airflow under pressure differential
SABRE Static WPM Test
Validate fairing function at Mach 0.8
SABRE Dynamic WPM test
Verification of ability to eject fairing at Mach 0.8
TVM and WPM Integration Tests
TVM Testing
WMP Testing
Notes: Presenter:
Moving the “X” next to integration tests because it was half off the screen

## Slide 55: WPM APOP Replica Test
Used to simulate Mach 0.8 airflow at 20,000 ft via a 3.5 psi pressure differential
Engine not operating
Equipment
  PVC pipe with attached pressure gauge and foam insert
  Air compressor
  Air lines and connectors
  Pressure regulator
  3D printed fairing
  Test mount
Facilities
  CU Aerospace Test Cell
Notes: Presenter: mention that this might have not tested exactly what what wanted, but still proved our CFD analysis because all of the air was redirected around the fairing, instead of through the fairing/engine----pressure regulator set to max output and no RPM was observed

## Slide 56: WPM APOP Replica Test Results
Preparation for SABRE test
At max pressure output there was 0 RPM
  Partially validated initial CFD Modelling and Assumptions
  CFD demonstrated air going around fairing rather than through
    APOP test confirmed this, with air escaping through foam insert seam
  Attempted to seal foam insert seam using duct-tape for 2nd run, still had 0 RPM
Determined test is broken, Air Force most likely did not predict our external design
Notes: Presenter: mention that this might have not tested exactly what what wanted, but still proved our CFD analysis because all of the air was redirected around the fairing, instead of through the fairing/engine----pressure regulator set to max output and no RPM was observed
Talk about test method and how we were testing AF test method

## Slide 57: Engine Testing Progression
Stock Run
Understand engine operation
Stock w/ Dummy Paddle
Mitigate stock engine electronics risks and validate paddle thermal model
Vibration and Thrust Baseline /
Characterize vibration and thrust
Static TVM Test
Validate ability to vector thrust using paddles preset in deflected position
Dynamic TVM Test
Verify ability to vector thrust by commanding paddle movement during engine operation
APOP Replica Test
Verify fairing prevents airflow under pressure differential
SABRE Static WPM Test
Validate fairing function at Mach 0.8
SABRE Dynamic WPM test
Verification of ability to eject fairing at Mach 0.8
TVM and WPM Integration Tests
TVM Testing
WMP Testing
Notes: Presenter:
Moving the “X” next to integration tests because it was half off the screen

## Slide 58: WPM High Speed Flow (SABRE) Tests
Provides Mach 0.8 airflow for several seconds to test fairing structural integrity and seal
Equipment
  2 pressure regulators
  2 pressure gauges
  Outlet nozzle (3D printed)
  SABRE tanks and system
  Engine test mount
  3D printed fairing mounted on engine
  Electronics and software
  Laser tachometer and/or video camera
Facilities
  CU Aerospace Test Cell
6ft
M=0.8
Pressure regulators
Pressure gauges
Notes: Presenter:
Promote that CU has resources through heritage project

## Slide 59: SABRE Test Airflow
Based calculations on work done by SABRE team
Large tank pressure - 175psi
Settling tank pressure - 35psi
SABRE used 3D printed nozzle with 1.005” throat diameter
  Used Mach-Area relationship to calculate outlet diameter to reach M=0.8
SABRE had run time of 20s at supersonic conditions
  Expect longer run time at lower velocity for WPM tests
WHiMPS nozzle is to the left of blue line
  Same inlet to fit SABRE tank, outlet diameter of 1.024”
Planning on using pitot tube to verify velocity
  Would occur in separate test before testing WPM
Notes: Presenter:

## Slide 60: SABRE Tests Expected Data
Primarily collect RPM data using a laser tachometer and video at rear
  For dynamic test, also collect video data of fairing ejection
Would have used RPM data to determine if fairing system works - expected to succeed based on APOP test results
  Would show if system met AFRL windmilling requirement
Would be used to validate CFD model of air leakage
  Show if air leaks through fairing or enters back of engine
Used to validate FR2 - incorporated WPM to limit rotation
Dynamic test would help validate FR3 - MCB control of mechanism
Notes: Presenter:

## Slide 61: Systems Engineering
Overview
Testing
Systems Engineering
Design Description
Project Management
Notes: Presenter:

## Slide 62: Systems Engineering “V”
Design Solution:
  Customer Design Requirements
    Functional Requirements
    Levels of Success
  Design Concept
    Prevent windmilling of the fan blades under M=0.8 flow at 20k ft
    Vector the thrust of the engine by ±10° on at least one axis
      Cannot impede nominal thrust
  Risk Analysis
    Thermodynamic and Structural Model
    CFD and FEA analysis
Document, Integration, and Testing:
  Unit testing electronics and software
  Design test stand for thrust measurements on two axes
  Document test plans and test results on GUI
Notes: Presenter:

## Slide 63: Trade Studies
WPM key trades:
  Performance (30%)
    Ensure no fan blade rotation under set conditions
  Simplicity (21%)
    Reduces risk of damaging engine
TVM key trades:
  Performance (31%)
    Ensure the flow is vectored to preferred angle
  Simplicity (24%)
    Reduces risk of damaging engine
Main concern was affecting the internal components and balancing of the engine
Main Concern | WPM % Weight | TVM % Weight
Performance | 30% | 31%
Simplicity | 21% | 24%
Notes: Presenter:
Too small of text
Either separate to two slides, or come up with a summarized table

## Slide 64: Design Flowdown
FR 1: The JetCat P-100RX engine shall have a thrust vectoring mechanism
  Design Requirements
    Change in nominal thrust is zero - cannot have mechanism that impedes nominal flow
    Does not affect engine operation - reduces risk of engine/project failure
FR 2: The JetCat engine shall have a windmill prevention mechanism
  Design Requirements
    Can be engaged/disengaged upon command - does not prevent airflow/fan blade rotation at all times
    Does not affect engine operation - reduces risk of engine/project failure
FR 3: The MCB shall control and monitor both of the incorporated mechanisms.
  Design Requirements
    Controls power to both mechanisms and incorporated electronics
    Sends and receives health/status data for both mechanisms and incorporated test apparati
FR 4: The MCB shall run the engine such that it remains within the nominal operating conditions.
  Design Requirements
    Maintains RPM limit - controls engine’s RPM
FR 5: The MCB shall receive data from and send data to the user interface.
  Design Requirements
    Controls engine, WPM, and TVM - permits team members to test at a safe distance from the engine
Notes: Presenter: talk about what they should be taking away from it
How did requirements flow down

## Slide 65: Design Flowdown
FR 1: The JetCat P-100RX engine shall have a thrust vectoring mechanism
  Design Requirements
    Change in nominal thrust is zero - cannot have mechanism that impedes nominal flow
    Does not affect engine operation - reduces risk of engine/project failure
FR 2: The JetCat engine shall have a windmill prevention mechanism
  Design Requirements
    Can be engaged/disengaged upon command - does not prevent airflow/fan blade rotation at all times
    Does not affect engine operation - reduces risk of engine/project failure
FR 3: The MCB shall control and monitor both of the incorporated mechanisms.
  Design Requirements
    Controls power to both mechanisms and incorporated electronics
    Sends and receives health/status data for both mechanisms and incorporated test apparati
FR 4: The MCB shall run the engine such that it remains within the nominal operating conditions.
  Design Requirements
    Maintains RPM limit - controls engine’s RPM
FR 5: The MCB shall receive data from and send data to the user interface.
  Design Requirements
    Controls engine, WPM, and TVM - permits team members to test at a safe distance from the engine
Commenced four-paddle design that does not impede exhaust flow when no vector angle is requested
Notes: Presenter: talk about what they should be taking away from it
How did requirements flow down

## Slide 66: Design Flowdown
FR 1: The JetCat P-100RX engine shall have a thrust vectoring mechanism
  Design Requirements
    Change in nominal thrust is zero - cannot have mechanism that impedes nominal flow
    Does not affect engine operation - reduces risk of engine/project failure
FR 2: The JetCat engine shall have a windmill prevention mechanism
  Design Requirements
    Can be engaged/disengaged upon command - does not prevent airflow/fan blade rotation at all times
    Does not affect engine operation - reduces risk of engine/project failure
FR 3: The MCB shall control and monitor both of the incorporated mechanisms.
  Design Requirements
    Controls power to both mechanisms and incorporated electronics
    Sends and receives health/status data for both mechanisms and incorporated test apparati
FR 4: The MCB shall run the engine such that it remains within the nominal operating conditions.
  Design Requirements
    Maintains RPM limit - controls engine’s RPM
FR 5: The MCB shall receive data from and send data to the user interface.
  Design Requirements
    Controls engine, WPM, and TVM - permits team members to test at a safe distance from the engine
Commenced fairing-ejection design that would be ejected after reaching the target air velocity and altitude
M = 0.8 @ 20k ft
Notes: Presenter: talk about what they should be taking away from it
How did requirements flow down

## Slide 67: Design Flowdown
FR 1: The JetCat P-100RX engine shall have a thrust vectoring mechanism
  Design Requirements
    Change in nominal thrust is zero - cannot have mechanism that impedes nominal flow
    Does not affect engine operation - reduces risk of engine/project failure
FR 2: The JetCat engine shall have a windmill prevention mechanism
  Design Requirements
    Can be engaged/disengaged upon command - does not prevent airflow/fan blade rotation at all times
    Does not affect engine operation - reduces risk of engine/project failure
FR 3: The MCB shall control and monitor both of the incorporated mechanisms.
  Design Requirements
    Controls power to both mechanisms and incorporated electronics
    Sends and receives health/status data for both mechanisms and incorporated test apparati
FR 4: The MCB shall run the engine such that it remains within the nominal operating conditions.
  Design Requirements
    Maintains RPM limit - controls engine’s RPM
FR 5: The MCB shall receive data from and send data to the user interface.
  Design Requirements
    Controls engine, WPM, and TVM - permits team members to test at a safe distance from the engine
Regulates power going to each component and reports data from sensors (thermocouples, RPM, etc.) back to one location for ease of operation
Notes: Presenter: talk about what they should be taking away from it
How did requirements flow down

## Slide 68: Design Flowdown
FR 1: The JetCat P-100RX engine shall have a thrust vectoring mechanism
  Design Requirements
    Change in nominal thrust is zero - cannot have mechanism that impedes nominal flow
    Does not affect engine operation - reduces risk of engine/project failure
FR 2: The JetCat engine shall have a windmill prevention mechanism
  Design Requirements
    Can be engaged/disengaged upon command - does not prevent airflow/fan blade rotation at all times
    Does not affect engine operation - reduces risk of engine/project failure
FR 3: The MCB shall control and monitor both of the incorporated mechanisms.
  Design Requirements
    Controls power to both mechanisms and incorporated electronics
    Sends and receives health/status data for both mechanisms and incorporated test apparati
FR 4: The MCB shall run the engine such that it remains within the nominal operating conditions.
  Design Requirements
    Maintains RPM limit - controls engine’s RPM
FR 5: The MCB shall receive data from and send data to the user interface.
  Design Requirements
    Controls engine, WPM, and TVM - permits team members to test at a safe distance from the engine
-Monitors the engine’s condition during operation
- Permits users to increase/decrease RPM
Notes: Presenter: talk about what they should be taking away from it
How did requirements flow down

## Slide 69: Design Flowdown
FR 1: The JetCat P-100RX engine shall have a thrust vectoring mechanism
  Design Requirements
    Change in nominal thrust is zero - cannot have mechanism that impedes nominal flow
    Does not affect engine operation - reduces risk of engine/project failure
FR 2: The JetCat engine shall have a windmill prevention mechanism
  Design Requirements
    Can be engaged/disengaged upon command - does not prevent airflow/fan blade rotation at all times
    Does not affect engine operation - reduces risk of engine/project failure
FR 3: The MCB shall control and monitor both of the incorporated mechanisms.
  Design Requirements
    Controls power to both mechanisms and incorporated electronics
    Sends and receives health/status data for both mechanisms and incorporated test apparati
FR 4: The MCB shall run the engine such that it remains within the nominal operating conditions.
  Design Requirements
    Maintains RPM limit - controls engine’s RPM
FR 5: The MCB shall receive data from and send data to the user interface.
  Design Requirements
    Controls engine, WPM, and TVM - permits team members to test at a safe distance from the engine
Allows users to coherently collect and observe engine data (temperature, RPM, etc.)
Notes: Presenter: talk about what they should be taking away from it
How did requirements flow down

## Slide 70: Engineering Challenges
APOP Replica Test
  Obtaining a pressure differential with fairing design
  Air leaks around the sides (tried to cover with duct tape!)
Two Projects in One
  Divided team to work on different parts of the project
  Worked on both mechanisms simultaneously
  Effectively doubled the work for deliverables
Machining TVM Components
  Took lots of man/woman-hours to machine all components
  Tedious and time-consuming
Notes: Presenter:
Mailing engine back and getting it fixed - time constraint
Change pictures - I like the tank picture, it is actually related to acquiring testing equipment

## Slide 71: Systems - Lessons Learned
Understanding all aspects of the project
  Varying levels of experience within team
    Offer advice and assistance to unfamiliar subjects when necessary
    Asked a lot of questions - Software/Electronics
Problem mitigation
  Contingency plans
    Highly useful in the event that something does not go as planned
    Used for WPM testing (APOP test did not go as planned - Had SABRE test as contingency)
  In-depth research
    Understanding what materials and capabilities are necessary for engine/testing functionality - test stand
Testing plans
  Very specific
    Important to cover your bases
    Results in better preparation and ultimately greater time efficiency
    Risk reduction
Notes: Presenter:
Make this more descriptive and project specific

## Slide 72: Project Management
Overview
Testing
Systems Engineering
Design Description
Project Management
Notes: Presenter: nick start

## Slide 73: Management Approach
Broke team into sub-teams early based on interest
  Originally TVM, WPM, and software/electronics
  In spring, moved to manufacturing, testing, and software/electronics
Meeting Schedule
  Bi-weekly meetings in the fall, switched to weekly meetings in the spring to maximize time conducting tests and manufacturing components
Encouraged team members to take leadership roles over every major item
  Ex. someone would take charge of the WPM APOP test, and others would help out
Allow delegation of tasks to happen primarily through individual interests/volunteering
Keep schedule margins relatively tight (~20%), with large margin at the end to allow for adjustments as issues occur
Notes: Presenter:

## Slide 74: Management Lessons Learned
Flexibility is crucial
  Our team was hit with a number of unexpected delays including:
    2 months longer to receive an engine than distributor specified
    P-card received 2 weeks later than other teams due to clerical error in the finance dept.
    Engine ECU broke week after that, which put stock testing behind an additional week
  Planning is needed, but schedule adjustments are important too
Can’t trust information from outside sources without verifying
    We didn’t evaluate APOP WPM test with respect to our design, which made it an effective “test of a test” but did not verify/validate requirements and models
Testing will often take longer than planned and issues will occur
  Examples we experienced: ECU breaking and thermocouple tape failing
Notes: Presenter:
Give examples

## Slide 75: Budget Comparison
Notes: Presenter:
What took the margin-bring up next slide

## Slide 76: Major Unexpected Expenses
Replacing ECU
  $660 for repair and shipping
Test stand development
  Additional $200 in materials to modify test stand
Electronics PCB
  Each revision of PCBs cost $200, which was not originally budgeted for
Risky Project
  Our project has a very expensive, fragile engine which increases budgetary risk
  Extreme thermal and aerodynamic loads on all manufactured components
  Left a large margin because of this, which kept us safe despite large unexpected expenses
Notes: Presenter:
What took the margin-bring up next slide

## Slide 77: Estimated Industry Cost
 | Current | Predicted Without Shutdown
Total Team Hours | 3456 | 4342
Hourly Wage | $30.77 | $30.77
Total Salary (without overhead) | $106,341 | $133,603
Total Salary (with overhead) | $319,023 | $400,810
Planned/Spent Expenses (Materials) | $2,818 | $2,818
Total Cost | $321,841 | $403,628
Notes: Presenter:
Consider putting fall/spring hours into a backup to be able to answer questions

## Slide 78: Final Thoughts
WHiMPS was not able to achieve many levels of success, but we were at the brink of reaching WPM level 3 and TVM levels 1 & 2
Reaching our maximum level of success was possible within our remaining budget and schedule
  Concerns of TVM affecting engine operation were mostly mitigated
Although project was not completed due to COVID-19 shutdown, it was a great learning experience for the team
We would like to thank the entire PAB for their support and guidance throughout the project
Notes: Presenter:
What took the margin-bring up next slide

## Slide 79: Questions?
Notes: Talk about models we didn’t get to validate

## Slide 80: Backup

## Slide 81: Thrust Vectoring Mechanism (TVM) Design Process
Trade approaches to satisfy requirements.
Create simple component with manufacturability in mind, using first-principle models.
Use thermal requirements to inform material choice.
Use FEA tools to predict performance in array of expected loading cases.
Iterate design toward appropriate safety factor values.
Notes: Presenter:

## Slide 82: Vibrational Analysis
Engine frequency range between idle and max thrust state (50 N to 100 N)
  733.3 Hz ≤ f ≤ 2566.7 Hz
Two main points of concern are the paddle and rod connection between actuator screw and paddle
  Actuator and screw will absorb some of the engine excitation (damper)
Material is modeled as T-600 Steel with a modulus of elasticity of ~200 GPa
  Paddle: f = 18.28 Hz
  Rod: f = 329 Hz
Actuator, screw, nozzle sheath, and housing will act as dampers to dissipate energy, further reducing risk of vibrational failure
Notes: Because the largest natural frequency is 329 Hz, which is far less than engine idle state, we can accept the components as good to go.

## Slide 83: Stock Engine Test Thermocouple Data
Notes: Should we add gridlines to graph? Might make it easier for PAB to see what the actual temps were
Note that 304 steel has a melting point of 1400C, but can be used in continuous manner up to 925C
Add model expectations and error bars

## Slide 85: Thrust Vectoring Test Safety Measures
Safety Concerns:
  Fuel fire
  Engine breaks and throws a fan blade
Safety Measures
  All tests performed in CU engine test cell
  Matt Rhode present for all tests
  Safety officer is only member in test cell once battery is plugged in
  Sentries posted outside of test cell to stop passersby from entering danger zone
Notes: Presenter:

## Slide 86: Windmill Prevention Test Safety Measures
Safety Concerns
  Over-pressurization of the APOP replica PVC Tube
  Failure of SABRE tank
  High speed air harming passersby of test cell
Safety Measures
  Matt Rhode present for all tests
  Pressure gauge on PVC tube
    Safety officer radios to valve operator to shut off if differential pressure exceeds 5 psi
  Remotely pulling SABRE tank lever
  Same sentry/perimeter procedure as engine tests
  Complete depressurization of SABRE tanks before any transportation of tanks
Notes: Presenter:

## Slide 87: Fairing Displacement
Dr. Maute identified component displacement as most important quality
FEA was conducted for each component separately
  Component Displacements:
    Left Side Fairing: 1.123e-7 mm
    Right Side Fairing: 4.03e-3 mm
These results are with each component acting independently
  Mounting the two pieces together will provide additional structural support
Notes: Zoe

## Slide 88: Design Validation
CFD conducted simulating Mach 0.8 at 20,000 ft
Professor John Mah confirmed the turbulent wake aft of the engine re-entering the nozzle should not be a concern
Notes: Zoe

## Slide 89: Thrust Vectoring Paddle Model
Conservation of Momentum
Assumptions
Steady, uniform flow
No leakage around paddles
Subsonic exhaust
Paddle is flat
Notes: Jon

## Slide 90: Thrust Vectoring Paddle Model
Notes: Jon

## Slide 91: Thrust Vectoring CFD
Fluid exit
Fluid inlet
Nozzle inlet
Notes: Desire to corroborate data via CFD
Jon

## Slide 92: Thrust Vectoring CFD Setup
Assumptions: steady, turbulent, sea level
Boundary Conditions: nozzle inlet mass flow is 0.23 kg/s, nozzle exit velocity is M=0.7, fluid inlet gage pressure and velocity is zero
Initial Conditions: fluid inlet and exit velocity is zero
Turbulence Model: k-epsilon
Autodesk CFD Characteristics: solves Navier-Stokes equations (approximates Euler conditions by using slip conditions with low viscosity), defaults to a slip condition on undefined surfaces
Notes: Desire to corroborate data via CFD
Jon
Turbulence model info - https://en.wikipedia.org/wiki/K-epsilon_turbulence_model
Emphasize BCs represent how we will be testing with compressed air if we are not able to run the engine

## Slide 93: Thrust Vectoring CFD Results
θ = 17°
θ = 11°
A = 1250mm2
A = 850mm2
Paddles are at 20°
Paddles are at 20°
Notes: Jon

## Slide 94: Sheath Structural Analysis
Material modeled as Aluminum 2024
Yield strength - 325 MPa
Max total axial force - 100N+
Failure mode is bending point
Load would be distributed with actuator linkage.
Notes: Jon

## Slide 95: Sheath Structural Analysis
Principle: Rate of conduction = rate of convection
145°C
25°C
Conduction
Convection
K = 0.25 W/m*k
H = 2 & 25 W/m^2*k for best and worst case scenario natural convection
H = 25 for worst case forced convection
Notes: Jon

## Slide 96: Actuator Housing Structural Analysis
ABS Plastic 3D printed structure
Assumes front lip is fixed; load is dynamic pressure on rear cross sectional area (overestimate).
ABS Strength ~ 40 MPa
Max von Mises stress = 643 kPa
FOS = 62
Glass transition temperature = 98°C
Engine base doesn’t get significantly hotter than ambient conditions in previous tests.
Notes: Jon
Strength from Simplify3D.com

## Slide 97: Paddle Structural Analysis
Service Temp of 700K > 668K max temp from thermal model
From CFD, each paddle experiences 7.31N normal to plane at center of paddle
  Similar to base principle estimate
Assumes pins fixed; 8N normal load to paddle
Max von Mises stress of 96 MPa < 620 MPa yield strength (FS = 6.5)
Notes: Jon

## Slide 98: List of Necessary Materials
Windmill Prevention Mechanism (acquire)
  PVC and PVC cap
  Pressure regulator
  Pressure gauge
  Air line (50ft)
  NPT connectors (¼”)
Thrust Vectoring Mechanism (acquire)
  Load cell/load cell amplifier
  Pillow blocks
  Steel shafts
  Aluminum plates
  Compression springs
Electronics/Software (acquire)
  Connectors
  Motor drivers
  Actuators
Windmill Prevention Mechanism (manufacture)
  Outlet 3D-printed nozzle (SABRE)
Thrust Vectoring Mechanism (manufacture)
  Paddles/linkages
Electronics/Software (manufacture)
  MCB
  LPBB (x4)
  ICUP
  MCB housing

## Slide 99: Stock engine testing (preheating)

## Slide 100: Stock engine testing (visible exhaust)

## Slide 101: Risk Reduction
ICUP design is being modified to resemble a bracelet, rather than a donut
  Reduces risk of ICUP breaking under load of the Mach 0.8 air and from ejection of the fairing hitting the ICUP
  Ensures that fairing ejection does not interfere with the electronic components onboard the engine
New design
Notes: Presenter:

## Slide 102: WPM Test #1 plan

## Slide 103: Stock Engine and Dummy Paddle Test

## Slide 104: First Semester Focus
Notes: Presenter:

## Slide 105: First Semester Focus
Feasibility Study/Concept Exploration:
  Trade studies conducted with ~6 solutions to both the WPM and TVM (total of 13 solutions)
  Risk, performance, profile, and safety were set with specific weights as to which was more important than another
  For the WPM, a fairing-cover was chosen
  For the TVM, a system of four paddles on the exhaust nozzle was chosen
Trade Studies and Key Trades in backup slides
Notes: Presenter:

## Slide 106: First Semester Focus
Concept of Operations:
  No actual mission set by the customer to utilize the incorporated mechanisms
  AFRL explained how they would test the developed mechanisms to simulate it’s target environment
    No windmilling of the fan blades at M=0.8 @20k ft
    Vector the thrust by ±10° on at least one axis
      Cannot decrease nominal thrust
  This resulted in the WHiMPS creating a CONOPS based on how the mechanisms could be utilized
    One CONOPS for WPM that leads into the CONOPS for TVM
First developed CONOPS
Notes: Presenter:

## Slide 107: First Semester Focus
System Requirements:
  Some requirements set by AFRL
    No fan blade rotation under set flight conditions
    Vector the thrust by ±10°
      Do not impede nominal thrust
  Some requirements set by WHiMPS
    The MCB shall control both mechanisms and read-in data from thermocouples and GSU
  Levels of Success based on:
    Getting the engine to run
    Getting one vs. two axes of thrust vectoring
    Incorporating the mechanisms onto a working engine
Functional and Design Requirements are in backup slides
Notes: Presenter:

## Slide 108: First Semester Focus
High-Level Design (PDR):
  Baseline design of WPM
    First iteration of fairing designed and used for structural analysis testing on Solidworks
  Baseline design of TVM
    Material selection of paddles
    Paddle deflection angle as a function of flow deflection angle
      Effect of paddle area on flow-turning efficiency
  Baseline design of MCB
    Software flowcharts
    Power and data feasibility analyses
  Analyses
    Structural analysis on Solidworks (WPM)
    Fairing ejection feasibility analysis (WPM)
    Thermal modelling of the paddles (TVM)
Analyses shown in backup slides
Notes: Presenter:

## Slide 109: First Semester Focus
Detailed Design (CDR):
  Detailed Electronics and Software
    Functional Block Diagram, Software Flowchart
    MCB, MCB Housing, ICUP, and LPBB designed
    GUI layout
  Completion of Components
    Fore and Aft Retention Rings
      Designed to hold WPM and TVM to engine body
    Actuator Housing, Nozzle Sheath, Paddles
  Detailed Analyses
    CFD and FEA performed on WPM
    CFD and structural analysis performed on components for TVM (actuator housing, sheath, paddles)
    Vibrational analysis
      Components act as dampers during operation to reduce vibrational effects
      Largest natural frequency less than engine idle state
  Full System Verification and Validation
    Test stand development (2-axis thrust measurement)
    WPM and TVM preliminary test design
    Risk mitigation
Notes: Presenter:

## Slide 110: Second Semester Focus
Notes: Presenter:

## Slide 111: Trade Studies
Notes: Presenter:

## Slide 112: Trade Studies
Notes: Presenter:

## Slide 113
Electronics & Software Slides

## Slide 114: Electronics Testing
Switch functionality
Voltage converter (5V)
Power protection circuit
GPIO/LED circuit
Power MOSFET circuit
Raspberry Pi functionality
I2C functionality
Solenoid circuit
Actuator/motor driver circuit
Linear potentiometer circuit
Harness continuity check
Temperature sensor circuit
Successful
Successful After Changes
Unsuccessful
MCB
ICUP
LPBB
All
Notes: Presenter:

## Slide 115: Upcoming Electronic Tests
Temperature sensor addresses
  Done by: 3/6/2020
Actuator/motor driver circuit
  Done by: 3/6/2020
Load cell/amplifier circuit
  Done by: 3/13/2020
Revision B MCB functionality
  Done by: 3/13/2020
Revision B ICUP functionality
  Done by: 3/13/2020
Revision B LPBB functionality
  Done by: 3/13/2020
Revision A PCBs
Notes: Presenter:

## Slide 116: Electronics Overview
Main Control Board (MCB)
Provides WHiMPS’ data processing and power distribution
Integrated Communication Unit Panel (ICUP)
Extends actuators and potentiometers’ data and power lines from the MCB to the engine
Linear Potentiometer Breakout Board (LPBB)
Converts potentiometer analog output to a digital signal (I2C)
ICUP
MCB
LPBB
Rev. A
Notes: Presenter:

## Slide 117: MCB Revision B
Changes from Revision A to B:
Took out MCB <-> ECM connector
Fixed the temperature sensor circuit
Added load cells connectors and amplifiers (2x)
Added more indicator LEDs
Added MOSFETs for all motor drivers/actuators
Took out software control (MOSFET) for Ammeter
Notes: Presenter:

## Slide 118: ICUP Revision B
Changes from Revision A to B:
Changed outline from a ring to a 4 panel “bracelet” design
  Each panel is connected together through SAMTEC locking connector assemblies
Motor drivers were replaced with the correct stepper motor driver
Fixed solenoid circuit
Using a surface mount rail system with one screw hole instead of 4 screw holes
1
MCB <-> ICUP
Actuator #1
Motor Driver #1
LPBB #1
2
Solenoid #1
Actuator #2
Motor Driver #2
LPBB #2
3
Actuator #3
Motor Driver #3
LPBB #3
4
Solenoid #2
Actuator #4
Motor Driver #4
LPBB #4
Notes: Presenter:

## Slide 119: LPBB Revision B
Changes from Revision A to B:
Changed to an ADC with multiple address for I2C
  Tie AD0 and AD1 resistors to either HIGH or LOW to get 4 address combinations
  18 bit ADC
Notes: Presenter:

## Slide 120: Test LabVIEW Front Panel

## Slide 121: Test LabVIEW Block Diagram

## Slide 122: WHiMPS LabVIEW Front Panel

## Slide 123: WHiMPS LabVIEW Flowchart

## Slide 124: Paddle Control Law
Notes: Presenter:

## Slide 125: Gantt – Manufacture & Test
Notes: Presenter:

## Slide 126: Gantt – Software & Electronics
Notes: Presenter: